ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                          version 2.1 - 26 May 1987                          º
º        1. tablev.exe<cr> - enter from DOS with no ram resident utilities    º
º        2. resdel<cr>     - to delete last memory resident utility           º
º                            it should abort if there are none.               º
º        3. resdel rem<cr> - remove all ram residents and replace vectors     º
º                                                                             º
º   To change the default drive for VECTOR.TBL:                               º
º        ren resdel.exe resdel.123<cr>                                        º
º        debug resdel.123                                                     º
º        ecs:04E4<cr>                                                         º
º        43.41<cr> ( to make drive A )                                        º
º        w<cr>                                                                º
º        q<cr>                                                                º
º        ren resdel.123 resdel.exe                                            º
º                                                                             º
º   The  program has two modes.  The first mode will remove the highest ram   º
º   resident program and the second will replace the  entire  vector  table   º
º   and  delete all ram resident programs.  To do this the program requires   º
º   that an accurate copy of the default vector table be made as a file  on   º
º   the disk where it can be located.  I wrote the program to look for this   º
º   vector table file in the root directory of my hard drive (C).             º
º                                                                             º
º   The first mode copies the vector table from the file to the 1024  bytes   º
º   of  memory at 0:0.  Then the program deallocates the environment blocks   º
º   and program segment prefix blocks from the end of DOS to the  beginning   º
º   of the program itself.  This is all of the RAM residents in low memory.   º
º   If a resident installs itself in high memory  and  then  readjusts  the   º
º   size  of  the  system memory, this program will not work and it will be   º
º   incompatible.  I have not run into this situation myself - yet.           º
º                                                                             º
º   The program's second mode reads from the program into lower memory  for   º
º   the next lower program segment prefix (PSP). If DOS is found, no action   º
º   is taken. Otherwise, the two memory blocks containing a copy of the PSP   º
º   and the environment strings are deleted.  The  vector table information   º
º   present in low  memory  is searched for references to the  PSP  of  the   º
º   deallocated  block.   These  vectors  are  replaced  with  the original   º
º   values.  In this way, the resident utility is effectively  removed  and   º
º   the memory freed for further use.                                         º
º                                                                             º
º   Program not finished - future revisions are possible.                     º
º   Ed Jordan                                                                 º
º   70357,2162                                                                º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼