PROCON CONTROL Version 1.0  25/11/1987

Copyright (C) Peter E. King, 1987

ADDRESS:       ProCon Software
               P.O. Box 43
               Essendon
               Victoria, 3040
               AUSTRALIA.    

               (This is a Down Under product)

Requirements:

IBM-PC  or  compatible  with  DOS version  2.0  or  higher.   One 
parallel printer port with inter-connecting hardware.  To run the 
BASIC  source programs,   BASICA,  GWBASIC or any  compiler   IBM 
BASIC compiler, QuickBASIC or Turbo-BASIC is required.


Copying and distribution:

PROCON  CONTROL  may  be copied and distributed  as  a  SHAREWARE 
program.   That  is  the  disk may be copied and  distributed  to 
others   provided  that  ALL  files  on  this  disk  are   copied 
unmodified.   It  may NOT be distributed on BBS's as NO  controls 
are  provided (This may be reviewed in future but little  returns 
have been forthcoming from BBS users!).   The program may NOT  be 
used  as  a value added product and NO fee can be charged  except 
for a disk and handling charge of up to $10 Australian or $6 U.S.

The copyright notices are to preserve my options,  and to protect 
you  from  the  untoward modifications  of  others.   It  is  NOT 
intended  to  prevent the public distribution of PROCON  CONTROL, 
subject to the above limitations.


INTRODUCTION
============

YES!   You  can  turn your IBM-PC or compatible into  a  COMPUTER 
CONTROL CENTRE.   On this disk are a number of programs which use 
any  OUTPUT port on the computer to control 8 relays.   In  fact, 
any system with a parallel printer output can be used!

To  get  started,  simply connect eight LED's via 1.5K  resistors 
from  each  data  line of your printer port (pins 2 to 9  of  the 
25  pin connector) to ground (pin 22).   Then,  when you run  the 
following programs you will be able to see what's happening.

If  you  use  PROCON CONTROL,  please support it  by  becoming  a 
registered user.   For $30 AUS ($25 U.S. from overseas), you will 
receive the lastest version on disk, complete with ALL source and 
executable code.   A circuit diagram of the necessary connections 
to control up to 12 relays from a single printer port is provided 
together with full instructions.  As a BONUS, I will also provide 
a simple logic control program which provides control of 8 inputs 
and  8  outputs on the computer in an inter-active PLC  language.  
(e.g.  AND X1,  OR X2,  OUT Y1 etc).   Ideal for controlling  all 
sorts   of  devices  and  learning  the  fundamentals  of   PLCs.  
(Programmable Logic Controller).

Suppport:

If  you are a contributor (bless your little heart!),   I'll most 
happily  help you with any difficulties encounted.   Mail is  the 
preferred  method  of exchange,  but you may also contact  me  on 
VIATEL no. 333749600 or FIDO-NET 631 node 323.

If  you are not a contributor (oh dear!),  please send a  stamped 
SAE,  and I'll try to get back to you.   Overseas letters will be 
answered but these will take a little longer.


PROBLEMS AND ENHANCEMENTS
=========================

I  am most certainly interested in any problems or bugs with  the 
programs.   And,  indeed,  if  you have any suggestions  or  have 
produced any enhancements to these programs I would be interested 
in  hearing from you.   Please READ THESE INSTRUCTIONS  CAREFULLY 
before reporting any problems.

I  am  continually improving these programs.   Your  contribution 
will  aid  the development of further  enhancements,  which  will 
include a memory resident REMOTE program - so you can continue to 
use  the computer for other things while it switches the  outputs 
ON  and OFF at selected times.   I am also working on day of week 
control  so  the  you can switch an output only  from  MONDAY  to 
FRIDAY  for example.  And random switching for burgular  deterent 
and lighting effects etc.


LIST OF FILES
=============

CLOCK.SYS      New system clock driver for DOS.

CONFIG.SYS     Configure system file for CLOCK.SYS.

CONTROL.COM    Controls relays from keyboard, memory resident.

EXAMPLE.BAS    BASIC program example of how to control relays.

STICK.BAS      BASIC program shows how to control from joystick.

REMOTE.BAS     BASIC program controls relays by DATE and TIME.

REMOTE.EXE     Compiled version of REMOTE program.

CLEAR.REM      REMOTE file to clear all settings.

TEST.REM       REMOTE file example of settings.

SHIFT.REM      REMOTE file example of shift register.

ORDER.DOC      ORDER form for contribution.

NEW.DOC        NEW products list.
     
README.DOC     This file.


SYSTEM FILES
============

The  CLOCK.SYS device driver is provided to allow the DATE to  be 
incremented  when the TIME clocks over to 00:00:00.00.   This  is 
done  already in DOS version 3 but not in version 2.   It is also 
useful  in DOS version 3 because some  programs  (i.e.  on-screen 
clocks  etc) may 'steal' the timer flag indicating that the clock 
has passed 24 hours.  Also, since this driver monitors the system 
timer  continually,  date increments cannot be lost when the time 
is  not  read for 24 hours.   To install the driver  simply  copy 
CLOCK.SYS  to  your boot disk and include DEVICE =  CLOCK.SYS  in 
your CONFIG.SYS file.  If one does not exist then copy the one on 
this disk to your boot disk.


CONTROL
=======

This  is  a  memory resident program which only needs to  be  run 
ONCE.  When installed,  the program allows the keyboard to toggle 
the eight data lines on your printer port ON and OFF.   Hold down 
the Ctrl key and press F1 to F8,  these toggle the eight outputs.  
To switch ALL outputs OFF press Ctrl-F10 and all ON by Ctrl-F9.

The  program  uses  the printer port 378.   To  change  the  port 
setting use your debug program as follows:

A>DEBUG CONTROL.COM           <execute DEBUG and load program>

-E104                         <enter into memory at 104>

XXXX:0104  78 LL  03 HH       <LL - low /HH - high port address>

-W                            <write new program>

-Q                            <quit - go back to DOS>


You may now run the program, which remains resident in memory and 
can be utilised at ANY TIME - even whilst running other programs!


BASIC PROGRAMS
==============

The  BASIC source programs show how the outputs can be controlled 
from:   1.  The computer (EXAMPLE)  2.  The joystick  (STICK) and  
3.  The system date and time (REMOTE).

To change the PORT address simply alter the line PORT=&H378.


REMOTE
======

A  compiled version of REMOTE is provided on the disk for  faster 
scanning  of the dates and times.    Execute this by entering the 
word  REMOTE then pressing Return.   You will first be asked  for 
the  printer port (if you have more than one!) which you wish  to 
use as the output.

The OPTION menu then appears:

(T)  Changes  system time and date.   And the repeat  time,  this 
     time  is  used when the (R) Reset and  execute  function  is 
     selected.

(L)  Load from file.   Allows all the 8 outputs (RL1 - RL8)  with 
     their ten settings to be loaded from disk.

(S)  Save  to file.   Allows the settings to be saved to disk for 
     later loading.

(R)  Reset  and  Execute.   This resets the time to 00:00:00  and 
     then begins execution.   This allows a timed sequence to  be 
     repeated.   When the repeat time is reached then the time is 
     again reset to zero and the sequence repeats once more.

(E)  Execute.   Begins  scanning dates and times from the current 
     setting.

(1)  Set ON/OFF dates and times for RL 1.

...  ....................................

(8)  Set ON/OFF dates and times for RL 8.


DATE AND TIME SETTINGS
======================

Each  output (RL1 to RL8) is allowed up to ten  ON/OFF  settings.  
DATE1  and  TIME1  set the ON time and DATE2 and  TIME2  the  OFF 
time.   NOTE:  ALL dates are entered in the format YYYY-MM-DD for 
comparison purposes. Times must be entered in the standard format 
HH:MM:SS  (24 hour clock).   When the ON date and time occurs the 
output  is switched ON and when the OFF date and time is  reached 
it turns OFF again.  If DATE1 is not provided then only the times 
are taken into account and the output switches ON and OFF at  the 
times set every 24 hours.


APPLICATIONS
============

This  program  may  be used to control a  sprinkler  system.   To 
switch  a radio or tape recorder ON and OFF.   Or as  a  burgular 
deterent  by  switching things ON and OFF at particular times  of 
the  night  and day.   The program could also be used  for  model 
control  such as a robot or train control by using the repeatable 
timed  sequence.  The output relays may be connected to a  remote 
control  allowing  the TV,  HI-FI etc to be controlled  from  the 
computer.  The applications are only limited by your imagination!


(C) 1987, ProCon Software, Box 43, Essendon, 3040, AUSTRLALIA.