================================================================================
       DOSMAX.EXE :  Ver. 2.1, Copyright (1992,93) by Philip B. Gardner
================================================================================

  DOSMAX.EXE is a device driver which will maximize the use of low memory
  by moving MS-DOS 3.1 and above system data to upper memory blocks provided
  by your upper memory manager.  It is not necessary to use any other
  programs to create upper memory data types like FILES, BUFFERS, FCBS,
  or LASTDRIV from Quarterdeck's QEMM386.  These data types are referred
  to as "sub-segments" in the rest of this document.

  In addition, if you are a DOS 5.0 or above user and are loading DOS high,
  then DOSMAX can prevent DOS from loading into the HMA and move the DOS
  kernel to an upper memory block.  This improves performance and allows
  programs which use the HMA more efficiently to utilize the HMA instead.
  Such programs include Microsoft WINDOWS and Quarterdeck's DESQVIEW.

  Version 2.0 now requires the device driver STOPMAX.SYS to prevent DOS from
  loading into the HMA (see STOPMAX.DOC).  The DOSMAX driver then moves
  the kernel into upper memory at the proper time.

  DOSMAX can also move a portion of COMMAND.COM into an upper memory block
  instead of the HMA.  This feature recovers space in low memory which is
  available when DOS is in the HMA.  Version 2.0 now requires the /C+ switch
  to enable this feature rather than /A0 to disable it.

  Support is automatically provided for Microsoft WINDOWS 3.x so that all
  FILES in your CONFIG.SYS can be loaded high.  Normally this would prevent
  WINDOWS from running, but the problem is circumvented.  Version 2.0 has
  changed the support algorithum significantly, see /W+ option below.

  Support is provided for:

    * moving all DOS's sub-segments types into upper memory
    * moving DOS's SYSTEM block (kernel) into upper memory (STOPMAX installed)
    * supporting WINDOWS start-up even if all FILES= are in upper memory
    * moving a portion of COMMAND.COM into high memory instead of the HMA
    * DOS Versions 3.1 - 3.31, DOS 4.x, DOS 5.x, and DOS 6.x (or better?)

  DOSMAX automatically moves all the data that can be moved dependent only
  upon the availability of upper memory.  It will automatically stop moving
  data when it determines that memory would be fragmented if the move were
  completed.

  Finally, a command line mode is provided to control Windows support, and
  check and report on the status of the high memory area reserved for
  COMMAND.COM.  Version 2.0 moves the Master Environment moving feature
  into a separate program, see ENVIMAX.DOC.

================================================================================

(Requirements)::

        * Requires MS-DOS Version 3.10 or better
        * Now supports DR-DOS 6.0
          
================================================================================

(Installation)::

        (CONFIG.SYS)::

        Installation of DOSMAX.EXE requires modifying the contents of
        your CONFIG.SYS file.

(Generic Configuration)::

        This configuration should work and be the most efficient in 95%
        of all configurations.  For a few real world examples see
        EXAMPLES.DOC
       
        DOS=HIGH[,UMB]                    (DOS 5.x or 6.x only)
        REM DEVICE=STOPMAX.SYS [options]  (Stops kernel from loading in HMA)
        DEVICE=(xms/umb memory manager)
        DEVICE=DOSMAX.EXE [options]       (DOSMAX loads high automatically)
        SHELL=SHELLMAX.COM COMMAND.COM /P
        BUFFERS=20
        FILES=40
        LASTDRIVE=Z

        For DESQView users, it is recommended that the DEVICE=STOPMAX.SYS is
        installed.  This enables DOSMAX's kernel moving feature.

        DOS 5.x and 6.x users should configure DOS to load high into the
        HMA.  The UMB parameter is optional, since both DOS 5.x and 6.x
        upper memory management and XMS upper memory blocks are supported.

        DOS=HIGH[,[UMB][NOUMB]] (Both DOS UMB's and XMS UMB's supported)

        Insert a DEVICE= line for DOSMAX.EXE in your config.sys.  Ver. 1.5
        of DOSMAX recommended that DOSMAX be loaded before the XMS and UMB
        memory manager, but DOSMAX should now be loaded after the XMS manager
        (DOSMAX will automatically load itself high if UMB's are available
        or you may use your memory manager's device loader).  Version 1.7
        provided another way to ensure that the DOS 5.0 or above kernel
        is moved into a UMB by DOSMAX.  The driver STOPMAX.SYS is inserted
        "before" the XMS manager and DOSMAX is inserted "after" the XMS
        manager (see STOPMAX.DOC).

        Version 2.0 now requires that STOPMAX.SYS is used to stop DOS from
        loading into the HMA, support for /B+,/I+ and /V+ have been removed
        from DOSMAX.EXE because these options caused confusion.

        Version 2.0 now requires /C+ to enable the upper memory support
        option for COMMAND.COM.  This option was provided by default in
        earlier versions and was disabled with /A0.  Normally you will
        want to use SHELLMAX.COM to load all of COMMAND.COM into upper
        memory (see SHELLMAX.DOC).  The /A0 option also caused confusion.

        REM DEVICE=STOPMAX.SYS [options]
        DEVICE=(Memory Manager)
        DEVICE=DOSMAX.EXE [/C:+][other options]

        One advantage of using DOSMAX.EXE, is that the STACKS=, BUFFERS=,
        FCBS=, FILES=, and LASTDRIVE= parameters may be configured normally.

        STACKS=9,256            (or =0,0 or default 9,128...etc...)
        BUFFERS=XX[,YY]         (XX = # of buffers, YY = lookahead cache)
        FCBS=XX,YY              (XX = # of FCBS, YY = # of protected FCBS)
        FILES=NN                (NN = # of system files)
        LASTDRIVE=Z             ( Z = Last reserved drive)

        Version 2.0 of DOSMAX now allows INSTALL=, you no longer have to
        remove these statements from your CONFIG.SYS.

        By default, DOSMAX.EXE Version 2.0 will not generate report messages
        for each successful operation or event, unless you enable the report
        with /R+.  You must also use /P+ to pause after this report.  Use
        /R+ and /P+ until you are satisfied with the configuration then
        remove these switches.

        DEVICE=DOSMAX.EXE /R+ /P+ 
        or DEVICE=DOSMAX.EXE /REPORT:+ /PAUSE:+ 

        (AUTOEXEC.BAT)::

        It is not necessary to modify the contents of AUTOEXEC.BAT, but
        since DOS data creators like FILES and BUFFERS are no longer
        required, it is recommended that these lines be removed

        REM BUFFERS=XX          (Remove FILE and BUFFER creator TSR's)
        REM FILES=NN

        (From the Command Line)::

        By default, DOSMAX.EXE, invoked from the command line, will generate
        a message for each successful operation or event.  The display will
        not pause in the command line mode unless the /P+ switch is used.
        After you are satisfied with the configuration and you want to disable
        the REPORT feature, use:

        DOSMAX.EXE /R-
 
        All switch options and possible messages for DOSMAX are detailed
        below:

(Loading DOSMAX High)::

        You may load DOSMAX high with your high memory loader, but DOSMAX
        will load itself high if upper memory is available.  To prevent
        DOSMAX from loading itself high, use /X- or load it before the
        memory manager is installed.

(Moving the DOS kernel into a UMB)::

        DOSMAX to move the DOS 5.0 or above kernel to a UMB, then DOS
        must not be in the HMA when DOSMAX loads.  If you desire to stop
        the kernel from moving into the HMA, then STOPMAX must be loaded
        before the xms/umb memory manager, so that the DOS kernel is not
        high when DOSMAX initializes.  If DOS is already in the HMA (not
        using STOPMAX), then Verision 2.0 now detects this condition and
        low memory is optimized correctly.

================================================================================

(Syntax)::

        The only thing to remember about syntax for the command line is
        that just about anything works.  What this means is that you
        should be able to type in the options on the command line the
        way they make sense to you.

        To illustrate this point, the following command line example
        is mutated several different ways.

        DEVICE=DOSMAX.EXE /H+ /R- /P- /A0
        DEVICE=DOSMAX.EXE -H+ -R- -P- -A0
        DEVICE=DOSMAX.EXE H R- P- A0
        DEVICE=DOSMAX.EXE HR-P-A
        DEVICE=DOSMAX.EXE -H+-R-P-A

        ... and so on.

        DOSMAX 1.9 and above adds optional full word syntax.  The new
        syntax looks like this:

        DEVICE=DOSMAX.EXE /ALLOWHI:+ /REPORT:- /PAUSE:- /AVAIL4A=0
        DEVICE=DOSMAX.EXE -ALLOWHI:+ -REPORT:- -PAUSE:- -AVAIL4A=0
        DEVICE=DOSMAX.EXE ALLOWHI REPORT:- PAUSE:- AVAIL4A=0
        DEVICE=DOSMAX.EXE ALLOWHIREPORT-PAUSE-AVAIL4A
        DEVICE=DOSMAX.EXE -ALLOWHI+-REPORT-PAUSE-AVAIL4A

        Obviously when using full words, it is easier to keep the words
        separated so that is clear to read.  An optional [:] or [=] may be
        used for switches (i.e. ALLOWHI:+ or AVAIL=0).  These optional
        delimiters are used interchangeably and can also be used with the
        single letter switches.  Remember to check your spelling because the
        single letter interface is still intact.

================================================================================

(Switch Options)::

        The following list of switch options is organized by:

         - Control of DOSMAX Reports (/R:/P:/N:)
         - Control of DOSMAX Operation (/M=/H:/L:/A=/S:/U=)
           - Setting the Memory Strategy (/M=)
           - Control the Location of the DOS Kernel (/H:/L:)
           - Control COMMAND.COM Split (/C:/A=)
           - Control EMS Usage (/Q:)
           - Control Sub-Segment Relocation (/S:)
           - Control Stack Interrupts (/U=)
           - Control DOSMAX Automatic UMB installation (/X:)
           - Response file for DOSMAX

  (Control of DOSMAX Reports)::

        (REPORT)::      R[+ or -]        (toggle:  default -)

        Use /R+ or /REPORT:+ to enable the report of additional status
        messages.

        (PAUSE)::       P[+ or -]        (toggle:  default -)

        Use /P+ or /PAUSE:+ to enable a pause after the execution of
        DOSMAX.EXE.

        (NOPAUSE)::     N[+ or -]        (toggle:  default -)

        Use /N+ or /NOPAUSE:+ to never pause after the report, even if
        there are errors.  This switch can be used if your configuration
        generates a warning or error message which you choose to ignore.

  (Control of DOSMAX Operation)::

    (Setting the Memory Strategy)::

        (STRATEGY)::    Mn               (value=  n = 0)   

        Use /Mn or /STRATEGY=n to control the memory allocation strategy
        which DOSMAX uses to allocate upper memory blocks.  The default
        strategy is is First Fit (/M0).  This means that DOSMAX will use the
        first upper memory block returned by the XMS manager.  The other
        available options are Best Fit (/M1) and Last Fit (/M2).  Best Fit
        uses the block which most closely matches the size needed, and
        Last Fit uses the last block big enough to handle the request.
        Values other than 0, 1, or 2 are ignored and the previous setting
        of this option is used.
 
        (SYSFSIZE)::    Fnn              (value=  nn = 59 )

        Use /Fnn or /SYSFSIZE=nn to set the System File Size:  The upper
        limit of nn is 61 in device mode, and 82 in command line mode.
        The lower limit is 40.  Values other than the MS-DOS 4.0 - 6.0
        System File Size of 59 are only allowed if the true MS-DOS version
        is greater than 5.0.  The /Fnn switch is only necessary if DOSMAX
        can't determine the System File Size automatically.

    (Control the Location of the DOS Kernel)::

        (ALLOWHI)::     H[+ or -]        (toggle:  default -)

        Use /H+ or /ALLOWHI:+ to allow DOS to load into the HMA anyway.
        This switch is now obsolete.  DOSMAX now detects the location of
        the kernel and automatically determines the proper setting of this
        switch.  It is for backward-compatability and debugging purposes only.

        (FORCELOW)::    L[+ or -]        (toggle:  default -)

        Use /L+ or /FORCELOW:+ to allocate DOS code block in low memory.
        This switch is now obsolete.  DOSMAX now detects the location of
        the kernel and automatically determines the proper setting of this
        switch.  It is for backward-compatability and debugging purposes only.

    (Control COMMAND.COM Split)::

        (CMDALLOC)::    C[+ or -]        (toggle:  default -)
        
        Use /C:+ or /CMDALLOC:+ to enable the /AVAIL4A=nnnnn parameter and
        the function which splits COMMAND.COM from DOS 5.0 in half.  This
        is for those users who chose not to load COMMAND.COM into a UMB.

        (AVAIL4A)::     Annnnn           (value=  nnnnn = 2080)

        Use /Annnnn or /AVAIL4A=nnnnn to set the number of bytes reserved
        in upper memory for COMMAND.COM and other DOS 5.0 and above programs
        which have the capability of moving a portion of themselves into the
        HMA.  These programs use INT 2Fh Function 4Ah to allocate a fixed
        number of bytes from the HMA.  DOSMAX has the capability of emulating
        this function in high memory.  By default, DOSMAX reserves 2080 bytes,
        which is the space needed to shrink COMMAND.COM.  To reserve more
        memory, increase this value.

        The command line mode of DOSMAX reports the size and allocation
        status of this area.  If the amount allocated or requested is not
        equal to the amount reserved, DOSMAX will report what the proper
        value should be.  Users of replacement shells like 4DOS.COM from
        J.P. Software, should disable this option with /A0.  Disabling the
        option or using the report feature of the command line mode to
        set the exact amount of memory required, is recommended since
        INT 21h 3306h (Get True Ver.), which is also hooked by DOSMAX,
        must return with a bit set which indicates that DOS is in the HMA
        until the amount of memory reserved is completely exhausted.

    (Control EMS Usage)::

        (LOADEMS)::      Q[+ or -]       (toggle:  default -)

        Use /Q:- or /LOADEMS:- to disable the default action of DOSMAX
        which allocates EMS to store the .EXE module until the DOS resources
        are built and ready to move.  DOSMAX will still be able to function,
        but disk compression schemes may cause confusion if DOSMAX.EXE is
        not on both the compressed and uncompressed drives.

    (Control Sub-Segment Relocation)::

        (SKIPSUB)::      S[+ or -]       (toggle:  default -)

        Use /S+ or /SKIPSUB:+ to tell DOSMAX to not move sub-segments
        data types.  The switch is provided mainly for diagnostic purposes,
        but may be useful when not enough high memory is available to
        move both the DOS code block and the sub-segments, or if
        you find this feature does not work in your configuration.

    (Control Stack Interrupts)::

        (UNHOOK)::       Unn             (value=  default none)

        Use /Unn or /UNHOOK=nn to tell DOSMAX that INT nn is to be
        "unhooked" from DOS STACKS when the STACKS are moved high.  This
        switch is useful for controlling which hardware interrupts are
        routed through the DOS STACKS mechanism.  Microsoft's EMM386 may
        cold-boot or lock-up if STACKS are present and moved to high memory,
        CTRL-ALT-DEL is pressed (warm-boot), and INT 09h is hooked by DOS
        STACKS.  The DOSMAX option /U09 maybe used to work-around this
        problem.  The interrupt number is in Hex-Notation and the valid
        values are the hardware interrupts 02, 08, 09, 0A, 0B, 0C, 0D, 0E,
        70, 72, 73, 74, 76, & 77.  Invalid interrupt numbers are ignored.
        Multiple invocations of this switch are permissable.
        
    (Control DOSMAX Automatic UMB installation)::

        (HILOAD)::       X[+ or -]       (toggle:  default +)

        Use /X- to stop DOSMAX.EXE from loading itself high if upper
        memory is available.  This switch is intended for diagnostic
        purposes only, since if you use your memory manager to load
        DOSMAX.EXE high this condition is detected and no second upper
        memory block will be allocated.

  (Response file for DOSMAX)::

        Parameters for DOSMAX may be read from a response file by using the
        @pathname syntax:
        
        DOSMAX.EXE @RESPONSE.FIL
 
        Response files may be commented by using a ";","#",or "*" character
        before the comment.

        There is also a feature implemented for DOS 6.0 config menus.  If a
        menu is configured for DOS 6.0, DOS puts the name of the effective
        section in an environment variable.  This environment variable is
        "CONFIG=."  You may optionally divide the response files into
        sections, identified with the familiar [SECTION] syntax, where
        "SECTION" is the name of the DOS 6.0 menu item selected.

(CONFIG.SYS Line)::

        DEVICE=DOSMAX.EXE [/-][R+P+N+L+H+FnnC+AnnnnMnUnnQ+X-]

        device default: /R-/P-/N-/X+/C-/M1

        *  disable Report status messages
        *  don't Pause after report
        *  Pause on errors or warnings
        *  use the Best Fit memory allocation strategy
        *  Load DOSMAX high if upper memory available

        *  everything in square brackets "[]" is optional

================================================================================

(Report Format)::

   DOSMAX.EXE :  Ver. 2.1, Copyright (1992,93) by Philip B. Gardner
        ERROR :  (Error Messages)
      WARNING :  (Warning Messages)
       ADVICE :  (Advisory Messages)
              :  (Report Messages)
              :  (Allocation Status)
        PAUSE :  Press any key to continue... 

(Report Note)::

        DOSMAX.EXE may be replaced by DOSMAX.SYS or DOSMAX.OVL.  The
        exact name of the module is dependent upon the circumstances
        under which DOSMAX.EXE is executed.  This detail is important
        only as diagnostic information.
        
================================================================================

(Error Messages)::

        MS-DOS version 3.10 or above is required
        DOS version is not compatible
        An 80186 processor or better is required
        Device not found, or version mismatch
        Not enough memory to relocate
        Unable to execute, can't open overlay 
        Unable to execute, not enough memory for overlay 

================================================================================

(Warning Messages)::

        Unknown option on the command line
        Unknown option on line #0000
        Extra characters on command line
        Line length overflow at line #0000
        INT 00h is not pointing into STACKS
        DOS Sub-Segment list is unmoveable
        System File Size not determined or out of range
        Unable to validate System Data area
        Couldn't validate DR-DOS data area
        Couldn't size System File Table
        Couldn't size System FCB Table
        Couldn't trace Buffer Chain
        Couldn't find Lastdrive Array
        Unable to calculate DR-DOS kernel control constants
        Unable to calculate kernel control constants

================================================================================

(Advisory Messages)::

        Set STACKS=0,0 in CONFIG.SYS
        Possible INSTALL= in CONFIG.SYS
        Try using /Fnn switch
        For maximum efficiency use /A00000

================================================================================

(Report Messages)::

        Processing option file XXXXXXXX.XXX
	Effection section is [XXXXXXXX]
        DOS System forced low
        DOS System in HMA
        DOS System not in HMA
        DOS Sub-Segments skipped
        DOS Sub-Segments skipped
        DOS Sub-Segments too small, staying resident
        System File Size set to 00
        Unhooked DOS STACKS INT 00h
        Moved 00000 bytes of DOS data high
        Found 00000 bytes allocated of 00000 bytes
        Freed EMS handle 0

================================================================================

(Allocation Status)::

        SYSTEM   moved to 0000
        Not enough Hi Memory for SYSTEM  
        INSTALL  moved to 0000
        Not enough Hi Memory for INSTALL
        STACKS   moved to 0000
        Not enough Hi Memory for STACKS
        DRDATA   moved to 0000
        Not enough Hi Memory for DRDATA
        LASTDRIV moved to 0000
        Not enough Hi Memory for LASTDRIV
        BUFFERS  moved to 0000
        Not enough Hi Memory for BUFFERS 
        WKBUFFER moved to 0000
        Not enough Hi Memory for WKBUFFER
        FCBS     moved to 0000
        Not enough Hi Memory for FCBS    
        FILES    moved to 0000
        Not enough Hi Memory for FILES   
        COMMAND  memory reserved at 0000
        Not enough Hi Memory for COMMAND
        DOSMAX   located at 0000
        Not enough Hi Memory for DOSMAX  

================================================================================

(Sub-Segment List)::

        The Sub-Segment List is searched from bottom to top for a block
        of moveable sub-segments, then moved in reverse order.

        The following chart attempts to show what can and cannot be moved
        with DOSMAX:

                        Sub-Segment Type                Not Moved  Moved
        ----------------------------------------------- ---------  -----
        "D"        DEVICE DRIVER                            x 
        "E"        DEVICE DRIVER APPENDAGE                  x
        "I"        IFS (Installable File System) DRIVER     x
        "F"        FILES=                                            x
        "X"        FCBS=                                             x
        "C"        BUFFERS /X Option (EMS workspace area)            x
        "B"        BUFFERS=                                          x
        "L"        LASTDRIVE=                                        x
        "S"        STACKS=                                           x
        "T"        INSTALL=                                          x

================================================================================

(Changes)::

    (Version 1.1)::

    (1) Fixed problem not cleaning up properly, when DOS goes to HMA
        anyway, (only /V+ switch, and some XMS Managers).

    (2) Fixed problem that occurred if no XMS UMB's available, and DOS 5
        UMB's tried, and if no DOS UMB's available either (not just not
        enough), memory was allocated from low memory, even though
        allocation strategy was set to try UMB's only.  Made sure UMB
        Link state was set properly.

    (3) Added support for DOS Versions 3.10 - 3.31 and DOS Version 4.x

    (4) Improved File Size determination algorithum

    (Version 1.2)::

    (1) Improved detection of DOS=LOW, and reduced the possibility of
        an errant "Should be the first DEVICE= in CONFIG.SYS" message.

    (Version 1.3)::

    (1) Added support for INT 2Fh, Function 4Ah, so that COMMAND.COM
        (and others??) can move a portion of their code to high memory
        too.  For COMMAND.COM users with DOS 5.0, this saves 2.1k of
        low memory.  Added the /Annnn switch to support this feature,
        plus an allocation status check for the command line mode.
        4DOS users should disable this feature with option /A0.

    (Version 1.4)::

    (1) Added capability to find and move the master environment for
        COMMAND.COM users.  Also implemented a special test mode with
        the /T+ option, which verifies that the master environment
        has been found and that it is moveable.  This test mode should
        only be necessary for diagnostic purposes.

    (Version 1.5)::

    (1) Added base 10 number display for /A parameter and changed
        System File Size message to base 10.

    (Version 1.6)::

    (1) Added /Mn option, to allow general control of memory allocation
        strategy.  First Fit = 0, Best Fit = 1, and Last Fit = 2 were
        implemented for both DOS 5 UMB's, and XMS UMB's.

    (2) Added check for a 186 processor or better (allows V20/V30).

    (3) DOSMAX will now move STACKS, so setting STACKS=0,0 is not
        necessary.  In most cases though, STACKS=0,0 is still a good
        idea.  Windows 3.1 supposed requirement for STACKS=9,256 is
        not really necessary in most cases.

    (4) Removed the check for an XMS manager and a check for extended
        memory.  This allows machines without extended memory to use
        UMB providers, which do not require extended memory, with DOSMAX.
        These checks were redundant since if DOS is in the HMA when
        DOSMAX loads, the message "DOS is HIGH already" is reported.
        It is still possible to use DOSMAX, but the /H switch must be
        used if DOS is HIGH first.

    (5) Added /I option which inhibits HIMEM.SYS from loading DOS HIGH.
        This switch is not very useful if HIMEM.SYS is not loaded high,
        since HIMEM will be about 30k in size.  This switch is intended
        for users who load HIMEM high after their UMB provider is installed.

    (6) Changed default WINDOWS high file support method to a new method
        which uses 2 system file handles, but no low memory, so it works
        when DOSMAX is loaded high.  The new method may be disabled with
        /Y-, or /W+ (/W+ enables the old method since it was proven to work
        and the code was already written).  The new method cannot be
        enabled or disabled from the command line.

    (7) Now supporting separate program DOSM86.EXE.  This program is 
        functionally identical to DOSMAX.EXE, but is compiled to work
        on 8086/8088 processors also.  I have learned that there are
        8086/8088 machines which can be configured with High Memory
        using some High Memory Managers, and this variation will make
        it possible for those users to put DOS in a UMB even though
        there is no HMA.  DOSM86.EXE requires 32 more bytes of memory.

    (8) Fixed high loading so it really works...Also added an automatic
        move to high memory of DOSMAX, if UMB's are available via DOS
        or the XMS manager.  If there is some reason you don't want
        DOSMAX loaded high when loaded after UMB's are available then
        use /X- to stop it.  If DOSMAX is high, then it takes 272 bytes,
        because extra code was needed to securely find and identify
        the DOSMAX stub in memory.

    (9) Fixed a problem which hung DOSMAX after loading high if DOS was
        not in the HMA yet and /V+ switch not used.
        
   (10) Changed order of first 5 handles in new windows support, and
        enhanced error checking to only warn when support will not
        work.  The new order maintains the AUX CON order and seems 
        more compatible.

   (11) Added routine to stop "Incompatible DOS" message if loaded high
        with a "device loader."  DOSMAX will now load high with a
        device loader like LOADHI.SYS or HIGHDRVR.SYS

   (12) Try DOS high memory allocation even if NO XMS manager present.
        This was necessary for PC's which don't have extended memory,
        and don't even load an XMS manager (UMB_DRVR creates DOS high
        memory and disappears).

   (13) Fixed DOSMAX not running second time if loaded high with LOADHI.

   (14) Fixed DOSMAX not moving anything high (sometimes) if loaded
        high by any device loader.  I broke this in fix (13).

   (15) Added /B+ option which will stop DOS from going to the HMA by
        patching the DOS initilization code in memory.  This method
        works no matter which memory manager is in use or how it is
        configured.  It also requires no resident memory.

    (Version 1.7)::

    (1) Added /Unn option to tell DOSMAX to unhook hardware INT nn from
        DOS STACKS if the STACKS are present and moved.  At the time
        which DOSMAX moves the STACKS it is safe to restore the interrupt
        to the pre-STACKS value.  This switch was added as a work-around
        to a warm-reboot problem in EMM386.EXE when STACKS are high.  To
        fix the warm-reboot problem use /U09.  The value is in Hex-Notation.

    (2) Fixed DOSMAX not removing remnants of the sub-segments low when
        the size of the DOS data area should have been 0.  This occurred
        when using a memory manager with no code low, no drivers low, and
        DOS in a UMB.  Changed method of recording sub-segment movement.

    (3) Removed DOS Version 3.x use of new windows method, it worked, but
        wasn't completely compatible.  Use FW3.BAT instead if your version
        of DOS is higher then 3.31 (rare).

    (4) Move master environment function now sets the MCB owner of the new,
        high environment back the primary shell.  This corrects a minor
        incompatiblity.

    (Version 1.8)::

    (1) Added specific support for 386MAX.  The high sub-segments and other
        DOSMAX managed data are now labeled using a method which automatically
        detects and adjusts to 386MAX's method of UMB management.

    (Version 1.9)::

    (1)  Reorganized code to enable an overlay method of module selection
         to automate processor selection and split up .SYS and .EXE modules
         to reduce the initialization memory to minimum.

    (2)  DOSMAX now automatically detects the processor type and chooses
         separate code modules if appropriate.  The 186 processor require-
         ment of previous versions is no longer applicable.

    (3)  Added optional full word syntax to argument parser.  The old style
         single letter switch interface is still intact.  The switch lists
         now show the optional word with the switch.

    (4)  Corrected problem with DOS 3.1 - 3.3 files which failed for some file
         settings (i.e. FILES=20 failed).

    (5)  DOSMAX updated for DOS 6.0.  Corrected a coding error while moving
         buffers.

    (6)  Changed default setting of /E switch.  To move the master environment
         high from the command line or AUTOEXEC, now use /E+.

    (Version 2.0)::

    (1)  Added support for INSTALL=, it is no longer necessary to remove
         INSTALL= from the CONFIG.SYS.

    (2)  Removed /B+,/V+, and /I+ options.  You must now use STOPMAX.SYS to
         prevent DOS from moving into the HMA.  The parameters were causing
         confusion.

    (3)  /H and /L are no longer necessary and you can use DOS=HIGH or DOS=LOW
         as you deem necessary.

    (4)  Added /C+ switch to enable the COMMAND.COM split feature.  For most
         users, /A0 was forgotten and only caused unecessary "Packed file
         corrupt" messages and wasted space.  You may still use this feature,
         but you must first enable it with /C+, since the default is now off.

    (5)  Moved /E+,/MASTERENV:+ into ENVIMAX.COM.  The triple mode of DOSMAX
         confused people and many just didn't realize that DOSMAX could be
         put into AUTOEXEC.BAT to move the master environment.

    (6)  Changed the Windows support method once again.  The /Y is gone (the
         old high file support method) and /W+ now works from both the .SYS
         and .EXE command lines.  This new method uses 256 bytes at 60:0 and
         if this is a conflict, you must use FW4-6.BAT and FW3.BAT after
         disabling the support with /W-.

    (7)  Added support for DRDOS 6.0.  See EXAMPLES.DOC.

    (8)  Added feature which preloads the .EXE portion of the DOSMAX into
         EMS and improves ease of configuration for STACKER/SSTOR users.
         Most of the time it is not necessary to duplicate DOSMAX.EXE on
         both the compressed and uncompressed drives (unless EMS 4.0 is not
         present).

    (9)  Added support for loading self high when DOS=UMB is configured

   (10)  Added option response file input with @filename.opt syntax

    (Version 2.1)::

    (1)  Fixed problem with finding DOS 6.0 CONFIG variable for machines
         whose bios'es don't intialize memory properly.

================================================================================