DIAGS.EXE  
       
              Special Serial, Parallel, Video diagnostics for the PC  
       
                             Written by Joan Riff for:  
       
                         Computerwise Consulting Services  
                          P.O. Box 813, McLean, VA 22101  
                                  (703) 280-2809  
       
   

   


                
                                   Introduction 
       
     DIAGS is a tool for the advanced PC  user,  period.  It  is  NOT  for  the  
     general  public.  This manual will not explain things in elementary terms.   
     If you know what a 6845 is,  and  what  an  8250  is,  and  what  parallel  
     handshaking lines are, then DIAGS will be extremely useful to you. If not,  
     then  you  may  have better things to do with your time than try to figure  
     out this program.   
       
     DIAGS started  out  as  a  testbed  for  our  new  interrupt-driven  RS232  
     libraries. The Serial Port Diagnostics were the first written, to test the  
     Microsoft version 3.0 'C' interface to these routines.   
       
     It  has  since  grown.  As  we  have  added more assembler routines to our  
     library, we have added corresponding DIAGS functions to test them.   
       
     Additionally,  DIAGS has been expanded as we experienced the need for  new  
     diagnostics capabilities. So the Parallel Port diagnostics were added when  
     we  had  to debug yet another unknown printer's handshaking.  And the 6845  
     diagnostics were added when we needed to test various  video  tricks  like  
     displaying 30 lines of text, smooth scrolling, etc.   
       
     As it now stands, DIAGS is a very powerful facility for:  
       
          1) Testing all sorts of asynch communications lines  
       
          2) Testing printer handshaking and cable wiring  
       
          3) Examining an unknown system's DOS environment, including: 
 
               a) Interrupt vectors  
               b) Resident device handlers  
       
          4) Directly manipulating the 6845. 

   



                                     Main Menu 
 
     The  main DIAGS menu displays information about the machine and about DOS,  
     and presents a list of the various diagnostics that  are  available.  When  
     you exit a particular diagnostic, you are returned to this main menu.    
     



 
 
                                    (D)isk Info 
       
     Let's describe the weakest and least important diagnostic first. 
       
     The DISK INFO selection from the main menu displays just about every-thing  
     that can be determined about a disk. Make sure that you have a diskette in  
     the indicated drive before selecting this option.   
       
     Since  there  are  other utilities which do just about everything that you  
     may want to do with a disk, we haven't done much with this diagnostic.  We  
     just display disk information as reported by DOS as well as by the  disk's  
     Boot Record.   
       
     Once in the Disk Info screen, the following keypresses are available to 
     you:  
       
          ESC - return to the main DIAGS menu 
 
          ALT-V - verify a diskette by reading every sector via DOS INT   
          025h. This is SLOW!!!! Think of this as a demo of just how 
          slow INT 025h can be.  
       
          ALT-R - reset drive. Doesn't do much, huh? That's what we  
          wanted to see.  
 
          A thru Z - select new drive for which statistics are to be 
          displayed. Again, be sure that you have a disk in whatever 
          drive you select.  
       
     That's it. Not much to it. If you need to do more, then use:  
       
          The Norton Utilities  
          Quaid's Disk Explorer  
          Central Point Software's Option Board  
       
 
 


  




                             (I)nterrupt Vector Display 
       
     This selection from the main menu displays the system's Interrupt 
     Vectors. For each interrupt, the following information is displayed: 
       
          The interrupt number  
          The interrupt vector's address within segment zero  
          The Segment:Offset of its handler  
          The interrupt's name and/or use  
       
     If an interrupt points to an IRET, then that fact is reported by a 
     highlighted "[IRET]" displayed after the name. 
 
       
     Once in the Interrupt screen, the following keypresses are available to 
     you:  
       
          ESC - exit back to main menu 
          Home - scroll display back to Interrupt 0 
          End - scroll display to the end of the interrupts (F0 thru FF)  
          PgDn - scroll to the next page of vectors 
          PgUp - scroll up to the previous page of vectors  
          Up Arrow - scroll up 1 line     
          Down Arrow - scroll down 1 line 
   
 
 
 
                              (P)arallel Diagnostics 
       
     This  is  a  more complicated set of diagnostics.  It allows you to do all  
     sorts of useful things with the parallel ports. We use these routines when  
     we're trying to figure out whether or not  some  new  printer  is  working  
     properly with the system.   
       
     At the top of the screen is displayed:  
       
          The number of parallel ports on the system (1 thru 4)  
          The number of the currently-selected printer (0 thru 3)  
          The base I/O address of the currently-selected printer  
          The trip character that is currently set (see below)  
          Whether interrupts are allowed or disallowed during sampling 
       
     The Parallel Port Diagnostics menu gives you the following choices: 
       
          (I)nit printer - does a ROM BIOS "init printer" call. 
       
          (E)nable  Interrupts  during  sampling - toggles the indicator on the  
          top line,  which indicates whether INTs are to be dis-allowed  during  
          sampling.   
       
          (N)ew  Trip  character  - allows you to specify a new character to be  
          sent to the printer to 'trip' it. This is initially a Linefeed.   
       

          (P)rinter switch - selects next printer (in sequence) as the  current  
          printer.   
       
          (T)rip printer - sends the current Trip character to the printer, and  
          then  captures  the  printer  Status port lines using a special high- 
          speed capture routine.  These lines are  dis-played  in  oscilloscope  
          format,  allowing  you  to  see at a glance the operation of the BUSY  
          line, ACK line, etc. Interrupts will be inhibited during the sampling  
          if the top line of the display shows "No Ints".  Press  ESC  to  exit  
          from the display of the status lines.    
          
       
          (U)nique  Printer  setup - sends custom codes to set various specific  
          printers into various modes. The printers currently supported are:   
          
       
               Data Products 8070 (and perhaps IDS Color Prism)  
               IBM Graphics Printer (and certain Epsons)  
               Fujitsu DL-2600 (and perhaps Epson JX color series)  
               Okidata Microline 93  
               Diable 630 (and C.ITOH Starwriter, F-10, etc)  
               C.ITOH Prowriter 
   


 
       
          Follow the prompts that are displayed when you make this 
          selection.  
       
          (Q)uit parallel diagnostics - to return to main menu  
       
          The following three selections are  invaluable  for  checking  proper  
          printer cabling and handshaking:  
       
          (D)ata lines - displays the parallel port  Data  I/O  port  lines  in  
          oscilloscope-like   format.   Press  ESC  to  exit  the  oscilloscope  
          display.   
       
          (S)tatus lines - as above,  but lines displayed are from the parallel  
          Status I/O port.   
       
          (C)ontrol lines - as above,  but lines displayed  are  from  parallel  
          Control I/O port.   
       
          The following selections send various strings to the printer:  
       
          (F)ox message - sends a continuous FOX message  to  the  printer  via  
          direct I/O (bypassing the ROM BIOS). Press ESC to stop it.   
       
          (A)scii character set - sends the complete ASCII character set to the  
          printer via direct I/O (bypassing the ROM BIOS).  No carriage returns  
          are sent. Press ESC to stop it.   
       
          (H)oriz and vert alignment tests - send various Formfeed,  Tab,  line  
          spacing  and  Backspacing  sequences  to printer.  This is useful for  
          testing the results of (U)nique printer setups,  and to  see  if  the 

          printer  supports  true  backspacing.  This  selec-tion  has  its own  
          submenu, which is exited via ESC.   
   
 


 
 
                             (S)erial Port Diagnostics 
       
     If you do PC communications as much as we do,  then this part of DIAGS  is  
     for  you!  It  provides  a  very powerful look at the comm line.  Its most  
     intriguing feature is the ability to serve as a line monitor  between  two  
     serial devices.   
 
     When  you  select  "Serial  Diagnostics"  from the main menu,  your screen  
     becomes a terminal screen.  At the top of the screen is displayed  various  
     port information as follows:  
       
          Whether the port is open ("OP") or closed ("CL")  
          The current serial port number  
          The current baud rate  
          The number of data bits being used  
          The type of parity being used  
          The number of stop bits being used  
          Whether the existing 8250 parameters are being re-used (this 
               feature is only used by us, for internal testing)  
          What port is being wrapped to (more on this later)  
          Whether keypresses are echoed to the screen  
          Whether DEBUG mode (HEX display) is set  
       
     To the right of this information are various stats,  displayed only if the  
     port is open and stats have been enabled. These stats include:  
 
          The size of the RS232 output queue (in HEX)  
          The size of the RS232 input queue (in HEX)  
          The status of Carrier Detect and DSR  
          The number of times (in HEX) that the following have occurred: 
       
               RING  
               BREAK  
               Framing Error  
               Parity Error  
               Overrun Error  
       
     Once the port has been opened,  any "normal" keys that you press are  sent  
     over  the  comm line by being queued into the output queue.  Incoming data  
     appears on the screen.  Incoming and outgoing characters are displayed  in  
     different colors, so that you can tell what's what.   
       
     The RS232 routines are entirely interrupt-driven. The output queue will be  
     serviced  only  if  the  8250  is properly interrupting the 8088.  This in  
     itself is a valuable test of proper system operation.  If  the  output  or  
     input  queue  sizes  stay  "stuck" at a non-zero value,  then something is  
     wrong with your system.   
   



      Besides the "normal" keys, you may use the following keypresses: 
 
       
          ALT-S - switch display between port 0 and port 1 (COM1: and  
          COM2:).  
 
          ALT-M - bring up a menu of miscellaneous features:  
 
               HANGUP the phone by dropping DTR  
               PICKUP the phone by raising DTR  
               RESET the Hayes 1200b by OUT1 toggle  
               FLUSH input and output queues  
               CRLF control (how to display incoming CR and LF)  
               STATS control - turning the stats off can speed up the 
                    terminal display considerable  
               TRAP - control what happens when you press ALT-T to trap 
                    some 8250 register  
       
          ALT-X - initiate an XMODEM transfer. This we use to test the  
          accuracy of XMODEM as implemented in other software packages.  
 
          ALT-P - control port parameters. This includes: 
 
               port OPEN and CLOSE  
               BAUDRATE  
               DATA bit selection  
               PARITY setting  
               STOP bit selection  
               REUSE of the 8250 params (for our internal use)  
               ECHO (of local keypresses) on/off  
               WRAP of incoming data to another comm port  
               DEBUG display toggle  
       
          ALT-T - to trap the data lines from a previously-defined 8250   
          register  
 
          ALT-R - display various 8250 registers  
 
          ALT-B - to send a BREAK       
 
          ALT-W - wait (do nothing) till next keypress. This is useful 
          for pausing a fast-moving display.  
 
          ALT-Q - quit back to main menu 
 
          ALT-F - send a single FOX message over comm line 
       
     Most of these functions contain their own prompts,  and require no further  
     explanation. Some, however, need to be explained in detail.   
       
     The  continuous  updating  of  the stats on the top line can slow down the  
     terminal display.  Turning  stats  off  (ALT-M  S)  can  speed  things  up  
     considerably.   
    
 

     The  baudrate  is  continuously  variable,  from  2 to 38400.  You are not  
     limited to "standard" PC baud rates.   
       
     If you want to clear the screen and reset the stats,  try switching  ports  
     twice (ALT-S ALT-S).   
       
     To  trap and display an 8250 register in the middle of communication,  you  
     must first define the register to be trapped (ALT-M T)  and  whether  INTs  
     are to be allowed during the sampling that follows.   
       
     Having done that, you cause the trap by pressing ALT-T. At that instant, a  
     special  high-speed  assembler  routine  is  executed  which  samples  the  
     designated register once every 50 machine cycles or so until  420  samples  
     have  been taken.  These sample bytes are then displayed as a screenful of  
     HEX bytes.  You may highlight a particular byte via the  arrow  keys.  The  
     highlighted  byte's interpretation is displayed on the message line toward  
     the top of the screen. Press ESC to exit this trap display.   
       
     The "wrap" feature is very useful.  It may be used to allow DIAGS to serve  
     as a line monitor located between two serial devices,  among other things.  
     Every incoming character is "wrapped" as an output to  whatever  port  you  
     have  specified  as the "wrap" port.  If you select as the "wrap" port the  
     same port that you're using,  then you have in effect become a full-duplex  
     system. The serial device connected to that port will see its "keypresses"  
     echoed back to itself.   
       
     Assuming  that  you  have  two  serial ports,  you may use DIAGS as a line  
     monitor by wrapping each port's input to the  other  port.  You  can  then  
     switch  between  ports (ALT-S) and generally watch everything that goes in  
     either direction.  You can turn on the DEBUG  display  (ALT-P  G)  to  see  
     things in more detail.   
   
 


 
 
                         (R)esident device handler display 
       
     This  main  menu selection allows you to see a list of all resident device  
     handlers.  As you highlight each handler's name (via the  left  and  right  
     arrow keys), the device's attributes are expanded on the screen. Press ESC  
     to exit this display.   
       
     Block devices are indicated by device names of the form "BLOCKnnn",  where  
     nnn is the number of devices supported by this block device handler.    
     
   


                               (V)ideo Manipulation 
       
     If you want to do some fancy 6845 programming,  then the Video  diagnostic  
     will  be of great interest to you.  It allows you to examine and alter the  
     6845 registers in a most graphic fashion.   
       
     Toward the top of the screen is a two-column list of all  6845  registers,  
     and  one  or  two  of  the special IBM PC video registers (the MODE and/or  
     COLOR registers).  There is a ">" pointer,  showing you which register  is  
     being worked with.   
       
     For each 6845 register, two values are shown:  
       
          1) The original value, as set by the ROM BIOS  
          2) The current value as set by you  
       
     You  move  the  ">"  pointer to various 6845 registers via the up and down  
     arrow keys.  As you select each 6845 register, that register's bit pattern  
     is expanded on the bottom half of the screen.   
       
     You  can  change the currently-selected 6845 register's value by using the  
     "+" or "-" keypad keys to increment or decrement its value. + - 
       
     You can also use the left and right arrow keys to move the  "bit  pointer"  
     across  the  various  bits  of the expanded byte on the bottom half of the  
     screen.  Pressing "1" or "0" sets or clears the bit currently pointed  to.  
     This is an alternate way to change the current value of a 6845 register.    
     
       
     The  updated  6845  registers are loaded into the 6845 ONLY WHEN YOU PRESS  
     RETURN.  This allows you to make extensive changes  to  registers  without  
     having intermediate states foul up the display.   
       
     If you hose things up and get an unreadable screen, just press ESC to exit  
     the Video Diagnostics, then enter it again. The 6845 is reset on exit from  
     the Video Diagnostics.   
       
     If  you  are  using  a  Color/Graphics Adapter,  then you may press "S" to  
     toggle Snow on or off.  The upper-right corner of the  display  shows  the  
     current status of snow as follows:  
       
          "Snow: YES" means that no effort is being made to eliminate 
          snow, and that snow is present (although you won't see it if 
          you have a good Color/Graphics board)  
       
          "Snow: NO" means that snow is being eliminated by our video 
          software.