Greetings from MEL's Diner BBS!       (909) 686-1522


IP is a serial interrupt and port verification program. Just run "ip" and the
program will check the RAM bios data area to see what port addresses your 
system is currently aware of. The program will then run a diagnostic routine
to discover any additional ports, and update the data area accordingly. In 
the meantime, IP will also tell you which IRQ's are being used by what ports. 

NOTE: IP does not assume that address 0x3F8 is connected to IRQ3, 0x2F8 to 
IRQ4, etc... as several other serial port diagnostic utilities do. IP acually
enables the 8250's interrupts and does a functional check of the 8259 
interrupt controller chip and it's associated circuitry. In doing so, IP 
determines exactly which hardware ports are connected to which IRQ's.

IP will now take a command line switch (/n or /x). The /n (default) switch 
tells IP to check standard IBM port addresses (3F8h,2F8h,3E8h,2E8h). The /x 
switch will allow IP to look for additional addresses which are sometimes 
used in nonstandard hardware schemes. The /x switch should be used with 
caution as some non-standard hardware layouts will crash unexpectedly when 
one of these additional port addresses are searched by IP. 

EXAMPLE:

Interrupt and Port Verifier (serial) - Version x.xx
Copyright (C) AM Research Co. 1990-1994.

Bios reports --> COM1:3F8 COM2:2F8 2 serial ports

PART#  BASE IRQ BAUD   OUTPUT LINES      INPUT LINES      INTERRUPT STATUS
					  DTR RTS GP1 GP2  CTS DSR DCD RI   RDA TBE RLS MSR 8259A
8250-B 03F8  4  2400  ( ) ( ) ( ) ( )  (*) (*) (*) (*)  ( ) ( ) ( ) ( )  OFF
16550A 02F8  3  1200  (*) (*) ( ) (*)  ( ) ( ) ( ) ( )  (*) ( ) ( ) ( )  ON!
8250A  03E8  4  2400  ( ) ( ) ( ) ( )  (*) (*) ( ) ( )  ( ) ( ) ( ) ( )  OFF

3 serial ports found!  Updating bios data area.

This utility brought to you by MEL's Diner BBS - (909) 686-1522


EXPLANATION:

The first info line after the copyright notice tells us that the system
bios data area (RAM) thinks that there are two serial port addresses in-
stalled in the computer under test. These addresses are found by the bios
POST routines when the system is first booted. Many older bios test routines
only check for COM1 and COM2 as the example shows.

After reading the bios, the program prints a list of each port address that
it found to contain a serial port. Each line will begin with the part number
of the UART chip which was found. After the part number the port address is
shown followed by the hardware IRQ line that the port is currently connected
to.

This is the place to look if you are having a problem that you suspect is due 
to an IRQ conflict. Generally speaking, it is ok for two ports to share the 
same IRQ as long as your work only uses one of the hardware devices at at 
time.
 
Next will follow the current baud rate for that port followed by the current
values of the port's output lines, input lines and the interrupt enable 
register. The values displayed may make more sense if you check the 8250 data 
sheet for register descriptions, etc. 

Next will follow the current interrrupt status of the 8259A interrupt 
controller's mask. Please note that almost all serial ports will have their 
interrupt mask turned OFF at the time you are performing the test. When an
application program decides to activate this port's interrupts, this mask
will be enabled and the port will now be able to generate an interrupt for
processing.

It is very important for the operator to realize that IP is a diagnostic
utility which is meant to be used in checking/troubleshooting a newly modifed
or questionable computer. As such, IP may therefore interfere with the 
system's operation as it actively enables and operates each port's interrupt 
circuitry. 

IP will probably NOT work properly if you have loaded any type of software 
that activates the port's interrupts such as fossil drivers, etc. IP may very 
well cause a crash if used with any type of multi-tasking software.

Finally, IP will modify the bios data area to report any additional ports it
discovers.

I would be quite interested in hearing from anyone with comments, 
suggestions, crashing reports, etc...

As you might imagine, IP remains Copyright (C) 1990-1994, AM Research Co. 

Hope you enjoy using it.

												  bye for now...
													  
													  MEL









IP HISTORY

Version 1.32 - Added 8259A register display.

Version 1.31 - Fixed problem displaying irq numbers when interrupts are
			   activated.

Version 1.30 - Modified the default data display format. The previous, 
			   register oriented display format is still available by using 
			   the /R command line switch. Removed the /U command line 
			   switch.

Version 1.23 - Added /P command line switch to create an output file called
			   ports.dat.

Version 1.22 - Fixed bug in the bios data area update routine. (It didn't
			   always update it!)

Version 1.21 - Fixed bug whereby NS16550's and NS16550A's wouldn't produce 
			   an interrupt if the fifo buffers were activated. Also added
			   NS16552 detection.

Version 1.20 - Added extended base addresses. Also protected system from the
			   isr test if interrupts are already activated.

Version 1.10 - Rewrote the isr. Works much better now.

Version 1.04 - Yet more bugs.

Version 1.03 - More minor bugs.

Version 1.02 - Minor bug fix.

Version 1.01 - First release.