CHEAP AND EASY REAL-WORLD CONTROL FUNCTIONS FROM YOUR PC




Here's a cheap and easy way to make an IBM-compatable PC perform
real-world control functions using NO special hardware, and the
software you are already familiar with.

LPTREAD is a program that allows you to read directly from
individual pins of a parallel printer port, thereby using the
printer port as a data acquisition device for external equipment.
LPTREAD punches a predefined character string through the
keyboard buffer, one string for each of the eight data pins on
the parallel port, just as if it had been typed at the keyboard
whenever the associated pin is connected to the port's ground
pins (pins 19 through 25).
                                                            
This makes it possible to have the PC monitor up to eight
external switch-closure type devices like alarm systems,
laboratory monitors, process control switches, or pushbuttons.
You can even connect the port to any TTL level device driver
circuit.

LPTREAD version 2.0 addresses five pre-mapped printer port
addresses, although these may have different physical addresses
on different computers. Your LPT1 might be someone elses LPT2. To
see a list of available printer port addresses and their mapping
numbers, type "LPREAD" with no parameters.

The calling protocol is this:

                          LPTREAD n NR

where n  := printer port address, 1 through 5, and [NR] is an
optional parameter which tells LPTREAD to operate in Non-Resident
mode.

Obviously, fiddling with your computer hardware is a little
risky. However, the LPT card is usually very resilient and
difficult to damage. Just be careful to observe all normal
electronic safeguards.


                     DEFINING KEYBOARD MACROS

Each of the eight data bits on the LPT port can be assigned a
key sequence of up to 40 bytes. This can include imbedded
carriage returns and control characters as well as alphanumerics.

The keyboard definition file, LPTREAD.DEF contains the macros.
LPTREAD.DEF is an ASCII flat file with eight variable length
records delimited with a carriage return/line feed pair. You can
create and modify this file using most word processors which do
not embed invisible control characters in the text (i.e. Wordstar
in Nondocument mode).


Following is an example of a valid LPTREAD.DEF file. Each text
line is a macro assigned to the associated data line, one through
eight. Semicolons are interpreted as chr(13) (a carriage return).
All lines should be flush-left in the file (no leading spaces,
unless you want them as part of the macro).

                         A;123;
                         B;
                         Jerry Garcia;
                         M;The Front Gate is Open!;
                         M;Someone's at the back door.;
                         1
                         2
                         Q;CD/;MENU.BAT



LPTREAD is Copyright (c) 1992 by Rob Cosgrove and is distributed
by Precision Data Corporation in Memphis, Tennessee. You are
hereby granted a limited license to use and distribute LPTREAD
and this documentation non-commercially, as long as you 1) don't
charge money for it, and 2) don't modify LPTREAD.COM to eliminate
the copyright message.

We can custom-modify LPTREAD for your application for our
regular programming rate of $70.00/hour.

We will also sell you limited rights to the source code, if you
want to modify it yourself. Source code costs $250, the only
limit being that you can't sell it as a stand-alone product to
compete in any way with LPTREAD itself. Otherwise, feel free to
include it in your own applications as often as you want.

LPTREAD is written for Turbo Pascal version 3.01.

If you send us a registration fee of $20.00 you will receive a
commercial version of LPTREAD, as well as a demo version of
LPTWRITE.COM (see the hype below).  We'll also put you on our
mailing list for future announcements of similar neat stuff. 

LPTWRITE is great for adding real-world control functions to
ANY program without difficult real-world programming. 

LPTWRITE.COM is a useful little program which allows you to
individually control up to eight external devices like relays,
LEDs, or TTL level devices by shelling out of your application,
and running LPTWRITE with parameters telling it which devices to
activate.

Check out the DEMO version of LPTWRITE, which contains complete
documentation and a simple schematic for the interface circuit.

Send $35.00 and receive the commercial versions of both programs.

We at PDC are available for consulting and programming using this
and other inovative technology for industrial control, data
aquisition, telemetry, and QC testing.

                
                   Precision Data Corporation
                  654 South White Station Road
                       Memphis, TN  38117

                        (901) 682-0732
 


                     CONTROL HARDWARE SCHEMATIC

                            for use with

                            LPTREAD.COM


    Parallel Port
      Connector
  -----------------
   Function    Pin
  _________________
                                             -----
     DATA 0    2 ---------------------------->   <--------+
                                                          |
                                             -----        |
     DATA 1    3 ---------------------------->   <--------+
                                                          |
                                             -----        |
     DATA 2    4 ---------------------------->   <--------+
                                                          |
                                             -----        |
     DATA 3    5 ---------------------------->   <--------+
                                                          |
                                             -----        |
     DATA 4    6 ---------------------------->   <--------+
                                                          |
                                             -----        |
     DATA 5    7 ---------------------------->   <--------+
                                                          |
                                             -----        |
     DATA 6    8 ---------------------------->   <--------+
                                                          |
                                             -----        |
     DATA 7    9 ---------------------------->   <--------+
                                                          |
                                                          |
                                                          |
     Ground   19 -----------------------------------------+



       -----
     -->   <--   :=   switch


You may find that you need to place 10K ohm pull-up resistors
between each of pins 2 through 9 and pin 17 (+ 5 VDC) to keep the
data pins from 'floating'.




         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 4,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.