CHEAP AND EASY REAL-WORLD CONTROL FUNCTIONS FROM YOUR PC


Here's a cheap and easy way to make an IBM-compatable PC perform
real-world control functions using NO special hardware, and the
software you are already familiar with.

LPTWRITE is a program that allows you to write directly to
individual pins of a parallel printer port, thereby using the
printer port as a control device for external equipment. It's
designed to be called from other programs by temporarily
returning to DOS, executing with parameters, then exiting back to
the calling program.

LPTWRITE can individually execute a data ON or data OFF state for
each of the eight data bits on the LPT port. These correspond to
pin 2 through pin 9 on the connector. Pin 17 is used as a +5vdc
supply, and the data state exists as a potential between each of
the eight data bits and pin 17.

LPTWRITE version 1.0 addresses printer ports 1 and 2, although
these may have different physical addresses on different
computers. Your LPT1 might be someone elses LPT2. You'll have to
experiment to see which is yours.

The calling protocol is this:

                      LPTWRITE n 00000000

where n  := printer port to write (1 or 2)

00000000 := output bite, binary-coded

The binary coded output byte contains one place for each of the
eight data pins on the LPT port. Entering a "0" in any of the
places turns OFF that pin, making it electrically neutral.
Entering a "1" in any of the places turns ON that pin, making it
electrically grounded.

As an example, the following command turns ON pins 2 and 4 on LPT
port 2, and turns OFF all others on that port:

                     LPTWRITE 2 01010000

LPTWRITE executes a data ON by connecting the pins to ground.
Placing a load between each data pin and pin 17 (see the
schematic) provides a way to make use of this state. There's
enough power on an average parallel printer board to run eight
jumbo 5-volt LEDs, eight low-power micro-relays, or to provide
input for any TTL level output driver circuit.

In the OFF state, each of the data pins is "floating" that is,
they are connected neither to ground nor to +5vdc. In a TTL
driver circuit, be sure to use 10K hold-down resistors between
each of the pins and LPT port ground, pins 19-25; AND be sure to
use pins 19-25 as common ground for your custom circuits.


When using micro-relays, be sure to place a surge-protection
diode across each relay to prevent damage to your computer by the
current generated in the relay coils when they de-energize.

Obviously, fiddling with your computer hardware is a little
risky. However, the LPT card is usually very resilient and
difficult to damage. Just be careful to observe all normal
electronic safeguards.

Initialize the LPT port you intend to use in your programs by
including the following command in your AUTOEXEC file:

                    LPTWRITE n 00000000

where n := the port number for your computer. This forces the
port to a binary zero and sets up the background task which
handles the port communications with your program.

Commercial versions of LPTWRITE will address all available pins
on all ports, and will allow for READING as well as writing
individual pins. These versions will be available as libraries
and OBJ modules for linking with your applications, and also as
small TSR's.

LPTWRITE is Copyright (c) 1991 by Rob Cosgrove and is distributed
by Precision Data Corporation in Memphis, Tennessee. You are
hereby granted a limited license to use and distribute LPTWRITE
and this documentation commercially or non-commercially, as long
as you 1) don't charge money for it, and 2) don't modify
LPTWRITE.COM to eliminate the copyright message.

If you send us a registration fee of $20.00 you will receive a
commercial version of LPTWRITE which writes to more than eight
pins on each port and has no sign-on message, as well as a demo
version of LPTREAD.COM (see the hype below).  We'll also put you
on our mailing list for future announcements of similar neat
stuff.

LPTREAD.COM is a useful little TSR which watches an LPT port and
executes up to eight different keystroke sequences through the
keyboard buffer - one for each of the eight data bits on the LPT
port. Close a data bit on the LPT port, and LPTREAD types the
associated key sequence through the keyboard - no matter what
software is running.

LPTREAD is great for adding real-world data acquisition functions
to ANY program without difficult real-world programming. LPTREAD
reads simple switch closures like in alarm systems, laboratory
monitoring, simple robotics, and automation. The commercial
version has programmable keyboard macros, up to 255 bytes long,
for each of the eight data bits PLUS some extra pins.

Send $35.00 and receive the commercial versions of both programs.

We at PDC are available for consulting and programming using this
and other inovative technology for industrial control, data
aquisition, telemetry, and QC testing.

                
                   Precision Data Corporation
                  654 South White Station Road
                       Memphis, TN  38117

                        (901) 682-0732
 


                     CONTROL HARDWARE SCHEMATIC

                            for use with

                            LPTWRITE.COM


    Parallel Port
      Connector
  -----------------
   Function    Pin
  _________________

     DATA 0    2 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
     DATA 1    3 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
     DATA 2    4 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
     DATA 3    5 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
     DATA 4    6 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
     DATA 5    7 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
     DATA 6    8 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
     DATA 7    9 ----------------------+--VUVUVUVU--------+
                                       |                  |
                                       +------|<----------+
                                                          |
                                                          |
     + 5 VDC  17 -----------------------------------------+



     VUVUVUVU   :=   Load (Relay, LED, or TTL level input)

     ---|<---   :=   1N4002 Silicone Rectifier

The Loads in this schematic are low-power 5 VDC relays. Solid
state relays work best. For testing you can use 5 volt LEDs. If
using an inductive load (relays), be sure to use the 1N4002
diodes to protect your computer equipment against surges from the
coils.




         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 4,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.





         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 4,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.