======================================================
             =                                                    =
             =                                                    =
             =          Parallel Port Information System          =
             =                                                    =
             =                   version 1.45                     =
             =                                                    =
             =                        by                          =
             =                                                    =
             =                     Jay Lowe                       =
             =                    Don Schuman                     =
             =                                                    =
             =             Parallel Technologies, Inc.            =
             =                                                    =
             =                                                    =
             ======================================================












                                  Version 1.45
                                  27 Oct 1994






                          Reference Sites for Parallel

                    Compuserve Home:    IBMHW forum (go IBMHW)
                    Internet Home:      netlab2.usu.edu/misc




     ======================================================================
     Parallel.Exe, v1.45, 27 Oct 1994           Parallel Technologies, Inc.
     Parallel Port Information Utility                    10603 170th Ct NE
     (C) Copyright 1993-1994 Jay Lowe                     Redmond, WA 98052

     This program may be used                             Lab  206-869-1136
     free of charge subject to the                        Fax  206-869-1133
     Restricted License Agreement                  Compuserve     76640,203
     as stated below                           Internet jaylowe@halcyon.com
     ======================================================================



Parallel Port Information System                                     Page 2
---------------------------------------------------------------------------

     Front Matter
     ------------


     IMPORTANT: This software is provided AS-IS under a license agreement
     stated below (see SOFTWARE LICENSE AGREEMENT). YOU ARE RESPONSIBLE for
     the safe usage of this program.  This requires that you READ THE
     DIRECTIONS if you are going to use the loopback feature for IRQ
     detection. We are informing you of the danger of physically damaging
     your parallel port if you are not CAREFUL AND GENTLE when inserting
     the loopback wire. We strongly recommend that you follow the procedure
     of making a LOOPBACK EXTENSION CABLE as described below. To the best
     of our (extensive) knowledge, there is no electrical danger to
     yourself or to your system or to the parallel port, since parallel
     ports are designed to withstand permanent shorts across any of their
     pins. HOWVER WE DO NOT GUARANTEE AN OF THIS AND CAN ACCEPT NO
     LIABILITY since we cannot control what you or your vendor may do.



     Parallel.Exe, Parallel.Doc, and all of the associated components of
     this utility are copyrighted material and may not be reproduced,
     redistributed, or sold without the express written consent of Parallel
     Technologies, Inc, except as provided by the License Agreement.


     Some of the terms, names, and/or symbols used in this document are the
     trademarks of the companies which own them.


     Permission is hereby given for distribution of Parallel on a not-for-
     profit basis.  Users may upload and share Parallel, provided it is not
     modified in any way.  Commercial vendors may make Parallel available
     via bulletin boards or other electronic forums, but may not distribute
     Parallel with their products without the permission of Parallel
     Technologies, Inc.  Parallel may be distributed by shareware vendors
     and by public electronic forums provided that such distributors do not
     charge more than $10 per copy.


     Support for Parallel and parallel port related issues is available
     only via Compuserve or Internet Email to the addresses given on the
     cover page of this manual.


     Parallel Technologies, Inc. does not provide telephone support for
     this program.



Parallel Port Information System                                     Page 3
---------------------------------------------------------------------------

     Acknowledgements
     ----------------

     We would like to express our appreciation to the many people and
     organizations who have given of their time and expertise to provide
     information and support for Parallel in various ways.  Some of these
     contributors include:

          Parallel Port Chipset Vendors:

               Intel Corporation
               Standard Microsystems Corporation
               National Semiconductor
               Chips and Technologies

          Parallel Port Direct Sales Vendors:

               Farpoint Communications
               JAZ Computer Products
               Essential Data, Inc.

          Standards Organizations:

               Members of the EPP Standards Committee
               Members of the IEEE 1284 Standards Committee

          Individuals:

               Larry Stein, Farpoint Communications
               Prof. Joe Dupnik, Utah State University
               Don Watson, Compuserve IBMHW Forum Sysop

          The users:

               who have reported test results, bugs, and feature requests!

          And the innumerable hackers who have gone before.


          My thanks to all of you for your generosity.


               And if I've left anyone out, my apologies. Please remind me.



Parallel Port Information System                                     Page 4
---------------------------------------------------------------------------

     Table of Contents
     -----------------



     FRONT MATTER                                                         2


     ACKNOWLEDGEMENTS                                                     3


     TABLE OF CONTENTS                                                    4


     WELCOME TO THE PARALLEL PORT INFORMATION UTILITY                     7


     QUICK STARTING PARALLEL                                              8


     DETAILED PROGRAM OPERATION                                           9

      How to Prepare Your System for Best Results                         9

      How to Run Parallel.Exe                                             9

      How to Get Quick Help                                               9

      How to Prevent Scrolling                                            9

      How to Save Parallel's Output                                       9

      How to Avoid the Funny Line Drawing Characters                      9

      How to get Help with your Parallel Port Questions                  10


     INTERPRETING PARALLEL'S DISPLAY                                     11

      Parallel Port Type                                                 11
       No Port                                                           11
       4bit ports                                                        12
       8bit ports                                                        13
       EPP ports                                                         14
       ECP ports                                                         16

      IO Address                                                         18

      Understanding the IRQ Level                                        20

      Understanding the BIOS Name                                        22

      Understanding the Notes and Comments                               24



Parallel Port Information System                                     Page 5
---------------------------------------------------------------------------

     AUTOMATIC IRQ DETECTION                                             30

      IRQ detection using the LoopBack Feature                           30

      Understanding Port Float                                           32

      TechNote: Making Your Own Loopback Connector                       33


     MISCELLANEOUS TOPICS                                                34

      Technote: Pseudo-Bidirectional Ports, A Special Case               34


     PARALLEL PORT STANDARDS                                             35

      4bit and 8bit parallel ports                                       35

      EPP Specification                                                  35

      ECP Specification                                                  35

      IEEE 1284 Specification                                            36

      Parallel Port Standards Diagram                                    37


     PARALLEL PORT BUYER'S GUIDE                                         38

      4bit parallel ports                                                38

      8bit parallel ports                                                38

      EPP Parallel Ports                                                 39

      ECP Parallel Ports                                                 41

      Advanced Parallel Port Chipsets                                    43


     VENDOR CONTACT INFORMATION                                          44


     TECHNICAL SUPPORT                                                   45


     ABOUT PARALLEL TECHNOLOGIES, INC.                                   46

      Firsts, Bests, and Mosts                                           46

      Partial List of Parallel Technologies' Developments                46

      Parallel Port Developer's Kits                                     47
       Level One Developer's Kit                                         47



Parallel Port Information System                                     Page 6
---------------------------------------------------------------------------

       Level Two Developer's Kit                                         48
       Super IEEE 1284 Developer's Kit                                   48

      DirectNet -- The Parallel Port Networking System                   48

      Parallel -- the Parallel Port Information Utility                  49

      Product Licensing                                                  49

      Development Services                                               50

      Consulting and Training                                            50


     SOFTWARE LICENSE AGREEMENT                                          51



Parallel Port Information System                                     Page 7
---------------------------------------------------------------------------

     Welcome to the Parallel Port Information Utility
     ------------------------------------------------

     Parallel is a simple utility which displays the configuration of the
     parallel ports (LPT ports) in your system. Parallel is useful for:

         1.  Configuring parallel port software such as Windows printer
             connections, parallel port device drivers, and print spoolers.

         2.  Resolving technical support problems with parallel devices,
             including printers and external peripherals such as network
             adapters, portable disks, tape drives, CD-ROMs, floppies, etc.

         3.  Configuring your parallel ports for best performance.

         4.  Resolving pesky IO address and IRQ contention problems.

         5.  Measuring the performance capabilities of your parallel ports.

         6.  Learning how your particular system's CMOS configuration
             relates to the actual configuration of your parallel ports.

         7.  Making informed decisions when buying parallel ports and
             external parallel port devices.

         8.  Getting the best parallel port performance for your dollar.

         9.  Experimenting with your parallel port configuration.

         10. Solving problems associated with print spoolers and network
             print capture programs which redirect printer output by
             changing the port mappings kept in the LPT Bios data area.

     Now is a good time for you to learn something about parallel ports.
     Parallel ports are becoming increasingly useful due to the recent
     explosion in the popularity of portable and external peripherals.
     New parallel port standards (such as EPP and ECP ) are breaking
     performance barriers and allowing full bus speed operation.

     Parallel ports have traditionally been perceived as "printer ports",
     which explains a lot about their idiosyncrasies. In fact, a relatively
     small percentage of parallel ports are actually used for printing. The
     ratio of PCs to printers is usually "many to few" in a group setting,
     and as networking and networked printers become increasingly common
     this trend will increase. In general, PC parallel ports are usually
     available for other purposes ... for portable, external peripherals
     and parallel port networking (Desktop and Personal Area Networking).

     There are major performance differences between different types of
     parallel ports and parallel port devices, and these differences are
     becoming of increasing significance to consumers. These applications
     of Parallel are discussed in more detail below. But first let's take a
     quick look at how you run the program itself and interpret the various
     information it displays.



Parallel Port Information System                                     Page 8
---------------------------------------------------------------------------

     Quick Starting Parallel
     -----------------------

     Parallel operates by testing each of the standard addresses in your
     system where parallel ports might be found and gathering a broad
     assortment of useful information about the specific port behavior.
     Parallel tests the ports and then produces a compact display which
     is convenient and easy to read. You may need to refer to these
     instructions or the built-in reference screen a few times until you
     learn what the various columns of information mean.

     How to use Parallel:

        Step 1 =>   Disconnect any attached parallel port peripherals such
                    as printers, LAN adapters, disks, CDROMs, etc

        Step 2 =>   Run PARALLEL from the DOS command line (not in Windows)

        Step 3 =>   Read the display as described below.

     Parallel will display five columns of information containing one or
     more lines about each port. The columns are:

       Port Type         The parallel port's IO capabilities. Types are:

                           No Port   -- No port is exists at the address
                           4 bit     -- A "unidirectional" port
                           8 bit     -- A "bidirectional" port
                           EPP       -- An Enhanced Parallel Port
                           ECP       -- An Extended Capabilities Port

       Address           IO Base Address of the port (3BC, 378, 278)

       IRQ               Interrupt level associated with the port (5 or 7)

       BIOS Name         Logical device name of the port (LPT1, LPT2, LPT3)

       Notes             A wide assortment of comments, warnings, and
                         miscellaneous additional information

       Port              On a single line, after the columnar display,
       Strangeness       Parallel ports a magic number called the
       Factor.           `Port Strangeness Factor'.

     This is simply the total number of strange or unusual properties that
     Parallel has found when examining your configuration. If your ports
     are considered strange by Parallel, you might want to take some action
     to correct the situtation, or at least appreciate the peculiarity.

     The Port Strangeness is not reported if your configuration is boring.

     Detailed procedures for using Parallel are given in the next section.



Parallel Port Information System                                     Page 9
---------------------------------------------------------------------------

     Detailed Program Operation
     --------------------------

        How to Prepare Your System for Best Results
        -------------------------------------------

        Before running Parallel, temporarily remove all parallel port
        devices and software to establish a baseline configuration.

        Temporarily disconnect printers and other parallel port devices
        such as disks, network adapters, tape drives, etc, and disable any
        special parallel port software you may have running, like print
        spoolers or parallel port device drivers for external devices.

        The interaction of Parallel with external devices is discussed in
        some detail later on, and you may find that disconnecting these
        devices is not necessary in your configuration.

        How to Run Parallel.Exe
        -----------------------

        Type PARALLEL at the DOS command line.

        Parallel will display the parallel port type, IO address, IRQ
        level, BIOS names, and an assortment of informative notes about
        your parallel ports. Running Parallel in a Windows DOS box
        generally provides useless results.

        How to Get Quick Help
        ---------------------

            PARALLEL ?               ; displays the a reminder screen

        How to Prevent Scrolling
        ------------------------

        If, perchance, the display scrolls off the screen, which might
        happen if Parallel is reporting extensive notes about interesting
        conditions on your ports, then use the MORE command as follows:

            PARALLEL | MORE          ; pauses the output every screen

        How to Save Parallel's Output
        -----------------------------

        Use DOS redirection to write Parallel's display to a file:

            PARALLEL > filename      ; redirects output to a file

        How to Avoid the Funny Line Drawing Characters
        ----------------------------------------------

        Sorry, you can't.  We plan to add a switch to omit or replace the
        linedrawing characters for more convenient display via email, etc.



Parallel Port Information System                                    Page 10
---------------------------------------------------------------------------


        How to get Help with your Parallel Port Questions
        -------------------------------------------------

          1. Contact your vendor.

             Your vendor has a responsibility to support you in using
             their products.

                    If you have a problem with a parallel port device, your
                    vendor may already know a successful resolution.

                    Some vendors maintain BBS systems or Compuserve forums
                    on which may occasionally be found useful information,
                    utilities, and driver software upgrades.

                    Many vendors of parallel port peripherals offer very
                    good technical support IF YOU GIVE THEM A CHANCE ... or
                    several chances!  Don't hesitate to be persistant.

                    If you have a problem configuring a PC parallel port,
                    your vendor may already have a fix ready for you. This
                    may consist of a utility program, a BIOS upgrade, or a
                    manual procedure for configuring the port.  Since PC
                    vendors use a bizarre array of different methods for
                    parallel port configuration, your best bet is really
                    the vendor themselves. Alas, however, some PC vendors
                    are completely clueless about parallel ports, although
                    this situation is improving rapidly.

             Give your vendor a chance to resolve the problem. They are
             sometimes the most responsive source of assistance, AND THEY
             NEED YOUR INPUT.  Let them know what you want, and what you
             are doing -- it helps them adjust their plans and priorities.
             If you are not getting the proper assistance, call your
             vendor and let the product manager know about the situation.

             Think of it as your contribution to overall product quality!

             And if Parallel doesn't detect your ports tell your vendor to
             (a) get a copy of Parallel and (b) help us detect their port!

          2. Post your question in the IBMHW forum on Compuserve or in the
             IBM PC Hardware newsgroup on the Internet.

             Quite a few technical gurus read these forums and they tend
             to be generous in giving you the benefit of their experience.

          3. Email to CIS ID 76640,203 or jaylowe@halcyon.com.

             We can't promise immediate service (or indeed any service at
             all!) but we try to do our best.  Please understand that we
             get quite a few random technical inquiries and have to fit
             them around our development schedule.



Parallel Port Information System                                    Page 11
---------------------------------------------------------------------------

     Interpreting Parallel's Display
     -------------------------------


        Parallel Port Type
        ------------------

        Parallel reports the port type as 4bit, 8bit, EPP, ECP or No Port.

           No Port
           -------
                    No port was found at the given IO Address.  This is a
                    normal result if no parallel port is installed at the
                    given address.

                    Parallel tests all the base addresses at which parallel
                    ports are commonly found and displays at least one line
                    of information about each base address, even if there
                    is no port installed at that address.

                    Parallel uses a rather more robust technique for
                    detecting a port than is used in any of the BIOSes we
                    have seen. This means that Parallel can detect ports
                    which fail the BIOS boot-time tests. Parallel uses a
                    rotating bit test and assumes the port exists if any of
                    the bits at the port location respond correctly.

                    Parallel is also starting to detect specific advanced
                    parallel port chipsets. Intel and SMC detection is
                    present in this release and National and C&T detection
                    will be included in the next release.

                    False Positives.  Parallel can be fooled into thinking
                    that a port is present when it is not (false positive)
                    only if there is some other device which behaves like a
                    parallel port located at the address being tested.  We
                    have only seen this on one system, an off-shore 286
                    laptop which had several other design problems as well.

                    False Negatives.  There is one way in which Parallel
                    can be fooled into thinking that a port does not exist
                    (false negative). If an active device is connected to
                    the data lines and is providing enough power to
                    "overdrive" the port, then the port existance test will
                    fail because the incoming data from the device will
                    spoof the readback test. We have only seen Parallel
                    produce false negatives when an external device is
                    actively driving the port's inputs or when the Loopback
                    connector is incorrectly installed. By the way, in this
                    case, the PC's BIOS will also fail to detect the port.
                    Remember, Parallel works best when you disconnect any
                    external parallel port devices or cables.



Parallel Port Information System                                    Page 12
---------------------------------------------------------------------------

           4bit ports
           ----------

                    The port can do 8bit byte output and 4bit nibble input.

                    These ports are often called "unidirectional", and are
                    most commonly found on desktop bus cards (also called
                    IO expansion cards, serial/parallel cards, or even 2S+P
                    cards) and older laptops. This is still the most common
                    type of port, especially on desktop systems.

         HOW FAST:  4bit ports are capable of effective transfer rates of
                    about 40-60 KBytes/sec (KBPS) in typical devices and
                    can be pushed upwards of 140 KBytes/sec with certain
                    design tricks. The port speed is also affected by
                    electrical characteristics of the noise suppression
                    circuitry. A few ports have completely ridiculous
                    arrangements of noise suppression circuits which slow
                    them down quite dramatically and can prevent their
                    correct functioning with parallel port peripherals.

        TECH NOTE:  The sample transfer rates given here reflect the actual
                    performance of parallel port network adapters, disks,
                    etc. The raw transfer rate of the port itself is higher
                    but since most parallel devices use software strobing
                    to access data , the effective transfer rate is
                    dependent on the quality of the software supplied with
                    the device. Due to the recent explosion of parallel
                    port peripherals entering the market, there is an
                    extreme degree of variability in the quality and
                    performance of these devices and their drivers.

      WHERE FOUND:  4bit ports are found on about 50% of all systems and
                    about 75% or more of desktop systems prior to 1993.
                    Systems built after 1993 are more likely to have more
                    capable parallel ports such as 8bit, EPP, or ECP.

        TECH NOTE:  Many new systems, especially laptops, have parallel
                    ports whose mode can be selected via a CMOS setup
                    procedure.  Often these system default to a 4bit port
                    type even if more port capabilities are present.

                    We do not recommend 4bit ports; 8bit ports are better.

        TECH NOTE:  There is a class of "semi-bidirectional" parallel ports
                    which appear to the PC to be 4bit ports, but actually
                    have 8bit capability when they are connected to
                    external devices with strong drivers. These include the
                    original PC/AT parallel port. Parallel will report such
                    ports as 4bit ports but they may actually function as
                    8bit ports with better parallel port peripherals which
                    are especially designed to use such port as 8bit.



Parallel Port Information System                                    Page 13
---------------------------------------------------------------------------

                    It is actually possible to identify this type of port
                    using a side-effect of Parallel's loopback test. See
                    the special section below on Semi-Bidirectional ports.

           8bit ports
           ----------

                    These ports can do both 8bit input and output.

                    These ports are sometimes called "bidirectional ports",
                    but that term is often misused by some vendors to refer
                    to 4bit ports as well. Most newer laptops have 8bit
                    capability although it may need to be enabled with the
                    laptop's vendor-specific CMOS setup function. This is
                    discussed below. A relatively smaller percentage of LPT
                    bus cards have 8bit capability which sometimes must be
                    enabled with a hardware jumper on the board itself.

                    True 8bit ports are preferable to 4bit ports because
                    they are considerably faster when used with external
                    devices that take advantage of the 8BIT capability.

         HOW FAST:  8bit ports are capable of speeds ranging from 80-300
                    Kbytes/second, again depending on the speed of the
                    attached device, the quality of the driver software,
                    and on the port's electrical characteristics.

      WHERE FOUND:  8bit ports are found on about 25% of desktops, about
                    50% of laptops, and 90% of laptops built since 1991.

     CAVEAT EMPTOR: A number of vendors claim "bidirectional" capability
                    for their parallel ports when they are actually mere
                    4bit ports. When buying a parallel port expansion card,
                    or an entire system, you might want to use Parallel to
                    find out the REAL capabilities of the port. Be aware
                    that a vendor's general reputation for quality may not
                    translate into good parallel ports.  There are examples
                    of well-known vendors making false claims for their
                    parallel ports... sometimes, it appears, simply because
                    they don't understand them... the claims or the ports.

                    We are not going to pan anyone's "bidirectional"
                    parallel ports specifically, but be warned that the use
                    of terms like "bidirectional" or "PS/2 compatible" may
                    have nothing to do with the port's actual capability.

                    Some vendors even refer to 8bit ports as "enhanced",
                    which is totally misleading and creates no end of user
                    confusion. Make sure exactly what you are getting.

                    The moral of the story ... use Parallel to test ports
                    to determine their real I/O behavior and compatibility.



Parallel Port Information System                                    Page 14
---------------------------------------------------------------------------

                    Remember that if Parallel can't detect the port, or
                    reliably report it's actual behavior, then chances are
                    good that other software won't be able to either!

           EPP ports
           ---------

                    Can do both 8bit input and output at ISA bus speeds.

                    This type of port is defined by the EPP 1.7 standard,
                    by the actual behavior if the Intel 360SL I/O chip, and
                    also by the IEEE 1284 standard (which is substantially
                    incompatible with the EPP 1.7 standard - more below).

         HOW FAST:  These ports are as fast as 8bit bus cards and can
                    achieve transfer rates of upwards of 1 Mbyte/sec. For
                    example, our EPP-capable external SCSI disk is faster
                    on a popular SL laptop than it's own internal drive.

                    EPP ports are supposed to conform to a well defined
                    electrical standard and many of them actually do so.
                    However, if you are buying a laptop and want to be sure
                    of using fast EPP-capable external peripherals, then
                    you should definitely arrange to try before you buy.

          HISTORY:  EPP ports came about as a joint effort involving
                    Zenith, Intel, and Xircom.  After the introduction of
                    the EPP port capability in the Intel 360SL I/O chip,
                    many manufacturers began providing this feature on
                    their SL-based laptops. An EPP Standards Committee was
                    formed which standardized the behavior of the Intel SL
                    EPP port as the EPP 1.7 standard ... and life was good.

                    Then the EPP standards committee merged with the IEEE
                    1284 committee which was itself struggling to specify
                    new parallel port type(s) with a predominant focus on
                    fast and bi-directional communication for printers.
                    Parallel port peripherals other than printers were
                    considered strange beasts and received extremely short
                    shrift in the 1284 deliberations, to the point that the
                    1284 specification does not really embody a long term
                    vision of the parallel port as a high-speed external
                    pathway for interfacing various peripherals to the PC.

                    Also, the 1284 committee did not like the details of
                    how the signalling occurred between the PC and the
                    attached device in the EPP 1.7 spec, and agreed to
                    include EPP within the scope of IEEE 1284 only if the
                    EPP standard was changed to correspond to the rules for
                    1284 signalling.  Hence the IEEE 1284 EPP spec, which
                    is incompatible with the original EPP 1.7 spec.

                    As a result, there are actually TWO standards for EPP
                    signalling, the original 1.7 specification (embodied in



Parallel Port Information System                                    Page 15
---------------------------------------------------------------------------

                    hundreds of thousands of SL laptops) and the IEEE 1284
                    EPP specification (embodied in a new generation of IEEE
                    compatible parallel ports which support multiple modes
                    of parallel port operation - see below). A typical IEEE
                    1284 style parallel port supports a combination of
                    Compatible (4bit and/or 8bit), EPP (version 1.7 and/or
                    1284) and/or ECP (which we visit in the next section).

         EPP BIOS:  To make matters more complicated, the EPP Standards
                    Committee began work on an EPP BIOS spec quite some
                    time ago but the specification is still not adopted
                    either formally by the (now) IEEE 1284 Committee or by
                    any significant numbers of vendors. It is uncertain
                    whether such a BIOS will ever be widely supported, and
                    in any case, it will be too little - too late, because
                    developers will still be required to support the
                    existing defacto standards for non-BIOS interfaces as
                    well as the hypothetical new BIOS standard. This
                    reduces the EPP BIOS's usefulness; instead of being a
                    global standard, it becomes just another special case.

                    If this seems complicated to you, then congratulations,
                    you have successfully evaluated the situation!

     CAVEAT EMPTOR: Therefore, when buying a system or external peripheral
                    which has high-speed EPP capability, it is crucial to
                    determine whether the system or device supports EPP 1.7
                    or EPP 1284 or both.  See the Buyer's Guide section for
                    more information on this subject.

                    Xircom was active in creating and defining the EPP 1.7
                    standard, and since their EPP-capable network adapters
                    are fairly common, it's worth mentioning that these
                    adapters can be used as a practical benchmark for the
                    goodness of a EPP 1.7 port. Crude but effective.

                    EPP ports are most often found on laptops using the
                    Intel 386SL chipset with the 360SL I/O support chip or
                    a register-compatible parallel port implmentation. You
                    can usually identify these laptops by the 'SL' suffix
                    in their name, HOWEVER this is not a hard and fast
                    rule, since there are non-SL systems with EPP ports as
                    well as SL systems which (in our tests) have non-
                    functioning or sub-standard EPP ports. Other vendors
                    offer add-in EPP cards for the ISA bus.

       The Future:  Standard Microsystems Corp., National Semiconductor,
                    and Chips and Technologies have released multifunction
                    chipsets with both EPP and ECP capability, so users can
                    expect to see fast ports become available on a wider
                    range of systems. Other such chipsets are on the way.

                    This new generation of chipsets, combined with the IEEE
                    1284 standard, provides another window of opportunity



Parallel Port Information System                                    Page 16
---------------------------------------------------------------------------

                    for a comprehensive parallel port technology solution.
                    It remains to be seen if parallel port hardware and
                    software vendors will produce a cohesive response, or
                    if parallel ports will remain the PC's neglected child.

           ECP ports
           ---------

                    Can also do both 8bit input and output at bus speeds.

                    The specification for this port type was jointly
                    developed by Microsoft and Hewlett-Packard.

                    ECP ports are distinguished by having DMA capability,
                    on-board FIFOs at least 16 bytes deep (too small), some
                    hardware data compression capability, and are generally
                    more featureful than other ports.

                    The MS/HP ECP port specification defines the ISA bus
                    registers by which the PC software can read and write
                    data at high speed to an attached device.

                    The MS/HP ECP port specification (what's inside the PC)
                    is related to the IEEE 1284 specification (what happens
                    on the wires outside the PC in various modes).

         HOW FAST:  These ports are as fast as 8bit bus cards and can
                    achieve transfer rates upwards of 1 Mbyte/sec and
                    faster on PCs whose buses will support it. The design
                    is capable of faster transfer rates in the future.

        TECH NOTE:  ECP port specification defines an ECR control register
                    with port mode configuration bits which may be used to
                    place the ECP port into several different submodes.

                    The ECP specification defines a multimodal port which
                    can support backward compatible and enhanced modes of
                    operation.

                    My goodness, this is starting to look like an excellent
                    solution to the proliferation of incompatible parallel
                    port standards. A standard port with multiple modes!

                    Alas, the ECP port specification does not define an EPP
                    mode, so vendors have chosen various ways of providing
                    an EPP capability within the framework of the ECP port
                    specification. Let's look at how this works.

                    SMC, for example, uses a reserved bit of the ECR
                    register to place the port into EPP 1284 mode on their
                    66xQFP chip (see Parallel Port Buyer's Guide). The
                    66xQFP chip, used on the Intel Pentium motherboards,
                    does not support EPP 1.7, which means that the large
                    installed base of parallel port network adapters,



Parallel Port Information System                                    Page 17
---------------------------------------------------------------------------

                    external disks, SCSI adapters, etc generally don't work
                    on such systems. When SMC figured this out, they
                    announced the 66xGT revision of the chip, which has TWO
                    EPP modes, 1.7 and 1284, as well as various bug fixes.

                    In addition, the SMC chip implements a TWO level
                    approach for controlling parallel port configuration.
                    The 66x contains configuration registers which ENABLE
                    the port to be in Standard, EPP-only, ECP-only, or EPP-
                    ECP modes. If the port is in ECP or EPP-ECP modes, then
                    the actual submode is SELECTED according to the ECP
                    spec by using the ECR register which appears on the bus
                    only when the chip is ENABLED for ECP or EPP-ECP.

                    To make matters even more complicated, other vendors
                    have taken other approaches to shoehorning EPP into the
                    framework of the ECP specification.

        STANDARDS:  Note that while both the EPP and ECP parallel port
                    specifications establish how the port operates within
                    the PC when it is enabled, the specs do not describe
                    how the enablement occurs - that is left to vendors.

                    For example, the EPP 1.7 specification defines the
                    various I/O registers of the EPP port, but does not
                    define how to detect such a port or enable it.

                    Similarly, the ECP port specification defines the port
                    I/O registers and some of the configuration processes,
                    but does not define exactly how such ports are enabled,
                    this is a constant problem with inadequate standards.

                    Therefore it is possible for vendor ABC's excellent EPP
                    1.7 (or ECP, etc) device to fail to operate on vendor
                    XYZ's system because XYZ implemented the port in a way
                    that ABC does not recognize (yet). Parallel port device
                    vendors are constantly challenged by the appearance of
                    new types of ports - and the better vendors frequently
                    have software upgrades which support specific ports.

                    Existing parallel port standards have missed the mark.

                    They do not qualify as fully conceived response to the
                    overall requirement for speed, vendor flexibility, and
                    ease of use in the PC environment. These standards have
                    focused on bringing short-term capabilities to market
                    rather than on providing a comprehensive, universal
                    solution to the end user.

                    In the Buyer's Guide section, we will attempt to throw
                    some light on your practical options when shopping for
                    a system with fast parallel ports. The Parallel Port
                    Standards section reviews the various parallel port
                    standards, de facto and de jure.



Parallel Port Information System                                    Page 18
---------------------------------------------------------------------------


        IO Address
        ----------

        Also called the "base address" the port. It will almost always be
        3BC, 378, or 278 hex. A very rare subset of parallel ports may
        support additional addresses such as 280, 290, etc.

        The IO address specifies the port's location on the PC's IO bus.

        Normally the first port is configured to 3BC, the second to 378,
        etc, however ports can be assigned to any of these three addresses.

        On bus cards, the IO address is usually set by a arrangement of
        jumpers unique to the particular board. You will need a manual or
        the ability to read PC board traces (gacck!). These jumpers are
        usually arranged to allow you to select one of three addresses.

        Sometimes these addresses are called by the "logical device names"
        of LPT1, LPT2, and LPT3, although this practice is quite misleading
        (see BIOS discussion below).

        Some boards offer a more limited selection of configurations,
        usually 378 and 278, and a few are actually hardwired to a specific
        address. Vendors do this to save a little money and to eliminate
        the chance of creating an address collision with the "standard"
        address of 3BC. Because of the increasing number of clones which
        are assembled from various components, we often see systems with
        one LPT card, configured to address 378. In fact, a fair number of
        systems are shipped with this 378 default configuration.

        A slightly interesting result we've seen in several desktops spins
        off when someone adds a second LPT card to a system which already
        has a LPT at 378, IRQ 7. Sometimes they naively reason that since
        378 is taken they can use 3BC and slap in the card without checking
        the IRQ level. This creates a configuration of 3BC and 378 both
        using IRQ 7, a situation which can lead to intermittent crashes
        when using interrupt-driven parallel port software.

        By the way, some systems have parallel ports and com ports built
        onto the motherboard itself and, in this case, the configuration
        jumpers will be found on the motherboard or, as in the case of more
        recent systems, in the CMOS SETUP utility.

        The new generation of ECP-capable parallel ports typically
        implement software selectable modes, base addresses, and IRQs.

        If you have one of these new parallel ports, you will require
        appropriate software in order to configure your port.  This may
        exist within the CMOS setup function or may exist as a separate
        utility.  When you buy a system or an add-in card with advanced
        parallel port functionality MAKE SURE YOU GET THE SOFTWARE which
        allows you to enable it. Some vendors include it, some don't.



Parallel Port Information System                                    Page 19
---------------------------------------------------------------------------

        Be aware of the distinction between configuration software which
        allows you to control the configuration of your port, and device-
        specific driver software which uses the port.

        Notice that there are three commonly used IO Addresses (3BC, 378,
        278) and two available interrupt levels (IRQ 7 and IRQ 5). This
        means that if you have three LPT cards in a system, two of them
        will probably be configured to share a hardware interrupt level.
        This is hardwarily permissible, and generally doesn't create any
        problems since most DOS and Windows software doesn't ENABLE
        interrupts for printing anyway. However, if you are using LPT
        software like an interrupt-driven print spooler or interrupt-driven
        LPT devices like external hard disks, external network adapters,
        and so forth, then you have to be sure that either (1) the ports
        are not using the same interrupt level, or (2) both the ports and
        the software are capable of "interrupt sharing".

        When adding or configuring LPT cards, we suggest using 3BC, IRQ 7
        for the first card; 378, IRQ 5 for the second card; and 278, no IRQ
        for the third card. This gives you two interrupt-capable LPT ports,
        and one port (at 278) which you should use only for non-interrupt
        driven usage, like the status-driven spooling provided by DOS.

        You should only configure your system to share interrupts when you
        are (1) absolutely sure that they will not be simultaneously
        enabled, and (2) when you have totally run out of other options.

        Also, you should know that many sound cards, like the SoundBlaster,
        arbitrarily use IRQ7 by default. This was a bad design decision,
        especially so since the SoundBlaster's implementation of interrupts
        creates a serious conflict when sharing the interrupt with other
        devices, but we are stuck with it.  If you are using a sound card
        on IRQ7 or IRQ5, then you should definitely AVOID ENABLING that
        level on any of your parallel ports.

        Armed with this understanding and the Parallel Utility, you are
        equipped to select a configuration which works for you.

           HOW TO:  The IO ADDRESS is a standard parameter in network
                    configuration files where it takes on different names
                    to confuse innocent users. (Base, Port, etc).

                    Some simple-minded parallel port peripherals (ones
                    without auto-configuring capability) require that you
                    specify the IO address, IRQ level, and sometimes the
                    Port Type in a vendor-specific way. Parallel provides
                    you with this information.

           HOW TO:  Resolving IO Address conflicts is usually fairly
                    simple, since it is rare to find a device which uses
                    the standard parallel port addresses.

                    A good procedure for eliminating potential IO address
                    conflicts when installing parallel port add-in boards



Parallel Port Information System                                    Page 20
---------------------------------------------------------------------------

                    is to remove all the boards, install one, use Parallel
                    to see what address it finds, install the next, and so
                    forth. If Parallel finds each board at a separate
                    addresses as you install them, then you can be sure of
                    your configuration.

        Understanding the IRQ Level
         ---------------------------

        This is the hardware interrupt level assigned to the port. It will
        almost always be either 7 or 5. Only a few specific parallel ports
        support IRQ levels other than 7 or 5.

        Parallel displays:

               "?" when it cannot detect the IRQ level of the port and
               "-" when it knows the the port doesn't exist.

        Parallel needs an external loopback connector to automatically
        detect the IRQ. With appropriate precautions (described in horrible
        and excruciating detail below) you can use a simple paperclip as a
        loopback connector.

        Normally IRQ 7 is assigned to the first port and IRQ 5 is assigned
        to the second port. However, due to the explosion of clones
        assembled from disparate parts, it is not uncommon to see systems
        with one LPT port located at 378 with an IRQ of 7 or 5. This is
        because clones are often assembled using offshore add-in LPT cards
        which are shipped configured to operate as a second LPT card.

        This is a good time to point out that there are few hard and fast
        rules when it comes to parallel port configuration. Ports can be
        located at any one of the three standard base address and can use
        either of the IRQ levels. If you are developing parallel port
        software, you should auto-detect the actual configuration rather
        than assume any standard usage.

        We offer libraries and source code for this purpose. Here at
        Parallel Technologies, we test our software using many strange
        configurations and delight in adding idiosyncratic ports to our
        extensive collection.

        The most common idiosyncrasy of port IRQ is IRQ inversion. The PC
        standard calls for interrupts to be generated on 0->1 transitions
        of the interrupt line.  A small percentage of parallel ports
        generate their interrupts on 1->0 transitions.  Ports with inverted
        IRQ can fail to operate with some interrupt software, particularly
        certain external network adapters, disks, and so forth. Parallel
        identifies these ports with a note "IRQ style is INVERTED".

        Some parallel ports have non-functioning IRQ lines. They are simply
        not capable of generating interrupts. Only a very few pieces of
        software are capable of dealing with these ports by using a polled
        mode of operation.



Parallel Port Information System                                    Page 21
---------------------------------------------------------------------------

        In the case of an add-in board with broken IRQ capability, check to
        be sure the IRQ jumper, if any, has not gone missing somehow.

        On ISA cards (bus cards in ISA slots) the interrupt level is
        usually set with jumpers on the board - these jumpers are different
        for every card so you need to hunt around for the manual in order
        to change them. If you're lucky there will be readable labels on
        the card itself.

        On laptops and an increasing number of desktops, the IRQ level can
        usually be set using the vendor's CMOS configuration (setup)
        program. Sometimes these CMOS setup programs are built into the
        ROM; sometimes they exist as separate programs or as part of the
        vendor's diagnostic program(s). Refer to your manual to find out
        how to enter the CMOS setup mode. BE CAREFUL when using the CMOS
        setup, since it gives you access to parameters that can disable
        your system if wrongly changed. KNOW WHAT YOU ARE DOING. DON'T
        CHANGE ANYTHING YOU DON'T FULLY UNDERSTAND. WRITE DOWN THE INITIAL
        VALUES OF ANY SETTINGS YOU CHANGE. ASK YOUR VENDOR FOR HELP.


                                ******************
                                * IMPORTANT NOTE *
                                ******************

        Misuse of your system's CMOS setup program can prevent your system
        from operating correctly, or in some cases, from operating at all!

        Be sure you know what you are doing; read your user's manual or get
        qualified help if you have any doubts.

        Another strange feature of these software configurable ports is
        that they often have very peculiar ideas about nomenclature. Often
        these CMOS setup programs use vendor specific "magic code words" to
        select various parallel port configurations, and these magic words
        can have non-obvious effects. Sometimes the vendor's manuals don't
        even provide a secret decoder ring to explain what their magic
        words really mean in terms of IO Address, IRQ, and Port Type.

        Parallel will be useful for determining the actual effect of the
        CMOS setup choices on your system.

        For example, on my Dell NL25 laptop, 4bit mode is called "Normal"
        and 8bit is called "Enhanced" and there is no choice at all for the
        real Enhanced Parallel Port (the SL's EPP port). So someone might
        obviously think they have enabled EPP by choosing "Enhanced".
        Futhermore, the IRQ level cannot be set directly, but rather is set
        as a by-product of selecting combinations of the IO address and the
        Port Type. Most of the choices on my Dell yield IRQ 7, but one
        lonely choice - LPT1, 278, Normal mode results in IRQ 5. It makes a
        bizarre sort of sense when you are experienced with parallel ports,
        but is likely to be confusing to the Average User (if we ever find
        him, or her).



Parallel Port Information System                                    Page 22
---------------------------------------------------------------------------

        The Dell is hardly alone in it's strange naming conventions ...
        most PCs have confusing, misleading, or incomplete labels and
        controls in their CMOS setup programs. This sort of indirect
        control in very common in CMOS setups and creates a lot of tech
        support calls from frustrated users.

        In addition, most SL laptops don't have the capability to enable
        their EPP ports from CMOS. Usually you need to run a separate
        vendor-supplied BIOS extension to enable EPP capability. These take
        the form of a tiny TSR which adds INT 17h BIOS extensions for
        controlling the EPP port, and handles command line arguments for
        enabling and disabling EPP. An interesting sidelight of switching
        into EPP mode can be that your port IO address may change on the
        fly. The Intel EPP hardware allows EPP ports to be configured at IO
        Addresses 378 and 278. So if you have set your port address to 3BC
        (with CMOS for example) and then switch into EPP mode, your port
        will appear to have moved.

        Parallel will come in handy in trying to make sense of what your
        system's CMOS settings are actually doing to your parallel ports.

        Understanding the BIOS Name
        ---------------------------

        This is the "human-readable" (hah!) name which you use to refer to
        the port when using DOS commands, Windows picklists, and so forth.
        It will be one of the following: LPT1, LPT2, LPT3.  LPT4 is
        extremely rare and Parallel currently ignores it.

        The port address is NOT the same as the BIOS name for the port. For
        example, LPT1 can refer to a port at any address: 3BC, 378, or 278.

        So how does the BIOS associate the LPT names with the actual ports?

        It works like this ...

        Whenever your system boots, the BIOS goes out and tries to write
        and read back data from locations 3BC, 378, and 278. If it can read
        back what it writes, then the BIOS decides that a parallel port is
        there and adds the IO address to a LPT table in the "Bios Data
        Area". This table is four words located at memory location 40:8.

        A command like "copy foo.txt lpt2:" really means "copy the file
        foo.txt to the second printer that BIOS knows about" and DOS uses a
        software interrupt, INT 17h, to do just that. INT 17h looks in the
        Bios Data area to find out the IO address of the "second printer
        port", which can be any of the IO addresses - 3BC, 378, or 278.

        The result is that LPT1 refers to the first port BIOS finds at boot
        time, wherever it may be. So "LPT1" means "the first port found in
        the address order", not necessarily 3BC, 378, or 278 specifically.
        Some BIOSes have unique methods for finding their LPT ports.



Parallel Port Information System                                    Page 23
---------------------------------------------------------------------------

        When you see LPT1, LPT2, or LPT3 used to refer to port locations,
        be alert for possible misleading information. Some well-known
        vendor's manuals use LPT1 to refer to 378 and LPT2 to refer to 278,
        etc, an entirely spurious practice which has confused many users.

        It is possible for some parallel port software to set the port into
        an IO mode that causes it to fail the simple BIOS test and seem to
        "disappear" from your system even after a soft boot (CTRL-ALT-DEL).

        Parallel has a better port detection test, and can usually find
        such ports. A hard reset (a power-off reset) will clear the port.
        Parallel ports are not completely trivial devices; they have a
        number of states that can affect their operation. So if you are
        having a parallel port problem, one of the first things to do is a
        power-off reset.

        Another factor here is that various programs can fiddle with the
        LPT table in order to rearrange how the names relate to the ports
        or to accomplish other effects like network print redirection.

        The utility SWAPPRT, for example, can be used to swap LPTx with
        LPTy which it does by moving the entries in the LPT table.

        There are variations of this redirection theme.  Network print
        capture functions (such as those found in Netware and so forth) put
        special values in the LPT BIOS table to mark that the port is not a
        physical port but rather is a "virtual port" which is actually
        served by a software function, usually redirection of INT 17.

        Some parallel port devices with passthrough printing ports also use
        this technique to intercept the output of programs which print
        using the INT 17 function call.

        If Parallel does not display a BIOS name for a port, that means the
        IO Address for that LPT position has been replaced with a value
        that does not match a valid hardware port. This can occur when some
        other parallel port software has grabbed possesion of the port by
        placing a "magic number" in the BIOS LPT Table.

        Remember, the BIOS decides how LPT symbolic names are mapped onto
        physical port addresses, generally by a test a boot time, not the
        vendor's manual, or the jumpers, or the CMOS settings.



Parallel Port Information System                                    Page 24
---------------------------------------------------------------------------



        Understanding the Notes and Comments
        ------------------------------------

        The "Notes" field of the display will contain various comments,
        depending on what Parallel has detected. Each note may be followed
        by one or more comments giving further information or directions.
        These secondary comments are indented one space under their note.

        "Port is an XYZZY chip"

                    Parallel is reporting the specific chipset used to
                    implement the parallel port at that address. Some
                    vendors may design completely compatible chipsets
                    (thank you) which spoof the specific chip detection.

                    Parallel may also report additional information about
                    the current setting of the chipset.

                    For example, in the case of an SMC 66x chip that is
                    enabled for EPP-ECP mode and which currently has the
                    Compatible submode of ECP selected (whew!), Parallel
                    will report an ECP port with a Note that the port is
                    currently in 4bit mode.

        "No port found at this address"

                    No parallel port is installed at this IO Address.

                    This is a normal result if no port in installed there.

                    However, it is possible that something is connected to
                    the parallel port and is overdriving the port's inputs,
                    which prevents the software readback test from working.

                    Be sure you have disconnected all external devices.

        "Need loopback to determine IRQ"

                    The port exists, but does not respond to attempts to
                    generate IRQs. This is because a loopback connector is
                    required for IRQ detection in most cases.

        "Port IRQs are not functioning"

                    This is pretty bad. It means that the loopback
                    connector is present and working correctly, but
                    Parallel still can't generate any interrupts.
                    Technically it means that transitions in the ACK line
                    are not causing interrupts through the PC's interrupt
                    controller.



Parallel Port Information System                                    Page 25
---------------------------------------------------------------------------

                    In practice, it means that interrupt-driven devices and
                    software won't work, unless they have polling support.

                    Possible reasons for failing the IRQ test include:

                    1. The port's interrupt capability is disabled

                         Check your CMOS configuration and/or the hardware
                         jumpers on the parallel port board(s) to be sure
                         that the interrupt is enabled. The function of
                         CMOS parameters and/or hardware jumpers varies
                         from system to system, so check your manual or
                         contact your vendor if you have problems enabling
                         the port's interrupt line.

                         Many CMOS and jumper arrangements combine enabling
                         the IRQ with selecting the level, ie, "enable
                         IRQ5" or "enable IRQ7". Installing the jumper may
                         combine selecting a level and enabling the IRQ.
                         Removing the jumper generally disables the IRQ.

                    2. The port does not have IRQ capability

                         Most ports DO have interrupt capability, but a
                         small percentage of older systems(at a guess %1 to
                         %5) do not. More laptops lack interrupts than add-
                         in cards. Add-in cards without IRQ are rare. Most
                         reports of non-functional parallel port IRQs in
                         desktop systems can be tracked to configuration
                         problems which create interrupt conflicts (see #3)
                         which effectively disable IRQ.

                    3. There is an IRQ conflict with another device

                         It is possible that another device in your system
                         is preventing the parallel port IRQs from
                         functioning.  For example, in IBM-PCs and XTs, the
                         disk controller may use IRQ5 and prevent parallel
                         ports configured to IRQ5 from creating interrupts.

                         Sound cards frequently use IRQ7 and are also
                         likely candidates for creating IRQ conflicts.

                         To isolate this problem, remove all boards from
                         your system which are not required to perform the
                         test. In other words, strip down to just the
                         parallel port, floppy controller and video, and
                         repeat the test.

                         If possible, configure the parallel port to IRQ7.
                         If the port can use IRQ7 interrupts, but not IRQ5
                         interrupts, then an interrupt conflict is likely.

        "IRQ determined by loopback"



Parallel Port Information System                                    Page 26
---------------------------------------------------------------------------


                         The loopback was detected, is operating correctly,
                         and the port's IRQs are functioning correctly.
                         The IRQ level found is given in the IRQ column.

        "IRQ estimated by port float"

                         No loopback connector was detected, but the port
                         is generating IRQs anyway. This probably means
                         that the port is connected to an inactive
                         (unpowered) external device. Treat IRQs determined
                         in this way with some skepticism; better to
                         disconnect the device and use a known-good
                         loopback connector.

        "IRQ determined by EPP hardware"

                         If the Port Type is determined to be Intel SL EPP,
                         then Parallel does not use the IRQ test, but
                         rather reports the IRQ which is standard for an
                         Intel EPP port at that IO Address. This only
                         applies to actual Intel SL type EPP ports.

        "IRQ noise is present"

                         Parallel has detected extraneous interrupts
                         occuring on IRQ level 5 or 7 during the IRQ test.

                         This condition is reported when the total number
                         of interrupts occurring on both IRQ5 and IRQ7
                         exceeds the number of interrupts Parallel expects.

                         This can mean several things:

                         1. PIC errors. The PC's interrupt controller (PIC)
                         is generating errors as described below.

                         2. An active device other than the parallel port
                         under test is generating interrupts on IRQ 5 or 7.
                         This is typically a sound card or another parallel
                         port with a enabled, floating, IRQ line.

                         3. The port's IRQ line is electrically noisy. This
                         has been seen with boards which have dual parallel
                         ports where transitions in one port's IRQ line
                         causes noise on the other port's IRQ line.

                         This result may be ignored if you are not having
                         any problems, but be informed that this condition
                         is quite likely to confuse parallel port software
                         which tries to autodetect the port's IRQ level.



Parallel Port Information System                                    Page 27
---------------------------------------------------------------------------

                         Noisy IRQ lines can also slow down or break driver
                         software which is not intelligent enough to defend
                         itself against this relatively common situation.

     TECHNICAL NOTE:     PIC errors are usually found with parallel port
                         chips whose "open" condition on the ACK line may
                         allow the IRQ signal to float randomly. This
                         effect creates PC interrupt controller errors
                         which are redirected by the PIC to IRQ7 where they
                         can be mistaken for "real" interrupts.

                         An PIC error condition is defined to occur when
                         the PIC attempts to service the requesting device
                         but the device's interrupt line has gone inactive.
                         These are also known as "lost interrupts", which
                         are not really lost but rather redirected to IRQ7.

                         A noisy IRQ line can create the appearance of lost
                         interrupts and this confuse driver software.

                         The effect of lost interrupts being redirected to
                         IRQ 7 explains why some parallel port driver
                         software works well on IRQ7 but not IRQ5, or vice
                         versa. The interrupt is lost, redirected to IRQ 7,
                         and thus becomes found again.  Strange.

                         Parallel port interrupt handlers have to account
                         for conditions that are generally not seen by
                         other device drivers. If you are having problems
                         with parallel port software you may want to try
                         configuring the port to the other interrupt level.

        "Data port has stuck bits!"

                         The rotating bit test has detected bits in the
                         data port which cannot be set or cleared properly.

                         This can mean that an enternal connection is
                         preventing the datalines from making the expected
                         transistions.  You may have inserted the Loopback
                         incorrectly.

                         Of course if there is no external device present,
                         then something else must be happening! It could be
                         that an active device is forcing some of the data
                         lines to a fixed level. It could also mean that
                         your port exists, but some of the data bits are
                         not working, which is a polite way of saying that
                         your port is busted.

                         A false Port Type may be reported in this case.

                         Make sure that the loopback, if used, is correct.
                         Make sure that all devices are disconnected.



Parallel Port Information System                                    Page 28
---------------------------------------------------------------------------


        "IRQ style is INVERTED"

                         The port's IRQ line functions in an opposite sense
                         from the PC standard. A significant amount of
                         software will fail to work with such ports. There
                         is no remedy for this condition in general; the
                         best we can advise is to use a different port if
                         you have a bus system or try other CMOS settings
                         on a laptop if that is possible. You might try
                         contacting your vendor.

                         Parallel may falsely report inverted IRQ if there
                         is an external device connected to the port.

        "Possible IRQ Conflict"

                         Two or more ports in your system are using the
                         same IRQ level. If you are not using interrupt-
                         driven parallel port peripherals or printing
                         software then you might simply ignore the warning
                         if you are not experiencing any problems. However,
                         you should know that some very strange results can
                         occur when two parallel ports are  trying to drive
                         the same IRQ line. Sometimes one or both ports can
                         falsely appear to have INVERTED IRQ.

                         The best solution is to move one of the ports to
                         another IRQ level, if that is possible.

        "BIOS Data doesn't match hardware"

                         The contents of the BIOS LPT Table does not match
                         the expected initial state at boot time.

                         This is probably due to a parallel port device
                         driver, a SWAPLPT program, or print spooler having
                         fiddled with the BIOS data, in which case it may
                         be considered normal operation.

                         Network drivers (typically the redirector clients)
                         also commonly rearrange the BIOS LPT Table in
                         other to provide network print redirection.

                         This information is useful if you are having
                         problems with print redirection. Also, some
                         parallel port device drivers do not examine the
                         hardware directly to determine which ports exist,
                         but rather only look at the BIOS. If you have run
                         other parallel port software which has changed the
                         BIOS in a non-standard way, then these device
                         drivers may fail to find any parallel ports, or
                         may try to access the wrong port with peculiar
                         results. This can often be solved by changing the



Parallel Port Information System                                    Page 29
---------------------------------------------------------------------------

                         order of loading or by manually configuring the
                         failing driver.

        "Port has latent EPP tendencies"

                         The port is an Intel SL EPP port, but it is
                         currently configured to a non-EPP mode. Use your
                         vendor-supplied CMOS or separate configuration
                         program if you need to enable the EPP capability.
                         Some vendors do not ship the ability to enable
                         EPP; an appropriate utility may be available on
                         the vendor's BBS.

                         In particular, the EPP function of Compaq SL
                         laptops may be enabled with their SETEPP utility.

        "EPP port is Intel SL flavored"

                         The EPP port is an Intel SL port (360SL chipset).

                         It is possible for Parallel to report a false
                         Intel EPP detection on some systems. One Toshiba
                         system (3600) has an 360SL onboard which does
                         respond to EPP detection but is NOT connected to
                         the outside world - instead their custom ASIC is
                         used to implement the parallel port. So Parallel
                         will report a false EPP result on this laptop.

        "EPP port is vanilla flavored"

                         The EPP port is NOT an Intel SL port, but does
                         pass a generic EPP write/readback test. This test
                         is only attempted if the EPP BUSY line is not
                         HIGH. This avoids hanging the CPU on EPP ports
                         which do not implement the access watchdog timer.



Parallel Port Information System                                    Page 30
---------------------------------------------------------------------------

     Automatic IRQ detection
     -----------------------

        Parallel uses two methods for automatic detection of a port's IRQ
        level: port float or the external loopback connector.

        IRQ detection using the LoopBack Feature
        ----------------------------------------

                                ******************
                                * IMPORTANT NOTE *
                                ******************

        First, DECIDE NOT TO SCREW UP YOUR PORT by crudely jamming wires
        into the wrong places with too much force.  REMEMBER that the
        female DB-25 connector is likely to be made out of CHEAP, BREAKABLE
        PLASTIC, so decide right now not to break it. WE ARE NOT LIABLE FOR
        ANY DAMAGE YOU MAY DO FOR WHATEVER REASON.

        The danger is that you will push too hard when inserting the
        loopback wire and force the female connector pin out of its
        position in the DB-25 shell. That is why WE SUGGEST MAKING A
        LOOPBACK PLUG using a male DB-25 connector as described below. If
        you cannot make a loopback plug, then use a parallel port extension
        cable instead. This protects your port from physical damage and
        also makes it a lot easier to work with.

        The port is supposed to be electrically designed to tolerate the
        loopback perfectly well. However there is a DANGER OF DAMAGE BY
        STATIC DISCHARGE so make sure that you GROUND YOURSELF TO THE PORT
        before inserting the loopback wire. It would be terrible if you
        blew out a $25 parallel port on a $1000 Pentium motherboard simply
        because you failed to PAY ATTENTION TO THESE PRECAUTIONS.

        PROCEED AT YOUR OWN RISK.

        The other danger is that you will apply the loopback to a port
        which is not really a parallel port at all. DON'T DO THIS. If you
        are not sure of what you are doing STOP RIGHT NOW. We have no
        control over what you might damage if you try this with a port
        other than a parallel port.

        Whew... now on with the instructions.

          1. Find the parallel port(s) you want to test. They will be
             female DB-25 connectors. MAKE SURE THAT YOU HAVE CORRECTLY
             IDENTIFIED THE PARALLEL PORT. Disconnect any devices
             (printers, network adapters, external disks, etc) which might
             be attached to other parallel ports on your system.

          2. Make sure that the connector IS NOT SOME OTHER TYPE OF
             CONNECTOR like an external SCSI connector or a COM port.



Parallel Port Information System                                    Page 31
---------------------------------------------------------------------------

             SCSI ports can be either female DB-25s or a larger connector,
             like a 37, 40, or 50-pin connector. COM ports are usually
             male DB-25 or small male DB-9 connectors, but this is not
             guaranteed.

             Look in your manual if there is any doubt. DON'T PROCEED
             unless you are sure you have identified the parallel port(s)
             correctly.

          3. Connect the Loopback Plug and go to Step 7.

             If you do not have a Loopback Plug, use a straight thru M-F
             parallel port extension cable to prevent damage to your port.
             Connect the male end of the extension cable to your port and
             place the loopback wire into the female end of the cable.

                             |---
                expensive    |   | +-+     cheap     +-+
                   PC        |   | | |---------------| | <- loopback here
              parallel port  |   | +-+     cable     +-+
                             |---

          4. Identify Pin 10 and Pin 9 on the female end of the extension
             cable. Refer to the illustration below. Notice that a DB-25
             connector is wider on one side.  The pins you want are the
             4th and 5th from the left on the wider edge.

             USE A FLASHLIGHT TO FIND THE MARKINGS IF YOU HAVE ANY DOUBT.

          Front View         -------- Pin 10 - 4th from left on wider edge
          Female DB-25       |   ---- Pin  9 - 5th from left on wider edge
          Connector          |   |
                             v   v
           ____________________________________________________________
          /                                                            \
          \     13  12  11  10   9   8   7   6   5   4   3   2   1     /
           \                                                          /
            \     25  24  23  22  21  20  19  18  17  16  15  14     /
             \______________________________________________________/

                    Pin 10 is the interrupt line (the ACK line)
                    Pin  9 is the high order data line (the 80h bit)

          4. Create a loopback wire. A standard paperclip works fine. Just
             straighten it out and bend it into a "U" shape with the ends
             1/8 inch apart. Make sure that the paperclip is SMOOTH and
             has NO ROUGH EDGES that might damage the plastic connector.

          5. GROUND YOURSELF to the PC and to the parallel port by
             touching your hand and the loopback wire first to the PC's
             metal chassis near the parallel port connector and then to
             one of the connector nuts or the connector metal housing
             itself. Do this to DISCHARGE ANY STATIC ELECTRICITY you may
             have about you (created for example by scooting across the



Parallel Port Information System                                    Page 32
---------------------------------------------------------------------------

             rug in a silk negligee on the way to your PC or by stroking
             your cat with woolen gloves while purusing this document).

             Parallel ports are usually resistant to static discharge, but
             not all ports are created equally, so don't ask for trouble.

          6. Carefully insert the paperclip into the extension cable's
             female DB-25 connector so that Pin 9 is connected to Pin 10.
             DON'T FORCE IT. It will insert at most about 1/4 inch (about
             .5 cm) and there should be absolutely no physical resistance.

          7. Now run Parallel. It will automatically use the loopback to
             determine which IRQ level the port is actually using. You may
             loopback more than one, or all, ports at the same time.

             Parallel will report that is has detected a proper loopback.

          8. Remove the loopback when you are done.

          9. Congratulate yourself on using reasonable handling
             precautions when working with expensive equipment.

        Understanding Port Float
        ------------------------

        Many parallel ports will "float" in a unstable logic state when
        connected to an unpowered external device such as a printer. This
        unstable logic state may cause the port to generate a limitless
        stream of apparent interrupts to the CPU if the port's interrupt
        line is enabled. This peculiar behavior is used to advantage by
        Parallel.

        If you have a unpowered (powered off) printer, or other device,
        attached to a port, then Parallel may be able to detect the
        interrupt level using this floating port behavior. In this case,
        Parallel will display "IRQ determined by port float". You should
        treat the IRQ determined in this way as a "best guess". To be sure
        of the IRQ, you need to disconnect the floating device and use
        loopback.

        In some cases, attaching a unpowered device to a port will enable
        Parallel to detect IRQ by loopback, since the combination of port
        and device appears indistinguishable from a loopback connector to
        Parallel.

        FLOATNOTE:  Powered on devices usually hold the interrupt line in a
                    stable state and prevent IRQ autodetection. Remember
                    that  it is best to disconnect your parallel port
                    device(s) and use the loopback connector when you need
                    the absolute best results from Parallel.

          EXAMPLE:  On my home system, an unpowered HP LaserJet II printer
                    on an 8bit port "floats" and Parallel reliably reports
                    IRQ5. Attached to a 4bit port on the same system, the



Parallel Port Information System                                    Page 33
---------------------------------------------------------------------------

                    LaserJet is indistinguishable from a loopback
                    connector.  So turning the LaserJet off converts it
                    into an expensive, but handy, paperclip. Turning it on
                    prevents IRQ detection.

        TECH NOTE:  Whether or not a given device and port combination will
                    float, emulate loopback, or be invisible to Parallel is
                    determined by the pull-ups on each end, CMOS vs TTL
                    logic behavior, and the power available at the port to
                    a unpowered device. In the above example, I suspect
                    that enough power is provided by the 8bit TTL port to
                    drive the unpowered CMOS logic in the LaserJet into an
                    unstable oscillating state, which appears to the system
                    as a frenzy of level 5 IRQs.

        Port float is a handy effect, but use Loopback for best results.

        The most reliable way to determine IRQ is to use an external
        loopback connection. Loopback is described in the next section.

        TechNote: Making Your Own Loopback Connector
        --------------------------------------------

        We strongly advise that you make a loopback connector, inside of
        using the expedient paperclip approach.

        Simply obtain a male DB-25 connector and solder a permanent
        connection bewteen Pin 9 to Pin 10 on the back of the connector.

        Male DB-25 connectors are inexpensive and available in electronics
        parts stores. Cheap DB-25 jumper boxes cost only a few dollars.

        This will prevent any physical damage to your port, which is the
        major source of risk with this procedure, and the reason for our
        incessant nagging about precautions. This sort of loopback
        connector will be no more dangerous to your system than a printer,
        and is a handy accessory if you frequently use Parallel.

                                      Connect Pin 10 to Pin 9

          Back View          -----    Pin 10 - 4th from left on wider edge
          Male DB-25         |   |    Pin  9 - 5th from left on wider edge
          Connector          |   |
                             v   v
           ____________________________________________________________
          /                                                            \
          \     13  12  11  10   9   8   7   6   5   4   3   2   1     /
           \                                                          /
            \     25  24  23  22  21  20  19  18  17  16  15  14     /
             \______________________________________________________/

                          Pin 10 is the interrupt line (the ACK line)
                          Pin  9 is the high order data line (the 80h bit)



Parallel Port Information System                                    Page 34
---------------------------------------------------------------------------

     Miscellaneous Topics
     --------------------

        Technote: Pseudo-Bidirectional Ports, A Special Case
        ----------------------------------------------------

        A 4bit port is pseudo-bidirectional (also called pseudo-8bit,
        sometimes semi-8bit) when it is capable of performing 8BIT input
        when connected to a device which has strong drivers. So this
        pseudo-bidirectionality comes about as the relationship between the
        port and the device it is connected to.

        This type of port will appear to be a 4BIT port with most parallel
        port external peripherals, since low power CMOS drivers are by far
        the most common in these external devices.

        A few peripherals have stronger TTL drivers which can achieve 8BIT
        operation by overdriving the port. There are even sub-classes of
        ports which can achieve the effect depending on what data is used.

        Some vendors describe their ports as bidirectional when actually
        they are only pseudo-bidirectional and will function as 4BIT ports
        with most peripherals. True 8BIT ports are preferable because they
        have a significant speed advantage with most external peripherals.
        Indeed, some parallel port peripherals require true 8BIT behavior.


        Identifying pseudo-bidirectional ports
        --------------------------------------

        Step 1  =>  Read the cautions and disclaimers applying to loopback

        Step 2  =>  Read them again

        Step 3  =>  Run Parallel with no loop connector. Select any 4bit 
                    port which does not have "stuck bits".

                    The test only applies to 4BIT ports.

        Step 4  =>  Attach a parallel port extension cable to the port

        Step 5  =>  At the female DB-25, loopback Pin 8 to Pin 21 (GND).

        Step 6  =>  Run Parallel

        Step 7  =>  If Parallel reports "Data port has stuck bits" then the
                    port is likely to have semi-bidirectional capability.



Parallel Port Information System                                    Page 35
---------------------------------------------------------------------------

     Parallel Port Standards
     -----------------------

        4bit and 8bit parallel ports
        ----------------------------

           There is no true standard for these types of ports other than
           the actual behavior of existing systems.

           The original IBM PC Technical Reference manual gave a schematic
           for the parallel port which was ambiguous about the ability to
           input from the printer port.

           Various vendors interpreted the ambiguity differently ... and
           this appears to have been the genesis of a persistantly loose
           and confused industry attitude toward parallel port standards.


        EPP Specification
        -----------------

           There are two substantially incompatible standards for EPP
           parallel ports: the original EPP Standards Committee version 1.7
           standard, and the IEEE 1284 Committee standard.

           We call these two types of EPP ports "EPP 1.7" and "EPP 1284".

           The two standards are sufficiently similar that new peripherals
           may be designed in such a way as to support both standards, but
           existing EPP 1.7 peripherals will generally not operate with EPP
           1284 ports.

           The reference implementation of EPP 1.7 is the Intel 360SL chip.

           There are several implementations of EPP 1284 including the SMC
           66x, the National PC87xxx family, and perhaps others. Chipset
           vendors are rapidly adding advanced parallel port functionality
           to their product lines.  We will continue to review these chips
           as they appear from other manufacturers.

        ECP Specification
        -----------------

           The ECP port standard was developed by Microsoft and Hewlett-
           Packard. The standard specifies a PC parallel port with certain
           I/O registers and features and an external signalling behavior.

           The external signalling specification has been incorporated into
           the IEEE 1284 specification as the ECP mode of 1284.

           Reference implementations of ECP include the SMC 66x, the
           National PC87xxx, and others. These chips vary in the processes
           required to configure, and specific PC implementations will vary
           in their setup and/or BIOS support.



Parallel Port Information System                                    Page 36
---------------------------------------------------------------------------

        IEEE 1284 Specification
        -----------------------

           The IEEE 1284 specification defines the electrical signalling
           behavior external to the PC for a multimodal parallel port which
           may support 4bit, 8bit, EPP, and ECP modes of operation. Not all
           modes are required by the 1284 specification and the standard
           allows makes some provision for additional modes.

           The IEEE 1284 standard is targeted at specifying the behavior
           between a PC and an attached device, most specifically attached
           printers, although the specification is of interest to vendors
           of parallel port peripherals (disks, LAN adapters, etc, etc).

           The IEEE 1284 standard is currently maintained by the IEEE
           Standards Department. Larry Stein of Farpoint Communications
           maintains the working versions of the IEEE 1284.2 and 1284.3
           standards. (see Vendor Contact section).

           The IEEE standard has additional "substandards", including IEEE
           1284.3 (daisychain and multiplex standard) and the committee is
           beginning work on operating system standards and certification
           processes. The IEEE 1284 style parallel port is required for PCs
           to comply with the PC95 platform specification. We know of no
           parallel port implementations with native plug-and-play support.

           Various non-PC/DOS/Windows hardware and software vendors (Sun,
           Apple, Next) have shown interest in the committee's efforts. It
           is very likely that future versions of Windows will support the
           1284 specification, at least in the area of high-speed printing.
           The 1284 specification will also likely be approved as a
           component of the Desktop Management Task Force (DTMF) standard
           for PC resource management.

           The downside of the IEEE 1284 specification is that it does not
           specify the PC's internal interface to a 1284 compliant parallel
           port, either at the ISA register level or a software API level.
           Each chipset vendor is implementing subtly different behaviors
           in their chipsets, especially as regards configuration and setup
           - a process which is recreating the same system and software
           management mess that exists on earlier generations of parallel
           port technology. In order words, the IEEE 1284 specification
           does not answer the basic question "What is a parallel port and
           how do I perform I/O to it?".

           Perhaps the Committee's efforts will successfully expand to
           provide a unified solution, and perhaps such efforts will again
           be too little, too late in the technology curve to achieve a
           unified practical standard.

           To date, the IEEE 1284 standard does not represent a unified
           solution to the challenges and potential of future parallel port
           technology.  It represents a tolerable, if uninspired, next step
           in the evolution of particular classes of the technology.



Parallel Port Information System                                    Page 37
---------------------------------------------------------------------------


        Parallel Port Standards Diagram
        -------------------------------

           The following diagram attempts to depict the interrelatedness of
           various standards affecting the PC parallel port.  It is useful
           to keep in mind the distinctions between systems, interfaces,
           port designs, and specific chips when considering parallel port
           issues.  Since the parallel port has been a "poor relation" in
           the evolution of these standards, there are gaping holes in the
           overall standarization process.

           For example, there is no standard for hardware independent I/O
           to any parallel port and device.  Existing proposed standards
           are inadequate to the purpose.  Such a standard must provide a
           level of adaptive flexibility in expanding dynamically to
           incorporate new instances of ports, devices, and I/O methods.

           Actually, the Plug-and-Play standards concept is an interesting
           paradigm for such a parallel port software standard, which would
           treat ports, devices, and I/O methods as pluggable entities in a
           comprehensive and real-time extensible software architecture.

       -------------------------------------------------------------------
                 |
       Platform  | PC95 Platform       DTMF            Individual
       Level     |   Standard        Standard        Operating System
       Standards |                                  Software Standards
                 |                                                 ^
       ------------------------------------------------------------|------
                 |                                                 |
       Interface |   IEEE 1284 Interface     possible future IEEE  |
       Standards |         Standard          software standards  --- ?
                 |
       -------------------------------------------------------------------
                 |
       PC Port   |   EPP 1.7 Port            MS/HP ECP Port
       Standards |    Standard                  Standard
                 |
       -------------------------------------------------------------------
                 |                                           C&T
       Specific  |    Intel        SMC        National       Cirrus Logic
       Chips     |    360SL        66x        PC87xxx        StarTech
                 |                                           others
                 |
       -------------------------------------------------------------------
                 |
       Example   |   SL laptops    Intel      IBM            unknown
       Specific  |   with 360SL    Pentium    ThinkPad       or
       Systems   |   or equiv.     Mthrbrd    755            forthcoming
                 |
       -------------------------------------------------------------------



Parallel Port Information System                                    Page 38
---------------------------------------------------------------------------

     Parallel Port Buyer's Guide
     ---------------------------

        This Guide is intended to serve as a starting point for user's in
        search of quality parallel ports and peripheral devices.

        Parallel Technologies makes no warranties regarding these products
        and indeed we remind you to independently verify that the product
        will perform as expected in your environment.

        Parallel's evaluation and recommendation policy is:

          1. We recommend only those products that we ourselves have
             tested extensively.

          2. We make only positive recommendations. Inferior products will
             generally NOT be mentioned unless we consider them patently
             offensive to the user.

          3. Vendors are invited to arrange evaluations of their products
             so that they may be included in the Buyer's Guide. We will
             evaluate the product and propose a short description of it's
             capabilities, features, and quality. The vendor has the
             option of requesting that the product not be listed.

          4. We are planning to expand the coverage in the Buyer's Guide
             to include parallel port peripheral devices: LAN adapters,
             disks, SCSI adapters, CDROMs, and so forth. Again, interested
             vendors are welcome to arrange and actively contribute to a
             review of their product. The "no-pan" rule will apply.

        Direct Sales suppliers of products are listed in those cases where
        such suppliers are known and have proven reliable in the past.

        See the Vendor Contact section for specific vendor information,
        including telelphone numbers and email addresses, if applicable.


        4bit parallel ports
        -------------------

           This type of port is not recommended. Although most external
           parallel devices will support this type of port quite well, it
           is considerably slower at input operations than all other port
           types and has no cost advantages.  At a minimum, get an 8bit
           port or better yet, one of the advanced port types (EPP, ECP, or
           a multimodal port which support both EPP and ECP).

        8bit parallel ports
        -------------------

           8bit parallel ports are adequate for CURRENT printing purposes
           and may be used with all parallel port devices.  However, you



Parallel Port Information System                                    Page 39
---------------------------------------------------------------------------

           should consider buying an advanced parallel port (particularly
           an EPP/ECP capable multimodal port) when buying new systems.

           Mfg & Model     Features                        Suppliers
           --------------  -----------------------------   ---------------

           STB DSP 550     basic 2S+P ISA add-in card      Essential Data
                           requires jumper for 8bit mode   JAZ COmputer
                           has 16550 serial ports

           --------------  -----------------------------   ---------------
           Everex MagicIO  very clean signals
                           hard to find

           --------------  -----------------------------   ---------------
           other           8bit generic 2S+P I/O cards
                           Parallel reliably detects them
                           highly variable quality

           --------------  -----------------------------   ---------------
           QuickPath       multifunction ISA add-in card   Essential Data
           PortFolio       IDE, 4 floppy, game port
                           4 serial ports with 16650's
                           2 parallel ports


        EPP Parallel Ports
        ------------------

           EPP-capable parallel ports are generally found only on laptops,
           as a result of their introduction on the Intel 360SL I/O chip
           which was part of the SL chipset designed for laptops. We have
           listed one supplier (FarPoint) for a ISA add-in card suitable
           for desktops.

           Be sure that you identify the VERSION of EPP support the port
           provides, EPP 1.7 or IEEE 1284 EPP.

                    EPP 1.7 is the older Intel-style EPP which is
                    compatible with many existing parallel port devices
                    such a Xircom LAN adapters, Trantor SCSI adapters,
                    SyDOS cartridge disks, and so forth.

                    IEEE 1284 EPP is a new specification for EPP which is
                    not completely backward-compatible with the EPP 1.7.
                    This means that most existing parallel devices do not
                    work with IEEE 1284 EPP.

        Tech Note:  It is possible to design parallel port devices so that
                    they are compatible with BOTH the EPP 1.7 and 1284 EPP
                    specs, however existing devices typically don't do this
                    yet. Existing devices generally support only EPP 1.7.



Parallel Port Information System                                    Page 40
---------------------------------------------------------------------------

                    If you are buying a parallel port device (LAN, Disk,
                    CDROM, etc, etc) for general use, consider holding out
                    for a version that support BOTH EPP 1.7 and IEEE 1284
                    EPP or ECP modes of operation.  This gives you support
                    for the large installed base of SL style laptops and
                    compatibility with future system where IEEE 1284 style
                    ports will predominate.

             Mfg & Model              Features                 Supplier
           --------------  -----------------------------   ---------------
           Intel SL-based  any laptop fully implementing   many and varied
           laptops         Intel 360SL compatibility
           or compatibles  more than 50 models available
                           provides EPP 1.7 capability

           --------------  -----------------------------   ---------------
           Farpoint Fport  ISA add-in card with EPP 1.7    Farpoint
                           downloadable personalities
                           has extra useful IO addresses
                           has extra useful IRQ levels
                           good documentation
                           value-added software for
                           port configuration and drivers
                           for fast DOS / NOVELL printing
                           excellent tech support

           When buying an EPP-capable laptop for use with EPP external
           peripherals, it is important to BE VERY CLEAR about what you are
           getting.  Even different models from the same manufacturer will
           have different implementations of EPP.  CHECK COMPATIBILITY with
           the specific peripherals you intend to use.

           Example 1:  Various SL-based Compaqs (SL25s, Conturas) have long
           has excellent implementations of EPP 1.7. However the more
           recent Compaq Aero appears to have a unique implementation which
           is not fully SL compatible.

           Example 2:  The IBM Thinkpad 750 has an SL-compatible EPP 1.7
           port, but the 755 model has a non-SL-compatible EPP port.
           Devices which work on one 700 model do not work on another.

           NOTE: This is not an indictment of these laptops by any means,
           they are fine systems overall. It IS A REMINDER that you must
           independently verify the current state of compatibility between
           any particular EPP-capable laptop and parallel devices you plan
           to use with them. Laptop vendors generally will not know the
           answers to your questions about parallel ports and the best bet
           is the peripheral vendor.

           EPP 1.7 type parallel ports MAY OR MAY NOT be supported by any
           specific new IEEE 1284 type peripheral. We predict that most
           developers of new devices will want to support EPP 1.7 in order
           to be compatible with the install base of SLs, however they may



Parallel Port Information System                                    Page 41
---------------------------------------------------------------------------

           opt to just support IEEE 1284 style EPP which leaves the SLs up
           the creek. It is possible to support both.

           So there is a certain risk factor in buying a laptop with only
           EPP 1.7 support today ... as an increasing number of systems are
           appearing with multimodal 1284 style ports. On the other hand,
           buying a laptop without EPP 1.7 leaves you incompatible with a
           large variety of existing external peripherals - you will have a
           bit of a wait as peripheral vendors scurry to support IEEE 1284.

           In the best of worlds, you will buy a system which supports all
           the IEEE 1284 modes, EPP 1.7 to boot, and comes with a handy
           utility which allows you to configure your port easily.


        ECP Parallel Ports
        ------------------

           There are some very nice chipsets coming out for multimodal
           parallel ports which support the multiple parallel port modes.

           These chipsets have been appearing in systems since early this
           year and have just now reached the stage where they are safe
           consumer choices given a little caution.

           In some cases, early "steps" of particular chips had significant
           flaws and the buyer should verify that he is getting the latest
           step - not something that's been in a warehouse since Easter.

           Vendors may or may not provide user level support for selecting
           the parallel port mode. Check that any PC you are considering
           has appropriate CMOS port configuration or at least a separate
           utility for the purpose. Be aware that vendors may have BIOS
           upgrades which retroactively enable such support.

           If you need immediate support for existing parallel port devices
           operating in EPP mode you should INDEPENDENTLY VERIFY that the
           device works with the particular system you are considering. Be
           aware that existing EPP 1.7 type devices may or may not work
           with any particular new multimodal parallel port. It is still
           early days yet for ECP support in parallel port devices and this
           caution also applies to any early versions of such devices you
           might consider - check that they work with your specific system.



           Mfgr & Model    Features                        Supplier
           --------------  -----------------------------   ---------------
           Intel Premiere  motherboard with SMC 665 chip   used in many
           Pentium PCI     66xQFP chip has various bugs    Pentium systems
           Motherboard     be sure you get the 665GT chip  from various
                           requires Plato version 10 BIOS  "manufacturers"
                           to enable EPP/ECP in Setup



Parallel Port Information System                                    Page 42
---------------------------------------------------------------------------

           --------------  -----------------------------   ---------------
           Other systems   be sure you get the 665GT chip  various
           with SMC 66x    check for software support

           --------------  -----------------------------   ---------------
           SIIG IDE        multifunction ISA add-in card   superstores, etc
           Professional    IDE, floppy, 2serial, parallel
                            uses the SMC 66x chip
                           again, avoid the QFP version
                           no port configuration software
                           no value-added software
                           decent jumper documentation

           --------------  -----------------------------   ---------------
           Farpoint        ISA add-in card with SMC 66x    Farpoint
           Fport Plus      serial and parallel port only
                           good configuration utility
                           fast DOS / Windows driver
                           1 16650 serial port
                           excellent tech support

           --------------  -----------------------------   ---------------
           Farpoint        ISA add-in card with SMC 66x    Farpoint
           Fport IDE       IDE, 2 serial, parallel
                           good configuration utility
                           fast DOS / Windows driver
                           2 16650 serial w/ extra IRQs
                           excellent tech support

           --------------  -----------------------------   ---------------
           Kouwell         typical clone SMC 66x ISA card  Essential Data
                           IDE, 2 16550 COM, parallel,
                           no value added software
                           very low cost
                           check that you get the GT step


           There are several bewares for the Intel Premiere PCI motherboard
           which has the SMC 66x I/O chip. Make sure you get the GT step
           rather than the QFP step of the 66x chip. The QFP step has only
           EPP 1284 (with minor bugs) and a serious bug in the serial port
           FIFOs which prevent them from operating as 16550-compatibles at
           high speed. Also, you will need the version 10 Plato BIOS in
           order to enable the ECP functionality via CMOS.  Previous Plato
           BIOSii limit the parallel port to "Normal" (4bit) or "Extended"
           (8bit) modes.



Parallel Port Information System                                    Page 43
---------------------------------------------------------------------------


        Advanced Parallel Port Chipsets
        -------------------------------

           Mfg & Model     Features                        Supplier
           --------------  -----------------------------   ---------------
           SMC 66xQFP      multifunction I/O chip          SMC
                           multiple parallel port modes
                           IEEE 1284 EPP and ECP
                           no EPP 1.7
                           has bad serial port FIFO bug
                           EPP mode has minor bugs
                           good chip, but use the GT step

           --------------  -----------------------------   ---------------
           SMC 66xGT       corrected version of 66xQFP     SMC
                           IEEE 1284 EPP and ECP
                           adds EPP 1.7
                           fixes various bugs, com FIFO


           --------------  -----------------------------   ---------------
           National        PC87xxx SuperI/O chip family    National
           Semiconductor   322 is EPP 1.7 only
                           332, 334, 303, 323, and 306
                           have EPP 1.7, EPP 1284 & ECP
                           various features on chips:
                           IDE, 16650 serial, floppy,
                           keyboard, clock, serial IR
                           5 volt and 3.3 volt versions

           --------------  -----------------------------   ---------------
           Chips &         information not available       C&T
           Technologies    at this time, watch this space



Parallel Port Information System                                    Page 44
---------------------------------------------------------------------------

     Vendor Contact Information
     --------------------------

     Parallel Technologies     Jay Lowe, VP          206-869-1136 voice
       parallel port wizards   CIS 76640,203         206-869-1133 fax
       contract development    Don Schuman, Pres
       product licensing       CIS 72242,3631
       DirectConnect(TM)
         technology licensing

     IEEE 1284 Standard        IEEE Standards Dept.  800-678-IEEE

     FarPoint Communications   Larry Stein           805-726-4420
       direct sales            CIS 71514,1057
       spec. in parallel port  IEEE 1284.2 & 1284.3
       very experienced          Chairman

     Essential Data            Bruce McKeag          800-795-4576 voice
       direct board sales      CIS 70572,2670        408-955-0440 voice
       active on Compuserve                          408-955-0821 fax

     JAZ Computer Products     J. Zarifis            914-632-9531 voice
       direct board sales      CIS 71042,1251
                               GEnie J.ZARIFIS

     Standard Microsystems     Robert Gross          516-273-3100
      chipset vendor

     National Semiconductor    Kishor Padmanabhan    408-721-4563
      chipset vendor

     Chips & Technologies      forthcoming
       chipset vendor

     IEEE 1284.2               Larry Stein           805-725-4420
          1284.3 Committees    CIS 71514,1057
                                - also -
                               EET:STDFRM CIS forum




          Reputable vendors of parallel port technology are invited to
                 forward us a short listing of their interests
                  and contact information for inclusion here.



Parallel Port Information System                                    Page 45
---------------------------------------------------------------------------

     Technical Support
     -----------------

        Parallel is Freeware, and comes with Freeware-style support. It has
        been extensively tested with a range of systems from original PCs
        to Pentiums and works with all parallel port devices we've seen.

        We are willing to offer friendly assistance on an as-available
        basis, but only via Compuserve mail (CIS 76640,203), via Internet
        Email to jaylowe@halcyon.com. or in the Compuserve IBMHW forum.

        Alas, we do not offer free telephone assistance to the public.

        If you are in dire need of technical support in solving port
        related problems, you may open a support account by contacting:

        Mailing Address                         Shipping Address
        ---------------------------             ---------------------------
        Parallel Technologies, Inc.             Parallel Technologies, Inc.
        PO Box 7                                10603 170th CT NE
        Redmond, Wa 98073-0007                  Redmond, Wa 98052
        (206) 869-1136
        (206) 869-1133 (fax)                    ( for UPS, FEDEX, etc )
        Compuserve: 76640,203
        InterNet:   76640.203@COMPUSERVE.COM
          -or-  :   jaylowe@halcyon.com

        Custom versions of the Parallel Port Information Utility, and
        source code, are available.

        Vendors of parallel port hardware are invited and requested to
        contact us so that we may ensure that Parallel is compatible with
        their products.

        Permission is given to distribute and use Parallel without charge,
        provided you adhere to the terms and conditions of the license
        agreement given below. Specifically, you may not charge anyone for
        for sharing or using Parallel, and you may not modify it or change
        it. Nor may you use it as part of a commercial product or service
        without our written permission.

        Vendors may freely distribute Parallel on an individual basis,
        without charge, by electronic BBS or other means.  However, you may
        not include it in or with your product without our written
        permission.

        We welcome your comments and suggestions by Email, phone, or fax.

        If you have particular features you would like to see supported by
        Parallel, we'd be more than glad to hear from you.



Parallel Port Information System                                    Page 46
---------------------------------------------------------------------------

     About Parallel Technologies, Inc.
     ---------------------------------

        We at Parallel Technologies' have been creating innovative parallel
        port devices and software since 1989. Here are a few highlights:


        Firsts, Bests, and Mosts
        ------------------------

            o  1st ... parallel port network adapter
            o  1st ... enhanced, bus-speed, parallel port
            o  1st ... parallel port external SCSI disk
            o  1st ... passthrough printing capability
            o  1st ... automatic self-configuring drivers
            o  1st ... universal support for all types of parallel ports
            o  1st ... network adapters with multiple media support
            o  1st ... Windows 3.1 multimedia driver for parallel adapter
            o  1st ... Multiple Parallel Device API for shared devices
            o  1st ... intelligent parasitic power for self-powered devices
            o  1st ... demonstration of daisychained parallel peripherals
            o  1st ... demonstration of multiplexed parallel peripherals
            o  1st ... Parallel Port Expansion System (now IEEE Multiport)
            o  1st ... Parallel Port Developer's Kits
            o  1st ... general purpose parallel port networking (DirectNet)
            o  1st ... Win 95 parallel port networking (DirectNet VCOMM)

            o  PC MAG Editor's Choice for Ethernet parallel port NIC
            o  most total network adapters  --  7 and counting...
            o  most total parallel port peripherals  --  25 and counting...


        Partial List of Parallel Technologies' Developments
        ---------------------------------------------------

            o  parallel port Arcnet adapter
            o  parallel port Ethernet Adapter (two versions)
            o  parallel port Token Ring Adapter (two versions)
            o  parallel port portable SCSI disk drive
            o  parallel port portable IDE disk drive
            o  parallel port MIDI interface for Windows
            o  parallel port Zero-Slot mouse adapter
            o  parallel port IR Wireless Adapter
            o  parallel port DSP signal processing interface
            o  parallel port Multiport daisychaining system
            o  parallel port Multiport 4-way parallel device multiplexor

            o  DirectNet ODI driver for parallel port networking
            o  DirectNet VCOMM driver for parallel port networking

            o  DirectNet 4BIT cables for parallel port networking
            o  DirectNet ECP cables for parallel port networking
            o  DirectNet Universal cables for parallel port networking



Parallel Port Information System                                    Page 47
---------------------------------------------------------------------------

            o  DirectNet 4BIT/ECP and UCM cable interface specification
                  licensed to Microsoft for joint Microsoft/PTI publication

            o  Parallel Port Developer's Kit (Level 1)
            o  Parallel Port Developer's Kit (Level 2)
            o  Super IEEE 1284 Printing System Developer's Kit
            o  DirectNet Parallel Port Networking Manufacturing License Kit
            o  DirectNet Parallel Port Networking Software License Kit


        Many of these products, or their hardware and software components,
        are available for OEM licensing.

        We have in-depth experience with the wonderful and sometimes
        bizarre world of the PC parallel port and have served on both the
        EPP and IEEE 1284 standards committees. Having created more than
        TWO DOZEN parallel port devices with their associated drivers and
        software utilities, we are the most experienced source for off-the-
        shelf technology, developer tools, and contract services.

        Here are a few of our current and forthcoming products that you may
        find interesting.


        Parallel Port Developer's Kits
        ------------------------------

        Parallel Technologies offers parallel port Developer's Kits which
        contain those hardware and software components necessary to build
        very high-speed, consumer-quality external devices.

        The Developer Kit technology has been used in over 25 parallel port
        devices including network adapters, parallel port SCSI and IDE
        disks, parallel port wireless IR adapters, parallel port MIDI and
        mouse interfaces, parallel to serial interfaces, and so forth.

        The software includes support for all types of ports, IO code that
        is extremely resistant to port idiosyncrasies, and full auto-
        detection of all port hardware features. The code is very well
        documented. A selection of sample drivers for parallel port devices
        is also available.


           Level One Developer's Kit
           -------------------------

                    Hardware schematics, timing diagrams, access methods
                    and all other hardware information required to
                    implement basic peripheral devices that are compatible
                    with 4BIT, 8BIT, semi-8BIT,and EPP parallel ports

                    The software section includes sample source code for
                    register and block data access to the sample device.



Parallel Port Information System                                    Page 48
---------------------------------------------------------------------------


           Level Two Developer's Kit
           -------------------------

                    Includes the Level One Kit PLUS

                         additional very high speed IO techniques,
                         passthrough port design techniques
                         daisychain and multiplexor Multiporting design
                         additional ECP hardware design techniques
                         additional source code for ECP I/O techniques
                         techniques for self-powered parallel devices

                         full source code for Parallel autodetect utility

                     Also includes full EPP and IEEE 1284 specifications.

           Super IEEE 1284 Developer's Kit
           -------------------------------

                    Prototyping board, printer side interface FPGA
                    equations, assembler source for 1284 negotiation,
                    Windows 3.1 driver source.

                    Allows the rapid development of IEEE 1284 printers.

                    Also Super 1284 goes BEYOND the IEEE 1284 spec to allow
                    very high-speed bi-directional I/O on 4BIT, semi-8BIT,
                    and 8BIT ports.  This means that Super 1284 printers
                    can operate bi-directionally at very high speeds
                    (upwards of 300Kbyte/sec) even on the installed base of
                    "old-fashioned" standard parallel ports.

                    Super 1284 maintains complete compatibility with IEEE
                    1284 ports and printers. It is a compatible enhancement
                    that allows printer vendors to support high-speed
                    operation without requiring EPP and ECP ports.

        DirectNet -- The Parallel Port Networking System
        ------------------------------------------------

                    The DirectNet parallel port networking system has been
                    incorporated into Windows 95 and may be licensed for
                    inclusion in other operating environments.

                    The DirectNet system is a family of completely external
                    connection devices and network driver software that
                    allows PC-to-PC plug-and-play cable connections to be
                    used as an alternative to more expensive LAN hardware.

                    The DirectNet hardware technology includes 3 point-to-
                    point cables, and multiport hub, and a distributed
                    multdrop system which uses RJ-11 standard phone wiring.



Parallel Port Information System                                    Page 49
---------------------------------------------------------------------------

                    DirectNet supports speeds of 40 - 500+ KBytes/sec
                    depending on the parallel ports involved and various
                    other factors. The system is completely self-adaptive.

                    Because DirectNet provides a suite of standard network
                    drivers, it may be used with many existing networking
                    and connectivity systems such as Windows 95, Windows
                    for Workgroups, Netware Lite and Personal Netware, etc.
                    DirectNet connections have been tested with more than a
                    dozen commonly available networking and connectivity
                    software packages.

                    DirectNet is now in a  BETA RELEASE status and Parallel
                    Technologies is providing manufacturing and software
                    licenses vendors who wish to include DirectNet products
                    or capability in their product lines.


        Parallel -- the Parallel Port Information Utility
        -------------------------------------------------

                    A handy utility which examines your system's parallel
                    ports and reports the Port Type, IO address, IRQ level,
                    BIOS name, and an assortment of informative notes and
                    warnings in a compact and easy to read display. The
                    output may be redirected to a file for tech support
                    purposes. Parallel uses very sophisticated techniques
                    for port and IRQ detection and is aware of a broad
                    range of quirky port features.

                    Parallel is the definitive parallel Tech Support tool.

                    Parallel is Freeware, subject to a restricted license
                    agreement. It may be used free of charge for any
                    personal, non-commercial purpose. Parallel may not be
                    sold for profit, nor may it be distributed with any
                    other product sold for profit. Vendors should contact
                    us regarding commercial licenses.


        Product Licensing
        -----------------

                    Most of our products are available for licensing,
                    including DirectNet "connectoids", network adapters,
                    EPP-capable disk, parallel-SCSI interface, parallel
                    MIDI adapter, and the MultiPort expansion system.

                    Also available are numerous off-the-shelf hardware and
                    software components including: device schematics, FPGA
                    equations, DOS and Windows driver source code, etc.



Parallel Port Information System                                    Page 50
---------------------------------------------------------------------------

        Development Services
        --------------------

                    We specialize in contract development of parallel port
                    peripherals and associated software including DOS and
                    Windows device drivers. Our broad and deep experience
                    with parallel port devices and our commitment to
                    specialization allows us to design, implement, test,
                    and support them very efficiently.

                    You might be interested in our 45/90 development offer.

                    We propose to convert almost any ISA peripheral into a
                    parallel port device in only 45 days to prototype, 90
                    days to production.

                    We also offer more limited development support, such as
                    developing additional device drivers or enhancements
                    for existing peripherals.

                    We are quite experienced with EPP and ECP ports and are
                    ready to upgrade your existing parallel port devices
                    for peak performance.


        Consulting and Training
        -----------------------

                    In support of in-house development, you will find our
                    consulting and training services invaluable in avoiding
                    the pitfalls of parallel port development - and achieve
                    the highest possible product performance and quality.

                    We conduct in-house trainings and design consultations
                    in hardware, software, and product design / management.

                    You may find these  trainings useful in bringing your
                    development and management team up to speed on parallel
                    port issues.



Parallel Port Information System                                    Page 51
---------------------------------------------------------------------------

     Software License Agreement
     --------------------------

                                    IMPORTANT

     Read this agreement before installing or using the Software. Installing
     and/or using the Software on your computer indicates your acceptance of
     these terms. If you do not agree to these terms and conditions, delete
     the Software and all it's associated files from your computer. This
     Software License Agreement gives you ONLY RESTRICTED RIGHTS to use the
     Software (and all it's associated files and documentation) as follows:

     YOU MAY

       1.  Use the Software without charge on as many systems as you wish,

       2.  Share the Software with others for their personal use, but only
           if you share it intact, without any changes or modifications of
           any kind, and complete with all it's documentation and associated
           files. You must pass it on exactly in the same form as we release
           it, or not pass it on at all.

       3.  Make backup copies of the Software, so long as you place our
           copyright notice on the backup copies,

       4.  Request and receive limited technical support as provided in the
           Freeware Product Support Policy below.

       5.  Vendors may distribute the Software free of charge by electronic
           or other means for the purpose of technical support, but may not
           include the Software in products without our written permission.

     YOU MAY NOT

       1.  Use the Software in any way except as provided in this agreement,

       2.  Modify, alter, copy, transfer, or reproduce the Software in any
           way, except as expressly allowed in this agreement,

       3.  Translate, de-assemble, de-compile, reverse program, or reverse
           engineer the Software or any of its components,

       4.  Charge any kind of fee for distributing the Software without our
           written permission,

       5.  Use the Software for commercial purposes without our permission,

       6.  Sublicense, lease, rent, sell, distribute, or otherwise dispose
           of the Software without our written permission.

     This license is effective from the date of first use of the Software and
     shall remain in force until terminated. You may terminate this agreement
     by destroying any and all copies of the Software and its documentation.



Parallel Port Information System                                    Page 52
---------------------------------------------------------------------------

     Parallel Technologies, Inc. may terminate this agreement if you fail to
     comply with any of the terms and conditions of it. You agree to destroy
     any and all copies of the Software and its documentation, in whatever
     form, if we terminate this license agreement, and you agree to provide
     us written certification of such destruction upon our request.

     Statement of Exclusion of Warranty

     ALL PRODUCTS DELIVERED PURSUANT TO THIS AGREEMENT ARE DELIVERED ON AN
     "AS-IS" BASIS AND PARALLEL TECHNOLOGIES, ITS DEALERS AND DISTRIBUTORS,
     EXPRESSLY DISCLAIM ANY AND ALL WARRANTIES OR CONDITIONS OF MERCHANTABLE
     QUALITY OR FITNESS FOR A PARTICULAR PURPOSE.

     Limitation of Liability

     PARALLEL TECHNOLOGIES DISCLAIMS ALL WARRANTIES RELATING TO THIS
     SOFTWARE, WHETHER EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO ANY
     IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR
     PURPOSE, AND ALL SUCH WARRANTIES ARE EXPRESSLY AND SPECIFICALLY
     DISCLAIMED.  NEITHER PARALLEL TECHNOLOGIES NOR ANYONE ELSE WHO HAS
     BEEN INVOLVED IN THE CREATION, PRODUCTION, OR DELIVERY OF THIS
     SOFTWARE SHALL BE LIABLE FOR ANY INDIRECT, CONSEQUENTIAL, SPECIAL,
     PUNITIVE, OR INCIDENTAL DAMAGES OR DAMAGES DUE TO LOST PROFITS, DATA,
     OR INFORMATION ARISING OUT OF THE USE OR INABILITY TO USE SUCH
     SOFTWARE EVEN IF PARALLEL TECHNOLOGIES HAS BEEN ADVISED OF THE
     POSSIBILITY OF SUCH DAMAGES OR CLAIMS.  IN NO EVENT SHALL PARALLEL
     TECHNOLOGIES' LIABILITY FOR ANY DAMAGES EVER EXCEED THE PRICE PAID FOR
     THE LICENSE TO USE THE SOFTWARE, REGARDLESS OF THE FORM OF CLAIM.  THE
     PERSON USING THE SOFTWARE BEARS ALL RISKS AS TO THE QUALITY AND
     PERFORMANCE OF THE SOFTWARE.  This warranty gives you specific rights
     and you may have other rights.

     This agreement shall be governed by the laws of the State of
     Washington and shall inure to the benefit of Parallel Technologies,
     Inc. and any successors, administrators, heirs and assigns.  Any
     action or proceeding brought by either party against the other arising
     out of or related to this agreement shall be brought only in a STATE
     or FEDERAL COURT of competent jurisdiction located in King County,
     Washington.