SPC 6.1

                     Integrated equipment utility

                                  by
                               Bob Eyer
                             [73230,2620]
                  INTERNET:73230.2620@compuserve.com

                 Canadian Micro Information Exchange
                     905-455-4843 & 905-455-6575

                            July 20, 1994


     -----------------------------------------------------------------
     SEE ENCLOSED SHARE.TXT FOR OTHER FINE PROGRAMS AVAILABLE FROM THE
     SAME AUTHOR.
     -----------------------------------------------------------------

     See bottom of doc for changes since version 6.0 posting.


     Syntax
     ------

     SPC [? H A P F E D S] [=identification] [>file/PRN/COMx]


     Options (any order, any case, any combination)
     ----------------------------------------------

     ? or H or HELP - Brief help screen.

     A -   Use  standard  ASCII  character  set,  to  accommodate Epson
           compatible  printers.   Default  is  to  use  extended ASCII
           character set for display.

     P -   Pause printer.  Intended to be used ONLY as  an  enhancement
           of  DOS  PRINT  when  loaded as a TSR.  To resume printing,
           enter PRINT.

     F -   Include drives A: and B: in drive report.  No include is the
           default.   When  running  in  a network environment, include
           this parameter, since  the  A:  and  B:  drives  are  likely
           reassigned network drives, not floppy drives.

     E -   Exclude UNDEF drives from totals.
           Default  is  to  include  drives flagged as UNDEF in totals.
           (UNDEF drives are most likely CDROM or Worm drives).

     D -   Force  DUPlicate  detection  instead of SUBSTed detection in
           drive  report  and  net  duplicates  out of the totals.  The
           default is SUBSTed detection, unless a supported network  is
           detected, in which case SPC defaults to DUPlicate detection,
           to  avoid  confusion  between  SUBSTed  detection  and drive
           reassignment  under  network  configuration.   The  D  or  S
           options are used for overriding these defaults.  For details
           see discussion below.

     S -   Force SUBSTed detection  instead of  DUPlicate  detection in
           drive report and net SUBSTed drives out of the totals.

     = -   Identification string.  SPC puts your identification  string
           on  the  right half of Line 1 of the display, overriding the
           author credit, if you use  '='  followed  by  your  selected
           identification information.  SPC looks for the occurrence of
           the equals sign on the commandline and interprets everything
           following it (up to but not including redirection and piping
           symbols)  as  an  identification  string  rather  than as an
           option.  SPC no longer converts  your  ID  string  to  upper
           case.   Maximum  length  is  14  characters.   Default is to
           display author credit.


     Use of SPC options
     ------------------
     SPC  options  are  provided  largely  to supply fine-tuning in SPC
     applications as well as solutions to  specialised  problems  which
     few  users will have.  For example, only network operators who are
     not using the network types which SPC  can  detect  will  find  it
     necessary to use the D option.

     Generally, use of SPC's options will not be needed.

     To get help on the use of SPC options, just enter

     SPC H

     The  following  is  a  brief explanation of SPC's display, hitting
     the  main  points  without  going  into   detail   (the   detailed
     explanation   is   available  in  the  complete  docs,  obtainable
     through registration).

     Let's look at a relatively full display.   Situation  is  we  have
     logged  in  remotely  to our own BBS and have remotely initiated a
     print job at the host through a shell allowing us  a  little  more
     than 200k of memory space.  We issue the command

     SPC P =Lan remote

     so as to document our work remotely (this assumes that SPC  is  in
     the DOS path at the host).

Ú Monday 06-06-1994  02:34:03 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ SPC 6.0  ¿
³ DOS 5.00  VGA  Color  3 MButtons    LPT1: S* PMP     ID: Lan remote ³
³ FC (01/15/88)  ISA - K R 8259 -  -----      80386/31.2    80387/140 ³
³ X...1.......2.......3*......4.!...5.........................    336 ³
³  Resident:        TIMEPARK-512     MARK-1392        QUICKEYS-448    ³
³  QUICKEYS-448     DOSEDIT-1968     MARK-1424        PRINT-7184      ³
³ -   -     -       655360/204720      1049      EMS 4.0: 1278/885  1 ³
³ Port Ä Address  Config  ÄÄÄÄÄÄ UART ÄÄ Modem ÄÄ DTR Ä RTS Ä Carrier ³
³ COM1:  3F8      19200 N 8 1    16550A  Ok       High  High  High    ³
³ COM2:  2F8      2400 N 8 1     16450   -        -     -     -       ³
³ Drv ÄÄ Status Ä Sector Ä Cluster ÄÄÄ Free Ä Allocated Ä Total Ä Drv ³
³ C:     BOOT       512     2048       3.170    14.629    17.799   C: ³
³ D:                512     2048       7.750    10.049    17.799   D: ³
³ E:                512     4096       3.318     3.698     7.016   E: ³
³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
³ M:   Totals less SUBSTed drives:    14.238    28.376    42.614   M: ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     This  is the look of the "snapshot" display advertised, and it is
     designed to present as much redirectable information as  possible
     in a very small space, yet in as meaningful a way as possible, so
     that the user can obtain a quick overview.

     There  are  many equipment programs available, some which present
     much more information than SPC.  However, SPC is the only program
     that  focuses  on  achieving  the  highest  possible   ratio   of
     information  to  examination time in the smallest possible space.
     SPC's philosophy is that the user should not have to flip through
     dozens of pages of output to get a fairly complete overview.  The
     overview should be quick and not  require  any  keystrokes  other
     than  those  needed  to run the program, and certainly should not
     use any non-redirectable display modes such as graphics or direct
     screen writing.  For, an equipment program should  make  possible
     the  fast  transfer  and  comparison  of  machine  information by
     Email.  This indeed, is the reason why SPC's display is precisely
     71 characters wide (within the usual limit for  email  processing
     systems).

     The  arrangement of the display is designed to trigger the user's
     memory of the meaning of the figures displayed.  Every  character
     has a meaning; the snapshot even draws a graph with two variables
     displayed   on  it.   The  user  should  have  little  difficulty
     understanding   the   display   after   reading   the   following
     description.


     Line  1  of  the display informs us that the machine is run under
     DOS 5, has a VGA color  monitor  with  a  3-button  Logitech-type
     mouse.  LPT1: is connected to a Selected printer (S--other values
     are  1  or  2,  which  may  have  different meanings to different
     printers) and data (*) is currently flowing to the  print  buffer
     through  the  DOS PRINT multiplexer (PM).  PMP indicates that the
     printer is about to be paused (see use  of  the  P  command  line
     parameter above).

     Line 2  provides  the  model  number  (FC--typical  of  AT  class
     machines),  the  BIOS  revision date, the type of motherboard bus
     architecture (ISA or  MCA).   This  is  immediately  followed  by
     technical motherboard information, specifically,

         Data                               Values

         Wait for external event installed  E or -
         Keyboard intercept used            K or -
         Real time clock installed          R or -
         Slave 8259 installed               8259 or -
         HD BIOS uses DMA channel 3         3 or -

     This is followed by the keyboard status group:

         Enhanced keyboard                  E or -
         Insert mode on                     I or -
         Caps lock set                      C or -
         Num lock set                       N or -
         Scroll lock set                    S or -

     Finally,   the   identity   and   speeds  of  the  processor  and
     coprocessor, if any.  the graph markers (X, 1,  2,  etc)  on  the
     next line correspond to the lower speed boundary for each type of
     machine:

         Processor         Speed Index   Clock speed

     X   8086              1             4.77 - 10 MHz
     1   80186             2             "
     2   80286             7             6 - 20
     3   80386             26            16 - 33
     4   80486             100           "
     5   80586 (Pentium)   300           60 - 200

     Line 3 presents the speed graph for both Processor  (*)  and  the
     coprocessor  (!).   The  maximum  of the scale is 18,000, and the
     scale  is  logarithmic.   At  the  end  of  this  line  is  total
     environment usage in bytes.

     The speed tests  are  simply  measures  of  how  many  arithmetic
     operations  are  done  by  each  processor  in  a fixed number of
     clock ticks.  In the case of  the  central  processor  (CPU)  the
     operation  is  integer  addition;  in  the  case  of  the numeric
     coprocessor (NCP), the operation  is  double-precision  division.
     Double-precision   arithmetic   is   always   done  by  hardwired
     routines in the coprocessor rather than in a  software  emulation
     if the former is available.

     The coprocessor speed test is normalised so that it  reads  about
     the same as the CPU test in lab test conditions when SPC does not
     detect  a  coprocessor.   For  display  purposes  by  end  users,
     however, SPC suppresses the coprocessor speed display when  there
     is no coprocessor.  For this reason, the coprocessor reading is a
     reasonably  accurate measure in relation to the central processor
     reading.

     The maximum limit of the speed graph has been adjusted to reflect
     the estimated maximum speed of  a  Pentium's  coprocessor,  given
     that  the  fastest Pentiums have clock speeds of the order of 200
     MHz.  Tests on a 60 MHz Pentium have given speed readings of  542
     for  the  CPU and 5601 for the NCP (nothing resident except DOS).
     It follows that a 200 MHz Pentium coprocessor  would  be  in  the
     18,000 range.  This is about 45 times faster than a 20 MHz 80387.

     Beginning with the 486, the sense of the graph markers is changed
     to  reflect  speed ranges under common resident loading patterns.
     For example, use of Windows for Workgroups may drop the Pentium's
     speed as seen by the end user all the way from 542 to  180.   Use
     of  a  few  common drivers and small TSR's may drop the Pentium's
     speed from 542 to the 300 range.

     Percentagewise, such large  speed  sacrifices  are  not  seen  in
     machines  at  the  386  class  or lower.  The implication is that
     Microsoft may not yet have developed software  capable  of  using
     the Pentium at maximum efficiency.

     The next group of lines labelled "Resident" presents a listing of
     TSRs (memory-resident programs) currently in memory with the size
     of  each  appended (without environment and data segments).  This
     list is presented only where the DOS version is 4 or later.

     The  "memory"  line then presents, in sequence, the Verify status
     (VER or -), a reserved area for future development, the  type  of
     network  or  multitasking  environment detected (WINDOWS, PC LAN,
     NOVELL, MS NET, or DV or DDOS), total/free  conventional  memory,
     available  extended memory in thousands of bytes, and information
     about expanded memory where detected including the number of  EMS
     handles in use.

     The extended memory readout refers to  installed  capacity  above
     the  first 1 Meg, rather than useful free space.  For DOS 4+ this
     readout will not  vary  with  EMS  conversion  or  allocation  to
     RAMDISK   use.   For  DOS  versions  below  4,  the  reading  may
     erroneously indicate no installed  capacity  if  SIMM  chips  are
     used.

     The  communications  port indicators are fairly self-explanatory.
     However, a couple of cautionary remarks are in order.  First, the
     UART indicator is designed to work in DOS environments.   Windows
     reconstructs  DOS  to  a  large  extent, but screws up in certain
     areas.   For  this  reason,  the  UART  indicator  may  not  read
     correctly  under  Windows.  Secondly, the modem function detector
     is based on the assumption that the  modem's  DSR  line  [Dataset
     Ready]  is  high  when  the modem is powered on.  Most modems and
     NVRAM factory defaults satisfy this  condition;  however,  others
     may not.

     The only things needing explanation in the drive listings are the
     Status indicators:

     Status   Meaning

     BOOT     Drive used for booting computer (DOS 4 or later).

     CSPEC    Drive where the CONFIG.SYS variable COMSPEC says
              COMMAND.COM is located.

     SUBST    A drive defined by redirection, usually through use of
              DOS's SUBST command.

     DUP      A  drive  that  has  the  same  free space as some other
              drive.  Except in extremely rare circumstances,  such  a
              drive will be the same as if it had been a SUBSTed drive
              on  a standalone machine.  Of course, in a network, many
              drives may be defined as redirected to  begin  with,  in
              which  case  each ought to appear in SPC's display as an
              "original" drive; for this reason SPC  defaults  to  DUP
              mode when a network is detected.

     UNDEF    A  drive  that  has more than 65,534 clusters (such as a
              CDROM drive).  The default  mode  of  SPC  is  to  count
              such drives in space totals.

              DOS drives identify the position of clusters for a  file
              through  a  File  Allocation Table, and this Table has a
              maximum size of 65,534 clusters (very large  drives  are
              made  possible through use of very large cluster sizes).

              CDROM  drives  do  not  need  to  use  this  method   of
              identifying  the  position  of files on the disk.  Since
              they  are  readonly  media,  there  is  no   reason   to
              anticipate  that  file  clusters  of  each  file are not
              consecutive (fragmented) on the disk.  This fact  allows
              CDROM  drives  to  accommodate  much  larger  numbers of
              "clusters".  Cluster readouts for CDROM drives using DOS
              programs therefore commonly give the number FFFF  (hex),
              which means "undefined" (in excess of the maximum number
              that DOS's Function 32, Int 21 can report)--hence, SPC's
              status symbol for them, UNDEF.

              For  this  reason,  the  actual space readings for UNDEF
              drives  are,  in  SPC,  given  merely  to   assist   the
              intuitions  of  the  user  when  looking at a multidrive
              display.  They are not accurate  measurements  of  CDROM
              drive space.

              Totalling  of  such  drives is stopped by the use of the
              E parameter on the command line.


     SPC's  default  is  to  use  SUBSTed  detection  rather  than DUP
     detection, unless a network or Windows is detected.  The  default
     detection  mode  may  be  overridden  by  the  use  of the S or D
     parameters on the command line.

     The  drive  specified  in the lower right and left corners is the
     value of LASTDRIVE given or assumed in CONFIG.SYS.

     Fuller documentation is obtainable through registration.

     Changes since SPC 6.0

     SPC 6.1
     -------
     Minor bug fix version
     - removes the renaming of PC LAN  to  PC  LAN?   when  MSCDEX  is
       detected  (analysis of other results revealed that erroneous PC
       LAN flags  due  to  operation  under  MS  Windows  rather  than
       MSCDEX).

     - removes   predisplay   computer   hangs  due  to  failure  to
       reinitialise memory  after  loading  the  resident  list,  just
       before loading the drive list.


     ---------------------
     End of documentation