================================================================================
       WRAPPER.SYS :  Ver. 1.0, Copyright (1992) by Philip B. Gardner
       WRAPP86.SYS (8086):  Ver. 1.0, Copyright (1992) by Philip B. Gardner
================================================================================

  WRAPPER.SYS is a device driver which enables the loading of programs in
  the CONFIG.SYS file as devices.  The program may be a Terminate-and-
  Stay Resident utility (TSR) or a program which simply executes but does
  not stay resident.  The driver DEBUGNXT.SYS is a companion to wrapper
  which complements WRAPPER's special support for loading debuggers, like
  MS-DOS's DEBUG.  By loading a debugger in the config.sys, programmers
  may trace and debug the initialization of device drivers.  High memory
  users may load WRAPPER and/or DEBUGNXT into high memory with a device
  loader, or using MS-DOS 5.0's DEVICEHIGH command.

================================================================================

(Requirements)::

        * 186 processor or better (WRAPP86.SYS and DEBUGN86.SYS are
          included to support 8086/8088 processors)
        * Requires MS-DOS Version 3.1 or better

================================================================================

(Installation)::

        (CONFIG.SYS)::

        Install WRAPPER.SYS in your CONFIG.SYS as a DEVICE

        DEVICE=WRAPPER.SYS [options] program.exe (or .com) [program options]

        All switch options and possible messages for WRAPPER are detailed
        below:

================================================================================

(Syntax)::

        The only thing to remember about syntax for the command line is
        that just about anything works.  What this means is that you
        should be able to type in the options on the command line the
        way they make sense to you.

        To illustrate this point, the following command line example
        is mutated several different ways.

        DEVICE=WRAPPER.SYS /R- /P- /M4 MYPROG.EXE
        DEVICE=WRAPPER.SYS -R- -P- -M4 MYPROG.EXE
        DEVICE=WRAPPER.SYS -R--P-M4 MYPROG.EXE

        ... and so on.

(Switch Options)::

        (REPORT)::      R[+ or -]       (toggle:  default +)

        Use /R- to disable messages from WRAPPER.SYS.

        (PAUSE)::       P[+ or -]       (toggle:  default +)

        Use /P+ to enable the pause after the any report messages.

        (NOPAUSE)::     N[+ or -]       (toggle:  default -)

        Use /N+ to never pause after the report, even if there
        are errors.  This switch can be used if your configuration
        generates a warning or error message which you choose to ignore.

        (DEBUGINT)::    D[xx]           (hex value:  default ?)

        Use /Dxx to tell WRAPPER to hook a user interrupt.  This is
        especially useful to ease the use of a debugger like MS-DOS's
        DEBUG.  A user vector is hooked by WRAPPER in the range of
        int 60h - 67h.  The target of the interrupt is the code necessary
        to keep the debugger resident.

           DEVICE=WRAPPER.SYS /C-/D/M32 C:\DEBUG.EXE
           DEVICE=DEBUGNXT.SYS
           DEVICE=MYDEVICE.SYS
 
           (Display at boot-up):

           WRAPPER.SYS :  Ver. 1.0, Copyright (1992) by Philip B. Gardner
                       :  User interrupt 60h hooked

           (Debug's prompt):

           -a 100                               ; assemble at 0100
           1234:0100 int 60                     ; the instruction "int 60"
           -g                                   ; go

           DEBUGNXT.SYS :  Ver. 1.0, Copyright (1992) by Philip B. Gardner

           (Stops at first instruction of MYDEVICE's strategy routine):

           AX=0000 BX=03E6 CX=0000 DX=0000 SP=05A6 BP=0000 SI=0000 DI=0000
           DS=0C96 ES=9087 SS=9087 CS=0C96 IP=0016 NV UP EI PL NZ NA PO NC
           0C96:0016 2E            CS:
           0C96:0017 891E1200      MOV     [0012],BX          CS:0012=0000
           -
 
        When you use /D with no hexadecimal parameter, WRAPPER will search
        for the 1st available interrupt.  You may also specify the interrupt 
        to use (if not in use already),  for example, /D63.  A valid input is
        a hexadecimal number between 60h and 67h.

        (CLOSE HANDLE 0)::      C[+ or -]       (toggle:  default +)

        Use /C- to tell WRAPPER not to close file handle 0 (CON input/output)
        after the specified program or TSR returns.  This is useful for
        programs which expect to write/read to STDOUT/STDIN after CONFIG.SYS.
        MS-DOS normally rearranges the file handles after CONFIG.SYS, so that
        AUX is handle 0.  If the program uses to handle 0 after CONFIG.SYS,
        the input/output will use AUX instead of CON.  This will cause a
        critical error (or interfere with communications), unless this switch
        is used.  MS-DOS's DEBUG is a good example of a program which
        requires this switch, and then only if an INT 03h (Trap interrupt) is
        encountered after CONFIG.SYS.  See the DEBUGINT example above.
        
        (MEMORY LIMIT)::        M[nnn]          (value:  default ?)

        Use /Mnnn to specify the amount of memory to limit a program to use.
        This switch is useful when loading a TSR high, or when loading a
        non-tsr like DEBUG, so that all available memory is not allocated by
        the program.  The value, nnn is in 1 Kbyte units, so /M32 would be
        limit the memory used by the program to 32K.  See the DEBUGINT example
        above.  The default (/M) is to use all memory available.

        *  everything in square brackets "[]" is optional

(CONFIG.SYS Line)::

        DEVICE=WRAPPER.SYS [/Dxx][/C-][/R-][/P+][/N-][/Mnnn]

        device default:  /C+/R+/P-/N-/M?

        *  Don't hook a User Interrupt
        *  Close File Handle 0
        *  Report status messages
        *  Don't Pause after report
        *  Pause on errors or warnings
        *  Use all memory available

================================================================================

(Report Format)::

        WRAPPER.SYS :  Ver. 1.0, Copyright (1992) by Philip B. Gardner
              ERROR :  (Error Messages)
            WARNING :  (Warning Messages)
             ADVICE :  (Advisory Messages)
                    :  (Report Messages)
                    :  (Allocation Status)
              PAUSE :  Press any key to continue... 

================================================================================

(Error Messages)::

        MS-DOS version 3.10 or above is required
        An 80186 processor or better is required
        Bad or missing program specification
        User Interrupts 60h - 67h are in use

================================================================================

(Warning Messages)::

        Unknown option in command line
        Extra characters on command line

================================================================================

(Advisory Messages)::

================================================================================

(Report Messages)::

        User interrupt 00h hooked
        Invalid Parameter for /D 00

================================================================================

(Allocation Status)::

================================================================================

(Changes)::

================================================================================



         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 4,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394