Dirt Cheap Frame Grabber V2.03
                         by Michael Day
                        as of 8 Feb 1992
                          Public Domain

This device is free and released to the public domain. 
If you actually find a use for it, all the more power to ya!

The purpose of the DCFG is to simply provide a very simple method 
to grab video pictures and display them on a computer monitor. 

Version 1.01 of the DCFG only provided 4 levels of gray scale.
Version 2.01 makes a modification which allows for 12 gray scales 
by reading the port four times and interpolating the results.
Version 2.02 fixes a schematic error (DO3 is pin 5, not pin 4).
Version 2.03 fixes the lack of CLDs before doing string instructions.

The DCFG requires at least a 80286 or better and a VGA 
display to run. While it is possible to change the program to 
allow operation on a 8086 and/or a different display, I'm not 
doing it. If you want to, you can. My intent was to just prove 
that it was possible. 

The frame grabber program at this point is very simple, and as a 
result has some problems. The heart of the program relies on a 
very fast IO port to memory instruction. It can operate as fast 
as the computer can shove data from the port to the memory. This 
is as fast as DMAing the data could do.  This method is sensitive 
to computer speed. As such, you may not get a stable picture at 
first. If you don't, use the left or right arrow keys to adjust 
the horizontal sample size. The up/down arrows adjust the 
vertical sample size, but this normally doesn't need to be done. 

You will probably notice some sparkles (pixels shifting left and 
right one pixel position). This is caused by sample jitter and is 
normal. All sampling systems have this problem. Some less than 
others. Even your TV has the problem, but it is normally good 
enough that you don't see it. 

The jitter is caused by the fact that the sampler is not 
perfectly synchronized to the incoming video signal. Your TV has 
a lot of circuitry in it to achieve the synchronization. Being 
that this is a dirt cheap frame grabber, there is only limited 
synchronization of the picture, and no synchronization of the 
sampler. If you want to try to improve on it, please do.

To use the Dirt Cheap Frame Grabber, plug it into a PC printer 
port, and attach the other end to the video output from a VCR or 
TV Monitor and run the program. Use the left or right arrow keys 
to adjust the horizontal sample size to obtain a stable picture.

Do not attach the Dirt Cheap Frame Grabber to the computer with a 
long printer cable. We are dealing with high speed signals here 
(up to 4MHz). It requires as short a connection to the computer 
as you can give it. I built my circuit inside the back shell of 
the connector that plugs into the printer port on the computer.

                    Dirt Cheap Frame Grabber
    (DB25P)                                     
    DO0 ---330ohm-------------*--->|--*-->|---*    IC1 = LM339   
    pin 2                  Vr |  red    1N914 |          quad    
                       (2.4v) |  led          |        comparator
    DO1 ---330ohm-------------*               |                   
    pin 3                     |               |    * = connection    
                             330ohm           |                       
          1N914               |               |    ) = no connect
    DO6 ---|<---*---1Kohm-----* Vc (2.21v)    |       (jump over)
    pin 8                     |               | 
          1N914               |               | Vr = ref voltage  
    DO7 ---|<---*---510ohm----*------*        |      2.4 volts        
    pin 9                     |      |        |                   
                   (trimmer) 5Kohm<--*        | Vc = 00 = 1.65v   
                              |               |      01 = 1.80v   
    DO2 ----------*-----------)------| |------*      10 = 1.95v   
    pin 4         |           |     .1uf      |      11 = 2.21v   
                 3|           |               |                       
    DC3           |/ |6       |               | Vz = 00 = 0.74v   
    (slct)     1 /  -|--------* Vz (1.0v)     |      01 = 0.81v   
    DS6 --------|IC1a|        |               |      10 = 0.88v   
    (ack)        \  +|----*   |               |      11 = 1.00v   
    pins 10,17     \ |7   |  360ohm           |                     
                          |   |               | Vy = 00 = 0.45v   
    DC2            / |4   |   |               |      01 = 0.54v     
    (init)     2 /  -|----)---* Vy (0.66v)    |      10 = 0.59v   
    DS5 --------|IC1b|    |   |               |      11 = 0.66v    
    (pe)         \  +|----*   |               |                   
    pins 12,16     \ |5   |  220ohm           | Vx = 00 = 0.34v   
                          |   |               |      01 = 0.37v        
    DC1            / |10  |   |               |      10 = 0.40v   
    (afd)     13 /  -|----)---* Vx (0.45v)    |      11 = 0.45v   
    DS4 --------|IC1c|    |   |               |                   
    (slct)       \  +|----*   |               | Vs = 00 = 0.086v  
    pins 13,14     \ |11  |  360ohm           |      01 = 0.093v  
                          |   |               |      10 = 0.101v  
    DC0            / |8   |   |               |      11 = 0.115v  
    (stb)     14 /  -|----)---* Vs (0.12v)    |  Assumes Vz set
    DS7 --------|IC1d|    |   |               |  for 1.0v using 
    (busy)       \  +|----*   |               |  5Kohm trimmer 
    pins 11,1   12|\ |9   |  120ohm           |  with DO6, DO7 
                  |       |   |               |  set high.      
    Gnd ----------*-------)---*---------------*------*--------*
    pins                  |   |               |      |        |
    18,19,20,21,          |  100Kohm          |     75ohm     |
    22,23,24,25           |   |      .1uf     |      |        |
                          *---*-------| |-----)------*------o )          
                   2N2222 |                   |             RCA   
            *---------C   E                   |            phono
            |           B                     |            jack 
    pin 5   |           |      1N914          | 
    DO3 ----*--4.7Kohm--*-------->|-----------*

-----------------------------------------------------------------


                         Parts List

    1ea  DB25P connector
    1ea  RCA phono jack
    1ea  5K ohm trimmer pot
    1ea  510 ohm resistor
    1ea  1K ohm resistor
    2ea  330 ohm resistor
    2ea  220 ohm resistor
    2ea  360 ohm resistor
    1ea  120 ohm resistor
    1ea  100K ohm resistor
    1ea  75 ohm resistor
    1ea  4.7K ohm resistor
    2ea  0.1uF capacitor 
    1ea  red LED
    4ea  1N914 diode (or 1N4148)
    1ea  2N2222 transistor (NPN)
    1ea  LM339 quad comparator


-----------------------------------------------------------------


                    Dirt Cheap Frame Grabber
                       Circuit Description                        

It is assumed that the video signal will be a NTSC type signal 
complying to the RS170A video standard with negative going sync 
and a signal level between 0.5Vpp to 2Vpp (1Vpp desired). This is 
the typical signal that is available on the video output jack of 
a VCR or TV monitor. 

If you are using a VCR type video signal, you can get a quick 
start by adjusting the bias trimmer (5Kohm pot) to obtain 
1.0volt at location Vz while insuring that the data output lines 
on the printer port are set to 0FFH. Once you get going you can 
fine tune the reference voltage by adjusting the trimmer to 
obtain the best picture.

The video input comes in on the RCA phono jack. The 75ohm 
resistor provides the proper load for the connection. The .1mf 
capacitor isolates the signal from the rest of the circuit and is 
used as a part of the level shifter to clamp the video input to 
ground reference on the computer. The 1N914 diode and 4.7K ohm 
resistor provides a voltage reference 0.7V above ground for the 
2N2222 clamp transistor. The transistor and diode get their 
supply voltage from the DO3 output pin. Typically this is around 
3.3volts and should have enough power for our needs assuming that 
the output driver is a 74LS374 driver which is the standard part 
for a PC printer port.

The transistor provides a low impedance charge path for the 
capacitor to clamp the sync tip to ground so as to insure the 
video signal sync tip is referenced to ground. The 100K ohm 
resistor provides a high resistance discharge path for the 
capacitor. Enough to provide a discharge path for the capacitor, 
but not enough to seriously affect the video signal level.

The clamped video signal is then applied to all four comparators 
in the LM339. The LM339 gets its power from the DO2 output pin.
Like the clamp transistor, normally there should be enough power 
from the data output pin to supply the IC. A .1mf capacitor is 
used to stabilize the power source. You can probably getaway 
without using the capacitor, but I'm paranoid. 

The four comparators receive their reference voltage from a 
resistor ladder consisting of 360ohm, 220ohm, and 360ohm 
resistors in series with the 120ohm resistor tied to the common 
ground. The voltage level on the 120ohm resistor provides the 
sync detector reference.  The other three resistor positions 
provide three increasing levels of amplitude detection. 

The resistor ladder voltages can be shifted up or down by the 
computer using the DO6 and DO7 data output lines on the printer 
port. This allows 12 gray scale levels to be detected instead of 
the basic 4 levels that would otherwise be available.

The resistor ladder requires a regulated source voltage with an 
adjustment to allow compensation for various input signal levels 
depending on the signal source. The 5Kohm trimmer pot provides 
for the bias adjustment which allows the circuit to be adapted to 
the absolute signal source level. The regulated source voltage is 
derived from the red LED in series with a 1N914 diode. A red LED 
will have a typical voltage drop of about 1.7 volts and the diode 
has a typical voltage drop of 0.7 volts giving a total of 2.4 
volts for the reference. 

The absolute level is not important since the trimmer can 
compensate for minor differences. The LED gets its power through 
the two 330ohm resistors attached to the D0 and D1 outputs. Two 
outputs are used here to insure that there is enough power to 
drive the LED and the resistor ladder while maintaining a 
regulated voltage source across the LED. 

The LED has a 1N914 diode in series with it to get the reference 
voltage in the range that we need it. This is the one area where 
I go beyond spec for the system. The 74LS374 driver is specified 
to have an output voltage of greater than 2.5volts at 2.5ma. I'm 
actually relying on the true output voltage for the part which is 
typically 3.3volts. Should your printer port use a different part 
than the 74LS374, the circuit may or may not work properly. A 
74HTC374 cmos type part will pull up to 5volts. This is not a 
problem, since all we need is 3 volts or better source voltage to 
supply the circuit. If the output device supplies less voltage, 
the circuit will not work because the LED and diode will not be 
able to maintain the required 2.4volt reference source.

The voltage reference is supplied through a 220ohm resistor to 
the bias adjustment trimmer pot. The 220ohm resistor is a load 
source for the 1Kohm and 510ohm gray level shift control 
resistors attached to the DO6 and DO7 data output pins. The gray 
level shift control lines change the reference voltage on the 
resistor ladder to allow the computer to adjust the reference 
voltage to four different levels. This allows us to multiply the 
gray level detection by four by reading in four sequential video 
frames at the four possible reference control levels and 
selecting the highest determined video level from the four frames 
that are collected. This gives us a total of 12 gray levels 
instead of the four levels that would otherwise be available.
The down side to this is that we have to collect four separate 
video frames to do this which means that motion will be blurred.

The comparators receive their pull-ups from the control lines DC0, 
DC1, DC2, and DC3. In a standard printer port these lines are 
open collector outputs with 4.7Kohm pull up resistors. It is 
presumed that this is the case for this circuit. It saves us the 
four pull up resistors. If you feel nervous about this, you can 
attach 4.7Kohm pull up resistors to the comparator outputs and 
attach two each to the remaining DO4 and DO5 output pins (pins 6 
and 7). Note that you should not draw more than 2.5ma from any 
data output pin or the output voltage may sag.

When wiring the circuit, remember that you are working with video 
signals. That means you are working with signals in the RF range 
(up to 4MHz). Keep all wiring as short as possible and the 
components close together. All grounds should be tied to one 
single point at the 25pin connector. The circuit must be built as 
close as possible to the DB25P connector. Do not attach this device 
to the computer with a long cable. The DB25P connector must plug 
directly into the computer to prevent signal loss. Any attaching 
cable should be no more than six inches long (alright, I've gotten 
away with cables as long as three feet, but it isn't recommended). 
If possible, I suggest building the circuit into the back shell of 
the connector so that there is no cable involved.

Remember that we are dealing with high speed signals here. 
Long cables don't work. Failure to keep the connection short will 
cause the sync signal not to be detected and the picture to blur 
or smear. The video cable attached to the RCA jack can be any 
length (within reason) since it is not as sensitive to cable 
length problems. Video cable lengths longer than 20 feet 
may cause problems, I haven't tried them that long.

If you are good at this stuff, it is possible to wire the whole 
circuit inside the connector shell (don't use a shielded shell, 
it will short out the circuitry). It's a very tight fit, but if 
you pick a large shell, and are very careful, it can be all 
stuffed in there. The trimmer pot should be made available for 
easy adjustment (I drilled a hole in the shell for access). 
Also, the led should be visible (another hole to drill) to be 
able to quickly determine if the circuit is working.

To make it all work, simply plug the connector into a printer 
port on the PC, and run the frame grabber program. When running 
the program, the LED should turn on. That indicates that the 
circuit has enough power to operate. If the LED does not come on, 
or it is very dim, there may not be enough power, and you can't 
use that printer port with the circuit. Try another port or a 
different computer. Note that you may see some minor flickering 
on the led when changing the DO6 and DO7 data output lines. This 
is normal and indicates that the circuit is working properly. 

Changing the DO6 and DO7 data output lines causes the current 
flow through the voltage reference ladder to change. This means 
that more or less current will be available to the LED, causing 
it to change in brightness. The LED should not go out completely 
nor become very dim. That would indicate that there is not enough 
power available to drive the voltage reference or a problem in 
your program.

You can operate in the simple mode by outputting a 0FFH to the 
data output port which sets all the output lines high. This 
provides power to the comparators, voltage reference, and clamp 
transistor. It also disables the gray scale control lines. 

To shift the gray scale reference voltage level, send either a 
03FH (gray ref 0), 07FH (gray ref 1), 0BFH (gray ref 2), or 0FFH 
(gray ref 3) to the data output port. 

The resulting detected output from the port is as follows:

    76543210
    1000xxxx  sync
    0000xxxx  level 0 (black)
    0001xxxx  level 1 (dark gray)
    0011xxxx  level 2 (gray)
    0111xxxx  level 3 (white)
    
Note that bits 0-3 are unknown and should not be relied on as 
being valid.

-----------------------------------------------------------------


                       Program Description

This program requires a 286 or better computer. A printer port 
with the attached device described above with a video signal 
driving it. And a MCGA or VGA type display system. You start the 
program up by entering its name at the DOS prompt followed by the 
printer port number you wish to use. 

Examples: DCFG2 1    <-- loads program for use with LPT1.
          DCFG2 2    <-- loads program for use with LPT2.

If you don't give it a number, the program will default to LPT1. 


Grabbing a Frame:

The program works by grabbing samples from the printer port in 
frames. Once each time through the loop, it sucks in a video 
frame from the video input.  

Actually, more than a frame is grabbed. How much is grabbed 
depends on the speed of access to the printer port on your 
computer. On a typical computer this is 1.5us per byte. At the 
1.5us access rate, 63.5us per scan line, and 265.5 scan lines per 
video frame, that results in 11240 bytes per frame required to be 
collected. The collection size is currently set to 20,000 bytes. 
That provides enough space to handle buss speeds up to 12MHz which 
should be adequate for most computers. 

The down side is that we collect 210 extra scan lines on a normal 
computer. In most situations this isn't a problem since three to 
four frames will typically be lost while the collected video data 
is being processed anyway. The extra partial frame has only a
slight effect on the over all collection time and results. The 
effect is minimized on a fast machine since nearly the entire 
array is filled anyway.

The maximum sample size allowed is 65520. More than that and we 
run out of segment space in memory. Also during this period I 
keep the system interrupts off so as to not have distortions of 
the collected data caused by the system deciding to go off and do 
something else.

In addition to the collection time, there is a pre-configure time 
while the loop is waiting for the vertical sync pulse to come in. 
I don't collect any data prior to the vertical sync pulse since 
it would be ignored anyway. 

The vertical sync is determined by watching the sync line. When 
it goes on for longer than 10us, you are in the vertical sync 
time. Less then 10us, and it is a horizontal sync pulse. 

Once the video data is collected, I release the interrupts to 
allow the computer to return to normal operation. Should no sync
come in during the vertical sync detection period, I terminate 
the loop after a while to allow the computer to continue to 
operate, and return an error condition so that the program will 
know that no data was collected. 

If you have an O'scope, you can verify the video collection time 
by observing data output line DO7 (pin 9). This line should never 
go high for longer than 50ms. Typically it should be around 20 to 
40ms in length. This should be the same whether you have a signal 
going into the video line or not. Though there may be a 
difference between the timing when a signal is present verses 
when it is not present.


Video Data Translation:

Once I get the data, I convert it to an intermediate form to be 
stored in the interpretation array. This array keeps the gray 
level values collected on the previous frames. The display 
routine will later interpret the values stored in the 
interpretation array into an absolute gray scale level for each 
display pixel.

The video data is converted by searching for the horizontal sync 
pulse. Once found, we search for the end of the sync pulse. 
Following the end of the sync pulse is the actual video data. 

Each collected byte in the scan line is read and converted to the 
intermediate gray scale level.  There are only four levels 
involved; 00, 01, 10, and 11. Note that since sync is not video 
data, it is not included in the gray scale level. Even if it were 
included, it would be a 00 value. Once converted, the byte is 
then shifted into it's proper frame position in the interpretation 
array byte and stored in the array. 

This is repeated until either the full width of the 
interpretation array is filled, or a new sync pulse is 
encountered. Should a sync pulse be encountered, the rest of the 
interpretation array values are filled with 00. Should the full 
width of the interpretation array be encountered, then the rest 
of the scan line is discarded until an new sync pulse is 
encountered. This sequence is continued until the entire frame 
has been converted.


Displaying the Data:

Once the frame has been converted, the interpretation array is 
then displayed. Each byte is read from the interpretation array 
and translated to an absolute gray level using the translation 
array located in the first 256 bytes of the interpretation array. 
There are 12 levels of gray available, plus black. The 
translation array was copied into the interpretation array at the 
time the interpretation array was created.















The translation array is formed from the following gray level 
conversion chart:

     gray level interpretation chart                       
          frame data                                       
gray    F3  F2  F1  F0   F3 = frame 3, F2 = frame 2        
level:  76  54  32  10   F1 = frame 1, F0 = frame 0        
   12:  11  xx  xx  xx   each group of two bits            
   11: <11  11  xx  xx   represent the video level         
   10: <11 <11  11  xx   for the frame indicated           
    9: <11 <11 <11  11                                     
    8:  10 <11 <11 <11   xx = any bit pattern              
    7: <10  10 <11 <11   <11 = less than 11; (10, 01, 00)  
    6: <10 <10  10 <11   <10 = less than 10; (01 or 00)    
    5: <10 <10 <10  10   11, 10, 01, or 00 = the indicated 
    4:  01 <10 <10 <10                absolute bit pattern 
    3:  00  01 <10 <10                                     
    2:  00  00  01 <10   the gray level for the specified  
    1:  00  00  00  01   bit pattern is shown at the left  
    0:  00  00  00  00                                     

There are no sync bytes in the interpretation array since they 
were stripped out during the process of converting the video data 
to the interpretation data. Note that it takes four video frames 
to completely update the interpretation array. However, the 
actual displayed data will reflect the highest gray level 
determined from the four previous reads. This means that if the 
video level shifts towards the white level, the change on the 
display will be immediate. If the video level moves towards the 
black level, the change on the display will take up to four frame 
grabs to reflect the lower video level for that pixel.  

One big problem is that since the number of scan lines collected 
is much greater than the resolution of pixels collected in each 
scan line, the aspect ratio of the picture would be out of whack 
if we were to display the data pixel for pixel as we received it.
In order to get the aspect ratio back to a reasonable value, we 
must throw data away. We do this by discarding three scan lines 
for every one that we show. If you have a very fast buss, you may 
want to change this to discard two scan lines instead of three 
in order to get a more reasonable aspect ratio.

The other thing I do is to pull a little trick to improve the 
horizontal resolution. Normally there is a typical horizontal 
resolution of about 40 pixels. This is not very much, and it 
would be useful if there were a better resolution. There is a 
halfway solution. 

What I do is display the even pixels on a scan line from the scan 
line that I'm currently processing. I then display the odd pixels 
from the next scan line on the succeeding video frame. What this 
does is to provide a random selection on the odd pixels between 
the normal two sequential scanned pixels that effectively 
improves the display resolution by about 50%. 

The downside is that it worsens the jitter/twinkle problem since 
the odd pixel is developed from a pseudo-random sampling 
mechanism which is not consistent. 

One thing to keep in mind is that the frame grab routine normally 
takes between one and three video frames to collect data, and 
during this time the interrupts are disabled. What that means is 
that if you are operating on a computer which has a clock 
interrupt faster than the normal 55ms, you will lose time, and 
may experience problems. 

Also note that since the interrupts are disabled, anything that 
uses high speed interrupts during the time the video data is 
being collected (such as RS232), will not work. The interrupts 
will be lost.

The main factor that affects speed on slower machines are the 
conversion and display routines. The INS instruction used to 
collect the video data is relatively cpu performance independent. 
The main thing that affects its operation is the buss performance 
of the computer. The faster the buss, the more video pixels that 
can be collected per scan line.

One possible consideration on slower machines would be to discard 
the extra scan lines in the Video to interpretation array 
conversion rather than in the interpretation to display routine. 
That way the extra scan lines would not even be processed, thus 
increasing the speed of the overall process loop. 

---

Future considerations for someone to do if they wish to improve 
on the design would be to improve the synchronization to reduce 
the jitter problem. At this point I don't have any ideas on how 
to improve the problem. 

Another improvement that is possible to do would be to analyze the 
captured video frame to determine the proper values to use for 
capturing the data such as scan line length in pixels, vertical 
sync length, total scan lines, etc. 

A mechanism to increase the size of the displayed picture, and 
maintain the best resolution possible while doing so. 

Save an image to disk or a series of images to make a movie.  
(see update information)

Be able to print a captured image.

Integrate the image with sound.

Add color (that's a tough one).

And of course integrating this stuff into Windows would be nice. 
(I'm working on it.)

That's all folks!
<eof>




         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 4,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.