ROMFNT  1.0 The ROM font loader.         Copyright 1991 Tim Godfrey

Before running this program, read the >>CAUTION<< section below!

This program writes new fonts into the VGA BIOS ROM (which must be already
loaded into shadow RAM). If your motherboard doesn't support shadowing the
video BIOS, then you can't use this program. You will have to enable video
BIOS shadowing in your CMOS setup before ROMFNT can work. The new fonts
will be permanent, and will survive mode changes. (and on some machines,
even a warm boot). This program is not a TSR, and doesn't change anything
in the VGA except the font data and ROM Checksum.

I wrote ROMFNT because I don't like the default "double dot" fonts (which
date back to the CGA and TV set monitors, but are still faithfully copied
by every VGA card). I don't like giving up memory to TSRs unless I have to,
either. ROMFNT will load a set of 'thin' fonts as a default if no font
files are supplied. Other fonts in suitable format are supplied with Tseng
Labs based VGA cards, as well as the Personics Ultravision product.

This program currently supports the following motherboard chipsets:

   Chips and Technologies NEAT chipsets for the 286 and 386. 
   Informtech IT386 motherboard with TI 386 chipset.
   SIS chipset for 386  (85C310).
   ETEQ chipset for 386 (82C491).


           >>>>>>>>>>>>>> CAUTION!<<<<<<<<<<<<<<<<<<<<

In order for this program to do what it does, it has to set bits in very
low level hardware configuration registers of the motherboard chipsets.
There are no standards for these registers between motherboards. I have
written this program to work with motherboards I have access to and could
test on. If your motherboard is different, there is no way to predict what
could happen. Possible side effects could cause a lockup requiring a cold
boot or power off, and in extreme cases, erasing of the CMOS setup
information. Be sure know what's in your CMOS setup before using this
program for the first time. This program does _not_ ever modify the CMOS
data, but strange things can (and do) happen.




Command Line Options:   (options can be flagged with a - or a / character)

-? option: 
         
         Help Screen

-D option: 

         Debug mode: status information is output

-L option: 

         Set lines of text on screen.
         -L25     Puts screen in 25 line mode after loading, with new font
         -L28     Puts screen in 28 line mode after loading, with new font
         -L50     Puts screen in 50 line mode after loading, with new font

         Note: If a -L option is not specified, the new fonts won't take
         effect until the next video mode change.

Filename.ext

         Up to 3 font file names can be supplied on the command line
         The three font formats are 8 line, 14 line and 16 line.
         These files must be in straight binary format, and must include the
         entire 256 character set. 
         
         The size of the file determines what kind of font it contains. IE,
         (file size / 256) = # lines of font. Font files need to be in the
         current directory, ROMFNT's directory, or on the path. 
         
         Example:  ROMFNT thisfont.fnt thatfont.fnt -L50

-H option: 

         Some font file formats include a "header" with some extra bytes
         at the start of the font. (IE: Tseng labs uses a 8 byte header, so
         the parameter would be -H8) the -Hnn parameter, where nn is an
         integer, will ignore the first nn bytes of the the font file. The
         header size will be taken into account in the file size/font size
         computation. (There can be only one -H parameter, so all font
         files must be in the same format).

-X option: 

         ROMFNT has three internal "thin" fonts. Normally, if all 3 font
         sizes are not specified as files on the command line, the default
         fonts are loaded into the unspecified sizes. If the -X option is
         used, the default fonts will not be loaded, and the original fonts
         will remain unchanged. Only the file font(s) will be loaded.

-@xxxx : 

         Chipset specification. ROMFNT is able to detect some chipsets
         who's makers managed to include some sort of ID bits. With all the
         varieties of motherboards in use, there are many ways the chipset
         check could be confused or wrong. It is also possible for just the
         process of checking to lock up machines based on other (unknown)
         chipsets. This parameter bypasses the software check, and directly
         specifies a chipset. Be sure you use the correct one! Note: SIS
         and ETEQ chips MUST be selected with the -@ parameter. 
         
         Currently supported choices are : C&T286 C&T386 INF33 SIS ETEQ