Version 0.62 of WAS.COM
                       Copyright 1990 by Charles Lazo III
                               All Rights Reserved

 WAS is a program that once loaded becomes memory resident.  Thereafter it
 captures lines that scroll off the top of the screen to a scroll back buffer
 kept in expanded memory.  If an attempt is made to reload WAS after it is once
 loaded it will buzz the speaker and state that WAS is already loaded.  Only
 after an improper installation of WAS will you hear this buzzing sound.  If
 the sound is heard at other times--after WAS has been successfully loaded--
 then the sound denotes a bug in the program and WAS will probably not function
 properly after that.

 WAS will display upon a user's screen the content of previous screens/lines
 that have scrolled off the top of the screen.  To perform this action WAS uses
 the Scroll Lock key.  If other software in the system is also using this key,
 then such software and/or WAS may fail to operate properly.  (Note, however,
 the descriptions of the '+' and '-' switches below.)  WAS necessarily requires
 the use of EMS memory.  It should work with EMS versions 3.2 and later, but
 it has only been tested on versions 3.2 and 4.0.  Emulated EMS memory should
 work fine.

 WAS is "Gratisware", that is, software that while copyrighted, may be freely
 distributed.  See the notice at the end of this document for the nature of the
 copyright restrictions.  A disclaimer also applies to WAS.  The author is not
 responsible for any damages that are caused by the use of the program whatever
 their nature.  By using the software you agree to this provision.  Having said
 that there is from the author's point of view, only a slight probability that
 any damage can occur.  A worst case situation would be that WAS may lock up
 the computer when the Scroll Lock key is pressed.  The probability of problems
 will tend to decrease as users of the program report them to the author.

 A few minor problems have been reported with version 0.50 and these hopefully
 have been fixed with this 0.62 version.  Most of the difference between 0.50
 and 0.62 is internal.  Principally this has been the addition of code that
 allows WAS to work with device drivers that extend the keyboard buffer, moving
 to an internal stack when WAS is in the hold state and clearing the prefetch
 queue after each I/O operation.  Three new switches have been added, the "d"
 switch is a kludge fix for a problem that is due to the way in which video
 function 0eh is implemented in the Orchid VGA BIOS that is installed in the
 system on which this version reached its final phase.  The problem was that
 each line in the scroll back buffer was appearing twice.  Hopefully I'll be
 able to auto detect this anomaly in at some point and thereby avoid the use
 of this switch.  Another switch added with version 0.62 is the "v" switch.
 When used after the initial installation this switch will display the version
 number and copyright notice.  Finally, the "e" switch enables the exiting of
 the WAS Scroll Lock hold by pressing the ESCape key.

 To install WAS simply enter the number of EMS pages (16k bytes each) to devote
 to WAS on the command line after the program's name following either letter
 "b" or "B" (no spaces allowed between "b" and the number), e.g., for a 20 page
 (EMS pages) scroll back buffer (320k bytes of EMS memory) simply enter this
 line at the DOS prompt or in a batch file:

                                    WAS b20

 Each EMS page will be enough to save approximately 102 lines of text.  (Part
 of the the memory assigned will be used to save up to 60 lines of the current
 screen for later restoration when WAS leaves the Scroll Lock state.  Thus by
 assigning only a single EMS page to WAS you will have enough space to store
 about two screens of 25-line text in the scroll back buffer.  (See, however,
 the description of the 'l' switch below.)

 Now that you know how to install WAS it might be easier to comprehend what
 follows if you leave whatever editor, file lister, etc. that you happen to
 be using to view this documentation, load WAS and then practice using the
 commands described below while reading the remainder of the documentation.
 (You can install WAS, TYPE this file to the screen, and then view it from the
 WAS scroll back buffer.)  Alternatively, you do not have to read the remainder
 of this file at all; WAS by default loads a command summary into the scroll
 back buffer memory and that may be all you need to get started.  Just install
 WAS, press the SCROLL LOCK key and then the HOME key to read the command
 summary in the scroll back buffer.

 If at some point in time you find the command summary superfluous you can tell
 WAS not to load it by using the 'n' switch on the command line when you run
 WAS, e.g.:

                                    was nb20

 WAS should perform adequately on all types of video hardware:  MDA, CGA, EGA,
 PGC, MCGA, VGA, etc.  Only 80 column text modes are supported.  Any other
 column size will definitely be incompatible with WAS.

 ==============================================================================

                      More about WAS Installation Options

 WAS installation options (command line switches) are symbols placed on the
 command line of WAS which are followed perhaps by numbers or other symbols
 that tell WAS how you want it to be installed.  Switches may be used in small
 case or capitals or any combination of case.  Spaces may be placed on the
 command line separating the invocations of each, but the parameter(s) of a
 switch (if any) must follow the switch without any intervening spaces.  This
 version supports six switches:

 'b' (Buffer size)         Already described.

 'd' (no double lines)     This switch is introduced in version 0.60 to fix
                           a problem that occurs due to the way that at least
                           one instance of the Orchid VGA BIOS implements a
                           a BIOS TTY screen scroll.  Possibly other video
                           BIOSes do something similar producing the same
                           result which is the doubling of lines in the scroll
                           back buffer.  If you have the line doubling problem
                           with WAS then try this switch, otherwise ignore it.
                           An attempt will be made to auto detect the problem
                           and so as to eliminate this switch in the future.

 'e'                       One person responding to my request for feedback
                           mentioned that he would like the ESCape key when
                           pressed to cause WAS to exit the hold state just
                           as the Scroll Lock key is designed to do.  That
                           would be fine on systems that were AT compatible,
                           but using ESCape to exit the hold state on PC or
                           XT systems would cause the scroll lock state (used
                           by WAS to signal a hold condition is desired) to
                           be out of sync with the keyboard status LED for
                           the Scroll Lock key.  So if you are using a PC or
                           XT system and you don't mind the out of sync
                           problem, then go ahead and use the "e" switch if
                           you want ESCape to exit a WAS hold.  YEAH FEEDBACK!

 'l' (maximum Line size)   The 'l' switch uses a number parameter like the 'b'
                           switch.  It sets the maximum number of screen lines
                           that WAS will save for the current (last, bottom,
                           active) screen.  This number must lie between 25 and
                           101 inclusive.  It is the maximum number of screen
                           lines that will ever be displayed on the terminal(s)
                           on which WAS is used.  For example, monochrome and
                           CGA displays typically use no more than 25 lines
                           maximum.  EGA usually is limited to 43 lines, and
                           VGA to 50 or 60 lines maximum.  Default for this
                           parameter (no 'l' switch specified) is 60 lines.
                           Making this number as small as possible will give
                           you additional lines in the scroll back buffer so it
                           should be small; however, WAS will not work properly
                           if it is set too low.  If you are using WAS on a
                           system that can display a large number of lines, but
                           you intend to never use more than a certain number,
                           say 28, then it would be okay to use the 'l' switch
                           to specify 28 lines maximum (and similarly for other
                           values).

 'n' (No command summary)  Include this switch if you do not wish the command
                           summary to be placed in the scroll buffer when WAS
                           is installed.

 's' (annex Summary file)  The 's' switch is used after the WAS source code has
                           been freshly assembled, linked, and exe2bined to
                           form a .com file).  More information about the 's'
                           switch can be obtained by running WAS without this
                           switch after a newly made WAS.COM file is produced
                           by assembling the source code.

 'v' (show version)        After installing WAS the version number (and the
                           same copyright notice that appears at installation)
                           will be displayed.

 '+' (enable WAS)          If you install WAS using the '-' switch all of the
        and                processing it normally does will be disabled until
 '-' (disable WAS)         you run WAS at some later time with the '+' switch.
                           WAS defaults to being active (enabled) and WAS can
                           be run again with either '+' or '-' switch at any
                           time after the initial install to change the enable/
                           disable status.  Disable WAS if you intend to use
                           software that also uses the Scroll Lock key, thereby
                           preventing conflicts.

                           V, +, and - are the only switches that are effective
                           after the initial installation.

 ------------------------------------------------------------------------------

 Examples:

    WAS -n b80             Installs WAS with a scroll back buffer of 1310720
                           = 1280k bytes.  (1310720 = 80 EMS pages).  No
                           command summary is placed in the scroll back buffer
                           and WAS is disabled until at some later time WAS is
                           run with the "+" switch.

    WAS L43 b20            A 20 EMS page buffer is assigned, and it is expected
                           that no more than 43 lines will be displayed during
                           this session.  The command summary is placed at the
                           top of the scroll back buffer.

 ==============================================================================

              Several command keys apply to the operation of WAS

 >>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>><<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<
 *-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*IMPORTANT NOTICE*-*-*-*-*-*-*-*-*-*-*-*-*-*-*-*
 >>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>><<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<

           The *ONLY* time that WAS takes notice of keypress commands
                is after it has placed the system the hold state
                  caused by pressing the Scroll Lock key!!!!!!

 >>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>><<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<

 When the Scroll Lock state is active WAS freezes the computer and sits in a
 holding loop waiting for keypresses that express commands to WAS.  When it
 freezes the system it also hides the cursor.  WAS unfreezes the computer when
 you press the Scroll Lock key again, thereby resetting the Scroll Lock state
 and restoring the cursor to view.  Other memory resident programs can pop up
 over WAS.  Some, such as Turbo Lighting, will refuse to perform their tasks
 when WAS has locked the computer via the Scroll Lock key.  Technically, any
 TSR that traps int 9 should be able to pop up over WAS in the hold state.  No
 response will be made to any command keys when the display is in a graphics
 mode, nor will WAS do any capture of scrolled lines.  It will, however, freeze
 the system in a manner similar to pressing the Pause key (same as the Ctrl-Num
 Lock keypress on non-enhanced keyboards) when the Scroll Lock key is pressed
 even in graphics modes.  The WAS hold routine is probably safer than Pause
 because WAS will not interfere with an interrupt-driven thread.  Following are
 descriptions of actions taken by WAS when the corresponding keys are pressed.

 Scroll Lock               Scroll Lock not only causes WAS to place the machine
                           on hold, but when pressed again will cause the hold
                           state to be removed.  See also the ESCape key
                           command.

 UP ARROW and DOWN ARROW   These keys allow the re-display of lines that have
                           scrolled off the top of the screen.  Pressing UP
                           ARROW scrolls the screen down placing scrolled off
                           lines one at a time on the top line of the screen
                           while moving all others down.  DOWN ARROW performs
                           the reverse action by scrolling the screen up and
                           replacing lines that have been removed from the
                           bottom line when UP ARROW was pressed.

 PgUp and PgDn             They work like the UP ARROW and DOWN ARROW keys
                           respectively, only they scroll the screen by the
                           full amount (the entire number of lines on the
                           screen) for each keypress.

 HOME and END              HOME places the first screen of WAS's scroll buffer
                           on the display and END will display the current
                           application or DOS screen (i.e., no scrolled-off
                           lines are displayed).

 INSERT                    Some application programs write to the screen
                           directly and perform screen scrolling by themselves
                           (instead of using the computer's built-in video BIOS
                           scroll routines).  WAS will not capture the lines
                           scrolled off the top of the screen by these
                           programs; however, if the screen being displayed is
                           the application or DOS screen (displayed by pressing
                           the END key) i.e., nothing is displayed from the WAS
                           scroll buffer, you can press the INSERT key and WAS
                           will capture the current screen in its buffer.

                           Many applications exist that allow the user to make
                           a choice between rapid screen updates and the slower
                           updates available through the video BIOS.  If you
                           find that WAS is not capturing the scrolled lines of
                           a program like this, then the choice of slower
                           scrolling (often implemented to prevent snow on some
                           CGA monitors) may allow the program's scrolled lines
                           to be captured by WAS.

 BACKSPACE                 It may be desired at times to disable the scroll
                           capture of WAS.  You may do that by pressing the
                           BACKSPACE key.  The BACKSPACE key also turns scroll
                           capture back on.  However, the INSERT key will still
                           operate the same way even with scroll capture
                           disabled.  Should you have forgotten whether capture
                           is on or off you can press the Alt key and WAS will
                           flash the capital letter "Y" in the upper left
                           corner of the screen if capture is on, otherwise a
                           capital "N" will flash.  When you let up on the Alt
                           key this signal will be extinguished.

 ESCape                    The Esc key when enabled with the "e" installation
                           option switch will cause the machine to exit a WAS
                           hold state produced by pressing Scroll Lock.  I.e.,
                           either Scroll Lock or Esc will remove a WAS hold.

 KEYPAD PLUS and MINUS     This covers the basic operation of WAS.  Another
                           feature of the program allows you to take text from
                           the scroll back buffer (or even the current screen)
                           and feed it to the keyboard buffer.  That is, the
                           text that you delineate with WAS will be given to
                           the running application or DOS just as if you had
                           typed it in yourself.  The first thing you must do
                           to feed the keyboard buffer from text in the scroll
                           back buffer is to mark it by pressing the KEYPAD
                           PLUS key.  The KEYPAD PLUS key marks text while the
                           KEYPAD MINUS key unmarks it.  A marked area may be
                           moved up or down in the display by first pressing a
                           shift key and then either the UP ARROW or DOWN ARROW
                           key.  The marked area can be resized horizontally by
                           holding down a shift key and then pressing either
                           LEFT or RIGHT ARROW keys.  The LEFT SHIFT key
                           controls resizing of the left side of the marked
                           area and the RIGHT SHIFT key controls resizing of
                           the right side.  Press down a shift key then either
                           LEFT or RIGHT ARROW.  After marking the text merely
                           press the Scroll Lock key to unfreeze the computer
                           and the marked text will be feed to the application
                           or DOS.  Trailing spaces following a line of text
                           will not be feed to the keyboard buffer.  Multiple
                           lines of text are marked by pressing the PLUS key
                           multiple times.

                           If you have marked a large section of text and feed
                           it to the keyboard buffer and then later decide you
                           made a mistake so now you want to stop the avalanche
                           of key feed; don't panic--just press Scroll Lock and
                           the feed will stop.

 DEL                       You can delete text in the scroll back buffer.  All
                           that is necessary is to mark one or more lines as
                           indicated above and then press the DELETE key.  The
                           text will remain marked (nothing will happen) if you
                           mark any of the current (last, bottom) screen.  No
                           warning will sound to indicate that you cannot
                           delete portions of the current screen.

 Enter and Asterisk        It may occasionally be useful to select a location
                           in the scroll buffer that you would like to return
                           to later.  You do that by pressing the RETURN
                           (Enter) key to specify the current location as a
                           place to "return".  When a location has been
                           selected this way, you return to that place by
                           pressing the asterisk (*) key.  (Either asterisk
                           next to the keypad or shift-8 will do.)


                             Files of Version 0.62

                    SPCPAK   C        2768 10-14-90   1:45p
                    SPCPAK   EXE      9023 10-14-90   1:45p
                    SUMMARY  062     10880 10-14-90   1:45p
                    W-DOC062 SUM      4315 10-14-90   1:45p
                    WAS      COM     10731 10-14-90   1:45p
                    WAS062   DOC     23379 10-14-90   1:45p
                    WAS062   ASM    119912 10-14-90   1:45p

         (Note:  Version 0.61 is being distributed with only the COM and
          DOC files.  It is otherwise identical to this version.)


                              Copyright Provisions

 The provisions of the copyright of WAS are that the program, source code, and
 documentation contained in the author's original release (for any particular
 version) may not be altered in any way when distributed and all files
 contained in the author's release must be included in every distributed
 version.  Alterations of the program and/or documentation--including possible
 additional documentation, data files and code--may be included with
 distributed versions of WAS.  There are no other restrictions on the use
 modification, or sale of the WAS software.

 The author may be reached either via CompuServe Mail (User ID 72210,17), the
 US mail or telephone.  All comments and criticisms are appreciated.

                             Charles Lazo III
                             P.O. Box 452
                             Hohenwald, TN 38462
                             Phone:  615/796-2640


 Thanks are due to Russ Ranshaw "Wizard of 10" (CIS User ID 70000,1010) for the
 suggestion of the term "Gratisware" to describe copyrighted software that may
 be freely distributed.  The term "Freeware" has been used to describe software
 of this kind (and other kinds as well); however, "Freeware" belongs to its
 respective copyright holder and should not be used by other individuals or
 organizations to denote software just as readily called Gratisware.

                                   Thanx Russ