OSTSR version 1.1 Copyright 1994 by Jay Clegg

   OSTSR requires OS/2 version 2.1 to run properly. Please read the legal
   disclaimer at the end of this document before using this program. DO NOT
   run OSTSR unless you are running OS/2 2.1, as running it from straight
   DOS will cause the machine to lock up.  It has not been tested with 2.0,
   and I do not know at this time whether it would work with that version.

   OSTSR is an acronym for OS/2 Time Slice Releaser.  It was designed to
   allow programs that are Desqview-aware run smoothly and consume less of
   the system's time when running under OS/2.

   If you are currently using OS2SPEED -or- OS2SPEED combined with TAME21,
   this program offers a speed/size enhancement over the capabilities of
   these two programs.

   OSTSR is, quite simply, a DOS TSR that, when it is run in an OS/2 2.x DOS
   session, will convert Desqview time-slices to OS/2 timeslices
   (technically, DV-PAUSEs are intercepted and converted to DOSSLEEP calls).

   Desqview-aware programs will typically consume FAR less CPU time when
   this program is running. Instead of having a high (up to 100%) CPU
   utilization all the time, OSTSR will cut CPU utilization for most
   DV-aware programs to below 50%, and as low as 0% in some situations. The
   exact amount depends on OSTSR's settings, the speed of the machine, and
   how much work the DV-aware program is doing at any particular time.

   OSTSR works by fooling DV-aware programs into thinking that they are
   running under Desqview.  When such a program makes a request to return
   the rest of its timeslice to Desqview, the call is intercepted by OSTSR
   and is turned into a similar request to OS/2.

   OSTSR has been tested and is known to work very well with the latest
   versions of the following programs:

        Wildcat!    TXZM
        COMMO       DSZ
        Qedit       SHEZ
	List
	SLMR/OLX

   ...and should work with any DV-aware program.  It will be ignored and
   have no effect on non-DV-aware programs.  OSTSR will work in full-screen,
   windowed, and minimized sessions.  OSTSR 1.1 takes only 336 bytes from a
   DOS session, and may be loaded into high memory.

   OSTSR allows the user to specify the amount of time to give back to OS/2
   when a DV-aware program relenquishes it's time slice.  The command line
   option allows settings from 0 to 65535 milliseconds. The actual amount of
   time taken from the application may vary, and is ultimately determined by
   OS/2's scheduler.  While this limits the actual amount of tweeking a
   person can do using this program, it generally insures that things run
   smoothly no matter what option you select.  Experimentation is the key to
   determining what setting is best for your system.  On tests that I and
   others have conducted, a setting of 2 or 3 seems to work best for almost
   any DV-aware program, although you may find a lower or higher setting
   works better for you. Note that a setting of 0 milliseconds does little
   for overall system performance, but should (I haven't been able to
   confirm this) give up the rest of a timeslice *if* another thread is
   running which has a higher priority.

   For starters, try a setting of 3, then go up or down to find what works
   best for you.  If you are running Wildcat! or other DV-aware
   communications programs, try a setting of 2 first, if that causes
   problems, try a setting of 1.

   OSTSR has a "monitor" mode that displays two indicators when a DV-aware
   program is running.  They are very usefull for determining which programs
   are DV-aware, and for gaugeing the impact of OSTSR. When in "monitor"
   mode, the indicators are displayed in the upper left-hand corner of the
   screen or window that it is running in.  The first one is a smiley face,
   which appears when OS/2 has taken from the application via OSTSR.  (i.e.
   when the program gives up it's time slice OSTSR displays the smiley, and
   when OS/2 returns to the program, the smiley is erased.)  The character
   to the right of the is a "twirly-bar" which moves one "notch" every time
   OSTSR returns part of a timeslice to OS/2.

   Generally, the more the smiley is displayed, the better for total system
   performance.

   It should be noted that these indicators will only be displayed if you
   are running a DV-aware program.

   Once you have "tweeked" your system, disable the monitor mode.  The
   monitor mode does impact on performance itself (particularly for dos apps
   that a run in a window), and should only be used for testing purposes.


                                -------

   QuickStart:

        Open a Dos session, either windowed or full-screen (full-screen
        is recomended for testing in monitor mode). Run OSTSR with these
        options:

        OSTSR 2 /m

        This loads OSTSR resident in your DOS session with a 2
        millisecond release setting, with monitor mode ON.

        Now run your Desqview-aware application(s) from this session. If
        they are indeed Desqview-aware, you should see the smiley and
        twirly-bar in the upper left-hand corner of the screen or window,
        indicating that OSTSR is doing it's job.

        (NOTE, if IDLE_SENSITIVITY in the settings folder for your DOS
        session is set to 100%, OSTSR will may not have a positive impact on
        performance. If it is set to 100%, change it to 99% or lower)

        Try running your DV-aware applications in a window, both with and
        without OSTSR loaded, while watching PULSE or another CPU
        utilization monitor.  This will gauge the impact that OSTSR has on
        increasing overall system performance.

                                -------

   Usage:
           OSTSR # [/M] [/D]

    where # is a number between 0 and 65535.  if # is not specified, a
    value of 1 is assumed.  /M and /D are optional.

      /M enables monitor mode.

      /D temporarily disables Desqview emulation. This usually has the
         effect that OSTSR will not seem to be present.  This switch was
         added to allow users to temporarily turn OSTSR 'off'.  OSTSR
         can be turned back 'on' by re-running it without the /D switch.
         Note that if the program requests a time-slice release, it will
         still be sent to OS/2, this simply disables the function that
         'fools' other programs into thinking they are running under
         DesqView. (New switch for version 1.1!)


   Examples:

	OSTSR			    (running OSTSR with no parameters
                                    specifies a default 1 ms DOSSLEEP,
                                    with no indicators.)

	OSTSR 3 		    ( 3 millisecond DOSSLEEP, no
				     indicators)

	OSTSR 2 /m		    ( 2 millisecond DOSSLEEP, with
				     "monitor" indicators turned on)

   Running OSTSR when it is already installed in memory will change the
   values of the already running copy.  This allows you to change its
   settings "on-the-fly".  If you do not specify otherwise, it will
   default to: Monitor Mode OFF, 1 ms release, DV-faking ON.

   You may wish to put OSTSR somewhere in your path so that you can use it
   from any directory.   However, most users will find it easiest to load
   OSTSR via their AUTOEXEC.BAT, so that it will be automatically loaded for
   each DOS session on startup.

				  -------

   OSTSR is copyrighted free-ware, which means you can use it as you see
   fit (free of charge) as long as you do not modify the program in any
   way.  Please do not distribute it without this documentation file.

   I have tested OSTSR to the best of my ability. However, if you find
   any bugs, or programs that cause incompatibilities, I'd appreciate
   hearing about them. I can be contacted at the address below, and also
   through the Wildnet! Programming conference, the FIDO OS/2 DOS support
   conference or via the Madmen & Maniacs BBS (706-860-5781).

			Jay Clegg
			P.O. 204201
			Martinez, GA 30907


				  -------

   Warranty: There is no warranty, period.
   Full Legalese follows:

                                DISCLAIMER

   Jay Clegg makes no warranty, either express or implied, including but not
   limited to implied warranties of merchantability and fitness for a parti-
   cular purpose with respect to this software.

   IN NO EVENT SHALL JAY CLEGG OR ANY OF HIS ASSOCIATES BE LIABLE FOR ANY
   DAMAGES, INCLUDING DAMAGES FOR LOSS OF BUSINESS PROFITS, BUSINESS
   INTERRUPTION, LOSS OF BUSINESS INFORMATION, OR OTHER PECUNIARY LOSS
   ARISING OUT OF THE USE OF OR INABILITY TO USE THIS PROGRAM, EVEN IF
   JAY CLEGG HAS BEEN ADVISED OF THE POSSIBILITY OF DAMAGES.

   Program history: OSTSR

	0.1  This version was written in C and was much larger
	     than the final product.  Just a test program to see if it
	     would work.

	0.8  ASM version with time slice indicator.  Seperated resident
	     code from startup code to squeeze resident size to a
	     minimum.  Allowed for specifying DOSSLEEP parameter.

	0.9  Beta test.  Added TS indicator switch, and allowed for
	     changing parameters of resident program by reruning the program.
	     Fixed a few esoteric buglets.

	1.0  First public release.

        1.1  'Maintenance release'.  Added support for converting MS-Windows
             time slice releases to OS/2 releases. Some programs (SHEZ)
             were calling this instead of the DV call.  Added switch to
             temporarily disable DesqView emulation (/d), when used,
             program will not emulate DV until OSTSR is re-run without
             the switch.  Some programs (Usurper - game door?) were
             trying to use additional DV functions which OSTSR simply
             cannot provide, hence, this allows users to temporarily
             disable OSTSR and re-enable it when a certain program has
             completed.  Refined code so that resident size is still 336
             bytes, despite additions.