*
*  Welcome to use WinTrace, WinTrace is a freeware which you can use it or
*  distribute it to your friends.
*

CONTENTS :
--------------------------------------------------------------------------------

1. Introduction

2. WinTrace Commands

3. Example

4. Feedback



INTRODUCTION :
--------------------------------------------------------------------------------

    WinTrace (WT.EXE) is a general purpose trace utility which allows you to
trap any Windows APIs (DLL functions) under your finger-tips. WinTrace is a
low-level debugging utility which requires users to know how windows API passes
its arguments on the stack and how windows API gets its returned values from
the registers.

    WinTrace is divided in two modes, CONSOLE mode & READY mode. In CONSOLE
mode, WinTrace grabs the control of keyboard and mouse from Windows, only
WinTrace commands can be entered in this mode. To release the control of
keyboard and mouse to Windows, you need to type 'G' command to return to READY
mode.

    CONSOLE mode : Except WinTrace, all other Windows programs are frozen.
                   Only WinTrace commands can be entered at this time.

    READY   mode : Re-activate Windows programs, and WinTrace waits for Windows
                   API trace events.

    The theory behind WinTrace is quite similar to DOS TSR programs, instead of
intercepting DOS/BIOS interrupts, WinTrace intercepts any Windows APIs (or any
DLL functions). The architecture of WinTrace is illustrated below :

********************************************************************************
  WinTrace (READY mode)


  WinTrace (CONSOLE mode, phase 0) <--------- User presses any key to trigger
                                              WinTrace console
    . set trace Windows API functions
    . type 'G' command to return to
      READY mode


  WinTrace (READY mode)

    . wait traced API events

                                              Traced Windows API (...)
                                              {

  WinTrace (CONSOLE mode, phase 1) <---------   call WinTrace console (phase 1)

    . dump traced API stack
    . dump traced API arguments
    . modify traced API arguments
    . type 'G' command             --------->   call original Windows API (...)


  WinTrace (CONSOLE mode, phase 2) ----------   call WinTrace console (phase 2)

    . dump traced API returned registers
    . modify traced API returned registers
    . dump traced API returned stack
    . dump traced API returned arguments
    . modify traced API returned arguments
    . type 'G' command             ---------> }


  WinTrace (READY mode)

    . wait traced API events
********************************************************************************

    There are three phases in WinTrace CONSOLE mode :

      phase 0 : allow user to set/remove traced Windows APIs

      phase 1 : allow user to check/modify the input arguments, before the
                actual Windows API is called.

      phase 2 : allow user to check/modify the returned registers and the
                output arguments, after the actual Windows API is called.




WINTRACE COMMANDS :
--------------------------------------------------------------------------------

** All the numerical input in WinTrace is in "HEX-DECIMAL" format.

** Most of Windows API functions are written in "pascal" calling convention,
   this means the last argument of API function is on the toppest (lowest
   address) trace stack.


(1) '?' or 'H' :
    Help command.

(2) 'G' or 'P' :
    Go or Proceed command, allow user to return to READY mode or traced API
    routine.

(3) 'S' :
    Set trace point command, only available in (CONSOLE mode phase 0).

(4) 'SL' :
     Set trace point List command.

(5) 'S' :
    Remove trace point command, only available in (CONSOLE mode phase 0).

(6) 'T' :
    dump trace sTack command, only available in (CONSOLE mode phase 1 & 2).

(7) 'D' :
    dump Data command.

(8) 'L' :
    dump Length command, the default dump length is 16 bytes.

(9) 'M' :
    Modify data command.

(A) 'X' :
    modify register command, only available in (CONSOLE mode phase 2).

(B) 'V' :
    View trace information, only available in (CONSOLE mode phase 1 & 2).



EXAMPLE :
--------------------------------------------------------------------------------

(A) Execute WinTrace program :

    * Execute WT.EXE in Windows

    * After WinTrace is executed, you will see WinTrace displays the following
      message, and WinTrace is in READY mode.

      Windows Trace Utility X.XX
      (C) Shiuh-Lin Lee
      ready> press any key to activate trace console


(B) Set trace point :

    * Press any key to change WinTrace into (CONSOLE mode phase 0), and you will
      see (phase 0) prompt.

      0>

    * Type 'S' command to set trace point.

      0> S
      dll type (1) module / (2) library :

    * Select the dll type '1'

      0> S
      dll type (1) module / (2) library : 1
      module name   :

    * Enter module name 'USER'

      0> S
      dll type (1) module / (2) library : 1
      module name   : USER
      function name :

    * Enter function name 'SETFOCUS', and you will see (phase 0) prompt again.

      0> S
      dll type (1) module / (2) library : 1
      module name   : USER
      function name : SETFOCUS
      0>


(C) Set another trace points :

    * The same as step (B), you can set another trace point as follow :

      0> S
      dll type (1) module / (2) library : 1
      module name   : GDI
      function name : TEXTOUT
      0>

    * If you have an external DLL library, you can set the trace point as
      follow :

      0> S
      dll type (1) module / (2) library : 2
      library name  : ODBC.DLL
      function name : SQLCONNECT
      0>


(D) Return to READY mode :

    Type 'G' command to return to READY mode.

    0> G
    ready> press any key to activate trace console


(E) Windows API is traced, and before original Windows API is called.

    * Traced Windows API will call WinTrace console, and WinTrace console will
      display (phase 1) prompt.

      [SETFOCUS] traced
      trace stack point (SS/SP) : 17BF/5AD4
      1>

    * Under (phase 1) prompt, you can type the following commands :

      'T' : dump trace stack
      'D' : dump any data pointer
      'L' : change dump length
      'M' : modify any data pointer
      'V' : view trace information

    * Type 'G' to close (phase 1) prompt, and return to traced Windows API.


(F) Windows API is traced, and after original Windows API is called.

    * Traced Windows API will call WinTrace console, and WinTrace console will
      display (phase 2) prompt.

      trace AX/DX : 0000/0000
      2>

    * Under (phase 2) prompt, you can type the following commands :

      'T' : dump trace stack
      'D' : dump any data pointer
      'L' : change dump length
      'M' : modify any data pointer
      'V' : view trace information
      'X' : modify trace registers

    * Type 'G' to close (phase 2) prompt, and return to READY mode.

(G) Close WinTrace program in READY mode




FEEDBACK :
--------------------------------------------------------------------------------

    WinTrace is a very simple Windows programming utility (simple user
interface and functions), but it is absolute free and useful for most Windows
programmers. I hope you will enjoy it, if you have any comments on this
program, please contact me through :


   CompuServe : 74601,2173

   E-Mail     : shiuhlin@wr_fs2.swrcb.ca.gov

   Address    : Shiuh-Lin Lee
                208 Riverbrook Way
                Sacramento, CA 95831
                USA