DESCRIPTION:

þÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄþ
I have designed and am now testing a special cable that allows you to 
transfer to the Game Server and back to the BBS without using passthrough.
As you have figured out with the passthrough you need 8 digiboard ports to
run a 4 node BBS, one port to the modem and one port to the BBS, it gets 
expensive to addon more nodes later.  My cable is rs232 line powered, no
external power supply needed, gets all it's operating power from the modem
DSR line.  It's small, about the size of a matchbox, contains many small
solidstate parts, and works well. I'm trying to locate parts vendors now
and should be able to produce cables in about 8-12 weeks.

One added benefit of these is that you can shut down the Game Server without
shutting down the BBS, it will continue to operate and the custom 'switch'
cables will prevent anyone from switching when the GS is offline.  Can you
say 'neat feature?', sure, I knew you could :)

*** FOR PCBOARD Systems ONLY ***
(Unless APCi or someone writes a 'switch routine DOOR' to access the switch)

Cost for each cable is going to be around $40 ready to plug and go.

Due to the fact that the relay is a custom ordered device with the minimum 
factory order being 50 pieces, the diagram will be of little use without it 
and is no longer being offered.
þÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄþ

THEORY of OPERATION:

Inside this little gem is to almost identical circuits. The custom 4PDT 
(4 pole, double throw) latching relay has two coils, activating one coil 
switches all 4 poles one way activating the other switches all 4 poles back.

All we need to switch is the RS232 signals RD/SD and CTS/RTS, Pins 2,3,4 & 5.
The two circuits consist of a charge pump and two timing configurations.

One timer is set for ~ 5/18ths of a second, the other for ~ 10/18ths of a 
second. They are triggered by the DTR lines coming from the BBS and the 
GameServer.  The BBS DTR normally drops for about one second when PCBoard
hangs up and recycles (~18/18 second or 1 second).  When the switch detects
a DTR  drop, the timers both start, the short timer pulls the modem over to 
the GameServer. The long timer pulls it back to the BBS as both timers expire
under one second. Now here's the trick, to drop DTR from the BBS for a period 
of time greater than the short timer but less than the long timer, see what
happens?  The short timer pulls the modem to the GameServer and we raise DTR
to stop the long time dead before it times out, viola! we have swithed the 
modem to the Game Server, time to play DooM!.  Now when done on the Game 
Server a user just presses 'X' to exit, and the Game Server drops DTR for 
the amount of time set in the Game Server "drop DTR for this long" 
configuration option. Two seconds is a good setting. Now this DTR DOES NOT 
go to the modem, the modem belongs to the BBS and is only on loan to the 
Game Server! The BBS has total control of the modem at all times!.  The Game 
Server DTR line goes only to the switch, and when it drops, it starts those 
timers and as long has DTR stays down for at least one second, the relay goes
CLICK - CLICK and the modem ends up back to the BBS.  

Now the guy in the back has his hand up I see, "what stops the modem from 
hanging up when the BBS drops DTR for 3/18's of a second?"  A very good 
question. Well, there just happens to be an 'S register' to set DTR response 
time in the modem, S25 in all I have checked so far. It defaults to around 
5/100 of a second but can be set from 1/100 of a second to 255/100 of a 
second (2.55 seconds), see what now??  Sure you do, we set this value to 
just over the time that is takes for the long timer to expire, but less than 
the one second that the BBS is going to drop DTR. I have found 80/100 to 
90/100 works, just under one second but longer than the long timer.

When the BBS drops DTR for one second, you should hear CLICK-CLICK and then 
the modem should hang up. The first click is the modem going to the GS, the 
second click is the modem coming back to the BBS and if DTR is still down at 
this time, the modem should time out and hang up.  

It works for me, but not having every brand of modem to test it on, I can't 
promise anything. Each cable is custom made to order, there are not any in 
'stock' to say, if you want one or more to try, order them and i'll build 
them.  It takes about 8 hours to build 4 (Saturday :)  If your not happy
with them, send 'im back. I'm not a hard-ass :)


WizBandit!


Modems tested and known to work:

USR v.32terbo
USR v.34
Hayes Accura 14.4
Hayes Optima v.fc & v.34
þÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄþ