---------- MSI312.HLP ------------ IR Radiometry ---------------      --



     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏ¸
     ³³    Application File     ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     ³³                         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     ³³
     ³³            Minarad Spectrum's Interactive Manual of
     ³³
     ³³             OPTICS, and IR RADIOMETRY Calculations
     ³³                                                                     L 10
     ³³             By Nelson Engborg and Paul Murphy
     ³³
     ³³            Technical Staff, Minarad Spectrum, Inc.
     ³³
     ³³      Application File  Version 3.12    02-01-1995


            (c) Copyright 1994, 1995 Minarad Spectrum, Inc.
            (c) Copyright 1981, 1995 PCSCC, Inc.
                                                                            L 20
                          All rights reserved.

   Read and understand   WARRANTY INFORMATION  . Highlight this line and
   type J to skip to this information.
   Instructions on using help file are at end of file. Type K to read.


ÕÍÍÍÍÍÍÍÍÍÍ¸
³ CONTENTS ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                            L 30
0.00                  Table of Contents

      *    To quickly jump to Sections, position the Section line number
      *    on the ³JUMP³ line (line 12) and type J or type Lxxx (enter)
      *    where xxx is line number. For example, to jump to line 139,
      *    type L139 (ent).  Type S or R to skip back/forth to Sections.

 SECTION                   TITLE                              PAGE³LINE

  0.00 ... Table of Contents ................................... 1    31    L 40
  1.00 ... Introduction ........................................ 3    97
  2.00 ... An Introduction to Calculations Using ............... 4   175
           AstroFormCalc 3.
  3.00 ... MSI Encourages Users to Submit Calculations. ........ 7   287
  4.00 ... Electromagnetic Radiation: The IR Source ............ 7   318
           (Blackbody)


    ------------------------------------------ 0.00 -- Table of Contents ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    2 --


  5.00 ... Calculation of Emitted BB Power in a Specified ...... 9   413
           Spectral Band.
  6.00 ... Behavior of the Aspherical Refraction Surface ...... 11   491
           (Cartesian Ovoid).                                               L 50
  7.00 ... Behavior of the Spherical Refraction Surface ....... 12   516
           (Paraxial Rays).
  8.00 ... Thin Lenses, Lensmaker's Formula, Gaussian ......... 13   582
           Formula and Newtonian Formula.
  9.00 ... Thin lenses, Focal Planes and Lateral or ........... 15   673
           Transverse Magnification.
  10.0 ... Compound Thin Lenses, Effective Focal Lengths ...... 17   741
           and Dioptric Power.
  11.0 ... Thick Lenses, Principal Planes and the Paraxial .... 17   776
           Approximation.                                                   L 60
  12.0 ... Thick Lenses, Design of Relay Lens for an IR ....... 18   802
           Spectrometer.
  13.0 ... Compound Thick Lenses, Principal Planes and ........ 19   850
           Effective Focal Lengths.
  14.0 ... Reflections from Planar, Aspherical and ............ 20   885
           Spherical Mirrors.
  15.0 ... Cassegrain and Gregorian Mirrors. .................. 21   956
  16.0 ... Bar Target Dimensions, Cycles/milliradian, ......... 22  1005
           Collimator FOV.
  17.0 ... Field of View (FOV) of IR Instrument. .............. 24  1061    L 70
  18.0 ... Figure of Merit of an IR System: Noise ............. 26  1157
           Equivalent Power Density (NEPD), Radiance (NEN)
           and Temperature (NETD).
  19.0 ... Calculations for Calibrating a Radiometer for ...... 30  1367
           Transmission.
  20.0 ... In-depth Design of a Spot Radiometer. .............. 33  1498
  21.0 ... In-depth Design of a Remote Sensing IR ............. 35  1566
           Thermometer.
  22.0 ... In-depth Design of a Filter Radiometer for Cloud ... 36  1620
           Viewing.                                                         L 80
  23.0 ... Calculation of Decibel Loss and %Transmittance ..... 42  1916
           of Fibers
  24.0 ... Circumference of an Ellipse: Calculation by ........ 43  1947
           Series and Integration
  25.0 ... About Minarad Spectrum. ............................ 44  2001
  26.0 ... Glossary of Terms .................................. 46  2075
  27.0 ... Product License and Warranty. ...................... 46  2111
  28.0 ... User Support. ...................................... 48  2177
  29.0 ... Order/Registration Form ............................ 48  2202
  30.0 ... Optics and Infrared References. .................... 50  2268    L 90
  31.0 ... Instructions for Manually Installing Package. ...... 51  2319
  32.0 ... Help File: Summary of File Viewing Commands ........ 52  2360


    ------------------------------------------ 0.00 -- Table of Contents ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    3 --



ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ INTRODUCTION  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

1.00          Introduction
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         To change the display colors to high-intensity white on blue      L 100
         type Q when the highlight bar is lighted on the EQU below.


    HWHITE BLUE


         This document is an on-line application file which discusses
         the theory and presents solved problems in Geometrical Optics
         which includes lenses and mirrors and in infrared technology
         (IR) which includes IR sources (blackbodies), fields of view,     L 110
         figure of merits (NEPD, NEN, NET) and other topics..  Excellent
         references, which can serve both as a supplement to an existing
         course in Optics, IR and Radiometry or as stand-alone study or
         self-help guides are listed at the end of this document in the
         REFERENCE section.

         Geometrical optics deals with the behavior of "light" (called
         Vis and closely related radiations like UV and IR in situations
         where the wave nature of the light is negligible.  Radiometry
         deals with the measurement of radiation such as UV, Vis and IR    L 120
         "light", microwaves and (radio frequencies) RF.

         Personal computers (PC's) and their automation and calculation
         capabilities were not available before 1981.  Proper use of the
         PC can reduce or eliminate much of the tedium associated with
         reducing theory into algebraic expressions and then into useful
         day-to-day applications.

         The staff of Minarad Spectrum has written this application to
         provide guidance to both students and professionals who work      L 130
         with Optics and especially infrared (IR) Radiometry.  The
         calculations discussed here can provide help in mastering the
         execution of the necessary algebra and math upon which Optics
         and UV Vis and IR Radiometry is heavily based.  The staff of
         Minarad Spectrum will continue to update this file with new
         discussions and calculations.  All registered users will be
         kept updated about releases of new versions.  The user is
         advised to register for the nominal fee (See below.).


    ----------------------------------------------- 1.00 -- Introduction ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    4 --



         The application is driven by a versatile spreadsheet/calculator   L 140
         call AstroFormulaCalculator 3 which exists as the file
         ACAL3.EXE.  Minarad Spectrum has obtained a distribution
         license for ACAL3.EXE and its on-line helpfile ACAL3HLP.HLP.
         from PCSCC Inc.

         ACAL3.EXE is a compact program that will run on any PC from the
         XT on up and on any DOS version from 2.1 up.  It contains a
         highly structured on-line helpfile with countless interactive
         examples on how to setup calculations.  This program is
         specifically tailored for analysis based on algebraic             L 150
         expressions, formulas or equations.  One of its main functions
         is to eliminate the "programming-type overhead" in working with
         known formulas and to allow meaningful learning to proceed
         rapidly.  It is also a virtually paperless program.  Its many
         and versatile operations can be learned from its highly
         structured on-line helpfile with countless interactive examples
         on how to setup calculations.

         AstroFormCalc 3 can also be used with any traditional outline
         manual or text to develop equation templates that solve           L 160
         specific problems.  For technical support of AstroFormCalc 3,
         the user is required to register for AstroFormCalc 3,
         separately.  See instructions in its on-line helpfile (type key
         F1 from the equations display).

         This file is organized by topics with are summarized in the
         Table of Contents.  The use of AstroFormCalc 3 is discussed in
         the on-line help file which is accessed by typing (F1) from the
         equations display.  This entire file can be searched using the
         auto-search command "A".                                          L 170

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ HOW TO CALCULATE  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

2.00     An Introduction to Calculations Using AstroFormCalc 3.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         This Section provides an introduction to numbers, number
         formats, variables, variable names, mathematical operations,
         equations and related topics.  In general, in order to avoid      L 180
         ambiguities, one must always express numbers, mathematical
         expression and equations in an acceptable way when entering
         them into a computer program.  These requirements lead to the
         formulation of a set of rules which are summarized in the


    ----- 2.00 -- An Introduction to Calculations Using AstroFormCalc 3. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    5 --


         on-line Help File for the ASTRO 3 program.  This help file can
         be reached from the main equation display by typing the (F1)
         key.

         For example:  It is very common to have to evaluate an
         expression which might be written as:                             L 190

                                 456.789 x 0.345

         As written, one would interpret this expression as:  Find the
         product that results from multiplying the decimal 456.789 by
         the decimal 0.345.  Because the letter symbols are most often
         associated with variable names, the use of "x" as a
         mathematical operator for multiplication and the
         equally-acceptable use of "x" as a variable name in an equation
         such as "y=x" would result in confusion for the                   L 200
         expression-interpreter of the program.  As a result, the
         multiplication operator is commonly the "*" symbol and the
         "by-the-rules" way to enter the above expression would be
         456.789 * 0.345 (enter) In the language of "computerese",
         "(enter)" means to type the enter key of the keyboard and
         usually results in some sort of computer action.

         The following examples illustrate some common ways to write
         mathematical expressions and the "by-the-rules" way they are
         entered into the ASTRO 3, and many other, computer programs.      L 210
         These examples exist as equations templates that can be
         "called-up" by scrolling the screen until the highlighted bar
         appears over the appropriate 'EQU line.

         After the templates are loaded, follow the instructions and
         always type (F2) from the main equation display to return to
         this application helpfile immediately after the 'EQU reference.

Topic # 1: ENTERING NUMBERS and EXPRESSIONS
                                                                           L 220
Discussion: The following examples show common representations for
 expressions and the proper way to enter these into this program. These
 expressions can be entered at the ENTER variable below.

    commonly used     ASTRO 3 way     Result          Reason

     24.1 x 56.7       24.1*56.7      1366.47        * means multipl.

          5
          -            5/180          2.77E-2 or    / means division       L 230


    ----- 2.00 -- An Introduction to Calculations Using AstroFormCalc 3. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    6 --


         180                          2.77*10^-2

        6 ù 3 ù 4      6*3*4          72           * not ù for multipl.

        2(-7)5         2*-7*5         -70            implied multipl.
                                                     not allowed.

        25ö5           25/5           5            / is division operat.

                                                                           L 240
         2      5
      14 -  + 8 -  (14+2/7)+(8+5/9)   22.84           express compound
         7      9                                     fractions as sums




                  ð ** If highlighted, type Q to get equations that **
    IRRAWRIT      ð ** solve this problem. Scroll down to highlight.**
                                                                           L 250

Topic # 2: ENTERING EXPONENTS and SQUARE ROOTS

Discussion: The following examples show common representations for
 expressions and the proper way to enter these into this program. These
 expressions can be entered at the ENTER variable below.

    commonly used     ASTRO 3 way     Result          Reason
        ___
       û144         (space) sqr(144)  12         use sqr(..) function      L 260
                                                 to take square root.
        2.3
      10             10^2.3           199.5       ^ means raise to power
               4
      5.67 x 10      5.67e4            56700      e means base 10
          4     3
      3x10 -2x10     3e4-2e3 or        28000      calculation in
                     3*10^4-2*10^3                scientific notation.
          2 -1
     (2x10 )        (2e2)^-1          0.005    no implied exponentiation   L 270

      ___
     û 6
     ------    (space) sqr(6)/(4*sqr(3))   .3535  must match parentheses
     4û3



    ----- 2.00 -- An Introduction to Calculations Using AstroFormCalc 3. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    7 --





                  ð ** If highlighted, type Q to get equations that **    L 280
    IRRAEXPO      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ WANT TO SUBMIT? ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

3.00       MSI Encourages Users to Submit Calculations.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         The on-line manual studies many scientific concepts which when    L 290
         grouped together are commonly called "Optics and IR
         Radiometry".

         This manual is designed for worldwide distribution over the
         "digital superhighway" as shareware.  It is very portable and
         will run on virtually any PC.  It will be uploaded to many BBS
         and online services such as CompuServe, GEnie, ...  It will
         also be included on the ASP CD-ROM and many other engineering
         and scientific CD-ROMS.
                                                                           L 300
         MSI also welcomes users of this file to submit their own
         examples for possible use in future releases.

         All submissions should include equations written in the style
         of the *.EQU files included with this manual.  The many *.EQU
         files can serve as templates.  Also, refer to the
         AstroFormulaCalculator 3 on-line helpfile (F1 key) for detailed
         instructions on entering equations and making calculations.
         Submissions should also include a comprehensive, but concise,
         text for inclusion in this manual.  MSI will give full author     L 310
         credit to all submissions which are accepted for this manual.
         Please submit these items on floppy media to the Minarad
         address in the "About Minarad " section, below.

ÕÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ RADIATION  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

4.00       Electromagnetic Radiation: The IR Source (Blackbody)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                           L 320
         Electromagnetic radiation propagates through space in
         wavefronts of fluctuating magnetic and electric fields.  The


    ------- 4.00 -- Electromagnetic Radiation: The IR Source (Blackbody) ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    8 --


         frequency, or wavelength, of this radiation identifies it as
         radio waves, microwaves, infrared, visible UV and so on.  The
         first equation template identifies the kind of radiation from
         its wavelength or frequency.  Geometrical optics and Radiometry
         is most applicable to radiation in and around the visible (Vis)
         which includes ultra-violet (UV) and infrared (IR) radiations.

Topic # 3: WAVELENGTH, RADIATION TYPE, FREQUENCY                           L 330

Problem # 3.1: Enter wavelength in microns.
 (a) What radiation has a wavelength of 400 nm (400E-3 microns)?
 (b) What radiation has a frequency of 400 THz (400*10^14 Hz)?

                  ð ** If highlighted, type Q to get equations that **
    IRRARAIN      ð ** solve this problem. Scroll down to highlight.**


         An IR source (blackbody) is the "perfect" absorber of all         L 340
         incident electromagnetic radiation.  It is also the "perfect"
         radiator because it is in equilibrium at a fixed temperature
         and so must emit all its incident energy.  However, the
         wavelength distribution of its emitted radiation follows
         Planck's Law, Setfan's Law and Wein's Law.  Emittance is mainly
         in the infrared region and is felt as heat, hence the term
         "blackbody".  Above 600øC objects begin to glow "red" as the
         emitted energy moves into the visible region.  Understanding
         these Laws is fundamental to understanding radiation in
         general.  However, the distribution of illuminance from a         L 350
         visible source rarely shows the IR-source distribution.  For
         example, a tungsten filament heated to 3000 K will show a
         "graybody" Planckian spectral distribution, but only in the
         transmission region of its quartz enclosure.

Topic # 4: RADIATION, POWER EMITTED vs ABSORBED, STEFAN'S LAW, BLACKBODY

Problem # 4.1: A household-type 'radiator' has emissivity of 0.6 and
 area of 2.0 m^2
 (a) At what rate is radiation absorbed by the radiator when the walls     L 360
 of the room are at 27øC?
 (b) At what rate is radiation emitted from the radiator when its
 temperature is 50øC?
 (c) What is the net radiation rate from radiator?

                  ð ** If highlighted, type Q to get equations that **
    IRRA1946      ð ** solve this problem. Scroll down to highlight.**



    ------- 4.00 -- Electromagnetic Radiation: The IR Source (Blackbody) ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------    9 --



         The relative radiance or power in any wavelength interval can     L 370
         be calculated by integrating Planck's equation.  The total
         power is found from Stefan's law which is the closed integral
         of Planck's equation over all wavelengths.  The following
         calculation shows how one estimates the percentage of blackbody
         radiation in any wavelength relative to the maximum
         theoretically possible.

Topic # 5: PLANCK'S LAW, EMISSIVE POWER, RADIATION IN WAVELENGTH
 INTERVAL
                                                                           L 380
Discussion: Calculate the emissive power in the far IR (1000 to 5.
 6microns) middle IR (5.6 to 1.5 micron) and near IR (1.5 to 0.72
 microns) for objects at 1000 and 100 øC.

                  ð ** If highlighted, type Q to get equations that **
    IRRAPLLW      ð ** solve this problem. Scroll down to highlight.**


         Finally, one can estimate the radiation cone of an IR source
         which is its "field of view".  Its FOV is based on a              L 390
         point-source located at the end of its cavity.  The rays are
         limited, or stopped, by its exit aperture.  One half of its FOV
         is its divergence angle.  IR will irradiate anything within the
         cone.  If a plane surface is placed perpendicular to the
         optical axis at a given working distance from the source, it
         will cast a spot on that plane.  Note, atmospheric effects are
         not included.

Topic # 6: SPOT DIAMETER, SIZE, FOCUS AT INFINITY, CONE ANGLE, WORKING
 DISTANCE, IR POINT SOURCE                                                 L 400

Discussion: What is the spot size ( = spot diameter) at a working
 distance of 2 inches from a cylindrical IR source with an aperture
 diameter of 1 inch and a cone angle of 12ø?

                  ð ** If highlighted, type Q to get equations that **
    IRRASFOV      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍ¸                                                             L 410
³ RADIATION  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

5.00 Calculation of Emitted BB Power in a Specified Spectral Band.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


    -- 5.00 -- Calculation of Emitted BB Power in a Specified Spectra... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   10 --



         The following example is included to illustrate a common
         calculation used to estimate the temperature and diameter of a
         BB source (cylindrical-conical cavity).MSI's sales
         representative requested the MSI staff to propose an IR source.
         A customer required a blackbody (BB) IR source that would         L 420
         provide 0.5 W over the 3-5 um band (a popular IR short wave
         band for thermal imaging cameras also sometimes called FLIR's).

         MSI reviewed his request for the BB source.  The MSI staff made
         the following calculations in order to determine the
         appropriate BB temperature to yield the 0.5 W emitted energy.
         MSI used both 1 and 2 inch exit apertures which correspond to
         our RBB-20-1000 and RBB-20-2000 cylindrical conical cavity
         sources.  These IR cavity sources are very good approximations
         to the ideal BB with emissivities greater than 0.98.              L 430

         The results of MSI's calculations are summarized here.  The
         formula template used to calculate these values is presented
         below.

       TøC     Exit H          Lambda       % of       Power   Power
               irradiance      Maximum      SB         W       W
               W/cmý           (um)         max H      1 inch  2 inch
               (3-5um)                                 apert.  apert.
                                                                           L 440
       500     0.6696          3.74         33         3.4     13.6

       400     0.3296          4.30         28         1.7     6.7

       300     0.129           5.05         21         0.65    2.6
                                                       ----
       200     0.0352          6.12         12         0.18    0.71
                                                               ----
         MSI would recommend our RBB-20-1000 at T=300øC or our
         RBB-20-2000 at 200øC.  Both will deliver approximately 0.5 W      L 450
         (See Table above).  The larger source RBB-20-200 offers a
         greater radiation surface of approximately 20 cmý vs 5 cmý for
         the smaller RBB-20-1000 source.

         The calculation template used to estimate the emitted energy in
         the 3-5 um spectral band as a function of BB temperature is
         included below.  Planck's equation is integrated to yield the
         spectral irradiance.  Follow the instructions included with the
         template.
                                                                           L 460


    -- 5.00 -- Calculation of Emitted BB Power in a Specified Spectra... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   11 --



                  ð ** If highlighted, type Q to get equations      **
    IRRASELB.EQU  ð ** discussed above.  Scroll down to highlight.  **


        Other useful calculations of energy in specific bands follow:

Topic # 7: PLANCK'S LAW, EMISSIVE POWER, RADIATION RATIO VS TEMPERATURE

Discussion: Calculate the ratio of emitted power in the 8 - 12 thermal     L 470
 IR band for perfect blackbody radiation at temperatures of 25 and
 100øC.

                  ð ** If highlighted, type Q to get equations that **
    IRRATVSW      ð ** solve this problem. Scroll down to highlight.**


Topic # 8: PLANCK'S LAW, EMISSIVE POWER, RADIATION RATIO, WAVELENGTH
 BAND
                                                                           L 480
Discussion: Calculate the ratio of emitted power in the 4 - 6 micron
 band to that in the 8 - 12 micron band at a temperature of 1000øC.

                  ð ** If highlighted, type Q to get equations that **
    IRRARVSW      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ ASPHERICAL REFRACTION  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                           L 490
6.00       Behavior of the Aspherical Refraction Surface (Cartesian
         Ovoid).
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         The following problem studies the behavior of a spherical wave
         diverging from a point source and impinging on an aspherical
         refracting surface known as a Cartesian Ovoid.  These surfaces
         include the ellipsoid, hyperboloid and paraboloid.

Topic # 9: ASPHERICAL REFRACTING SURFACES, CARTESIAN OVOID                 L 500

Problem # 9.1: Write an expression for the Cartesian ovoid with image
 and object distances of 15 and 12 cm, respectively. Ovoid made of
 glass Ng=1.5 and surrounded by air Na=1.
 (a) Calculate the ray length from ovoid surface to its image if that
 point is 14 cm from the source object.


    -- 6.00 -- Behavior of the Aspherical Refraction Surface (Cartesi... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   12 --


 (b) What does a negative distance mean?

                  ð ** If highlighted, type Q to get equations that **
    IRRA402       ð ** solve this problem. Scroll down to highlight.**    L 510


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ SPHERICAL REFRACTION   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

7.00       Behavior of the Spherical Refraction Surface (Paraxial
         Rays).
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         The basis of most geometrical optics is the spherical             L 520
         refracting surface which is of higher symmetry than its
         aspherical cousins, discussed above.  This higher symmetry
         allows many basic formulas to be derived.  The following
         problems deal with spherical surfaces.

Topic # 10: SPHERICAL REFRACTING SURFACES, PARAXIAL RAYS

Problem # 10.1: The input end of a wide glass (Ng=1.6) fiber is ground
 to a convex hemisphere of 1.5 cm radius.
 (a) If a point source is located 4 cm to the left of the hemisphere's     L 530
 vertex, where will its image be?

                  ð ** If highlighted, type Q to get equations that **
    IRRA405       ð ** solve this problem. Scroll down to highlight.**


Topic # 11: SPHERICAL REFRACTING SURFACES, PARAXIAL RAYS

Problem # 11.1: The input end of a wide glass (Ng=1.6) fiber with
 convex hemisphere of 1.5 cm radius is dipped in water (Nw=1.32).          L 540
 (a) If a point source is located 4 cm to the left of the vertex, where
 will its image be?

                  ð ** If highlighted, type Q to get equations that **
    IRRA406       ð ** solve this problem. Scroll down to highlight.**


Topic # 12: SPHERICAL REFRACTING SURFACES, OBJECT FOCAL LENGTH

Problem # 12.1: An interface separates air on the left and glass (Ng=1.    L 550
 44) on the right.
 (a) What is the object focal length if its radius of curvature is 6


    ----- 7.00 -- Behavior of the Spherical Refraction Surface (Paraxial ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   13 --


 cm?

                  ð ** If highlighted, type Q to get equations that **
    IRRA408       ð ** solve this problem. Scroll down to highlight.**


Topic # 13: SPHERICAL REFRACTING SURFACES, IMAGE FOCAL LENGTH
                                                                           L 560
Problem # 13.1: An interface separates air on the left and glass (Ng=1.
 44) on the right.
 (a) What is the image focal length if its radius of curvature is 6 cm?

                  ð ** If highlighted, type Q to get equations that **
    IRRA408A      ð ** solve this problem. Scroll down to highlight.**


Topic # 14: SPHERICAL REFRACTING SURFACES, OBJECT FOCAL LENGTH
                                                                           L 570
Discussion: What is the radius of curvature of a glass fiber (Ng=1.48)
 required to focus light rays 95 cm in front of its spherical interface
 in a non-aqueous media of isopropanol (Nm=1.38)?

                  ð ** If highlighted, type Q to get equations that **
    IRRA409       ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ THIN LENSES ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ   L 580

8.00       Thin Lenses, Lensmaker's Formula, Gaussian Formula and
         Newtonian Formula.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         The majority of calculations in geometrical optics make two
         basic assumptions:  1) the impinged-upon surface is a sphere
         (spherical approximation) and 2) the impinging light strikes
         that surface at small angles with respect to its optical axis
         (paraxial approximation).  In general practice, however, one      L 590
         usually invokes these formulas for any lens calculation.  The
         following problems deal with "thin" lenses.  Such a lens is
         infinitely thin and all distances are measured from their
         interior principal plane which passes through its center.

         An illustration of a "thin" lens is shown below.  Its center is
         marked by "||".  All distances are measured from it.



    ----- 8.00 -- Thin Lenses, Lensmaker's Formula, Gaussian Formula and ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   14 --


                     ss
                    s  s                                                   L 600
                    s  s                     M[T] + means erect image
  Ë Y[O]           s    s
  ºúúúúúúoúúúúúúúúúsú||úsúúúúúúúúoúúúúúúúúúúo  S source point
  S     F[O]       s    s       F[I]        º  P image point
                    s  s               Y[I] Ê  S[O] Source distance
  |úX[O]ú|úúúfúúúúú s  súúúúúfúúú|úúúúX[I]úú|  S[I] Image distance
                     ss
  |--------S[O]------|-----------S[I]-------|

Sign Convention:  X[O] + means its left of F[O]        focal_length < 0    L 610
                  X[I] + means its right of F[I]           means
           Y[I], Y[O] + means above optical axis        diverging lens.

         The following problems illustrate a number of calculations
         involving thin lenses.

Topic # 15: THIN SPHERICAL LENS EQUATION, LENSMAKER'S FORMULA

Discussion: The source and image points are located 5 and 7 cm,
 respectively, from a spherical concave lens with source radius of -3      L 620
 cm and image radius of 4 cm. What should the index of refraction of
 the glass be?

                  ð ** If highlighted, type Q to get equations that **
    IRRA410       ð ** solve this problem. Scroll down to highlight.**


Topic # 16: THIN SPHERICAL LENS EQUATION, LENSMAKER'S FORMULA

Problem # 16.1: A source is 20 cm from a glass (ng=1.6) convex-plano       L 630
 lens with a radius of curvature of 4 cm. Where is the image located
 (a) when its flat surface faces source and
 (b) when its flat surface is away from source?

                  ð ** If highlighted, type Q to get equations that **
    IRRA411       ð ** solve this problem. Scroll down to highlight.**


Topic # 17: THIN SPHERICAL LENS EQUATION, FOCAL LENGTH vs N[G], N[L]
                                                                           L 640
Discussion: Calculate the focal length of a bi-concave thin lens made
 of glass (Ng=1.6) and immersed in isopropanol (Na=1.35). The source
 radius is -9 and the image radius is 18 cm.



    ----- 8.00 -- Thin Lenses, Lensmaker's Formula, Gaussian Formula and ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   15 --


                  ð ** If highlighted, type Q to get equations that **
    IRRA413       ð ** solve this problem. Scroll down to highlight.**


Topic # 18: LENS EQUATION, FOCAL LENGTH vs INDEX REFRACTION, RADIUS CURV
                                                                           L 650
Problem # 18.1: A bi-concave (R1=-8 cm, R2=12 cm) thin lens is made of
 hepa-fluor (Ng=1.37) and is immersed in solvent alpha-k-1 (Nm=1.77).
 (a) What is its focal length?
 (b) is it converging or diverging?

                  ð ** If highlighted, type Q to get equations that **
    IRRA414       ð ** solve this problem. Scroll down to highlight.**


Topic # 19: MEASURING INDEX REFRACTION in MEDIUM from FOCAL LENGTHS        L 660

Problem # 19.1: A bi-convex lens of index 1.6 has a focal length of 60
 cm in air and 240 cm when immersed in a transparent fluid.
 (a) What is the index of refraction of the transparent fluid?

                  ð ** If highlighted, type Q to get equations that **
    IRRA416       ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸                                                      L 670
³ THIN LENS IMAGING ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

9.00       Thin lenses, Focal Planes and Lateral or Transverse
         Magnification.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         Predicting or estimating the location of an object, also called
         a source or target, and the location of its image are very
         important.  The following problems deal with this topic.
                                                                           L 680
Topic # 20: THIN LENS IMAGERY, CONVEX, TRANSVERSE MAGNIFICATION

Problem # 20.1: A thin bi-convex lens of index 1.6 has equal radii of
 40 cm in air.
 (a) Compute the focal length.
 (b) If the image is to be projected full-size on a white wall, what
 are the image and object distances?

                  ð ** If highlighted, type Q to get equations that **
    IRRA419       ð ** solve this problem. Scroll down to highlight.**    L 690


    -------- 9.00 -- Thin lenses, Focal Planes and Lateral or Transverse ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   16 --




Topic # 21: THIN LENS IMAGERY, CHARACTERISTICS for REAL OBJECTS,
 GAUSSIAN

Problem # 21.1: A 10 cm tall statue of Curly Howard is sitting 100 cm
 from a positive (converging) lens of 30 cm focal length.
 (a) Describe Curly's image.

                  ð ** If highlighted, type Q to get equations that **    L 700
    IRRA420       ð ** solve this problem. Scroll down to highlight.**


Topic # 22: THIN LENS IMAGERY, CHARACTERISTICS for REAL OBJECTS,
 NEWTONIAN

Problem # 22.1: A 9 cm tall statue of Mo Howard is sitting 100 cm from
 a positive (converging) lens of 30 cm focal length.
 (a) Describe Mo's image.
                                                                           L 710
                  ð ** If highlighted, type Q to get equations that **
    IRRA421       ð ** solve this problem. Scroll down to highlight.**


Topic # 23: THIN LENS IMAGERY, MAGNIFICATION, OBJECT, IMAGE DISTANCES

Problem # 23.1: An object positioned 38 inches to the right of a
 positive lens is imaged 8 inches to its left.
 (a) Where will the object appear if its image is moved to 2 inches
 from the lens?                                                            L 720
 (b) Describe it.

                  ð ** If highlighted, type Q to get equations that **
    IRRA423       ð ** solve this problem. Scroll down to highlight.**


Topic # 24: THIN LENS IMAGERY, FIND F from R1, R2, BI-CONVEX, GAUSSIAN

Problem # 24.1: A thin bi-convex glass (N[g]=1.6) with radii of 20 and
 70 cm casts a half-sized image of a plant pot on a white wall.            L 730
 (a) What is its focal length?
 (b) What are the lens to plant and lens to wall distances?

                  ð ** If highlighted, type Q to get equations that **
    IRRA425       ð ** solve this problem. Scroll down to highlight.**



    -------- 9.00 -- Thin lenses, Focal Planes and Lateral or Transverse ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   17 --



ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ COMPOUND THIN LENSES ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                           L 740
10.0       Compound Thin Lenses, Effective Focal Lengths and
         Dioptric Power.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         Lens combinations are very useful.  The following problems deal
         with combinations of "thin" lenses.

Topic # 25: COMPOUND THIN LENSES, MAGNIFICATION, FRONT BACK FOCAL
 LENGTHS
                                                                           L 750
Problem # 25.1: A compound lens consists of two bi-convex lenses of
 focal lengths 15 and 30 cm, respectively, separated by 60 cm.
 (a) Describe the image generated by a statue 10 cm tall placed 12 cm
 in front of the first lens.
 (b) What separation distance is required for unity magnification.

                  ð ** If highlighted, type Q to get equations that **
    IRRA427       ð ** solve this problem. Scroll down to highlight.**

                                                                           L 760
Topic # 26: COMPOUND THIN LENSES, MAGNIFICATION, MICROSCOPE

Problem # 26.1: A low cost microscope is fabricated out of a bottom
 lens of 2 cm focal length, a 10 cm cardboard tube and a top lens with
 a 8 cm focal length.
 (a) Locate the image of an ant 3 cm from the bottom lens.
 (b) Describe the ant.

                  ð ** If highlighted, type Q to get equations that **
    IRRA431       ð ** solve this problem. Scroll down to highlight.**    L 770


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ THICK LENSES ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

11.0 Thick Lenses, Principal Planes and the Paraxial Approximation.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         The basic thin lens formalism and equations can be applied to
         "thick" lenses if effective focal lengths and principal planes    L 780
         (from which distances are measured) are properly defined.  The
         single principal plane of the thin lens is split into two


    -- 11.0 -- Thick Lenses, Principal Planes and the Paraxial Approx... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   18 --


         principal planes H1 and H2 separated by the lens thickness D.
         The next problem deal with this topic.

Topic # 27: THICK LENS, GAUSSIAN FORMULA, PARAXIAL APPROXIMATION

Problem # 27.1: A double convex lens has radii of 6 and 24 cm, a
 thickness of 3 cm and index of 1.6.
 (a) Locate both the principal and focal points and compute the image      L 790
 distance for an object 15 cm in front of V1.
 (b) determine the magnification of the image and
 (c) determine the f.f.l. and b.f.l.

                  ð ** If highlighted, type Q to get equations that **
    IRRA442       ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ THICK LENSES ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ   L 800

12.0 Thick Lenses, Design of Relay Lens for an IR Spectrometer.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         The MSI VIR-20 Vis-SWIR (short-wave Infrared) is a
         comprehensive and versatile spectrometer/spectroradiometer
         which provides a spectral range from 300 to 2500 nm.  It
         contains two miniature Fastie-Ebert grating monochromators.
         The external collectors are fiber light-guide bundles with
         circular apertures at remote-sensing probe interfaces and         L 810
         slit-like apertures at the spectrometer interfaces.  This
         arrangement allows virtually any sensor (transmission cell,
         integrating sphere, immersion probe, reflectance probe, etc.)
         to be interfaced to the VIR-20.  The collected energy (as an
         approximate 4x0.6mm slit-like image) is focused directly on the
         entrance slit of the visible monochromator and is folded, via a
         steering mirror, to the entrance slit of the SWIR
         monochromator.

         For the SWIR channel the image must be transferred over an        L 820
         additional 60 mm path length.  A bi-convex lens is used to
         transfer the energy via 1-to-1 image transfer optics.  The next
         calculation shows how to calculate the proper radius of
         curvature for this lens as a function of the lens center
         thickness, index of refraction and total path length.  The
         actual lens is chosen with an effective focal ratio (f-number)
         lower or "faster" than the system f-number of approximately
         F/3.  For example, an F/1 lens would be 15 mm in diameter if


    -- 12.0 -- Thick Lenses, Design of Relay Lens for an IR Spectrome... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   19 --


         the efl (effective focal length) of the thick lens is about 15
         mm, as it is in the next example.  As always, the calculated      L 830
         radius of curvature and optical layout must allow for some
         adjustment in order to be compatible with the lens
         manufacturer's tooling, assembly and alignment and so on.

Topic # 28: THICK LENS, IR RELAY, BI-CONVEX, IMAGE TRANSFER

Problem # 28.1: A double convex lens is used as a relay lens for image
 transfer across a 60 mm path. CaF2 stock with index of 1.426 at 1.5
 microns is chosen.
 (a) What is the radius of curvature?                                      L 840
 (b) What is its effective focal length?

                  ð ** If highlighted, type Q to get equations that **
    IRRARLAY      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ COMPOUND THICK LENSES ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

13.0       Compound Thick Lenses, Principal Planes and                     L 850
         Effective Focal Lengths.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         As with "thin" lenses, "thick" lenses can also be used in
         combinations.  It should be noted that if the thickness of the
         individual lenses, as measured between their principal planes,
         approaches 0.0, then the solutions are the same as for the
         "thin" lens combinations discussed above.  The following
         problems deals with this topic.
                                                                           L 860
Topic # 29: LENS COMBINATIONS, THICK LENSES, GAUSSIAN FORMULA

Discussion: Two identical bi-convex lenses are separated by 30 mm. Each
 lens has a radius of 50 and 30 mm, a thickness of 20 mm and an index
 of 1.6. Calculate individual and system focal lengths.

                  ð ** If highlighted, type Q to get equations that **
    IRRA443       ð ** solve this problem. Scroll down to highlight.**

                                                                           L 870
Topic # 30: LENS COMBINATIONS, THICK LENSES, GAUSSIAN FORMULA

Discussion: A bi-concave lens (radius=-50 mm, index=1.6) is positioned
 150 mm up a plastic tube in front of a plano-convex lens (radius 50 mm,


    ---------------- 13.0 -- Compound Thick Lenses, Principal Planes and ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   20 --


 index 1.6). Calculate the image location of a 9 mm carpenter ant 90 mm
 in front of the device.

                  ð ** If highlighted, type Q to get equations that **
    IRRA446       ð ** solve this problem. Scroll down to highlight.**
                                                                           L 880

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ MIRRORS     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

14.0       Reflections from Planar, Aspherical and Spherical
         Mirrors.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         Lenses are refracting surfaces and mirrors are reflecting
         surfaces.  There exists a correspondence between the equations    L 890
         that predict the behavior of mirrors and those of lenses if one
         takes into account sign conventions, etc.  A spherical convex
         mirror is shown below.  Mirror surface is represented by 's'.
         The convex mirror has a "virtual" focal point and image.  The
         virtual image lies behind or "in" the mirror between the mirror
         and the focal point.  The concave mirror has both the image and
         object in the "real" domain on the same side of the mirror.  In
         general, image/object distance are considered positive if they
         are "real" and negative if they are virtual.  Thus, the convex
         mirror has one positive and one negative distance while the       L 900
         concave mirror has two positive distances.

               ø
                   ø      s
                      ú oú                   S = source object
               ú  ø    s ø                   V = vertex of sphere
        ú  ø          s   ø P     C          P = image (between F and C)
S úøú ú ú ú ú ú ú ú úoú ú úøo ú ú o          R = 2 * F
|                   V|s     |  úø
|                    | s   ú|ø  R      S[O] = distance S to vertex         L 910
|                    |  sø  |         S[I] = distance vertex to image
|-------S[O]---------|-S[I]-|    C = center of sphere R = radius curvat.

Sign Convention: S[O] + means its left of vertex V,
                 S[I] + means its left of vertex V,
                 R    + means center C is right of V
                      Convex mirror has negative focal length
                      Concave mirror has positive focal length

         The following problems deal with mirrors.                         L 920


    ---------- 14.0 -- Reflections from Planar, Aspherical and Spherical ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   21 --



Topic # 31: SPHERICAL REFRACTING MIRRORS, PARAXIAL RAYS

Problem # 31.1: A convex mirror (17 cm radius) casts the image of a
 bird on a screen 20 cm distant.
 (a) Where is the bird located and
 (b) what will it look like?

                  ð ** If highlighted, type Q to get equations that **
    IRRA460       ð ** solve this problem. Scroll down to highlight.**    L 930


Topic # 32: SPHERICAL REFRACTING MIRRORS, IMAGE vs MAGNIFICATION

Problem # 32.1: A spherical mirror casts an inverted half-sized image
 of an object that is located 110 in from its vertex.
 (a) Where will the image be located?

                  ð ** If highlighted, type Q to get equations that **
    IRRA461       ð ** solve this problem. Scroll down to highlight.**    L 940


Topic # 33: SPHERICAL REFRACTING MIRRORS, IMAGE vs MAGNIFICATION

Problem # 33.1: An eraser 5 cm tall sits 150 cm in front of a concave
 mirror of focal length 400 cm.
 (a) Describe the image.

                  ð ** If highlighted, type Q to get equations that **
    IRRA495       ð ** solve this problem. Scroll down to highlight.**    L 950


ÕÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ CASSEGRAIN ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

15.0       Cassegrain and Gregorian Mirrors.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         Mirror optics offer broadband spectral characteristics and are
         useful as collectors and as transfers in instruments designed     L 960
         for broadband operation such as the Minarad SA-200 and SA-1200
         spectroradiometers.  The Cassegrain and Gregorian are very
         similar.  They both have concave primary mirrors.  The
         Cassegrain has a diverging or convex secondary while the
         Gregorian has a converging or concave secondary.  The
         Cassegrain style with its diverging secondary mirror allows a


    -------------------------- 15.0 -- Cassegrain and Gregorian Mirrors. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   22 --


         longer optical path from the detector to the secondary mirror.
         Thus, it is more accommodating to the radiometer's IR hardware
         such as Minarad's inline blackbody reference cavity, field stop
         and filter/CVF.  Minarad uses the Cassegrain in its SA-200 and    L 970
         SA-1200 spectroradiometers

         The following problems deal with Cassegrain and Gregorian
         mirror systems.

Topic # 34: CASSEGRAIN OPTICS, SPHERICAL THIN MIRRORS, MAGNIFICATION

Discussion: A Cassegrain optic has a large concave mirror of FL=12 in.
 and smaller convex of FL=4 in., respectively, initially separated by
 10 in. Focus the system on a 3 inch tall target 42 inches in front of     L 980
 the primary and describe the image located 2 inches behind the primary
 mirror's hole.

                  ð ** If highlighted, type Q to get equations that **
    IRRACASS      ð ** solve this problem. Scroll down to highlight.**


Topic # 35: GREGORIAN OPTICS, SPHERICAL THIN MIRRORS, MAGNIFICATION

Problem # 35.1: A Gregorian optic has a large concave mirror of FL=12      L 990
 in. and smaller convex of FL=6 in., respectively, initially separated
 by 8 in.
 (a) Focus the system on a 3 inch tall target 42 inches in front of the
 primary and describe the image located 3 inches behind the primary
 mirror's hole.

                  ð ** If highlighted, type Q to get equations that **
    IRRAGREG      ð ** solve this problem. Scroll down to highlight.**

                                                                          L 1000

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ FIELD OF VIEW ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

16.0 Bar Target Dimensions, Cycles/milliradian, Collimator FOV.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         MSI specializes in the design of target projectors (TP).  TP's
         find use in calibration of thermal imaging equipment and in MTF
         (Modulation Transfer Function) instruments.  TP's are            L 1010
         electro-optical devices which consist of a collimator (usually
         an off-axis parabolic mirror type with exit apertures ranging


    -- 16.0 -- Bar Target Dimensions, Cycles/milliradian, Collimator ... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   23 --


         from 5 to 14 inches in diameter).  Aperture and pattern wheels
         position various masks at the collimator's focal point.  Masks
         are illuminated by an IR source (blackbody) which projects the
         mask's pattern from the collimator to the unit under test
         (UUT).  MSI supplies complete TP systems including collimator,
         aperture/target wheels, IR sources and optics table.  For
         example, the MSI TP-5-30 system would have a collimator with a
         5 inch off axis parabolic mirror and 2x2 inch square targets.    L 1020

         Aperture targets are usually illuminated with circular BB's
         such as the MSI RBB-20-1000 1 inch cylindrical-conical source
         with operating temperatures from 50 to 1000øC.  2x2 or 4x4 inch
         masks are more commonly illuminated with square radiation-plate
         sources such as the MSI RBB-30 series (heat only) or the RBB-40
         series (thermoelectric heat/cool varieties).

         Very often one must calculate the dimensions of the bar
         targets, also called Nyquist targets, used to measure spatial    L 1030
         properties of optics such as the minimum detectable and
         resolvable temperature difference (MDTD and MRTD).  It should
         be noted that a "bar target" with one bar is more commonly
         called a "slit" target if it has a high aspect ratio or called
         a uniform-illumination target if it has an aspect ratio near
         unity.  The spatial frequency of bar patterns is also closely
         related to the spacing of pixels in focal plane array (FPA)
         detectors.

         The calculation, included below, allows one to calculate the     L 1040
         total dimensions of each bar target (usually with 4 bars) as a
         function of the spatial frequency in cycles/milliradian.  In
         addition, the minimum FOV (field of view) at the collimator's
         exit aperture is also calculated.  If the actual FOV is less
         than this value, the projected pattern will be clipped.

Topic # 36: TARGET DIMENSIONS, TARGET PROJECTOR, COLLIMATOR, FOCAL
 LENGTH, SPATIAL FREQUENCY, MILLIRADIANS, N BAR PATTERN (N=4, TYPICAL)

Discussion: Calculate dimensions of a 4-bar Nyquist target with 7/1       L 1050
 aspect ratio and freq of 0.53 cycles/milliradian. Targets are to be
 placed at the focal point of a 70 inch collimator.

                  ð ** If highlighted, type Q to get equations that **
    IRRABARC      ð ** solve this problem. Scroll down to highlight.**



    -- 16.0 -- Bar Target Dimensions, Cycles/milliradian, Collimator ... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   24 --


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ FIELD OF VIEW ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                          L 1060
17.0       Field of View (FOV) of IR Instrument.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


         What an IR instrument "sees" is usually characterized by its
         field of view, FOV.  The FOV is twice its acceptance angle.  If
         an IR detector is located at the focal point of an optical
         system containing a single converging (convex lens), the
         illustration, below, can be used to identify terminology:
                                                                          L 1070
 FOV/2 is 1/2 of FIELD OF VIEW
      ³ ù   <----- FOV/2                    or ACCEPTANCE ANGLE
      ³......ø.....ù
    S ³            |    ø     ù          |
    P ³    OPTIC-->|              ø      |<-- DETECTOR
    O ³            |          ù   ø      |
    T ³...... .... ù ø Detector at focal point of
      ³ ù    ø                                 optical system.
      |---WORK_DIS-|--------S[DET]-------|
                   |---------FL----------|                                L 1080

         Detector:  The IR detector's diameter, if circular, or the
                    length of its sides, if square or rectangular.
         S[DET]:  Distance from the center of the lens to the detector.
         OPTIC:   Diameter of the lens  FL:  The focal length of lens
         WORK_DIS:  the distance from the center of the lens to a plane,
         perpendicular to the optical axis and containing an image of
         the detector called its "spot".
         SPOT: The diameter of the image of the detector at WORK_DIS.
         FOV: Field of view in degrees, Acceptance angle is FOV/2         L 1090

         The shape of the spot is assumed to be the same as that of the
         detector.  A circular detector has a circular spot (and the
         same FOV in all directions perpendicular to the optical axis).
         A rectangular one has a rectangular spot (and two FOV's), a
         square detector has a square spot (but only one FOV).

         If the detector is a perfect point, then the systems FOV is 0ø.
         For any sized detector, a collimating location exists, measured
         from the lens, at S[DET] = FL + F# * DIAM_DET.  For example, a   L 1100
         1 mm detector in an F/2 system will have a 0ø FOV if the
         detector is located 2 mm from the focal point.  A negative FOV
         implies that the detector's image is focussed in front of the
         lens.


    ---------------------- 17.0 -- Field of View (FOV) of IR Instrument. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   25 --



         The following equations can be used to calculate FOV's working
         distances, spot sizes and F# for any simple system with a
         detector at an arbitrary location behind the lens.

Topic # 37: FOV OPTICAL SYSTEM, DETECTOR VS DISTANCE FROM LENS            L 1110

Problem # 37.1:
 (a) Calculate the FOV of a radiometer with a 0.3 inch lens, a 0.6 inch
 FL and a 4 mm detector 8 mm behind its focal point.
 (b) What is the spot diameter at 400 inches in front of the lens?

                  ð ** If highlighted, type Q to get equations that **
    IRRAFDET      ð ** solve this problem. Scroll down to highlight.**

                                                                          L 1120
         The next set of equations can be used to make system
         calculations when the detector is located at the optical focal
         point, a very common location in IR systems.

Topic # 38: FOV OPTICAL SYSTEM, DETECTOR AT FOCAL POINT

Problem # 38.1:
 (a) Calculate the FOV of a radiometer with a 0.3 inch F/2 lens and a 4
 mm detector at its focal point.
 (b) What is the spot diameter at 4 inches in front of the lens?          L 1130

                  ð ** If highlighted, type Q to get equations that **
    IRRAFFOC      ð ** solve this problem. Scroll down to highlight.**


         The FOV (or acceptance or divergence angle) and lens diameter
         can be measured experimentally by measuring the spot diameter
         vs.  the working distance and using linear regression.  The
         following example illustrates this procedure.
                                                                          L 1140
Topic # 39: SPOT DIAMETER vs WORKING DISTANCE, FOV, DIAMETER OPTIC,
 LINEAR REGRESSION

Discussion: A quality department wants to measure its laser's
 divergence angle (FOV/2) and its exit aperture by measuring the spot
 diameter vs working distance and using linear regression. If data are
 (11 mm, 10 ft), (23,20), (49, 50) and (95.1, 100), what are the FOV
 and aperture diameter?

                  ð ** If highlighted, type Q to get equations that **   L 1150


    ---------------------- 17.0 -- Field of View (FOV) of IR Instrument. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   26 --


    IRRASVSW      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ FIGURE OF MERIT ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

18.0       Figure of Merit of an IR System: Noise Equivalent Power
         Density (NEPD), Radiance (NEN) and Temperature (NETD).
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                          L 1160
         The performance of an IR instrument depends on many factors.
         Some of the more important are:  field of view (FOV), usually
         from 1 mrad to 20ø, spectral bandwidth typically from 1.3 to 2
         % of its nominal wavelength if a CVF is used, detector type,
         such as InSb, MCT or a sandwich combination of these, and
         electrical bandwidth (from 1 to 20 KHz or wider, depending on
         the acquisition rate).  Performance is usually evaluated in two
         different ways depending upon whether the target fills the
         detector field of view or whether the target is essentially a
         point source within the detector field.                          L 1170

         At least three useful figures of merit are available for
         evaluating an IR instrument's ability to sense target radiation
         above its electrical noise.  1) The noise equivalent power
         density (NEPD) which characterizes its ability to detect a
         target (essentially a point-source) that does not fill the
         detector field of view.  2) The noise equivalent radiance (NEN)
         which indicates the instrument's ability to detect a target
         that fills the instrument's FOV.  3) The noise equivalent
         temperature (NET) which is the smallest different in target      L 1180
         temperature that can be detected.


         Definitions of calculated and supplied parameters follow:

         PEAK_WAVE - The wavelength of maximum spectral radiance as
         predicted by the Wein Displacement Law.

         FOV[MRAD] - The field of view (FOV) in milliradians.  Usually
         the FOV is express in degrees if FOV>0.5ø and in mrad if         L 1190
         FOV<0.5ø.

         W_R[STER] - The solid angle subtended by the FOV.  The FOV is
         the apex angle of a plane bisecting the FOV cone.  For a FOV
         that can be approximated as a right-circular cone, the solid
         angle is equal to 2*pi*(1-cos(FOV/2)) or pi*tan(FOV/2)^2.


    -- 18.0 -- Figure of Merit of an IR System: Noise Equivalent Powe... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   27 --



         NEP[W] - The noise equivalent power in Watts at the detector.
         NEP is calculated from the detector D* (dee-star) at the
         specified wavelength, the detector area DT_AREA in mm and the    L 1200
         detector bandwidth DT_BW in Hz.

                    NEP= sqr(DT_AREA*DT_BW)/D_STAR.

         NEP[W] is used to supply "the noise" in most figure of merit
         calculations.

         NEPD[W] - The noise equivalent power density at the entrance of
         the collecting optic in Wattsöcmý.  The NEPD (also sometimes
         called the noise equivalent irradiance or NEI) is the target     L 1210
         energy density required to equal the detector noise scaled to
         its energy density at the entrance of the collecting optic.
         With NEPD, the instrument achieves a signal-to-noise ratio of
         1.  The smaller the NEPD, the better the performance of the IR
         instrument.  NEPD is derived from a point source target which
         does not fill the instruments field of view and is always
         measured above the background irradiance.

         NEN[W] - The noise equivalent radiance at the entrance of the
         collecting optic in Wattsöcmýöster.  The NEN is the target       L 1220
         radiance required to equal the detector noise scaled to its
         equivalent radiance at the entrance of the collecting optic.
         With NEN, the instrument achieves a signal-to-noise ratio of 1.
         The smaller the NEN, the better the performance of the IR
         instrument.  NEN is always derived from a target that fills the
         instrument FOV.

         N_EFF - the effective radiance at the entrance to the
         collecting optics for a blackbody target at temperature TEMP[C]
         and in the specified spectral bandwidth SP_BW[HZ]                L 1230

         WET[W] - The power at the detector equivalent to N-EFF.

         S_N - the system signal-to-noise ratio.  Calculated for a
         blackbody target filling its FOV.  It is calculated from the
         ratio of the target power at the detector WET to the noise
         equivalent power NEP.

         NETD[C] - The blackbody temperature difference (always at a
         specific temperature TEMP[C]) equal to the detector/electronic   L 1240
         system noise.  NETD is directly related to the system's NEN and
         the filter region/spectral bandwidth of the filter used in the


    -- 18.0 -- Figure of Merit of an IR System: Noise Equivalent Powe... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   28 --


         system.  NETD = NEN / (dNEN/dT at TEMP[C]).


         The following parameters are known for the instrument's
         intended design.

         CL_A[CMý] - The net collecting area in cmý of the entrance
         optic reduced for any obscuration such as from the secondary     L 1250
         mirror of the Cassegrain collector.

         DT_A[MMý] - The area of the detector in square mm.

         DT_BW[HZ] - The electrical bandwidth of the system in Hz.

         D-STAR - The detector detectivity in cm sqr(Hz)/Watt.  Usually
         supplied with the detector specifications.

         FOV[ø] - The instruments FOV in degrees.  Generally, based on    L 1260
         the limiting aperture which may be the detector or a field
         stop.

         OPTEFF - The optical efficiency of the instrument.  The product
         of the individual efficiencies of collecting optics, filters,
         transfer optics and demodulating circuits.

         SP_BW[U] - The spectral bandwidth in microns(U).  (Usually the
         width of the 50% transmission or power points relative to the
         center of the filter.)                                           L 1270

         TEMP[C] - The target temperature in øC.  The target is always
         assumed to be a blackbody, a perfect emitter.

         WVLNG[u] - The spectral wavelength in microns.  The center of
         the filter band.

         An equation template that calculates NEPD, NEN, S_N and NET for
         a blackbody target that fills the instrument FOV follows.
                                                                          L 1280

                  ð ** If highlighted, type Q to get equations      **
    IRRASENS.EQU  ð ** discussed above.  Scroll down to highlight.  **


         For an instrument with an InSb detector at 77K and CVF spectral
         selector with 2% nominal resolution, use this template:



    -- 18.0 -- Figure of Merit of an IR System: Noise Equivalent Powe... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   29 --


Topic # 40: INFINITY FOCUS, FULL FOV, FIGURE OF MERIT, INSB DET(77K),
 2% CVF                                                                   L 1290

Discussion: Calculate NEPD, NEN and NET for an InSb, CVF radiometer
 with the following: Detector area 1 sq mm, det bandwidth 1 Hz, optical
 efficiency of 0.06, collecting area of 120 sq cm, FOV of 2.5 mr,
 target temperature of 90øC at wavelengths of 1, 3 and 5 microns.

                  ð ** If highlighted, type Q to get equations that **
    IRRAINSB      ð ** solve this problem. Scroll down to highlight.**

                                                                          L 1300
         For an instrument with an MCT (HCT, Mercury Cadmium Telluride,
         mercad) detector at 77K and CVF spectral selector with 2%
         nominal resolution, use this template:

Topic # 41: INFINITY FOCUS, FULL FOV, FIGURE OF MERIT, MCT DET(77K), 2%
 CVF

Discussion: Calculate NEPD, NEN and NET for an MCT, CVF radiometer with
 the following: Detector area 1 sq mm, det bandwidth 1 Hz, optical
 efficiency of 0.06, collecting area of 120 sq cm, FOV of 2.5 mr,         L 1310
 target temperature of 90øC at wavelengths of 6, 12 and 14 microns.

                  ð ** If highlighted, type Q to get equations that **
    IRRAMCT       ð ** solve this problem. Scroll down to highlight.**


         A plot of estimated signal-to-noise vs wavelength for a Minarad
         Spectrum SA-1200 narrow FOV (2.5 mr), CVF radiometer with a 6
         inch Cassegrain collector and MCT detector is shown below.
                                                                          L 1320



    -- 18.0 -- Figure of Merit of an IR System: Noise Equivalent Powe... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   30 --


 1658-                                                        k
     |         Signal to noise vs. wavelength              k
     |         MSI SA-1200 Radiometer                   k     k
     |         6 inch Cassegrain Collector          k           k
     |         MCT (77K) detector                k              k
 1243-         2.5 mr FOV                      k
     |                                       k                    k
     |                                     k                      k       L 1330
     |                                   k
     |                                  k                           k
 829.-                                k                             k
     |                              k                                 k

     |                             k
     |                            k                                   k
     |                          k
 414.-                        k
     |                       k
     |                     k                                              L 1340
     |                   k
     |                k
+0.00-k k   k   k  k
     ||--------------|--------------|--------------|--------------|-----
      1             4.0            7.0            10.0           13.0
                                wavelength (microns)


         To plot this spectral response use the following template.
         Type comma first to read the comment for instructions.           L 1350

Topic # 42: INFINITY FOCUS, FULL FOV, FIGURE OF MERIT, MCT DET(77K), 2%
 CVF, PLOT SIGNAL to NOISE VS WAVELENGTH

Discussion: Plot the signal-to-noise for an MCT, CVF radiometer with
 the following: Detector area 1 sq mm, det bandwidth 1 Hz, optical
 efficiency of 0.06, collecting area of 120 sq cm, FOV of 2.5 mr,
 target temperature of 90øC from 1 to 14.9 microns.

                  ð ** If highlighted, type Q to get equations that **   L 1360
    IRRAPSN       ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ RADIOMETER TRANSMISSIONÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

19.0 Calculations for Calibrating a Radiometer for Transmission.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         All values are nominal values.  All equation values are:         L 1370
         wavelength (lambda), microns or U; distances, in, mm, cm and m;
         and Neff (effective radiance in the pass band); watts/
         cmý-ster.  Where a spectral selecting CVF (continuously
         variable filter) is defined, the bandwidth is approximately 2%
         of instantaneous Lambda peak response.

         When atmospheric transmission measurements are desired over a
         known measured distance, it has been established that a
         radiometer and matching size off-axis collimator when placed in
         contact, and in perfect alignment, allow generation of a zero    L 1380


    -- 19.0 -- Calculations for Calibrating a Radiometer for Transmis... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   31 --


         absorbtion Lambda-wavelength transmission file.  This is only
         true when the value of irradiance H from the collimator in
         contact with the radiometer is the same as the value received
         from the collimator placed at the desired operating distance.

         It is very useful to simulate long path distances in the
         laboratory by stopping down the collimator exit aperture such
         that the radiometer can be placed directly in front of the
         collimator.  In order to properly calibrate the radiometer, one
         must adjust the collimator exit irradiance H by substituting an  L 1390
         accurately measured aperture of the correct size to generate
         the correct zero-distance value of H.

         Formula: H = Neff * A0/(FL+D)^2 = Neff * A1/FL^2

         H is the irradiance.  A0 is the exit area of the collimator and
         radiometer and D is the desired distance.  A1 is the area of
         the aperture after stopping and FL is the collimator focal
         length.  The effective target radiance, Neff, is constant at
         both zero and desired distances.  Note :  FL << D approximation  L 1400
         made.

         The following template calculates the stopping diameter of the
         aperture.  Note: A Minarad Spectrum C-6-32 collimator has a 6
         inch exit aperture and a 32 inch focal length.  For energy
         measurements, it typically includes a MSI RBB-20-1000 1 inch
         (50 to 1000øC) blackbody as its illuminant.

Topic # 43: TRANSMISSION, COLLIMATOR, SOURCE, APERTURE-EQUIVALENT
 IRRADIANCE                                                               L 1410

Discussion: What diameter must the exit aperture of a MSI C-6-32
 collimator be stopped down to in order for its irradiance H at zero
 distance to be identical to its irradiance at 4 kilometers (without
 stopping) as collected by a identical-diameter radiometer (neglect
 atmospheric absorbtion effects)?

                  ð ** If highlighted, type Q to get equations that **
    IRRADIAH      ð ** solve this problem. Scroll down to highlight.**
                                                                          L 1420

         The next problem illustrates how the figure of merit of the
         collecting radiometer can be estimated when it is at zero
         distance in the laboratory rather that at 4 kilometers in the
         field.  These calculations can be used to test the practicality
         of attempting to collect energy from the collimator at 4


    -- 19.0 -- Calculations for Calibrating a Radiometer for Transmis... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   32 --


         kilometers.  The S/N ratio should be 100 or greater if the
         experiment is to be practical.

         Assume:                                                          L 1430

         A Minarad Spectrum C-6-32 6 inch Collimator with an RBB-20-1000
         IR source with 1 inch clear opening operating at 1000øC ( an
         effective radiance value of 4.390E-2), Lambda peak at 5.0
         microns.  CVF bandwidth 2% of peak bandwidth).  Collimator
         irradiance H from previous example is 5.003e-11 (See equation
         template below).

         A Minarad Spectrum SA-1200 6 inch diameter spectral radiometer
         with the following specifications:                               L 1440

         Collecting area A0 in cmý: 120
         FOV (field of view): 5 milliradians
         Filter CVF spectral range: 1.8-5.5 microns
         Detector 1x1 =1 mmý InSb D* (dee star): 2.0E11
         Electrical bandwidth: 10 Hz

         System Thruput Analysis:
         (Mirrors 0.95 reflectance) ^4 * (CVF transmission 0.4) *
         (Synchronous demodulation factor 0.315) *                        L 1450
         (Detector lens transmission 0.7)
         --yield-->  0.0718 system transmission.

         Using the 6 inch MSI C-6-32 collimator previously described we
         find the following:

         (N.E.P.) = (Det area cm2 * bw in hz)^1/2
                    -------------------------      = 1.58E-12
                             D*
                                                                          L 1460
         (N.E.P.D.) =         N.E.P.
                      ---------------------   =   1.835E-13
                       A0 * System thruput


         S./N. Ratio =  H value at the radiometer    5.003E-11
                       --------------------------  = --------- = 272.6
                               N.E.P.D.              1.835E-13

         The above problem assumes zero transmission losses at 5.0 mic.   L 1470
         In reality transmission losses occur even in the IR
         transmission bands depending upon concentration of absorbing


    -- 19.0 -- Calculations for Calibrating a Radiometer for Transmis... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   33 --


         materials.  These calculations strongly suggest that if the
         radiometer is positioned next to the collimator with the proper
         stopped-down aperture (See previous example.), the radiometer
         should be able to "see" the target in the lab and also in the
         field when the radiometer is positioned 4 kilometers away from
         the collimator without the stop.

         The template which contains a generalized form of this           L 1480
         calculation appears next.

Topic # 44: RADIOMETER, SIGNAL-TO_NOISE, COLLIMATOR, SOURCE, IRRADIANCE,
 RADIANCE, NEP, NEPD

Discussion: What signal-to-noise is expected for a Minarad Spectrum
 SA-1200 6 inch diameter spectroradiometer with an InSb detector and
 CVF spectral selector collecting energy at 5 microns from a 6 inch
 collimator source at a distance of 4 kilometers?
                                                                          L 1490
                  ð ** If highlighted, type Q to get equations that **
    IRRASNEP      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ SPOT RADIOMETER DESIGNÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

20.0       In-depth Design of a Spot Radiometer.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                          L 1500
         Most radiometers are focussed at infinity.  Some applications
         required the radiometer to be focussed up close.  For example,
         We might require a 8 mm spot at working distance of 200 mm.
         The spectral region is lambda peak 7.9 microns, bandwidth 0.5
         micron with minimum target temperature of 200 øC.  Electrical
         bandwidth is 10 Hz.  A Minarad Spectrum spot radiometer or
         remote-sensing thermometer has the following specifications:

         Optic Collecting Diameter= 1.0 inch (25.4 mm).  Spot size:
         (Note:  the spot size is defined as the half-power FOV * 3 or,   L 1510
         in this case, 8.0 mm/3) = 2.666 mm FOV size.  Detector:  pyro
         1x1 mm, D* (dee star)= 2E8.  effective target radiance Neff:
         lambda 7.9, bw 0.5 at 200 øC = 4.2111E-3

         Defining lens FL (focal length) as

         FOV / obj distance   =  det size / img distance



    ---------------------- 20.0 -- In-depth Design of a Spot Radiometer. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   34 --


         Solving this proportion equation for img distance yields 75 mm.
         The lens focal length:  1/f = 1/obj + 1/img = 55mm .             L 1520

         In practice we would use a 50 mm standard lens (F/2) and
         readjust the detector to lens distance for best focus at 200 mm
         target distance.

         The power appearing at the detector is included in the solid
         angle At/d^2 with respect to the FOV diameter.  Area of the
         target (At)= 5.58E-2 cmý/ distanceý= 400 cmý yields target
         solid angle of 1.395E-4 ster.  The radiometer lens collecting
         area (Ac) is 5.064 cmý Power at the detector is                  L 1530

         P = Ac * solid angle * Neff.

         Power = 5.064 * 1.395E-4 * 4.211E-3  = 2.9748E-6

         System thruput efficiency = lens transmission * filter
         transmission * synchronous demodulator factor.  Efficiency =
         0.9 * .8 * .315 = 0.2268

         (N.E.P.) = (area of detector in cmý * bw in hz)^1/2              L 1540
                    ---------------------------------       = 6.972E-9
                     ( detector D_star * thruput efficiency)

         S/N = Power/N.E.P.  = 426, a very reasonable signal to noise
         ratio.

         The template which contains a generalized form of this
         calculation appears next.

Topic # 45: SPOT RADIOMETER, FOV, DETECTOR SIZE, OBJECT, IMAGE, SIGNAL-   L 1550
 TO_NOISE, NEP

Problem # 45.1:
 (a) What focal length (1 inch dia. biconvex lens) and detector image
 distance are required to produce an 8 mm spot at 200 mm.
 (b) What signal- to-noise is expected for a 200øC target using a pyro
 detector at 7.9 mics, spectral BW 0.5 mics and electrical BW of 10 Hz?

                  ð ** If highlighted, type Q to get equations that **
    IRRASPRD      ð ** solve this problem. Scroll down to highlight.**   L 1560



    ---------------------- 20.0 -- In-depth Design of a Spot Radiometer. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   35 --



ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ IR THERMOMETER DESIGNÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

21.0       In-depth Design of a Remote Sensing IR Thermometer.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         A radiometer is to be calibrated as a remote-sensing
         thermometer.  We require a full field of view of 1.146 degrees   L 1570
         (20 mrad).  Spectral band of lambda 1.8 - 3.0 microns (peak
         lambda=2.4 mic, BW=1.2 mic).  Electrical bandwidth 20 Hz.
         Minimum detectable temperature 60øC, Neff (1.8 - 3.0) =
         2.70E-6.

         The Minarad Spectrum industrial temperature measuring
         instrument such as RST-20 remote sensing thermometer has the
         following specifications.

         Lens (Water free Quartz), 1.0 inch diameter, FL 50 mm.  Filter   L 1580
         coated Germanium LP.  Germanium cuts on at 1.8 mic.  and the
         detector cutoff is approximately 3.0 microns.  Detector is 1.0
         x 1.0 mm single stage cooled PbS, 20% bias.  Power on a PbS or
         PbSe detector is approximately 1mw/mm-sq Electrical BW = 20 Hz.

         Power at the detector = Ao * instrument solid angle * Neff

         Power = 5.06 * 2*PI*SIN(20E-3/2)ý * 8.7107E-7 = 8.6E-9

         System thruput = lens transmission * filter * synchronous        L 1590
         modulator.  Efficiency = .9 * .85 * .315 = 0.2409

         (N.E.P.)= (area of detector cm * bw (electrical))^1/2
                   --------------------------------------   = 4.64E-11
                       ( D_star    * thruput efficiency )

         S_N = P / N.E.P. = 185. This value suggests 60øC is near the
         minimum useful temperature (S_N=100) of this instrument.

         The template which contains a generalized form of this           L 1600
         calculation appears next.  The example in this template
         actually shows how one can estimate the minimum detectable
         temperature of an IR thermometer if one knows something about
         how it was built.

Topic # 46: REMOTE SENSING THERMOMETER/ RADIOMETER, FOV, DETECTOR SIZE,
 SIGNAL-TO_NOISE, MINIMUM DETECTABLE TEMP

Discussion: What is the minimum detectable temperature for a PbS IR
 thermometer with a 1.146ø FOV and 1.8 to 3.0 microns spectral range, 1   L 1610


    -------- 21.0 -- In-depth Design of a Remote Sensing IR Thermometer. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   36 --


 inch collector and 20 Hz electrical BW?

                  ð ** If highlighted, type Q to get equations that **
    IRRARST1      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ ADVANCED RADIOMETER DESIGNÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

22.0 In-depth Design of a Filter Radiometer for Cloud Viewing.            L 1620
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         Minarad Spectrum's (MSI) is pleased to submit informal
         specifications for a spectral radiometer for temperature
         measurements of small areas such as clouds in cold regions of
         the sky.

         The MSI staff has thoroughly investigated the possibility of
         using uncooled detectors, such as pyroelectric.  We have also
         looked into the use of our standard 6-inch SA-1000 filter        L 1630
         radiometer with 120 cm of collecting area and have found it
         would still require a field size of at least 6 milliradians to
         insure adequate NETD (noise equivalent temperature difference).
         We are providing two sets of procurement specifications.  The
         first procurement specification utilizes an uncooled selected
         D* PYROELECTRIC detector and our standard 6-inch SA-1000
         radiometer system.  The second procurement specification
         utilizes a liquid-nitrogen-cooled MCT detector with our
         standard 4-inch SA-1000 radiometer system.
                                                                          L 1640
***********************************************************************
      Specification for PYROELECTRIC detector and 6 inch optic system:
***********************************************************************

         a) The radiometer system shall utilize a 6-inch diameter
         Cassegrain mirror with a 120 cm collecting area.

         b) All optics utilized in the system shall be mirrors, where
         possible, to insure lowest system losses.
                                                                          L 1650
         c) The system shall utilize a temperature-stabilized (45øC)
         PYROELECTRIC detector of selected D* 3.0e8.

         d) A heated BB reference (45øC) shall be used to provide a
         stable reference and, through proper phase switching, allow
         heated blackbodies to be utilized for calibration testing.


    -- 22.0 -- In-depth Design of a Filter Radiometer for Cloud Viewi... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   37 --



         e) The field of view shall be of a precision mask (user
         changeable).  Two masks shall be supplied:  2.5 mr
         (milliradian), and 6.0 mr.                                       L 1660

         f) The sights shall consist of one rifle scope for quick
         alignment, and one manually operated through the optics sight.

         g) The instrument's field of view shall be described by the
         limits of the field where the signal level falls to 50% of the
         peak signal (mid-field) when scanned by a modulated source.
         The instrument's chopper is stopped in the open position during
         the field profile scanning.  The aperture size used on the
         source shall be a compromise between field resolution and S/N.   L 1670
         The source aperture shall be as small as possible in
         combination with source temperature to achieve a mid-field peak
         signal level of minimum 200/1.

         h) The instrument's actual FOV shall be desired value +/- 10%.
         The instrument's field flatness shall be at least 90% of the
         peak response over 80% of the FOV.

         i) The electrical bandwidth shall be variable in two steps ,
         1Hz, and 3 Hz.                                                   L 1680

         j) The electronics and data processing unit shall be an IBM
         type compatible computer, with 486 cpu, 8 megs of onboard
         memory, a hard disk with a capacity of 250 megabytes and a 1.44
         meg 3.5-inch floppy disk, keyboard, and mouse.  The monitor
         shall be a VGA 14-inch color monitor.

         k) The electronics shall use RS-232 or RS-422 serial link for
         control and data communications between radiometer head and
         electronics unit.                                                L 1690

         l) The electronics shall be capable of displaying the
         radiometer data in øC over a range from -90 to +10 øC.  The
         electronics shall be capable of logging temperature data to the
         hard disk at user-selected time intervals.

         m) The complete radiometer system shall have an NETD of 1 øC or
         less in the 3 Hz bandwidth.  Stability of the radiometer over
         the environmental temperature range shall be less than +/- 0.1
         øC.  The system shall reach maximum stability within 30 minutes  L 1700
         after startup.



    -- 22.0 -- In-depth Design of a Filter Radiometer for Cloud Viewi... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   38 --


         n) The interconnecting cable between radiometer head and
         electronics shall be 15 feet in length.

         o) The instruction manual shall contain all appropriate
         operation, set-up, and calibration procedures, as well as block
         diagrams and schematics.  Care and cleaning procedure for the
         mirror optics shall be included.  The FOV plots vertical and
         horizontal, as well the measured net in each electrical          L 1710
         bandwidth.

         p) The system shall be capable of proper operation while the
         power line voltage is within 110-125 volts, frequency 58-62 Hz.

         q) The computer shall run under a Windows environment using
         Visual Basic and/or Visual C++ as the operating program.

         r) The system shall be delivered with a warranty agreement
         covering parts and labor for a period of 12 months.  The         L 1720
         warranty period shall start at the time of delivery, providing
         the system meets the specifications.  The buyer shall have two
         weeks to test and evaluate system performance.  If, during the
         warranty period, the system fails or ceases to meet
         specifications, the user shall notify Minarad Spectrum by FAX
         or writing, effectively stopping the warranty clock.  Once the
         unit is returned to the buyer and buyer rechecks the system
         operation, they shall notify Minarad by FAX or mail, thus
         restarting the warranty clock.
                                                                          L 1730
         Minarad is not responsible for buyer's gross abuse, negligence,
         and/or mishandling.  The warranty shall cover normal wear and
         tear, and shipping and handling.

**************** PYRO detector Sensitivity Worksheet********************

         The following calculations were used to estimate the S/N
         (signal-to-noise ratio) of this system.  In general, only
         theoretical designs with S/N's greater than 100 have been shown
         to result in functional systems.                                 L 1740

         System:  MSI SA-1000 Filter Radiometer with PYRO

         Temp(øC):  -90

         Filter Wavelength (microns):  10.8 filter

         Spectral Bandwidth (microns):  1.5


    -- 22.0 -- In-depth Design of a Filter Radiometer for Cloud Viewi... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   39 --



         FOV (milliradians):  6.0                                         L 1750

         Detector Area (sq mm):  1

         Electrical Bandwidth (Hz):  3

         Optics:  6 inch Cassegrain

         Net Collecting Area (cm):  120

         Total Optical efficiency:  0.14                                  L 1760

         ***** derived values *****

         Peak Wavelength (microns):  15.8

         Solid angle W_R steradians:  2.8e-5

         NEP noise equivalent power in Watts:  5.77e-10

         NEPD noise equivalent power density in Watts/cmý:  3.44e-11      L 1770

         NEN noise equivalent radiance in Watts/cmý-ster:  1.22e-6

         N_EFF effective irradiance in Watts/cmý-ster:  8.44e-5

         WET equivalent power at detector in Watts:  4.00e-8

         S/N signal-to-noise ratio:  69

         NETD noise equivalent temperature difference øC: 0.314           L 1780

         Note:  the S/N is 69 and less than 100.  This theoretical
         design is likely to be realized in our SA-1000 Filter
         Radiometer but performance may be marginal.  The equations and
         calculations used to derive these values can be reviewed by
         recalling the following template.


                  ð ** If highlighted, type Q to get equations      **
    IRRACLPY.EQU  ð ** discussed above.  Scroll down to highlight.  **   L 1790


***********************************************************************
Informal Specifications for a liquid-nitrogen-cooled MCT 4-inch


    -- 22.0 -- In-depth Design of a Filter Radiometer for Cloud Viewi... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   40 --


             Cassegrain-mirror radiometer system:
***********************************************************************

         Note:  omitted letters imply specifications identical to those
         of the PYROELECTRIC system described above.
                                                                          L 1800
         a) The radiometer system shall utilize a 4-inch diameter
         Cassegrain mirror with a 45 cm collecting area.

         c) The system shall utilize a liquid-nitrogen-cooled MCT
         detector of a minimum D* of 2.0e10.  The detector shall have a
         minimum hold-time of 8 hours after initial fill and top off.

         e) The field of view shall be of a precision mask (user
         changeable).  Two masks shall be supplied:  2.5 mr and 5.0 mr.
                                                                          L 1810
         i) The electrical bandwidth shall be variable in three steps
         1Hz, 3Hz, 10Hz.

         l) The electronics shall be capable of displaying the
         radiometer data in øC over a range from -90 to +10 C.  The
         electronics shall be capable of logging temperature data to the
         hard disk at user-selected time intervals.

         m) The complete radiometer system shall have an NET of .08 ø C
         or less in the 3 Hz bandwidth (2.5mr FOV).  Stability of the     L 1820
         radiometer over the environmental temperature range shall be
         less than +/-0.1 ø C.  The system shall reach maximum stability
         within 30 minutes after start-up.

******************* MCT detector Sensitivity Worksheet******************

         The following calculations were used to estimate the S/N
         (signal-to-noise ratio) of this system.  In general, only
         theoretical designs with S/N's greater than 100 have been shown
         to result in functional systems.                                 L 1830

       System:  MSI SA-1000 Filter Radiometer with MCT (cooled at 77K)

       Temp(øC):  -90

       Filter Wavelength (microns):  10.8 filter

       Spectral Bandwidth (microns):  1.5

       FOV (milliradians):  2.5                                           L 1840


    -- 22.0 -- In-depth Design of a Filter Radiometer for Cloud Viewi... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   41 --



       Detector Area (sq mm):  1

       Electrical Bandwidth (Hz):  3

       Optics:  4 inch Cassegrain

       Net Collecting Area (cm):  45

       Total Optical efficiency:  0.14                                    L 1850

       ***** derived values *****

       Peak Wavelength (microns):  15.8

       Solid angle W_R steradians:  4.9e-6

       NEP noise equivalent power in Watts:  8.66e-12

       NEPD noise equivalent power density in Watts/cmý:  1.37e-12        L 1860

       NEN noise equivalent radiance in Watts/cmý-ster:  2.81e-7

       N_EFF effective irradiance in Watts/cmý-ster:  8.44e-5

       WET equivalent power at detector in Watts:  2.60e-9

       S/N signal-to-noise ratio:  300

       NETD noise equivalent temperature difference øC:  7.29e-2          L 1870

         Note:  the S/N is greater than 100.  This theoretical design is
         likely to be successfully realized in our SA-1000 Filter
         radiometer.  The equations and calculations used to derive
         these values can be reviewed by recalling the following
         template.


                  ð ** If highlighted, type Q to get equations      **
    IRRACLMC.EQU  ð ** discussed above.  Scroll down to highlight.  **   L 1880


***********************************************************************
              Additional Comments and explanations:
***********************************************************************



    -- 22.0 -- In-depth Design of a Filter Radiometer for Cloud Viewi... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   42 --


         1) A precision in-line heated reference source provides a great
         many improvements in system performance, such as (a) absolute
         reference value vs.  target radiance, (b) the increased S/N
         when sky temperatures are close to the ambient temperature, and  L 1890
         (c) the ability as in d) above to switch synchronization
         polarity and use absolute values of bb references of hotter
         than internal reference temperature for calibration or
         calibration check.

         2) The software we provide includes Visual Basic source code,
         if applicable, running in a Windows environment.  The source
         code is licensed by Minarad to the model number and serial
         number of the instrument.  Having access to the source code
         allows the user to modify the Minarad programs as they wish.     L 1900

         3) A table of hotter than reference black body temperature vs.
         equivalent cold temperature will be provided to you with the
         instrument.

         4) Although Minarad has chosen a temperature range we feel will
         work for you, please feel free to suggest the temperature range
         or ranges you desire, as well as alternate FOV precision field
         stop masks.
                                                                          L 1910
         We look forward to your comments on our specifications.

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ FIBER OPTICS ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

23.0       Calculation of Decibel Loss and %Transmittance of Fibers
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         The MSI VIR-20 spectrometer/spectroradiometer uses fiber light
         guides to couple energy from sensors to its internal             L 1920
         monochromators.  The VIR-20 has two independent channels:  a
         sample or main channel and a reference or auxiliary channel.
         The VIR-20's spectral range covers 300 to 2500 nm.  For this
         range UV-enhanced water-free quartz fibers are chosen.  For
         longer wavelengths, HMFG (heavy metal fluoride glass) and
         chalcogenide fibers are appropriate.  The calculations
         presented below are useful for estimating the transmittance
         factor for a short fiber length.  The transmittance factor is
         then included in the overall system throughput factor used to
         estimate S/N (signal-to-noise).                                  L 1930

Topic # 47: FIBER OPTICS, LOSS DB/KM, %TRANSMITTANCE/METER


    -- 23.0 -- Calculation of Decibel Loss and %Transmittance of Fibe... ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   43 --



Problem # 47.1:
 (a) Calculate a fiber's loss in decibels per kilometer LOSS_DB_KM
 given a percent transmittance per meter T_%_MTR of 97 and
 (b) the percent transmission per meter if the LOSS_DB_KM is 100.
 (c) What are the DB loss and % transmittance for a 4 meter length?

                  ð ** If highlighted, type Q to get equations that **   L 1940
    IRRAFIBL      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ SERIES and INTEGRATION ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

24.0       Circumference of an Ellipse: Calculation by Series and
         Integration
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                          L 1950
         Calculations involving integration and summation of formulas
         are relevant to all math-based theories.  The following
         examples illustrate these methods.

         The circumference of an ellipse with axes lengths of "a" and
         "b" as measured from its origin cannot be expressed in a simple
         "closed" form by a formula.  The approximate value is
         calculated as:

                l ÷ 2 * pi * sqr( (a^2 + b^2)/2 )                         L 1960

         Thus if a = 50 and b = 10, the circumference, l ÷ 226.5.  The
         circumference can be express "exactly" by use of the elliptic
         integral of the second kind E(k,è):

                l = 4 * a * E(k,è)   k= sqr( abs(a^2-b^2) )/a

         There are at least two methods to obtain a higher degree of
         accuracy:  the first is to use a series expansion for E(k,è)
         and the second is to numerically integrate E(k,è).  The          L 1970
         following two examples show how AstroFormCalc 3 can be used to
         sum up a series or to accurately integrate an equation.  The
         methods are very general and are applicable to many problems in
         Optics as well as virtually all other disciplines.  It should
         be noted that the "approximation" formula, given above, is only
         accurate to about 8%.

Topic # 48: SERIES, ARC LENGTH (CIRCUMFERENCE) OF ELLIPSE


    ----- 24.0 -- Circumference of an Ellipse: Calculation by Series and ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   44 --



Discussion: Estimate the circumference of an ellipse with axes lengths    L 1980
 of 50 and 10 cm as measured from its origin. Use the series
 approximation.

                  ð ** If highlighted, type Q to get equations that **
    IRRAELSE      ð ** solve this problem. Scroll down to highlight.**


Topic # 49: INTEGRATION, ARC LENGTH (CIRCUMFERENCE) OF ELLIPSE

Discussion: Estimate the circumference of an ellipse with axes lengths    L 1990
 of 50 and 10 cm as measured from its origin. Use the elliptic integral
 method.

                  ð ** If highlighted, type Q to get equations that **
    IRRAELIN      ð ** solve this problem. Scroll down to highlight.**


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ MINARAD SPECTRUM INFO ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                          L 2000
25.0         About Minarad Spectrum.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         As a matter of background, Minarad Spectrum designs and
         manufactures a complete line of electro-optical products
         including:

         Radiometers, spectroradiometers, Vis/IR spectrometers, IR
         thermometers and IR sources (blackbodies).
                                                                          L 2010
              Radiometers measure absolute radiance or irradiance
              relative to their internal reference blackbody over an
              entire wavelength interval.  Spectroradiometers perform
              the same functions but at many discrete wavelengths across
              a spectral interval.  IR spectrometers usually measure the
              transmittance and absorbance of the target relative to a
              reference over many discrete wavelengths.  IR thermometers
              actually measure radiance but display the equivalent
              blackbody temperature.
                                                                          L 2020
         IR sources (blackbodies), heat-only and thermoelectric, conical
         cavity and extended area, absolute and differential modes,

              The IR source or blackbody emits a spectral radiance


    ------------------------------------ 25.0 -- About Minarad Spectrum. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   45 --


              distribution which closely approximates that predicted by
              Planck's function.  It is the primary reference for most
              IR work.

         IR test sets, collimators, target wheels, target projectors and
         targets/masks,                                                   L 2030

              IR test sets usually consist of an IR source with an
              aperture wheel or variable slit, and optionally a filter
              wheel, optical modulator (chopper) and possibly a shutter.
              A collimator (off-axis parabolic mirror style) is used to
              project parallel IR energy with a FOV which depends on the
              widths of target masks located in its focal plane. A
              target projector consists of an IR test set, target wheel,
              collimator and a series of apertures/targets/masks located
              in its focal plane.                                         L 2040

         IR microscopes and telescopes with remote sensing applications,

              IR microscopes are used for measuring small spots (10
              microns) at relatively short distances (0.5 to 3 inches,
              typical).  IR telescopes are used to study larger spots (1
              or 2 feet diameters) are very long distances ( 500 feet or
              more).  Radiance, temperature or IR spectroscopy
              measurements result.
                                                                          L 2050
         Field-portable UV, Vis and NIR and SWIR spectrometers,

              Compact spectrometers and spectrophotometers
              (tungsten-halogen, xenon and deuterium sources included)
              using Si CCD photodiode arrays for detectors and fiber
              optics.  Cover from the near UV (190 nm, blue enhanced Si
              detector) to the near IR (1100 nm), this includes the
              visible (Vis) from 400 to 800 nm.

         Custom instrument interface software using LabVIEW for Windows,  L 2060

         Upgrades of older Barnes Engineering Corp (BEC) radiometers
         such as the Mark II 12-550 spectroradiometer.

         Many of the calculations presented in this application manual
         are used in the design and operation of these instruments.

         If you need any guidance related to these instruments, please
         contact the Minarad Staff at (203) 452-8310 or fax a note to
         (203) 452-8311.                                                  L 2070


    ------------------------------------ 25.0 -- About Minarad Spectrum. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   46 --



ÕÍÍÍÍÍÍÍÍÍÍÍ¸
³ GLOSSARY  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

26.0     Glossary of Terms
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

       º Note, Use the Jump command to locate a glossary reference.    º
       º Scroll the screen until the reference is in the middle at lineº
       º 12.  The Jump box will light up.  Type J to locate.  Repeat   º  L 2080
       º typing A, as needed, to continue the search.                  º


Cartesian ovoid.  See  IRRA402 .

Compound thick lenses.  See  IRRA443 .

Compound thin lenses.  See  IRRA427 .

Integration.  See  IRRAELIN .                                             L 2090

IR Source (blackbody).  See  IRRA1946 .

Lens Imagery.  See  IRRA419 .

Mirrors.  See  IRRA495 .

Series.  See  IRRAELSE .

Spherical refracting surfaces.  See  IRRA405 .                            L 2100

Radiation.  See  IRRASLWV .

Thick Lenses.  See  IRRA442 .

Thin Lenses.  See  IRRA410 .

ÕÍÍÍÍÍÍÍÍÍ¸
³ LICENSE ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                          L 2110
27.0         Product License and Warranty.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

               Software License Agreement  (Registered Users)

         If you are a registered user, Minarad Spectrum, Inc.  (MSI)


    ------------------------------ 27.0 -- Product License and Warranty. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   47 --


         grants you the right to use this Software for a single-user
         computer or a workstation not attached to a network.  You may
         not rent or lease this Software without the expressed written
         permission of MSI.  You may not decompile, disassemble, reverse  L 2120
         engineer, copy, create a derivative work, or otherwise use this
         Software except as stated in this agreement.  The license
         authorizes you to create and use an extra copy of the Software
         on a home or laptop computer, as long as the extra copy is
         never loaded at the same time this Software is loaded on the
         primary computer on which you use this Software.

         If any provision of this agreement is found to be unlawful,
         void, or unenforceable, then that provision shall be severed
         from this Agreement and will not affect the validity and         L 2130
         enforceability of any of the remaining provisions.  This
         agreement shall be governed by the laws of the State of
         Delaware.

         The Software and accompanying materials are provided with
         Restricted Rights.  Use, duplication, or disclosure by the
         Government is subject to restrictions as set forth in
         subparagraph (c) (1) (ii) of The Rights in Technical Data and
         Computer Software clause at DFARS 252.227-7013, or
         subparagraphs (c) (1) and (2) of the Commercial Computer         L 2140
         Software--Restricted Rights at 48 CFR 52.227-19, as applicable.
         Contractor/manufacturer is Minarad Spectrum, Inc., at the
         address listed below.

         Non registered users must comply with the Shareware policy
         described elsewhere in this software Package.

                   Type T to return to the Table of Contents.

                              Warranty Information                        L 2150

         Minarad Spectrum, Inc.  (MSI) hereby disclaims all warranties
         relating to this Software, whether express or implied,
         including without limitation any implied warranties of
         merchantability or fitness for a particular purpose.  MSI will
         not be liable for any special, incidental, consequential,
         indirect or similar damages due to loss of data, loss of
         profits, lost savings or any other reason, even if MSI or an
         agent of MSI has been advised of the possibility of such
         damages.  In no event shall MSI's liability for any damages      L 2160
         ever exceed the price paid for the license to use Software,
         regardless of the form of the claim.  The person using the


    ------------------------------ 27.0 -- Product License and Warranty. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   48 --


         Software bears all risk as to the quality and performance of
         the Software.  This Software is licensed AS IS.

         Any action or proceeding brought by either party against the
         other arising out of or related to this agreement shall be
         brought in a STATE or FEDERAL COURT of competent jurisdiction
         located in Fairfield County, Connecticut.  The parties hereby
         consent to in personam jurisdiction of said courts.              L 2170

                   Type T to return to the Table of Contents.

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ USER SUPPORT ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

28.0                    User Support.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         This program has undergone over 5 years of "beta testing"        L 2180
         around the world.  The algorithms have been in use since the
         1960's, are proven and believed highly reliable.  However,
         comprehensive programs of this nature may develop what are
         called "bugs".  User support is provided to all registered
         users for a minimum of 3 months without charge.  Registered
         users can receive such help via phone/mail.  Registration also
         enrolls the user for notification of "bug" fixes, upgrades, new
         versions, new products and many more benefits.  The phone and
         fax numbers for Minarad Spectrum are:
                                                                          L 2190
                  Voice: 203 452-8310        Fax: 203 452-8311

         To jump to the registration section, position the jump line in
         the center of the display and type J.   ùRegistrationù .
         Support will be provided to non-registered users and users
         beyond the free support period on a time and materials basis.


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ REGISTRATION ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ   L 2200

29.0                 Order/Registration Form
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         If a printer is available, position the order form (part 1) on
         the screen and type the "(print screen)" key to make a copy.
         Then, advance the text and position the order form (part 2) on
         the screen and type "(print screen)" again to finish.


    ------------------------------------ 29.0 -- Order/Registration Form ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   49 --



      Minarad Spectrum Products Order/Registration Form  (part 1)         L 2210

    Name:________________________________  Title:________________

    Company:_____________________________________________________

    Address:____________________________ City:___________________

    State:___________   Zip:_____________  Country:______________

    Date:_____/_____/_____           (Fill out form completely)           L 2220

    ---------------------------------------------------------------
    Product                     #     Price/ea     S&H       Total
    ---------------------------------------------------------------

   OPTICS, IR and RADIOMETRY   ___    _$29.95_    _$5.00_   _______
   Calculations By Nelson
   Engborg and Paul Murphy

                                                                          L 2230

------------------------------------------------------------------------
------------------------------------------------------------------------
           Minarad Spectrum Order/Registration Form  (part 2)

    * Canadian Orders, Add $2.00 per copy                   _______

    * International Orders, Add $6.00 per copy              _______

    * CT Residents add appropriate sales tax                _______       L 2240

                                     TOTAL ENCLOSED      __________

    Disk Size: [ ] 5-1/4"   [ ] 3-1/2"   [ ] Check  [ ] Visa  [ ] MC

    Card# __________________________________     Exp. Date ________

    Signature ______________________________

    How did you hear about our Products?    [ ] BBS   [ ] Friend          L 2250
    [ ] Other _____________________________________________________

                  Mail Completed form with Payment to:



    ------------------------------------ 29.0 -- Order/Registration Form ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   50 --


                 Minarad Spectrum, Inc.   Dept. MSI312
                          126 Monroe Turnpike
                   Trumbull,  CT   06611   06404  USA

    Support ONLY,  203 452-8310     Fax ONLY, 203 452-8311
                                                                          L 2260
         [Feb 1995]  Prices subject to change without notice.

               Type T to return to the Table of Contents.

ÕÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ REFERENCES ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

30.0           Optics and Infrared References.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                                                                          L 2270
 M.  Born and E.  Wolf, "Principles of Optics", Pergamon, Oxford, 1980.

 Dr.  M.  Foigel, Chief Editor, "The Optics Problem Solver", Research
 and Education Association, 61 Ethel Road West, Piscataway, New Jersey,
 08864, Revised Printing 1990

 E.  Hecht, "Optics", Addison-Wesley, Reading, Massachusetts, 1988.

 Eugene Hecht, Ph.D., "Optics", Schaum Outline of Theory and Problems,
 McGraw-Hill Book Company, New York, 1975                                 L 2280

 M.  V.  Klein and T.  E.  Furtak, "Optics", John Wiley & Sons, New
 York, 1986.

 R.  S.  Longhurst, "Geometrical and Physical Optics", John Wiley &
 Sons, New York, 1964.

 F.  W.  Sears, " Optics", Addison-Wesley, Cambridge, Massachusetts,
 1948.
                                                                          L 2290
                ------------- IR References -------------

 Nelson Engborg, Al Kozlowski and Paul Murphy, "IR polarization:
 Applications to sources and radiometers", Technical Note #11, Minarad
 Spectrum, Inc., May 1994.

 Nelson Engborg and Paul Murphy, "Discussion of Field of View (FOV),
 spot diameter and working distance for an infrared system", Technical
 Note #21, Minarad Spectrum, Inc., May 1994.
                                                                          L 2300


    ---------------------------- 30.0 -- Optics and Infrared References. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   51 --


 Nelson Engborg and Paul Murphy, "Non-contact temperature measurement
 with the infrared microscope", Technical Note #31, Minarad Spectrum,
 Inc., May 1994.

 Al Kozlowski, Al Waldie, Nelson Engborg and Paul Murphy, "8 inch Target
 Projector:  Collimator, target wheel and IR source", Technical Note
 #41, Minarad Spectrum, Inc., May 1994.

 Gerald C.  Holst, "Testing and Evaluation of Infrared Imaging Systems",
 JCD Publishing Co., 2923 Cove Trail, Maitland FL 32751, 1993.            L 2310

 W.  L.  Wolfe and G.  J.  Zissis, "The Infrared Handbook", Infrared
 Information and Analysis Center (IRIA), Environmental Research Institue
 of Michigan, Revised Printing, 1985.

ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ MANUALLY INSTALLING ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

31.0           Instructions for Manually Installing Package.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  L 2320

     The following are minimal instructions for manually installing
     Minarad Spectrum's Optics and IR Radiometry Package.

         Minimum distribution files:  README.1ST, MSI312.ICO, ACAL3.EXE,
         ACAL3HLP.HLP and MSI312.HLP with its *.EQU files.

         These files will probably be bundled in a compressed file such
         as MSI312.ZIP, MSI312.SDN, or something similar.  Please
         unload.                                                          L 2330

         Create a DOS directory named MSI and change to it:  cd\ (enter)
         md\msi (enter) cd \msi (enter)

         Copy ACAL3.EXE, ACAL3HLP.HLP, MSI.ICO and MSI312.HLP and all
         *.EQU file into the directory MSI. Copy MSI312.BAT into root.

         Add these statements to AUTOEXEC.BAT in the base directory:
         SET ASTRO3=C:\MSI. Append to existing PATH statement ;C:\MSI;
                                                                          L 2340
       Running Under Windows as a Non-Windows Application

         Follow the installation instructions and install on the hard
         drive C.  Start WINDOWS (tm, MicroSoft).  Click on FILE then
         click on PROPERTIES.  Enter the following information for each
         of the fields.  Description:  Optics and Radiometry, Command:


    -------------- 31.0 -- Instructions for Manually Installing Package. ---






    ---------- MSI312.HLP ------------ IR Radiometry ---------------   52 --


         ACAL3.EXE MSI312.HLP, Working Directory:  \MSI.  Click on
         CHANGE ICON.  Enter Filename:  C:\MSI\MSI312.ICO.  Click on OK
         to exit and click on OK to exit FILE.  The MSI icon should
         appear in the accessory window.  Click on it to run MSI312.      L 2350

         To start:  cd\msi (enter)    acal3 MSI312.hlp (enter)

         Access on-line help (file: ACAL3HLP.HLP) from equations
         display with (F1) key.

ÕÍÍÍÍÍÍÍÍÍÍÍ¸
³ HELP FILE ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

32.0          Help File: Summary of File Viewing Commands                 L 2360
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

    A - Auto-search of entire text for user-supplied string. Search is
        in uppercase and is case insensitive. If string found,
        type A to continue or to enter new string, type (space) A.
    B,N - Move back or ahead 18 lines.  Also use (backspace) for "B".
    E, (esc) - Exit from help file to equations display.
    F,T,K - Jump to the first (beginning), T.O.C or last (end) line.
    G - Skip to Glossary of terms or summary of functions, if present.
    J,(ent) - Search line on ³JUMP³, Reference is after  . Jump to        L 2370
              line number or perform autosearch ahead if text reference.
    L,P - Jump to line/page. Type Lxxx(ent) or Pyy(ent) to jump to
          line #xxx or page #yy. With + or -, ahead or back 56 lines.
    S,R - Skip ahead (S) or back (R) in help file to major headings
    W - Skip to Summary of useful calculations or warnings, if present
    1 to 9 - Typing 1 to 9 advances the text by 1 to 9 lines.
    (ctrl Q) - Exit from help file.  Same as command "E".
    Edit keys - Use edit keys: (Home) (up arrow) (PgUp) (left arrow)
                (right arrow) (End) (down arrow) (PgDn).
                                                                          L 2380
     Entry into the application file is at/near the last position.
     Type: T to return to Table of Contents or E to exit the file.












    ---------------- 32.0 -- Help File: Summary of File Viewing Commands ---