|
                                     C A P     


            PCPAINT-Compatible Picture and Clipping Capture Utility

               Written by John Bridges for Microtex Indutstries




























                         Another USEware product from:

                           Microtex Industries, Inc.
                          2091 Business Center Drive
                              Irvine, Ca.  92715
                                (714) 476-0777

                  (714) 545-8100 - PCPaint Picture Swap Line

      Current release number: 1.1B          Current release date:08/86
















                                 WHAT IS CAP?


      CAP  is  a  utility  to  aid GRASP users in capturing clippings and
      pictures from programs other  than PCPAINT  PLUS(tm).   With CAP, a
      user  can  capture  images  from  virtually  any  other program and
      quickly move images into  presentations  running  under  GRASP. The
      pictures  and  clippings  created  by  CAP  are  completely PCPAINT
      PLUS(tm),  GRASP(tm)  and  ARTOOLS(tm)  compatible.  CAP  is memory
      resident and occupies approximately 26K of memory.


                                HOW TO RUN CAP

      To run  CAP, just  be sure  that CAP.COM  is either  on the current
      drive and directory, or  is accessible  by your  PATH statement. If
      this isn't clear, the put the GRASP distribution disk into drive A,
      close the door, and type the following:

      A: {enter}
      CAP {enter}

      You should see a message that looks like:


      Resident Capture Utility v1.1
      Written by John Bridges
      Microtex Industries, Inc. 1986
      Press ALT rightSHIFT to capture screen

      CAP is now loaded and ready for use.



      WARNING:  Please do NOT run CAP twice. Sometimes, depending on your
      machine, it  will cause  the system to hang.  Keep track of whether
      you have loaded CAP or not and only  load it  once. If  you need to
      remove it, use the procedure below, REMOVING CAP.


                                BRINGING UP CAP

      To activate CAP, hold down the ALT key and press the shift key that
      is on the right side of the keyboard  (opposite from  ALT). Release
      both keys and you should see a flashing crosshairs in the center of
      the screen. At this  point, you  would do  whatever you  want to do
      inside  CAP  (see  USING  CAP  for  more details), then quit CAP by
      pressing ESC.



                 CAP - Resident Capture Utility for GRASP(tm)
                                   Page:  1









                                 REMOVING CAP

      If CAP is the LAST memory resident utility you loaded, and
      you want to free up the memory it occupies, just press CTRL-Q while
      you have the CAP crosshairs on the screen. In other words,
      where you  would normally  press ESC  to quit  CAP, press CTRL-Q to
      quit and remove it from memory instead.


                             CHANGING THE CAP KEYS

      As was stated before,  to  bring  up  CAP  you  press  the  ALT and
      rightSHIFT  keys  together.  If  this  particular  key  arrangement
      conflicts with your application software, you may change  it. There
      are 4 keys available, of which you must choose 2. The 4 keys are:

      C - Control                         L - Left-side Shift Key
      A - ALT                             R - Right-side Shift Key

      If you want to use any combination 2 of these 4, just specify so on
      the command line when you first run CAP.  For example,  if you want
      the 2 shift keys together to being up CAP, type:

      CAP /k:LR

      Or if  you want  Control ALT  (the same as Sidekick - be careful!),
      type:

      CAP /k:AC

      That's all there is to it!  Remember you  must use  2 keys.  If you
      specify just  1 key,  no keys,  or invalid  keys, CAP  will use its
      default keys, AR.

                               USING INTERRUPTS

      One other thing you can do is to  enable a  user interrupt  for CAP
      initialization. This  is very  useful if the software you are using
      is  being  particularly  stubborn  about  allowing  you  to capture
      screens. To  assign a  user interrupt to CAP, use the /i: parameter
      as follows:
       
      CAP /i:x
       
      where x is the  number  of  the  interrupt  you  want  enabled. For
      example,  if  you  want  to  invoke  CAP  with the SHIFT-PrtSc key,
      interrupt 5, you would type:
       
      CAP /i:5


                 CAP - Resident Capture Utility for GRASP(tm)
                                   Page:  2









                                   USING CAP


                                Saving Pictures

      The simplest  way  to  save  a  picture  is  to  use  the following
      procedure:

      Assuming you  have already  run CAP and are now in your application
      program...

      1) Set the screen  set up  the way  you want  with your application
      program.

      2) Bring  up CAP  by pressing  ALT rightSHIFT. You will see the CAP
      crosshairs in the middle of the screen.

      3) Press ENTER. You will see the top lines of  the screen disappear
      and be replaced with the prompt:

      PIC name:

      Enter up  to 8 characters for your picture name and press enter. If
      you want to use an extension other than  .PIC, you  must specify it
      here. The drive will spin and your picture will be saved.

      4) You  should now see your screen with the crosshairs again. Press
      ESC to go back to running your application.


      You picture is now save and  you can  go on  using your application
      program. If  you need  to capture  another screen, just repeat this
      procedure.


















                 CAP - Resident Capture Utility for GRASP(tm)
                                   Page:  3









                               Saving Clippings

      Saving a clipping is much like  saving a  picture, except  that you
      must first tell CAP which portion of the screen you want to be your
      clipping. This is done using the arrow keys to move  the crosshairs
      and the  SPACEBAR to  tell CAP to start a new clipping. Here is the
      procedure:


      Assuming you have already run CAP and are  now in  your application
      program...

      1) Set  the screen  set up  the way  you want with your application
      program.

      2) Bring up CAP by pressing  ALT rightSHIFT.  You will  see the CAP
      crosshairs in the middle of the screen.

      3)  Move  the  crosshairs  using  the  arrow  keys.  You will see a
      rectangle being created. This is  the  boundary  of  your clipping.
      When the  crosshairs gets to one of the corners of what you want to
      be your  clipping,  press  SPACEBAR.  This  tells  CAP  to  start a
      clipping definition from here.

      4) Move  the crosshairs  to the  opposite corner  of the region you
      want to be your clipping.

      5) Press ENTER. You will see the top lines of  the screen disappear
      and be replaced with the prompt:

      CLP name:

      Enter up to 8 characters for your clipping name and press enter. If
      you want to use an extension other than  .CLP, you  must specify it
      here. The drive will spin and your clipping will be saved.

      IMPORTANT NOTE: The way that CAP decides whether you want to save a
      picture or a clipping  is  that  if  there  is  a  rectangular area
      defined, CAP  will save  a clipping. If not, it will save the whole
      screen. If you start to define a clipping with the arrow keys, then
      change your  mind and  want a picture, just press SPACEBAR to clear
      current clipping definition and the press  ENTER to  save the whole
      screen as a picture. 

      ALSO note  that when  CAP saves  a clipping,  it saves the rows and
      columns of points UNDER the rectangle as part of the clipping. This
      is consistent  with the  way the  'edit-box' or  'marquee' works in
      PCPAINT PLUS(tm).



                 CAP - Resident Capture Utility for GRASP(tm)
                                   Page:  4









                               Special Features



      CTRL-B  ...  BSAVE mode - After you bring up CAP and are looking at
      the crosshairs,  pressing CTRL-B  will toggle BSAVE on and off. You
      cannot BSAVE multiple bit-plane screens  like  EGA  16  color mode.
      BSAVE is really only useful for mode A, or CGA 4 color mode screens
      that you may want  to load  into a  BASIC program.  Pressing CTRL-B
      again will return to packed page format.



      CTRL-V   ...   Forced Video  Mode -  After you bring up CAP and are
      looking at the crosshairs, pressing CTRL-V will enable forced video
      mode. You  will be  prompted to  enter a video mode letter and then
      CAP will try to save  the  current  screen  in  the  format  of the
      requested  video  mode.  Video  modes  are  the same as for PCPAINT
      PLUS(tm) and GRASP(tm). For example, if you are in EGA 16 color hi-
      resolution mode,  but the  program you are running didn't set it up
      properly according to BIOS, just  force video  mode G  and CAP will
      save out a 16 color hi-resolution screen.

      Please  note  that  modes  0,1  and  2  are  text modes and are not
      available in PCPAINT PLUS(tm). Also note that H1 and H2  only refer
      to CAP. PCPAINT PLUS(tm) and GRASP both use Hercules page 1 and the
      video mode is set with just the letter H.

      Valid Video Modes for Forced Video Over-ride

          0  - 40 column color text
          1  - 80 column color text
          2  - 80 column monochrome text
          A  - 320x200 4 color CGA
          B  - 320x200 16 color PCjr / STB / TANDY 1000
          C  - 640x200 2 color CGA
          D  - 640x200 16 color CGA
          E  - 640x350 2 color EGA
          F  - 640x350 4 color EGA
          G  - 640x350 16 color EGA
          H  - 720x348 2 coloe Hercules/AST Preview - page 1
          H1 - (same as H)
          H2 - 720x348 2 color Hercules/AST Preview - page 2
          I  - 320x200 16 color Plantronics/AST CGPLUS
          J  - 320x200 16 color EGA






                 CAP - Resident Capture Utility for GRASP(tm)
                                   Page:  5











      ;  ...   Seek a clipping - During the clipping  definition process,
      if the rectangle you are stretching completely surrounds the object
      you want to grab, and lies entirely in a region of a  single color,
      pressing the  ; key will cause all 4 edges of the rectangle to seek
      inward until an edge is found. This is useful for isolating objects
      when you  don't want  a lot of extra 'white space' surrounding your
      object. Try a few tests to get the feel of it.

      .  ...  Change  active  corner  -  During  the  clipping definition
      process, you are dragging one of the corners of the rectangle. This
      corner is called the 'active corner'. To change  the active corner,
      press the  . key.  You will notice that the corsshairs moves around
      in a clockwise direction to the adjacent corner. This is useful for
      altering regions without having to start a new one.

      1-0 ... Change crosshairs step - by pressing one of the number keys
      at the  top of  the keyboard  while the  crosshairs is  up, you can
      change  the  number  of  points  the crosshairs moves each time you
      press an arrow key. Pressing 1 means move the crosshairs  one point
      for each arrow key press. 0 means move the crosshairs 10 points for
      each arrow key press.  This is  useful for  moving more  quickly or
      finer adjustments.



























                 CAP - Resident Capture Utility for GRASP(tm)
                                   Page:  6