GREY 1.0
           PCX Dithered Halftone to PCX Grey Halftone Converter
           Copyright 1989 by Curtis Philips
           
           DOCUMENTATION
           
           Grey is a utility designed to convert Publishers Paintbrush
           (or Paintbrush Plus) 8x8 dithered halftone PCX or PCC files
           to 63-grey-level PCX or PCC file formats, using the 256-
           color (greyscale) ZSoft pallette.
           
           From the DOS prompt, the syntax is:
           
                GREY [inputfile.pcx] [outputfile.pcx]
           
           This program is designed specifically for use with
           Paintbrush/Scanner configurations that produce an 8x8
           dithered halftone grid, such as the Canon IX-12. The utility
           reads the first 8x8 pixel grid (8 bytes) and converts it to
           a one-byte grey value proportionate to the number of pixels
           that are "lit," from a range of 1.5% grey to 98.5% grey. The
           program then shifts right by 4 pixels (half a grid) and
           converts the next overlapping 8x8 grid. This overlapping
           ensures a finer degree of detail and a larger-size output
           image to work with. After the first line is read and
           converted, the program shifts down by 4 pixels each time to
           convert the next grid-line, producing a vertically
           overlapping 8x8 grid in addition to the horizontal
           overlapping grids. The possible grey levels total 63.
           
           The output file will be approximately the same size as the
           input file, generally a few K less. But the image itself
           will be about one-fourth the height and width of the
           original.
           
           The output file can be viewed on a VGA or analog monitor in
           grey values (or colors) as a PCX or PCC file. To import the
           image into Ventura Publisher and take advantage of Ventura's
           advanced image handling capabilities, the file should be
           converted into TIFF format. To do this, run the output file
           from GREY through the PCXTIF utility available from ZSoft
           through their BBS (404-427-1045). Then load the TIFF image
           into a Ventura frame, select Image Settings from the Frame
           Menu, and find the optimal screen angle and frequency
           settings. Printing at higher resolution on a Linotronic may
           be the only way to fully take advantage of the number of
           grey levels/resolution embedded within the file.
           
           Even if the resolution of your laser printer does not allow
           you to produce the full number of greys (or resolution)
           generated by GREY, perhaps the most important benefit of
           using a grey-level file format is that the image can be
           reduced or enlarged to any size without interference
           patterns being generated, and even enlarging the image
           beyond its original size will not increase the size of the
           halftone dots as is the case with its dithered counterpart.
           









           If you continue to use this utility, you are requested to
           make a contribution. Thank you.
           
           Comments and contributions can be made to the address below,
           or comments on CompuServe to ID number 72251,226.
           
           Curtis Philips
           520 Heathcliff Drive
           Pacifica, CA  94044






















































         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  The P(s)L cannot de-
         bug programs over the telephone.

         Disks in the P(s)L are updated monthly, so if you did not get
         this disk  directly from the P(s)L,  you should be aware that
         the files in this set may no  longer be the current versions.

         For a copy of the latest monthly software library newsletter
         and a list of the 1,800+ disks in the library, call or write

                        The Public (Software) Library
                              P.O.Box 35705 - F
                           Houston, TX 77235-5705
                               (713) 665-7017