ASCII File Printing Utility                  PR (2.2)



      NAME
            pr - print file (or files)

      SYNOPSIS
            pr [ option ] ... [ file ] ...

      ACKNOWLEDGMENTS:

           This  is an enhancement of an excellent Printer Utility  written 
      by Morris Jones of MicroPro and submitted - with source - to the user 
      community.   The current author (Michael Bate) has attempted to  make 
      this  a more generally useful utility by expanding the  options,  and 
      adding a facility for customization.

           pr is written in Microsoft C and uses their runtime library.

      PURPOSE:

           Pr  produces  a printed listing of one or  more   files.     The 
      output is separated into pages headed by "standard header" or a head-
      er line specified by the user.

      HOW TO USE:

           Pr is invoked via:

                             pr [ option ] ... [ file ] ...

           Wildcards may be used to specify files.

           All the options must precede all the files.  Options are in  the 
      form of "switches", beginning with a "-".  Each option is  identified 
      by  a single letter (case is not significant), which may be  followed 
      by:

                1. Nothing, i.e. '-f'  -  use form feeds.

                2. A number,  '-w80'  - set page width to  80.   NOTE  that 
                     there  must  be no space between the  option  and  the 
                     number.

                3. A possibly lengthy parameter, which is usually placed in 
                     quotes,  i.e. '-h "This is my header" which  sets  the 
                     page header.

           The first two kinds of options may be grouped (i.e., '-fw80').

           An example of a fairly complicated invocation of "pr" is:

        pr  -a "1b 41 30" -w132f -i7 -n -o outfile.typ infile.doc in2.doc

      This would print two files (infile.doc & in2.doc) one after the other 


                                         1



                     ASCII File Printing Utility                  PR (2.2)


      and  send the printer-formatted output not to the printer, but  to  a 
      file named "output.typ".  The output would be preceded by three bytes 
      - ESC A 0 - and would be indented seven columns.  Each line would  be 
      preceded by a line number.

      HELP AND ERROR MESSAGES:

           If  you invoke pr with no options, or with improperly  specified 
      options,  pr  will  display  a  list of  its  options  with  a  brief 
      description of each one.

           pr has only the simplest error messages.


      FILE NAMES:

           You  can  use full MS-DOS paths for file names, both  for  input 
      files and output redirection ("-o" option).

      PAGE HEADERS:

           Normally pr assumes that the files are NOT already formatted for 
      the printer and (a) adds a heading line to each page and (b) supplies 
      blank lines to space over page perforations.

           The page header normally consists of the file name and the  date 
      the file was last modified (as shown in the file directory).  If  the 
      page  is  wide enough (about 90 columns plus margin),  it  will  also 
      show the current date.

           The "-h" option may be used to specify your own header in  place 
      of the normal one.

           The "-e" option (Exact print) indicates that the file is already 
      formatted for the printer.  Neither headers nor extra blank lines are 
      generated.

      HORIZONTAL TABS:

           pr  normally expands horizontal tabs, to a width of  8  columns.  
      The "-t" option may be used to specify a different width, or - if you 
      specify  a  width of zero - to send the tab character to  the  output 
      without translation.

      HIGH-ORDER BITS AND GRAPHICS:

           pr  normally  sends all characters (except tab)  to  the  output 
      without translation.

           The  "-x"  option causes the high order bit of each byte  to  be 
      masked out.  This is useful if you want to print a file that has been 
      formatted  by  a  word processor which uses the high  order  bit  for 
      control  information.  (Although you'd probably be better  off  using 


                                         2



                     ASCII File Printing Utility                  PR (2.2)


      the word processor to print it).

           The "-x" option also causes all non-printing control  characters 
      to be ignored - not sent to the output at all.

           Null characters (all zeroes) are never sent to the output.

           If  you  are printing with a graphics printer,  you  should  NOT 
      specify the "-x" option and you SHOULD specify "-t0" so you will  get 
      the graphics presentation of the horizontal tab.

      PRINTING IN COLUMNS:

           pr  can  print one file in several vertical columns  across  the 
      page.   It can also print several files simultaneously, one  in  each 
      column.  The actual column width is the same for each column, and  is 
      compute  from the page width, left margin (if specified), and  number 
      of files or columns requested.  The "-b" switch requests multi-column 
      output  of  a  single file.  The "-m"  option  requests  simultaneous 
      printing  of  more  than  one file.   These  two  options  CANNOT  be 
      requested together.

      PRINTING MORE THAN ONE FILE:

           pr will print as many files as you specify on the command  line, 
      including all the files that match wildcard expressions. Normally the 
      files are printed one at a time.  If you specify the "-m" option, all 
      the files will be printed at once, in vertical columns.

      HANDLING "LONG" LINES:

           pr  normally truncates any line that is too long to fit  in  the 
      available  space on the page.  This space is computed from  the  page 
      width, left margin (if specified), number of columns (if "-m" or "-b" 
      is  specified), and line-number width (if the line-numbering   option 
      ["-n"]  is specified).  You can request (with the "-c"  option)  that 
      long  lines  be wrapped onto the next line.  This option may  NOT  be 
      specified if you are using one of the multi-column modes.

      OVERPRINTING:

           If a line ends in a carriage-return only, instead of the  normal 
      carriage-return   -  linefeed  combination,  this  means   that   the 
      subsequent  line  should be printed on top of it.  Normally  this  is 
      used  for  underlining  or special effects  such  as  strikeout.   pr 
      handles  this  situation correctly only if you do NOT  specify  line-
      numbering  ("-n"  option) or multiple-columns ("-b",  "-m"  options).  
      Also,  overprinting will not work for any line that is wrapped  ("-c" 
      option),  but  will work for short lines when the "-c" option  is  in 
      effect.





                                         3



                     ASCII File Printing Utility                  PR (2.2)


      OUTPUT REDIRECTION:

           Normally pr sends its output to your printer (PRN device).   You 
      may  use the "-o" option to send the output to a disk file, a  device 
      (such  as  CON),  or the standard output.  Standard  output  may,  of 
      course, be piped to another program.

      READING THE STANDARD INPUT:

           pr  may be requested to read the standard input instead of -  or 
      in  addition  to - MS-DOS disk files.  Thus the  standard  output  of 
      another program can be piped to pr.

      PRINTER INITIALIZATION:

           The  two  options '-a' and '-z' allow you to send  an  arbitrary 
      string of characters (not necessarily printable) before and after the 
      files  formatted  by  pr.  These options are designed  for  use  with 
      printer  "escape sequences" that do such things as set the  character 
      width or print mode.  The characters to be sent must be specified  in 
      hex, i.e.,

                 pr -a "1b,41,30"   -z  "1b 43 30"     files...

      Note that characters may be separated by blanks or commas.  They need 
      not be separated at all.  That is "1b  43" is the same as "1B,43"  is 
      the same as "1B43".

      DETAILED LIST OF OPTIONS:

           The  following  options are available (# refers to one  or  more 
      decimal digits):

                     -a   This option must be followed by a parameter  that 
                          specifies  (in  hex)  a  printer   initialization 
                          string.

                     -b#  Produce n-column output.

                     -c   Don't  cut off each line when the page  width  is 
                          reached.  Instead,  wrap each line  to  the  next 
                          printer  line.   May not be used  in  combination 
                          with multi-column (including '-m' output).

                     -e   Exact  print - The file is already formatted  for 
                          the  printer.  Do not add headers or blank  lines 
                          to  space over perforations.  May not be used  in 
                          combination with '-#', '-m' options.

                     -f   Use  formfeeds  instead of newlines  to  separate 
                          pages.  A formfeed is assumed to use up two blank  
                          lines   at  the top  of a page.   (Thus this  op-
                          tion does not affect the effective page length.)


                                         4



                     ASCII File Printing Utility                  PR (2.2)


                     
                     -h   Take the next argument as a page header.

                     -i#  Indent each line by # spaces.  Generally used  to 
                          add  a  left margin so pages can be placed  in  a 
                          notebook.

                     -l#  Take the length of the page to be #  lines   ins-
                          tead  of the default 66.

                     -m   Print all files simultaneously, each in one  col-
                          umn.

                     -n   Number each line.  Space is allowed for 6  digits 
                          plus a separating space.   If '-i' is also speci-
                          fied, the number comes after the margin.

                     -o   Redirect  output  to the filename  given  in  the 
                          following  parameter.  You may specify an  MS-DOS 
                          filename, device name (such as CON), or "stdout". 
                          If  this parameter is not specified, output  goes 
                          to PRN.

                     -sc  Separate columns by the single character c   ins-
                          tead  of by a white space.   A missing c is taken 
                          to  be a tab.  This only applies if you are  also 
                          using '-b' or '-m'.

                     -t#  Take  the width of a tab character to be  #  ins-
                          tead   of the default 8.  If # is ZERO, then  the 
                          tab  character will be treated as  a  non-graphic 
                          control  character  (see  option  '-x',   below).

                     -u   Pause before printing each page.

                     -w#  Take   the  width of the page to be #  characters 
                          instead  of  the default 80.  This is  the  TOTAL 
                          page  width,  including margin ('-i')  and  line-
                          numbers ('-n').

                     -x   Mask  the  high-order byte  from  each  character 
                          printed.     Also   ignore   any    non-printable 
                          characters (outside the range hex 20-7E).  If you 
                          do  not specify this option, the program  assumes 
                          that  you  have  a printer  capable  of  printing 
                          characters such as 03 (heart symbol).

                     -y   Print  the  standard input, in  addition  to  any 
                          files specified.

                     -z   This option must be followed by an argument  that 
                          specifies  (in hex) a  printer  de-initialization 
                          string.


                                         5



                     ASCII File Printing Utility                  PR (2.2)





      CUSTOMIZATION

           You  may customize your copy of PR.EXE by patching with  a  hex-
      ascii file editor, such as FIXFILE, DISMOD, MasterKey, or the  Norton 
      Utilities.   In this way you can change the default value of most  of 
      the command-line options.

           The first step is to search the file for the string:

                           ___PARAMETERS START HERE___

      This will be followed by the options.  Each has the form:

                                   NAME:value

      where  NAME is an all upper-case parameter name and value is  one  or 
      more  bytes containing the value.
      The options are as follows:

        INITCOUNT:   (-a) 1 byte, initially 0.  The number of bytes in  the 
                     initialization string sent to the printer.

        DEINITCOUNT: (-z) 1 byte, initially 0.  The number of bytes in  the 
                     de-initialization string sent to the printer.

        INIT_STRING: (-a) up to 16 bytes, initially zeroes.  The initializ-
                     ation string sent to the printer.

        DEINIT_STRING: (-z) up to 16 bytes, initially zeroes.  The de-init-
                     ialization string sent to the printer.

        OUTPUT_FILE: (-o) up to 100 bytes, initially zeroes.  If you supply 
                     insert  anything here (that is, the first byte  is  no 
                     longer  hex 00), it will be taken as the name  of  the 
                     output  file.  It may be an MS-DOS filename, a  device 
                     name, or "stdout".

        IF_LINENO:   (-n)  1 byte, initially 0.  If you set this  non-zero, 
                     the program will do line-numbering.

        IF_CUTOFF:   (-c)  1 byte, initially 1.  If you set this  to  zero, 
                     the program will wrap (instead of cut off) long lines.

        IF_MASK7     (-x)  1 byte, initially 0 - if you set this  non-zero, 
                     the program will mask the high bit off all  characters 
                     from  the file, and will NOT try to  print  characters 
                     that are "non-printable".  

        LINES_PER_PAGE:  (-l) 1 byte, initially 42 hex (66  decimal).   The 
                     total length of a page in lines, including header  and 


                                         6



                     ASCII File Printing Utility                  PR (2.2)


                     trailer  lines.   For standard 8 1/2 x 11 paper  at  6 
                     lines per inch, this comes to 66 lines.

        PRINTER_WIDTH:  (-w) 1 byte, initially 50 hex (80  decimal).    The 
                     total  width of the page, in characters.  Margins  and 
                     line-numbers  come  out  of this width.   50  hex  (80 
                     decimal)  is a good value for standard paper and  pica 
                     type.   You  might want to change this to 60  hex  (96 
                     decimal)  for elite type, or 84 hex (132 decimal)  for 
                     a wide computer printer (program listing files, etc.).

        TAB_WIDTH:   (-t)  1  byte,  initially  8.   The  total  width   of 
                     horizontal  tabs.  If set to zero, the  tab  character 
                     will be handled as a non-graphic control character.

        #_COLUMNS:   (-b)  1 byte, initially 1.  Must NOT be set  to  zero.  
                     The number of columns of text across the page.

        IF_HEADER:   (-h)  1 byte, initially 0.  If you set this  non-zero, 
                     the  program will print the page heading specified  in 
                     HEADING, below.

        MARGIN:      (-i)  1  byte, initially 0.  The number of  spaces  to 
                     indent each line to provide a left margin.

        START_PAGE:  (-p)  2 bytes, initially 00.  The page number on which 
                     to  start  printing.   Note that  this  is  a  4-digit 
                     hexadecimal number and that the least significant byte 
                     appears first.

        MULTIPLE:     (-m) 1 byte, initially 0.  If you set this  non-zero, 
                     the  program  will print all the  specified  files  in 
                     columns across the page.

        STD_INPUT:   (-y)  1 byte, initially 0.  If you set this  non-zero, 
                     the program will always include the standard input  as 
                     one of the files to be printed.

        COLUMN_SEPARATOR:  (-s)  1 byte, initially space  (hex  20).   This 
                     character  will be used to separate columns in  multi-
                     column output.

        HEADING:     (-h) 200 bytes, initially zeroes.  This is the text of 
                     the  page header.  Make sure it is not too  big.   The 
                     text  is terminated by a character  containing  binary 
                     (not ASCII) zero - that is, hex 00.


      AUTHOR

      Morris Jones, mojo@micropro.UUCP.

      Version 2 enhancements by Michael Bate


                                         7



                     ASCII File Printing Utility                  PR (2.2)



      TROUBLE REPORTS

           Please report any problems with this program to:

                          Michael Bate
                          195 Lake View Ave.
                          Cambridge, MA 02138
                          (617)-864-4358

           You  may also leave me a message on the CHANNEL1 bulletin  board 
      in Cambridge - (617)-354-8873.

      CHANGE HISTORY

           Version 2.0 contained many new features and enhancements.
           Version 2.1 fixed bugs in version 2.0.
           Version 2.2 fixed more bugs.





































                                         8