NEWPS.COM               (c) 1991 Pierre Jelenc
       version 2.1  (October 91)

        NEWPS.COM is a TSR that intercepts Int 05h in order to redirect
        PrntScr to LPT2 (or upon customization to any other parallel port).
        
        What NEWPS does: It installs itself resident and takes over the
        handler for Int 05h. When called by a SHIFT PRNTSCR, the resident
        portion of the program first test whether the shift key used was 
        the right side one. If that is the case, NEWPS issues a FormFeed to
        the designated printer, and exits. If the shift key was the left 
        side one, (or no shift key in the case of keyboards that issue an 
        Int 05h via the unshifted PrntScr), the resident program effects a 
        Print Screen similar to the original one, except that it is directed 
        to the alternate LPT port.
        In case of error, the error flag at 050:00h is set to 0FFh as with 
        the original handler, in case a program wants to look at it.

        New for Version 2.1
        This version fixes a problem that caused NEWPS to refused repeated
        requests with certain configurations, especially with MS DOS 5.0

        New For Version 2:
        NEWPS will look in the BIOS data area for the number of lines  per 
        screen stored at 0040:0084h and print the appropriate number of 
        lines. This will depend on your video mode being well behaved enough
        to update the data whenever it is set to a new value. If there is no
        graphics adapter installed, the default of 25 lines will be used.

        What NEWPS does NOT do: It does not check that the port it is 
        redirected to, is in fact connected to anything; on the other hand, 
        at installation time, it announces on screen the new LPT, so that
        it is easy to check that the redirection is as intended. NEWPS does 
        not uninstall itself, nor deactivate itself. For those who need a
        temporary installation, use the INSTALL/REMOVE pair from PC Magazine,
        or the shareware MARK/RELEASE to permit uninstallation.

        The port identity is kept in a variable at offset 0103h in the COM
        program. NEWPS.COM can thus be easily modified to work with another
        port by patching the byte at 0103h. Note that in this scheme of 
        things LPT1:=0, LPT2:=1 (the default), LPT3:=2. Byte 0104h must 
        remain zero, since the variable is actually used as a word rather 
        than a byte. The sequence of bytes at the begining of the code looks
        like this: E9 A9 00 01 00 19 FB
            It is this byte  ^  that should be changed to change the port.


        Pierre Jelenc  72431,3252