VPS
                         VPS-Versatile Printer Setup Utility
                             Version 1.0        03-01-86


         WHAT IS VPS?

         VPS is an attempt to provide a generic printer setup utility that
         may be configured for any printer that uses escape sequences to
         control the printer.  There are many good printer setup utilities
         available, but they usually are designed to work with a specific
         model or brand of printer and with a limited set of escape codes.
         VPS allows you to define the escape sequences that you want to use
         and can be tailored for your specific printer and needs.  If you
         have more than one printer, you can create setup definitions for
         each printer and use VPS as needed to configure each printer based
         upon the printer definition you choose.

         There are three programs available.

         VPS - a menu driven version where options are selected by the cursor
               control keys.

         VPSB - a 'batch' version which may be used in BAT files.

         VPSRES - a version similar to VPS that remains resident.  This
                  version is available only to registered users.

         USING VPS

         VPS [d:\path\vpsfile]

         vpsfile - a text file which contains definitions for various printer
                  commands and options.  If not specified VPS.DEF is assumed.

         EXAMPLES:

           VPS vps.ibm
              - Will look for a file named vps.ibm on the logged drive.

           VPS A:vps.oki
              - Will look for a file named vps.oki on drive A:

           VPS C:\DOS\vps.eps
              - Will look for a file named vps.eps on drive C: in directory
                DOS

           VPS
              - Will look for a file named vps.def on the current logged
                drive and directory.

         Once VPS is activated use the cursor keys UP-ARROW, DOWN-ARROW,
         LEFT-ARROW, and RIGHT-ARROW to select an item from the VPS menu and
         then press RETURN to send the associated printer control codes to
         the printer.  The VPS menu is sensitive to the first character of
         each menu item.  An item may be selected by pressing the key
         corresponding to the first character of the desired menu item.  This
         method not only selects the option, but also sends the control codes
         to the printer.  Of course for this method to work properly you must
         insure that the first characters of all the menu options are unique.
         The PgUp and PgDn keys may be used to select LPT1, LPT2, or LPT3.

         VPSB lptx: [d:\path\vpsfile or /nn,nn,...,nn/]

         VPSB is a batch version of VPS.  It can be placed in BAT files.  A
         typical use would be in AUTOEXEC.BAT to initialize a printer at boot
         time.

         lptx: - is used to specify which printer you want to initialize.
         Valid values are LPT1:, LPT2:, LPT3: The colon is required.

         vpsfile - a text file which contains definitions for various printer
         options and commands.  The format of this file is the same as used
         by VPS and VPSRES.  All printer control characters found in the file
         will be sent to the printer.







                                     VPS  page 2


         /nn,nn,...,nn/ - this is alternative method of specifying the
         printer control codes.  The nn's represent escape codes in either
         decimal or character format.  The slashes are required.  See
         DEFINING PRINTER CONTROL FILES for more information.

         EXAMPLES:

         VPSB LPT1: vps.int

         - Will look for a file named vps.int on the current logged drive and
           directory and send all printer codes to LPT1:

         VPSB LPT2: /27,"C",68/

         - Will send the escape codes 27 C 68 to LPT2:

         VPSB LPT3: C:\DOS\vps.eps

         - Will look for a file named vps.eps on drive C: in directory DOS
           and send all printer control codes to LPT3:

         VPSRES [d:\path\vpsfile] [activate key] [deinstall key]

         VPSRES is a resident version of VPS.  This version map be activated
         at the press of a key, control codes sent to a printer, and return
         to your original application.

         vpsfile - see previous descriptions

         [activate key] - optional parameter which if specified must be a
         decimal key code for the keys you wish to use to activate VPSRES.
         The default is 91 which is SHIFT-F8.  A partial list of key codes is
         provided in APPENDIX A.

         [deinstall key]- optional parameter which if specified must be a
         decimal key code for the keys you wish to use to deinstall VPSRES.
         There is no default.  Deinstalling VPSRES can cause problems if some
         other memory resident programs have been loaded after VPSRES was
         loaded.  Use this option only if VPSRES was loaded last.

         NOTE: these parameters are positional.  In order to specify a
         deinstall key you must specify a vpsfile and an activate key code.

         EXAMPLES:

         VPSRES \DOS\vps.ibm 91 93

         - Will load VPSRES and look for a file named vps.ibm in directory
         DOS on the current looged drive.  SHIFT-F8 (91) will be used to
         activate VPSRES.  SHIFT-F10 (93) will be used to deinstall VPSRES.

         VPSRES

         - WIll load VPSRES and look for file vps.def in the currently logged
         drive and directory.  SHIFT-F8 (the default) will be used to
         activate VPSRES.  No key is provided to deinstall VPSRES.

         VPSRES vps.ibm

         - Will load VPSRES and look for a file named vps.named vps.ibm on
         the current logged drive and directory.  SHIFT-F8 will be used to
         activate VPSRES and no deinstall key will be defined.

         NOTE: VPSRES will only be loaded once (i.e. become resident).  The
         printer definition file will not be accessed until the first time
         VPSRES is actually activated.  Thereafter the printer definition
         file will not be accessed again unless errors were detected while
         loading the printer control codes.  Once the control codes are
         loaded without errors the printer definition file will not be
         accessed again and need not be available.  Once the printer
         definition file is loaded, another file cannot be loaded unless
         VPSRES is first deactivated.  This is one reason that an option is
         provided for deactivation.  Remember that VPSRES may only be safely
         deinstalled if it was the last program to become resident.






                                     VPS  page 3

         Once VPSRES is activated use the cursor keys UP-ARROW, DOWN-ARROW,
         LEFT-ARROW, and RIGHT-ARROW to select an item from the VPSRES menu
         and then press RETURN to send the associated printer control codes
         to the printer.  The VPSRES menu is sensitive to the first character
         of each menu item.  An item may be selected by pressing the key
         corresponding to the first character of the desired menu item.  This
         method not only selects the option, but also sends the control codes
         to the printer.  Of course for this method to work properly you must
         insure that the first characters of all the menu options are unique.
         The PgUp and PgDn keys may be used to select LPT1, LPT2, or LPT3.

         DEFINING PRINTER CONTROL FILES

         A printer control code file is a text file that you create using
         your favorite editor.  It is used to provide information to the VPS
         programs about the escape sequences that your printer will
         recognize.

         The statements in this file have the following format:

         <desc>=nn,nn,nn,...,nn     where:

         <desc> - up to 20 bytes of descriptive text which will be displayed
         in the VPS menus.  This must begin in column 1. If the first
         character is unique then the menu option may be selected by pressing
         the key for that character.  This descriptive text is terminated
         with and equal sign (=).

         nn,nn - ASCII decimal or character escape codes.  If character
         format is used the characters must be enclosed in quotes (").
         Character strings are limted to a max of four characters.  A max of
         20 escape codes may be specified per statement.  Two special control
         codes have been defined to perform two special functions.  INIT
         which will force a hardware reset of the printer with a 2 second
         delay after the reset.  WRIT which will display some test text
         information to assist in determining whether the printer is
         responding properly to the printer escape codes.

         NOTE: some printers have a reset escape sequence which should be
         used in preference to the INIT code.  The Epson FX-100+ is one such
         printer.  If the INIT function is used, sometimes a CANCEL (24) code
         is required in conjunction with the INIT.

         In addition, three special <desc> (@LPT, @TITLE, and @WRITDATA) have
         been provided to allow definition of default printer, menu title
         information and to override the default test text.  These three
         special <desc>'s must be in upper case only.

         EXAMPLES:

         @LPT=x where x=1 or 2 or 3   - To define the default printer.

         @TITLE=IBM GRAPHICS PRINTER SETUP   - To define a menu title.

         @WRITDATA=This is some sample text for use with VPS
              - To define some test text.

         FORM FEED=12
              - the descriptive text "FORM FEED" will be display in the VPS
                menus. When this option is chosen a form feed character (12)
                will be sent to the printer.

         LINE FEED=10
            - the descriptive text "LINE FEED" will display in the VPS menus.
              When this option is chosen a line feed character (10) will be
              sent to the printer.

         UNDERLINE ON=27,"-1"   or   UNDERLINE ON=27,"-","1"
            - the descriptive text "UNDERLINE ON" will display in the VPS menus.
              When this option is chosen the codes 27 "-1" will be sent to the
              printer.

         UNDERLINE ON=27,45,49
            - this equivalent to the above since decimal 45 is a "-" and 49 is
              a "1".

         7-TINY TEXT=15,27,"3",15,27,"S1",27,"M"
            - will turn on elite subscripting compressed with 15/216 line
              spacing.  Valid for Epson FX-100+ printers.


                                         VPS
                                     APPENDIX A

                                      KEY CODES


         KEY           UNSHIFTED     SHIFT       CTRL         ALT
         ------------------------------------------------------------
         F1               59          84          94          104
         F2               60          85          95          105
         F3               61          86          96          106
         F4               62          87          97          107
         F5               63          88          98          108
         F6               64          89          99          109
         F7               65          90          100         110
         F8               66          91          101         111
         F9               67          92          102         112
         F10              68          93          103         113
         LARR             75                      115
         RARR             77                      116
         UARR             72
         DARR             80
         HOME             71
         END              79                      117
         PGUP             73                      132
         PGDN             81                      118
         INS              82
         DEL              83
         A                                                    30
         B                                                    48
         C                                                    46
         D                                                    32
         E                                                    18
         F                                                    33
         G                                                    34
         H                                                    35
         I                                                    23
         J                                                    36
         K                                                    37
         L                                                    38
         M                                                    50
         N                                                    49
         O                                                    24
         P                                                    25
         Q                                                    16
         R                                                    19
         S                                                    31
         T                                                    20
         U                                                    22
         V                                                    47
         W                                                    17
         X                                                    45
         Y                                                    21
         Z                                                    44


                               APPENDIX A

                               KEY CODES


         KEY           UNSHIFTED     SHIFT       CTRL         ALT
         --------------------------------------------------------
         0                                                    129
         1                                                    120
         2                                                    121
         3                                                    122
         4                                                    123
         5                                                    124
         6                                                    125
         7                                                    126
         8                                                    127
         9                                                    128








                                         VPS
                                     APPENDIX B

         SAMPLE 1

         @LPT=1
         @TITLE=Epson FX100+ Printer Setup
         @WRITDATA=This is some test data, which can be used to verify options
         A-RESET=27,"@"
         B-8LPI=27,"0"
         C-6LPI=27,"2"
         D-DEFAULTS=27,"@",27,"M",27,"0",27,"C",68,27,"N",3
         E-ELITE ON=27,"M"
         F-DBL WIDTH ON=27,"W1"
         G-DBL WIDTH OFF=27,"W0"
         H-FORM FEED=12
         I-LINE FEED=10
         J-COMPRESS ON=15
         K-COMPRESS OFF=18
         L-PROPORTIONAL ON=27,"p1"
         M-PROPORTIONAL OFF=27,"p0"
         N-UNDERLINE ON=27,"-1"
         O-UNDERLINE OFF=27,"-0"
         P-ITALIC ON=27,"4"
         Q-ITALIC OFF=27,"5"
         R-EMPHASIZED ON=27,"E"
         S-EMPHASIZED OFF=27,"F"
         T-DBL STRIKE ON=27,"G"
         U-DBL STRIKE OFF=27,"H"
         V-BEEPER=7
         W-UNIDIRECTIONAL ON=27,"U1"
         X-UNIDIRECTIONAL OFF=27,"U0"
         Y-IMMEDIATE ON=27,"i1"
         Z-IMMEDIATE OFF=27,"i0"
         1-68 LINES/PAGE=27,"C",68
         2-INITIALIZE=INIT,24
         3-SUPERSCRIPT ON=27,"S0"
         4-SUBSCRIPT ON=27,"S1"
         5-SUB/SUPER OFF=27,"T"
         6-WRITE TEST DATA=WRIT
         7-TINY=15,27,"3",15,27,"S1",27,"M"
         8-FORWARD 1/216 IN=27,"J",1
         9-REVERSE 1/216 IN=27,"j",1
         0-66 LINES PAGE=27,"C",66

                                  APPENDIX B
         SAMPLE 2:
         @TITLE=IBM Color Printer Setup
         @WRITDATA=This is some test data, which can be used to verify options
         A-SET DEFAULTS=27,"C",68,27,"0",27,58
         B-DBL WIDTH ON=27,"W",1
         C-DBL WIDTH OFF=27,"W",0
         E-ELITE ON=27,58
         F-FORM FEED=12
         G-PROPORTIONAL ON=27,"p",1
         H-PROPORTIONAL OFF=27,"p",0
         I-COMPRESS ON=15
         J-COMPRESS OFF=18
         L-LINE FEED=10
         M-UNDERLINE ON=27,"-1"
         N-UNDERLINE OFF=27,"-0"
         O-EMPHASIZED ON=27,"E"
         P-68 LINES/PAGE=27,"C",68
         Q-EMPHASIZED OFF=27,"F"
         R-RESET TO POWER UP=27,"?",0,INIT
         S-DBL STRIKE ON=27,"G"
         T-DBL STRIKE OFF=27,"H"
         U-UNIDIRECTIONAL ON=27,"U1"
         V-UNIDIRECTIONAL OFF=27,"U0"
         W-WRITE TEST DATA=WRIT
         X-SUPERSCRIPT ON=27,"S",0
         Y-SUBSCRIPT ON=27,"S",1
         Z-SUB/SUPER OFF=27,"T"
         1-SET TOP OF PAGE=27,52
         2-TINY=15,27,"3",15,27,"S",1,27,"M"
         3-DP QUALITY PRINT=27,"I",1
         4-TEXT QUALITY PRINT=27,"I",2
         5-LETTER QUALITY PRINT=27,"I",3
         6-6LPI=27,"2"
         8-8LPI=27,"0"
         9-PRINT LABELS=INIT,27,"I",3
         0-66 Lines/Page=27,"C",66

                                     APPENDIX B

         SAMPLE 3
         --------
         @TITLE=Okidata 192/193 Printer Setup
         @WRITDATA=This is some test data, which can be used to verify the options
         A-RESET TO POWER UP=INIT,24
         B-8LPI=27,48
         C-LETTER QUALITY ON=27,88,1
         D-LETTER QUALITY OFF=27,88,0
         E-DBL WIDTH ON=27,"W",1
         F-DBL WIDTH OFF=27,"W",0
         G-FORM FEED=12
         H-LINE FEED=10
         I-COMPRESS ON=15
         J-COMPRESS OFF=18
         K-ELITE=27,58
         L-UNDERLINE ON=27,"-1"
         M-UNDERLINE OFF=27,"-0"
         N-EMPHASIZED ON=27,"E"
         O-EMPHASIZED OFF=27,"F"
         P-DBL STRIKE ON=27,"G"
         Q-DBL STRIKE OFF=27,"H"
         R-BEEPER=7
         S-UNIDIRECTIONAL ON=27,55,1
         T-UNIDIRECTIONAL OFF=27,55,0
         U-68 LINES/PAGE=27,"C",68
         V-SUPERSCRIPT ON=27,"S",0
         W-SUBSCRIPT ON=27,"S",1
         X-SUB/SUPER OFF=27,"T"
         Y-WRITE TEST DATA=WRIT
         Z-TINY=15,27,"3",15,27,"S",1,27,"M"
         1-DP QUALITY PRINT=27,"I",1
         2-TEXT QUALITY PRINT=27,"I",2
         3-LETTER QUALITY PRINT=27,"I",3

         General Information
         -------------------

         The VPS programs were developed on a PC/XT with 512K using DOS 2.1.
         The resident version VPSRES requires approximately 39K of address
         space.  The following files are provided in the library:

                     VPS.COM    - menu driven version
                     VPSB.COM   - batch version
                     VPS.DEF    - default printer code file (Epson FX-100+)
                     VPS.OKI    - printer code file for OKIDATA 193
                     VPS.IBM    - printer code file for IBM Graphics Printer
                     VPS.DOC    - this document

         FX-100+ is a registered trademark of EPSON AMERICA Inc.
         IBM is a registered trademark of International Business Machines.
         OKIDATA is a registered trademark of OKIDATA.

         License information
         -------------------

         You are free to use, copy and distribute all VPS files providing that

                    NO FEE IS CHARGED FOR USE, COPYING, OR DISTRIBUTION

                    IT IS NOT MODIFIED IN ANY WAY

         These programs are provided AS IS without any warranty, expressed or
         implied, including but not limited to fitness for a particular
         purpose.

         If you find these programs to be useful, a $10 contribution would be
         appreciated.  For a $20 contribution you become a registered user
         entitled to the resident version VPSRES and the latest versions of
         the other programs and documentation.

         You may not use these programs in a commercial environment or a
         government organization without paying a licesnse fee of $20.

         In any case, you are encouraged to provide any comments,
         suggestions, or problems to:

                                    S & S SYSTEMS
                                    P.O. BOX 1725
                                 CLAREMORE, OK 74018






                   This disk copy provided as a service of

                        The Public (Software) Library

                           the software library of
                     The Houston Area League of PC Users

         Program disks are available for as little as $2 each and a
         20-page monthly newsletter reviewing all the latest public
         domain and shareware software plus a listing of all the
         disks in our library is available for just $12 a year.

         For a copy of the latest monthly software library newsletter
         and program directory, send a self-addressed, stamped (with
         two stamps), legal-size envelope or send $1 to

                        The Public (Software) Library
                                P.O.Box 61565
                                   Dept. D
                              Houston, TX 77208