USING THE LASERJET/THINKJET PRINT SCREEN UTILITY
                          FOR THE IBM PC OR IBM PC/XT

The PRINT SCREEN utility allows you to print the contents of your
IBM PC or PC/XT display screen using the LaserJet or ThinkJet printers.
The PRINT SCREEN utility also operates with the HERCULES high-
resolution graphics board.

These instructions explain how to install and use this
utility.  Before performing the instructions, be sure to make a copy
of your current DOS disc so that you will have a backup available for
printing with other printers.  (When your operating system disc is
modified for use with the PRINT SCREEN program, it may not operate
with other printers.)  Notice that there are two sets of installation
instructions--one for LaserJet printers and one for ThinkJet printers.
If you have any problems, there is an "IN CASE OF DIFFICULTY" section
at the end of these instructions.

Now proceed to the installation instructions for your printer.


*************************
**LASERJET INSTALLATION**
*************************

The LaserJet printer is configured at the factory to communicate
at 9600 baud.  If you wish to increase the speed of
the PRINT SCREEN utility, you can set the printer's baud rate to
19200 by following steps a. through g. below.  If you wish to leave the
baud rate at 9600, skip to step h.

a.  Switch the LaserJet power switch to the OFF (0) position and
    remove the printer power cord from the wall socket.

         ____________________________________________________

                               WARNING

         Removing the back panel of the LaserJet printer can
         expose hazardous voltages--be sure the printer power
         switch is OFF and the power cord unplugged before
         removing the back panel.
         ____________________________________________________

b.  Remove the back panel from the LaserJet by removing the 4
    screws.

c.  Remove the vertical support at the center of the cabinet (1
    screw).

d.  Set the switches on switch bank #1 (SW1) to the following
    settings:

     1     2     3     4     5     6     7     8
    OFF   ON    ON    OFF   OFF   OFF   OFF   ON

e.  Replace the vertical support and the back panel.

f.  Plug in the printer power cord and set the printer power
    switch to the ON (1) position.

g.  Reboot the IBM PC or PC/XT by pressing the "Ctrl", "Alt", and "Del" keys
    simultaneously.  (If you have an IBM PC, your operating system (DOS) disc
    must be installed in drive A.)  NOTE:  If an error number 40 appears
    on the LaserJet display, press the CONT. key on the LaserJet Operator
    Control Panel--this is caused by booting up the computer while the
    printer is on-line.

h.  Copy the LASERJET.EXE file from the PRINT SCREEN disc to the operating
    system (DOS) disc.  To do this, follow the procedure below for your computer.
    (NOTE:  If you are using a HERCULES high-resolution graphics board,
    substitute HERCULES.EXE for LASERJET.EXE in this step.)

    For the IBM PC:

    1.  With your system (DOS) disc in drive A, load your PRINT SCREEN
        disc in drive B.

    2.  From the A> prompt, type:   COPY B:LASERJET.EXE A:   then Enter.

    For the IBM PC/XT:

    1.  Place your PRINT SCREEN disc in drive A.

    2.  From the C> prompt, type:   COPY A:LASERJET.EXE C:   then Enter.

i.  Next, you need to create or add some lines to your AUTOEXEC.BAT file so that
    every time you boot up your computer, the PRINT SCREEN program will
    automatically load.  To see if you already have an AUTOEXEC.BAT file
    on your system disc, type DIR and then Enter from the A> prompt (or
    from the C> prompt if you have an IBM PC/XT).  When you press the Enter
    key, a file directory listing will be printed on your display screen.
    Check the listing for an AUTOEXEC.BAT file.  If you do not see a file
    with this title, proceed to step j.  If you already have an AUTOEXEC.BAT
    file, do the following:

    1.  For the IBM PC:

        From the A> prompt, type:   EDLIN AUTOEXEC.BAT    then Enter.

        The screen will read "end of input file" and the * prompt will appear.

        For the IBM PC/XT:

        From the C> prompt, type    EDLIN AUTOEXEC.BAT    then Enter.

        The screen will read "end of input file" and the * prompt will appear.

    2.  For both the IBM PC and PC/XT, type L and then press Enter from the
        * prompt.  The contents of the AUTOEXEC.BAT file will be listed on
        your screen and the * prompt will reappear.

    3.  Notice that each line in the AUTOEXEC.BAT file has a line number
        to the left of it.  Add "1" to the largest line number in your
        AUTOEXEC.BAT file and type the resulting number, followed by an I,
        and then press the Enter key.  This step allows you to add information
        to the end of your AUTOEXEC.BAT file (see step 4).

        For example, if the largest line number in your AUTOEXEC.BAT file
        is 4, you would type 5I and then press the Enter key.  This would
        allow you to add information on line number 5.

    4.  Add the following lines to the AUTOEXEC.BAT file by typing
        the following (choose the correct baud rate--9600 is standard).
        (NOTE:  If you have a HERCULES high-resolution graphics board installed
        in your IBM PC or PC/XT, replace LASERJET A (or B) in the lines below
        with HERCULES A or HERCULES B (depending on the desired baud rate).

             For 9600 Baud

           MODE COM1:9600,N,8,1,P                    then Enter
           MODE LPT1:=COM1                           then Enter
           LASERJET A                                then Enter
           ^Z   (Hold the "Ctrl" key and press "Z")  then Enter
           (The * prompt will appear)

             For 19200 Baud

           MODE COM1:9600,N,8,1,P                    then Enter
           MODE LPT1:=COM1                           then Enter
           LASERJET B                                then Enter
           ^Z   (Hold the Ctrl key down and press Z) then Enter
           (The * prompt will appear)


           ___________________________________________________________

                                NOTE

           If there are any commands in the AUTOEXEC.BAT file for
           other screen dump programs (such as IBM "GRAPHICS"),
           remove them from the file.

           Some application programs may automatically load "GRAPHICS"
           or a similar program.  Such applications are not compatible
           with this PRINT SCREEN utility without modification to
           prevent them from loading "GRAPHICS".

           To delete a line from the AUTOEXEC.BAT file, type the line
           number you want deleted, followed by the letter d, and then
           press Enter.  For example, if you list your file and see that
           line number 3 loads a GRAPHICS program (which is
           incompatible with the PRINT SCREEN utility), you may delete
           that line by typing 3D and then pressing Enter.
           To return to the A> prompt, type END and then press Enter.
           ___________________________________________________________

    5.  Type END and press the Enter key to return to the A> prompt.


j.  If you do not already have an AUTOEXEC.BAT file on your
    system disc, type the following lines from the A> prompt (for IBM
    PC) or C> prompt (for IBM PC/XT).  This will create an AUTOEXEC.BAT
    file for you.  (If you have a HERCULES high resolution graphics board,
    type HERCULES A or HERCULES B in place of the LASERJET A (or B)
    below.)

                For 9600 Baud

        COPY CON: AUTOEXEC.BAT      then Enter  (no prompt will appear)
        MODE COM1:9600,N,8,1,P      then Enter
        MODE LPT1:=COM1             then Enter
        LASERJET A                  then Enter
        ^Z    (Hold the Ctrl key down and press Z) then Enter

                For 19200 Baud

        COPY CON: AUTOEXEC.BAT      then Enter  (no prompt will appear)
        MODE COM1:9600,N,8,1,P      then Enter
        MODE LPT1:=COM1             then Enter
        LASERJET B                  then Enter
        ^Z    (Hold the Ctrl key down and press Z) then Enter


k.  Reboot the system by pressing the "Ctrl", "Alt", and "Del" keys
    simultaneously.


*************************
**THINKJET INSTALLATION**
*************************

Perform the following steps to install the PRINT SCREEN utility:

a.  Switch the ThinkJet power switch to the OFF (0) position.

b.  Set the switches in the back of the ThinkJet printer as
    follows:

                   SWITCH 1                           SWITCH 2
         (Parallel & Serial Printers)            (Serial Printers Only)

     1    2    3    4    5    6    7    8      1    2    3    4    5
    DOWN DOWN DOWN DOWN DOWN  UP   UP  DOWN    UP  DOWN DOWN DOWN DOWN

c.  Switch the ThinkJet power switch to the ON (1) position.

d.  Reboot the IBM PC by pressing the "Ctrl", "Alt", and "Del" keys
    simultaneously.  (If you have an IBM PC, your operating system disc
    must be installed in drive A.)

e.  Copy the THINKJET.EXE file from the PRINT SCREEN disc to the operating
    system (DOS) disc.  To do this, follow the procedure below:
    (NOTE:  If you are using a HERCULES high-resolution graphics board,
    substitute HERCULES.EXE for THINKJET.EXE in this step.)

    FOR THE IBM PC:

    1.  With your system (DOS) disc in drive A, load your PRINT SCREEN
        disc in drive B.

    2.  From the A> prompt, type:   COPY B:THINKJET.EXE A:   then Enter.

    FOR THE IBM PC/XT:

    1.  Place your PRINT SCREEN disc in drive A.

    2.  From the C> prompt, type:   COPY A:THINKJET.EXE C:   then Enter.

f.  Next, you need to add some lines to your AUTOEXEC.BAT file so that
    every time you boot up your computer, the PRINT SCREEN program will
    automatically load.  To see if you already have an AUTOEXEC.BAT file
    on your system disc, type DIR from the A> prompt (or from the C> prompt
    if you have an IBM PC/XT).  When you press the Enter key, a file directory
    listing will be printed on your display screen.  Check the listing for
    an AUTOEXEC.BAT file.  If you do not see a file with this title, proceed
    step g.  If you already have an AUTOEXEC.BAT file, do the following:

    1.  For the IBM PC:

        From the A> prompt, type:   EDLIN AUTOEXEC.BAT    then Enter.

        The screen will read "end of input file" and the * prompt will appear.

        For the IBM PC/XT:

        From the C> prompt, type    EDLIN AUTOEXEC.BAT    then Enter.

        The screen will read "end of input file" and the * prompt will appear.

    2.  For both the IBM PC and PC/XT, type L and then press Enter from the
        * prompt.  The contents of the AUTOEXEC.BAT file will be listed on
        your screen and the * prompt will reappear.

    3.  Notice that each line in the AUTOEXEC.BAT file has a line number
        to the left of it.  Add "1" to the largest line number in your
        AUTOEXEC.BAT file and type the resulting number, followed by an I,
        and then press the Enter key.  This step allows you to add information
        to the end of your AUTOEXEC.BAT file (see step 4).

        For example, if the largest line number in your AUTOEXEC.BAT file
        is 4, you would type 5I and then press the Enter key.  This would
        allow you to add information on line number 5.

    4.  Add the following lines to the AUTOEXEC.BAT file.  (If your ThinkJet
        printer has a parallel interface, skip the first two lines [start
        with the THINKJET line].)  NOTE:  If you have a HERCULES high-resolution
        graphics board installed in your IBM PC or PC/XT, type HERCULES A
        in place of THINKJET in the lines below.

           MODE COM1:9600,N,8,1,P    then Enter  (serial interface only)
           MODE LPT1:=COM1           then Enter  (serial interface only)
           THINKJET                  then Enter
           ^Z   (Hold the "Ctrl" key and press "Z")  then Enter
           (The * prompt will appear)

           ___________________________________________________________

                                NOTE

           If there are any commands in the AUTOEXEC.BAT file for
           other screen dump programs (such as IBM "GRAPHICS"),
           remove them from the file.

           Some application programs may automatically load "GRAPHICS"
           or a similar program.  Such applications are not compatible
           with this PRINT SCREEN utility without modification to
           prevent them from loading "GRAPHICS".

           To delete a line from the AUTOEXEC.BAT file, type the line
           number you want deleted, followed by the letter d, and then
           press Enter.  For example, if you list your file and see that
           line number 3 loads a GRAPHICS program (which is
           incompatible with the PRINT SCREEN utility), you may delete
           that line by typing 3D and then pressing Enter.
           To return to the A> prompt, type END and then press Enter.
           ___________________________________________________________

    5.  Type END and press the Enter key to return to the A> prompt.

g.  If you do not already have an AUTOEXEC.BAT file on your
    system disc, type the following lines from the A> prompt (for IBM
    PC) or C> prompt (for IBM PC/XT).  This will create an AUTOEXEC.BAT
    file for you.  (If your ThinkJet printer has a parallel interface,skip
    the two lines beginning with MODE.  (If you have a HERCULES high resolution
    graphics board, type HERCULES A in place of THINKJET below.)

        COPY CON: AUTOEXEC.BAT      then Enter  (no prompt will appear)
        MODE COM1:9600,N,8,1,P      then Enter  (Serial interface only)
        MODE LPT1:=COM1             then Enter  (Serial interface only)
        THINKJET                    then Enter
        ^Z  (Hold the Ctrl key down and press Z)  then Enter


h.  Reboot your IBM system by pressing the "Ctrl", "Alt", and "Del" keys
    simultaneously.


USING THE PRINT SCREEN UTILITY

Once you have performed the installation procedure, the PRINT
SCREEN utility will be loaded every time you boot your computer.
To print the contents of the IBM PC or PC/XT display, read and then
perform the following two-step procedure:

a.  Press and hold the "SHIFT" key (key with upward-pointing arrow)
    and then press the "PrtSc" key.  After a 5-second delay, your display
    screen will be dumped to the printer.  Note that if the display is
    in Alpha mode, an "A" will flash in the upper left corner of the
    screen.  If the screen is in Graphics mode, a short horizontal line
    will appear in the upper left corner of the screen.

b.  You may select any of the options from the list below by pressing
    the key of the desired option within 5 seconds of pressing the "SHIFT"
    and "PrtSc" keys.  One option from each group (orientation, print
    positioning, or page ejection) may be selected.  Printing will begin
    5 seconds after the last key is pressed.  The Enter key may be
    pressed to terminate the 5-second delay.  NOTE:  If you select any
    of the options listed below, you do not have to select one from each
    group--those that are not specified will default automatically.

                        KEY              OPTION

ORIENTATION            * P -- PORTRAIT ORIENTATION  (LaserJet only)
                         L -- LANDSCAPE ORIENTATION (LaserJet only)

PRINT POSITIONING      * T -- TOP OF PAGE (PORTRAIT MODE ONLY)
                         M -- MIDDLE OF PAGE (PORTRAIT MODE ONLY)
                         B -- BOTTOM OF PAGE (PORTRAIT MODE ONLY)

PAPER EJECTION         * Y -- AUTO FORM FEED AT END OF PAGE
                         N -- NO AUTO FORM FEED AT END OF PAGE

           ENTER KEY -- TERMINATES 5-SECOND TIME-OUT PERIOD

     *  Default values

EXAMPLE:  To print a page of graphics, centered on the page, press
          the "SHIFT" key and "PrtSc" key, immediately followed by
          pressing the "M" key.  Your graphics will be dumped from
          the display and printed at the center of the page.

        ______________________________________________________

                            NOTE

        The PRINT SCREEN utility can print one graphics
        screen and one alphanumeric screen on the same
        page, but cannot print two graphics screens on
        the same page because of limited LaserJet memory.
        However, two graphs may be printed
        on the same page by printing one graph using the
        form feed option (to eject the page) and then manually
        feeding the same page through the printer to print
        the second page.
        ______________________________________________________


**********************************************************
**USING THE PRINT SCREEN UTILITY WITH THE HERCULES BOARD**
**********************************************************

If you have a HERCULES high-resolution board installed in your IBM
PC, the PRINT SCREEN utility operates almost the same as without
the HERCULES board.  The exception is that the HERCULES version does
not have the "C/W (Color/Black-White) option.  Instead, a "1/2" command
can be used to specify the first or second page of graphics memory on
the HERCULES board.  For example, to print the second screen (HERCULES
allows you to store two display screens), you simply press the "SHIFT"
key and "PrtSc" key, and then press the "2" key.  (NOTE:  Attempting to
print a large graphics image may cause the LaserJet graphics buffer to
overflow.  If this happens, elimination of graphics near the right side
of the page (borders, for example) may alleviate the problem.


*************************
**IN CASE OF DIFFICULTY**
*************************

If you have any problems printing a screen, be sure that the printer
is ready to print (the LaserJet printer must be on-line--ON LINE indicator
illuminated; the ThinkJet printer PWR light must be illuminated and the
yellow light [located below the blue box near the PWR light] must NOT be
blinking).  The IBM PC or PC/XT must be correctly configured for the
specified printer (LaserJet or ThinkJet).

If you are using a software package that automatically loads an
AUTOEXEC.BAT file, you may have problems with the PRINT SCREEN utility.
In this case, check to make sure that the AUTOEXEC.BAT file does not 
load another screen dump program, such as GRAPHICS.  If it does, you may
have to eliminate that line from the AUTOEXEC.BAT file to operate the
PRINT SCREEN program successfully.

        __________________________________________________________

                               NOTE

        Characters which can be printed on the IBM display screen,
        but are not part of the printer's available font, will not
        be dumped from the display as intended.
        __________________________________________________________

When using some software packages, the screen will not print as
desired.  In these cases, try the following options to enable you
to print the screen.  Use these options only after you have already
tried the PRINT SCREEN utility unsuccessfully.  These options are accessed
the same way as the other options (by pressing the key associated with
the option within 5 seconds of pressing the "SHIFT", "PrtSc" keys).


       KEY             OPTION

        A    -- ALPHA SCREEN DUMP
        G    -- GRAPHICS SCREEN DUMP

        C    -- COLOR GRAPHICS
        W    -- BLACK & WHITE GRAPHICS

        4    -- 40 CHARACTERS/LINE ALPHA
        8    -- 80 CHARACTERS/LINE ALPHA

For example, when printing a color bar chart using LOTUS 1-2-3,
you must first press "SHIFT", "PrtSc", and then "G"
and "C" (for color graphics).

If you have difficulty printing your display screen with a
particular software package, try the above options until the
screen prints correctly.


______________________________________________________________

IBM is a registered trademark of International Business
Machines Corp.

LOTUS and 1-2-3 are registered trademarks of Lotus Development
Corp.
______________________________________________________________