Program:            SETDEV.EXE     (DOS Version)
                    SETDEV2.EXE    (OS/2 32bit Version NOT YET RELEASED)
Version:            1.000
Description:        Set Device (Initalize Device)

Shareware pricing:  Single user license:          $ 10
                    Per server license:           $120
                    Internal corporate license:   $600
                    Distribution license:         CALL

<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<  NOTICE!! >>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>
SETDEV is a SHAREWARE product.  This means you are welcome to
distribute this program to your colleagues and friends.  If, after
30 days, you find yourself using SETDEV, a registration fee is
required.  For distribution licensing prices contact me at the address
below.
     
     Register your copy by sending check or money order to:
     (Print file ORDER.FRM for easy ordering)

               Kurt Kellner
               5313 S Tabor Way
               Littleton CO 80127

Custom software and modifications available upon request.  Comments are
welcome.  

          E-Mail address (Internet):  Kurt_Kellner@mail.amsinc.com
          Voice Mail:    1-800-543-5607 x4344

          To send me e-mail through CompuServe type 'INTERNET:'
          before the internet address when prompted for user name.
          (ie. INTERNET:Kurt_Kellner@mail.amsinc.com )

<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<<>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>>

ABOUT THE PROGRAM
-----------------

SETDEV is a program originally written to send landscape and compress codes
to a laserjet printer.  It expanded so that you could easily define a new
code without changing the program itself.  The next logical progression was
the ability to support multiple printers.

As it turns out, SETDEV has the ability to send any byte(s) to any device.
Output devices can include parallel ports (LPT1-LPTn), serial ports
(COM1-COM2), files (FILENAME.TXT), or any hardware device with a known I/O
address.

Some examples:      Send LANDSCAPE code to a laserjet printer.
                    Send COMPRESS code to an Epson printer.
                    Send AT commands to a modem.
                         - Send "ATM0" to modem (speaker off)
                         - Send "ATZ" to modem (reset modem)

You can define as many devices and as many commands as you would like.

SETDEV reads a file (SETDEV.INI by default) that defines all devices and
commands.  This is the format of the configuration (INI) file:

<<< START OF FILE >>>>
; Global commands
GLOBOL_COMMAND=CODE,CODE2

[DEFAULT_SETTINGS]
CMD_SETS=COMMAND_SET,COMMAND_SET2
DEFAULT_CMD_SET=COMMAND_SET
DEFAULT_DEVICE=LPT1
PORT_COM1=0x3f8,9600,8,n,1
PORT_COM2=0x2f8,9600,8,n,1

[DEVICE_NAME]
DEFAULT_CMD=!COMMAND
PRE_DEV_CMD=
POST_DEV_CMD=
COMMAND=CODE,CODE2,COME3,ETC
COMMAND2=CODE,CODE2

[DEVICE_NAME2]
DEFAULT_CMD=
PRE_DEV_CMD=
POST_DEV_CMD=
COMMAND=CODE,CODE2,COME3,ETC
COMMAND2=CODE,CODE2
<<< END OF FILE >>>>

Some definitions are needed to understand the SETDEV.INI file:

DEVICE              -    An output location.  (ie. LPT1-LPTn, COM1-COMn,
                         File, Hareware address)

CODE                -    A byte of data to be sent to the DEVICE.
                         A CODE can be: Decimal        65
                                        Hexadecimal    0x41
                                        String         "A"
                         CODEs are separated with commas.

COMMAND (External)  -    A named group of CODEs that can be sent to a
                         DEVICE.

COMMAND (Internal)  -    A named function SETDEV can perform internally.

COMMAND-SET         -    A named group of COMMANDs.




For example, say we want to send the LANDSCAPE command to a LaserJet
printer.  First we would need to create a COMMAND-SET section to put this
command.  Since the LANDSCAPE code for a LaserJet will work with all PCL
printers, let's call our command-set "PCL".  In the "PCL" command-set
section, we would define LANDSCAPE.  So far we have:

[PCL]
Landscape=27,38,108,49,79

Note, commands are NOT case sensitive.  CODEs are separated by commas. 
Let's add a few more commands:

[PCL]
Landscape=27,38,108,49,79
Reset=27,69
Return=0x0d,0x0a
Compress=27,38,107,50,83
FormFeed=0x0c
Test=!landscape,!compress,"This is a test",!return,"Line two",!formfeed

Note, if a CODE has a "0x" as the first two characters, it is assumed to be
a hexadecimal number.  Any text within quotes is sent byte for byte to the
output DEVICE.  The most important (and powerful) command to explain in the
above example is the TEST command.  Any CODE that has an exponential-mark
(!) is considered to be a EXTERNAL COMMAND.  External commands are defined
somewhere else in the INI file.  If we were to execute the Test command in
the above example, the first CODE is !landscape, SETDEV would look for the
definition of landscape in the INI file, this process is known as
dereferencing.

Let's move to another example.  You have a modem that you would like to send
AT commands (ie. ATM0).  Let's make a Command-set called "MODEM" and add a
few commands.

[MODEM]
Return=0x0d,0x0a
Reset="ATZ",!return,$tone:2000;2,$tone:4000;2,$echo "Modem has been reset."
SpeakerOn="ATM1",!return
SpeakerOff="ATM0",!return
Dial="ATDT 555-1234",!return,$delay:5000
Save="AT&W1",!return
 
This example presents a new command type called INTERNAL COMMAND.  As we
said before any command beginning with a exponential-mark (!) is an EXTERNAL
COMMAND, any command that begins with a dollar sign ($) is an INTERNAL
COMMAND.  Here is a list of the INTERNAL COMMANDs:




   Internal commands     Discription
   -----------------     ---------------------------------------------
   $echo:"text"          Echo text to display
   $clear_screen         Clears the text screen.
   $pause                Wait for any keystroke from user. (will auto-flush)
   $delay:ms             Wait for [ms] milliseconds (will auto-flush)
   $tone:p;d             Sound tone for p;d (pitch;duration)
   $flush                Flush codes to output device
   $run:progname         Run external program. (ie. $run:C:\COMMAND.COM)
                         If the directory is not given, the PATH will be
                         searched for program.  The file extention (COM, 
                         EXE, or BAT) MUST be included in program name.
                         NOTE: TSRs should NOT be loaded with this command!

To explain the $flush command, an understanding of how SETDEV works is
needed.  When SETDEV executes a command, any output CODEs (bytes) are
buffered until one of the following happens; the command is complete, the
$flush or $delay:ms command is encountered, or the buffer is full.

When sending codes to a printer, the $flush is not normally used, however,
when sending codes to a modem or other hardware device, it can be very
important to know exactly when the codes are sent. The $flush command gives
you that control.  Since the $delay:ms command is normal used for output
timing, it automatically calls the $flush command.

Text within quotes is sent byte for byte to the either the output device, or
to the display in the case of the $echo command.  There are three several
special cases to note when creating text.  They are:

\n        - Return
\t        - Tab
\xnn      - Hex number nn
\\        - The back-slash character
\"        - The quote character

To display the string C:\FILE.TXT with two returns afterward:

$echo:"C:\\FILE.TXT\n\n" 




Here is the MODEM command-set from the previous example with some changes:

[MODEM]
DEFAULT_CMD=!speakeroff
PRE_DEV_CMD=
POST_DEV_CMD=!return
Return=0x0d,0x0a
Reset="ATZ",!return,$tone:2000;2,$tone:4000;2,$echo "Modem has been reset."
SpeakerOn="ATM1"
SpeakerOff="ATM0"
Dial="ATDT 555-1234",!return,$delay:5000
Save="AT&W1"

Every command-set section has the option of having three special commands
defined.  These are:

   DEFAULT_CMD=code      This is the CODE(s) that will be executed if
                         no command was given.

   PRE_DEV_CMD=code      This is the CODE(s) that will be executed BEFORE
                         the user specifed command is executed.

   POST_DEV_CMD=code     This is the CODE(s) that will be executed AFTER
                         the user specifed command is executed.




In our last modem example, if SETDEV is used without a command, the
!speakeroff command will be assumed (DEFAULT_CMD=!speakeroff).  After EVERY
command that is sent from the modem command-set section, a !return will be
appended (POST_DEV_CMD=!return).  No prefix command was defined
(PRE_DEV_CMD= ).


If you look at both our [PCL] and our [MODEM] command-set sections, you will
see we defined "Return=0x0d,0x0a".   There are many commands that you might
needed defined for ALL command-sets.  GLOBEL commands can be defined by
placing them BEFORE any COMMAND-SETs.  For example:

;   Define GLOBEL commands 
Return=0x0d,0x0a
Sound=$tone:2000;2,$tone:4000;2
WaitASec=$delay:1000

[DEFAULT_SETTINGS]
CMD_SETS=PCL,MODEM,TEST
DEFAULT_CMD_SET=MODEM
DEFAULT_DEVICE=TEST.TXT
PORT_COM1=0x3f8,9600,8,n,1
PORT_COM2=0x2f8,9600,8,n,1

[PCL]
Landscape=27,38,108,49,79
FormFeed=0x0c
Test=!landscape,"This is a test",!return,"Line two",!formfeed

[MODEM]
Dial="ATDT 555-1234",!return,$delay:5000
Save="AT&W1",!return


The above example INI file show another new section named DEFAULT_SETTINGS. 
This section is used to define all command-sets and any default
configuration settings.  The DEFAULT_SETTINGS section has the following
commands:

CMD_SETS=PCL,MODEM            <--- Used to define ALL command-sets.
DEFAULT_CMD_SET=MODEM         <--- Used to define the default command-set.
DEFAULT_DEVICE=LPT1           <--- Used to define the default output device.
PORT_COM1=0x3f8,9600,8,n,1    <--- Used to define unique hardware devices.
PORT_COM2=0x2f8,9600,8,n,1



The PORT_x command in the DEFAULT_SETTINGS section is used to define unique
hardware devices that cannot be sent CODEs through DOS.  For example,
PORT_COM1=0x3f8,9600,8,n,1  defines COM1 at address 0x3f8 with 9600 baud,
eight data bits, no parity, and one stop bit.  If the COMn address is
specifed but the port parameters are left out, whatever the current settings
for the COMn port are will be used.  For example if COM1 was last used at
2400 baud and the line PORT_COM1=0x3f8 was placing in the INI file, output
to COM1 would use 2400 baud (current setting) to send output CODEs.

If the PORT is COM1-COMn the DSR (TR) signal is raised before any output is
sent to the PORT and is lowered again after all CODEs have been sent.  This
is the normal operation of a serial port.

Any hardware device can be defined.  For example, if data needed to be sent
to a digial I/O card, just define that card in the INI file as follows:
PORT_IOCARD=0x130.  Any output from SETDEV that is sent to "IOCARD" would go
to hardware address 0x130.  You can name hardware devices whatever you would
like.

HOW TO RUN SETDEV
-----------------
With a correctly configured INI file you can send commands with SETDEV as
follows:

SETDEV cmd     <--  This will look in the INI file for the "cmd" command in
                    the default command-set section.  It will send the CODEs
                    in finds to the default output device.

SETDEV landscape compress     <--  This will first send the "landscape"
                                   command then the "compress" command to
                                   the default output device.

NOTE:     To see exactly what is sent to the output device, and how the
          commands are being executed, use TRACE option.  This is a command
          line switch that will trace through commands as they are executed. 
          EXAMPLE:  SETDEV landscape compress /Trace  



You can change the default output device, command-set, and INI file name
with the following options:

Options: /Port=name         -  Output to port "name"
         /CmdSet=name       -  Command-set name to use
         /INIfile=filename  -  Use filename as alternate INI file

         /Trace             -  Trace (debug) command output
         /Quiet             -  Quiet mode (suppress screen banner)

NOTE:     You need only to use the CAPital letters when using an option. 
          For example, to change the default output device you could type
          /port=myfile.txt, or you could simply type /p=myfile.txt.  
 
SETDEV_ARG is an environment variable that SETDEV reads when it is run.  If
it finds this environment variable, SETDEV will append whatever options it
finds in the SETDEV_ARG variable to the command line options.  In other
words type "SET SETDEV_ARG=/Options" where /Options is the command(s) you
wish to use every time you execute SETDEV. For example, if you wish to use
the INI file MYFILE.INI everytime you run SETDEV, then type
"SET SETDEV_ARG=/INIfile=myfile.ini".

HISTORY
-------

1.000     Shareware release