INSTRUCTION MANUAL






                                           tm
                                    wsNOTE


                                note formatter
























                     (c)1991, Eric Meyer
                              3541 Smuggler Way
                              Boulder, CO  80303  USA



                                 ABOUT wsNOTE
                                 ------------


     wsNOTE is a small, fast, easily used program that enables you to produce 
numbered footnotes or endnotes with your WordStar program.  It has some 
additional formatting features as well.  wsNOTE is completely independent of 
WordStar, and requires no modifications to your present copy of it; yet wsNOTE 
can be run without ever leaving WordStar.
     Its advantages include:

* -  Simple,natural file format.  No strange embedded commands; no control 
    codes to conflict with your printer installation, or other software.
* -  Fast, one-pass operation produces either footnotes or endnotes from the 
    same source file; notes can be typed along with text or separately.
* -  Can also function as a simple numbering utility, for example, numbering 
    items in a bibliography.
* -  Figure Block feature offers space for illustrations without interrupting 
    the flow of text.
* -  Large documents may be split into separate files,which can be chained 
    together for output or processed separately.
* -  You have complete flexibility in format of note numbers and text.

     wsNOTE works on text files created with WordStar 3.3/4.0 or compatible 
programs (like NewWord).  The CP/M version runs on any CP/M or compatible 
(ZRDOS) computer.  The MSDOS version runs on any PCDOS or MSDOS computer 
(including IBM compatibles) with at least 128K RAM.




     This manual contains no special codes other than formfeeds.  It can be 
printed out, or examined onscreen with any editor.  It was written using VDE, 
a shareware program from the same author.



                               SHAREWARE POLICY
                               ----------------


     The wsNOTE program is "shareware", user supported software.  There is no 
initial obligation: feel free to give wsNOTE a thorough trial.  But if you 
decide to keep the program and to continue using it, this usage policy 
requires that you send a modest contribution of $25 (individual user) or $50 
(corporate site license) to the author:

           Eric Meyer
           3541 Smuggler Way                CompuServe [74415,1305]
           Boulder, CO  80303  USA


Mention the version of wsNOTE that you are using, and you will receive an 
update to the current version if revisions have been made.  Sorry, printed 
copies of this manual are not available from the author.


       ****************************************************************
       *****    The wsNOTE utility and its documentation are      *****
       *****     (c)1988-91 E. Meyer, all rights reserved.        *****
       *****   They may not be circulated in any incomplete or    *****
       *****     modified form, nor sold for profit, without      *****
       *****          written permission of the author.           *****
       ****************************************************************


     DISCLAIMER: You undertake to use wsNOTE at your own risk.  The author 
accepts no liability for any damages resulting from its use or misuse.  Direct 
problem reports and suggestions to the author; include a stamped return 
envelope for a reply if desired.





     NOTES: Please observe in what follows that "WordStar", "NewWord", and 
"Mailmerge", are trademarks of MicroPro International or NewStar Software.
     The wsNOTE program was formerly sold as a commercial product; it is now 
released as shareware by the author.



                               GETTING STARTED
                               ---------------


     The wsNOTE package should contain the following files:
          WSNOTE.EXE (or COM) - the wsNOTE program
          CONFIG.EXE (or COM) - a configuration utility
          SAMPLE.FIL - a sample text file to practice with

In addition there may be a READ.ME file, containing last-minute updates to the 
information in this Manual.  If so, TYPE or PRINT this file, or edit it with 
WordStar or VDE, to read it.  Eventually you will want to move WSNOTE, and 
possibly its CONFIG utility, onto your working WordStar disk (if there's room).

     wsNOTE is a "post-processor": it reads through a text file that you 
create with WordStar, and it creates a formatted file for you to print.  This 
means that wsNOTE consumes no memory, and will not interfere with your 
existing writing process.  The same input file may be processed to produce 
either footnotes or endnotes, as desired.  The output is a standard WordStar 
document file, and any other software (like indexing utilities) may be used on 
it prior to printing.
     You can convert existing documents for use with wsNOTE.  The easiest way 
is to replace all the note numbers with "##" signs, and collect all the notes 
in a separate ".XNT" file (see "EXTERNAL NOTE OPTION", below).


     This Manual is short; please read it thoroughly.  It covers:
        1.  How to create or modify text files for use with wsNOTE.  (You may       
           want to examine the file SAMPLE.FIL as you read this.)
        2.  How to run the WSNOTE program itself, to format and number your 
           notes, and proofread and print the output.
        3.  How to use the CONFIG program to take advantage of the many 
           formatting options of wsNOTE.

     You will need to be familiar with the use of WordStar itself on your 
computer, including the "dot commands" used by WordStar (and Mailmerge) for 
print-time formatting.  If you find yourself needing to refresh your memory on 
any of this, keep your WordStar manual handy as you proceed.
     The following instructions apply to both the MSDOS and CP/M versions of 
wsNOTE, and to the use of either WordStar or NewWord, identically.



                                 FILE FORMAT
                                 -----------


     First, you need to know how to type a note call in your text, the place 
where the note number should go.  Just type it as you always have, except that 
instead of an actual number like 17, type two or three "#" characters.  The 
number may be formatted in any way you like: in square brackets "[##]", or 
superscripted "^T##^T", etc. The "#"s will be replaced by the actual note 
number when you run WSNOTE.  Use of two "#"s gives note numbers up to 99; use 
three only if you expect you will need numbers larger than 99.
     Once you make your choices of format and number of digits, every note 
call in the file must be done the same way.  Any call that is not done exactly 
like the first will not be recognized.  (There is one exception: when you want 
the note number to reset to 1, as at the start of a new chapter, you may use 
"#1" instead of "##", or "##1" instead of "###".)

EXAMPLE:      Try the ^SwsNOTE^S^T#1^T program to format your notes.^T##^T

                            1                              2
RESULT:       Try the wsNOTE  program to format your notes.

     Second, you need to know how to type the actual notes.  They can be put 
after the end of any paragraph, either before or after their calls, though 
they should be reasonably close.  The natural place is at the end of the 
paragraph in which the calls occurred.  Keep the notes in the proper order, 
and remember not to try to put them into the middle of a text paragraph; they 
would not be recognized.
     Each note (or group of several notes) must be enclosed as a "note block" 
between the characters "{}" (curly braces), which distinguish a note block 
from a paragraph of ordinary text.  The "{" must be the first character on its 
line, and the "}" the last on its.  Neither brace will appear in the printed 
output; they are markers only.
     Each note within the block must have somewhere on its first line a number 
"##" or "###" with the same number of digits as the calls have. They may be 
formatted differently from the calls, but again all notes must be done the 
same way.  You can, for example, use "[##]" for the calls and "##." for the 
notes.  Use of "#1" and "##1" in the notes is allowed, if it helps you keep 
things straight, but is not needed, and has no effect.

EXAMPLE:      {    ##.  "wsNOTE" is a trademark of the author.
                  ##.  The program can produce either footnotes or endnotes,
              depending on your preferences.}


     EXTERNAL NOTE OPTION: Most users find note blocks integrated with the 
text to be easiest to use and keep track of.  However, if you prefer to type 
your notes in a separate file (or have already done so), wsNOTE has an 
"external note" option.  Don't put any note blocks in your text.  In the note 
file, just type in the notes as desired, with "##" in place of the numbers; 
don't use block markers ("{}").  Give the note file the same name as the text 
file, and the type ".XNT"; for "PAPER2" or "MAGAZ.ART", use "PAPER2.XNT" or 
"MAGAZ.XNT".  If an ".XNT" (external note) file is present, wsNOTE will 
automatically use it.


                                 DOT COMMANDS
                                 ------------


     When using wsNOTE, a few WordStar/Mailmerge dot commands should not 
ordinarily be used.  Others will operate somewhat differently than usual, 
because wsNOTE interprets them itself at formatting time, and may or may not 
pass them along to WordStar as well.  Also, two new ones are available.

     Dot commands that should usually not be used are: ".LH", which would 
change the vertical spacing of lines; ".PF", ".LM", and ".RM", which would 
cause print-time reformatting of text.  If wsNOTE encounters these commands, 
it will issue a warning message, but will keep going.  Thus you can use them 
if you really know what you're doing; but this is not encouraged, and page 
misalignment may result.
     (You should also avoid the formfeed character, ^PL.)

     Dot commands whose usage differs under wsNOTE are:
     ".PL", ".MT", ".MB" can each be used only once, at the beginning of your 
file, before any text, or page misalignment may result.  If used, they 
override any default set with CONFIG.
     ".CP" may not function as intended if the text it governs includes 
footnote calls, since the notes cause the page to fill sooner than expected.
     ".LS" will affect the spacing of the output text, but not the notes.  In 
particular, ".LS 2" will produce double spaced text, while the notes remain 
single spaced.  This (rather than typing with ^OS) is the recommended method.
     ".FI" should be used only at the end of a file, where it will chain to a 
new input file.  Don't specify a drive; the file will be sought on the same 
drive as the original one.  This is the easiest way to break up a large 
document.  For example, PART1.DOC might end with the line ".FI PART2.DOC".
     (Although ".LS" and ".FI" are Mailmerge commands, you don't need Mail- 
merge for them to work, because wsNOTE is processing them itself.)

     wsNOTE also has two new dot commands of its own:
     ".NN" (Note Number), sets the current note number the same way ".PN" sets 
page numbers.  This can be used to reset to 1 at the start of a chapter, or to 
synchronize numbers across multiple files.
     ".FB" (Figure Block), provides an extra feature which WordStar lacks.  
".FB nn" causes the next 'nn' lines of text (or blank space) to appear 
together on the next page, while the surrounding text continues to flow around 
normally.  Thus in contrast to ".CP", no premature page break occurs.  If you 
can't see immediately how this is useful, try it out!  This feature is used 
for printing tables intact, or setting aside space for an illustration to be 
pasted in, without interrupting the text in an unnatural way.  Figure blocks 
can be no larger than one page.
     (WordStar will of course not recognize ".NN" and ".FB" as valid dot 
commands; don't be disturbed by the "?" shown in the flag column.)



                                RUNNING wsNOTE
                                --------------


     Once you've done the work of writing your file, actually formatting it is 
easy.  You can do this either from the operating system prompt, or from within 
WordStar via the Opening (No-File) Menu "R" command.  If you've never used the 
"R" command, now is the time to discover it.  It allows you to run nearly any 
command or program, without exiting from WordStar.  At the Opening Menu, type 
"R".  WordStar asks "COMMAND?", and you simply type in the name (followed by 
any required arguments) and press <RETURN>.  When the program is finished, the 
message "Hit any key to return to WordStar" will appear; doing this brings 
back the Opening Menu.
     In either case, WSNOTE takes two arguments.  The first is your text 
filename, and is required.  Include the drive, if different from the current 
drive.  The second is an optional flag "-e", if you want endnotes; omit it if 
you want footnotes.

EXAMPLES: (from DOS, with endnotes)          A>wsnote b:sample.fil -e
          (from WordStar, with footnotes)    COMMAND? wsnote sample.fil

     There must be enough free space on the disk in use for another complete 
copy of your document.  Remember to add together the sizes of any files you 
are chaining together, and add a few extra K just to be safe.  When wsNOTE 
stops, there will be a new file on the disk, with the same name as the (first) 
input file, but the type ".PRN".  (SAMPLE.FIL will produce SAMPLE.PRN.)  This 
is the formatted output, all set to print using WordStar's "P" print command.
     It is wise to make a habit of proofreading the ".PRN" file before 
printing it, in order to check the page layout.  Edit it in "D" (document) 
mode, and scroll through it at will.  But remember, to make corrections you 
should edit your source file, then run wsNOTE again.  Make changes directly in 
the ".PRN" file only when needed to get it to print the way you want; and 
never do anything resulting in a net change of the number of lines.  This 
would cause pages to become misaligned in printing.  (Make sure WordStar's 
page break indicators agree with the wsNOTE "..page" markers.)
     If you selected endnotes ("-e"), there will be a second output file with 
the type ".NOT", containing your notes.  It is also a document file, but may 
be edited or reformatted as you like before printing.  (You may, for example, 
want to insert a ".PN" command to get the right page numbering.)



     NUMBERING OPTION: It is also possible to use wsNOTE to simply number 
items in a list, for example a bibliography.  Just enter the usual "##" (or 
"###") for the number of each item, making sure that all are formatted exactly 
the same way.  Then run WSNOTE on the file, with the option "-n":

EXAMPLE:            COMMAND? wsnote bibliog.104 -n

The numbering will proceed sequentially from 1 (unless modified with "##1" or 
the .NN command).  Other wsNOTE features (such as figure blocks) also remain 
active.  The output file will have the type ".PRN".



                                  USAGE TIPS
                                  ----------

     Make sure that you either (1) use CONFIG to set the page length, top and 
bottom margins in wsNOTE to agree with the defaults you have installed in your 
copy of WordStar, or (2) always put ".PL", ".MT", and ".MB" commands at the 
top of your file.  Otherwise wsNOTE and WordStar won't agree on the page 
format, and pages will get misaligned.

     Follow the "FILE FORMAT" instructions exactly.  If a note call or number 
is not done correctly or consistently, wsNOTE won't recognize it, and notes 
may start getting mismatched, or an error may occur.  If a note block is not 
correctly marked off, it will appear to be missing, or not to end, and an 
error will result.
     Be careful if you "block move" a note block, to be sure that it still 
stands as a paragraph: begins after, and ends with, a hard carriage return.
     If you use right justified text, don't use three "###" signs unless you 
will need numbers over 99.  The extra one will add an unnecessary space.

     wsNOTE features don't "nest": you can't put dot commands, note calls, or 
note blocks inside of other note blocks or figure blocks.

     The .LS command is the easiest way to produce double-spaced text.  The 
alternative, multiple line spacing with ^OS in WordStar, can cause problems in 
the spacing of notes, and is not recommended.  If you must use ^OS, be sure 
that only a single <RETURN> precedes and follows each note block.

     If you want a blank line between each note in your output, insert an 
extra <RETURN> after every note in the source file.  Remember to do this for 
the last note in each block, too (before the closing "}"), or some notes will 
not be spaced properly.

     There are two ways to handle a document consisting of multiple files.  
First, you can chain the files together with a ".FI" at the end of each.  This 
will produce a single ".PRN" file, with the name of the first input file.  (If 
you are using external notes, they must also be in a single ".XNT" file with 
that name.)
     Alternatively, you can process each file quite separately.  At the start 
of each file, you can use the ".PN" and ".NN" commands to synchronize the page 
and note numbers.  This is best if a single output file would be unwieldy.

     Problems can occur in printing the ".PRN" file, if a page ends while an 
alternate print mode (underlined, compressed, etc) is in effect.  For example, 
the footnotes and next page header may also print in that mode, or the text 
may fail to return to it on the next page.  In this event you will need to 
stop the printing, edit the ".PRN" file, and manually insert extra print codes 
where needed to correct the problem.  Then print out the offending pages 
again.  Be careful not to insert or delete any lines in the process, or pages 
will become misaligned.

     The smaller the capacity of your disk drive, the smaller you should keep 
your text files.  WordStar always makes temporary and backup files; this can 
quickly fill up a small floppy disk.  Delete ".BAK" files when you can, and 
".PRN" files once they're printed.


                                 USING CONFIG
                                 ------------


     The CONFIG utility offers you a number of quick, useful ways to customize 
the use of wsNOTE to suit your tastes, or the requirements of a style manual.  
Most people will only need to run CONFIG once.  If you often have to use 
different styles, you will need to either keep CONFIG on your disk with WSNOTE 
or set up several different copies of WSNOTE.
     CONFIG takes a single argument, the name of your wsNOTE program.  (In- 
clude the drive if it's not the current drive.)  Again, CONFIG may be run from 
either the system prompt or the "R" command in WordStar.

EXAMPLE:        COMMAND? config wsnote.exe
 
     You will see a menu of all the parameters you can change, which are 
described below, and their current values.  Type the menu letter of the one 
you wish to change, then enter the desired value.  When you're through, hit 
<RETURN> to save your changes, or type ^C to abort without saving.  This copy 
of WSNOTE.EXE (or COM) will be modified as you chose.
     Read this list now, to familiarize yourself with the control you have 
over the appearance of the printed output.  The choices, in order, are:


     A: note number character.  The default is "#".  If you want or need to 
use a different character to designate note numbers, you may.

     B,C: note block delimiters.  The defaults are "{}".  Again, if you 
prefer different characters you may change these.

     D,E: note line character, length.  The character to use for the note 
separator line between text and footnotes (D), and how long the line should 
be (E).  Defaults are "-", 20 characters.  You may prefer "~", "_", etc, or 
a longer line.  If you want no line, set the length to 0.

     F,G: blank lines before, after line.  These are the number of lines you 
want to skip before and after the note separator line.  Defaults are 1 line 
before (F), and 0 after (G).

     H: minimum lines for note start.  Setting this to "n" means that if 
there is not room on the page for the first "n" lines of a footnote, the 
note will be postponed to the next page.  Default is 1 (no postponement).

     I,J: printer codes for notes.  You can get your notes to automatically 
print in a different mode from the text (such as compressed), if you want.  
Enter the WordStar control code you've installed to turn on the printer mode 
desired for the notes (I), and the one to return to your text mode (J).  
These might be, for example, ^Q and ^R; type these codes in directly.
     If you use a print mode with a different character width, be sure to 
format your note blocks with appropriately adjusted margins, so their prin- 
ted width will match that of the text.
     Defaults: no codes.  (This displays as "none", and may be entered from 
the keyboard by typing <RETURN> alone.)


     K: physical page length.  This is the number of lines on a page.  Set
it to agree with whatever you have installed in WordStar.  This setting is 
overridden by the .PL command, if used.  Default: 66 lines (for ordinary 11" 
paper, 6 lines per inch).

     L,M: top, bottom margins.  Again, set these to agree with the defaults 
you have installed in WordStar.  These settings will be overridden by the 
commands .MT or .MB, if used.  Defaults: 0 lines top, 0 lines bottom.

     N: new page resets to note 1?  To change this, enter "Y" or "N".  If 
you set this to "Yes", the first note number on each page starts over again 
at 1.  Default: "No", note numbers continue to increment.

     O: notes up on short pages?  Enter "Y" or "N".  Ordinarily "No", and 
footnotes always print at the very bottom of the page.  If set to "Yes", on 
a partly filled page, notes (if present) print up right under the text.

     P: avoid widow text lines?  Enter "Y" or "N".  Ordinarily "No"; if you 
set this to "Yes", wsNOTE will avoid beginning a paragraph on the last line 
of a page (it will begin on the next page instead).

     Q: right justified text?  Enter "Y" or "N".  Ordinarily "Yes", and 
extra (soft) spaces are inserted where necessary to preserve justification 
(for example, after one-digit note numbers).  Set to "No" to avoid these 
extra spaces in unjustified text.

     R: buffer size in K.  There are four buffers in wsNOTE, each of this 
size (default: 6K).  The minimum is 2K.  If you start getting "buffer over- 
flow" error messages from wsNOTE, increase this size.  If you get "buffers 
exceed available RAM", decrease it.




                                CONFIG ERRORS

     CONFIG modifies the actual WSNOTE.EXE file.  This cannot be done if the 
disk WSNOTE is on is write-protected, or Read/Only.  In such cases, a BDOS 
Error message will appear, and the changes will not be made.
     Note that CONFIG will refuse to save if you have specified a buffer size 
below 2K, or a page length that's too small for the margins.  Correct the 
offending value(s) and try again.

     In addition, two error messages may appear when you try to run CONFIG:

"can't open input file" - The name you gave for your wsNOTE program doesn't 
  exist.  Either it's misspelled or incomplete, or it's on another drive.

"can't CONFIG that file" - The file exists, but it either isn't wsNOTE, or 
  isn't the correct version.



                                ERROR MESSAGES
                                --------------


     Every effort has been made to trap and identify errors neatly.  When an 
error causes wsNOTE to abort formatting, the output file(s) will of course be 
incomplete.  Take a look at the end of the ".PRN" file, to get an idea of 
where in your source file the problem occurred.  Then refer to this alpha- 
betical list, for some suggestions as to the likely cause.


"bad dot command argument" - The number following a dot command appears to 
  be invalid or missing.

"bad figure block" - A figure block was still being read in when the end of 
  your file was reached.  Either some of its text is missing, or you need to 
  decrease the number of lines in the ".FB" command.

"bad note block" - A note block was still being read in when the end of your 
  file was reached.  This means the note block is not terminated properly 
  with "}", <RETURN>.

"bad option specified" - The only thing allowed on the command line after 
  "WSNOTE INPUT.FIL" is "-E" or "-N".  You typed something else.

"buffers exceed available RAM" - Your computer doesn't have room for four 
  buffers of the current size.  Use CONFIG to decrease your buffer size.  
  The maximum under CP/M will be about 10K; under MSDOS, about 15K.

"can't open file" - The file specified in a ".FI" command can't be found.  
  There is an error in the filename, or you tried to specify a drive.

"can't open input file" - The file you gave on the wsNOTE command line can't 
  be found on the current (or specified) disk.  Did you misspell it, or is 
  it on a different disk?

"can't open output file" - wsNOTE can't write its output on the current (or 
  specified) disk.  Either it's read-only, or its directory is full.  (This 
  error can occur if your input file has the type ".PRN" or ".NOT", which 
  you should avoid.)

"figure block exceeds page" - A ".FB" command has requested a figure block 
  larger than the current number of free lines on a page.  Decrease the 
  header and bottom margins, or make the figure block shorter.

"figure buffer overflow" - The text of a figure block filled the available 
  buffer.  Decrease the amount of text in the block, or use CONFIG to 
  increase your buffer size.

"foot buffer overflow" - The text of footnotes already scheduled to print 
  has filled the available buffer.  Don't call so many notes from a single 
  page, or make them shorter, or use CONFIG to increase your buffer size.


"missing note block" - A note block was still being searched for when the 
  end of your file was reached.  Either some notes are missing, or there are 
  too many calls in the text.

"no file specified" - You didn't give wsNOTE the name of your text file, so 
  it couldn't even get started.

"no note in buffer" - The contents of a note block don't look like notes, 
  because there is no proper "##" number on the first line.  There is 
  probably a simple error in its format.  The same error in a subsequent 
  note in the block will cause it to become part of the preceding one.
     In external note mode (with an ".XNT" file), this message indicates 
  that there weren't enough notes in the file for all the calls in the text.

"note buffer overflow" - Your note block appears to be too long to fit in 
  the note buffer.  Probably, the block isn't terminated properly with "}", 
  <RETURN>.  Possibly you've left out some calls, and so have too many 
  notes.  If your notes are simply too large, or you've put in too many 
  before their calls, you need to increase your buffer size with CONFIG.
     In external note mode (with an ".XNT" file), this message means that 
  one single note was too large to fit in the buffer.

"page align error" - This is very unlikely.  It indicates that wsNOTE can't 
  cope with the combination of page length, header and bottom margins that 
  you have set with CONFIG, which must be pretty strange.

"source line too long" - There appears to be a line in the text file that 
  exceeds the maximum length, currently 256 characters.  You probably forgot 
  to reformat a paragraph.

"text buffer overflow" - While looking ahead to find a note block, the text 
  buffer filled up.  You need to put this note block closer to the point in 
  the text where it was called, or to increase your buffer size with CONFIG.

"[Warning: extra notes]" - This is only a warning.  wsNOTE has finished, but 
  there still seem to be unused notes.  Probably you left out a call in the 
  text, and the following notes may all be mismatched as a result.  Proof- 
  read the output carefully.
     In numbering ("-n") mode this error means that a note block was found.

"[Warning: found .XX]" - This is only a warning; formatting does not stop.  
  You have used a dot command that is not recommended, and will likely cause 
  misaligned pages in your printout.  Abort wsNOTE with ^C if this was a 
  mistake.  Proofread the output carefully.

"[Warning: multiple spacing]" - This is only a warning.  wsNOTE has found 
  text that was multiple-spaced with ^OS.  This may cause spacing problems 
  in the notes.  Proofread the output carefully.



                                    [END]

                        wsNOTE Manual Rev. 1.35b (03/91)

         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 3,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                 Orders only:
                                1-800-2424-PSL
                              MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.