D51 8051/8052 Disassembler - Copyright 1990 by Jeffery L. Post
Version 1.0 - June 24, 1990
Version 1.1 - Aug 4, 1990

    D51 is a cross disassembler for MSDOS machines. It generates an 8051
assembly source code file from either a binary file or an Intel hex file.
The executable code for D51 is public domain. The C source code for this
program is NOT public domain but may be purchased from the author for
personal or educational use only. To obtain the C source on a standard
360K MSDOS 5 1/4" diskette, send $10 cash, check, or money order to:

        Jeffery L. Post
        22726 Benner Ave.
        Torrance, CA  90505

The executable program may be freely distributed through public domain
channels (bulletin boards, PD software houses, friends, etc) provided
this documentation file is included.

    Command line format is: d51 filename [options]. The filename should
be entered without an extension. The default extension is HEX. If the 'b'
(binary file) option is used, the default extension is BIN. The 'd' (data)
option will append a comment field to each assembly line consisting of the
address of the instruction and hex and ascii representations of the code
byte(s). Option entry is freeform: 'db' 'd b' '-bd' '-b -d' all mean the
same thing.

    Version 1.1 - Now allows user to specify a hexadecimal offset to be
added to the program data. This is done by using the 'x' option on the
command line, ie: 'd51 file -d b x100'. The hexadecimal offset (100h in
this example) will be added to all data read from either a .bin or .hex
file. While this is not very useful when applied to a .hex file, it may
be of critical importance in some .bin files (for example: a program for
a single processor contained in two or more eproms). If used, the x option
must be the last specified in the command line.

    D51 does three passes over the code being disassembled. The first pass
searches for opcodes that reference program locations (such as jumps and
calls) so that labels may be generated in the source listing. Pass two does
the actual disassembly and writes source lines to the output file. Pass three
then searches for references to locations outside of the initialized program
space or to locations that lie in the middle of opcodes and generates equate
statements for them.

    All three passes display the 'current pc' as they do their work. Despite
the three pass design of D51, it is a very fast disassembler. It will dis-
assemble an 8K binary file, outputing a 58K assembly source file, in about
20 seconds on an 8 MHz machine.

    D51 is an 'intelligent' disassembler. Since uninitialized space in a
program will normally be filled with either 0 or 0ffh, blocks of such data
will not be disassembled as page after page of NOP or MOV A,R7. They will
be skipped over and an ORG statement will be inserted in the assembly output
when the next initialized code is encountered.

    References to special function registers will generate names for the
appropriate register, ie: 75 98 20 will be disassembled as 'mov scon,#20h'
instead of just 'mov 98h,#20h'. Likewise, references to sfr bits will
produce names: C2 AF disassembles as 'clr ea', not 'clr ie.7'. As a conven-
ience to 8051 programmers, direct references to registers generate names
for the register. For example, F5 12 becomes 'mov rb2r2,a' to indicate r2
of register bank 2 at address 12h. This obviously requires that the programmer
add an equate statement to the file before sending it back through an 8051
cross assembler.

    Not all cross assemblers recognize the additional special function
registers of all 8052 family members. Since D51 generates the proper sfr
name for all family members known to the author, the programmer may have
to add some equates defining such sfrs, ie:
        t2con   equ     0c0h
        csr     equ     0e8h
and equates for the bits in the additional sfrs:
        tf2     bit     t2con.7
        mb0     bit     csr.6

    Despite all it's wonderfulness, D51 does have some drawbacks. Chief among
them is that it does not try to analyze program flow, and therefore cannot
tell the difference between valid executable code, data tables, and/or ascii
data. This can lead to some strange looking disassembly when ascii data or
address tables are encountered. The 'd' option is useful for identifying such
problems.

    Comments, suggestions, bug reports, praise, or diatribes of any kind may
be sent to the author at the address given above.




         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 2,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                                 MC/Visa/AmEx

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.