DZ80 Z80 Disassembler - Copyright 1990 by Jeffery L. Post
Version 1.0 - Aug 22, 1990

    DZ80 is a cross disassembler for MSDOS machines. It generates a Z80
assembly source code file from either a binary file or an Intel hex file.
The executable code for DZ80 is public domain. The C source code for this
program is NOT public domain but may be purchased from the author for
personal or educational use only. To obtain the C source on a standard
360K MSDOS 5 1/4" diskette, send $15 cash, check, or money order to:

        Jeffery L. Post
        22726 Benner Ave.
        Torrance, CA  90505

The executable program may be freely distributed through public domain
channels (bulletin boards, PD software houses, friends, etc) provided
this documentation file is included.

    Command line format is: DZ80 filename [options]. The filename should
be entered without an extension. The default extension is HEX. If the 'b'
(binary file) option is used, the default extension is BIN. The 'd' (data)
option will append a comment field to each assembly line consisting of the
address of the instruction and hex and ascii representations of the code
byte(s). Option entry is freeform: 'db' 'd b' '-bd' '-b -d' all mean the
same thing. The 'x' option specifies a hexadecimal offset to be added to
the program data. This is useful when disassembling CP/M com files, among
other things. If used, the x option must be the last specified in the
command line.

    DZ80 does three passes over the code being disassembled. The first pass
searches for opcodes that reference program locations (such as jumps and
calls) so that labels may be generated in the source listing. Pass two does
the actual disassembly and writes source lines to the output file. Pass three
then searches for references to locations outside of the initialized program
space or to locations that lie in the middle of opcodes and generates equate
statements for them.

    All three passes display the 'current pc' as they do their work. Despite
the three pass design of DZ80, it is a very fast disassembler. It will dis-
assemble an 5K binary file, outputing a 37K assembly source file, in about
14 seconds on an 8 MHz machine.

    DZ80 is an 'intelligent' disassembler. Since uninitialized space in a
program will normally be filled with either 0 or 0ffh, blocks of such data
will not be disassembled as page after page of NOP or RST 38h. They will
be skipped over and an ORG statement will be inserted in the assembly output
when the next initialized code is encountered.

    Despite all it's wonderfulness, DZ80 does have some drawbacks. Chief among
them is that it does not try to analyze program flow, and therefore cannot
tell the difference between valid executable code, data tables, and/or ascii
data. This can lead to some strange looking disassembly when ascii data or
address tables are encountered. The 'd' option is useful for identifying such
problems.

    Comments, suggestions, bug reports, praise, or diatribes of any kind may
be sent to the author at the address given above.