-------------------------------------------
                  KBDINT - A KEYBOARD INTERRUPT DEMONSTRATION
                  -------------------------------------------

In recent days, I've been trying to write an Interrupt Service Routine (ISR)
for the keyboard interrupt INT 9, which will respond to a keypress of any key 
on the keyboard, including [Caps Lock], [Num Lock] and [Scroll Lock].

After several attempts, using snippets of code from books, I discovered that
the code cited in all the books I had referred to, would not work for the
[Caps Lock], [Num Lock] and [Scroll Lock] keys (on my computer at least).
My computer would either just lock up and not respond to any keypress - 
requiring a cold boot - or the ISR would act in a way I didn't expect - in 
my particular case, a variable, which should have been incremented only once, 
was incremented eight times.

I concluded that the original ISR, which must be called by my own ISR (to
prevent a system crash !), probably executes the INT 9 instruction when the
[Caps Lock], [Num Lock] or [Scroll Lock] key is pressed.  So I adjusted the
code of my own ISR to allow for this.

Thinking that it might be of interest to others how I did this, I decided to
write a small program to demonstrate the results of each of the three
versions of my ISR.  The main purpose of the ISR is to increment (once) the
variable 'bKbhit' in the main program, each time a key is pressed.  The main
program, in this case however, exits after one keypress.

KBDINT.EXE uses the successful version.  To run it just type KBDINT.
To see how KBDINT works with the other versions just change line #26 of 
KBDINT.ASM:

from
INT09_ROUTINE   =       INT09_RIGHT
to
INT09_ROUTINE   =       INT09_WRONG1
or
INT09_ROUTINE   =       INT09_WRONG2

and re-assemble and link.  It would be easiest to reassemble and link using 
the included makefile, KBDINT.MAK, and MAKE version 3.6 or later, with the
command:

make -f kbdint  (for earlier versions use: make -fkbdint)

If you replace INT09_RIGHT with INT09_WRONG1 in the equate above, you'll have
to cold-boot your computer (I had to cold-boot mine anyway).  If you use
INT09_WRONG2 in the above equate, the system doesn't crash, but you must wait
about a minute for the program to end and return control back to DOS.

The output displayed by KBDINT is identical using all three versions of the
int 9 ISR (all named Int09) unless the [Caps Lock], [Num Lock] or
[Scroll Lock] key is pressed.  That is:

The old interrupt address was: XXXXH:XXXXH
The new interrupt address is : XXXXH:XXXXH
Press any key...
'bKbhit' variable was incremented 1 time(s).
The interrupt address is restored to: XXXXH:XXXXH

With INT09_ROUTINE set to INT09_RIGHT, the output is the same as above when  
the [Caps Lock], [Num Lock] or [Scroll Lock] keys are pressed.  However, when
set to INT09_WRONG1, the system locks up at line 3 (Press any key...).  When
set to INT09_WRONG2, line 4 (on my system) changes to:

'bKbhit' variable was incremented 8 time(s).

If there is anyone who might have some better ideas for making a better ISR
for the keyboard interrupt 9, or if you just want to make some comments or
ask some questions, please contact me via CompuServe Mail.

My CompuServe ID number is:     1000236,2477


ABOUT ASMS.LIB
--------------
KBDINT.ASM includes some procedures in ASMS.LIB - a library of procedures
(for the small memory model) which I wrote, and which I have frequently found
useful in my programs.  If you would like a description of how to use these
procedures, or the original source code, I would be happy to send it to you
via CompuServe Mail, but I'll probably have to charge a small fee for the
service (sorry - but I have to try to make a living from writing my 
programs).  A complete list of the procedures is in ASMS.LST.