;Video routine short instruction list

========================================================================
    Copyright (C) Copr. 1990 by Sidney J. Kelly
            All Rights Reserved.
            Sidney J. Kelly
            150 Woodhaven Drive
            Pittsburgh, PA 15228
            home phone 412-561-0950 (7pm to 9:30pm EST)

     CompuServ   70043,1656
     Genie       S.KELLY8

========================================================================

          The following routines are designed to do something
useful to text without regard to the type of monitor actually
installed.  These routines are text mode primitives.  In most
cases that give you direct control over the hardware in a fashion
that cannot be done except in assembly language.  You can save
the display, write characters or attributes at high speed to the
display, or write to the display using DOS compatible modes to
allow you to use multi-taskers or ANSI.SYS.  You can change text
or attributes on the display.  You can adjust cursor size, turn
off blinking, BLOAD help files, etc.
          These routines are part of a larger freeware library of
QBASIC routines that is currently under construction.  The full
version will be released two days AFTER an OOPS version of QBASIC
is released by MICROSOFT-- at which time few will want to use
these routines.
          Why these were written:
          I originally wrote these routines to parrot Dick Evers
window routines written exclusively in BASIC (You can see his
influence in the demo program).  Then an old issue of PC Magazine
showed how to call MASM video routines from QBASIC, which I think
is based on an earlier BYTE magazine article.  Other PC Magazine
routines, and the discussions about IBM Technical reference video
adapter recognition routines, showed how to identify display
types using just BIOS calls.  Then the quest began: I began my
search of back issues of PC Magazine for programming tidbits, I
bought old assembly language guide books back with the earth was
fresh and the IBM PC with 64kb of memory and two floppies was a
wonder to behold, searched the standard databases for public
domain routines; read more programming books, etc.  The
bibliography at the end of this document should answer your
requests for additional information.
          The video display was selected for improvement because
that is one area a user can really notice the difference between
fast code and slow code.  Some of these routines allow you to do
things that are impossible otherwise.  Other routines allow you
to do something much faster and in an attractive fashion.  All
the routines avoid the agony of using ON ERROR GOTO traps.
          Programmers Assumptions:
          These routines are designed to work with MONO, CGA,
HERC, MCGA (mostly color, though generally untested), EGA (mono
or color, 25 or 43 line mode), and VGA (mono or color, 25 or 50
line mode).  In a very limited way, the routines support dual
displays.  These routines assume that the display width is 80
columns wide, mostly because there is no known way to determine
in advance if a particular user's display will support 132 column
mode.  Anyway that is QBASIC's assumption too.  More importantly
I don't own a multi sync display, and I do not access to 10 types
of EGA and 50 types of VGA displays that are necessary to test
everything out on.  Finally, there are several shareware
libraries that already have some of the ATI, Paradise, VESA and
Video Seven EGA/VGA routines built in.  Unfortunately, after
looking at the freeware version of FRACINT (a nifty graphics time
waster that draws fractals), it appears that there are about five
or six different ways to switch displays into high resolution
mode.  Even FRACINT requires the user to select the display type.
(How can I convince my wife that I need a register compatible
8514/A display and adapter for the ultimate in text mode
displays??????????).
          It is possible to devote many hours to routines for
hardware 95% of the users wont have or need in text mode.  Most
of the direct screen routines use macros that are hard coded for
an 80 column width display. (Lengths of 25, 43, and 50 are
allowed).  This is done for speed in case the poor user only has
a CGA on a PC clone (he needs all the speed he can get).  To show
how it is done, I have included a few routines that actually do
use the BIOS ram data areas to determine the current display
width.
          QBASIC Theory.
          Aside from the current DEF SEG setting, most of QBASIC
video information storage registers are not available inside the
QB.EXE environment, though it is available inside the .EXE
program (which makes testing the routines way too time
consuming).  My routines had to come up with such information
independently.  My solution is store the key variables in the
default data segment in QBASIC (its name in MASM is DGROUP).  To
save space in DGROUP, only 7 bytes of information is kept by the
video routines.  This allows transparent sharing of the
information.  The reason for such "stupid" names (B$V...) for the
DGROUP variables is to only give the MASM routines access to such
information, and prevent normal QBASIC routines (or someone
else's library routines) from messing them up.
          Generally QBASIC only keeps simple variables, (INT,
LONGINT, SINGLE and DOUBLE, and STRINGS) in DGROUP.  Arrays and
TYPE records are usually kept outside DGROUP, with only the
STRING Descriptor or the undocumented Array descriptor kept in
DGROUP.  Thus, the library routines assume that all information
passed from simple variables is information about a near (DGROUP)
address.  If we pass simple integers to MASM routines, and don't
care to have MASM change those variables, we use BYVAL to send
the information to MASM.  If we want to have MASM send
information back about multiple variables, we pass the address
information for the variables without using BYVAL.  If we use
arrays, we must use a combination of BYVAL and VARSEG and VARPTR
to get the information we need to manipulate the information
inside the arrays.  VARSEG and VARPTR are necessary because there
is a very great chance that the arrays will be stored as far data
(i.e. not stored in DGROUP).
          Text strings are sent by QBASIC as near address
(relative to DS and DGROUP).  The fist value in the descriptor is
the length of the string.  The second value is the offset address
inside DGROUP.  Fixed length strings are not referenced with
string descriptors.  For that reason, I don't allow such strings
as variables in my routines.
          QBASIC requires that MASM preserve BP, SI, DI, DS, and
keep the direction flag clear (CLD).  All these routines do this.
You will note that MICROSOFT'S CALL INTERRUPT routines do not
save BP (apparently to give you access to some EGA VGA palette
and character font selection routines in the BIOS), and thus will
crash if a critical error occurs.  MICROSOFT offers a replacement
routine, that overcomes this error by preventing any change to
BP.  You should get it if you don't already have it.
          The choice of defining MASM routines as SUB's or
FUNCTION's depends on whether you want to get information from
MASM in DX:AX (the format for FUNCTIONs), or if the MASM routine
either sends back no information or more than one variable (the
format for SUBs).  For simple one variable routines when MASM is
just returning a value, use FUNCTIONs.  To use such functions
inside QBASIC you must either assign the value of the function to
a QBASIC variable or use IF ... THEN statements (C style).  For
everything else use SUBS.
          Note due to an error in the QBASIC parser, always use
the CALL keyword to call the library routines if there is any
chance that you will use a colon as a separator on a line.
Without the CALL keyword, the QBASIC parser assumes that the
routine name followed by a colon is intended as a line label, and
not as a SUB name.  You must use CALL if you will use a SUB that
does not need any parameters and will follow that SUB name by a
colon.
          CGA Theory:
          The CGA is a slow, and sometimes snowy display.  These
routines deal with snow in four ways.  If the CGA is good display
(e.g. COMPAQ, AT&T, or ZENITH) then snow checking can be turned
off automatically.  If a user has a CGA display that does not
display snow (one of many clones, none of which I have access to
or have tested), he can use TOGGLESNOW to turn snow checking off.
The routine can assume the that CGA is snowy and turn off the CGA
for a instant, then turn it back on.  This causes flicker, but I
use when I am changing the entire display.  See BLOADHELP.  The
last alternative is to delay writing words or bytes to the
display until the display is in either vertical or horizontal
retrace mode.  This can be fast (1.5 times as fast as QBASIC's
PRINT routine, while if snow checking is turned off these
routines are 5 to six times faster than QBASIC library routines).
Hardware interrupts are temporarily turned off, so a timer tick
or a keystroke will not upset the counting and writing routines.
The routines generally only allow enough time to read and write
one word.  If any further manipulation is required, the wait-for-
retrace loop has to be re-entered a second time.  For speedier
displays (MONO, HERC, EGA, VGA and MCGA), a jump is made to a
faster routine that does not have to wait for retrace.
          There is a fifth way to avoid snow on a CGA, and that
is send one word while the video display is in horizontal retrace
and 400 words while in vertical retrace mode.  However, that was
considered too complicated.  See, Wilton, "Programmer's Guide to
PC & PS/2 Video Systems" (Microsoft 1987).
          Video Theory:
          Video memory in text mode starts at segment &HB000 for
mono displays, and &HB800 for color displays.  The offset of the
first page is 0, then &H1000 (80 x 25) for as many pages as are
allowed.  The screen has no internal divisions representing ROWS
and COLUMNS (except in HERC and CGA graphics modes), it simply is
a logical concept.  At the BIOS/hardware level, for purposes of
displaying a character, the upper left is 0,0 and lower right of
the display in SCREEN 0: WIDTH 80,25  is 24,79.  Thus the
location of a particular word on the display is (Row (0 biased)
times 160 plus Column) times 2.  The 160 is merely 80 columns
times two bytes (character and attribute).  That figure is
hardcoded in my routines so I can use shifts rather than MUL's on
old PC's and speed up the video location MACROS.  On an 8088,
shifts are faster then MUL's (some of the macros show the clocks
for shifts versus MUL's on an 8088 and on an 80286).  When
writing to the display, the attribute is stored (and read into)
in AH, and the character is stored (and read into) in AL.  To
only write characters or attributes, the routines increment DI
(usually) after every write.  This allows certain routines to
write to the display sending only characters or only attributes.
          MASM Theory:
          The MASM routines were designed to be compiled with MS
QUICK ASSEMBLER, using simplified segment names.  They should
compile with MS MASM 5.1 and above.  The DOSSEG keyword might not
be supported in MASM, so use the MASM keyword that arranges the
segments in DOS order, rather than ALPHA order.  If you use TASM
with QUIRKS (IDEAL too?) you should be able to compile these
programs with TASM.  Because A86 does not make MS .OBJ files, you
probably cannot use it.  The same may be true with OPTASM.
          The simplified directives really save time when you
have to identify variables on the stack, and push and pop
variables.  I use the full PROC function and the regular PROC
keywords interchangeably.  Full PROC format is not necessary when
there is no need to address variables on the stack (i.e. no need
to change BP to address the stack) and the QBASIC routine is
described as a FUNCTION.
          The EVEN directive is used to word align loops for
80286 and 80386 machines.  EVEN inserts NOPS as necessary to word
align loops.  The QBASIC BYVAL directive is used to get
information directly from QBASIC without having to use [BX] or
[SI] to fish out the correct information.  You will note that DS
and OFFSET are used in an unusual way in these routines.  The
string move MASM opcodes use DS:SI (source) to move video bytes
to ES:DI (destination).  We have to wait to set DS to the proper
address until we have removed information from the stack, as DS
must point to DGROUP to properly use the stack.  In addition,
OFFSET is faster than LEA to address information in .CODE
segment.  However, for OFFSET to work, MASM must be told that
ASSUME DS:NOTHING, ES:NOTHING.  This makes the offset relative to
beginning of code segment, and not relative to DGROUP (which is
the default if simplified segments are used).  Should anyone have
problems with this, please let me know.   To allow for
compatibility with the 8088 chip, shifts rather than MULs are
used for speed.  I use .code to store most of my variables to
save space in DGROUP, which is comparatively tiny and easily
filed with string data.
          To program in OS/2 .code segment variables are
verbotten, and you must use local variables on the stack.  I
don't have access to the OS/2 DOS compatibility box, so I don't
know how these routines would work under OS/2.  I am certain that
none of these routines would work smoothly under protected mode.

 Video routine short instruction list
 ===========================================================================
  DECLARE SUB BACKFILL _
 (BYVAL ULR%, BYVAL ULC%, BYVAL LRR%, BYVAL LRC%, BYVAL ATTRIB%, BYVAL TEXTCHAR%)
  CALL BACKFILL(ULR%, ULC%, LRR%, LRC%, ATTRIB%, TEXT$)
  Description of parameters:
     Because a rectangle can be described by two points, we us the following
     data points:
        ULR Upper left row
        UCL Upper left column
        LRR Lower right row
        LRC Lower right column
        Attribute% = Background color (range 0 to 15) x 16 + Foreground color
            (Range 0 - 15).  The color can be easily described in Hex as &H47
        which yields a red background and white foreground.
        TextChar% = is simply the character code that you want to fill display
        with.  Common characters are 32 or space, 176 - 178 which makes for an
        attractive background character for windowing.
  Fills the display area with a character and a fixed text attribute

 ============================================================================
  DECLARE SUB BLOADHELP (FileName$)
  CALL BLOADHELP(FileName$)

  Purpose:
          to BLOAD help files without defining size of help file or type of
          display, DEFSEG location, or anything else

  Assumes:
          Both BSAVED file and CRT is setup for SCREEN 0, 80 x 25
          Routine does not provide any critical error support.
          Minor file errors will cause abort unless ON ERROR GOTO support
          is provided to handle common errors.

          FileName$ must be a near string in DGROUP, cannot be FIXED Length
          or TYPE'd.

 ===========================================================================
  DECLARE SUB CHANGEPAGE ()
  CALL CHANGEPAGE
 Purpose:
         Adjust the current VIDEOSEG to reflect current active page that is set
         by QBASIC.  This routine does not change the page that is currently
         written to, you must use QBASIC to do it.

         Also reinitializes Video Data Area

 Limit:
         This will permit 25, 43, & 50 line displays
         Note on many HERC's the page size is fixed at 16kb even though
         it really is 4kb in Text Mode.  Because QBASIC does not believe that
         a HERC display has video pages in text mode, this routine ignores
         ignores the possibility of video pages for HERC display.
  Typical page limits in 80 x 25 text mode:
  Mono, HERC    = 0 pages
  CGA           = 4 pages
  EGA (w/128kb) = 8 pages
  VGA           = 8 pages
  With careful tinkering of CODE you could get 32 pages for 256kb EGA/VGA's
  and 8 pages for HERC.  However, QBASIC and PRINT would become all confused.
  That is why this is left to reader to implement.
  Returns:
         Nothing, Video Data Area Filed

 ===========================================================================
  DECLARE SUB _
  CLEARAREA (BYVAL ULR%, BYVAL ULC%, BYVAL LRR%, BYVAL LRC%, BYVAL ATTRIB%)
  CALL CLEARAREA (ULR%, ULC%, LRR%, LRC%, ATTRIB%)
  Description of parameters:
     Because a rectangle can be described by two points, we us the following
     data points:
        ULR Upper left row
        UCL Upper left column
        LRR Lower right row
        LRC Lower right column
        Attribute% = Background color (range 0 to 15) x 16 + Foreground color
            (Range 0 - 15).  The color can be easily described in Hex as &H47
        which yields a red background and white foreground.
  Changes the attribute of an area on the screen in text mode

 =========================================================================
 DECLARE SUB CLEARSCR (BYVAL ULR%, BYVAL ULC%, BYVAL LRR%, BYVAL LRC%,
 _BYVAL ATTRIB%)
 CALL CLEARSCR(ULR%,  ULC%,  LRR%,  LRC%, ATTRIB%)
       range:   1-50  1-80  1-50   1-80   0-255
  Uses the video bios to scroll a window.

 ===========================================================================
  DECLARE SUB CLREOL ()
     CLREOL
  Purpose:
        Clears to end of current display line w/o changing attribute
  Assumes:
        80 Column mode, assumes that DI has been set by SETQP; QPRINT;
        QPRINTL; or  QPRNT

 ============================================================================
  DECLARE SUB CURSET (Mode%)
  Input:
        Mode = 0  turn off cursor
             NOTE on a VGA with ANSI.SYS installed it might not be possible
             to turn off all attributes of the cursor.
        Mode = 1  turn on normal cursor
        Mode = 2  turn on half block
        Mode = 3  turn on full block
  Returns:
        Nothing
  Purpose:
        Selects attractive cursor sizes over the default QBASIC format.
        Complicated because of need to overcome cursor emulation on VGA/EGA
        With an EGA/VGA if want a full block cursor, cannot rely on cursor
        emulation, must adjust for actual display box (assume 80 x 25).

 ============================================================================
  DECLARE FUNCTION DOSPRINT% (BYVAL Row%, BYVAL Col%, Text$)
  IF DOSPRINT% (Row%, Col%, Text$) THEN
      PRINT "Error in text$: null or invalid character"
  END IF
  If you don't need a return code, simply DECLARE as a SUB

  Print Text$ at Row%, Column
  Uses DOS Write services to print to STDERR.  STDERR always == CON.
  Does not change the current background attribute, uses whatever was there.
  Only prints to page 0, but no range checks on ROW and COL.  Most useful when
  operating in a multitasking environment or if want to use ANSI.SYS control
  strings.

  Returns:
         Error code:
          0 if no error
         -1 if ASCII CHR$(26) found in input stream

  Warning:
         Assumes Text$ only contains ASCII text or Carriage return
         control characters.  Any other control characters, e.g. CTRL-C
         will cause Program to terminate, probably destroying file.
         Routine checks for C/R, CTRL-C, CTRL-S, CTRL-P after each character
         If don't want this character checking, use DMPRINT

  Notes:
  Moves the cursor to the beginning of the string.  However does not tell
  QBASIC the current cursor location.  Should be a well managed function
  under WINDOWS or other multitasker.

 ============================================================================
  DECLARE FUNCTION DMPRINT% (BYVAL Row%, BYVAL Col%, Text$)
  IF DMPRINT% (Row%, Col%, Text$) THEN
      PRINT "Error in text$: null or invalid character"
  END IF

  If you don't need a return code, simply DECLARE as a SUB

  Uses DOS Write services to print to STDERR.  STDERR always == CON.
  Does not change the current background attribute, uses whatever was there.
  Only prints to page 0, but no range checks on ROW and COL.
  Returns:
         Error code:
          0 if no error
         -1 if CON error.
  If you don't need a return code, simply DECLARE as a SUB

  Warning:
         Ignores any control characters, merely prints string.

  Notes:
  Moves the cursor to the beginning of the string.  However does not tell
  QBASIC the current cursor location.  Should be a well managed function
  under WINDOWS or other multitasker.

  Routine is about 1.23 times faster than DOSPRINT on an EGA

 =======================================================================
 DECLARE FUNCTION DSPATTRIB% (BYVAL Foreground%, BYVAL Background%)
 Takes Background color x 16 plus Foreground color
 to make an attribute used by the system routines
 allows Background% > 15, so can blink
 This routine is not necessary, it just makes life easier for the programmer
 who remembers the format for COLOR.

 ============================================================================
  DECLARE FUNCTION DUALDISPLAY% ()
  Returns:
        True  (<> 0)  if two displays found
        False (0)     if only one CRT found

 ============================================================================
  DECLARE EGAMONO (BYVAL Mode%)
  CALL EGAMONO (Mode%)
  Purpose:
        Forces VGA/EGA mono display to normal MONO attributes
        This allows programmer to have the same attributes appear on a
        HERC, MONO, or EGA Mono Display
  Input:
        Mode%  = 0 if want default mono attributes
        Mode% <> 0 if want Herc type attributes
  Returns: Nothing

  Limitations:
         For contrast, colors can only be used against White or Intense.
         Primary colors appear as Black.
         Only White or Intense can be contrasted against Black.
         Blue and Intense Blue attributes are not underlined, unlike HERC/MONO
         All intense colors appear as white.
  Full control over VGA is not possible because of GRAY scaling and large
  number of DAC/palette registers.  To get control over those two features would
  make the program much larger.
  Tinkering required for mono MCGA, but who has one of those?

 ============================================================================
  DECLARE SUB FADE ()
  CALL FADE
  Purpose: Clever visual effect, fades out display to white on black.
  Changes all characters to spaces.
  Works in TextMode only.  Sensitive to all video modes (i.e. no snow on CGA's)
  Assumes: Display width is 80 x 25, 80 x 43 or 80 x 50

 ============================================================================
  DECLARE FUNCTION FINDCOLOR% ()
  Returns:
        True  (<> 0)  if color CRT found, even if not active
        False (0)     if color CRT not found

 ============================================================================
  DECLARE FUNCTION FINDMONO% ()
  Returns:
        True  (<> 0)  if mono CRT found, even if not active
        False (0)     if mono CRT not found

 ============================================================================
  DECLARE SUB HERCMODE (BYVAL Mode%)
  CALL HERCMODE (Mode%)
  Purpose is a to control dual displays with color and HERC

  Input:
        Mode =  0, Sets a Herc display to half-mode, so it can use a CGA
        Mode <> 0, Sets a Herc display to full-mode, can not use a CGA
  Does not test for existence of Herc display.

 =======================================================================
  DECLARE FUNCTION INCOLOR%()
        IF INCOLOR% THEN
            ... etc.
  Tests if have a color or mono display attached.  Test primary display only.
  returns          -1 if color display (may be a single color display)
                    0 if BW mono display
  Note will not be fooled by Herc CGA emulation routines.  Doesn't test
  for single color displays like COMPAQ, AT&T

 =======================================================================
  DECLARE SUB LSCROLL (BYVAL Attribute%)
  CALL LSCROLL(Attribute%)
  Scrolls screen left
  Mostly for fun.  To be really useful would have to set it up for windows
  and would have to print using VPRINT.
  Designed to handle an 80 x 25 text display

 ============================================================================
 DECLARE SUB MAKEBOXES _
 (BYVAL ULR%, BYVAL ULC%, BYVAL LRR%, BYVAL LRC%, BYVAL HASNO%, BYVAL BORDER%,_
  BYVAL ATTRIB%)
 CALL MAKEBOXES(ULR,ULC,LRR,LRC,HASHNO,BORDER,ATTRIB)

  Description of parameters:
     Because a rectangle can be described by two points, we us the following
     data points:
        ULR = Upper left row
        UCL = Upper left column
        LRR = Lower right row
        LRC = Lower right column

        HashNo% = is simply the character code that you want to fill display
        with.  Common characters are 32 or space, 176 - 178 which makes for an
        attractive background character for windowing.

        Border = Select border type:
           0 = no border
           2 = single sided
           3 = single vertical, double horizontal
           4 = double vertical, single horizontal
           5 = solid box
           Default or 1 = double vertical, double horizontal

        Add 256 to BORDER if want shadows.  Shadow designed for 80 x 25 windows,
        to prevent page overlap.  Shadow color is White on blue background for
        a mono display, is white on black background

        Attribute% = Background color (range 0 to 15) x 16 + Foreground color
            (Range 0 - 15).  The color can be easily described in Hex as &H47
        which yields a red background and white foreground.

  Somewhat shorter and 1.0076 times faster than using the primitives
  in this .OBJ file to do the same thing

 ============================================================================
  DECLARE SUB QATTRIB (BYVAL ROW%, BYVAL COL%, BYVAL NUMCHAR%, BYVAL ATTRIB%)
  Row, Column is the starting location. attribute is the color
  and Numchar is the number of characters to change.
  Changes the attribute of characters on the screen in text mode
  Assumes: Display width is 80 columns, Rows are 25, 43, or 50

 ============================================================================
  QPRINT.ASM - performs Quick Printing in the QuickBASIC
  DECLARE SUB QPRINT (BYVAL ROW%, BYVAL COL%, Text$, BYVAL ATTRIBUTE%)
  Works in TextMode only, ignores all special characters
  Sensitive to all video modes (i.e. no snow on CGA's)
  If no attribute is selected, the default attribute is &H07 (normal)
  Assumes: Display width is 80 columns, Rows are 25, 43, or 50

 ===========================================================================
  DECLARE SUB QPRINTL (Text$)
          CALL QPRINTL(Text$)
  Usage: CALL SETQP(ROW%, COLL%, Attribute%) the first time to set
  the defaults to current display size.  Then QPRINTL on down the display.
  You should use SETQP to start, since scroll routine needs the proper
  attribute to scroll the screen up.

  Purpose:
          To work similarly to PRINT Text$

          Major differences are:
          a)  Assumes that a VIEW PRINT has been executed
          b)  will not parse the Text$ and start a new line if length of
            Text$ is longer than remaining space on current line.  PRINT
            is designed for formatted column printing, while this
            routine is not.
          c) if at Last Row, Column 80, QPRINTL will scroll the display
             can't stop it.

  Speed:
        Varies with length of Text$ and length of display
          for a color EGA on a 10 Mhz AT, the speed varies from 3% faster
          (if LEN(Text$) = 80) to 48% faster.
          Typical speed increase is 12%

 ============================================================================
  QPRT.ASM - performs Quick Printing in the QuickBASIC
  DECLARE SUB QPRT (BYVAL ROW%, BYVAL COL%, TEXT$)
  Works in TextMode only, ignores all special characters
  Sensitive to all video modes (i.e. no snow on CGA's)
  Does not change the attribute, uses whatever was there.
  Much faster than LOCATE X,Y : PRINT T$
  Routine is about 6   times faster than PRINT on a color EGA on an AT
             about 4.5 times faster than PRINT on a color VGA on a 386SX
             about 7   times faster than PRINT on a mono EGA on an AT
             about 1.5 to 2 times faster than PRINT on a CGA on an IBM PC
             about 5   times faster than PRINT on a HERC on an AT
             about 6   times faster than PRINT on a COMPAQ Portable

  Assumes: Display width is 80 columns, Max Rows are 25, 43, or 50

 ============================================================================
  DECLARE SUB RECOLOR (BYVAL OrigColor%, BYVAL NewColor%)
  CALL RECOLOR( OrigColor%, NewColor%)
  Purposes: Change one specific color to another without upsetting the display
  or using palette registers (which couldn't be restored easily using an EGA)

  Color is written as BackGround x 16 + ForeGround color

  Sensitive to all video modes (i.e. no snow on CGA's)
  Assumes: Display width is 80 x 25, 80 x 43 or 80 x 50

 ========================================================================
 RESTSCRN.ASM - restores 80 x 25 page text screen in QuickBASIC array
 Parameters:
  DECLARE SUB RESTSCRN (BYVAL Segment%, BYVAL Offset%)
  DIM ARRAY%(2000)
  CALL RESTSCRN(VARSEG(ARRAY%(0)), VARPTR(ARRAY%(0)))
  To save display call SAVESCRN

 =======================================================================
  DECLARE SUB RSCROLL (BYVAL Attribute%)
  CALL RSCROLL(Attribute%)
  Scrolls screen right
  Mostly for fun.  To be really useful would have to set it up for windows
  and would have to print using VPRINT.
  Designed to handle an 80 x 25 text display

 ========================================================================
 SAVESCRN.ASM - saves 80 x 25 text screen page in QuickBASIC array
 Parameters:
  DECLARE SUB SAVESCRN (BYVAL Segment%, BYVAL Offset%)
  DIM ARRAY%(2000)
  CALL SAVESCRN( VARSEG(ARRAY%(0)), VARPTR(ARRAY%(0)))
  To restore call RESTSCRN

 ===========================================================================
 DECLARE FUNCTION S2BUFF  ;put text screen in buffer
 DECLARE FUNCTION BUFF2S  ;get text screen from buffer

 Allows movement of text screens, page 0 to and from a buffer.
 Modified to handle a CGA display so will NOT cause SNOW on a CGA

 Handles  80 x 25, 80 x 43, and 80 x 50 displays.  Checks current status each
 time it makes a shift.

 Storage in Code Segment used to save space in DGROUP, makes DATA near
 without using up the limited amount of DGROUP space.  However prevents
 use of program in OS/2 which prohibits any change to CodeSeg values.

 ===========================================================================
 DECLARE SUB SCN2BUFF ()  ;put text screen in buffer
 DECLARE SUB BUFF2SCN () ;get text screen from buffer

  Allows movement of text screens, page 0 to and from a buffer.
  Modified to handle a CGA display so will NOT cause SNOW on a CGA

  Handles only 80 x 25 displays. Will not crash on 80 x 43 or 80 x 50 just wont
        save the entire display.  See S2BUFF if want larger displays.

  Storage in Code Segment used to save space in DGROUP, makes DATA near
  without using up the limited amount of DGROUP space.  However prevents
  use of program in OS/2 which prohibits any change to CodeSeg values.

 =========================================================================
 DECLARE SUB SCROLLDOWN (BYVAL ULR%, BYVAL ULC%, BYVAL LRR%, BYVAL LRC%, BYVAL
 _ ROWS%, BYVAL ATTRIB%)
 CALL SCROLLDOWN(ULR%, ULC%, LRR%, LRC%, ROWS%, ATTRIB%)
  If ROWS%=0 then entire window cleared
  Description of parameters:
     Because a rectangle can be described by two points, we us the following
     data points:
        ULR = Upper left row
        UCL = Upper left column
        LRR = Lower right row
        LRC = Lower right column
        Rows = number of rows to scroll
  Uses the video bios to scroll a window.

 =========================================================================
 DECLARE SUB SCROLLUP (BYVAL ULR%, BYVAL ULC%, BYVAL LRR%, BYVAL LRC%, BYVAL
 _ ROWS%, BYVAL ATTRIB%)
 CALL SCROLLUP(ULR%, ULC%, LRR%, LRC%, ROWS%, ATTRIB%)
  If ROWS%=0 then entire window cleared
  Description of parameters:
     Because a rectangle can be described by two points, we us the following
     data points:
        ULR = Upper left row
        UCL = Upper left column
        LRR = Lower right row
        LRC = Lower right column
        Rows = number of rows to scroll
  Uses the video bios to scroll a window.

 ===========================================================================
  DECLARE SUB SETQP (BYVAL ROW%, BYVAL COLL%, BYVAL Attribute%)
          CALL SETQP(ROW%, COLL%, Attribute%)
  Purpose:
          Initializes varibles, and sets DI to target address.  This is the
  initialization routine for QPRINTL.  Selects the attribute used to scroll
  the display upward.
  Assumes that user wants to set page size to full size of current dsplay
  such as 80 x 25, 80 x 43, or 80 x 50

 ===========================================================================
  DECLARE SUB SETBLINK (BYVAL Status%)
  CALL SETBLICK (Status%)
  Purpose:
        Toggles background blinking/intensity for MONO, CGA, EGA, VGA
        allows use of background colors that would otherwise flash
  Parameters:
        =  0 turn off blinking, enable intensity
        <> 0 to turn it on again
  Returns:
        nothing

 ===========================================================================
  DECLARE SUB SNOWCHECK ()
  CALL SNOWCHECK
  Purpose:
         Clears the snowcheck variable (B$DVIDEOPORT) if it finds a CGA
         display by OLIVETTI (AT&T), COMPAQ, or ZENITH

  Returns:
         Nothing DGROUP Data Area Filed

 ============================================================================
  DECLARE SUB SWAPCOLOR ()
  CALL SWAPCOLOR
  Purpose:
          If have a CGA and a MONO display, this makes the CGA active
  Note:
          Does not test if have either CGA or MONO installed
  See the FIND routines
  Side Effect: Display Cleared

 ============================================================================
  DECLARE SUB SWAPMONO ()
  CALL SWAPMONO
  Purpose:
          If have a CGA and a MONO display, this makes the MONO active
  Note:
          Does not test if have either CGA or MONO installed
  See the FIND routines
  Side Effect: Display Cleared.  If have dual displays, the mono display is put
        in HERC half mode for CGA compatibility purposes.   Feedback please!

 ===========================================================================
  DECLARE SUB TOGGLESNOW (Mode%)
  CALL TOGGLESNOW(Mode%)
 Input: If Mode% =  0, clears SNOWCHECK
        If Mode% <> 0, leaves SNOWCHECK set
 Purpose:
         Clears the snowcheck variable (B$DVIDEOPORT) if find a CGA display
         Also reinitializes Video Data Area

 Returns:  Nothing
           Video Data Area Filed

 ===========================================================================
  DECLARE SUB VADDR (Row%, Column%)
   CALL VADDR(Row%, Column%)
   returns the current end of string address for the qprint routines

 ============================================================================
  DECLARE SUB VIDINFO (MODE%, ROW%, COLUMN%, CURPAGE%, PAGESIZE%)
  CALL VIDINFO(MODE%, ROW%, COLUMN%, CURPAGE%, PAGESIZE%)
  Purpose:
        Returns information about current video display status.
        Mode%     = current video mode using BIOS format
        Row%      = number of rows currently being displayed
        Cols%     = width of display in columns
        Curpage%  = currently active page
        Pagesize% = size of current page in bytes, default is 4kb
                    for an 80 x 25 display.
  Note:
        PAGESIZE% on many HERC clones will be incorrect and reflect the
  information of the HERC display in HALF mode or 16kb size.
  Routine will store correct Row% length in BIOS ram for CGA, HERC & MONO

 ===========================================================================
  DECLARE FUNCTION VIDEOSTAT% ()

  VideoStatus Analyzer
  Program returns video information for use by QBASIC
  returns highest level of SCREEN mode supported by the Hardware.
  Returns information about the PRIMARY display only
  This routine with a SELECT CASE, can tell you how many display pages
  are available in text mode, SCREEN 0: WIDTH 80,25
  VGA has 8 pages (0 to 7)
  EGA with > 64kb has 8 pages (0 to 7)
  EGA with 64kb has 4 pages (0 to 3)
  CGA has 4 pages (0 to 3)
  MONO has 1 pages (0)
  HERC has 1 page in SCREEN 0 (0), 2 pages in SCREEN 3 (0 to 1)

  Exceptions:
  MCGA color returns a mode 11, so can contrast w/ VGA
  HERC w/o MSHERC.COM reports a -3 so you can tell user to correct matters
  COMPAQ with CGA reports -2 so can force use of monchrome attributes.
  EGA's with CGA displays report -8 if have only 64kb of memory
  EGA's with ECD display report  8 if have only 64kb of memory

  Returns:
  Mono         =   0
  CGA          =   2
  PGA          =   2   (Untested, assume PGA would be treated as CGA)
  COMPAQ - CGA =  -2   to tell that user may have a single color display
  HERC         =   3   if have HERC and MSHERC.COM
  HERC         =  -3   if have HERC but w/o MSHERC.COM
  AT&T         =   4,  but only if have just CGA display, not EGA or VGA
      Microsoft QuickC/C makes Olivetti EGA and VGA return a separate code.
      I don't know why anyone would care if the EGA/VGA emulation were
      good.
  EGA64        =   8   Because resolution limited for 64k EGA
  EGA64 w/CGA  =  -8   Because resolution limited to CGA modes
  EGA          =   9   Have minimum of 128kb of video ram
  EGA w/CGA    =  -9   Since resolution limited to CGA modes
  MCGA         =  11   If have an analog color display
  MCGA         = -11   If have an EGA ECD digital color display, since
                       resolution of this display is limited to EGA modes
  VGA          =  13
  EGA/VGA mono =  10   I guess will catch MCGA mono too

  The above numbering routine was selected so if the programmer put ABS in
front of the returned value, a SCREEN command could be entered.  The other
advantage was that the routines are much faster thant the ON ERROR GOTO
traps using ERR 5 to determine what is allowed and what is not.

  Version 0.92

  Tested:     CGA clone, HERC clone, EGA mono, EGA color, VGA color, COMPAQ CGA,
              VGA clone, EGA clone (Paradise clone, ATI EGA Wonder), AT&T 6300
  Not tested: PGA, VGA monochrome, MCGA (color or monochrome)

 ===========================================================================
  VPRINT.ASM - performs Vertical Printing in the QuickBASIC
  DECLARE SUB VPRINT (BYVAL ROW%, BYVAL COL%, Text$, BYVAL ATTRIBUTE%)
  Works in TextMode only, ignores all special characters
  Sensitive to all video modes (i.e. no snow on CGA's)
  If no attribute is selected, the default attribute is &H07 (normal)
  Assumes: Display width is 80 columns

 ============================================================================
  VPRT.ASM - performs Vertical Printing in the QuickBASIC
  DECLARE SUB VPRT (BYVAL ROW%, BYVAL COL%, TEXT$)
  Works in TextMode only, ignores all special characters
  Sensitive to all video modes (i.e. no snow on CGA's)
  Does not change the attribute, uses whatever was there.
  Assumes: Display width is 80 columns

 ==============================================================================
     WINDREST.ASM - restores a portion of the text screen in QuickBASIC;

  DECLARE SUB WINDREST(BYVAL ULR%,BYVAL ULC%,BYVAL LRR%,BYVAL LRC%,
 _BYVAL SEGADD%, BYVAL OFFADR% )
  CALL  WINDREST(ULR%,ULC%,LRR%,LRC%,VARSEG(STORAGE(0)),VARPTR(STORAGE(0)))
  Description of parameters:
     Because a rectangle can be described by two points, we us the following
     data points:
        ULR = Upper left row
        UCL = Upper left column
        LRR = Lower right row
        LRC = Lower right column
     Dimension storage array to handle size of display in bytes
    E.g. 80 x 20 display would require an integer array of 1600

 ===============================================================================
     WINDSAVE.ASM - saves a portion of the text screen in QuickBASIC
  call from Quickbasic:
  DECLARE SUB WINDSAVE(BYVAL ULR%,BYVAL ULC%,BYVAL LRR%,BYVAL LRC%,
 _BYVAL SEGADD%, BYVAL OFFADR% )
  DIM STORAGE(2000)
  CALL  WINDSAVE(ULR%,ULC%,LRR%,LRC%,VARSEG(STORAGE(0)),VARPTR(STORAGE(0)))

  Description of parameters:
     Because a rectangle can be described by two points, we us the following
     data points:
        ULR = Upper left row
        UCL = Upper left column
        LRR = Lower right row
        LRC = Lower right column
     Dimension storage array to handle size of display in bytes
    E.g. 80 x 20 display would require an integer array of 1600

 ===============================================================================

Acknowledgments:
        Most of my deeper insight into video programming came from a set of
public domain TASM video routines by Dave Bennett, (with the Toad Halls
tweaks), from 1988.  He is the source of the routine for using both the
horizontal and vertical retrace to write to a CGA.  In addition, his code
showed the simple techniques used to write just characters and just attributes
to the display.

Author  : Dave Bennett
Version : 1.0
Date    : 11/9/88
CIS PPN : 74635,1671

Bibliography:
        General DOS/BIOS routines:  Ray Duncan and Peter Norton's programming
books.  If you can only afford one book, get Duncan's.  Duncan, "Advanced MS-
DOS Programming" (2d Ed. Microsoft 1988).  Very easy to read and to refer to
specific routines.  The text is very well formatted for easy reference.
        Norton, "The New Peter Norton Programmer's Guide to the IBM PC and
PS/2" (Harper & Row 1988).  A book designed to help you visualize what is
going on.  Having been "burned" by writing a book on the PC Junior, and
experienced the agony of hardware incompatibilities in writing the Norton
Utilities, Peter wants everybody to use the bios and documented DOS routines.
        EGA/VGA Programming:
        Michael Abrash, "Power Graphics Programming" (Que 1990).  Excellent
reprint of Programmer's Journal (Buy this magazine!) columns.  Does not cover
Super VGA and beyond (that is being done now in the Programmer's Journal).
Mostly useful for graphics routines.  The best book on the subject, and the
only technical book that one could actually enjoy reading as a book rather
than as a reference.  See also various issues of PC Magazine for programming
tidbits.
        Ferro, "Programmer's Guide to the EGA and VGA Cards," (Addison-Wesley
1988).   Good, but slightly disorganized.  The only book that discusses the
registers (unfortunately more in the nature of a dictionary rather than in
examples of how to manipulate the registers).  A good list of typical bios
defaults, which are important for the EGA since you can't read the registers.
        Herc:
        Doty, "Programmer's Guide to Hercules Graphics Cards" (Addison-Wesley
1988).  Good book on the subject.  Describes the high end Herc systems.  Many
programming examples and port descriptions.
        Herc, CGA, EGA, VGA:
        Wilton, "Programmer's Guide to PC & PS/2 Video Systems" (Microsoft
1987).  Excellent general purpose book.  Said to have some errors, though I
have found nothing more than a few typos.  Does not cover Super VGA and
beyond.  Partial information is set forth in Phoenix's "System Bios for
PC/XT/AT Computers and Compatibles" (Addison-Wesley 1989).
        MONO and CGA:
        Bradley, "Assembly Language Programming for the IBM Personal
Computers" (Prentice Hall 1984).  Good technical descriptions of the original
PC.  Only book I have seen that has really shown how to switch displays,
manipulate DMA, make sound, and manipulate floppy disk drives at the PORT
level (teaches you why we have BIOS and DOS routines).  Good book on the 8087.
Probably now out of print.  I bought my copy at a book store that sells
remainders.
        DOS Programming:
        Detteman, "DOS Programmer's Reference (2d Ed. Que 1989).  Excellent
book with a very helpful look at undocumented DOS.  Doesn't preach about not
using undocumented DOS as does Peter Norton.
        Waite Group "Dos Developer's Guide" (2d Ed Sams 1989).  Good book on
Expanded memory and math chips.  Several good discussions of the undocumented
DOS functions.  Such a big book, that you feel you got your money's worth
based just on weight.
        General Programming:
        Holzner, "PS/2-PC Assembly Language"  (Brady 1989)  Good introduction
to assembly language programming.  In many respects better than Holzner,
"Advanced Assembly Language on the IBM PC" (Brady 1987).
        Tischer, "PC System Programming for Developers" (ABACUS 1989).  Good
technical survey of PC/AT systems.  Comes with a lot of programs showing how
to do useful things in MASM, QBASIC, PASCAL and C.  The only shortcoming is
that the book is printed on very cheap paper.  One of the few books to show
register usage of DOS and BIOS routines (important so you can save variables
in registers rather than in memory or pushed on the stack.)  Doesn't discuss
DOS Version 4 in an integrated fashion.  Such a big book, that you feel you
got your money's worth based just on weight.
        Young, "Inside DOS: A Programmer's Guide", (Sybex 1990).  Good source
of MASM code, with a primary emphasis on C (The MASM code is similar for both
C and QBASIC).  A reprint of "MS DOS Advanced Programming" (Sybex 1988).  (I
didn't discover this until I purchased both).
        Wyatt, "Using Assembly Language" (2d Ed. QUE 1989).  Some decent video
routines.  No useful description of VGA.  EGA routines are primitive.  Good
insight into programming for high level languages.  Complete listing of all
the Intel keywords, but reads too much like an Intel-English disctionary.
Most of the examples in the keyword section are not really helpful and the
ASCII math routines are not well described.  One major programming feature
dropped from the 1st edition was the AT keyboard programming routines.  Does
this mean AT keyboards are only marginally compatible on the hardware level?
Feedback please.
        QBASIC Programming:
        Goodwin, "QuickBASIC Advanced Programming Tools" (MIS 1989).  A much
better book for QBASIC code (sorting, popup windows, dropdown windows and
menubar programs) than for MASM code.  The MASM code relies on video bios to
do things (which is slow, though always compatible).  Moreover, screens are
stored in STRINGs rather than arrays, which greatly limits the usefulness of
his MASM routines.  (I agree storing screens in arrays takes more work).  A
programmer can have access to several hundred KB of far data in arrays, while
he can only have access to 30 to 40kb of precious string space in DGROUP.
        Lesser,  "Advanced Quickbasic 4.0 Language Extensions with Modular
Tools" (Bantam 1988).  This is how I learned about MASM/QBASIC programming.
Talks more about ideas that were important for QBASIC Version 3.0/MASM pre-
version 5.1  (before simplified directives) than for QBASIC Version 4.x.
BELIEVES in structured programming.  Not too many hardware insights.  Offers
generally sound advice.
        Shammas, "QuickBASIC- Programming Techniques and Library Development"
(M&T Publishing 1988).  Good QBASIC code.  Some of the string routines are
fast.  He has some BTREE and high level math routines.
        Books Not Recommended (How daring!):
        Murray & Pappas, "80386/80286 Assembly Language Programming"
(Osborne/McGraw Hill 1986).  Only feature of the book is a list of clock
cycles for 80286/80386 opcodes.  Reads like an Intel-English dictionary.
        Duntemann, "Assembly Language from Square One" (Scott, Foresman 1990)
Designed for the beginning programmer.  Suffers from a serious case of
excessive cuteness.  See game of "Big Bux", page 8.  PC Techniques (a good
programming magazine, like those HAX) shows he is capable of much, much more.

What's next:
        Two more freeware QBASIC libraries will be released: a) Mouse and
Keyboard routines; and b) DOS and Equipment ID routines.  All will include
MASM source and .OBJ code.  If I get any significant feedback, I might even
release revised libraries.
        I think once you are finished using these libraries you will discover
that programming is much like fishing.  At first, you just go fishing, then
you want to catch big fish.  After a while, you become content to merely catch
fish with whatever is fast, cheap and handy.
        Oh yes, I almost forgot, in case you are wondering, I am a tax lawyer
trying to "catch big fish"


         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 2,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.