I B M C O M                           

IBM RS232 interrupted driven communications routines. BBS version
has small model lib file for ibmcom. 

Since the BBS version supplies only object,the following assumptions
have been made:

        o Buffer input size is defined to be 2000 characters per 
          port.

        o Buffer output size for putsi_com() routine is defined to be 
          80 characters.

Purchasers of the source can change the above buffer size's.  If you
whish to obtain source and/or to see these routines continue to be
supported with ehancements,bug fixes, protocals, terminal
emulators,etc.

  Send $15 to:								

	Intrinsic Computers                 
	RR 4								
	Oak Ridge,NJ   07438						

	 Send $25 and we'll give you the latest   
	 version on a diskette plus code for a    
         reentrant xmodem recieve protocal. We    
	 also are available for consulting.			


 Description of Routines:

  int init_handl( int port_num)						
     Initializes port_num interrupt routines. 		
     Must be called after init_port(),but before 	
     using any other routines. Returns FALSE if
     port_num is not 1 thru 4,otherwise TRUE.
									
  void init_buffer_out(int port_num)                   
     Sets up the circular buffers for interrupt   
     output (specifically putsi_com()).  Should   
     be called only once.                         
									
  int init_port(int port_num,int baudrate,char parity,
        int data_bits,int stopbit)						
     Must be called before init_handl(). It sets	
     the port_num's baud rate,parity,etc..			
  Variables used:
        port_num   1,2,3, or 4
        baudrate   3 or 300   for 300 baud
                   6 or 600   for 600 baud
                  12 or 1200  for 1200 baud
                  24 or 2400  for 2400 baud
                  48 or 4800  for 4800 baud
                  96 or 9600  for 9600 baud
                  19 or 19200 for 19200 baud
                  38 or 38400 for 38400 baud
                  56          for 56000 baud
                 112          for 112000 baud
        parity    'E' for even
                  'N' for none
                  'O' for odd
        data_bits  5,6,7, or 8
        stopbit    1 or 2
  Returns
        TRUE if params ok.
        FALSE if illegal params.
									
  int check_port_hw(int port_num) 
						
     Used to check if a port error has occured or	
     if no error it returns the number of char		
     in the ports interrupt buffer. If error has
     occurred it returns the NEGATIVE of the port's
     line control register.  In programmers terms
     if the return value is >= 0 you got the # chars
     in port_num's buffer, otherwise if its < 0, you
     got an error on the port.  The error is cleared
     by calling this routine.
									
  int check_port_buf(int port_num)					

     Returns port_num's buffer overflow status.	
        1 for yes its overflowed
        0 for no overflow
									
  unsiged com_status(int port_num)						
     Returns port_num's port status.				
									
  void disable_txmit_int(int port_num)   		  
			
     Turns off interrupt driven output. You DON'T 
     call this unless you want to stop midstream  
     the output of a string. Normally the         
     interrupt handler inself will turn off Tx    
     interrupts when it finishes the string.      
                                                  
  int disable_port_int(int port_num)                      

     Turns off interrutps for port_num. Returns FALSE if
     illegal port_num, otherwise TRUE.
									
  int reset_port(int port_num)

     Resets port_num so that it will not interrupt
     the IBM anymore. Used to halt communications 
     Should be called before exiting your programs
     or interrupts will still be active and			
     hang the machine (or worse). Returns FALSE if illegal
     port_num, otherwise TRUE.
									
  void putc_com(int port_num,char *string)						

     Outputs the string to port_num	
     Does not buffer the character. It uses a		
     polling technique.                   			
									
  int puts_com(int port_num,char *string,int num_char)				

     Outputs the indicated num_char from string   
     to port_num using a polling technique. Returns
     TRUE.
									
  int putsi_com(int port_num,char *string,int num_char)				

     Same as puts_com() except it outputs the     
     string using an interrupt driven technique.  
     You must call init_buffer_out() once before  
     ever using putsi_com. Returns TRUE if able to
     handle the string passed to it, otherwise FALSE.
     See the demo program for further explanation.
									
  unsigned char getc_com(int port_num)						

     Gets a char from port_num's buffer.If the	
     buffer is empty it returns 0xFF which could	
     be a valid character. This routine should be	
     used in conjunction with check_port_buf() to	
     see if any characters are in the buffer 	
     before calling this routine. Returns char gotten.
								
  int gets_com(char *buffer,int num_bytes,int port_num)			

     Gets num_bytes from port_num and puts it into buffer. 
     Returns actual number of bytes transferred into buffer.
								
  void report_serial_status(unsigned error_code)			

     Will print out a nice report of the port status if you pass	
     it the port status (obtained from com_status(). Note, not 
     all status bits are errors, some are normal.
								
  int set_porthw_parm(int port_num, int port_ad,       
                 int vector_num, unsigned char    
                 mask)                            
                                                  
     Sets port_num hardware address parameters    
     where port_ad is the base hardware address   
     of the port, vector_num is the interrupt     
     number, and mask is the mask for the 8259    
     PIC. This routine generally is not needed    
     for ports 1 & 2, however since ports 3 & 4   
     hardware addressing is not standard this     
     routine will allow you to change these       
     parameters if your particluar hardware is    
     different than the following defaults:       
                                                         
       Port 3 base hardware ad = 0x3e8            
              vector number    = 12               
              mask             = 0xef             
                                                         
       Port 4 base hardware ad = 0x2e8            
              vector number    = 11               
              mask             = 0xf7    
         
     Returns TRUE if port_num is 1 tru 4,otherwise
     FALSE.

  Linking Instructions:					

     Must be linked with a main().  Supplied object in 
     BBS version is small model only.