HIM
                     Human Interface Manager
                        Programmer's Guide
                          Second Edition
 
                         For Version 1.1
 
 
                  Copyright 1987, 1988  Allsoft
                       ALL RIGHTS RESERVED.


 
 
                           Published by
 
                             Allsoft
                    100 Calle Playa Del Sol NE
                      Albuquerque, NM  87109
                          (505) 821-7760
 
                     (C) 1987, 1988  Allsoft
 
     All rights reserved.  No part of this publication may be
       stored in a retrieval system, or transmitted in any
   form or by any means, electronic, mechanical, photocopying,
   recording or otherwise except as specified in this manual.
          Printed in the United States of America.
 
 
 
 
                   First Printing: March, 1988
                 Second Printing: November, 1988
 
 
 
 
 
            HIM and Allsoft are trademarks of Allsoft
                MS-DOS is a trademark of Microsoft
   IBM is a trademark of International Business Machines Corp.









                                                                                
























































 

                               Table of Contents

1 Human Interface Manager (HIM)......................................... 1 - 1  
   1.1 Overview......................................................... 1 - 1  
      1.1.1 Introduction................................................ 1 - 1  
      1.1.2 Compilers Supported......................................... 1 - 1  
      1.1.3 Components.................................................. 1 - 1  
      1.1.4 Notational Conventions...................................... 1 - 2  
   1.2 Getting Started.................................................. 1 - 3  
      1.2.1 Backing Up Your Disks....................................... 1 - 3  
      1.2.2 Disk Contents............................................... 1 - 3  
      1.2.3 Include Files............................................... 1 - 3  
      1.2.4 Library Files............................................... 1 - 3  
      1.2.5 Skeleton MAIN()............................................. 1 - 4  
      1.2.6 Compiling................................................... 1 - 5  
      1.2.7 Linking..................................................... 1 - 5  
   1.3 Shareware........................................................ 1 - 5  
      1.3.1 Registration................................................ 1 - 6  
      1.3.2 Technical Support........................................... 1 - 7  
2 List Manager.......................................................... 2 - 1  
   2.1 Introduction..................................................... 2 - 1  
   2.2 Symbolic Constants............................................... 2 - 1  
      2.2.1 Error Constants............................................. 2 - 1  
      2.2.2 List ordering constants..................................... 2 - 1  
   2.3 Module Initialization............................................ 2 - 2  
   2.4 Include Files.................................................... 2 - 2  
   2.5 Function Overview................................................ 2 - 2  
   2.6 Function Definitions............................................. 2 - 2  
3 Keyboard Manager...................................................... 3 - 1  
   3.1 Introduction..................................................... 3 - 1  
   3.2 Components....................................................... 3 - 1  
   3.3 Symbolic Constants............................................... 3 - 3  
      3.3.1 Error Codes................................................. 3 - 3  
      3.3.2 UIR Function Codes.......................................... 3 - 3  
      3.3.3 Keycode Definitions......................................... 3 - 3  
      3.3.4 Module Initialization....................................... 3 - 5  
      3.3.5 Include Files............................................... 3 - 6  
      3.3.6 Function Overview........................................... 3 - 6  
      3.3.7 Function Definitions........................................ 3 - 7  
4 Help Manager.......................................................... 4 - 1  
   4.1 Introduction..................................................... 4 - 1  
   4.2 Help File Builder................................................ 4 - 1  
   4.3 Symbolic Constants............................................... 4 - 2  
      4.3.1 Error Constants............................................. 4 - 2  
   4.4 Module Initialization............................................ 4 - 2  
   4.5 Include Files.................................................... 4 - 2  
   4.6 Function Overview................................................ 4 - 3  
   4.7 Function Definitions............................................. 4 - 3  
5 Window Manager........................................................ 5 - 1  
   5.1 Introduction..................................................... 5 - 1  
   5.2 Components....................................................... 5 - 1  
   5.3 Symbolic Constants............................................... 5 - 1  
      5.3.1 Colors...................................................... 5 - 1  
      5.3.2 Cursor Types................................................ 5 - 2  
      5.3.3 Scroll Directions........................................... 5 - 2  
      5.3.4 Wninput Data Types.......................................... 5 - 3  



                               Table of Contents

      5.3.5 Error Codes................................................. 5 - 3  
   5.4 Module Initialization............................................ 5 - 3  
   5.5 Include Files.................................................... 5 - 4  
   5.6 Function Overview................................................ 5 - 4  
   5.7 Function Definitions............................................. 5 - 6  
6 Menu Manager.......................................................... 6 - 1  
   6.1 Introduction..................................................... 6 - 1  
   6.2 Module Initialization............................................ 6 - 1  
   6.3 Include Files.................................................... 6 - 1  
   6.4 Symbolic Constants............................................... 6 - 1  
      6.4.1 Error Constants............................................. 6 - 1  
      6.4.2 Menu Types.................................................. 6 - 2  
      6.4.3 Menu Location and Size...................................... 6 - 2  
      6.4.4 Pre-Defined Action Routines................................. 6 - 2  
      6.4.5 Mmpromenu func values....................................... 6 - 2  
      6.4.6 Hotkey Compare Constant..................................... 6 - 2  
      6.4.7 Function Overview........................................... 6 - 2  
      6.4.8 Function Definitions........................................ 6 - 4  





































 



1 Human Interface Manager (HIM)


1.1 Overview


1.1.1 Introduction

HIM (Human Interface Manager) is a library of more than 230 functions and macros
designed for use in C programs.  HIM makes designing and coding user interfaces
much easier by providing a rich set of functions designed specifically for
presenting information to, and obtaining information from a user of your
application.

1.1.2 Compilers Supported

The HIM library has been successfully tested using the Microsoft C V4.0, 5.0,
5.1 and Borland Turbo C V1.5 and 2.0 compilers.  Others will be supported in
the near future.

1.1.3 Components

HIM is divided into 7 separate categories, each performing a different task
relating to a user interface.
 
List Manager - With the List Manager your application can create a list, add and
delete any kind of data structure to the list, sort with the option of using
your comparision routine, and query items in the list via search, next, and
previous functions.
 
Keyboard Manager - No more messy switch statements every time you ask for a key.
Just tell the Keyboard Manager what function to call when a certain key is
pressed and the routing is handled for you!  Multiple input sources, outputs,
and journal files are supported as well as the ability to define a background
routine which will be called repeatably while waiting for input.
 
Window Manager - Yes, it does do windows (sorry, no floors).  Colors, titles on
4 sides, and a rich set of output and editing functions will give your
applications that snappy and professional look.  Flexible output with color is
available with our printf() look-alike, wnprintf().  Full data entry capability
is supported with our bullet-proof wninput() routine which supports all of the
C data types.
 
Help Manager - Nothing is appreciated more by a user than a program with
complete online documentation.  The Help Manager in combination with the
Keyboard Manager's ability to trap specific keycodes (F1 maybe??) gives you the
option of providing online help easily and painlessly.  All you need to do is
inform the help manager what help should be given at different points in your
program, when the user asks for help it will be there.
 
Menu Manager - The normally messy chore of providing menus is easy with the Menu
Manager, just create a menu, add menu items to it and call the process function!
Different flavors of menus such as Pop-Up, Pull-Down, and Lotus style Light-Bar
are available.  Menu elements can be made read-only dynamically so you can

                                                                        1 - 1  

                                                                                

disable user options if other criteria in your application have not been met.
In addition to full control over placement, menu items can have a C routine
assigned or another menu called when the element is picked by the user.
 
Forms Manager (optional) - Data entry couldn't be easier.  With the Forms
Manager you have the ability of completely defining a input screen, field types,
flow thru the screen, individual data field help, and validation.  Using these
functions in combination with the Form Painter program lets you code an
application in hours instead of days!
 
Form Painter (optional) - Used in combination with the Forms Manager, this nifty
utility lets you completely define forms "on-screen", enter help text, and
test the forms for proper input validation.  After the forms have been defined
you can keep them in their Screen Definition File (SDF) for later use at runtime
or create C source code which becomes part of your finished application program.

1.1.4 Notational Conventions

The following notational conventions are used throughout this manual:
 
Italics - Italics are used for the names of arguments to library routines.  In
an actual program, a specific name or value replaces the italicized argument
name.  In an actual program, the user supplies a particular argument for the
placeholder lnum.  In the description text of a routine, parameter names are
italicized so that you can scan the text and easily find the section pertaining
to the parameter of interest.
 
Examples - Programming examples are displayed in a special typeface to resemble
the output on your screen.  Note that comments in the examples are not delimited
by /* and */ in order to produce cleaner text.  If you use the program fragments
or examples you will need to delimit comments with /* and */.
 
Ellipsis dots - Vertical ellipsis dots are used in program example to indicate
that a portion of the program is omitted.  For instatnce, in the following
example, the ellipsis dots between the two statements indicate that intervening
program lines occur but are not shown:
 
int lnum;
 
lnum = lmcreate(NULL,0,0);
    .
    .
    .
lmdestroy(lnum);
 
Horizontal ellipsis dots following an item indicate that more items having the
same form may appear.  For instance,
 
   ={ expression [,expression]...}
 
indicates that one or more expressions separated by commas may appear between
the braces ({ }).



                                                                        1 - 2  

                                                                                

1.2 Getting Started

This section describes what's in the HIM Library disk set, information regarding
compiling and linking, and a skeleton program which illustrates the hardest part
of any program, getting started.

1.2.1 Backing Up Your Disks

Since the distribution disks are not copy protected in any way, the normal DOS
DISKCOPY command will work just fine.  Consult your DOS reference manual
regarding DISKCOPY.

1.2.2 Disk Contents

There is a file named DISKCONT.DOC on the disk 1 distribution floppy which
contains a listing of all distribution disks.

1.2.3 Include Files

Each package in the HIM Library has a .h include file.  These files MUST be
included into your application source using the #include preprocessor directive.
For ease of updating later, put the Forms Processing include files in a separate
directory and then add this directory to your environment variable INCLUDE.
This environmental variable is filled in using the DOS SET command:
 
   SET INCLUDE=directory1;directory2...
 
When the Microsoft C compiler sees a #include line it will search each of the
directories specified in the above INCLUDE variable.
 
If using Turbo C, the file TURBOC.CFG must have a line for each directory to be
searched of the form:
 
    -Idirectory1
    -Idirectory2
 
See your compiler reference manual for further details.

1.2.4 Library Files

HIM has one library for each of the 4 memory models:
 
    himmss - Microsoft Small Model Library
    himmsm - Microsoft Medium Model Library
    himmsc - Microsoft Compact Model Library
    himmsl - Microsoft Large Model Library
 
    himtcs - Turbo C Small Model Library
    himtcm - Turbo C Medium Model Library
    himtcc - Turbo C Compact Model Library
    himtcl - Turbo C Large Model Library
 
The large model library can be used for Huge model programs.  In order for the
linker to find your libraries you must tell it where to search,  this is handled

                                                                        1 - 3  

                                                                                

by defining an environmental variable LIB= using the DOS SET command:
 
   SET LIB=directory1;directory2
 
By putting the HIM Library in one of the directories specified in the SET LIB=
command you need only specify the library name on the link line, not the entire
path.
 
If using Turbo C, the file TURBOC.CFG must have a line for each directory to be
searched of the form:
 
    -Ldirectory1
    -Ldirectory2
 
MAKE SURE that the library version matches the compiler version you're using.
The Turbo C HIM library for V1.5 will not work with a Turbo C V2.0 compiler.
Specify the correct compiler and version when ordering.

1.2.5 Skeleton MAIN()

Below is a skeleton main() which illustrates the include files to use and
initialization of each module in the HIM package.  Note that this example
assumes you are using all modules of the package.  If you were not going to use
the Help Manager for example, you would not include its .h file and would
not call its initialization routine.  An important note is that the List Manager
is used by everybody and therfore MUST be initialized.  Also, each of the
initialization routines accept parameters which define how the package will
perform.  The parameters shown in the example are what most likely would be
used, you fill in the parameters to suit your application best.
 
  or
 
 
main()
/*****/
{
int kbhit(), getch();                 /* used in kminit() call */
 
lminit(malloc,free,0);                /* init list manager FIRST */
kminit(kbhit,getch);                  /* init keyboard manager SECOND */
wninit(0,0,NULL,malloc,free);         /* init window manager before menus */
mminit(kmgetch, NULL);                /* init menu manager after window */
hminit("goodhelp.hlp",0,0,0,          /* init help manager */
        WNBLACK,WNCYAN);
fpinit();                             /* init forms manager */
 
kmsir(KF1,hmhelp);                    /* setup keycode intercept of F1 to */
hmscontext("level1_help");            /* invoke help when pressed */
   .
   .                                  /* do your stuff */
   .
} /* end of main */



                                                                        1 - 4  

                                                                                

1.2.6 Compiling

Assuming your program source file is named "goodstuf.c", the command to compile
using Microsoft C V5.0 is:
 
    CL /c /AL goodstuf.c
 
The command for Turbo C V1.5 is:
 
    TCC -c -ml goodstuf.c
 
The /AL and -ml switches tells the compiler to compile for Large model.  The
default without the switch is Small model.  Case is important here.  Remember
to set the INCLUDE= variable to point to your include files if using Microsoft
or modify the TURBOC.CFG file if using Borland.

1.2.7 Linking

After compiling "goodstuf.c" you will end up with "goodstuf.obj" which needs to
be linked with the HIM Library as well as other .obj modules or libraries you
might have.  The link line to use for Microsoft Link V3.51 is:
 
    LINK/NOE/map goodstuf,goodstuf,goodstuf,himmsl;
 
The command for Turbo Link V1.xx and V2.0 is:
 
    TCC -ml -lm goodstuf.obj himtcl.lib
 
When using TCC, the -ml tells which model you used and is important because the
TCC shell will tell the linker which startup .obj and libraries to use
automatically.  The .ojb and .lib extension are also important.  It tells TCC
that you want to link, not compile.
 
Remember to set the LIB= variable to point to the subdirectory containing
himmsl.lib if using Microsoft or modify the TURBOC.CFG file if using Borland.

1.3 Shareware

Allsoft distributes HIM with the marketing approach called "shareware".  The
diskette(s) with the base library files (EXCLUDING forms and forms painter)
can be freely copied and shared with others, or purchased from Allsoft for a
small fee.  We ask you to help us distribute HIM by sharing unmodified copies
of the diskette, to make it easy for other people to try HIM.  We also permit
unlimited copying of the diskette(s) to make it easy for people in a company,
school, or other group to use HIM.
 
Support and continued development of HIM depends on programmers who "register"
their copy of the HIM library.  Registration has a number of benefits:
 
    - A hardbound copy of the full Human Interface Manager manual.
    - Diskettes with your unique registration number.
    - Allsoft support service for one year:
        - Compuserve E-mail for technical questions.
        - Software updates.

                                                                        1 - 5  

                                                                                

    - C source code for base HIM library (EXCLUDING forms and form painter).
    - Option to buy Forms Manager and Form Painter utility.
    - Thanks from us for your support and encouragement!
 
 
Your registration makes it possible for us to enhance HIM with new
features YOU want to see and support if you have technical problems or
questions.  We believe every user of HIM should have one of our manuals.
 
You MUST register if you incorporate any HIM routine(s) in a commercial software
program.  You must NOT use any HIM routine(s) in a competing product.  There is
no royalty due for registered users.
 
Registered owners receive a commission when someone else registers from one of
their copies.  People who like HIM register and give copies to friends or
associates with IBM PC's or compatibles.  The commission is our way of thanking
you for distributing HIM.
 
Allsoft sells HIM manuals and other materials in quantity.  Larger organizations
often copy the diskette and buy our manuals.  Registration for yearly support
service is available separately if you already have a manual.  Call or write
for a full price list.
 
We really do encourage you to give away HIM diskettes...with some restrictions.
As the copyright owner, Allsoft will permit you to sell or give away copies of
the HIM library(s) diskette, with the following restrictions:
 
    - You must NOT distribute the Forms Manager or Form Painter software.
    - You must distribute ALL files on the base HIM library diskette(s).
    - You must NOT distribute copies of the printed manual.
    - You must NOT distribute any files from the HIM SOURCE diskette(s).
    - You must use Allsoft copyright notices on media with Allsoft files.
    - You must use Allsoft trademark notices on "Allsoft" and "HIM".
 
You may add your own files, put files on several diskettes, distribute files
via modem, or compress files as long as their contents remain unchanged.  You
may print, copy, and distribute any text (OTHER THAN SOURCE CODE) contained
on the disks.

1.3.1 Registration

To register, send a check or call us with your Visa/MasterCard number.  We also
accept purchase orders from established companies or organizations.  If your
copy of HIM came from someone else, we need your old registration number to
credit the owner.  You can get your new registration number over the phone or
by mail on your diskette(s).  Use the order form following this section or
print the file HIMORDER.DOC to print your own.
 
When you get a registered copy from Allsoft, you receive new HIM diskettes with
your registration number on them.  Use this number for technical support and
make sure to write it on any copies you make for associates so that the
commission can be properly sent to you.



                                                                        1 - 6  

                                                                                

1.3.2 Technical Support

Technical support is obtained by one of two ways; phone call-back or Compuserve
E-mail.
 
    The phone call-back number is:
 
            (505) 821-7760
 
    The Compuserve E-Mail tech support account is:
 
            [76505,2014]
 
Be sure to give your registration number, name, and a voice phone number where
you can be reached.  If your problem is of any complexity don't bother
explaining it via E-mail, just leave your registration number, name, and phone,
voice is faster than typing!






































                                                                        1 - 7  

                                                                                

Allsoft ORDER FORM  (good thru 6/89)
 
SEND TO:
Allsoft                       Via Compuserve:
100 Calle Playa Del Sol NE         [76505,2014]
Albuquerque, NM  87109
(505) 821-7760
 
Quanity Item                        Price   Total
======= ====                        =====   =====
[   ]   HIM Diskettes               $18.00  _____
[   ]   Hardbound Manual            $45.00  _____
[   ]   Support (1 yr.)             $35.00  _____
[   ]   Full Registration           $89.00  _____
          Includes:
           - HIM Diskettes and manual
           - Support, 2 updates or C source code.
[   ]   Forms Manager
            Libraries (all models)  $75.00  _____
            Libraries and Source    $99.00  _____
[   ]   Form Painter (Source incl.) $49.00  _____
               Overseas Shipping    $20.00  _____
               NM orders add 5.25%          _____
               TOTAL                        _____
 
Note :  Forms Manager and Form Painter purchase
        requires full registration.
 
Registration Number on current disks : __________
 
[  ] Check  [  ] P.O.  [  ] Visa/MC
 
Visa/MC # : _____________________________________
Exp. Date : _____________________________________
Signature : _____________________________________
 
SHIP TO:
Name      : _____________________________________
Company   : _____________________________________
Address   : _____________________________________
City, St  : _____________________________________
Zip       : _____________________________________
Day Phone : _____________________________________
Compiler  : MSC5.0___ MSC5.1___ TC1.5___ TC2.0___











                                                                        1 - 8  



2 List Manager


2.1 Introduction

The List Manager is a collection of library routines which allow you to
manage lists of various flavors.
 
Some of the List Manager highlights:
 
    - Creation of up to 32767 lists
    - Ability to store header information with list
    - Elements in list can be "Marked" and "Unmarked"
    - Flexible ordering function for organizing lists
    - Object oriented
 
The last item, object oriented, is a useful feature that deserves some
explanation.  Unlike most library packages the List Manager routines do
not require that applications maintain pointers to complicated structures.
Instead, your application uses the package to create a list and in turn
receives an integer list number back.  This number is used to reference the
list in all other calls to the List Manager routines.  This has advantages
in that your application only has to manipulate a simple data type, an int,
and later changes to the internal list structure are transparent to older
applications

2.2 Symbolic Constants

The following symbolic constants can be found in the include file <lm.h>.

2.2.1 Error Constants

A successful List Manager function call will return a value greater than or
equal to zero.  An error condition will cause one of the following negative
values to be returned:
 
    Constant    Value   Description
    ========    =====   ===========
    LMMAERROR   -1      memory allocation error
    LMBLERROR   -2      bad list number
    LMBEERROR   -3      bad element number
    LMNOEL      -4      no more elements

2.2.2 List ordering constants

One of these constants can be used in the lmreorder() function:
 
    Constant    Value   Description
    ========    =====   ===========
    LMORIG       1      original order
    LMASC        2      ascending order
    LMDESC       3      descending order



                                                                        2 - 1  

                                                                                

2.3 Module Initialization

Before creating and using a list there needs to be a one time initialization
of the List Manager package.  This initializes internal data structures and
allows you to specify your own memory allocation/deallocation routines to be
used.  See the function  LMINIT()  for details on initialization.

2.4 Include Files

The C include file "lm.h" must be #includ'ed at the top of your application
source file in order to use the List Manager package.  This gives you
access to symbolic constants used by the packages as well as letting the
compiler do parameter type checking.

2.5 Function Overview

All List Manager functions return an error code value.  Zero or greater
indicates success.  The functions are:
 
elnum=  lmael(lnum,ptr,len,localf)      add an element to list lnum
lnum =  lmcreate(ptr,len,localf)        create new list w/optional header info
code =  lmdel(lnum,elnum)               delete an element.  -1 does all
code =  lmdestroy(lnum)                 destroy, release mem used by list.
stat =  lmelstat(lnum,elnum)            mark status of an element -1 tells any
elnum=  lmfindel(lnum,str,slen,casef,strt) search for an element
ptr  =  lmgel(lnum,elnum)               get ptr to an element in list lnum
elnum=  lmgfirstel(lnum)                get first el with current order
ptr  =  lmgheader(lnum)                 get pointer to header.
elnum=  lmglastel(lnum)                 get last el with current order
elnum=  lmgnextel(lnum)                 get next el with current order
num  =  lmgnumels(lnum)                 return number of elements in list.
elnum=  lmgprevel(lnum)                 get prev el with current order
code =  lminit(mar,mfr,debugf)          init package
code =  lmmarkel(lnum,elnum)            mark an element.  -1 does all
code =  lmreorder(lnum,order,croutine)  reorder list.  LMORIG, LMASC, or LMDESC
code =  lmsel(lnum,ptr,len,localf)      change size of data area for element
code =  lmunmarkel(lnum,elnum)          unmark an element  -1 does all

2.6 Function Definitions

These List Manager function definitions are presented in alphabetical order,
each starting on a new page, to facilitate your search for information.
Function definitions are comprised of the following sections:
 
  - Summary       - function and parameter declarations
  - Description   - detailed description
  - Return Value  - explanation of return values
  - See Also      - related functions
  - Example       - programming example
 
A negative return value by any function indicates an error.




                                                                        2 - 2  

                                                                          lmael

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmael(lnum, ptr, len, localf);
 
int  lnum;                            list number that element gets added to
char *ptr;                            points to element data
int  len;                             size of element data
int  localf;                          memory allocation flag

Description:

The lmael function is used to add something to an existing list.  You must first
create a list using lmcreate before you can add something to it.  Lnum is the
list number you're adding an element to, ptr points to the element data, len
is the size in characters of your data, and localf tells this function whether
or not to allocate memory for your element data and store it locally.  A value
of 0 supplied for len will cause this routine to assume that ptr points to a
null terminated string and the size (including null)  will be calculated for
you.  A value of 1 for localf will cause memory to be allocated and the data
pointed to by ptr will be copied into this allocated block.  Elements added to
a list via lmael are stored in the order they were added.  If you want a
particular order for later retrieval you must use the lmreorder function.

Return Value:

The lmael function returns a positive integer for future reference to this newly
added element.  A negative value will be returned if lnum is invalid or memory
allocation failed.  Symbolic error constants can be found in the include file
<lm.h>.

See Also:

lmdel, lmgel, lmsel

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum, elnum1, elnum2;
 
struct emp_info_s{
    char name[40];
    int  age;
    } employee;
 
lminit(malloc,free);                   init the list manager package
lnum = lmcreate(NULL,0,0);             create empty list without header
   .
   .
printf("\nEnter your name , age ");

                                                                        2 - 3  

                                                                          lmael

scanf("%s,%d", employee.name, &employee.age);
 
elnum1 = lmael(lnum,"Good Info1",0,0);              add string to list
elnum2 = lmael(lnum,&employee,sizeof(employee),1);  add employee record to list



















































                                                                        2 - 4  

                                                                        lmcreate

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmcreate(ptr, len, localf);
char *ptr;                        pointer to list header info
int  len;                         size of list header
int  localf;                      storage allocator flag

Description:

The lmcreate function is used to create an empty list with optional header
information.  Ptr is a pointer to a block of memory which holds important
information that you would like to be stored with the list structure.  If you do
not have any information to be stored with the list supply a value of NULL.  Len
is the size of your header structure in units of char.  Localf specifies whether
memory for your header information is needed.  If localf is set to 1, len amount
of memory will be allocated and your header information pointed to by ptr will
be copied into this memory block.  A value of 0 for localf causes just ptr to be
saved with the list.
 
If your list header information is known at compile time and is static then you
would want to supply a localf value of 0.  If you are building the header
structure at run time and have not allocated permanent storage for it, supply a
value of 1 for localf and the needed allocation will be done for you.  You can
later obtain a pointer to the allocated block by a call to the lmgheader
function.  If ptr is NULL, len and localf are ignored.  If a value of 0 is
supplied for len then it will be assumed that ptr points to a null terminated
string and the size (including the null) will be calculated for you.  If you
supply a non-zero value for len be sure to account for your null.

Return Value:

The lmcreate function returns a positive integer list number which you will need
in order to call other list manager functions.  A negative return value
indicates a memory allocation error.

See Also:

lmdestroy, lmael

Example:

#include   "malloc.h";
#include   "lm.h";
 
struct good_stuff_s{     header to be kept with list
    int   goodint;
    char  goodstr[80];
    } good_header;
int ln;                  to use our list later
 
lminit(malloc,free);     init the package

                                                                        2 - 5  

                                                                        lmcreate

ln = lmcreate(&good_header, sizeof(good_header), 1);






















































                                                                        2 - 6  

                                                                          lmdel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmdel(lnum,elnum);
int  lnum;                            list number
int  elnum;                           element number

Description:

The lmdel function is used to delete an element of a list.  If -1 is supplied as
elnum, all elements of lnum will be deleted.  Once all elements of a list have
been deleted it is neccessary to call lmdestroy to delete the empty list
structure.  Only memory allocated for local element data storage (localf == 1)
will be freed.

Return Value:

A return value of 0 indicates all went well.  A negative value means either lnum
or elnum was invalid.

See Also:

lmael, lmcreate

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum1,lnum2,elnum;
 
lminit(malloc,free);                   init the package
lnum1 = lmcreate(NULL,0,0);            create empty list wo/header
lnum2 = lmcreate("LIST #2",0,0);       create empty list w/header
elnum = lmael(lnum1,"Good_Info",0,0);  create element for list
lmael(lnum2,"Menu Item 1",0,0);        build another list
lmael(lnum2,"Menu Item 2",0,0);
lmael(lnum2,"Menu Item 3",0,0);
   .
   .
   .
lmdel(lnum1,elnum);                    delete 1 element from 1st list
lmdel(lnum2,-1);                       delete all elements from 2nd list










                                                                        2 - 7  

                                                                      lmdestroy

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int   lmdestroy(lnum);
int   lnum;                      list number to be destroyed

Description:

The lmdestroy function is used to destroy a list that was created with lmcreate.
Any memory that was allocated for list elements and header information will be
freed.  Lnum is the list number you wish to destroy.  Supplying a value of -1
for lnum will destroy ALL lists that have been created.  This function will only
free memory that was allocated for a list when the localf value in the lmcreate
call was set to 1.  You are responsible for your own static data structures.

Return Value:

This function returns a value of 0 if all went well.  A negative integer will be
returned if a bad list number is given (excluding -1).

See Also:

lmcreate, lminit, lmael

Example:

#include   "malloc.h";
#include   "lm.h";
 
int ln1, ln2;
 
lminit(malloc,free);                      init the package
ln1 = lmcreate("password=SECRET", 0, 0);  string is static so don't allocate
memory
ln2 = lmcreate(NULL,0,0);                 no header needed
    .
    .
    .
lmdestroy(-1);                            get rid of ALL lists created














                                                                        2 - 8  

                                                                        lmelstat

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmelstat(lnum,elnum);
int  lnum;                            list number
int  elnum;                           element number

Description:

The lmelstat function returns the "mark" status of element elnum in list lnum.
If -1 is supplied for elnum, the logical OR of all list elements will be
returned.  This allows to easily see if any elements are marked.

Return Value:

A value of 0 will be returned if the list element is "unmarked", 1 indicates the
element is "marked", and a negative return value indicates that lnum or elnum i
invalid.  All elements are initially created with a status of "unmarked".

See Also:

lmmarkel, lmunmarkel

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum, elnum;
char name[40];
char sex;
 
lminit(malloc,free);                  init the package
lnum = lmcreate(NULL,0,0);            create empty list
 
printf("\nEnter your name, sex <M|F> ");
scanf("%s,%c",name,&sex);
elnum = lmael(lnum,name,0,1);         add name to list
if (toupper(sex) == 'M')
    lmmarkel(lnum,elnum);             mark name if sex == male
   .
   .
   .
printf("\nName               Sex");
printf("\n======================");
printf("\n%19s%c",lmgel(lnum,elnum),(lmelstat(lnum,elnum) == 1)?'M':'F');







                                                                        2 - 9  

                                                                        lmfindel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmfindel(lnum,str,slen,casef,strt);
int  lnum;                                  list number
char *str;                                  search target
int  slen;                                  how many chars to match
int  casef;                                 case sensitive flag
int  strt;                                  start element

Description:

The lmfindel function is used to search for an item in a list.  Lnum is the list
to search, str is the string to search for, and strt sets the search starting
position in the list.  A value of 0 for casef signifies a case insensitive
search, 1 means case matters.  Only the first slen characters of str are looked
at in doing the search.  If slen is 0, the entire string is searched for.
 
If you want the search to start at the first element of lnum, set strt to 0.
Since lmfindel uses the retrieval functions lmgel and lmgnextel the list will be
traversed in the order that was set by lmreorder.
 
Note that this function is only good for searching list elements that are
strings.  If you need to search for binary data such as structures, create your
own search routine using lmgel, lmfirstel, and  lmnextel.

Return Value:

A positive integer return value from lmfindel indicates that an element matching
your search criteria was found.  This positive number will be the actual element
number which can be used in the retrieval routine lmgel.  A negative number
returned indicates a match was not found.

See Also:

lmgfirstel, lmgnextel, lmgprevel, lmglastel, lmgnumels

Example:

#include   "malloc.h";
#include   "lm.h";
 
int lnum, elnum;
 
lminit(malloc,free);                         init the package
lnum = lmcreate(NULL,0,0);                   create empty list wo/header
lmael(lnum,"Pyle, Gomer",0,0);               build a list of names
lmael(lnum,"Butts, Seymour",0,0);
lmael(lnum,"Peabody, Prisilla",0,0);
    .
    .
lmreorder(lnum,LMASC,(int (*)())NULL);       order list alphabetically

                                                                        2 - 10 

                                                                        lmfindel

elnum = lmfindel(lnum,"P",1,0,0);            will find "Peabody, Prisilla"
elnum = lmfindel(lnum,"Butts, Seymour ",0,0,0); no match.  Space after "Seymour"





















































                                                                        2 - 11 

                                                                          lmgel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
char  *lmgel(lnum,elnum);
int   lnum;                             list number
int   elnum;                            element number

Description:

The lmgel function obtains a pointer to list element elnum from list number
lnum.  The element must have been added using the lmael function.

Return Value:

A character pointer to the list element data is returned.  If list lnum or
element elnum doesn't exist, NULL will be returned.  Be sure to cast the
character pointer returned to the data type that was stored.

See Also:

lmael, lmsel

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum, elnum;
char *name[40];
 
lminit(malloc,free);                     init the package
lnum = lmcreate(NULL,0,0);               create list wo/header
    .
    .
printf("\nEnter your name");
scanf("%s",name);
elnum = lmael(lnum,name,0,1);            add name to list
















                                                                        2 - 12 

                                                                      lmgfirstel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmgfirstel(lnum);
int  lnum;                            list number

Description:

The lmgfirstel function will obtain the first element in list lnum.  "First"
depends on the ordering of your list.  If lmreorder has not been called then the
first element added with lmael will be obtained.

Return Value:

A positive integer returned indicates you now have the first element in the
list.  A negative return value means the list is empty or lnum is invalid.

See Also:

lmgnextel, lmgprevel, lmglastel, lmgnumels

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum;
 
lminit(malloc,free);                    init the package
lnum = lmcreate(NULL,0,0);              create empty list wo/header
lmael(lnum,"ZZZZ",0,0);                 build backward ordered list
lmael(lnum,"YYYY",0,0);
lmael(lnum,"XXXX",0,0);
    .
    .
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "ZZZZ" will print
lmreorder(lnum,LMASC,(int (*)())NULL);  now list is in ascending order
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "XXXX" will print















                                                                        2 - 13 

                                                                      lmgheader

Summary:

#include   "malloc.h";
#include   "lm.h";
 
char  *lmgheader(lnum);
int   lnum;                   list number

Description:

The lmgheader function obtains a pointer to the header information for list
number lnum.  The existence of this header information depends on what
parameters were passed in the call to lmcreate.

Return Value:

A character pointer to the header information specified for lmcreate will be
returned.  If header information doesn't exist for lnum, NULL will be returned.

See Also:

lmcreate

Example:

#include   "malloc.h";
#include   "lm.h";
 
lminit(malloc,free);                    init the package
ln = lmcreate("Heres my header",0,0);   create the list w/header
    .
    .
    .
printf("\Header == %s",lmgheader(ln));  print it





















                                                                        2 - 14 

                                                                      lmglastel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmglastel(lnum);
int  lnum;                            list number

Description:

The lmglastel function will obtain the last element in list lnum.  "Last"
depends on the ordering of your list.

Return Value:

A positive integer returned indicates you now have the last element in the list.
A negative return value means the list is empty or lnum is invalid.

See Also:

lmfirstel, lmgprevel, lmgnextel, lmgnumels

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum;
 
lminit(malloc,free);                    init the package
lnum = lmcreate(NULL,0,0);              create empty list wo/header
lmael(lnum,"ZZZZ",0,0);                 build backward ordered list
lmael(lnum,"YYYY",0,0);
lmael(lnum,"XXXX",0,0);
    .
    .
printf("\nlast element is %s",lmgel(lnum,lmglastel(lnum)));  "XXXX" will print
lmreorder(lnum,LMASC,(int (*)())NULL);  now list is in ascending order
printf("\nlast element is %s",lmgel(lnum,lmglastel(lnum)));  "ZZZZ" will print
















                                                                        2 - 15 

                                                                      lmgnextel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmgnextel(lnum);
int  lnum;                            list number

Description:

The lmgnextel function will obtain the next element in list lnum.  "Next"
depends on the ordering of your list and what retrieval function has been called
last.  Any list manager function that returns an element number sets an internal
pointer.  The lmgnextel and lmgprevel routines use this internal pointer in
deciding which element to return.

Return Value:

A positive integer returned indicates you now have the next element in the list.
A negative return value means there is no next element or lnum is invalid.

See Also:

lmfirstel, lmgprevel, lmglastel, lmgnumels

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum;
 
lminit(malloc,free);                    init the package
lnum = lmcreate(NULL,0,0);              create empty list wo/header
lmael(lnum,"ZZZZ",0,0);                 build backward ordered list
lmael(lnum,"YYYY",0,0);
lmael(lnum,"XXXX",0,0);
   .
   .
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "ZZZZ" will print
lmreorder(lnum,LMASC,(int (*)())NULL);  now list is in ascending order
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "XXXX" will print
printf("\nNext element is %s",lmgel(lnum,lmgnextel(lnum)));  "YYYY" will print












                                                                        2 - 16 

                                                                      lmgnumels

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmgnumels(lnum);
int  lnum;                            list number

Description:

The lmgnumels function returns the number of elements in a list.  All elements,
regardless of their "mark/unmark" status are counted.

Return Value:

The total number of elements in lnum is returned.  A negative value indicates an
invalid lnum value.

See Also:

lmael, lmgfirstel, lmgnextel

Example:

#include   "malloc.h";
#include   "lm.h";
 
int lnum;
 
lminit(malloc,free);                         init the package
lnum = lmcreate(NULL,0,0);                   create empty list wo/header
lmael(lnum,"item 1",0,0);                    build a list
lmael(lnum,"item 2",0,0);
    .
    .
    .
printf("\nThere are %d elements in list %d",lmgnumels(lnum),lnum);


















                                                                        2 - 17 

                                                                      lmgprevel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmgprevel(lnum);
int  lnum;                            list number

Description:

The lmgprevel function will obtain the previous element in list lnum.
"Previous" depends on the ordering of your list and what retrieval function has
been called last.  Any list manager function that returns an element number sets
an internal pointer.  The lmgnextel and lmgprevel routines use this internal
pointer in deciding which element to return.

Return Value:

A positive integer returned indicates you now have the previous element in the
list.  A negative return value means there is no previous element or lnum is
invalid.

See Also:

lmfirstel, lmgnextel, lmglastel, lmgnumels

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum;
 
lminit(malloc,free);                    init the package
lnum = lmcreate(NULL,0,0);              create empty list wo/header
lmael(lnum,"ZZZZ",0,0);                 build backward ordered list
lmael(lnum,"YYYY",0,0);
lmael(lnum,"XXXX",0,0);
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "ZZZZ" will print
lmreorder(lnum,LMASC,(int (*)())NULL);  now list is in ascending order
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "XXXX" will print
printf("\nnext element is %s",lmgel(lnum,lmgnextel(lnum)));  "YYYY" will print
printf("\nprev element is %s",lmgel(lnum,lmgprevel(lnum)));  "XXXX" will print












                                                                        2 - 18 

                                                                          lminit

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int     lminit(umar,umfr,debugf);
char    *(*mar)();                Pointer to memory allocation routine
void    (*mfr)();                 Pointer to memory free routine
int     debugf;                   true if internal node checks to be done

Description:

Lminit initializes the list manager package and must be called prior to
calling any other list manager routines.  Umar points to a function which
allocates, and returns a pointer to, a specified block of memory.  Umfr
points to a function which frees a previously allocated block of memory.
 
The synopsis for umar and umfr is:
 
char *(*umar)(size);
int  size;              number of characters to allocate
 
void (*umfr)(cptr);
char *cptr;             pointer to allocated block
 
If size characters of memory cannot be allocated by your supplied routine
umar then a value of NULL should be returned.  The supplied routine umfr will
never be called with cptr pointing to an invalid block of memory, therefore
your routine does not need to have this checking built in.
 
The reason for using supplied allocation/free routines is to give you a hand
in monitoring that all important resource, system memory.  If you do not want
to supply your own allocation/free routines then supply pointers to the built
in C library routines  malloc() and free().
 
The value of debugf determines if internal consistency checks are to be done
each time a list is accessed.  A value of one (1) turns the checks on, a
value of zero (0) turns them off.  When consistency checks are on, the list
manager runs very slow but can help when an errant pointer elsewhere in your
program decides to trash memory.  When checking is enabled (debugf == 1) and
a list node is determined to be corrupted a error message will be printed to
stderr and your program aborted.

Return Value:

The lminit() function always returns an integer value of 0.

See Also:

lmcreate, lmdestroy

Example:

#include   "malloc.h";

                                                                        2 - 19 

                                                                          lminit

#include   "lm.h";
 
lminit(malloc,free,0);  All allocation/free calls will be to library routines




















































                                                                        2 - 20 

                                                                        lmmarkel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmmarkel(lnum,elnum);
int  lnum;                          list number
int  elnum;                         element number

Description:

The lmmarkel function is used to "mark" element elnum is list lnum.  If -1 is
supplied for elnum, all elements in lnum will be marked.  This mark attribute is
for use by application routines you write and is not looked at by any of the
list manager functions.  When you create a new element via lmael, its mark
status is set to FALSE.

Return Value:

A return value of 0 indicates all went well.  A negative value indicates an
invalid list or element number.

See Also:

lmunmarkel, lmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
 
int lnum, el1, el2, el3;
 
lminit(malloc,free);                 init the package
lnum = lmcreate(NULL,0,0);           create list wo/header
el1  = lmael(lnum,"Bob",0,0);        build the list
el2  = lmael(lnum,"Samantha",0,0);
el3  = lmael(lnum,"Sonya",0,0);
lmmarkel(lnum,el1);                  mark the males
















                                                                        2 - 21 

                                                                      lmreorder

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmreorder(lnum,order,croutine);
int  lnum;                             list number
int  order;                            type of ordering
int  (*croutine)();                    compare routine

Description:

The lmreorder function is used to change the ordering of elements in a list.
Lnum is the list to be reordered, order indicates ascending, descending, or
original reordering, and croutine points to an optional comparision routine that
lmreorder is to use in sorting the list.
 
The following symbolic constants for order can be found in the include file
<lm.h>:
 
  Constant   Ordering
  ========   ========
  LMASC      Ascending order
  LMDESC     Descending order
  LMORIG     Original order elements were added via lmael
 
If croutine is supplied it must be written for the following synopsis:
 
int  (*croutine)(element1, element2, order);
char *element1, *element2;
int  order;
 
The return value expected back is:
 
    1 if element1 and element2 should be swapped based on order.
    0 if element1 and element2 should not be swapped based on order.
 
The criteria for determining what value your comparision should return is this:
 
    - Assume element1 and element2 are the only 2 elements of a list.
    - Assume element1 is the first element in the list.
 
    Depending on the value of order:
 
    -- If element1 and element2 need to be swapped, return 1.
    -- If element1 and element2 do not need to be swapped, return 0.
 
A built in string comparision routine will be used if croutine is set to
(int (*)())NULL.

Return Value:

A value of 0 will be returned if all went well.  A negative value indicates an
invalid value for lnum.

                                                                        2 - 22 

                                                                      lmreorder


See Also:

lmgfirstel, lmgnextel, lmglastel

Example:

#include   "malloc.h";
#include   "lm.h";
 
int  lnum;
 
lminit(malloc,free);                    init the package
lnum = lmcreate(NULL,0,0);              create empty list wo/header
lmael(lnum,"ZZZZ",0,0);                 build backward ordered list
lmael(lnum,"YYYY",0,0);
lmael(lnum,"XXXX",0,0);
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "ZZZZ" will print
lmreorder(lnum,LMASC,(int (*)())NULL);  now list is in ascending order
printf("\n1st element is %s",lmgel(lnum,lmgfirstel(lnum)));  "XXXX" will print



































                                                                        2 - 23 

                                                                          lmsel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmsel(lnum,elnum,ptr,len,localf);
int  lnum;                              list number
int  elnum;                             element number
char *ptr;                              pointer to new element data
int  len;                               size of new data
int  localf;                            storage allocation flag

Description:

The lmsel function is used when you need to change the size of a list element's
data area.  Lnum and elnum are the list and element number you're referencing.
Ptr, len, and localf perform the same function as in lmael.  Essentially, this
function allows you to change an elements data pointer, size, and/or storage
while keeping the same element number.

Return Value:

The lmsel function returns 0 if all went well.  A negative return value
indicates either a bad list number or element number, or a memory allocation
error.  Symbolic error constants can be found in the include file <lm.h>.

See Also:

lmael

Example:

#include   "malloc.h";
#include   "lm.h";
 
int lnum, elnum;
 
lminit(malloc,free);                     init the package
lnum = lmcreate(NULL,0,0);               create list wo/header
elnum = lmael(lnum,"Default data",0,0);  create an element
   .
   .
moddata(lnum,elnum);
   .
   .
 
moddata(lnum,elnum)
/*****************/
int  lnum, elnum;
{
char name[80];
 
printf("\nEnter your name");
scanf("%s",name);

                                                                        2 - 24 

                                                                          lmsel

lmsel(lnum,elnum,name,80,1);    store new element data.  Localf value of 1
                                will cause 81 bytes of memory to be allocated
                                and the contents of name[] will be copied
                                into the allocated block.
}


















































                                                                        2 - 25 

                                                                      lmunmarkel

Summary:

#include   "malloc.h";
#include   "lm.h";
 
int  lmunmarkel(lnum,elnum);
int  lnum;                          list number
int  elnum;                         element number

Description:

The lmunmarkel function is used to "unmark" element elnum is list lnum.  If -1
is supplied for elnum, all elements in lnum will be unmarked.  This mark
attribute is for use by application routines you write and is not looked at by
any of the list manager functions.  When you create a new element via lmael, its
mark status is set to FALSE.

Return Value:

A return value of 0 indicates all went well.  A negative value indicates an
invalid list or element number.

See Also:

lmmarkel, lmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
 
int lnum, el1, el2, el3;
 
lminit(malloc,free);                 init the package
lnum = lmcreate(NULL,0,0);           create list wo/header
el1  = lmael(lnum,"Bob",0,0);        build the list
el2  = lmael(lnum,"Samantha",0,0);
el3  = lmael(lnum,"Sonya",0,0);
lmmarkel(lnum,el1);                  mark the male
    .
    .
    .
lmunmarkel(lnum,-1);                 unmark all marked elements












                                                                        2 - 26 



3 Keyboard Manager


3.1 Introduction

The Keyboard Manager allows you great flexibility in obtaining and redirecting
keystrokes from a user while running your application.  Features include:
 
    - Input from keyboard, file, or defined input sources
    - Filtering allows input of function keys from all input sources
    - Input can be redirected to a file and/or defined outputs
    - Intercept functions can be called when a defined key is hit
    - Application defined background routine called before each key input
    - Object oriented

3.2 Components

As can be seen in Figure KM-1, the Keyboard Manager is made up of 4 separate and
complete modules, an input multiplexer, filter, redirector, and intercept
processor.
 
Multiplexer - The multiplexer provides a means of obtaining keycodes from many
different input sources, while as an added convenience has a mechanism for
calling a background function when waiting for input.  Referring to Figure KM-1,
the possible input sources to the multiplexer are the keyboard, text file, or
user supplied input functions.  All of these sources are definable by you and
there is no limit on the number of user input routines you can have.  An example
user input routine which reads a mouse and simulates arrow keys is supplied with
this package for your use.
 
Filter - The filter provides a mechanism for inputting non-printable ASCII
characters and IBM specific function keys from an input source other than the
keyboard.  If a character sequence of the form:  ~ddd   is encountered by the
filter it will be translated into a single keycode output, where  ddd  is the
decimal equivalent of the desired keycode.  This convention for representing
keycodes allows for easy input from a file or user input routines and is used by
the next module, the redirector.
 
Redirector - The redirector module has the ability to redirect keycodes to an
open journal file and/or user supplied output routines.  There is no limit on
the number of user output routines you can have and the file output will be put
in a form usable by the filter module.  Note that all keycodes entering this
module are passed to the calling routine in addition to the outputs.
 
Intercept Processor - This last module provides a very powerful function, that
of calling a user supplied routine whenever a certain keycode is encountered.  A
code returned by the keycode activated function determines if the code is passed
to the calling routine.







                                                                        3 - 1  

                                                                                

               Keyboard    File    Application Input Routines
                   \        |        /
                    \       |       /
               **************************
               *                        *
               *    Input Multiplexer   * ---> Background Routine
               *                        *
               **************************
                            |
                            | Code (0-255) or (300-432)
                           \|/
               **************************
               *                        *
               *          Filter        *
               *                        *
               **************************
                            |
                            | Code (0-255) or (300-432)
                           \|/
               **************************
               *                        * ---> File
               *       Redirector       *
               *                        * ---> Application Output Routines
               **************************
                            |
                            | Code (0-255) or (300-432)
                           \|/
               **************************
               *                        *
               *   Intercept Processor  * ---> Application Intercept Routines
               *                        *
               **************************
                            |
                            | Code (0-255) or (300-432)
                           \|/
 
                     Calling Routine
 
                       Figure KM-1
                    Keystroke Pipeline
 
Context Save/Restore - The last feature needing mention is the ability to push
and pop the current module context.  This allows a child subroutine, such as an
editor, to save the current state of the keyboard manager, reconfigure it to
its liking, and before exiting restore the package to the state it was in before
being called.  There is no limit on the depth of context nesting other than
available memory.








                                                                        3 - 2  

                                                                                


3.3 Symbolic Constants

All of the following constants are defined in the include file <km.h>.

3.3.1 Error Codes

Any negative return value indicates one of the following errors:
 
     Constant   Value  Description
     =============================================
     KMMAERROR   -1    Memory allocation error
     KMFOERROR   -2    File open error
     KMFCERROR   -3    File close error
     KMFRERROR   -4    File read error
     KMFWERROR   -5    File write error

3.3.2 UIR Function Codes

These are the possible operations that may be asked of a user supplied input
routine:
 
     Constant   Value  Description
     =============================================
     fuirsabort   1    Set active abort code
     fuirqabort   2    Is abort code pending?
     fuirchavail  3    Is character available?
     fuirgetch    4    Return a character

3.3.3 Keycode Definitions

Any keycode returned that is in the range 0-127 will map to a normal ASCII
character.  A keycode value >300 indicates that one of the keyboard function
keys has been pressed.  Here are constants that your applications should use
when looking for certain keycodes:
 
   Constant       Value    Description
   ==============================================
   KBELL          7        ctrl - g
   KBS            8        back space
   KTAB           9        tab
   KLF            10       line feed
   KFF            12       form feed
   KCR            13       enter
   KESC           27       escape
   KBTAB          315      shift tab
   KAA            330      alt - a
   KAB            348
   KAC            346
   KAD            332
   KAE            318
   KAF            333
   KAG            334
   KAH            335

                                                                        3 - 3  

                                                                                

   KAI            336
   KAJ            337
   KAK            338
   KAL            339
   KAM            350
   KAN            349
   KAO            324
   KAP            325
   KAQ            316
   KAR            319
   KAS            331
   KAT            320
   KAU            322
   KAV            347
   KAW            317
   KAX            345
   KAY            321
   KAZ            344
   KF1            359      Function key 1
   KF2            360
   KF3            361
   KF4            362
   KF5            363
   KF6            364
   KF7            365
   KF8            366
   KF9            367
   KF10           368
   KHOME          371      home
   KUP            372      up arrow
   KPGUP          373      page up
   KLEFT          375      left arrow
   KRIGHT         377      right arrow
   KEND           379      end
   KDOWN          380      down arrow
   KPGDN          381      page down
   KINS           382      Ins
   KDEL           383      Del
   KSF1           384      Shift F1
   KSF2           385
   KSF3           386
   KSF4           387
   KSF5           388
   KSF6           389
   KSF7           390
   KSF8           391
   KSF9           392
   KSF10          393
   KCF1           394      Ctrl - F1
   KCF2           395
   KCF3           396
   KCF4           397
   KCF5           398
   KCF6           399

                                                                        3 - 4  

                                                                                

   KCF7           400
   KCF8           401
   KCF9           402
   KCF10          403
   KAF1           404      Alt - F1
   KAF2           405
   KAF3           406
   KAF4           407
   KAF5           408
   KAF6           409
   KAF7           410
   KAF8           411
   KAF9           412
   KAF10          413
   KCPRTSC        414      ctrl - print screen
   KCLEFT         415      ctrl - left arrow
   KCRIGHT        416      ctrl - right arrow
   KCEND          417      ctrl - end
   KCPGDN         418      ctrl - pgdn
   KCHOME         419      ctrl - home
   KA1            420      alt 1  (top of keyboard)
   KA2            421
   KA3            422
   KA4            423
   KA5            424
   KA6            425
   KA7            426
   KA8            427
   KA9            428
   KA0            429
   KAMINUS        430      alt - (top of keyboard)
   KAEQUAL        431      alt =
   KCPGUP         432      ctrl - pgup
   KF11           433      Function key 11
   KF12           434
   KSF11          435      Shift F11
   KSF12          436
   KCF11          437      ctrl - F11
   KCF12          438
   KAF11          439      alt - F11
   KAF12          440

3.3.4 Module Initialization

Before the Keyboard Manager can be used it must be initialized.  This is
accomplished by calling the kminit function before any other Keyboard Manager
functions and AFTER calling the list manager initialization function lminit.
Since the Keyboard Manager makes extensive use of the List Manager it must be
initialized first.  By calling kminit you are allowing internal data structures
to be setup and telling the package which functions to call for obtaining a
"keyboard" character.  A skeleton initialization is given here:
 
                                     This file (km.h) MUST be included
 

                                                                        3 - 5  

                                                                                

int  kbhit(), getch();               used by keyboard manager
 
lminit(malloc,free,0);               initialize the list manager first
kminit(kbhit,getch);                 initialize the keyboard manager
 
The 2 function pointers supplied in the kminit call tell the package which
routines to call for determining when a keycode is ready (kbhit), and for
obtaining a keycode (getch).  You can supply pointers to your own routines by
following the following synopsis:
 
int  kbhit();                        returns non-zero if keycode ready
int  getch();                        waits for keycode then returns it
 
Note that the routine you supply in place of kbhit does not wait for a key, it
just reports whether or not one is ready.
 
If you intend to use other HIM routines it is important that you return codes
as given in the Symbolic Constants section otherwise it is up to you what codes
to return and how you use them.

3.3.5 Include Files

The C include file "km.h" must be #includ'ed at the top of your application
source file in order to use the Keyboard Manager package.  This gives you
access to symbolic constants used by the packages as well as letting the
compiler do parameter type checking.

3.3.6 Function Overview

All Keyboard Manager functions return an error code value.  Zero or greater
indicates success.  The functions are:
 
code    =   kmclosei()                  close input journal file
code    =   kmcloseo()                  close output journal file
            kmdbgr()                    delete background routine
            kmdir(keycode)              delete intercept routine for keycode
code    =   kmduir(unum)                delete user input routine
            kmduor(unum)                delete user output routine
ptr     =   kmgbgr()                    get pointer to background function
keycode =   kmgesc()                    get current filtering escape char
keycode =   kmgetch()                   wait for keycode from an input source
ptr     =   kmgir(keycode)              get pointer to intercept routine
ptr     =   kmguir(unum)                get pointer to user input routine
ptr     =   kmguor(unum)                get pointer to user output routine
code    =   kminit(kquery,kget)         init keyboard manager
code    =   kmkbhit()                   query if keycode available
code    =   kmopeni(filename)           open file for input
code    =   kmopeno(filename)           open file for output
code    =   kmpop()                     pop keyboard manager context
code    =   kmpush()                    push keyboard manager context
            kmresumebgr()               resume calling background routine
            kmresumei()                 resume input from input file
            kmresumeir(keycode)         resume intercept routine for keycode
            kmresumeo()                 resume output to output file

                                                                        3 - 6  

                                                                                

            kmresumeuir(unum)           resume input from user input routine
            kmresumeuor(unum)           resume output to user output routine
ptr     =   kmsbgr(ptr)                 register background routine
code    =   kmsesc(keycode)             register escape char for filtering
code    =   kmsir(keycode,ptr)          register intercept routine for keycode
code    =   kmsuir(ptr)                 register user input routine
code    =   kmsuor(ptr)                 register user output routine
            kmsuspendbgr()              suspend background routine
            kmsuspendi()                suspend input from open input file
            kmsuspendir(keycode)        suspend intercept routine for keycode
            kmsuspendo()                suspend output to open output file
            kmsuspenduir(unum)          suspend user input routine
            kmsuspenduor(unum)          suspend user output routine

3.3.7 Function Definitions

These List Manager function definitions are presented in alphabetical order,
each starting on a new page, to facilitate your search for information.
Function definitions are comprised of the following sections:
 
  - Summary       - function and parameter declarations
  - Description   - detailed description
  - Return Value  - explanation of return values
  - See Also      - related functions
  - Example       - programming example
 
A negative return value by any function indicates an error.




























                                                                        3 - 7  

                                                                        kmclosei

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmclosei();                    close input file

Description:

The kmclosei function is used to close an open keycode input file.

Return Value:

A 0 return value indicates a successful close while a negative value indicates
an error.  You will not get an error for closing an already closed file.

See Also:

kmcloseo, kmopeni, kmopeno, kmsuspendi, kmsuspendo

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
    .
    .
kmopeni("D:\\goodin.dat");         open input file
    .
    .
    .
kmclosei();                        close it

















                                                                        3 - 8  

                                                                        kmcloseo

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmcloseo();                    close output file

Description:

The kmcloseo function is used to close an open keycode output file.

Return Value:

A 0 return value indicates a successful close while a negative value indicates
an error.  You will not get an error for closing an already closed file.

See Also:

kmclosei, kmopeni, kmopeno, kmsuspendi, kmsuspendo

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
    .
    .
kmopeno("D:\\goodout.dat");        open output file
    .
    .
    .
kmcloseo();                        close it

















                                                                        3 - 9  

                                                                          kmdbgr

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  kmdbgr();                  delete background routine

Description:

The kmdbgr functions is used to delete the currently registered background
routine.

Return Value:

The kmdbgr functions has no return value.

See Also:

kmsbgr, kmgbgr, kmsuspendbgr, kmresumebgr

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
 
int  kbhit(), getch();             used in kminit() call
void showtime();                   for kmsbgr() function call
void (*ptr)();                     for kmgbgr() function call
int  wnum;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wnum = wncreate(0,0,80,25,WNBLUE,
           WNCYAN,WNBLUE,WNCYAN);  open full screen window
kmsbgr(showtime);                  register background routine
ptr = kmgbgr();                    get pointer to current background
    .
    .                              do other stuff
    .
kmdbgr();                          delete current background routine
}
 
showtime()                         show time while waiting for key input
{
static long lasttime;
long nowtime;
long time();
struct tm *newtime;
 
if (time(&nowtime) != lasttime){   we'll display time if changed

                                                                        3 - 10 

                                                                          kmdbgr

    wnlocate(wnum,1,1);            position the cursor in main window
    newtime = localtime(&nowtime); get time in usable format
    wnprintf(wnum,"%s",
             asctime(newtime));    print time in upper left of window
    lasttime = nowtime;            update the status var
    }
}
















































                                                                        3 - 11 

                                                                          kmdir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmdir(keycode);                   delete intercept routine
int  keycode;                          keycode to intercept

Description:

The kmdir function will delete the intercept routine being called for keycode.
A value of -1 supplied for keycode will delete ALL intercept routines.

Return Value:

A value of 0 indicates all went well.  A negative return indicates an IR with
keycode does not exist.

See Also:

kmgir, kmsir, kmsuspendir, kmresumeir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  myhelproutine();              called when F1 is pressed
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
kmsir(KF1,myhelproutine);          register F1 as help key
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
kmsuspendir(KF1);                  don't give help for password
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
kmresumeir(KF1);                   make help active again
    .

                                                                        3 - 12 

                                                                          kmdir

    .
    .
kmduor(-1);                        delete ALL output routines
kmdir(-1);                         delete ALL intercept routines
    .
    .
    .
myhelproutine(code)                called when F1 is pressed
/*****************/
int code;                          current key being input
{
    .                              this would be a help routine
    .                              for your user.  Instead of writing
    .                              your own, use the Help Manager!
}








































                                                                        3 - 13 

                                                                          kmduir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmduir(unum);                delete UIR
int  unum;                        user input routine number

Description:

The kmduir routine will delete UIR unum from the internal list of input sources.
A value of -1 supplied as unum will delete ALL user input routines.

Return Value:

The kmduir function returns 0 if all went well.  A negative return indicates
an invalid unum.

See Also:

kmguir, kmsuir, kmsuspenduir, kmresumeuir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
see kmsuir for example

























                                                                        3 - 14 

                                                                          kmduor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmduor(unum);                delete UOR
int  unum;                        user output routine number

Description:

The kmduor function is used to delete a User Output Routine (UOR).
 
A value of -1 for unum will cause the kmduor function to delete ALL registered
User Output Routines.

Return Value:

A value of 0 indicates all went well.  A negative return indicates an invalid
unum.

See Also:

kmguor, kmsuor, kmsuspenduor, kmresumeuor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
    .
    .
    .

                                                                        3 - 15 

                                                                          kmduor

kmduor(-1);                        delete ALL output routines






















































                                                                        3 - 16 

                                                                          kmgbgr

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  (*kmgbgr())();             get pointer to background routine

Description:

The kmgbgr function is used to get a pointer to the currently registered
background routine.

Return Value:

The kmgbgr will return a pointer to the currently registered background
routine.  If there is no background routine a value of  (void (*)())NULL
is returned.

See Also:

kmsbgr, kmdbgr, kmsuspendbgr, kmresumebgr

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
 
int  kbhit(), getch();             used in kminit() call
void showtime();                   for kmsbgr() function call
void (*ptr)();                     for kmgbgr() function call
int  wnum;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wnum = wncreate(0,0,80,25,WNBLUE,
           WNCYAN,WNBLUE,WNCYAN);  open full screen window
kmsbgr(showtime);                  register background routine
ptr = kmgbgr();                    get pointer to current background
    .
    .                              do other stuff
    .
kmdbgr();                          delete current background routine
}
 
showtime()                         show time while waiting for key input
{
static long lasttime;
long nowtime;
long time();
struct tm *newtime;

                                                                        3 - 17 

                                                                          kmgbgr

 
if (time(&nowtime) != lasttime){   we'll display time if changed
    wnlocate(wnum,1,1);            position the cursor in main window
    newtime = localtime(&nowtime); get time in usable format
    wnprintf(wnum,"%s",
             asctime(newtime));    print time in upper left of window
    lasttime = nowtime;            update the status var
    }
}














































                                                                        3 - 18 

                                                                          kmgesc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int     kmgesc();                   get escape character
int     kmsesc(ch);                 set escape character
int     ch;                         new escape character

Description:

The kmgesc function is used to obtain the current filter "escape" character
while kmsesc is used to set a new escape character.
 
The "escape" character is the one character the user types in order to signal
the keyboard manager that they are entering a 3 digit keycode.
 
At initialization, the escape code is a tilde (~) character.  If the user
wanted to input the keycode for Ctrl-G  he/she could type ~007 and the
keyboard manager would only pass one keycode (ctrl-g) to the calling
application.
 
Note that the escape code setting does not get passed to the new keyboard
context if a kmpush is done.

Return Value:

The kmgesc function returns the current escape character.  The kmsesc function
has no return value.

See Also:

kmpush, kmpop

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
 
kmsesc('$');                       use dollar sign as trigger







                                                                        3 - 19 

                                                                        kmgetch

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmgetch();

Description:

The kmgetch function is used to obtain a keycode from the Keyboard Manager.
Unlike the kmkbhit function, this routine will not return until a keycode is
available from an input source.  If a particular input source was active the
last time this function was called, that source will be the first one queried
for a keycode.
 
While this routine is waiting for a keycode from an input source the registered
background routine (if any) will be called repeatabley.  Also, no matter what
input source is active, if another input source has an abort character pending
it will be passed thru.  An example of this would be if keycodes were coming
from an input file but the user pressed the abort code at the keyboard.
Normally you would not want mixing of input characters like this but the abort
code is the exception.

Return Value:

A keycode in one of the ranges 0-127 or 300-432 will be returned.  A keycode in
the range 0-127 indicates the user entered a normal ASCII character while a
keycode in the range 300-432 indicates a function key was input.

See Also:

kmkbhit, kmopeni, kmsbgr, kmsuir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
 
c = kmgetch();                     wait for a keycode








                                                                        3 - 20 

                                                                          kmgir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  (*kmgir(keycode))();              get pointer to intercept routine
int  keycode;                          keycode to intercept

Description:

The kmgir function obtains a pointer to the intercept routine registered for
keycode.  This allows a subroutine to reassign a keycode and put it back before
returning (a better way is to use kmpush and kmpop).

Return Value:

Kmgir will return a pointer to the routine being called when keycode is input.
A value of (void (*)())NULL  will be returned if there is no intercept routine
registered for keycode.

See Also:

kmsir, kmdir, kmsuspendir, kmresumeir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  myhelproutine();              called when F1 is pressed
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
kmsir(KF1,myhelproutine);          register F1 as help key
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
kmsuspendir(KF1);                  don't give help for password
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output

                                                                        3 - 21 

                                                                          kmgir

kmresumeir(KF1);                   make help active again
    .
    .
    .
kmduor(-1);                        delete ALL output routines
kmdir(-1);                         delete ALL intercept routines
    .
    .
    .
myhelproutine(code)                called when F1 is pressed
/*****************/
int code;                          current key being input
{
    .                              this would be a help routine
    .                              for your user.  Instead of writing
    .                              your own, use the Help Manager!
}






































                                                                        3 - 22 

                                                                          kmguir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  (*kmguir(unum))();           get pointer to UIR
int  unum;                        user input routine number

Description:

The kmguir function will return a pointer to user input routine unum.

Return Value:

A pointer to User Input Routine unum will be returned by kmguir.  If unum does
not exist, a value of  int  (*)())NULL  will be returned.

See Also:

kmsuir, kmduir, kmsuspenduir, kmresumeuir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
see kmsuir for example


























                                                                        3 - 23 

                                                                          kmguor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  (*kmguor(unum))();           get pointer to UOR
int  unum;                        user output routine number

Description:

The kmguor function is used to get a pointer to a User Output Routine (UOR).

Return Value:

The kmguor function returns a pointer to registered UOR unum or
(void (*)())NULL  if unum is invalid.

See Also:

kmsuor, kmduor, kmsuspenduor, kmresumeuor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
    .
    .
    .
kmduor(-1);                        delete ALL output routines



                                                                        3 - 24 

                                                                          kminit

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kminit(kquery,kget);
int  (*kquery)();                   keycode ready? routine
int  (*kget)();                     keycode fetch routine

Description:

The kminit function is used to initialize the Keyboard Manager and must be
called before any other Keyboard Manager routines and AFTER the List Manager
lminit function.  Kquery is a pointer to a function which will be called when
the Keyboard Manager needs to know if a keycode is ready while kget points to a
function which will be called when the package needs to fetch a keycode.  Under
normal circumstances you will supply pointers to the built in functions kbhit
and getch.
 
Since the Keyboard Manager makes extensive use of the List Manager it is
important to call lminit before any other routines.

Return Value:

A value of 0 will be returned if all went well.  A negative return value
indicates a memory allocation error was returned from a call to the List
Manager.

See Also:

kmkbhit, kmgetch

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
 
lminit(malloc,free);               init the list manager
kminit(kbhit,getch,0);             init the keyboard manager












                                                                        3 - 25 

                                                                        kmkbhit

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmkbhit();

Description:

The kmkbhit function is used to tell if there is a keycode available from the
Keyboard Manager.  All input sources are (keyboard, file, user input routines)
are queried and if a keycode is available this function will return a true
value.
 
Note that if the user is in the midst of entering a manual keycode (see kmsesc)
you will not get a true status returned even though actual keycodes have been
entered.
 
If there is an active background routine registered it will be called before any
input sources are queried.

Return Value:

A non-zero return value indicates a keycode is available for fetching via
kmgetch.  A zero value means there are no keycodes available.

See Also:

kmgetch

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free);               init the list manager
kminit(kbhit,getch);               init the keyboard manager
    .
    .
while (!kmkbhit())
   ;                               wait for keycode
c = kmgetch();                     get the keycode








                                                                        3 - 26 

                                                                        kmopeni

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmopeni(filename);
char *filename;                    input file

Description:

The kmopeni function is used to open an ASCII text file pointed to by filename
which will be used as an input source when obtaining keycodes.  If there are no
other active input sources all keycodes will be obtained from the text file
until it is empty, suspended, or closed.
 
To represent non-printing ASCII characters and function keys in the text file
use the following format:  ~xxx   Where xxx is the 3 digit decimal keycode
preceded by the tilde (~) character.  Here are some examples:
 
    character/key        code
    ============================
    Ctrl-C               ~003
    ESC                  ~027
    Tilde (~)            ~126
    F10 function key     ~368
 
Note that even though keycodes are being obtained from a file it is possible for
another input source (keyboard, user input routine) to supply the active abort
character.  In this case the abort character will be passed thru to the calling
application.
 
If the filename you specify is not found in the current directory then all
directories found in the environment PATH specification will be searched.

Return Value:

The kmopeni function returns 0 if all went well.  A negative value indicates an
error.  Error codes can be found in the include file <km.h>.

See Also:

kmclosei, kmsuspendi, kmresumei, kmsesc, kmfgesc

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager

                                                                        3 - 27 

                                                                        kmopeni

    .
    .
    .
kmopeni("D:\\goodin.txt");         open input file



















































                                                                        3 - 28 

                                                                        kmopeno

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmopeno(filename);
char *filename;                    output file

Description:

The kmopeno function is used to open an ASCII text file pointed to by filename
which will receive all input keycodes.  After opening this output file, all
input keycodes will be written to this file in addition to being supplied to the
calling routine.
 
To represent non-printing ASCII characters and function keys in the text file
the following format will be used:  ~xxx   Where xxx is the 3 digit decimal
keycode followed by the tilde (~) character.  Here are some examples:
 
    character/key        code
    ============================
    Ctrl-C               ~003
    ESC                  ~027
    Tilde (~)            ~126
    F10 function key     ~368

Return Value:

The kmopeno function returns 0 if all went well.  A negative value indicates an
error.  Error codes can be found in the include file <km.h>.

See Also:

kmcloseo, kmsuspendo, kmresumeo

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
    .
    .
    .
kmopeno("D:\\goodout.txt");        open output file





                                                                        3 - 29 

                                                                          kmpop

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
kmpop();                             pop to previous context

Description:

The kmpop function will restore the context of the Keyboard Manager to what it
was prior to calling kmpush.

Return Value:

A value of 0 is returned if all went well.  A negative value indicates you
are at the top level and can't pop any further.

See Also:

kmpush, kminit, kmsuir, kmsuor, kmsir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  myhelproutine();              called when F1 is pressed
int  dosomething();                a do something routine
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
kmsir(KF1,myhelproutine);          register F1 as help key
kmsir(KF10,dosomething);           F10 will cause dosomething() to be called
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
kmsuspendir(KF1);                  don't give help for password
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
kmresumeir(KF1);                   make help active again

                                                                        3 - 30 

                                                                          kmpop

    .
    .
    .
kmduor(-1);                        delete ALL output routines
kmdir(-1);                         delete ALL intercept routines
    .
    .
    .
myhelproutine(code)                called when F1 is pressed
/*****************/
int code;                          current key being input
{
    .                              this would be a help routine
    .                              for your user.  Instead of writing
    .                              your own, use the Help Manager!
}
 
dosomething(code)
/****************/                 called when F10 is pressed
int code;
{
kmpush();                          save current context
    .
    .                              now, the entire keyboard manager could be
    .                              reconfigured.
kmpop();                           And now the previous state is restored
}




























                                                                        3 - 31 

                                                                          kmpush

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmpush();                        push current context

Description:

The kmpush function will save the current context of the Keyboard Manager
including all input sources, filter character, outputs, and intercept routines.
After the push the Keyboard Manager will be in the same state as just after
calling kminit.

Return Value:

The kmpush function will return 0 if all went well or a negative value if an
error occured.

See Also:

kmpop, kminit, kmsuir, kmsuor, kmsir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  myhelproutine();              called when F1 is pressed
int  dosomething();                a do something routine
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
kmsir(KF1,myhelproutine);          register F1 as help key
kmsir(KF10,dosomething);           F10 will cause dosomething() to be called
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
kmsuspendir(KF1);                  don't give help for password
getpassword();                     call a useful routine

                                                                        3 - 32 

                                                                          kmpush

kmresumeuor(unum);                 resume output
kmresumeir(KF1);                   make help active again
    .
    .
    .
kmduor(-1);                        delete ALL output routines
kmdir(-1);                         delete ALL intercept routines
    .
    .
    .
myhelproutine(code)                called when F1 is pressed
/*****************/
int code;                          current key being input
{
    .                              this would be a help routine
    .                              for your user.  Instead of writing
    .                              your own, use the Help Manager!
}
 
dosomething(code)
/****************/                 called when F10 is pressed
int code;
{
kmpush();                          save current context
    .
    .                              now, the entire keyboard manager could be
    .                              reconfigured.
kmpop();                           And now the previous state is restored
}


























                                                                        3 - 33 

                                                                    kmresumebgr

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  kmresumebgr();

Description:

The kmresumebgr function resumes calling the registered background routine.

Return Value:

This function has no return value.

See Also:

kmsuspendbgr, kmsbgr, kmgbgr, kmdbgr

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
 
int  kbhit(), getch();             used in kminit() call
void showtime();                   for kmsbgr() function call
int  wnum;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wnum = wncreate(0,0,80,25,WNBLUE,
           WNCYAN,WNBLUE,WNCYAN);  open full screen window
kmsbgr(showtime);                  register background routine
    .
    .                              do other stuff
    .
kmsuspendbgr();                    stop displaying time for awhile
    .
    .
    .
kmresumebgr();                     resume showing time
}
 
showtime()                        show time while waiting for key input
{
static long lasttime;
long nowtime;
long time();
struct tm *newtime;
 

                                                                        3 - 34 

                                                                    kmresumebgr

if (time(&nowtime) != lasttime){   we'll display time if changed
    wnlocate(wnum,1,1);            position the cursor in main window
    newtime = localtime(&nowtime); get time in usable format
    wnprintf(wnum,"%s",
             asctime(newtime));    print time in upper left of window
    lasttime = nowtime;            update the status var
    }
}















































                                                                        3 - 35 

                                                                      kmresumei

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  kmresumei();                 resume input from file

Description:

The kmresumei function will resume input from a suspended input file.

Return Value:

This function has no return value.  It will not cause any problem to resume a
file that is not suspended.

See Also:

kmresumeo, kmopeni, kmopeno, kmsuspendi, kmsuspendo

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free),0);            init the list manager
kminit(kbhit,getch);               init the keyboard manager
kmopeni("goodin.put");             read keycodes from an input file
while ((c = kmgetch()) != KESC)
    ...                            do something
kmsuspendi();                      suspend the input file
    ...                            now process the keyboard
kmresumei();                       resume input from file

















                                                                        3 - 36 

                                                                      kmresumeir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int   kmresumeir(keycode);              resume a suspended intercept routine
int   keycode;                          intercept routine to suspend/resume

Description:

The kmresumeir function will resume a suspended intercept routine.  A value
of -1 for keycode will resume ALL suspended interception routines.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid keycode.

See Also:

kmsuspendir, kmsir, kmgir, kmdir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  myhelproutine();              called when F1 is pressed
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
kmsir(KF1,myhelproutine);          register F1 as help key
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
 
kmsuspenduor(unum);                suspend output for awhile
kmsuspendir(KF1);                  don't give help for password
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
kmresumeir(KF1);                   make help active again

                                                                        3 - 37 

                                                                      kmresumeir

    .
    .
    .
kmduor(-1);                        delete ALL output routines
kmdir(-1);                         delete ALL intercept routines
    .
    .
    .
myhelproutine(code)                called when F1 is pressed
/*****************/
int code;                          current key being input
{
    .                              this would be a help routine
    .                              for your user.  Instead of writing
    .                              your own, use the Help Manager!
}







































                                                                        3 - 38 

                                                                      kmresumeo

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  kmresumeo();                 resume output to file

Description:

The kmresumeo function will resume output to a suspended output file.

Return Value:

This function has no return value.  It will not cause any problem to resume a
file that is not suspended.

See Also:

kmresumei, kmopeni, kmopeno, kmsuspendi, kmsuspendo

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free);               init the list manager
kminit(kbhit,getch);               init the keyboard manager
kmopeno("goodout.put");            put keycodes to a journal file
while ((c = kmgetch()) != KESC)
    ...                            do something
kmsuspendo();                      suspend the output file
    ...                            now process the keyboard
kmresumeo();                       resume output to file

















                                                                        3 - 39 

                                                                    kmresumeuir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int   kmresumeuir(unum);               resume a user input routine
int   unum;                            uir number to suspend/resume

Description:

The kmresumeuir function is used to resume input from user input routine unum.
A value of -1 supplied for unum will resume ALL suspended user input routines.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid unum.

See Also:

kmsuspenduir, kmsuir, kmguir, kmduir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  goodroutine();                our user input routine
int  myuir;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
myuir = kmsuir(goodroutine);       register goodroutine as an input source
    .
    .
kmsuspenduir(myuir);               turn off goodroutine as an input source
    .
    .
    .
kmresumeuir(myuir);                resume input from goodroutine












                                                                        3 - 40 

                                                                    kmresumeuor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int   kmresumeuor(unum);               resume a user output routine
int   unum;                            UOR to suspend/resume

Description:

The kmresumeuor function will resume a suspended UOR.  A value of -1 supplied
for unum will cause all suspended UOR's to be resumed.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid unum.

See Also:

kmsuspenduor, kmsuor, kmduor, kmguor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
    .
    .
    .
kmduor(-1);                        delete ALL output routines


                                                                        3 - 41 

                                                                          kmsbgr

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  (*kmsbgr(ptr))();          set pointer to background routine
void  (*ptr)();                  pointer to background routine

Description:

The kmsbgr function is used to register a background routine.  The function
pointed to by ptr will be called by the Keyboard Manager once before each
keycode is input and repeatedly while waiting for input.  An integer
parameter will be passed to your background routine which tells you which
input source is currently supplying characters:
 
    Constant    Source
    ========    ======
    KFILE       Input file is feeding input.
    KKBD        Keyboard is feeding input.
    KNONE       All sources idle, waiting for input.
A value greater than 0 indicates a user input routine (UIR) is the current
source with the value being the UIR number.  No return value is expected from
your background routine.
 
If you would like more than 1 background routine to be called you will have to
utilize the kmgbgr function and build the chain of functions yourself.

Return Value:

The kmsbgr function returns a pointer to the background routine that existed
before this call.

See Also:

kmgbgr, kmdbgr, kmsuspendbgr, kmresumebgr

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
 
int  kbhit(), getch();             used in kminit() call
void showtime();                   for kmsbgr() function call
void (*ptr)();                     for kmgbgr() function call
int  wnum;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wnum = wncreate(0,0,80,25,WNBLUE,

                                                                        3 - 42 

                                                                          kmsbgr

           WNCYAN,WNBLUE,WNCYAN);  open full screen window
kmsbgr(showtime);                  register background routine
ptr = kmgbgr();                    get pointer to current background
    .
    .                              do other stuff
    .
kmdbgr();                          delete current background routine
}
 
showtime()                         show time while waiting for key input
{
static long lasttime;
long nowtime;
long time();
struct tm *newtime;
 
if (time(&nowtime) != lasttime){   we'll display time if changed
    wnlocate(wnum,1,1);            position the cursor in main window
    newtime = localtime(&nowtime); get time in usable format
    wnprintf(wnum,"%s",
             asctime(newtime));    print time in upper left of window
    lasttime = nowtime;            update the status var
    }
}































                                                                        3 - 43 

                                                                          kmsesc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int     kmgesc();                   get escape character
int     kmsesc(ch);                 set escape character
int     ch;                         new escape character

Description:

The kmgesc function is used to obtain the current filter "escape" character
while kmsesc is used to set a new escape character.
 
The "escape" character is the one character the user types in order to signal
the keyboard manager that they are entering a 3 digit keycode.
 
At initialization, the escape code is a tilde (~) character.  If the user
wanted to input the keycode for Ctrl-G  he/she could type ~007 and the
keyboard manager would only pass one keycode (ctrl-g) to the calling
application.
 
Note that the escape code setting does not get passed to the new keyboard
context if a kmpush is done.

Return Value:

The kmgesc function returns the current escape character.  The kmsesc function
returns the escape character that existed before the call.

See Also:

kmpush, kmpop

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
 
kmsesc('$');                       use dollar sign as trigger







                                                                        3 - 44 

                                                                          kmsir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmsir(keycode, ptr);              register intercept routine
int  keycode;                          keycode to intercept
int  (*ptr)();                         pointer to intercept routine

Description:

The kmsir function is used to register a user supplied Intercept Routine.
Ptr points to the intercept routine that will be called when keycode is input
thru the Keyboard Manager.  When keycode is seen by the Keyboard Manager it
will be passed to ptr as follows:
 
        (*ptr)(keycode);
 
If your intercept routine returns a value of -1 keycode will NOT be passed to
the calling application.  Any other value WILL be passed.  Note that this allows
your "intercept" routine to do keycode filtering/translating as well as some
other useful action.

Return Value:

The kmsir function will return keycode if all went well.  A negative value
indicates an error.

See Also:

kmgir, kmdir, kmsuspendir, kmresumeir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  myhelproutine();              called when F1 is pressed
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
kmsir(KF1,myhelproutine);          register F1 as help key
    .

                                                                        3 - 45 

                                                                          kmsir

    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
kmsuspendir(KF1);                  don't give help for password
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
kmresumeir(KF1);                   make help active again
    .
    .
    .
kmduor(-1);                        delete ALL output routines
kmdir(-1);                         delete ALL intercept routines
    .
    .
    .
myhelproutine(code)                called when F1 is pressed
/*****************/
int code;                          current key being input
{
    .                              this would be a help routine
    .                              for your user.  Instead of writing
    .                              your own, use the Help Manager!
}






























                                                                        3 - 46 

                                                                          kmsuir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmsuir(ptr);                 set User Input Routine
int  (*ptr)();                    pointer to user input routine

Description:

The kmsuir is used to register a User Input Routine (UIR).
 
The kmsuir function adds the function pointed to by ptr to the internal list of
possible input sources.  When the Keyboard Manager needs input, ptr will be
queried along with all other input sources.  The function you supply as an input
source must be capable of responding to the following synopsis:
 
int  (ptr)(func,data);
int  func;                        function code
int  data;                        data to pass to your input function
 
Depending on func, your input function needs to do different things:
 
func == fuirsabort
If your input function is called by the Keyboard Manager with a func value of
fuirsabort you are being requested to make a note of the new abort code.  For
this function code, data will contain the new abort keycode.
 
func == fuirqabort
Your input function will be called with this function code when the Keyboard
Manager needs to know if your input source has the current abort code pending.
A non-zero return value from your input function indicates an abort code is
pending.
 
func == fuirchavail
This function code is asking your input routine if any keycode is pending.  A
non-zero return value from you indicates that a keycode is ready.
 
func == fuirgetch
This function call tells your input function to not return until a keycode is
available from its input.  The return value will be the input keycode.

Return Value:

A positive UIR number is returned from kmsuir if all went well.  A negative
number indicates an error (see km.h).

See Also:

kmguir, kmduir, kmsuspenduir, kmresumeuir




                                                                        3 - 47 

                                                                          kmsuir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
/*
mouseuir.c
 
This program will demonstrate how a mouse can be used to simulate arrow
keycodes with the Keyboard Manager package.  It will be registered as
a User Input Routine (UIR) and whenever movement of the mouse is noted the
correct arrow keycode will be sent to the Keyboard Manager.  Added
capabilities such as button command support is not present in this
example but could easily be added.
 
This program will create a window and place the cursor in the center.  As
the user enters arrow keycodes the cursor will be moved.  Hit the ESCAPE
key or press any mouse button to exit the program.
 
This program must be linked with the mouse driver library in addition to
the Forms Processing Lib.
 
NOTE:  The mouse driver must be loaded.
 
*/
 
 
 
int  m1,m2,m3,m4;
 
main()
/***********/
{
int  kbhit(),getch();           /* for kminit call */
int  crow,ccol,lrow,lcol;       /* current and last cursor row,col */
int  keycode;
int  wnum;                      /* window number */
int  uir;                       /* uir number from kmsuir() */
int  mouseuir();                /* our mouse User Input Routine */
 
lminit(malloc,free,0);          /* init list manager */
kminit(kbhit,getch);            /* init keyboard manager */
wninit(0,0,NULL,0,malloc,free); /* init window manager */
 
wnum = wncreate(0,0,80,25,WNBLUE,WNCYAN,WNBLUE,WNCYAN); /* create window */
wnttitle(wnum,"[ Mouse Tester ]");                      /* put up top title */
wnbtitle(wnum,"[ ESC or mouse button to exit ]");       /* bottom title */
 
m1 = 0;
MOUSE;                          /* see if driver is installed (m1==0) */
if (m1 != -1){
    wndestroy(wnum);            /* take down window */
    printf("\nSorry.  Mouse driver not found.");

                                                                        3 - 48 

                                                                          kmsuir

    exit(1);
    }
else{
    uir = kmsuir(mouseuir);     /* register User Input Routine */
    kmmsabort(KESC);            /* tell keyboard package what an abort is */
    crow = 10;
    lrow = -1;
    ccol = 40;
    lcol = -1;
    for (;;){
        if ((lrow != crow) || (lcol != ccol)){ /* don't move unless changed */
            wnlocate(wnum,crow,ccol);   /* position cursor */
            lrow = crow;
            lcol = ccol;        /* update last coords */
            }
        keycode = kmgetch();    /* get a key from keyboard manager */
        switch (keycode){
            case    KUP:        /* up arrow key */
                crow = (crow == 1)?crow:--crow;
                break;
            case    KDOWN:      /* down arrow key */
                crow = (crow == 23)?crow:++crow;
                break;
            case    KRIGHT:     /* right arrow key */
                ccol = (ccol == 78)?ccol:++ccol;
                break;
            case    KLEFT:      /* left arrow key */
                ccol = (ccol == 1)?ccol:--ccol;
                break;
            case    KESC:       /* escape keycode */
                wndestroy(wnum);/* take down window */
                exit(0);
                break;
            }
        }
    kmduir(uir);                /* remove from list just to be clean */
    }
wndestroy(wnum);
printf("\nbye bye...");
exit(0);
} /* end of main */
 
/************** User Input Routine section **************/
 
/* these global static vars are for the mouse input routines */
 
int  current_abort_code = KESC;
int  waiting_keycode[KQ];
int  nwaiting,in,out;
 
mouseuir(func,data)
/******************/
/* This is the actual user input routine which was registered via kmsuir()
   above.

                                                                        3 - 49 

                                                                          kmsuir

*/
int func,data;
{
int tkey;
 
switch(func){   /* a UIR must be capable of performing 4 functions: */
    case    fuirsabort:             /* set abort keycode */
        current_abort_code = data;
        break;
 
    case    fuirqabort:             /* is abort code pending */
        m1 = 3;                     /* get mouse position and button status */
        MOUSE;     /* call the mouse driver */
        if (m2 & 7){
            push_keycode(current_abort_code);
            return(1);              /* button down, return abort true */
            }
        else
            return(0);              /* no button down */
        break;
 
    case    fuirchavail:            /* keycode ready yet? */
        return(mouseuirchavail());
        break;
 
    case    fuirgetch:              /* don't return until char ready */
        while (!mouseuirchavail())
            ;                       /* wait for keycode */
        return(pop_keycode());
        break;
    }
} /* end of mouseuir */
 
mouseuirchavail()
/****************/
{
if (any_keycodes())
    return(1);
else{
    if (mouseuirbuttondown()){
        push_keycode(current_abort_code);
        return(1);                  /* yes, keycode is ready */
        }
    m1 = 11;                        /* get relative mouse movement */
    MOUSE;         /* call driver */
    if (m3 > 0)                     /* did mouse move to the right? */
        push_keycode(KRIGHT);
    else if (m3 < 0)                /* did mouse move to the left? */
        push_keycode(KLEFT);
    if (m4 > 0)                     /* did mouse move down? */
        push_keycode(KDOWN);
    else if (m4 < 0)                /* did mouse move up? */
        push_keycode(KUP);
 

                                                                        3 - 50 

                                                                          kmsuir

    return(any_keycodes());         /* return updated status */
    }
} /* end of mouseuirchavail */
 
mouseuirbuttondown()
/*******************/
{
m1 = 3;                             /* get mouse position and button status */
MOUSE;                              /* call driver */
if (m2 & 7)
    return(1);                      /* yes, button is down */
else
    return(0);
}
 
clear_keycodes()
/****************/
{
nwaiting = 0;
in = out = 0;
}
 
any_keycodes()
/*************/
{
return(nwaiting);
}
 
push_keycode(keycode)
/********************/
int keycode;
{
if (nwaiting < KQ){
    waiting_keycode[in++] = keycode;
    in = (in == KQ)?0:in;
    nwaiting++;
    }
}
 
pop_keycode()
/*************/
{
int i;
 
i = waiting_keycode[out++];
out = (out == KQ)?0:out;
nwaiting--;
return(i);
}






                                                                        3 - 51 

                                                                          kmsuor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kmsuor(ptr);                 set User Output Routine
int  (*ptr)();                    pointer to user output routine

Description:

The kmsuor function is used to register a User Output Routine (UOR).  Each
active registered UOR will be called every time a keycode is made available
to a calling application via kmgetch.
 
When your output function is called via ptr, it will be passed the current
keycode that was input:
 
           (*ptr)(keycode);
 
No return value is expected from your UOR.

Return Value:

The kmsuor function will return a positive integer unum which is used to
identify the newly registered UOR.  A negative return value indicates an error.

See Also:

kmguor, kmduor, kmsuspenduor, kmresumeuor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()

                                                                        3 - 52 

                                                                          kmsuor

kmsuspenduor(unum);                suspend output for awhile
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
    .
    .
    .
kmduor(-1);                        delete ALL output routines
















































                                                                        3 - 53 

                                                                    kmsuspendbgr

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  kmsuspendbgr();

Description:

The kmsuspendbgr function tells the Keyboard Manager to temporarily stop calling
the registered background routine.

Return Value:

This function has no return value and it will not cause problems by suspending
an already suspended background.

See Also:

kmresumebgr, kmsbgr, kmgbgr, kmdbgr

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
 
int  kbhit(), getch();             used in kminit() call
void showtime();                   for kmsbgr() function call
int  wnum;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wnum = wncreate(0,0,80,25,WNBLUE,
           WNCYAN,WNBLUE,WNCYAN);  open full screen window
kmsbgr(showtime);                  register background routine
    .
    .                              do other stuff
    .
kmsuspendbgr();                    stop displaying time for awhile
    .
    .
    .
kmresumebgr();                     resume showing time
}
 
showtime()                        show time while waiting for key input
{
static long lasttime;
long nowtime;
long time();

                                                                        3 - 54 

                                                                    kmsuspendbgr

struct tm *newtime;
 
if (time(&nowtime) != lasttime){   we'll display time if changed
    wnlocate(wnum,1,1);            position the cursor in main window
    newtime = localtime(&nowtime); get time in usable format
    wnprintf(wnum,"%s",
             asctime(newtime));    print time in upper left of window
    lasttime = nowtime;            update the status var
    }
}













































                                                                        3 - 55 

                                                                      kmsuspendi

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  kmsuspendi();                   suspend input

Description:

The kmsuspendi function will suspend input from an already opened input file.

Return Value:

This function has no return value.  It will not cause any problem to suspend
an already suspended file.

See Also:

kmsuspendo, kmopeni, kmopeno, kmresumei, kmresumeo

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
kmopeni("goodin.put");             read keycodes from an input file
while ((c = kmgetch()) != KESC)
    ...                            do something
kmsuspendi();                      suspend the input file
    ...                            now process the keyboard
kmresumei();                       resume input from file

















                                                                        3 - 56 

                                                                    kmsuspendir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int   kmsuspendir(keycode);             suspend an intercept routine
int   keycode;                          intercept routine to suspend/resume

Description:

The kmsuspend function will temporarily suspend interception of keycode.  A
value of -1 for keycode will suspend ALL interception routines.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid keycode.

See Also:

kmresumeir, kmsir, kmgir, kmdir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  myhelproutine();              called when F1 is pressed
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
kmsir(KF1,myhelproutine);          register F1 as help key
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
 
kmsuspenduor(unum);                suspend output for awhile
kmsuspendir(KF1);                  don't give help for password
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
kmresumeir(KF1);                   make help active again

                                                                        3 - 57 

                                                                    kmsuspendir

    .
    .
    .
kmduor(-1);                        delete ALL output routines
kmdir(-1);                         delete ALL intercept routines
    .
    .
    .
myhelproutine(code)                called when F1 is pressed
/*****************/
int code;                          current key being input
{
    .                              this would be a help routine
    .                              for your user.  Instead of writing
    .                              your own, use the Help Manager!
}







































                                                                        3 - 58 

                                                                      kmsuspendo

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
void  kmsuspendi();                   suspend input
void  kmsuspendo();                   suspend output

Description:

The kmsuspendo function will suspend output to an open output file.

Return Value:

These functions have no return value.  It will not cause any problem to suspend
an already suspended file.

See Also:

kmsuspendi, kmopeni, kmopeno, kmresumei, kmresumeo

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
kmopeno("goodout.put");            put keycodes to a journal file
while ((c = kmgetch()) != KESC)
    ...                            do something
kmsuspendo();                      suspend the output file
    ...                            now process the keyboard
kmresumeo();                       resume output to file
















                                                                        3 - 59 

                                                                    kmsuspenduir

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int   kmsuspenduir(unum);              suspend a user input routine
int   unum;                            uir number to suspend/resume

Description:

The kmsuspenduir function is used to temporarily suspend input from user input
routine unum.  A value of -1 supplied for unum will suspend ALL user input
routines.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid unum.

See Also:

kmresumeuir, kmsuir, kmguir, kmduir

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  goodroutine();                our user input routine
int  myuir;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
myuir = kmsuir(goodroutine);       register goodroutine as an input source
    .
    .
kmsuspenduir(myuir);               turn off goodroutine as an input source
    .
    .
    .
kmresumeuir(myuir);                resume input from goodroutine











                                                                        3 - 60 

                                                                    kmsuspenduor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int   kmsuspenduor(unum);              suspend a user output routine
int   unum;                            UOR to suspend/resume

Description:

The kmsuspenduor function will temporarily suspend output to User Output Routine
unum.  A value of -1 supplied for unum will cause all UOR's to be suspended.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid unum.

See Also:

kmresumeuor, kmsuor, kmduor, kmguor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
 
int  kbhit(), getch();             used in kminit() call
int  goodout();                    my output routine
int  outwin;                       where output will be echoed
int  unum, c;
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
wncreate(0,0,20,6,WNBLUE,WNCYAN,
         WNBLACK,WNRED);           create output window for goodout()
 
unum = kmsuor(goodout);            register the output routine
    .
    .
    .
while ((c = kmgetch()) != KESC)    just wait for esc.  Everything will be
    ;                              sent to goodout()
kmsuspenduor(unum);                suspend output for awhile
getpassword();                     call a useful routine
kmresumeuor(unum);                 resume output
    .
    .
    .
kmduor(-1);                        delete ALL output routines


                                                                        3 - 61 

                                                                                
























































                                                                        3 - 62 



4 Help Manager


4.1 Introduction

The Help Manager is a collection of library routines which allow your
applications to provide online, context sensitive help.  The text file used by
the Help Manager is created by a supplied utility program, HFBILDER.EXE.

4.2 Help File Builder

Before online help can be supplied to your users a normal ASCII text file which
contains the help text must be massaged into a format the Help Manager likes to
work with, this is done by the utility program HFBILDER.EXE.  The format your
help text file must follow is:
 
~label_1
          text
          text
          text
~label_2
          text
          text
          text
 
Where:
        ~       - is the ASCII tilde character
        label_x - a label of up to 32 characters
                  to identify the help text to
                  follow.
        text    - lines of text which make up the
                  help message (78 chars max).
 
All text lines following a label (blank lines included) up to the next label or
end of file comprises a help message.  When help is activated all lines
comprising a help message will be shown to the user.
 
To run the help file builder program from DOS just type:
 
        HFBILDER
 
You will be prompted for your input filename and an output filename.  The
program will not allow input and output to have the same name but if the output
file already exists it will be overwritten without warning.  The output filename
you specify is the same name that must be used in the hminit function call.
 
A sample help text file, HELPFILE.TXT, and demo program, HELPDEMO.EXE is
included in this package for your examination.







                                                                        4 - 1  

                                                                                


4.3 Symbolic Constants

The following symbolic constants can be found in the include file <hm.h>.

4.3.1 Error Constants

A successful Help Manager function call will return a value greater than or
equal to zero.  An error condition will cause one of the following negative
values to be returned:
 
    Constant   Value   Description
    ========   =====   ===========
    HMMAERROR  -1      memory allocation error
    HMFOERROR  -2      file open error
    HMFCERROR  -3      file close error
    HMFRERROR  -4      file read error
    HMFWERROR  -5      file write error

4.4 Module Initialization

Before the Help Manager can be used it must be initialized.  This is done by
calling the hminit function before all other help routines and AFTER
initializing the Help Manager via lminit, Keyboard Manager via kminit, and
Window Manager via wninit.  Since the Help Manager uses the List, Keyboard, and
Window Manager packages these must be initialized first.  Here is a startup
segment you might want to use:
 
 
main()
{
int  kbhit(),getch();            used in kminit call
 
lminit(malloc,free,0);           init the list manager
kminit(kbhit,getch);             init the keyboard manager
wninit(0,0,NULL,0,malloc,free);  init the window manager
hminit("C:\\GOODHLP.HLP",0,
       0,0,WNBLUE,WNCYAN);       init the help manager
 
kmsir(KF1,hmhelp);               help routine will be called when F1 pressed
hmscontext("main_help");         set help context
    .
    .                            body of code
    .
} end of main

4.5 Include Files

The C include file "hm.h" must be #includ'ed at the top of your application
source file in order to use the Help Manager package.  This gives you
access to symbolic constants used by the packages as well as letting the
compiler do parameter type checking.



                                                                        4 - 2  

                                                                                

4.6 Function Overview

All Help Manager functions return an error code value.  Zero or greater
indicates success.  The functions are:
 
code  = hminit(file,loadf,row,col,bc,fc);   init help manager
code  = hmterm()                            close help file
code  = hmscontext(str)                     set help context
        hmhelp()                            show, wait for key, then unshow
        hmpush(newcontext)                  push context
        hmpop()                             pop context

4.7 Function Definitions

These Help Manager function definitions are presented in alphabetical order,
each starting on a new page, to facilitate your search for information.
Function definitions are comprised of the following sections:
 
  - Summary       - function and parameter declarations
  - Description   - detailed description
  - Return Value  - explanation of return values
  - See Also      - related functions
  - Example       - programming example
 
A negative return value by any function indicates an error.






























                                                                        4 - 3  

                                                                      hmgcontext

Summary:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
char    *hmgcontext();

Description:

The hmgcontext function returns the currently active help label.

Return Value:

A character pointer pointing to the current help label will be returned.  The
string pointed to will have a length of zero (0) if there is no current help
context.

See Also:

hmscontext, hmpush, hmpop

Example:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
printf("\nThe current help context is %s",hmgcontext());
























                                                                        4 - 4  

                                                                          hmhelp

Summary:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
int  hmhelp();

Description:

The hmhelp function will display the current help text to the user, wait for ESC
to be pressed, and then remove the help window.  Here's what you will see when
hmhelp is called:
 
     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ[ help_label ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º                                           º
     º If there are more help lines than will    º
     º fit on the screen, the message "more"     º
     º will appear on the left window edge.      º
                                                 º
     M If the help file can't be found the user  º
     O will get the message:                     º
     R    "Sorry, could not open help file."     º
     E                                           º
       If help_label has not been defined in yourº
      file the message:                         º
        "Sorry, help context could not be found" º
     º                                           º
     º will be displayed.                        º
     º                                           º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍ**[ Press ESC ]**ÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
 
Note that your help labels will be used as titles in the help display window.

Return Value:

The hmhelp function is meant to be used as an intercept routine via the Keyboard
Manager kmsir function.  A value of -1 will be returned to the calling function.
Since a -1 causes the Keyboard Manager to throw away the intercepted key your
calling routine WILL NOT SEE the key which invoked hmhelp.

See Also:

hmscontext, hmpush, hmpop

Example:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
main()

                                                                        4 - 5  

                                                                          hmhelp

{
int  kbhit(),getch();            used in kminit call
int  c;
 
lminit(malloc,free,0);           init the list manager
kminit(kbhit,getch);             init the keyboard manager
wninit(0,0,NULL,0,malloc,free);  init the window manager
hminit("C:\\GOODHLP.HLP",0,
       0,0,WNBLUE,WNCYAN);       init the help manager
 
kmsir(KF1,hmhelp);               help routine will be called when F1 pressed
hmscontext("main_help");         set help context
    .
    .
c = kmgetch();                   get key from user
    .                            if F1 is pressed, hmhelp will be called
    .                            and the help text for "main_help" will be
    .                            displayed to the user.  After the user
    .                            ESCapes from hmhelp the keyboard manager
    .                            will still wait for a key.  The F1 key
    .                            WILL NOT be passed thru.


































                                                                        4 - 6  

                                                                          hminit

Summary:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
 
int  hminit(filepath,loadf,row,col,bc,fc);
 
char *filepath;                       help file to open and use
int  loadf;                           load flag (1=open now, 0=when help called)
int  row,col;                         center coords of help window
int  bc,fc;                           colors of help window

Description:

The hminit function is used to initialize the help manager package and must be
called prior to any other Help Manager routines and AFTER lminit, kminit, and
wninit.  The filename pointed to by filepath must have been created with
HFBILDER.EXE, loadf tells the package whether to load the help file immediately
(loadf == 1) or wait until the first time hmhelp is called (loadf == 0).  The
CENTER position of the help window is specified by row and col while the window
background and foreground (text) colors are given by bc and fc.
 
If the help file specified by filepath cannot be opened in the current
directory, all sub-directories in the environment PATH specification will be
searched in the order they appear.

Return Value:

A value of 0 will be returned if all went well.  A negative value indicates an
error such as out of memory or file open error.  Symbolic error codes can be
found in the include file <hm.h>.  Note that if loadf is set to 0 indicating
that you want the help file opened at the first call of hmhelp and filepath does
not exist, you will not get an error from this function, instead, hmhelp will
display an error message to the user when it is called.

See Also:

hmhelp, hmterm

Example:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
main()
{
int  kbhit(),getch();            used in kminit call
 
lminit(malloc,free,0);             init the list manager

                                                                        4 - 7  

                                                                          hminit

kminit(kbhit,getch);             init the keyboard manager
wninit(0,0,NULL,0,malloc,free);  init the window manager
hminit("C:\\GOODHLP.HLP",0,
       0,0,WNBLUE,WNCYAN);       init the help manager
 
kmsir(KF1,hmhelp);               help routine will be called when F1 pressed
hmscontext("main_help");         set help context
















































                                                                        4 - 8  

                                                                          hmpop

Summary:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
void  hmpop();

Description:

The hmpop function will restore the last help context saved by hmpush.

Return Value:

This function has no return value.  If there is no saved help context, your
request will be ignored.

See Also:

hmpush, hmscontext

Example:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
main()
{
int  kbhit(),getch();            used in kminit call
 
lminit(malloc,free,0);           init the list manager
kminit(kbhit,getch);             init the keyboard manager
wninit(0,0,NULL,0,malloc,free);  init the window manager
hminit("C:\\GOODHLP.HLP",0,
       0,0,WNBLUE,WNCYAN);       init the help manager
 
kmsir(KF1,hmhelp);               help routine will be called when F1 pressed
hmscontext("main_help");         set help context
goodsub();                       call a subroutine
    .
    .
}
goodsub()
{
hmpush("goodsub_help");          set new help context for F1 key
    .
    .                            do something
    .
hmpop();                         restore previous help context
}


                                                                        4 - 9  

                                                                          hmpush

Summary:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
int  hmpush(newcontext);
char *newcontext;                new help label

Description:

The hmpush function pushes the current help context onto an internal stack and
then sets it to newcontext.

Return Value:

A value of 0 will be returned if all went well.  A negative value indicates an
error, probably memory allocation.

See Also:

hmpop, hmscontext

Example:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
main()
{
int  kbhit(),getch();            used in kminit call
 
lminit(malloc,free,0);           init the list manager
kminit(kbhit,getch);             init the keyboard manager
wninit(0,0,NULL,0,malloc,free);  init the window manager
hminit("C:\\GOODHLP.HLP",0,
       0,0,WNBLUE,WNCYAN);       init the help manager
 
kmsir(KF1,hmhelp);               help routine will be called when F1 pressed
hmscontext("main_help");         set help context
goodsub();                       call a subroutine
    .
    .
}
goodsub()
{
hmpush("goodsub_help");          set new help context for F1 key
    .
    .                            do something
    .
hmpop();                         restore previous help context

                                                                        4 - 10 

                                                                          hmpush

}






















































                                                                        4 - 11 

                                                                      hmscontext

Summary:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
void  hmscontext(label);
char  *label;                     current help context label

Description:

The hmscontext function sets the current help context such that all text
following label in the current help file will be displayed to the user when
hmhelp is called.  The current context label (if any) will be lost.
 
Note that label must match a label you have entered in your help text file and
it must contain NO spaces.

Return Value:

This function has no return value.  If label does not exist in your help file,
hmhelp will notify the user.

See Also:

hmpush, hmpop

Example:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
main()
{
int  kbhit(),getch();            used in kminit call
 
lminit(malloc,free,0);           init the list manager
kminit(kbhit,getch);             init the keyboard manager
wninit(0,0,NULL,0,malloc,free);  init the window manager
hminit("C:\\GOODHLP.HLP",0,
       0,0,WNBLUE,WNCYAN);       init the help manager
 
kmsir(KF1,hmhelp);               help routine will be called when F1 pressed
hmscontext("main_help");         set help context








                                                                        4 - 12 

                                                                          hmterm

Summary:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
int  hmterm();

Description:

The hmterm function will close the file opened by hminit and free all memory
used by the Help Manager package.  It is NOT neccessary to call hmterm prior to
exiting your application since all open files will be closed by the C runtime
routines, however you must call hmterm if you want to open a different help file
via hminit.

Return Value:

A return value of 0 indicates all went well.  A negative value means an error
occured, probably a file close error.

See Also:

hminit

Example:

#include   "lm.h";
#include   "wn.h";
#include   "km.h";
#include   "hm.h";
 
main()
{
int  kbhit(),getch();            used in kminit call
 
lminit(malloc,free,0);           init the list manager
kminit(kbhit,getch);             init the keyboard manager
wninit(0,0,NULL,0,malloc,free);  init the window manager
hminit("C:\\GOODHLP.HLP",0,
       0,0,WNBLUE,WNCYAN);       init the help manager
 
kmsir(KF1,hmhelp);               help routine will be called when F1 pressed
hmscontext("main_help");         set help context
    .
    .
kmdir(KF1);                      disconnect the F1 key
hmterm();                        close help file
hminit("C"\\DIFFHELP.HLP",0,
       0,0,WNRED,WNYELLOW);      set up different help environment




                                                                        4 - 13 

                                                                                
























































                                                                        4 - 14 



5 Window Manager


5.1 Introduction

The Window Manager is a collection of library routines which allow you to
create, manipulate, and print in text screen windows.  Features of the Window
Manager include:
 
    - Screen area under window can be saved to memory or a file
    - Titles can be placed on all 4 window sides
    - Definable border drawing characters or none at all
    - Two styles of cursor -- different in each window
    - Completely definable colors
    - Extensive editing functions
    - Windows can be changed after creation
    - Wnprintf() with color
    - Wninput() to input all C data types
    - Wneditstring() mini editor
    - Object oriented functions
 
Object oriented means you will not have to maintain pointers to internal data
structures of the window package.  Once a window is created, you will receive an
integer window number.  All future references to the newly created window will
be thru this number.  This allows a separation between your application and the
data structures of the Window Manager which produces fewer bugs and allows us to
change our internal structure without affecting existing routines.

5.2 Components

The window manager routines can be broken down into 8 separate categories:
 
    - Initialization, creation, and deletion of windows
    - Window query routines
    - Window set routines
    - Size and movement routines
    - Titling routines
    - Printing routines
    - Editing routines
 
Since the Window Manager is a object oriented package, there are over 50
routines which allow your application to obtain or change a window's location,
appearance, or content.  Since your application doesn't have access to any data
structures all window manipulations are done thru a well behaved, debugged, set
of routines.

5.3 Symbolic Constants

All of the following constants are defined in the include file <wn.h>.

5.3.1 Colors

The following color constants or values can be used when specifying background
and/or foreground colors:

                                                                        5 - 1  

                                                                                

 
    Constant    Value      Description
    ==================================
    WNBLACK       0        Black
    WNBLUE        1        Blue
    WNGREEN       2        Green
    WNCYAN        3        Cyan
    WNRED         4        Red
    WNMAGENTA     5        Magenta
    WNBROWN       6        Brown
    WNGRAY        7        Gray
    WNDGRAY       8        Dark Gray
    WNLBLUE       9        Light Blue
    WNLGREEN      10       Light Green
    WNLCYAN       11       Light Cyan
    WNLRED        12       Light Red
    WNLMAGENTA    13       Light Magenta
    WNYELLOW      14       Yellow
    WNWHITE       15       White
 
All of the above values can be used to specify a background color, only 0-7 may
be used as a foreground color.
 
Blinking - To make your text blink, bitwise OR the constant WNBLINK with the
text foreground constant ( blinking cyan == WNCYAN | WNBLINK).
 
Mono Highlight - The following values can be used to specify the type of
highlighting to be used on mono displays:
 
    Constant      Value    Description
    ==================================
    WNNORMAL      0x07     White text on black
    WNREVERSE     0x70     Black text on white
    WNUNDERLINE   0x47     White text w/underline

5.3.2 Cursor Types

The wnswcmode function allows these window cursor styles:
 
    Constant      Value    Cursor Type
    ==================================
    WNNOCURSOR    0        No Cursor
    WNUNDCURSOR   1        Underline cursor
    WNSOLCURSOR   2        Solid cursor

5.3.3 Scroll Directions

The following values can be used in the wnscroll function for scrolling a
window:
 
    Constant      Value    Direction of Scroll
    ==========================================
    WUP           0        Up
    WDOWN         1        Down

                                                                        5 - 2  

                                                                                


5.3.4 Wninput Data Types

These data types are supported by the wninput function:
 
    Constant      Value
    ===================
    WNCHAR        0x0001
    WNCHARSTR     0x0002
    WNINT         0x0003
    WNUINT        0x0004
    WNLINT        0x0005
    WNULINT       0x0006
    WNFLOAT       0x0007
    WNDOUBLE      0x0008
 
Use this mask when testing a dtype:
 
    WNDTYPEMASK   0x000f

5.3.5 Error Codes

All error codes returned by the window routines are negative integers or a NULL
character pointer.  These are the possible error return codes:
 
    Error Code    Value    Description
    ==================================
    WNOK          0        no error
    WNMAERROR    -1        memory allocation error
    WNFWERROR    -2        file write error
    WNBADWIN     -3        bad window number
    WNFRERROR    -4        file read error
    WNWTBERROR   -5        window dimension(s) to big
    WNBVMERROR   -6        unsupported video mode
    WNPORERROR   -7        parameter out of range
    WNDTBERROR   -8        data to big for len in wninput

5.4 Module Initialization

Before any windows can be created and used the initialization routine wninit()
must be called.  This is a one time call and must be done AFTER the List Manager
is initialized via lminit.  The Window Manager makes extensive use of lists
therefore the List Manager must be initialized prior to calling wninit.  When
calling wninit you need to supply parameters which tell whether screen saves are
to be done to memory or a file, memory allocation/deallocation routines to use,
file transfer buffer and size, and an already opened file handle.  The state of
the memory/file save parameter determines which of the other parameters need to
be supplied.  A basic initialization synopsis is shown here:
 
 
int  wnum;
 
lminit(malloc,free,0);            init the list manager
wninit(0,0,NULL,0,malloc,free);   init window manager, screen saves to memory

                                                                        5 - 3  

                                                                                

    .
    .
wnum = wncreate(....);            create a window
    .
    .                             move, manipulate, and print in window
    .
wndestroy(wnum);                  remove the window when your done

5.5 Include Files

The C include file "wn.h" must be #includ'ed at the top of your application
source file in order to use the Window Manager package.  This gives you
access to symbolic constants used by the packages as well as letting the
compiler do parameter type checking.

5.6 Function Overview

All Window Manager functions return an error code value.  Zero or greater
indicates success.  The functions are:
 
** Create, destroy, misc
 
code    = wninit(mfflag, wh, wbuf,
                 wbsize, wmar, wmfr);   init window manager
wnum    = wncreate(row,col,width,height,
                   bc,fc,bbc,bfc);      create new window
code    = wndestroy(wnum);              remove a window
code    = wncls(wnum);                  clear a window
code    = wnfill(wnum,c);               fill a window with fill character
att     = wnghmatt();                   get highlight colors for mono
code    = wnshmatt(att);                set highlight colors for mono
code    = wngcparms(&wsave,&wscroll,
                    &wcmode,&ul,&ur,&ll,
                    &lr,&vti,&vbi,&hli,
                    &hri,&ic,&vc,&hc);  get parameters used for new windows
code    = wnscparms(wsave,wscroll,wcmode,
                    ul,ur,ll,lr,vti,vbi,
                    hli,hri,ic,vc,hc);  set parameters used for new windows
 
 
** Query Functions
 
wnum    = wngcwnum();                   get window with cursor active
row     = wngwrow(wnum)                 get row of upper left window corner
col     = wngwcol(wnum)                 get col of upper left window corner
width   = wngwwidth(wnum)               get width of window
height  = wngwheight(wnum)              get height of window
bc      = wngwbc(wnum)                  get background color
fc      = wngwfc(wnum)                  get foreground color
bbc     = wngwbbc(wnum)                 get border background color
bfc     = wngwbfc(wnum)                 get border foreground color
tbc     = wngwtbc(wnum)                 get titles background color
tfc     = wngwtfc(wnum)                 get titles foreground color
crow    = wngwcrow(wnum)                get cursor row in window

                                                                        5 - 4  

                                                                                

ccol    = wngwccol(wnum)                get cursor col in window
cmode   = wngwcmode(wnum)               get current cursor mode in window
wwrap   = wngwwwrap(wnum)               get word wrap status
scroll  = wngwscroll(wnum)              get scroll status
code    = wngwbchars(wnum,&ul,&ur,&ll,
                     &lr,&vc,&hc,&vti,
                     &vbi,&hli,&hri,&ic)get current window border characters
 
cols    = wngscols();                   get max columns in current video mode
rows    = wngsrows();                   get max rows in current video mode
 
** Modify Functions
 
code    = wnscwnum(wnum)                set window with cursor active
code    = wnswcolor(wnum,bc,fc)         set background,foreground color
code    = wnswbcolor(wnum,bbc,bfc)      set border background,foreground color
code    = wnswtcolor(wnum,tbc,tfc)      set titles background,foreground color
code    = wnswcmode(wnum,cmode)         set current cursor mode in window
code    = wnswscroll(wnum,scroll)       set window scroll flag
codd    = wnswbchars(wnum,ul,ur,ll,lr,
                     vc,hc,vti,vbi,hli,
                     hri,ic)            set border drawing chars
code    = wnsize(wnum,newwidth,
                 newheight)             resize existing window
code    = wnmove(wnum,newrow,newcol)    move existing window
 
** Character/Color Manipulation
 
code    = wnmovechar(wnum,torow,tocol)  move char at current cursor
code    = wngchar(wnum)                 get char from current cursor location
code    = wnmoves(wnum,torow,tocol,len) move string at current cursor
code    = wnscroll(wnum,srow,nrows,dir) scroll window contents up or down
code    = wndline(wnum)                 delete current row and bring up text
code    = wndeol(wnum)                  delete to end of line w/out bring up
code    = wndeow(wnum)                  delete to end of window
code    = wnbs(wnum)                    destructive backspace in window
code    = wninsline(wnum)               open up blank row
code    = wninschar(wnum)               open up blank character.
code    = wnputncolor(wnum,bc,fc,len);  change attribute of displayed text
code    = wnlputncolor(wnum,row,col,bc,
                       fc,len)          change attribute of text at row,col
code    = wnputhcolor(wnum,bc,fc,len);  change att of highlighted text
code    = wnlputhcolor(wnum,bc,fc,len); change att of text at row,col
 
** Titles
 
code    = wnttitle(wnum,str);           put title at top of window
code    = wnbtitle(wnum,str);           put title at bottom of window
code    = wnltitle(wnum,str);           put title at left edge of window
code    = wnrtitle(wnum,str);           put title at right edge of window
 
** Printing
 
code    = wnxlatwtos(wnum,&row,&col);   xlate window row,col to screen row,col

                                                                        5 - 5  

                                                                                

code    = wninwindow(wnum,row,col);     returns true if row,col INSIDE window
code    = wnlocate(wnum,row,col);       locate cursor in window
code    = wnputchar(wnum,c);            put char at current cursor location
code    = wnputs(wnum,str);             put string at current cursor location
code    = wnprintf(wnum,cstr,args...);  printf to current cursor location
count   = wnprintfcount(cstr,args...);  number chars that wnprintf will print
code    = wnlputchar(wnum,row,col,c);   put char at specified location
code    = wnlputs(wnum,row,col,str);    put string at specified location
 
** Editing
 
code    = wneditstring(wnum,buf,maxbufsize,    edit a buffer within a window
                       maxlinelen,maxlines,    with just this one call!
                       actionr);
 
** Data Input
 
code    = wninput(wnum,dtype,dptr,
                  len,precision,charset,
                  badinaction);         bullet proof data entry

5.7 Function Definitions

These Window Manager function definitions are presented in alphabetical order,
each starting on a new page, to facilitate your search for information.
Function definitions are comprised of the following sections:
 
  - Summary       - function and parameter declarations
  - Description   - detailed description
  - Return Value  - explanation of return values
  - See Also      - related functions
  - Example       - programming example
 
A negative return value by any function indicates an error.





















                                                                        5 - 6  

                                                                            wnbs

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnbs(wnum);
int   wnum;                        window number

Description:

The wnbs function is used to move all characters to the right of, and including,
the current cursor position 1 position to the left.  The current cursor position
will be updated after the characters have been moved.  If the current cursor
column is already column 1, the function will do nothing.  All color attributes
will be moved with the characters.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnins

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnlocate(wnum,2,1);                   position cursor
wnprintf(wnum,"Hello world");
wnlocate(wnum,"2,4);
wnbs(wnum);                           row 2 contains "Helo world"











                                                                        5 - 7  

                                                                        wnbtitle

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnbtitle(wnum,str);           bottom title routine
int  wnltitle(wnum,str);           left title routine
int  wnrtitle(wnum,str);           right title routine
int  wnttitle(wnum,str);           top title routine
 
int  wnum;                         window number
char *str;                         title string

Description:

The wnbtitle, wnltitle, wnrtitle, and wnttitle functions are used to place a
title string, str, in the border of window wnum.  The title string str will be
centered vertically if using wnltitle or wnrtitle, horizontally if using
wnbtitle or wnttitle.  Passing a null terminated string with length of 0 will
cause a displayed title to be removed.  If the title string is too long it will
be truncated to fit the window border.
 
The string str will be bordered on both ends by the current window border
characters so if you want something that looks clean you should probably
bracket your title strings with something like "[ good title ]" instead of
just "good title".
 
After creation, window title colors will be the same as the border characters.
Use the wnswtcolor function prior to calling a titling routine if you want
different title colors.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 

                                                                        5 - 8  

                                                                        wnbtitle

wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnttitle(wnum,"[ Main Menu ]");       top title same color as border
wnswtcolor(wnum,WNBLUE,WNCYAN);       color for new titles
wnbtitle(wnum,"[ ESC to Exit ]");     bottom title with new colors


















































                                                                        5 - 9  

                                                                          wncls

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wncls(wnum);
int  wnum;                        window to clear with spaces

Description:

The wncls function is used to fill the inside of window wnum with spaces and
locate the cursor at row,col 1,1. Note that it is not neccessary to use wncls
right after creating a window, it will be called for you.

Return Value:

A return value of 0 indicates all went well.  A negative value means an invalid
wnum was supplied.

See Also:

wnfill

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wncls(wnum);                                              clear window
















                                                                        5 - 10 

                                                                        wncreate

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wncreate(row,col,width,height,bc,fc,bbc,bfc);
 
int  row,col;           screen position of upper left window corner
int  width,height;      size of window
int  bc,fc;             window background, foreground color
int  bbc,bfc;           window border background, foreground color

Description:

The wncreate function is used to create and display an empty screen window.
Row, and col specify where the upper left window corner should appear on the
screen.  Width and height specify the window size including the border.  Bc and
fc specify the internal window colors, where bc is the background color and fc
is the text color.  Bbc and bfc specify the window border colors, both
background and foreground.
 
Unless the creation defaults are change via wnscparms, newly created windows
will have the following default properties:
 
    Screen save       - on
    Window scroll     - on
    Cursor type       - WNUNDCURSOR
    Title colors      - same as border colors
    Border characters - double line drawing set
    Cursor position   - 1,1 with window cleared

Return Value:

The wncreate function will return a positive integer window number which is to
be used with other Window Manager routines.  A negative return value indicates
an error.  Symbolic error and color constants can be found in the include file
<wn.h>.

See Also:

wndestroy, wnscparms

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing

                                                                        5 - 11 

                                                                        wncreate

wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window




















































                                                                        5 - 12 

                                                                          wndeol

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wndeol(wnum);
int   wnum;                       window number

Description:

The wndeol function will delete all characters from the current cursor position
to the right edge of window wnum.  All deleted characters including the current
cursor position will be set to blanks using the current background color.  If
the entire line is deleted due to the cursor being at column 1, the lines below
the current line will not be scrolled up.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wndline

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnprintf(wnum,"This is line 1\n");
wnprintf(wnum,"This is line 2\n");
wnprintf(wnum,"This is line 3\n");
wnprintf(wnum,"This is line 4\n");
wnprintf(wnum,"This is line 5\n");
wnprintf(wnum,"This is line 6\n");
    .
    .
    .
wnlocate(wnum,3,7);                    position cursor at row 3, col 7
wndeol(wnum);                          line 3 now "This i"




                                                                        5 - 13 

                                                                          wndeow

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wndeow(wnum);
int   wnum;                         window number

Description:

The wndeow function will delete all characters from the current cursor position
to the last row and column in window wnum.  All deleted characters will be set
to blanks using the current window background color.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wndeol, wndline

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnprintf(wnum,"This is line 1\n");
wnprintf(wnum,"This is line 2\n");
wnprintf(wnum,"This is line 3\n");
wnprintf(wnum,"This is line 4\n");
wnprintf(wnum,"This is line 5\n");
wnprintf(wnum,"This is line 6\n");
    .
    .
    .
wnlocate(wnum,1,7);                    position cursor at row 1, col 7
wndeow(wnum);                          only "This i" of line 1 remains






                                                                        5 - 14 

                                                                      wndestroy

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wndestroy(wnum);
int  wnum;                           window to take down

Description:

The wndestroy function is used to remove a window from the screen, restore the
screen under the window if it was saved, and finally, free any memory that was
used by the window.  Wnum is the window number to be removed, -1 supplied for
wnum will remove all existing windows in the reverse order of creation.  Note
that if you choose to destroy windows individually you must pay attention to the
order so that screen area under the windows are restored properly.
 
If the file screen save mode was specified in wninit, it is the applications
responsibility to close this file.

Return Value:

The wndestroy function returns 0 if all went well.  A negative value indicates
an error.  Symbolic error codes can be found in the include file <wn.h>.

See Also:

wncreate, wninit

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
wndestroy(wnum);                      take window down










                                                                        5 - 15 

                                                                        wndline

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wndline(wnum);
int   wnum;                       window number

Description:

The wndline function is used to delete the current cursor line in window wnum.
All lines below the current line will be scrolled up.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wndeol

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnprintf(wnum,"This is line 1\n");
wnprintf(wnum,"This is line 2\n");
wnprintf(wnum,"This is line 3\n");
wnprintf(wnum,"This is line 4\n");
wnprintf(wnum,"This is line 5\n");
wnprintf(wnum,"This is line 6\n");
    .
    .
    .
wnlocate(wnum,3,1);                    position cursor at row 3, col 1
wndline(wnum);                         line 3 now missing







                                                                        5 - 16 

                                                                    wneditstring

Summary:

#include   "wn.h";
 
int     wneditstring(wnum,buf,maxbufsize,maxlinelen,maxlines,actionr);
 
int     wnum;               window to edit string in
char    *buf;               string buffer to edit
int     maxbufsize;         how big buf is
int     maxlinelen;         max length a line can be
int     maxlines;           maximum number of lines
int     (*actionr)();       function to call when user wants to exit or quit

Description:

The wneditstring function is basically a text editor which operates inside
an existing window wnum.  If wnum is at least 60 characters wide, a status
line telling the current row, column, lines, and characters will be displayed
while the user is in the edit function.
 
The buffer to hold the edited string is pointed to by buf with the maximum
number of characters it can hold being maxbufsize.  The contents of buf on
entry to this function will be copied to a local buffer which will be allocated
using the allocation routine specified in the wninit() function.  If the user
aborts the editing, the contents of buf will be unchanged.
 
Maxlinelen and maxlines specify the "world" size the user will be allowed to
scroll around in while editing.  The size of the local editing buffer is the
product ( (maxlinelen + 12) * maxlines ).  The values to pick for maxlinelen
and maxlines depend on the kind of text you're editing.  The value of
maxbufsize does NOT have to be as big as the "world" you pick.  Under normal
editing, the user does not fill the entire length of every line with text.
 
When the editor starts up and allocates its local buffer, it breaks buf up
by lines where the end of a line is signified by a '\n' character.  When the
user exits and the local buffer is passed back in buf, it will be in line
format.  Buf must be passed with a terminating '\0' character and will be
passed back with one.  Make sure that the longest line in buf does not exceed
maxlinelen or it will be truncated.  A truncated line will set the dirty flag
which gets passed to the action routine.
 
Actionr must point to one of your functions which will get called when the
editor has been readied for user input, and when the user wants to quit or
exit.  The synopsis for actionr is:
 
    int (*actionr)(code,dirty,nlines,nchars);
 
    int code;     -1 == initial setup done.  Ok to set intercept routines.
                   0 == user wants to quit.
                   1 == user wants to exit w/changes.
    int dirty;    0 == no edits have be made, 1 == edits have been made
    int nlines;   total number lines with text, spaces, or '\n' on them
    int nchars;   total number of characters to pass back in buf (wo/'\n')
 

                                                                        5 - 17 

                                                                    wneditstring

Actionr can return 1 of 3 values:
 
    -1  == will cause editing to resume.
     0  == will quit editor without passing changes back in buf.
    >0  == will exit editor with changes passed back in buf.
 
A default action routine will be used if you supply the constant WNACTIONNULL
for actionr.  This default routine will return 0 when the ESCAPE key is pressed
and 1 when F10 is pressed.  The user will not be asked if he/she is sure they
want to quit/exit.
 
When the editor starts, it will do a Keyboard Manager context push via
kmpush() and set intercept routines for its use.  On exit, the keyboard context
will be restored.  You can redefine the keyboard context however you like when
your action routine is called initially with a code == -1.  The keys that are
used by default in the editor are:
 
  WNEESC      KESC    aborts editing ( 0 passed to actionr)
  WNEHELP     KF1     displays window with key assignments
  WNEDEOL     KF2     delete to end of line
  WNEEXIT     KF10    exits editing ( 1 passed to actionr)
  WNEHOME     KHOME   moves to beginning of line
  WNEEND      KEND    moves to end of text on line
  WNEINS      KINS    toggles insert/overstrike mode
  WNEDEL      KDEL    deletes one character to right
  WNEBS       KBS     destructive backspace
  WNECR       KCR     newline
  WNEUP       KUP     move cursor up one line
  WNEDOWN     KDOWN   move cursor down one line
  WNERIGHT    KRIGHT  move cursor right one column
  WNELEFT     KLEFT   move cursor left one column
  WNETAB      KTAB    insert 4 spaces
  WNEPGUP     KPGUP   move window towards begin of buffer 1 row
  WNEPGDN     KPGDN   move window towards end of buffer 1 line

Return Value:

A negative return indicates an error.  If there are no errors then the value
returned from wneditstring is whatever is passed back from the actionr
function.  Zero means the editing was aborted and buf is unchanged.

See Also:

wninit, wncreate

Example:

#include   "wn.h";
 
{
int  wnum;
char buf[7981];       /* 132 by 60 with '\n' for each line and '\0' at end. */
int  kbhit(), getch();
int  editaction();    /* our action routine */

                                                                        5 - 18 

                                                                    wneditstring

 
lminit(malloc,free,0);                init list manager first thing
kminit(kbhit,getch);                  init keyboard manager next
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(0,0,70,20,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnttitle(wnum,"[ Edit Test Window ]");
strcpy(buf,"now is\nthe time\nfor all\ngood men\nto come"); something to edit
wneditstring(wnum,buf,7980,132,60,editaction);
wndestroy(wnum);
}
 
 
editaction(code,dirty,nlines,nchars)
/*********************************/
int code;   /* 0 == user wants to quit, 1 == user wants to exit */
int dirty;  /* 0 == edits not done, 1 == edits done */
int nlines; /* number lines with something on them */
int nchars; /* total characters that will be passed back in buf (wo/'\0') */
{
int awnum;
int key;
int myhelp();
 
if (code == -1){            /* initial setup */
   kmsir(KF1,myhelp);       /* redefine the help routine to mine */
   return(-1);
   }                        /* keep on editing */
if (code == 0){             /* ask user if sure to abort */
    awnum = wncreate(0,0,20,3,WNBLACK,WNWHITE,WNBLACK,WNWHITE);
    wnprintf(awnum,"Ok to abort? (Y/<N>) ");
    key = kmgetch();
    wndestroy(awnum);
    if (tolower(key) == 'y')
        return(0);          /* tell wneditstring to abort */
    else
        return(-1);         /* tell it to keep editing */
    }
else
    return(1);              /* don't even ask permission to exit. ha ha */
};














                                                                        5 - 19 

                                                                          wnfill

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnfill(wnum,c);
int  wnum;                         window number to fill
int  c;                            fill character

Description:

The wnfill function is used to paint the inside of a window with a specified
fill character c.  The current background/foreground in effect for the
window wnum will be used for the fill.

Return Value:

The wnfill returns 0 if all went well.  A negative return value indicates an
invalid wnum.

See Also:

wncls.

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnfill(wnum,176);                     fill window with  character















                                                                        5 - 20 

                                                                        wngchar

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int     wngchar(wnum)
int     wnum;           window to get character from

Description:

The wngchar function is used to obtain the character at the current cursor
location in window wnum.

Return Value:

The ASCII character value at the current window cursor location will be
returned.  If wnum is illegal, 0 will be returned.  If there is another window
overlapping the current cursor position of wnum the returned value will be
undefined.

See Also:

wnputchar

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlocate(wnum,2,3);                   position cursor
wnputchar(wnum,'V');                  put a character at 2,3
wnlocate(wnum,2,3);
c = wngchar(wnum);                    c == 'V'











                                                                        5 - 21 

                                                                      wngcparms

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void wngcparms(wsave,wscroll,wcmode,ul,ur,ll,lr,f1,f2,f3,f4,f5,vc,hc);
 
int  *wsave;               screen save flag
int  *wscroll;             window scroll flag
int  *wcmode;              cursor style
int  *ul,*ur,*ll,*lr;      border corner characters
int  *f1,*f2,*f3,*f4,*f5;  dummy fill characters
int  *vc,*hc;              vertical and horizontal drawing characters

Description:

The wngcparms function is used to obtain the default window creation parameters
that are not specified in the wncreate call.  The state or value of these
parameters are used when creating windows via wncreate.  Wsave is false if
screen saves under new windows are NOT to be done, wscroll and wcmode are the
default scroll flag and cursor style to be used, ul, ur, ll, lr, vc, and hc are
the characters used when drawing the window border.  F1, f2, f3, f4, and f5 are
dummy variables, in later versions they will represent characters used for
drawing crossbars and intersecting lines inside of windows.

Return Value:

This function has no return value.

See Also:

wnscparms, wncreate, wninit, wngwbchars

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
int  save,scroll,cmode;
int  ul,ur,ll,lr;
int  f1,vc,hc;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wngcparms(&save,&scroll,&cmode,&ul,&ur,&ll,&lr,&f1,&f1,&f1,&f1,&f1,&vc,&hc);



                                                                        5 - 22 

                                                                        wngcwnum

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int wngcwnum();         get window with cursor active
int wnscwnum(wnum);     set window with cursor
int wnum;               window number

Description:

The wngcwnum function is used to obtain the window number which contains
the active cursor.  The wnscwnum function will set the active cursor window
to the window specified by wnum.  The cursor will remain active in this
window until a different window other than wnum is accessed in some way via
a window manager routine.
 
The purpose of these routines is to allow an interrupt routine, such as a
keycode intercept, to save the active window, write to a different one, and
restore the cursor to its original state.

Return Value:

The wngcwnum function will return a negative number if a window is not active.
A positive value indicates a valid window number.  The wnscwnum function
returns 0 if all went well and a negative value if wnum is invalid.

See Also:

wngwcmode, wnswcmode

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
 
int  kbhit(), getch();             used in kminit() call
void showtime();                   for kmsbgr() function call
void (*ptr)();                     for kmgbgr() function call
int  mwnum,cwnum;                  main window, clock window
 
main(){
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
mwnum = wncreate(0,0,80,22,WNBLUE,
           WNCYAN,WNBLUE,WNCYAN);  open working window
cwnum = wncreate(22,0,80,3,WNBLUE,

                                                                        5 - 23 

                                                                        wngcwnum

           WNCYAN,WNBLUE,WNCYAN);  open clock window
kmsbgr(showtime);                  register background routine
    .
    .                              do other stuff in working window
    .
 
}
 
showtime()                         show time while waiting for key input
{
static long lasttime;
long nowtime;
long time();
struct tm *newtime;
int tempwnum;
char buf[30];
 
tempwnum = wngcwnum();
if (time(&nowtime) != lasttime){   we'll display time if changed
    newtime = localtime(&nowtime); get time in usable format
    strcpy(buf,asctime(newtime));
    buf[strlen(buf) - 1] = '\0';   get rid of newline in time buf
    wnlocate(cwnum,1,1);           position the cursor in main window
    wnprintf(cwnum,"%s",buf);      print time in clock window
    lasttime = nowtime;            update the status var
    wnscwnum(tempwnum);            put cursor back to window that was active
    }
}



























                                                                        5 - 24 

                                                                        wnghmatt

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wnghmatt();

Description:

The wnghmatt function retrieves the attribute currently being used by newly
created windows for displaying highlighted text on a mono display.  This value
is used by the wnputhcolor function which in turn is used by the menu and field
processing routines.  By setting this value you can affect how highlight items
look when run on a mono display.

Return Value:

Currently there are 3 possible return values:
 
  WNNORMAL      -- Normal white on black background
  WNREVERSE     -- Reverse video black text on white
  WNUNDERLINE   -- Normal white on black with underline

See Also:

wnshmatt, wnputhcolor, wnlputhcolor, wnputncolor, wnlputncolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
int  att;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
att = wnghmatt();










                                                                        5 - 25 

                                                                        wngnmatt

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wngnmatt();

Description:

The wngnmatt function retrieves the attribute currently being used by newly
created windows for displaying normal text on a mono display.  This value is
used by the wnputhcolor function which in turn is used by the menu and field
processing routines.  By setting this value you can affect how normal items look
when run on a mono display.

Return Value:

Currently there are 3 possible return values:
 
    WNNORMAL      -- Normal white on black background
    WNREVERSE     -- Reverse video black text on white
    WNUNDERLINE   -- Normal white on black with underline

See Also:

wnshmatt, wngnmatt, wnputhcolor, wnlputhcolor, wnputncolor, wnlputncolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
int  att;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
att  = wngnmatt();











                                                                        5 - 26 

                                                                        wngscols

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int wngscols();         get max columns for current video mode
int wngsrows();         get max rows for current video mode

Description:

The wngscols and wngsrows functions can tell you the maximum screen size for
the video mode that was current when wninit() was called.
 
When calling wncreate with window size and location parameters, you will get
an error if an attempt is made to go outside of the boundries returned by
wngscols and wngsrows.

Return Value:

The maximum number of screen columns will be returned by wngscols.  The maximum
screen rows will be returned by wngsrows.  A zero value indicates that whatever
video mode was current when wninit was called is not supported by the window
manager.

See Also:

wninit, wncreate

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
int  row,col;
int  w,h;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
w    = 20;
h    = 10;
row  = (wngsrows() - w) / 2;          center window no matter screen size
col  = (wngscols() - h) / 2;
wnum = wncreate(r,c,w,h,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window







                                                                        5 - 27 

                                                                        wngsrows

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int wngscols();         get max columns for current video mode
int wngsrows();         get max rows for current video mode

Description:

The wngscols and wngsrows functions can tell you the maximum screen size for
the video mode that was current when wninit() was called.
 
When calling wncreate with window size and location parameters, you will get
an error if an attempt is made to go outside of the boundries returned by
wngscols and wngsrows.

Return Value:

The maximum number of screen columns will be returned by wngscols.  The maximum
screen rows will be returned by wngsrows.  A zero value indicates that whatever
video mode was current when wninit was called is not supported by the window
manager.

See Also:

wninit, wncreate

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
int  row,col;
int  w,h;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
w    = 20;
h    = 10;
row  = (wngsrows() - w) / 2;          center window no matter screen size
col  = (wngscols() - h) / 2;
wnum = wncreate(r,c,w,h,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window







                                                                        5 - 28 

                                                                        wngwbbc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wngwbc(wnum);             return current background color
int   wngwfc(wnum);             return current foreground color
int   wngwbbc(wnum);            return current border background color
int   wngwbfc(wnum);            return current border foreground color
int   wngwtbc(wnum);            return current titles background color
int   wngwtfc(wnum);            return current titles foreground color
int   wnum;                     window number

Description:

The wngwbc, wngwfc, wngwbbc, wngwbfc, wngwtbc, and wngwtfc return the current
color settings for window wnum.

Return Value:

A positive return value from any of the functions indicates the color for which
you were interested in.  Any foreground color > 128 indicates blinking is
active.  A negative return value means wnum is invalid.

See Also:

wnswcolor, wnswbcolor, wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
color = wngwtbc(wnum);  WNBLUE will return since titles default at creation time
                        to the border colors unless changed.










                                                                        5 - 29 

                                                                          wngwbc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wngwbc(wnum);             return current background color
int   wngwfc(wnum);             return current foreground color
int   wngwbbc(wnum);            return current border background color
int   wngwbfc(wnum);            return current border foreground color
int   wngwtbc(wnum);            return current titles background color
int   wngwtfc(wnum);            return current titles foreground color
int   wnum;                     window number

Description:

The wngwbc, wngwfc, wngwbbc, wngwbfc, wngwtbc, and wngwtfc return the current
color settings for window wnum.

Return Value:

A positive return value from any of the functions indicates the color for which
you were interested in.  Any foreground color > 128 indicates blinking is
active.  A negative return value means wnum is invalid.

See Also:

wnswcolor, wnswbcolor, wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
color = wngwtbc(wnum);  WNBLUE will return since titles default at creation time
                        to the border colors unless changed.










                                                                        5 - 30 

                                                                      wngwbchars

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwbchars(wnum,ul,ur,ll,lr,vc,hc);
int  wnum;                                 window number
int  *ul,*ur;                              upper left/right corner characters
int  *ll,*lr;                              lower left/right corner characters
int  *vc,*hc;                              vertical/horizontal drawing character

Description:

The wngwbchars function is used to obtain the current border box drawing
characters for window wnum.  Ul, ur, ll, lr are the 4 corner characters while vc
and hc are the vertical and horizontal drawing characters.

Return Value:

A value of 0 will be returned if all went well.  A negative value indicates an
invalid wnum.

See Also:

wncreate, wngcparms, wnscparms, wnswbchars

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
int  ul,ur,ll,lr,vc,hc;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wngwbchars(&ul,&ur,&ll,&lr,&vc,&hc);












                                                                        5 - 31 

                                                                        wngwbfc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wngwbc(wnum);             return current background color
int   wngwfc(wnum);             return current foreground color
int   wngwbbc(wnum);            return current border background color
int   wngwbfc(wnum);            return current border foreground color
int   wngwtbc(wnum);            return current titles background color
int   wngwtfc(wnum);            return current titles foreground color
int   wnum;                     window number

Description:

The wngwbc, wngwfc, wngwbbc, wngwbfc, wngwtbc, and wngwtfc return the current
color settings for window wnum.

Return Value:

A positive return value from any of the functions indicates the color for which
you were interested in.  Any foreground color > 128 indicates blinking is
active.  A negative return value means wnum is invalid.

See Also:

wnswcolor, wnswbcolor, wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
color = wngwtbc(wnum);  WNBLUE will return since titles default at creation time
                        to the border colors unless changed.










                                                                        5 - 32 

                                                                        wngwccol

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwccol(wnum);               get current cursor column
int  wngwcrow(wnum);               get current cursor row
int  wnum;                         window number

Description:

The wngwccol and wngwcrow functions are used to obtain the current cursor
position for a given window wnum.

Return Value:

The cursor column number is returned by wngwccol while the current cursor row is
returned by wngwcrow.  Both values are referenced from the window origin and are
zero based.  If the cursor for window wnum were at the upper left corner, just
inside the window border, values returned would be row 1, column 1.

See Also:

wngwcmode, wnswcmode

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
wnlocate(wnum,2,5);                   position cursor
wnprintf(wnum,"Hello");               this will move cursor
row = wngwcrow(wnum);                 row will == 2
col = wngwccol(wnum);                 col will == 10 (5 + "Hello" == 10)










                                                                        5 - 33 

                                                                      wngwcmode

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwcmode(wnum);
int  wnum;                         window number

Description:

The wngwcmode function returns the current cursor mode for window wnum.

Return Value:

The following possible return values indicate the current cursor type for window
wnum:
 
    Return Value             Cursor Type
    =============================================
    WNNOCURSOR               None
    WNUNDCURSOR              Underline Blinking
    WNSOLCURSOR              Solid Blinking

See Also:

wnswcmode

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnswcmode(wnum,WNSOLCURSOR);          set the cursor type
ctype = wngwcmode(wnum);              return value will be WNSOLCURSOR











                                                                        5 - 34 

                                                                        wngwcol

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwcol(wnum);                return column of upper left corner
int  wngwrow(wnum);                return row of upper left corner
int  wnum;                         window number

Description:

The wngwcol and wngwrow functions are used to obtain the current position of
window wnum.  The values returned are those for the upper left corner of the
indicated window.

Return Value:

Wngwcol returns the column (0-79) that contains the upper left window corner.
Wngrow returns the row (0-24) that contains the upper left window corner.  A
negative return value from either functions indicates an invalid wnum.

See Also:

wnmove, wnsize, wngwwidth, wngwheight

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
row  = wngwrow(wnum);                 5 will be returned
col  = wngwcol(wnum);                 10 will be returned












                                                                        5 - 35 

                                                                        wngwcrow

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwccol(wnum);               get current cursor column
int  wngwcrow(wnum);               get current cursor row
int  wnum;                         window number

Description:

The wngwccol and wngwcrow functions are used to obtain the current cursor
position for a given window wnum.

Return Value:

The cursor column number is returned by wngwccol while the current cursor row is
returned by wngwcrow.  Both values are referenced from the window origin and are
zero based.  If the cursor for window wnum were at the upper left corner, just
inside the window border, values returned would be row 1, column 1.

See Also:

wngwcmode, wnswcmode

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
wnlocate(wnum,2,5);                   position cursor
wnprintf(wnum,"Hello");               this will move cursor
row = wngwcrow(wnum);                 row will == 2
col = wngwccol(wnum);                 col will == 10 (5 + "Hello" == 10)










                                                                        5 - 36 

                                                                          wngwfc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wngwbc(wnum);             return current background color
int   wngwfc(wnum);             return current foreground color
int   wngwbbc(wnum);            return current border background color
int   wngwbfc(wnum);            return current border foreground color
int   wngwtbc(wnum);            return current titles background color
int   wngwtfc(wnum);            return current titles foreground color
int   wnum;                     window number

Description:

The wngwbc, wngwfc, wngwbbc, wngwbfc, wngwtbc, and wngwtfc return the current
color settings for window wnum.

Return Value:

A positive return value from any of the functions indicates the color for which
you were interested in.  Any foreground color > 128 indicates blinking is
active.  A negative return value means wnum is invalid.

See Also:

wnswcolor, wnswbcolor, wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
color = wngwtbc(wnum);  WNBLUE will return since titles default at creation time
                        to the border colors unless changed.










                                                                        5 - 37 

                                                                      wngwheight

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwheight(wnum);              return window height
int  wngwwidth(wnum);               return window width
int  wnum;                          wnum

Description:

The wngwheight and wngwwidth functions are used to obtain the current size of
window wnum.

Return Value:

Wngwheight returns the height of wnum and wngwwidth returns the width.  Both
values include the window border.  A negative return value indicates an invalid
wnum.

See Also:

wnsize

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
width = wngwwidth(wnum);              70 will be returned
height = wngwheight(wnum);            10 will be returned














                                                                        5 - 38 

                                                                        wngwrow

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwcol(wnum);                return column of upper left corner
int  wngwrow(wnum);                return row of upper left corner
int  wnum;                         window number

Description:

The wngwcol and wngwrow functions are used to obtain the current position of
window wnum.  The values returned are those for the upper left corner of the
indicated window.

Return Value:

Wngwcol returns the column (0-79) that contains the upper left window corner.
Wngrow returns the row (0-24) that contains the upper left window corner.  A
negative return value from either function indicates an invalid wnum.

See Also:

wnmove, wnsize, wngwwidth, wngwheight

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
row  = wngwrow(wnum);                 5 will be returned
col  = wngwcol(wnum);                 10 will be returned












                                                                        5 - 39 

                                                                      wngwscroll

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwscroll(wnum);
int  wnum;                          window number

Description:

The wngwscroll function returns the scroll status for window wnum.  The ability
to turn scroll on or off is needed if you want to place a character at the lower
right window corner.  If scroll is on, all text lines will scroll up in the
window.  If scroll is off, the cursor will wrap to location 1,1.

Return Value:

A return value of 0 indicates window scrolling is off, 1 is on, and a negative
value means an invalid wnum.

See Also:

wnswscroll

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
sstat = wngwscroll(wnum);















                                                                        5 - 40 

                                                                        wngwtbc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wngwbc(wnum);             return current background color
int   wngwfc(wnum);             return current foreground color
int   wngwbbc(wnum);            return current border background color
int   wngwbfc(wnum);            return current border foreground color
int   wngwtbc(wnum);            return current titles background color
int   wngwtfc(wnum);            return current titles foreground color
int   wnum;                     window number

Description:

The wngwbc, wngwfc, wngwbbc, wngwbfc, wngwtbc, and wngwtfc return the current
color settings for window wnum.

Return Value:

A positive return value from any of the functions indicates the color for which
you were interested in.  Any foreground color > 128 indicates blinking is
active.  A negative return value means wnum is invalid.

See Also:

wnswcolor, wnswbcolor, wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
color = wngwtbc(wnum);  WNBLUE will return since titles default at creation time
                        to the border colors unless changed.










                                                                        5 - 41 

                                                                        wngwtfc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int   wngwbc(wnum);             return current background color
int   wngwfc(wnum);             return current foreground color
int   wngwbbc(wnum);            return current border background color
int   wngwbfc(wnum);            return current border foreground color
int   wngwtbc(wnum);            return current titles background color
int   wngwtfc(wnum);            return current titles foreground color
int   wnum;                     window number

Description:

The wngwbc, wngwfc, wngwbbc, wngwbfc, wngwtbc, and wngwtfc return the current
color settings for window wnum.

Return Value:

A positive return value from any of the functions indicates the color for which
you were interested in.  Any foreground color > 128 indicates blinking is
active.  A negative return value means wnum is invalid.

See Also:

wnswcolor, wnswbcolor, wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
color = wngwtbc(wnum);  WNBLUE will return since titles default at creation time
                        to the border colors unless changed.










                                                                        5 - 42 

                                                                      wngwwidth

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wngwheight(wnum);              return window height
int  wngwwidth(wnum);               return window width
int  wnum;                          wnum

Description:

The wngwheight and wngwwidth functions are used to obtain the current size of
window wnum.

Return Value:

Wngwheight returns the height of wnum and wngwwidth returns the width.  Both
values include the window border.  A negative return value indicates an invalid
wnum.

See Also:

wnsize

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
width = wngwwidth(wnum);              70 will be returned
height = wngwheight(wnum);            10 will be returned














                                                                        5 - 43 

                                                                          wninit

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wninit(mfflag, wh, wbuf, wbsize, wmar, wmfr);
 
int  mfflag;        memory/file screen save flag
int  wh;            file handle
int  wbuf;          file transfer buffer
int  wbsize;        file transfer buffer size
char *(*wmar)();    memory allocation routine
void (*wmfr)();     memory free routine

Description:

The wninit function is used to initialize the Window Manager package and must be
called BEFORE any other window routines and AFTER calling the List Manager
initializer, lminit.  Mfflag determines where screen saves under a window will
be put, 0 for memory, or 1 for saving to a file.  If screen saves are to be put
in a file (mfflag), wh, wbuf, and wbsize must be supplied.  Wh is the file
handle of an already opened file, wbuf is a pointer to a transfer buffer, and
wbsize is the size of the buffer.  The buffer size must be at least  char
buf[2].  Wmar and wfr point to routines for allocating/deallocating memory
that the Window Manager will use for creating internal data structures.  The
synopsis for these 2 routines are:
 
char *(*wmar)(lsize);
void  (*mfr)(cptr);
 
unsigned int  lsize;     size of memory to allocate of size char
char  *cptr;             pointer to allocated memory block

Return Value:

The wninit function returns 0 if all went well.  A negative number indicates
an error such as lack of memory or the current video mode is not supported.
Even if you specify mfflag = 1 there can be a memory allocation error when
this module calls the List Manager package to create various internal data
lists.

See Also:

wncreate

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 

                                                                        5 - 44 

                                                                          wninit

int           wnum, fileh;
static char   wbuf[4096];              file transfer buffer
 
fileh = open("wjunk.dat", O_RDWR | O_CREAT); screen save file
 
lminit(malloc,free,0);                 init list manager first thing
wninit(1,fileh,wbuf,4096,malloc,free); init window manager, save to a file
    .
    .
    .
close(fileh);
remove("wjunk.dat");











































                                                                        5 - 45 

                                                                        wninput

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int     wninput(wnum,dtype,dptr,len,precision,charset,badinaction);
 
int     wnum;               window number to input from
int     dtype;              data type to input
char    *dptr;              pointer to data
int     len;                size of data if char, else input buffer size
int     precision;          decimal precision if float or double
char    *charset;           allowable characters, NULL for default
int     (*badinaction)();   routine to call if bad input attempted

Description:

The wninput function is used to obtain data from an interactive user via
window wnum.  It is assumed that the cursor is already positioned where you
would like the data to be input from.
 
The type of data you want obtained is specified by dtype.  These are the current
possible input types:
 
    dtype       Data Type               Default Len Used
    =====       =========               ================
    WNCHAR      Single Unsigned char        1
    WNCHARSTR   Unsigned char string    to edge of window
    WNINT       Integer                     6
    WNUINT      Unsigned Integer            5
    WNLINT      Long Integer                11
    WNULINT     Unsigned Long Integer       10
    WNFLOAT     Float                       13
    WNDOUBLE    Double                      13
 
The pointer to where the data gets put is specified by dptr.  You must assure
that the size of buffer pointed to by dptr is big enough to hold the data
specified by dtype.  If inputting type WNCHARSTR, your buffer must be len + 1
bytes deep in order for the '\0' to fit.
 
The amount of room that the user will be allowed to navigate in is set by len.
This will be the total number of characters the user will be allowed to input.
After he/she hits the ENTER key, this string will be converted to the data type
specified by dtype.  Supplying a value of 0 for len will give the defaults
listed above.  The signed inputs are 1 longer than unsigned to allow for "+/-"
input.
 
If the dtype is WNFLOAT or WNDOUBLE, precision will be used when a sscanf is
done to your data area.
 
Charset is a string of characters that you only want allowed for input.  If
a value of NULL or a zero length charset is supplied these are the characters

                                                                        5 - 46 

                                                                        wninput

that will be legal:
 
    dtype       Default Legal Characters
    =====       ========================
    WNCHAR      1 - 256
    WNCHARSTR   1 - 256
    WNINT       "1234567890-+ "
    WNUINT      "1234567890 "
    WNLINT      "1234567890-+ "
    WNULINT     "1234567890 "
    WNFLOAT     "1234567890-+eE. "
    WNDOUBLE    "1234567890-+eE. "
 
Unless specified otherwise, the data input area will be blanked, default data
displayed, and the user put at the current cursor position of wnum.  You have
some control over the displayable data by OR'ing one or more of these values
with dtype:
 
    OR with dtype       Causes
    =============       ======
    WNDPTRDISPLAY       Data pointed to by dptr
                        displayed before input.
 
    WNDISPLAYONLY       Data pointed to by dptr or
                        default if WNDPTRDISPLAY not
                        used, displayed and wninput
                        returns immediately.  WNOK
                        returned if data displayed ok.
 
    WNWIPE              Will cause data to be cleared
                        when user hits first non-editing
                        key while in first edit column.
 
    WNCRCHOP            An interesting method of input that
                        your users will either love or hate
                        you for.  If used, will blank the
                        input field to the right of, and
                        including the cursor when the user
                        hits ENTER.  If at the far right of
                        the input field the last character
                        will not be chopped.
 
    WNNOECHO            Characters will be entered but not
                        displayed.
 
If WNDPTRDISPLAY is not used here are the default values that will be presented
for editing:
 
    dtype       Default Display
    =====       ====================
    WNCHAR      " "     (space)
    WNCHARSTR   ""      (nul string)
    WNINT       "0"
    WNUINT      "0"

                                                                        5 - 47 

                                                                        wninput

    WNLINT      "0"
    WNULINT     "0"
    WNFLOAT     "0.0"
    WNDOUBLE    "0.0"
 
While editing the input, the user will be allowed to use the following movement
keys:
 
    Editing Keys        Causes
    ============        ======
    Left Arrow          Moves 1 column to left if possible.
    Right Arrow         Moves 1 column to right.
    Ins                 Toggles Insert/Overstrike mode.
    Del                 Deletes 1 col, pulls chars left.
    Backspace           Destructive left move.
    Escape              Terminates.  Original data intact.
    Enter               Terminates.  Entered data returned.
 
The user is only allowed to return via hitting the ENTER key if the data
input is valid per your dtype request.  Otherwise, the routine pointed to by
badinaction will be called with this synopsis:
 
    int   (*badinaction)(wnum,dtype,code,key,curbuf);
    int   wnum;                         current window
    int   dtype;                        data type being entered
    int   code;                         WNESC, WNCR, or WNBADCHAR
    int   key;                          key input if code == WNBADCHAR
    char  *curbuf;                      current input buffer
 
The default action routine (badinaction == WNACTIONNULL) will beep at the user
for WNCR or WNBADCHAR and return -1 to wninput.  A WNESC will return WNESC.
 
If, in your badinaction routine, you want to switch() on dtype you will need to
mask it like this:
 
    switch(dtype & WNDTYPEMASK){
        case    WNCHAR: .....
        case    WNINT:  .....
 
Just so you know exactly what happens when the user hits ENTER or ESC, here is
the pseudocode for the wninput function when ENTER or ESC is pressed:
 
For ESCAPE:
 
    IF keycode == ESCAPE THEN
        call action routine (wnum,dtype,WNESC,key,curbuf)
        IF action return == -1 THEN
            keep editing
        ELSE
            IF WNDPTRDISPLAY specified THEN
                set dptr to original data
            ELSE
                set dptr to default data
            ENDIF

                                                                        5 - 48 

                                                                        wninput

            display dptr data
            RETURN action routine return value
        ENDIF
 
For ENTER:
 
    IF keycode == ENTER THEN
        IF WNCRCHOP specified THEN
            blank field from cursor to end of field
        ENDIF
        IF field == all spaces THEN
            IF WNDPTRDISPLAY specified THEN
                IF dtype == WNCHARSTR THEN
                    set dptr = '\0'
                    display dptr data
                    RETURN WNCR
                ELSE
                    fill curbuf with dptr data
                ENDIF
            ELSE
                fill curbuf with default data
            ENDIF
 
        validate current input buffer (curbuf)
        IF data good THEN
            sscanf curbuf to dptr
            display dptr data
            RETURN WNOK
        ELSE
            call action routine (wnum,dtype,WNCR,key,curbuf)
            IF action return == -1 THEN
                keep editing
            ELSE
                IF WNDPTRDISPLAY specified THEN
                    set dptr to original data
                ELSE
                    set dptr to default data
                ENDIF
                display dptr data
                RETURN action routine return value
            ENDIF
        ENDIF

Return Value:

A negative value indicates an error which can be found in <wn.h>.  A positive
value indicates one of the following:
 
    wninput return      Means
    ==============      =====
    WNOK                User actually entered data or
                        default was accepted.
    WNCR                0 length string returned.
    WNESC               User pressed ESC key.

                                                                        5 - 49 

                                                                        wninput

 
If dtype is WNCHARSTR and the user only enters spaces (if they're allowed) it
will be the same as if he/she just pressed ENTER.  WNCR will be returned and
the first character of dptr will be set to '\0'.
 
If the dtype modifier WNDISPLAYONLY is used without WNDPTRDISPLAY then your
dptr will contain the default data just as if the user had accepted it via
a ENTER key.

See Also:

wnputchar, wnputs, wnprintf

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
promptuser(prompt,fbuf,len)
/*
    a little routine that will display a window, prompt user, and stuff the
    result string in fbuf.  The window will be centered on the screen with
    the prompt displayed and the answer to the right.  If the len given plus
    prompt won't fit on one line, the prompt will be displayed and the answer
    input on the next window line.
 
    If fbuf contains something already it will be displayed as a default.
 
    WNOK  is returned if something was entered or user accepted default.
    WNCR  is returned if a zero length string was returned.
    WNESC is returned if user hits escape.
    -255  is returned if prompt or len is to big.
          any other negative return indicates a window error.
*/
 
char *prompt;   /* what to display to user */
char *fbuf;     /* where to put the string */
int  len;       /* max input length that can be input */
{
int wnum, row, col, width, height, dtype, code;
 
if ((len <= 0) || (strlen(prompt) > (wngscols() - 4))
    return(-255);
width  = strlen(prompt) + len + 4; /* window sides + gap == 4 */
height = 5;                        /* window top/bottom, input, gap lines */
if (width > wngscols()){           /* is it bigger than screen can handle? */
    width = len + 4;
    height++;
    }
if (width > wngscols())
    return(-255);                  /* can't do it */
 

                                                                        5 - 50 

                                                                        wninput

row   = (wngsrows() - height) / 2;
col   = (wngscols() - width) / 2;
dtype = WNCHARSTR;
if ((wnum = wncreate(row,col,width,height,WNBLACK,WNCYAN,WNBLACK,WNCYAN)) < 0)
    return(wnum);
wnlputs(wnum,2,2,prompt);
if (height > 5)
    wnlocate(wnum,3,2);           /* overflow to next line */
if (*fbuf)                        /* show default data? */
    dtype |= WNDPTRDISPLAY | WNWIPE;
 
code = wninput(wnum,dtype,fbuf,len,0,NULL,WNACTIONNULL);
wndestroy(wnum);
return(code);
};
/*
    See the demo/test program WNINDEMO.c on distribution disk for complete
    example of multiple field entry with up/down arrow processing.
*/




































                                                                        5 - 51 

                                                                      wninschar

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wninschar(wnum);
int   wnum;                         window number

Description:

The wninschar function is used to open a blank character slot at the current
cursor position,  all characters to the right of, and including, the current
cursor position will be shifted to the right 1 character.  The rightmost window
character will be lost.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnbs, wndeol, wninsline

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnlputs(wnum,2,3,"hello world");
wnlocate(wnum,2,5);
wninschar(wnum);                      row 2 is now "hell o world"













                                                                        5 - 52 

                                                                      wninsline

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wninsline(wnum);
int   wnum;                        window number

Description:

The wninsline function is used to insert a blank line at the current cursor
position in window wnum.  The inserted blank line is filled with the current
background color and all rows below the current row are scrolled down.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wndline, wnscroll

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnlputs(wnum,2,1,"this is row 2");
wnlputs(wnum,3,1,"this is row 3");
wnlocate(wnum,3,1);
wninsline(wnum);
wnputs(wnum,"this is between row 2 and old row 3");












                                                                        5 - 53 

                                                                      wninwindow

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wninwindow(wnum,row,col);
int  wnum;                        window number
int  row,col;                     position in window

Description:

The wninwindow function tells you if the position row,col is INSIDE the border
of window wnum.

Return Value:

A 0 return value indicates that row,col is not inside the border, 1 indicates
row,col is inside, and a negative return value means wnum is invalid.

See Also:

wnwrowtos, wnwcoltos

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum, stat;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
stat = wninwindow(wnum,0,0);          stat is false
stat = wninwindow(wnum,1,1);          stat is true
stat = wninwindow(wnum,8,68);         stat is true
stat = wninwindow(wnum,9,68);         stat is false












                                                                        5 - 54 

                                                                        wnlocate

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnlocate(wnum,row,col);
int  wnum;                        window number
int  row,col;                     new cursor position

Description:

The wnlocate function is used to position the cursor for window number wnum.
Row,col is the desired cursor location.  Window Manager text placement routines
will use the current cursor location as their printing start point.
 
With this routine it is possible to position the cursor on the window border
(0,0 ...).  This will allow you to put text on the border corners, however, the
text colors will be those set by wnswcolor.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.  If the values for row or col are outside window wnum they will be ignored
and the cursor position will not be changed.

See Also:

wnlputchar, wnlputncolor, wnlputhcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlocate(wnum,0,0);                   locate cursor at upper left corner
wnprintf(wnum,"%d",wnum);             print window number








                                                                        5 - 55 

                                                                      wnlputchar

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnlputchar(wnum,row,col,c);
int  wnputchar(wnum,c);
int  wnum;                          window number
int  row,col;                       cursor position
int  c;                             character to print

Description:

The wnlputchar and wnputchar functions are used to print a single character, c,
in window wnum.  The wnlputchar function will call wnlocate with row,col prior
to printing while wnputchar assumes you have called wnlocate.  Colors used will
be those set in the wncreate or wnswcolor functions.  If row or col are outside
the window, the cursor position will not change and a character will not be
printed.
 
After printing, the cursor will be advanced 1 character to the right.  If the
new column is in the right edge border or beyond, the cursor row will be
advanced and the cursor column set to 1.  If the new cursor row (if any) winds
up in the bottom border or beyond, the window scroll flag will be looked at.  If
the scroll flag is set, all text in the window will be scrolled up and the
cursor row will be set just above the bottom border.  If the scroll flag is
false, the cursor row will be set to 1 and the window text will not be scrolled.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnlputs, wnputs, wnprintf

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputchar(wnum,0,0,'1');             put "1" at upper corner in border

                                                                        5 - 56 

                                                                      wnlputchar

wnlocate(wnum,2,5);                   locate cursor
wnputchar(wnum,'X');                  place an "X"





















































                                                                        5 - 57 

                                                                    wnlputhcolor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnlputhcolor(wnum,row,col,bc,fc,len);
void  wnputhcolor(wnum,bc,fc,len);
int   wnum;                                 window number
int   row,col;                              cursor position
int   bc;                                   background color
int   fc;                                   foreground color
int   len;                                  number of characters to color

Description:

The wnlputhcolor and wnputhcolor functions are used to color existing text in
window wnum.  One of these 2 functions should be used when it is desired to
highlight text in an existing window.
 
If running on a color monitor, there is no difference between wnputncolor and
wnputhcolor, when running on a monochrome monitor though things are a little
different.  In a mono display system the values of bc and fc are ignored and a
monochrome highlight attribute (as set by wnshmatt) is used.  This approach
allows you to set up a color scheme that looks good on a color display without
worrying about how things will look on a mono display.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnputncolor, wnlputncolor, wnshmatt

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnshmatt(WNUNDERLINE);                how highlight will look on mono
wnsnmatt(WNREVERSE);                  how normal text will look on mono
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputs(wnum,2,1,"Hello World");      will be reverse video on mono

                                                                        5 - 58 

                                                                    wnlputhcolor

    .
    . because of how we set the monochrome attributes before the wncreate, the
    . next line will cause "World" to turn green on yellow in a color system,
    . underlined on a mono display.
    .
wnlputhcolor(wnum,2,7,WNYELLOW,WNGREEN);

















































                                                                        5 - 59 

                                                                    wnlputncolor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnlputncolor(wnum,row,col,bc,fc,len);
void  wnputncolor(wnum,bc,fc,len);
int   wnum;                           window number
int   bc;                             background color
int   fc;                             text color
int   len;                            number of columns to color
int   row,col;                        cursor location

Description:

The wnlputncolor and wnputncolor are used to change the colors of text already
displayed in window wnum.  The wnputncolor function will change the color of len
number of characters, starting at the current cursor position.  The background
will be changed to bc and the foreground to fc.  The wnlputncolor routine will
change the current cursor position to row,col via wnlocate prior to changing
text colors.
 
Here are the available color constants as defined in the include file <wn.h>:
 
    Constant    Value    Description    Fc/Bc
    ==============================================
    WNBLACK       0      Black          Both
    WNBLUE        1      Blue           Both
    WNGREEN       2      Green          Both
    WNCYAN        3      Cyan           Both
    WNRED         4      Red            Both
    WNMAGENTA     5      Magenta        Both
    WNBROWN       6      Brown          Both
    WNGRAY        7      Gray           Both
    WNDGRAY       8      Dark Gray      Bc Only
    WNLBLUE       9      Light Blue     Bc Only
    WNLGREEN      10     Light Green    Bc Only
    WNLCYAN       11     Light Cyan     Bc Only
    WNLRED        12     Light Red      Bc Only
    WNLMAGENTA    13     Light Magenta  Bc Only
    WNYELLOW      14     Yellow         Bc Only
    WNWHITE       15     White          Bc Only

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnputhcolor, wnlputhcolor, wnprintf


                                                                        5 - 60 

                                                                    wnlputncolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputs(wnum,3,1,"Hello World");
    .
    . The next line will change "World" to blinking green on yellow (yuk)
    .
wnlputncolor(wnum,3,7,WNYELLOW, WNGREEN | WNBLINK);




































                                                                        5 - 61 

                                                                        wnlputs

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnlputs(wnum,row,col,str);
int  wnputs(wnum,str);
int  wnum;                         window number
int  row,col;                      cursor position
char *str;                         null termination string to print

Description:

The wnlputs and wnputs function print a null terminated string, str, in window
wnum.  The wnlputs function will call wnlocate with row,col prior to printing
while wnputs assumes you have called wnlocate.  Colors used will be those set in
the wncreate or wnswcolor functions.  If row or col are outside the window, the
cursor position will not change and your string will not be printed.
 
Rules for cursor wrap and scrolling are the same as the wnputchar function.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnputchar, wnlocate, wnprintf

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputs(wnum,2,7,"Hello World");      locate and print string








                                                                        5 - 62 

                                                                        wnltitle

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnbtitle(wnum,str);           bottom title routine
int  wnltitle(wnum,str);           left title routine
int  wnrtitle(wnum,str);           right title routine
int  wnttitle(wnum,str);           top title routine
 
int  wnum;                         window number
char *str;                         title string

Description:

The wnbtitle, wnltitle, wnrtitle, and wnttitle functions are used to place a
title string, str, in the border of window wnum.  The title string str will be
centered vertically if using wnltitle or wnrtitle, horizontally if using
wnbtitle or wnttitle.  Passing a null terminated string with length of 0 will
cause a displayed title to be removed.  If the title string is too long it will
be truncated to fit the window border.
 
The string str will be bordered on both ends by the current window border
characters so if you want something that looks clean you should probably
bracket your title strings with something like "[ good title ]" instead of
just "good title".
 
After creation, window title colors will be the same as the border characters.
Use the wnswtcolor function prior to calling a titling routine if you want
different title colors.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 

                                                                        5 - 63 

                                                                        wnltitle

wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnttitle(wnum,"[ Main Menu ]");       top title same color as border
wnswtcolor(wnum,WNBLUE,WNCYAN);       color for new titles
wnbtitle(wnum,"[ ESC to Exit ]");     bottom title with new colors


















































                                                                        5 - 64 

                                                                          wnmove

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnmove(wnum,row,col);
int  wnum;                             window number
int  row,col;                          new window location

Description:

The wnmove function is used to move existing window wnum to a new screen
location row and col.  The new position is where you want the upper left
window corner to be placed.  All text, colors, and titles will be moved with the
window but it is the applications responsibility for making sure the window
being moved will fit at the new location.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wncreate, wnsize

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnmove(wnum,7,13);                    move right 2, down 3












                                                                        5 - 65 

                                                                      wnmovechar

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnmovechar(wnum,torow,tocol);
int   wnum;                           window number
int   torow,tocol;                    new position

Description:

The wnmovechar function moves the character and color from the current cursor
location in wnum to the new location torow,tocol.  The old character location
will be filled with a space using the default window background color.  The
current cursor location does not change.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnmoves

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlocate(wnum,2,3);                   position cursor
wnputchar(wnum,'V');                  put a character at 2,3
wnlocate(wnum,2,3);
wnmovechar(wnum,5,7);                 move "V" to 5,7  blank now at 2,3










                                                                        5 - 66 

                                                                        wnmoves

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnmoves(wnum,torow,tocol,len);
int   wnum;                           window number
int   torow,tocol;                    new position
int   len;                            number of characters to move

Description:

The wnmoves function is used to move a string from the current cursor position
in wnum to a new position; torow,tocol.  Len number of characters will be moved
along with their color attributes.  The space previously occupied by the string
will be filled with blanks using the current window background color.
Overlapping of the old and new locations will be handled correctly but it is
your responsibility to ensure that the new location will accomodate len
characters.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnmovechar

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnprintf(wnum,"Hello world");         print something
wnlocate(wnum,1,1);
wnmoves(wnum,1,13);                   now we have "world Hello"







                                                                        5 - 67 

                                                                        wnprintf

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnprintf(wnum,formatstring[,argument...]);
int  wnum;                                      window number
char *formatstring;                             format control

Description:

The wnprintf function formats and prints a series of characters and values to
the window wnum.  The formatstring consists of ordinary characters, escape
sequences, and, if there are arguments following the formatstring, format
specifications.  Oridinary characters and escape sequences are simply copied to
wnum in order of their appearance.
 
If there are arguments following the formatstring, then the formatstring must
contain format specifications that determine the output format for these
arguments.  Format specifications always begin with a percent sign (%) or tilde
(~), and are described in greater detail below.
 
The formatstring is read left to right.  When the first format specification (if
any) is encountered, the value of the first argument after the formatstring is
converted and output according to the format specification.  The second format
specification causes the second argument to be converted and output, and this
continues through the end of the formatstring.  If there are more arguments than
there are format specifications, the extra arguments are ignored.  The results
are undefined if there are not enough arguments for all the format
specifications.
 
A format specification has the following form:
 
%[flags][width][.precision][{F|N|h|l}]type
 
or
 
~{bccolor|*},{fccolor|*}~
 
 
The second format specification type allows color change information to be
imbedded in formatstring.  Each color change specification must include both
background and foreground colors delimited on each side by the tilde (~)
character.  An asterisk (*) supplied for one or both colors will cause a change
to the appropriate window default color.  Color change specifications are in
effect for a single wnprintf statement, subsequent wnprintf calls will use the
window default colors.
 
Each field of the first format specification is a single character or a number
signifying a particular format option.  The type character, which appears after
the last optional format field, determines whether the associated argument is
interpreted as a character, a string, or a number (see Table P.1).  The simplest

                                                                        5 - 68 

                                                                        wnprintf

format specificatin contains only the percent sign and a type character (for
example, %s).  The optional fields control other aspects of the formatting, as
follows:
 
 
flags - Justification of output and printing of signs, blanks, decimal points,
octal and hexadecimal prefixes (see Table P.2).
 
width - Minimum number of character output.
 
precision - Maximum number of characters printed for all or par of the output
field, or minimum number of digits printed for integer values (see Table P.3).
 
bccolor - New background color for subsequent output in this wnprintf call.
 
fccolor - New foreground color for subsequent output in this wnprintf call.
 
F,N - Prefixes that allow user to override default addressing conventions of
memory model being used:
 
   F - Used in small model to print value that has been declared far.
 
   N - Used in medium, large and huge models for near value.
 
F and N should be used only with the s and p type characters, since they are
relevant only with arguments that pass a pointer.
 
h - Used as a prefix with the integer types d,i,o,u,x, and X to specify that the
argument is a short int.
 
l - Used as a prefix with d,i,o,u,x, and X types to specify that the argument is
a long int; also used as a prefix with e,E,g, or G types to show that the
argument is double, rather than float.
 
 
If a percent sign (%) is followed by a character that has no meaning as a format
field, the character is simply copied to wnum.  For example, to print a percent-
sign character, use %%.
 
Table P.1
 
wnprintf Type Characters
========================
 
d - Integer - Signed Decimal integer
 
i - Integer - Signed decimal integer
 
u - Integer - Unsigned decimal integer
 
o - Integer - Unsigned Octal integer
 
x - Integer - Unsigned hexadecimal integer, using "abcdef"
 

                                                                        5 - 69 

                                                                        wnprintf

X - Integer - Unsigned hexadecimal integer, using "ABCDEF"
 
f - Floating point - Signed value having the form [-]dddd.dddd, where dddd is
one or more decimal digits.  The number of digits before the decimal point
depends on the magnitude of the number, and the number of digits after the
decimal point depends on the requested precision.
 
e - Floating point - Signed value having the form [-]d.dddd e [sign]ddd, where d
is a single decimal digit, dddd is one or more decimal digits, ddd is exactly
three decimal digits, and sign is + or -.
 
E - Floating point - Identical to the "e" format, except that "E" introduces the
exponent instead of "e".
 
g - Floating point - Signed value printed in "f" or "e" format, whichever is
more compact for the given value and precision (see below).  The "e" format is
used only when the exponent of the value is less than -4 or greater than
precision.  Trailing eros are truncated and the decimal point appears only if
one or more digits follow it.
 
G - Floating point - Identical to the "g" format, except that "E" introduces the
exponent (where appropriate) instead of "e".
 
c - Character - Single character
 
s - String - Characters printed up to the first null character ('\0') or until
precision is reached.
 
n - Pointer to integer - Number of characters successfully written so far to the
stream or buffer; this value is stored in the integer whose address is given as
the argument.
 
p - Far pointer - Prints the address pointed to by the argument in the form
zzzz.yyyy, where zzzz is the segment and yyyy is the offset, and the digits x
and y are uppercase hexadecimal digits; %Np prints only the offset of the
address, yyyy. Since %p expects a pointer to a far value, pointer arguments to p
must be cast to far in small-model programs.
 
 
Table P.2
 
wnprintf Flag Characters
========================
 
Flag    ==> -
Default ==> Right justify
Meaning ==> Left justify the result within the field width.
 
Flag    ==> +
Default ==> Sign appears only for negative signed values (-).
Meaning ==> Prefix the output value with a sign (+ or -) if the output value
            is of a signed type.
 
Flag    ==> blank (' ')

                                                                        5 - 70 

                                                                        wnprintf

Default ==> No blank
Meaning ==> Prefix the output value with a blank if the output value is signed
            and positive; the "+" flag overrides the blank flag if both appear,
            and a positive signed value will be output with a sign.
 
Flag    ==> #   (o,x,X)
Default ==> No Prefix
Meaning ==> When used with the o,x, or X format, the "#" flag prefixes any
            nonzero output value with 0, 0x, or 0X, respectively.
 
Flag    ==> #   (e,E,f)
Default ==> Decimal point appears only if digits follow it.
Meaning ==> When used with the e,E, or f format, the "#" flag forces the output
            value to contain a decimal point in all cases.
 
Flag    ==> #   (g,G)
Default ==> Decimal point appears only if digits follow it.  Trailing zeros are
            truncated.
Meaning ==> When used with the g or G format, the "#" flag forces the output
            value to contain a decimal point in all cases and prevents the
            truncation of trailing zeros.  The "#" flag is ignored when used
            with c,d,i,u, or s.
 
The width is a non-negative decimal integer controlling the minimum number of
characters printed.  If the number of characters in the ouput value is less than
the specified width, blanks are added on the left or the right (depending on
whether the "-" flag is specifed) until the minimum width is reached.  If width
is prefixed with a 0, zeros are added until the minimum width is reached (not
useful for left-justified numbers).
 
The width specification never causes a value to be truncated; if the number of
characters in the output value is greater than the specified width , or width is
not given, all characters of the value are printed (subject to the precision
specification).
 
The precision specification is a non-negative decimal integer preceded by a
period (.), which specifies the number of characters to be printed, or the
number of decimal places.  Unlike the width specification, the precision can
cause truncation of the output value, or rounding in the case of a floating-
point value.
 
The precision specification may be an asterisk (*), in which case an argument
from the argument list supplies the value.  The precision argument must precede
the value being formatted in the argument list.
 
The interpretation of the precision value, and the default when precision is
omitted, depend on the type, as shown in Table P.3
 







                                                                        5 - 71 

                                                                        wnprintf

Table P.3
 
How wnprintf Precision Values Affect Type
=========================================
 
Type(s) ==> d,i,u,o,x,X
Meaning ==> The precision specifies the minimum number of digits to be printed.
            If the number of digits in the argument is less than precision,
            the output value is padded on the left with zeros.  The value is
            not truncated when the number of digits exceeds precision.
Default ==> If precision is 0 or omitted entirely, or if the period (.) appears
            without a number following it, the precision is set to 1.
 
Type(s) ==> e,E,f
Meaning ==> The precision specifies the number of digits to be printed after the
            decimal point.  The last printed digit is rounded.
Default ==> Default precision is six; if precision is 0 or the period (.)
            appears without a number following it, no decimal point is printed.
 
Type(s) ==> g,G
Meaning ==> The precision specifies the maximum number of significant digits
            printed.
Default ==> All significant digits are printed.
 
Type(s) ==> c
Meaning ==> No effect
Default ==> Character printed
 
Type(s) ==> s
Meaning ==> The precision specifies the maximum number of characters to be
            printed.  Characters in excess of precision are not printed.
Default ==> Characters are printed until a null character is encountered.

Return Value:

The wnprintf function returns the number of characters printed.

See Also:

wnputchar, wnputs

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
char ch = 'h', *string = "hello world";
int  count = 234, *ptr, hex = 0x10, oct = 010, dec = 10;
double fp = 251.7366;
 
lminit(malloc,free,0);                init list manager first thing

                                                                        5 - 72 

                                                                        wnprintf

wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(0,0,70,20,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnttitle(wnum,"[ Test Window ]");
 
wnprintf(wnum,"%d    %+d    %06d    %X    %x    %o\n\n",
         count, count, count, count, count, count);
 
wnprintf(wnum,"1234567890234%n45678901234567890\n\n",&count);
 
wnprintf(wnum,"Value of count should be 13; count = %d\n\n",count);
 
wnprintf(wnum,"%10c%5c\n\n",ch,ch);
 
wnprintf(wnum,"%25s\n%25.4s\n\n",string,string);
 
wnprintf(wnum,"%f    %.2f    %e    %E\n\n",fp, fp, fp, fp);
 
wnprintf(wnum,"%i    %i    %i\n", hex, oct, dec);
 
ptr = &count;
wnprintf(wnum,"%Np    %p    %Fp\n",ptr, (int far *)ptr, (int far *)ptr);
 
wnprintf(wnum,"cyan on black~%d,%d~ red on yellow",WNYELLOW,WNRED);
 






























                                                                        5 - 73 

                                                                        wnprintf

Output:
 
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ[ Test Window ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º234    +234    000234    EA    ea    352                             º
º                                                                     º
º123456789012345678901234567890                                       º
º                                                                     º
ºValue of count should be 13; count = 13                              º
º                                                                     º
º         h    h                                                      º
º                                                                     º
º                 hello world                                         º
º                     hell                                            º
º                                                                     º
º251.736600    251.74    2517366e+002    2.517366E+002                º
º                                                                     º
º16    8    10                                                        º
º127A    1328:127A    1328:127A                                       º
º                                                                     º
ºcyan on black red on yellow                                          º
º                                                                     º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

































                                                                        5 - 74 

                                                                  wnprintfcount

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnprintfcount(formatstring[,argument...]);
char *formatstring;                             format control

Description:

The wnprintfcount function will return the actual number of characters that
WOULD be output to a window if you call wnprintf() with a window number and
the very exact formatstring and arguments.

Return Value:

A value equal or greater than 0.

See Also:

wnprintf

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int count;
    .
    .
    .
 
count = wnprintf(wnum,"cyan on black~%d,%d~ red on yellow",WNYELLOW,WNRED);
/*
    count should be == 27
*/















                                                                        5 - 75 

                                                                      wnputchar

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnlputchar(wnum,row,col,c);
int  wnputchar(wnum,c);
int  wnum;                          window number
int  row,col;                       cursor position
int  c;                             character to print

Description:

The wnlputchar and wnputchar functions are used to print a single character, c,
in window wnum.  The wnlputchar function will call wnlocate with row,col prior
to printing while wnputchar assumes you have called wnlocate.  Colors used will
be those set in the wncreate or wnswcolor functions.  If row or col are outside
the window, the cursor position will not change and a character will not be
printed.
 
After printing, the cursor will be advanced 1 character to the right.  If the
new column is in the right edge border or beyond, the cursor row will be
advanced and the cursor column set to 1.  If the new cursor row (if any) winds
up in the bottom border or beyond, the window scroll flag will be looked at.  If
the scroll flag is set, all text in the window will be scrolled up and the
cursor row will be set just above the bottom border.  If the scroll flag is
false, the cursor row will be set to 1 and the window text will not be scrolled.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnlputs, wnputs, wnprintf

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputchar(wnum,0,0,'1');             put "1" at upper corner in border

                                                                        5 - 76 

                                                                      wnputchar

wnlocate(wnum,2,5);                   locate cursor
wnputchar(wnum,'X');                  place an "X"





















































                                                                        5 - 77 

                                                                    wnputhcolor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnlputhcolor(wnum,row,col,bc,fc,len);
void  wnputhcolor(wnum,bc,fc,len);
int   wnum;                                 window number
int   row,col;                              cursor position
int   bc;                                   background color
int   fc;                                   foreground color
int   len;                                  number of characters to color

Description:

The wnlputhcolor and wnputhcolor functions are used to color existing text in
window wnum.  One of these 2 functions should be used when it is desired to
highlight text in an existing window.
 
If running on a color monitor, there is no difference between wnputncolor and
wnputhcolor, when running on a monochrome monitor though things are a little
different.  In a mono display system the values of bc and fc are ignored and a
monochrome highlight attribute (as set by wnshmatt) is used.  This approach
allows you to set up a color scheme that looks good on a color display without
worrying about how things will look on a mono display.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnputncolor, wnlputncolor, wnshmatt

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnshmatt(WNUNDERLINE);                how highlight will look on mono
wnsnmatt(WNREVERSE);                  how normal text will look on mono
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputs(wnum,2,1,"Hello World");      will be reverse video on mono

                                                                        5 - 78 

                                                                    wnputhcolor

    .
    . because of how we set the monochrome attributes before the wncreate, the
    . next line will cause "World" to turn green on yellow in a color system,
    . underlined on a mono display.
    .
wnlputhcolor(wnum,2,7,WNYELLOW,WNGREEN);

















































                                                                        5 - 79 

                                                                    wnputncolor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnlputncolor(wnum,row,col,bc,fc,len);
void  wnputncolor(wnum,bc,fc,len);
int   wnum;                           window number
int   bc;                             background color
int   fc;                             text color
int   len;                            number of columns to color
int   row,col;                        cursor location

Description:

The wnlputncolor and wnputncolor are used to change the colors of text already
displayed in window wnum.  The wnputncolor function will change the color of len
number of characters, starting at the current cursor position.  The background
will be changed to bc and the foreground to fc.  The wnlputncolor routine will
change the current cursor position to row,col via wnlocate prior to changing
text colors.
 
Here are the available color constants as defined in the include file <wn.h>:
 
    Constant    Value    Description    Fc/Bc
    ==============================================
    WNBLACK       0      Black          Both
    WNBLUE        1      Blue           Both
    WNGREEN       2      Green          Both
    WNCYAN        3      Cyan           Both
    WNRED         4      Red            Both
    WNMAGENTA     5      Magenta        Both
    WNBROWN       6      Brown          Both
    WNGRAY        7      Gray           Both
    WNDGRAY       8      Dark Gray      Bc Only
    WNLBLUE       9      Light Blue     Bc Only
    WNLGREEN      10     Light Green    Bc Only
    WNLCYAN       11     Light Cyan     Bc Only
    WNLRED        12     Light Red      Bc Only
    WNLMAGENTA    13     Light Magenta  Bc Only
    WNYELLOW      14     Yellow         Bc Only
    WNWHITE       15     White          Bc Only

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wnputhcolor, wnlputhcolor, wnprintf


                                                                        5 - 80 

                                                                    wnputncolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputs(wnum,3,1,"Hello World");
    .
    . The next line will change "World" to blinking green on yellow (yuk)
    .
wnlputncolor(wnum,3,7,WNYELLOW, WNGREEN | WNBLINK);




































                                                                        5 - 81 

                                                                          wnputs

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnlputs(wnum,row,col,str);
int  wnputs(wnum,str);
int  wnum;                         window number
int  row,col;                      cursor position
char *str;                         null termination string to print

Description:

The wnlputs and wnputs function print a null terminated string, str, in window
wnum.  The wnlputs function will call wnlocate with row,col prior to printing
while wnputs assumes you have called wnlocate.  Colors used will be those set in
the wncreate or wnswcolor functions.  If row or col are outside the window, the
cursor position will not change and your string will not be printed.
 
Rules for cursor wrap and scrolling are the same as the wnputchar function.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnputchar, wnlocate, wnprintf

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnlputs(wnum,2,7,"Hello World");      locate and print string








                                                                        5 - 82 

                                                                        wnrtitle

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnbtitle(wnum,str);           bottom title routine
int  wnltitle(wnum,str);           left title routine
int  wnrtitle(wnum,str);           right title routine
int  wnttitle(wnum,str);           top title routine
 
int  wnum;                         window number
char *str;                         title string

Description:

The wnbtitle, wnltitle, wnrtitle, and wnttitle functions are used to place a
title string, str, in the border of window wnum.  The title string str will be
centered vertically if using wnltitle or wnrtitle, horizontally if using
wnbtitle or wnttitle.  Passing a null terminated string with length of 0 will
cause a displayed title to be removed.  If the title string is too long it will
be truncated to fit the window border.
 
The string str will be bordered on both ends by the current window border
characters so if you want something that looks clean you should probably
bracket your title strings with something like "[ good title ]" instead of
just "good title".
 
After creation, window title colors will be the same as the border characters.
Use the wnswtcolor function prior to calling a titling routine if you want
different title colors.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 

                                                                        5 - 83 

                                                                        wnrtitle

wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnttitle(wnum,"[ Main Menu ]");       top title same color as border
wnswtcolor(wnum,WNBLUE,WNCYAN);       color for new titles
wnbtitle(wnum,"[ ESC to Exit ]");     bottom title with new colors


















































                                                                        5 - 84 

                                                                      wnscparms

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnscparms(wsave,wscroll,wcmode,ul,ur,ll,lr,0,0,0,0,0,vc,hc);
 
int   wsave;                screen save flag
int   wscroll;              scroll on/off flag
int   wcmode;               cursor style
int   ul,ur,ll,lr,vc,hc;    border drawing characters

Description:

The wnscparms allows you to determine what parameters will be used in creating
new windows.  Unless you call the wnscparms function the following parameters
will be used when creating new windows:
 
  Parameter    Description                Value
  ==============================================
  wsave        Screen save under window - on
  wscroll      Window scroll            - on
  wcmode       Cursor type              - WNUNDCURSOR
  ul,ur,ll,lr
  vc,hc        Border characters        - double line
 
If wsave is true, newly created windows will have the screen under them saved to
either memory or file, whichever was specified in the wninit function.  A true
value for wscroll will cause all window text to scroll up when a character is
written to the lower right window corner, a false value will cause the cursor to
wrap to position 1,1.  Wcmode specifies the cursor style.  Ul, ur,ll, and lr ar
the corner characters for the window border, vc is used for the left and right
sides while hc is used for the top and bottom.  The zeros supplied in the call
are for parameters to be used in future releases.



















                                                                        5 - 85 

                                                                      wnscparms

If you don't want your windows to have borders, supply a space character for all
of the box drawing set.  Normal window printing routines will still stay within
the border confines though.  Here are different border types you might want to
have:
 
       Default
 
   201   hc     187          218         191
    ÉÍÍÍÍÍÍÍÍÍÍÍÍ»            ÚÄÄÄÄÄÄÄÄÄÄÄ¿
    º ul      ur º            ³           ³
    º            º            ³           ³
    º            º            ³           ³
    º 186        º vc         ³ 179       ³
    º            º            ³           ³
    º            º            ³           ³
    º ll      lr º            ³           ³
    ÈÍÍÍÍÍÍÍÍÍÍÍÍ¼            ÀÄÄÄÄÄÄÄÄÄÄÄÙ
   200   205    188          192   196   217
 
 
   214          183          213         184
    ÖÄÄÄÄÄÄÄÄÄÄÄÄ·            ÕÍÍÍÍÍÍÍÍÍÍÍ¸
    º            º            ³           ³
    º            º            ³           ³
    º            º            ³           ³
    º 186        º            ³ 179       ³
    º            º            ³           ³
    º            º            ³           ³
    º            º            ³           ³
    ÓÄÄÄÄÄÄÄÄÄÄÄÄ½            ÔÍÍÍÍÍÍÍÍÍÍÍ¾
   211   196    189          212   205   190

Return Value:

This function has no return value.

See Also:

wngcparms, wnswcmode, wnswscroll, wnswbchars

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnscparms(1,1,WNSOLCURSOR,218,191,192,217,0,0,0,0,0,179,196);
    .

                                                                        5 - 86 

                                                                      wnscparms

    . now we'll create a window.  Screen save will be on, scroll on,
    . cursor will be a blinking solid, and the box drawing set will
    . use single line characters.
    .
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window


















































                                                                        5 - 87 

                                                                        wnscroll

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnscroll(wnum,srow,nrows,dir);
int   wnum;                                window number
int   srow;                                top row of scroll area
int   nrows;                               rows to scroll
int   dir;                                 scroll direction

Description:

The wnscroll function is used to scroll a block of lines inside wnum either up
or down as set by dir.  Startrow defines the top row of the scroll window,
nrows tells how many rows will be scrolled.  If scrolling up, the top line of
the scroll window will be lost while the new bottom line will be filled with
blanks using the current window background color.  If scrolling down, the bottom
line will be lost and the top will be set to blanks.
 
The current setting of the window scroll flag has no effect on this function.
 
Symbolic values that can be used for dir:
 
    Constant           Direction
    ============================
 
    WUP                Up
    WDOWN              Down

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
illegal wnum or parameters out of range.

See Also:

wninsline, wndline

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window

                                                                        5 - 88 

                                                                        wnscroll

wnprintf(wnum,"This is line 1\n");
wnprintf(wnum,"This is line 2\n");
wnprintf(wnum,"This is line 3\n");
wnprintf(wnum,"This is line 4\n");
wnprintf(wnum,"This is line 5\n");
wnprintf(wnum,"This is line 6\n");
    .
    .
    .
wnscroll(wnum,3,3,WUP);                line 3 now missing, blank line between
                                       5 and 6












































                                                                        5 - 89 

                                                                        wnscwnum

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int wngcwnum();         get window with cursor active
int wnscwnum(wnum);     set window with cursor
int wnum;               window number

Description:

The wngcwnum function is used to obtain the window number which contains
the active cursor.  The wnscwnum function will set the active cursor window
to the window specified by wnum.  The cursor will remain active in this
window until a different window other than wnum is accessed in some way via
a window manager routine.
 
The purpose of these routines is to allow an interrupt routine, such as a
keycode intercept, to save the active window, write to a different one, and
restore the cursor to its original state.

Return Value:

The wngcwnum function will return a negative number if a window is not active.
A positive value indicates a valid window number.  The wnscwnum function
returns 0 if all went well and a negative value if wnum is invalid.

See Also:

wngwcmode, wnswcmode

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
 
int  kbhit(), getch();             used in kminit() call
void showtime();                   for kmsbgr() function call
void (*ptr)();                     for kmgbgr() function call
int  mwnum,cwnum;                  main window, clock window
 
main(){
 
lminit(malloc,free,0);             init the list manager
kminit(kbhit,getch);               init the keyboard manager
wninit(0,0,NULL,0,malloc,free);    init the window manager
mwnum = wncreate(0,0,80,22,WNBLUE,
           WNCYAN,WNBLUE,WNCYAN);  open working window
cwnum = wncreate(22,0,80,3,WNBLUE,

                                                                        5 - 90 

                                                                        wnscwnum

           WNCYAN,WNBLUE,WNCYAN);  open clock window
kmsbgr(showtime);                  register background routine
    .
    .                              do other stuff in working window
    .
 
}
 
showtime()                         show time while waiting for key input
{
static long lasttime;
long nowtime;
long time();
struct tm *newtime;
int tempwnum;
char buf[30];
 
tempwnum = wngcwnum();
if (time(&nowtime) != lasttime){   we'll display time if changed
    newtime = localtime(&nowtime); get time in usable format
    strcpy(buf,asctime(newtime));
    buf[strlen(buf) - 1] = '\0';   get rid of newline in time buf
    wnlocate(cwnum,1,1);           position the cursor in main window
    wnprintf(cwnum,"%s",buf);      print time in clock window
    lasttime = nowtime;            update the status var
    wnscwnum(tempwnum);            put cursor back to window that was active
    }
}



























                                                                        5 - 91 

                                                                        wnshmatt

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnshmatt(att);
int   att;                  highlight mono attribute

Description:

The wnshmatt function sets the highlight attribute that will be used for newly
created windows.  Currently this value is used by the wnputhcolor function which
in turns is used by the menu package and field processing routines.  The value
of att determines how highlighted text will appear on a mono display.
 
    att value       display format
    ==============================================
    WNNORMAL        white text on black background
    WNREVERSE       black text on white background
    WNUNDERLINE     white on black w/underline

Return Value:

The wnshmatt function has no return value.

See Also:

wnghmatt, wnputhcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnshmatt(WNUNDERLINE);                new windows will underline if mono
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window










                                                                        5 - 92 

                                                                          wnsize

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnsize(wnum,width,height);
int  wnum;                              window number
int  width,height;                      new window size

Description:

The wnsize function is used to resize existing window wnum.  The top left corne
of the window will remain at its original location and all text and titles will
be destroyed.  Cursor style, scroll, border chars, and color will remain as they
were, with only width and height changing.
 
The parameters width and height specify the new size of window wnum.
 
Only a window that does not have another window "on top" of itself should be
resized.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wncreate, wnmove

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnsize(wnum,60,5);                    shrink window








                                                                        5 - 93 

                                                                        wnsnmatt

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
void  wnsnmatt(att);
int   att;                  normal mono attribute

Description:

The wnsnmatt function sets the normal text attribute that will be used for newly
created windows when running on a monochrome display.  Currently this value is
used by the wnputhcolor function which in turns is used by the menu package and
field processing routines.  The value of att determines how normal text will
appear on a mono display.
 
    att value       display format
    ==============================================
    WNNORMAL        white text on black background
    WNREVERSE       black text on white background
    WNUNDERLINE     white on black w/underline

Return Value:

The wnshmatt function has no return value.

See Also:

wnghmatt, wnshmatt, wngnmatt, wnputhcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
wnsnmatt(WNUNDERLINE);                new windows will underline if mono
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window










                                                                        5 - 94 

                                                                      wnswbchars

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnswbchars(wnum,ul,ur,ll,lr,vc,hc);
int  wnum;                                 window number
int  ul,ur,ll,lr,vc,hc;                    border characters

Description:

The wnswbchars function is used to change the border characters of an existing
window.  Ul, ur,ll, and lr are the corner characters, vc is the left/right side
character, and hc is the top/bottom character.  Any existing titles will be
destroyed and need to be regenerated.  For "clean" window display you should use
the wngcparms and wnscparms functions to alter the border drawing characters
prior to creating your windows.  Here are a few window formats and their box
characters:
 
   201   hc     187          218         191
    ÉÍÍÍÍÍÍÍÍÍÍÍÍ»            ÚÄÄÄÄÄÄÄÄÄÄÄ¿
    º ul      ur º            ³           ³
    º            º            ³           ³
    º            º            ³           ³
    º 186        º vc         ³ 179       ³
    º            º            ³           ³
    º            º            ³           ³
    º ll      lr º            ³           ³
    ÈÍÍÍÍÍÍÍÍÍÍÍÍ¼            ÀÄÄÄÄÄÄÄÄÄÄÄÙ
   200   205    188          192   196   217
 
   214          183          213         184
    ÖÄÄÄÄÄÄÄÄÄÄÄÄ·            ÕÍÍÍÍÍÍÍÍÍÍÍ¸
    º            º            ³           ³
    º            º            ³           ³
    º 186        º            ³ 179       ³
    º            º            ³           ³
    º            º            ³           ³
    º            º            ³           ³
    ÓÄÄÄÄÄÄÄÄÄÄÄÄ½            ÔÍÍÍÍÍÍÍÍÍÍÍ¾
   211   196    189          212   205   190

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wngwbchars, wnscparms



                                                                        5 - 95 

                                                                      wnswbchars

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnswbchars(wnum,214,183,211,189,186,196);  single top/bottom, double sides









































                                                                        5 - 96 

                                                                      wnswbcolor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnswbcolor(wnum,bbc,bfc);
int  wnum;                     window number
int  bbc;                      border background color
int  bfc;                      border foreground color

Description:

The wnswbcolor function is used to change the border background and foreground
colors of window wnum.  Bbc is the new background color, bfc is the new
foreground color.
 
Note:
This function causes the window border to be redrawn, therefore you will lose
any titles currently present on the window.
 
The following color constants or values can be used when specifying background
and/or foreground colors:
 
    Constant    Value    Description    Bbc/Bfc
    ==============================================
    WNBLACK       0      Black          Both
    WNBLUE        1      Blue           Both
    WNGREEN       2      Green          Both
    WNCYAN        3      Cyan           Both
    WNRED         4      Red            Both
    WNMAGENTA     5      Magenta        Both
    WNBROWN       6      Brown          Both
    WNGRAY        7      Gray           Both
    WNDGRAY       8      Dark Gray      Bc Only
    WNLBLUE       9      Light Blue     Bc Only
    WNLGREEN      10     Light Green    Bc Only
    WNLCYAN       11     Light Cyan     Bc Only
    WNLRED        12     Light Red      Bc Only
    WNLMAGENTA    13     Light Magenta  Bc Only
    WNYELLOW      14     Yellow         Bc Only
    WNWHITE       15     White          Bc Only

Return Value:

This function returns 0 if all went well, a negative number indicates an invalid
wnum.

See Also:

wnswcolor, wnswtcolor, wngwbbc, wngwbfc



                                                                        5 - 97 

                                                                      wnswbcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
    .
    .
wnswbcolor(wnum,WNGRAY,WNGREEN);       border now green on gray






































                                                                        5 - 98 

                                                                      wnswcmode

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnswcmode(wnum,cmode);
int  wnum;                      window number
int  cmode;                     cursor mode

Description:

The wnswcmode function changes the cursor style for window wnum.  The desired
cursor style, cmode, can be 1 of the following:
 
    Constant        Description
    ==========================================
    WNNOCURSOR      No cursor
    WNUNDCURSOR     Underline blinking cursor
    WNSOLCURSOR     Solid blinking cursor

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wngwcmode, wnscparms

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
wnswcmode(wnum,WNSOLCURSOR);          set cursor to solid









                                                                        5 - 99 

                                                                      wnswcolor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnswcolor(wnum,bc,fc);
int  wnum;                     window number
int  bc;                       text background color
int  fc;                       text foreground color

Description:

The wnswcolor function is used to change the inside text background and
foreground colors of window wnum.  Bc is the new background color, fc is the new
foreground color.  The new colors will take effect immediately causing already
present text and subsequent text to appear in the new colors.
 
The following color constants or values can be used when specifying background
and/or foreground colors:
 
    Constant    Value    Description    Fc/Bc
    ==============================================
    WNBLACK       0      Black          Both
    WNBLUE        1      Blue           Both
    WNGREEN       2      Green          Both
    WNCYAN        3      Cyan           Both
    WNRED         4      Red            Both
    WNMAGENTA     5      Magenta        Both
    WNBROWN       6      Brown          Both
    WNGRAY        7      Gray           Both
    WNDGRAY       8      Dark Gray      Bc Only
    WNLBLUE       9      Light Blue     Bc Only
    WNLGREEN      10     Light Green    Bc Only
    WNLCYAN       11     Light Cyan     Bc Only
    WNLRED        12     Light Red      Bc Only
    WNLMAGENTA    13     Light Magenta  Bc Only
    WNYELLOW      14     Yellow         Bc Only
    WNWHITE       15     White          Bc Only

Return Value:

This function returns 0 if all went well, a negative number indicates an invalid
wnum.

See Also:

wnswbcolor, wnswtcolor, wngwbc, wngwfc

Example:

#include   "malloc.h";
#include   "lm.h";

                                                                        5 - 100

                                                                      wnswcolor

#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
    .
    .
wnswcolor(wnum,WNGRAY,WNGREEN);       inside now green on gray










































                                                                        5 - 101

                                                                      wnswscroll

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnswscroll(wnum,scrollflag);
int  wnum;                        window number
int  scrollflag;                  scroll on/off flag

Description:

The wnswscroll function determines cursor positioning when the printing routines
place a character at the lower right window corner.  If scrollflag is true, all
text in the window will be scrolled up, false causes the cursor to be wrapped to
position 1,1 without scrolling the window text.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wngwscroll, wnscparms

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
wnswscroll(wnum,1);                   turn scrolling on
    .
    .  The next 2 lines will print the word "hello" at the lower right corner
    .  causing all text in the window to scroll up.
    .
wnlocate(wnum,8,64);
wnprintf(wnum,"hello");               window will scroll
    .
    .
wnswscroll(wnum,0);                   turn scrolling off
wnlocate(wnum,8,64);
wnprintf(wnum,"hello");               cursor wrapped to 1,1



                                                                        5 - 102

                                                                      wnswtcolor

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnswtcolor(wnum,tbc,tfc);
int  wnum;                     window number
int  tbc;                      titles background color
int  tfc;                      titles foreground color

Description:

The wnswtcolor function is used to change the title text background and
foreground colors of window wnum.  Tbc is the new background color, tfc is the
new foreground color.  This function will not affect existing titles, only new
ones.
 
The following color constants or values can be used when specifying background
and/or foreground colors:
 
    Constant    Value    Description    Tbc/Tfc
    ==============================================
    WNBLACK       0      Black          Both
    WNBLUE        1      Blue           Both
    WNGREEN       2      Green          Both
    WNCYAN        3      Cyan           Both
    WNRED         4      Red            Both
    WNMAGENTA     5      Magenta        Both
    WNBROWN       6      Brown          Both
    WNGRAY        7      Gray           Both
    WNDGRAY       8      Dark Gray      Bc Only
    WNLBLUE       9      Light Blue     Bc Only
    WNLGREEN      10     Light Green    Bc Only
    WNLCYAN       11     Light Cyan     Bc Only
    WNLRED        12     Light Red      Bc Only
    WNLMAGENTA    13     Light Magenta  Bc Only
    WNYELLOW      14     Yellow         Bc Only
    WNWHITE       15     White          Bc Only

Return Value:

This function returns 0 if all went well, a negative number indicates an invalid
wnum.

See Also:

wnswbcolor, wnswcolor, wngwbc, wngwfc

Example:

#include   "malloc.h";
#include   "lm.h";

                                                                        5 - 103

                                                                      wnswtcolor

#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
    .
    .
wnswtcolor(wnum,WNGRAY,WNGREEN);      new titles now green on gray










































                                                                        5 - 104

                                                                        wnttitle

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnbtitle(wnum,str);           bottom title routine
int  wnltitle(wnum,str);           left title routine
int  wnrtitle(wnum,str);           right title routine
int  wnttitle(wnum,str);           top title routine
 
int  wnum;                         window number
char *str;                         title string

Description:

The wnbtitle, wnltitle, wnrtitle, and wnttitle functions are used to place a
title string, str, in the border of window wnum.  The title string str will be
centered vertically if using wnltitle or wnrtitle, horizontally if using
wnbtitle or wnttitle.  Passing a null terminated string with length of 0 will
cause a displayed title to be removed.  If the title string is too long it will
be truncated to fit the window border.
 
The string str will be bordered on both ends by the current window border
characters so if you want something that looks clean you should probably
bracket your title strings with something like "[ good title ]" instead of
just "good title".
 
After creation, window title colors will be the same as the border characters.
Use the wnswtcolor function prior to calling a titling routine if you want
different title colors.

Return Value:

This function returns 0 if all went well.  A negative value indicates an invalid
wnum.

See Also:

wnswtcolor

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 

                                                                        5 - 105

                                                                        wnttitle

wnum = wncreate(5,10,70,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
 
wnttitle(wnum,"[ Main Menu ]");       top title same color as border
wnswtcolor(wnum,WNBLUE,WNCYAN);       color for new titles
wnbtitle(wnum,"[ ESC to Exit ]");     bottom title with new colors


















































                                                                        5 - 106

                                                                      wnxlatwtos

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnxlatwtos(wnum,row,col);       window position to screen translation
int  wnum;                           window number
int  *row,*col;                      POINTERS to row,col to translate

Description:

The wnxlatwtos function is used to obtain the display screen coordinates if
the windows coordinates are known.  These routines are most helpful when
creating overlapping windows.  Wnum is the window number, row and col are the
window coordinates you want translated to screen coordinates.
 
Remember, you must supply Pointers to the variables row and col which will be
changed by this routine.

Return Value:

A value of 0 indicates the translation went well.  A negative return value
indicates an invalid wnum.
 
It is your responsibility for ensuring that row and col are inside the window
boundries.

See Also:

wncreate, wninwindow

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
 
int  wnum1, wnum2;
int  row,col;
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
 
wnum1 = wncreate(5,10,30,10,WNBLACK,WNCYAN,WNBLUE,WNRED);  create window
    .
    . The next few lines will allow us to create a window "on top" of wnum1
    . without knowing the exact location of wnum1.
    .
    .      wnum1 ÉÍÍÍÍÍÍÍÍÍÍÍ»
    .            º           º
    .            º           º

                                                                        5 - 107

                                                                      wnxlatwtos

    .            º           º
    .            º     ÉÍÍÍÍÍÍÍÍÍÍÍ»
    .            º     º           º
    .            º     º           º
    .            ÈÍÍÍÍÍº           º
    .                  º           º
    .                  º           º
    .                  º           º
    .                  ÈÍÍÍÍÍÍÍÍÍÍÍ¼  wnum2
    .
row = wngwheight(wnum1) / 2;
col = wngwwidth(wnum1) / 2;
wnxlatwtos(wnum1,&row,&col);       find screen center of wnum1
wnum2 = wncreate(row,col,30,5,WNBLACK,WNCYAN,WNBLUE,WNRED); create window









































                                                                        5 - 108



6 Menu Manager


6.1 Introduction

The Menu package will allow your applications to create and display menus of
various flavors to a user with a minimum of effort.  Features include:
 
    - Pop-Up, Pull-Down, and Light-Bar menus supported
    - Nesting to any depth
    - Each menu item can specify another menu or routine to call
    - Colors and titles completely definable
    - Multiple pages and best fit handled automatically
    - User can "mark/unmark" items
    - "Hot-Key" can be defined for each menu item

6.2 Module Initialization

Prior to using any of the Menu Manager functions you must call the function
mminit().  This will initialize internal data structures as well as tell the
menu manager package which routines it should call for obtaining keyboard
status and input.  Since this module does use other HIM modules they must be
initialized PRIOR to calling the routine mminit().
 
There are four (4) demo programs in this distribution that show you how to use
the HIM Menu Manager.  The first, MFDEL.c, is a file deletion utility that
creates a menu of all files in the current directory and allows you to mark
which ones you would like deleted.  The other 3 demos, MMDEMO1.c, MMDEMO2.c, and
MMDEMO3.c, show how to build and use a POPUP, LIGHTBAR, and PULLDOWN menu.

6.3 Include Files

The C include file "mm.h" must be #includ'ed at the top of your application
source file in order to use the Menu Manager package.  This gives you
access to symbolic constants used by the packages as well as letting the
compiler do parameter type checking.

6.4 Symbolic Constants

All of the following constants are defined in the include file <mm.h>.

6.4.1 Error Constants

All error values returned from the Menu Manager are either negative integers
or NULL character pointer.
 
   MMMAERROR   -1       memory allocation error
   MMBADMNUM   -2       bad menu number
   MMBADMEL    -3       bad menu element number
   MMNMMELS    -4       no more elements
   MMMTBERROR  -5       menu or menu element too big/small
   MMBMTERROR  -6       bad menu type in mmcreate call
   MMPORERROR  -7       parameter out of range
   MMBMCERROR  -8       mcall name in doesn't exist

                                                                        6 - 1  

                                                                                

   MMDMNERROR  -9       dup menu name tried to be created
   MMFWERROR   -10      file write error, from window mngr
   MMFRERROR   -11      file read error, from window mngr
   MMMNDERROR  -12      menu not currently displayed

6.4.2 Menu Types

Currently these are the menu types supported by the Menu Manager.
 
   MMPOPUP     1        pop up menu
   MMPULLDOWN  2        pull down menu
   MMLIGHTBAR  3        "lotus" style light bar menu

6.4.3 Menu Location and Size

By OR'ing these values together you can determine whether your menu
will be automatically located and sized or some combination in between.
 
   MMABSDEF    0x0000   size and location automatic
   MMABSR      0x0001   absolute row location
   MMABSC      0x0002   absolute col location
   MMABSW      0x0004   absolute width
   MMABSH      0x0008   absolute height
   MMABSRC     MMABSR  | MMABSC
   MMABSWH     MMABSW  | MMABSH
   MMABSRCWH   MMABSRC | MMABSWH

6.4.4 Pre-Defined Action Routines

Use one of these action routines in mmcreate() or mmamel() if you don't
want or need to supply one of your own.
 
   MMACTIONNULL         no action routine
   MMACTIONESC          simulates escape
   MMACTIONESCONLY      only returns 0 when ESC hit

6.4.5 Mmpromenu func values

One of these can be used as 'func' in the mmpromenu() function.
 
   MMDISPLAY   1   Display primary portion of menu and return.
   MMDESTROY   2   Take down menu.
   MMPROCESS   3   Display menu and interact with user.

6.4.6 Hotkey Compare Constant

Do a OR of this constant with your hotkey parameter in mmamel() if you want
both upper and lower case to work for the hotkey.
 
   MMNOCASE    0x1000

6.4.7 Function Overview

All Menu Manager functions return an error code value.  Zero or greater

                                                                        6 - 2  

                                                                                

indicates success.  The functions are:
 
code    = mminit(mgetch,dynaloadfile);                  init package
 
mnum    = mmcreate(name,mtype,row,col,
                   width,height,abs,
                   ttitle,btitle,hdr,hsize,
                   lf,retkeyonly,actionr,actionn)       create menu
mnum    = mmgmnum(name)                                 get mnum from name
code    = mmsmnum(mnum,name,row,col,width,height,
                  abs,ttitle,btitle,retkeyonly,
                  actionr,actionn)                      redefine a menu
code    = mmdestroy(mnum);                              destroy menu
 
mel     = mmamel(mnum,name,mdata,mdesc,mcall,lf,
                 ronly,hotkey,actionr,actionn)          create menu item
code    = mmsmel(mnum,mel,name,mdata,mdesc,mcall,
                 lf,ronly,hotkey,actionr,actionn)       redefine element
code    = mmdmel(mnum,mel)                              delete menu element
 
code    = mmgcparms(&bc,&fc,&bbc,&bfc,&rbc,&rfc,
                    &mbc,&mfc,&hbc,&hfc,&tbc,&tfc,
                    &markchar,&markkey)                 get creation parms
code    = mmscparms(bc,fc,bbc,bfc,rbc,rfc,mbc,mfc,
                    hbc,hfc,tbc,tfc,markchar,markkey)   set creation parms
 
code    = mmpromenu(mnum,func,mel);                     process menu
 
name    = mmgmname(mnum)                                get name from mnum
mtype   = mmgmtype(mnum)                                get menu type
row     = mmgmrow(mnum)                                 get current pos
col     = mmgmcol(mnum)                                 upper left corner
width   = mmgmwidth(mnum)
height  = mmgmheight(mnum)                              current size
hdr     = mmgmheader(mnum)                              get header ptr
ttitle  = mmgmttitle(mnum)                              get top title
btitle  = mmgmbtitle(mnum)                              get bottom title
mnum    = mmgcmnum()                                    get current mnum
 
mel     = mmgmel(mnum,name)                             get mel from name
nmels   = mmgnummels(mnum)                              get number mels
mel     = mmgfirstmel(mnum)                             get 1st mel of mnum
mel     = mmgnextmel(mnum)                              get next mel
name    = mmgmelname(mnum,mel)                          get name from mel
mdata   = mmgmelmdata(mnum,mel)                         get mdata
mdesc   = mmgmelmdesc(mnum,mel)                         get description
mcall   = mmgmelmcall(mnum,mel)                         get sub-menu
ronly   = mmgmelronly(mnum,mel)                         readonly stat
hotkey  = mmgmelhotkey(mnum,mel)                        current hotkey
stat    = mmgmelstat(mnum,mel);                         get mark stat
 
code    = mmsmelmark(mnum,mel);                         mark an element
code    = mmsmelunmark(mnum,mel);                       unmark an element
code    = mmsmelronly(mnum,mel);                        set element ronly

                                                                        6 - 3  

                                                                                

code    = mmsmelnonronly(mnum,mel);                     non-readonly

6.4.8 Function Definitions

These List Manager function definitions are presented in alphabetical order,
each starting on a new page, to facilitate your search for information.
Function definitions are comprised of the following sections:
 
  - Summary       - function and parameter declarations
  - Description   - detailed description
  - Return Value  - explanation of return values
  - See Also      - related functions
  - Example       - programming example
 
A negative return value by any function indicates an error.








































                                                                        6 - 4  

                                                                          mmamel

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int     mmamel(mnum,name,mdata,mdesc,mcall,lf,ronly,hotkey,actionr,actionn);
 
int     mnum;           menu to add this menu item to
char    *name;          name of this element
char    *mdata;         string to display as menu item
char    *mdesc;         description line for lightbar menu type
char    *mcall;         name of menu to call when this item selected
int     lf;             static/auto flag for mdata and mdesc
int     ronly;          true if this menu item is read-only
int     hotkey;         pick item immediately key
int     (*actionr)();   action routine to call when item selected
char    actionn;        name of actionr routine.  Not supported in V1.1

Description:

The mmamel function is used to add a menu element to existing menu mnum.  Name
is an optional character string (9 chars + '\0' max) used to identify the menu
element.
 
Mdata is the character string which gets displayed when the menu is shown to
the user.  Mdesc is the description string that gets displayed as the second
line on the lightbar menu and is only used on this type of menu.  Lf is a flag
which tells if mdata and mdesc are static or auto strings.  A value of lf == 0
tells mmamel that both mdata and mdesc will be around for the life of this menu
and need not be stored internally.  Lf == 1 will cause a storage area in the
menu manager to be allocated and both strings copied to it.  The minimum length
for mdata must be 1 character, while the maximum is determined by the size,
location, and abs flag used in the mmcreate call.
 
Mcall is the name of a menu you want called when this menu item is selected by
the user.  Notice that this approach requires you to build your menus "bottom
up" so that all names are defined when you get to your top level menu and need
to specify mcall.  If you want an action routine to be called instead of a menu
when this item is selected, just pass NULL or a zero length string for mcall.
 
A value of true (non-zero) for ronly tells mmamel that this item is read-only
and invalid for selection by the user when the menu is processed via mmpromenu.
You can change this read-only status via mmsmelronly() during the lifetime of
the menu.
 
If a non-zero positive hotkey value is specified this menu item will be selected
immediately when the user presses this key while in mmpromenu().  A zero value
specifies no hotkey.  If a hotkey is specified and the item is currently read
only, the user still won't be able to select the item.  If you have more than
one menu element with the same hotkey defined a forward search from the
currently highlighted item is done.  If you do a logical OR (|) of your hotkey

                                                                        6 - 5  

                                                                          mmamel

value with the constant MMNOCASE a case insensitive comparision will be done
if your hotkey is an upper or lower case alpha.
 
Actionr is a pointer to a function which will get called when this item is
selected in mmpromenu().  When a user makes a menu selection, the order of
evaluation for "what to do next" is:
 
    - If the selected menu element has an action routine, call it.
    - Else if the selected menu element has a sub-menu call defined, call it.
    - Else if the MENU has an action routine, call it.
    - Else return the menu element number that was selected.
 
If you supply a action routine pointer it will be called using this synopsis:
int (*actionr)(mnum,mel,hotkey);
int mnum;                   menu number being processed
int mel;                    menu element that was selected
int hotkey;                 0 if <CR> selected element, >0 if hotkey
 
Before your actionr routine is called, the current menu item will be
de-highlighted.  Mnum is the number of the menu that was being processed and
mel is the menu element number that was selected.  You can use the query
routines to obtain information about the menu or menu element.  A value of -1
for mel means the ESCAPE key was pressed and usually indicates (by de-facto
convention) the user wants out of the menu. When menu elements are added to a
menu they start at number 1 and are contiguous.  The user will not be allowed
to select a read-only menu element so your action routine does not have to
check for it.
 
A value of -1 returned from your actionr routine causes the user to stay in
the menu.  A 0 or greater value will cause the menu to be taken down and the
value returned to the mmpromenu() caller.  For the pull-down menu type, the top
light bar will NOT be taken down.  You must use the mmpromenu routine with the
MMDESTROY function to get rid of it.
 
Actionn is a character string name of the actionr routine specified.  For now
it should be NULL.  Later versions will use this for dynamically loading menus.
 
The include file <mm.h> declares some default actionr functions which you can
use:
 
  Actionr Constant    ESCAPE Return   Selection Return
  ================    =============   ================
  MMACTIONNULL        0               Menu Element #
  MMACTIONESCONLY     0               0
 
Note:  An actionr function can not be specified for an element of a pulldown
menu, only a mcall to the "pop-up" menu which will be located just below the
lightbar is allowed.
 
Standard wnprintf() color change commands apply to mdata and mdesc.

Return Value:

A positive value indicates success and can be used in the future to query this

                                                                        6 - 6  

                                                                          mmamel

menu element (mel).  A negative value indicates an error which can be found in
<mm.h>.

See Also:

mminit, mmcreate

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mel;
char buf[80];
 
/* main menu (mm) */
/* assume that mmw, mmr, and mmc have been created already.. */
 
mm = mmcreate("mm",MMPOPUP,1,1,0,0,MMABSDEF,"[ mmdemo1 ]","",NULL,0,0,0,noaction
 
sprintf(buf,"~*,%d~W~*,*~orksheet",WNRED);
mmamel(mm,"",buf,"Global, Insert, Delete, Column, Erase, Titles, Window, Status,
             "mmw",1,0,MMNOCASE | 'w',MMACTIONNULL,NULL);
sprintf(buf,"~*,%d~R~*,*~ange",WNRED);
mmamel(mm,"",buf,"Format, Label, Erase, Name, Justify, Protect, Unprotect, Input
             "mmr",1,0,MMNOCASE | 'r',MMACTIONNULL,NULL);
sprintf(buf,"~*,%d~C~*,*~opy",WNRED);
mmamel(mm,"",buf,"Copy a cell or range of cells",
             "mmc",1,0,MMNOCASE | 'c',MMACTIONNULL,NULL);
    .
    .





















                                                                        6 - 7  

                                                                        mmcolorm

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int  mmcolorm(ttitle,btitle,row,col,bc,fc,defcolor,colortype,defflag,actionr);
 
char *ttitle, *btitle;      top and bottom menu titles
int  row,col;               position of CENTER of menu
int  bc,fc;                 colors to display
int  defcolor;              default color
int  colortype;             background or foreground
int  defflag;               determines if "default" is displayed at bottom
int  (*actionr)();          function to call with selection

Description:

This popup will make its own list of available colors based on the value of
colortype, if colortype==0 then a list of items (each with a different
background color) will be presented to the user.  Each item's foreground color
will be the same (the value of fc) and the starting menu item (one current on
entry) will be the background that matches bc.  There are 8 possible background
colors.  If bc == -1 then the default item will be the starting pick.
 
If colortype==1 then each item will have a different foreground color on a
background of bc.  There are 16 possible foreground colors.
 
If defflag==true (1) then an additional item will be put on the bottom of the
list, the string "Default".  On a background menu this will be item 8, on a
foreground menu this will be item 16.  If colortype==0, meaning you're wanting
a background color returned, the background color of the last item will be
defcolor.  The opposite is true if colortype == 1, the foreground color will
be  defcolor.
 
The routine pointed to by actionr will be called when the user hits a key.  If
you do not want an action routine called, set actionr to the value
(int (*))NULL.

Return Value:

The value passed to the action routine will be in the range 0-7 or 0-15
for defflag==0, 0-8 or 0-16 for defflag==1.  If your action routine returnes
a non-negative number, it will be returned by this menu function.
 
A value of -1 will be passed to the action routine if the user presses ESC.  If
your action routine returns this value, the user will stay in the menu.  If
there is no action routine, -1 will be returned by this function when ESC is
pressed.



                                                                        6 - 8  

                                                                        mmcolorm

See Also:

pmmenu, pmmenumu, pmlist

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
main()
{
int  kbhit(), getch();                  declare for kminit() function
int  wnum, lnum;
 
 
lminit(malloc,free,0);                  init the list manager first
kminit(kbhit,getch);                    now the keyboard manager
wninit(0,0,NULL,0,malloc,free);         do the window manager
hminit("GOODHELP.HLP",0,0,0,
       WNBLACK,WNGREEN);                init help manager
 
wnum = wncreate(0,0,80,25,WNBLUE,WNCYAN,
       WNBLUE,WNCYAN);                  create our main window
wnttitle(wnum,"**[Good Title]**");      add a top title
kmsir(KF1,hmhelp);                      make F1 activate help
hmscontext("help_label1");              set help context
    .
    .
mmcolorm("[Pick a Foreground Color","",0,0,
         WNBLACK,WNRED,WNCYAN,1,1,(int (*)()) );
 
/*
 
The above mmcolorm call will cause a menu with 17 items to be displayed.
The first item will be "Black", item 16 will be "White", and item 17 will
be the word "Default".
 
Since the colorflag is set true (1) we are asking for a foreground color.
 
The background color for each item will be Black (bc == WNBLACK).
 
The menu item that will be active on entry to the menu will be Red on Black
(fc = WNRED).
 
The last menu item, "Default", will be displayed as Cyan on Black (Defcolor =
WNCYAN).
 
There will be no action routine called.
 
*/

                                                                        6 - 9  

                                                                        mmcolorm

 
wndestroy(wnum);                        remove the window
}




















































                                                                        6 - 10 

                                                                        mmcreate

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int     mmcreate(name,mtype,row,col,width,height,abs,ttitle,btitle,
                 hdr,hsize,lf,retkeyonly,actionr,actionn);  create menu
 
char    *name;                      menu name
char    *ttitle,*btitle;            top and bottom titles
int     mtype;                      MMPOPUP, MMPULLDOWN, or MMLIGHTBAR
int     row,col;                    location of menu
int     width,height;               size of menu
int     abs;                        autosize or absolute
char    *hdr;                       user defined menu header
int     hsize;                      size of header
int     lf;                         local storage flag for hdr
int     retkeyonly;                 must hit CR to select menu item
int     (*actionr)();               menu action routine
char    *actionn;                   for V2.0 dynamic loading of menus

Description:

The mmcreate function is used to create an empty menu.  After creation and
adding menu elements via mmamel() you can process the menu using mmpromenu().
 
Name is a character string (10 chars + '\0' max) that you can optionally name
this menu with.  If you intend on using nested menus a name is needed. Otherwise
supply a zero length string.  Case is not significant but duplicate names are
not allowed.
 
Mtype is the type of menu you are creating.  The symbolic constants MMPOPUP,
MMPULLDOWN, and MMLIGHTBAR can be found in <mm.h> and used for this parameter.
 
Ttitle and btitle are character string titles which will be used if mtype is
set to MMPOPUP.  Use zero length strings if a title is not wanted.
 
The location and size of the menu is specified by row, col, width, height,
and abs.  If abs is set to MMABSDEF then width and height have no meaning.  The
menu size will be automatically sized to the elements added via mmamel() and
row/col will be interpreted to be the screen location you want the CENTER of the
menu to be placed at.  A "best" attempt to get the menu at this location will be
performed.  Row 0, col 0 is the upper left of the screen while the lower right
is determined by calls to the window manager wngsrows and wngscols functions.
Remember that all values are 0 based.  The rightmost column on a 80 column
screen is number 79.  The valid range for width and height depend on where you
put the menu.  Assuming 0,0 these are the legal sizes:
 
  Menu Type   Min Width   Min Height  Max Width  Max Height
  =========   =========   ==========  =========  ==========
  MMPOPUP        6            3       wngscols() wngsrows()

                                                                        6 - 11 

                                                                        mmcreate

  MMPULLDOWN     6            1       wngscols()     1
  MMLIGHTBAR     6            2       wngscols()     2
 
Since a pulldown menu is really just a lightbar menu which calls a popup,
the min/max height is only for the lightbar portion.
 
If you do not want a automatically sized and located menu you can supply one
or more of the following constants ORed together to pass as the abs parameter:
 
  abs constant  Description
  ============  ===========
  MMABSR        Row value is absolute upper row of where
                menu will be placed.  Col will be
                interpreted as a center coordinate.
 
  MMABSC        Col value is absolute left edge of where
                menu will be placed.  Row will be
                interpreted as center coordinate.
 
  MMABSRC       Same as  MMABSR | MMABSC.
 
  MMABSW        Width given is absolute.  Menu width
                will be this exact number of columns wide.
 
  MMABSH        Height given is absolute.  Menu height
                will be this exact number of rows high.
                Ignored for MMPULLDOWN and MMLIGHTBAR.
 
  MMABSWH       Same as MMABSW | MMABSH.
 
  MMABSRCWH     Same as MMABSRC | MMABSWH.
 
Hdr is a pointer to a block of memory you wish "tacked on" to this menu for
your own use.  Hsize is the number of bytes contained in this block.  If hsize
is 0 then hdr will be scanned using the strlen() function and the hsize
calculated for you.  Supply a value of NULL for hdr if none is desired.  Lf is
a flag which tells the Menu Manager whether or not hdr is static or auto.  A
setting of lf == 0 means hdr is static and will not go away for the lifetime
of your program.  Lf == 1 will cause the Menu Manager to allocate memory
(using the List Manager) for hdr.
 
If retkeyonly is set to true (non zero), then the only way a user can make a
menu choice is by hitting the RETURN key while a menu element is highlighted.
A false value (retkeyonly == 0) will allow the user to hit a "hot key" which
you define for each menu element and immediately cause that element to be
activated which means either calling another sub-menu or a C routine you
specify.
 
Actionr is a pointer to a function which will get called when you don't feel
like defining individual action routines sub-menus for the menu elements.  When
a user makes a menu selection the order of evaluation for "what to do next" is:
 
    - If the selected menu element has an action routine, call it.
    - Else if the selected menu element has a sub-menu call defined, call it.

                                                                        6 - 12 

                                                                        mmcreate

    - Else if the MENU has an action routine, call it.
    - Else return the menu element number that was selected.
 
If you supply a action routine pointer it will be called using this synopsis:
int (*actionr)(mnum,mel,hotkey);
int mnum;                   menu number being processed
int mel;                    menu element that was selected
int hotkey;                 0 if <CR> selected element, >0 if hotkey
 
Before your actionr routine is called, the current menu item will be
de-highlighted.  Mnum is the number of the menu that was being processed and
mel is the menu element number that was selected.  You can use the query
routines to obtain information about the menu or menu element.  A value of -1
for mel means the ESCAPE key was pressed and usually indicates (by de-facto
convention) the user wants out of the menu. When menu elements are added to a
menu they start at number 1 and are contiguous.  The user will not be allowed
to select a read-only menu element so your action routine does not have to
check for it.
 
A value of -1 returned from your actionr routine causes the user to stay in
the menu.  A 0 or greater value will cause the menu to be taken down and the
value returned to the mmpromenu() caller.  For the pull-down menu type, the top
light bar will NOT be taken down.  You must use the mmpromenu routine with the
MMDESTROY function to get rid of it.
 
Actionn is a character string name of the actionr routine specified.  For now
it should be NULL.  Later versions will use this for dynamically loading menus.
 
The include file <mm.h> declares some default actionr functions which you can
use:
 
  Actionr Constant    ESCAPE Return   Selection Return
  ================    =============   ================
  MMACTIONNULL        0               Menu Element #
  MMACTIONESCONLY     0               0
 
The default colors used when a menu is created are determined by values set via
the mmscparms() function.  If you want each of your menus to have different
colors you will have to call mmscparms() just before each of your mmcreate
calls.

Return Value:

A positive ( > 0) menu number will be returned if all went well.  A negative
value indicates one of the errors defined in <mm.h>.  A MMMTBERROR (menu too
big error) means either row, col, width, height, or a combination of these
were out of range.
 
The maximum number of times you can call mmcreate per initialization is 32767.

See Also:

mminit, mmscparms, mmamel, mmdestroy


                                                                        6 - 13 

                                                                        mmcreate

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mnum,mel;
int accrecaction();  /* routine to call when user picks an account */
char *accountname;
 
mnum = mmcreate("acctsrecv",MMPOPUP,0,0,0,0,MMABSDEF, /* autosize at middle */
                "[ Accounts Receivables ]","",NULL,0,
                0,0,accrecaction,NULL);
 
accountname = getfirstaccountname();   /* some routine you supply */
while (accountname != NULL){
   mel = mmamel(mnum,"",accountname,"","",1,0,0,MMACTIONNULL,NULL);
   if (accountoverdue(accountname))
      mmsmelmark(mnum,mel);
   /* else leave alone, default stat at mmamel time is unmarked */
   accountname = getnextaccountname();
   }
  .
  .
  .
mmdestroy(mnum);



























                                                                        6 - 14 

                                                                      mmdestroy

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmdestroy(mnum);
int   mnum;

Description:

The mmdestroy function will free all memory taken up by menu number mnum.  A
value of -1 supplied for mnum will destroy ALL menus currently known to the
Menu Manager.

Return Value:

A value of 0 indicates all went well.  A negative return means there was an
error.

See Also:

mmcreate

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mnum,mel;
int accrecaction();  /* routine to call when user picks an account */
char *accountname;
 
mnum = mmcreate("acctsrecv",MMPOPUP,0,0,0,0,MMABSDEF, /* autosize at middle */
                "[ Accounts Receivables ]","",NULL,0,
                0,0,accrecaction,NULL);
 
accountname = getfirstaccountname();   /* some routine you supply */
while (accountname != NULL){
   mel = mmamel(mnum,"",accountname,"","",1,0,0,MMACTIONNULL,NULL);
   if (accountoverdue(accountname))
      mmsmelmark(mnum,mel);
   /* else leave alone, default stat at mmamel time is unmarked */
   accountname = getnextaccountname();
   }
  .
  .
  .
mmdestroy(mnum);

                                                                        6 - 15 

                                                                      mmdestroy
























































                                                                        6 - 16 

                                                                          mmdmel

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mmdmel(mnum,mel);
int mnum;                       menu number
int mel;                        menu element to delete, -1 does all

Description:

The mmdmel routine is used to delete menu element mel of existing menu mnum.
 
After calling this function, any new menu element added to mnum will be placed
at the END of the menu.  Mel will never be available again.
 
A value of -1 supplied for mel will delete ALL menu elements of menu mnum.

Return Value:

A value of 0 is returned if all went well.  A negative value indicates either
mnum or mel is invalid.

See Also:

mmcreate, mmamel, mmsmel

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
mmdmel(mnum,-1);    that will do all of em..
















                                                                        6 - 17 

                                                                        mmgcmnum

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgcmnum()      get current menu number

Description:

The mmgcmnum function will return the menu number that is currently being
processed by the mmpromenu function.
 
A normal use for this function would be by a help routine attached to a function
key via the keyboard manager.  Your help routine could call mmgcmnum to see if
a menu is active and if so, using the returned menu number (mnum), obtain
information about the menu such as its type and explain to the user exactly how
to navigate.

Return Value:

A positive value indicates a menu is being processed.  A negative value
tells you no menu is active.

See Also:

mmgmtype, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
global_user_help()
/****************/
/*
    This could be a kind of master help giver routine that you could have
    registered as an intercept function with the keyboard manager kmsir()
    function:
                kmsir(KF1,global_user_help);
 
    Everytime the user presses F1, this routine will get called.  This of
    course assumes that you are using the keyboard manager routines for
    fetching keystrokes.
*/
{
int mnum;

                                                                        6 - 18 

                                                                        mmgcmnum

 
if ((mnum = mmgcmnum()) > 0)         /* See if user is in an active menu.. */
    switch(mmgmtype(mnum)){
        case    MMPOPUP:
                /* tell how to navigate a pop-up menu */
            break;
        case    MMPULLDOWN:
                /* tell how to navigate a pull-down menu */
            break;
        case    MMLIGHTBAR:
                /* tell how to navigate a lightbar menu */
            break;
        }
else{                                /* user some where else in your app */
    /* give other help */
    }
return(-1);     /* so keyboard manager acts like no key was pressed at all */
};





































                                                                        6 - 19 

                                                                      mmgcparms

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
void mmgcparms(bc,fc,bbc,bfc,rbc,rfc,mbc,mfc,hbc,hfc,tbc,tfc,markchar,markkey);
 
int *bc,*fc;      menu window background/foreground colors
int *bbc,*bfc;    menu window border (if any) background/foreground colors
int *rbc,*rfc;    colors for read-only menu elements
int *mbc,*mfc;    colors for mark character if menu element is marked
int *hbc,*hfc;    colors for current menu element
int *tbc,*tfc;    menu window title colors (if any)
int *markchar;    current mark character (default == '*')
int *markkey;     current mark/unmark key (default == space)

Description:

The mmgcparms function is used to obtain the default colors assigned to a menu
when it is created via mmcreate().
 
The defaults that are in effect right after mminit is called are:
 
    bc  / fc    ==  WNBLACK / WNWHITE
    bbc / bfc   ==  WNBLACK / WNWHITE
    rbc / rfc   ==  WNBLACK / WNDGRAY
    mbc / mfc   ==  WNBLACK / WNWHITE
    hbc / hfc   ==  WNGRAY  / WNWHITE
    tbc / tfc   ==  WNBLACK / WNWHITE
    markchar    ==  '*'
    markkey     ==  space

Return Value:

This function has no return value.  Make sure you supply POINTERS to the above
parameters.

See Also:

mmscparms

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int bc,fc,bbc,bfc,rbc,rfc,mbc,mfc,hbc,hfc,tbc,tfc,mc,mk;
 

                                                                        6 - 20 

                                                                      mmgcparms

mmgcparms(&bc,&fc,&bbc,&bfc,&rbc,&rfc,&mbc,&mfc,&hbc,&hfc,&tbc,&tfc,&mc,&mk);
 
mmscparms(WNRED,   WNYELLOW,         /* back/fore */
          WNRED,   WNBLACK,          /* border back/fore */
          WNRED,   WNLRED,           /* read only back/fore */
          WNBLACK, WNLCYAN,          /* mark character back/fore */
          WNBLACK, WNRED,            /* hightlight back/fore */
          WNBLACK, WNYELLOW,         /* title colors */
          ' ','\0');                /* mark character, no mark key */
 
mmwg = mmcreate("mmwg",MMPOPUP,4,4,0,0,MMABSRC,"[ Global ]","",NULL,0,0,0,nomore
/*
    now put the creation parms back..
*/
mmscparms(bc,fc,bbc,bfc,rbc,rfc,mbc,mfc,hbc,hfc,tbc,tfc,mc,mk);








































                                                                        6 - 21 

                                                                    mmgfirstmel

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgfirstmel and mmgnextmel functions are to be used in a loop combination
for traversing the items that have been added to a menu.  Mmgnextmel must be
called after mmgfirstmel and will return a negative error code if no more
elements are found in the menu.

See Also:

mmgmel, mmgnummels, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
 
/*
   mfdel.c     Menu File Delete
 

                                                                        6 - 22 

                                                                    mmgfirstmel

   A little file delete utility which will build a menu of
   files in the current directory and allow you to mark/unmark each file.
   When enter is pressed all marked files will be deleted.
 
   When the list is built, all files with a read-only attribute will show
   up on the list but will be marked read-only so the user can't do anything
   with it.
*/
 
 
 
main(argc,argv)
/*****/
int  argc;
char *argv[];
{
int code,mnum,mel,count;
struct find_t cfile;
int kbhit(),getch();
char *cfs;
 
lminit(malloc,free,0);              /* init list manager */
wninit(0,0,NULL,0,malloc,free);     /* window manager using memory */
kminit(kbhit,getch);                /* keyboard manager */
mminit(kmgetch,NULL);               /* menu manager */
 
mmscparms(BC,FC,BBC,BFC,RBC,RFC,MBC,MFC,HBC,HFC,TBC,TFC,MC,MK);
mnum = mmcreate("files",MMPOPUP,ROW,COL,WIDTH,HEIGHT,ABSATT,
                "[ Files in Current Directory ]",
                "[ Space to Mark, ESC to Abort, Enter to Delete Marked ]",NULL,0
                0,1,MMACTIONNULL,NULL);
 
count = 0;
if (argc > 1)
   cfs = argv[1];
else
   cfs = "*.*";
code = _dos_findfirst(cfs,_A_NORMAL | _A_RDONLY,&cfile);
while (code == 0){
   count++;
   mel = mmamel(mnum,"",cfile.name,"","",1,0,MMNOCASE | cfile.name[0],
                MMACTIONNULL,NULL);
   if (cfile.attrib & (_A_RDONLY | _A_HIDDEN | _A_SYSTEM |
                       _A_VOLID | _A_SUBDIR))
      mmsmelronly(mnum,mel);                    /* make read only */
   code = _dos_findnext(&cfile);
   }
 
if (count){
   code = mmpromenu(mnum,MMPROCESS,1);
   if (code != 0){                              /* user didn't ESCAPE */
      if (mmgmelstat(mnum,-1) > 0){                /* user marked files */
         mel = mmgfirstmel(mnum);
         while (mel > 0){

                                                                        6 - 23 

                                                                    mmgfirstmel

            if (mmgmelstat(mnum,mel)){
               if (unlink(mmgmelmdata(mnum,mel))){      /* delete file */
                  printf("\nError deleting file [%s].",mmgmelmdata(mnum,mel));
                  }
               }
            mel = mmgnextmel(mnum);
            }
         }
      }
   }
else{
   printf("\nNo files matching [%s]",cfs);
   }
mmdestroy(mnum);
exit(0);
}







































                                                                        6 - 24 

                                                                      mmgmbtitle

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmbtitle function will return a pointer to the current bottom title of
menu mnum.  The titles can be set to something other than the current value by
using the mmsmnum() routine.

See Also:

mmgmname, mmgmnum, mmgmtype, mmgmrow, mmgmcol, mmgmwidth, mmgmheight

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
char *cp;
 
cp = mmgmbtitle(mnum);







                                                                        6 - 25 

                                                                        mmgmcol

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmrow and mmgmcol functions return the current upper left corner position
of menu mnum.  A negative return means mnum is invalid.  If the menu was create
with abs set to true, these values will be the same as you supplied.  However,
if the menu is automatically being sized (with each call to mmamel) then these
position coordinates will change as you add menu elements.

See Also:

mmgmname, mmgmnum, mmgmtype, mmgmrow, mmgmwidth, mmgmheight, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
my_delete_files_menu_action_routine(mnum,mel)
/*******************************************/
int mnum,mel;
/*
    assume you have built a pop-up menu that has as one of its items:
 
        "Delete all files on hard disk C:"

                                                                        6 - 26 

                                                                        mmgmcol

 
and you of course want to ask the user if this is all right.  Let's put up
a pretty hot-red window exactly over the menu he/she just selected from and
ask if it's ok.
*/
{
int  r,c,w,h;
int  wnum;
char yesno;
 
r = mmgmrow(mnum);
c = mmgmcol(mnum);      /* gets the upper window corners */
w = mmgmwidth(mnum);
h = mmgmheight(mnum);   /* gets the total window size of the menu */
 
wnum = wncreate(r,c,w,c,WNRED,WNWHITE,WNRED,WNWHITE);   /* build window */
wnprintf(wnum,"Are you sure? (Y/<N>) ");
yesno = 'N';
wninput(wnum,WNCHAR | WNDISPLAY, 0,0,&yesno,"yYnN");    /* ask user if ok */
if ((yesno == 'y') || (yesno == 'Y')){
    /*
        do the unspeakable act....
    */
    }
else{
    /*  tell user he/she made a wise choice.. */
    }
wndestroy(wnum);
return(-1);             /* keep user locked in menu */
};

























                                                                        6 - 27 

                                                                          mmgmel

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmel function will return a menu element if the name of the element is
known.  A negative return indicates name could not be found or mnum is invalid.

See Also:

mmgnummels, mmgfirstmel, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mnum,mel;
int accrecaction();  /* routine to call when user picks an account */
char *accountname;
 
mnum = mmcreate("acctsrecv",MMPOPUP,0,0,0,0,0,        /* autosize at middle */
                "[ Accounts Receivables ]","",NULL,0,

                                                                        6 - 28 

                                                                          mmgmel

                0,0,accrecaction,NULL);
 
accountname = getfirstaccountname();   /* some routine you supply */
while (accountname != NULL){
   mel = mmamel(mnum,"",accountname,"","",1,0,0,MMACTIONNULL,NULL);
   if (accountoverdue(accountname))
      mmsmelmark(mnum,mel);
   /* else leave alone, default stat at mmamel time is unmarked */
   accountname = getnextaccountname();
   }
   .
   .
   .
accrecaction(mnum,mel)
/********************/
/*
   This action routine would be called when the user picks a menu element
   in the above menu or presses ESCAPE.
*/
if (mel < 0)   /* user pressed ESCAPE */
   return(0);
else{
   processaccount(mmgmelname(mnum,mel));
   if (!accountoverdue(accountname))
      mmsmelunmark(mnum,mel);
      /* when user is put back in menu, the mark character will be gone. */
   return(-1);    /* this will keep user in accounts receivable menu */
   }



























                                                                        6 - 29 

                                                                    mmgmelhotkey

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmelhotkey function will return the hotkey currently defined for mel.  A
negative value indicates an invalid mnum or mel.  Zero indicates there is no
hotkey defined while a positive value means there is.

See Also:

mmgmel, mmgnummels, mmgfirstmel, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
showhotkeys(mnum)
/*
   This little routine will build a list of hotkeys that each item in
   mnum has.
*/

                                                                        6 - 30 

                                                                    mmgmelhotkey

int mnum;
{
int localmnum,mel;
char buf[80];
 
sprintf(buf,"[ Hot-Keys Defined for menu %s ]",mmgmname(mnum));
localmnum = mmcreate("",MMPOPUP,0,0,80,10,MMABSWH, /* absolute width/height */
                buf,"",NULL,0,0,0,MMACTIONNULL,NULL);
 
mel = mmgfirstmel(mnum);
while (mel > 0){
   hotkey = mmgmelhotkey(mnum,mel);
   if (hotkey > 0)
      sprintf(buf,"Hotkey == %5d",hotkey);
   else
      sprintf(buf,"No Hotkey defined.");
   mmamel(localmnum,"",buf,"","",1,0,0,MMACTIONNULL,NULL);
   mel = mmgnextmel(mnum);
   }
 
mmsmelronly(localmnum,-1);       /* make all elements read only for listing */
mmpromenu(localmnum,MMPROCESS,1);/* show the list */
mmdestroy(localmnum);
}































                                                                        6 - 31 

                                                                    mmgmelmcall

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmelmcall function will return the name of the menu to be called when this
menu item is selected.  A NULL value indicates an invalid mnum or mel.  A zero
length string is returned if this element doesn't call a menu when selected.
Don't modify this string.

See Also:

mmgmel, mmgnummels, mmgfirstmel, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
showcalls(mnum)
/*
   This little routine will build a list of sub-menus that each item in
   mnum calls

                                                                        6 - 32 

                                                                    mmgmelmcall

*/
int mnum;
{
int localmnum,mel;
char buf[80];
char *cp,*mcall;
 
sprintf(buf,"[ Sub-Menus called by menu %s ]",mmgmname(mnum));
localmnum = mmcreate("",MMPOPUP,0,0,80,10,MMABSWH, /* absolute width/height */
                buf,"",NULL,0,0,0,MMACTIONNULL,NULL);
 
mel = mmgfirstmel(mnum);
while (mel > 0){
   mcall = mmgmelmcall(mnum,mel);
   if (strlen(mcall) > 0)
      cp = mcall;
   else
      cp = "No Sub-Menu Defined";
   mmamel(localmnum,"",cp,"","",1,0,0,MMACTIONNULL,NULL);
   mel = mmgnextmel(mnum);
   }
 
mmsmelronly(localmnum,-1);       /* make all elements read only for listing */
mmpromenu(localmnum,MMPROCESS,1);/* show the list */
mmdestroy(localmnum);
};





























                                                                        6 - 33 

                                                                    mmgmelmdata

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmelmdata function will return a pointer to the menu element data that
is displayed when the menu is displayed.  A NULL value is returned if mnum or
mel is invalid.  Don't modify this string.

See Also:

mmgmel, mmgnummels, mmgfirstmel, mmgnextmel, mmgmelname
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mnum,mel;
int subcreate();
int subdelete();
int submodify();
 

                                                                        6 - 34 

                                                                    mmgmelmdata

mnum = mmcreate("main",MMPOPUP,0,0,0,0,0,        /* autosize at middle */
                "[ Account Actions ]","",NULL,0,
                0,0,MMACTIONNULL,NULL);
mmamel(mnum,"","Create an Account","","",0,0,0,subcreate,NULL);
mmamel(mnum,"","Delete an Account","","",0,0,0,subcreate,NULL);
mmamel(mnum,"","Modify an Account","","",0,0,0,subcreate,NULL);
mmpromenu(mnum,MMPROCESS,1);
   .
   .
   .
 
subcreate(mnum,mel)
/*****************/
/*
   this routine will be called when the user picks item 1 above.
*/
int mnum,mel;
{
/*
   now at this point we would probably put up a window or another window
   with a title.  The title could be the same as the element the user
   just picked so that he/she is constantly aware of where he/she is in
   your program.
*/
int wnum;
 
wnum = wncreate(0,0,80,25,WNBLACK,WNWHITE,WNBLACK,WNWHITE);
wnttitle(wnum,mmgmelmdata(mnum,mel));
   .
   .
   .
























                                                                        6 - 35 

                                                                    mmgmelmdesc

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmelmdesc function will return a pointer to the menu element description
string that is used if the menu is a LIGHTBAR type.  A NULL value is returned if
mnum or mel is invalid.  A zero length string is returned if mel has no
description.  Don't modify this string.

See Also:

mmgmel, mmgnummels, mmgfirstmel, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmcall, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
similar to mmgmelmdata().




                                                                        6 - 36 

                                                                      mmgmelname

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmelname function will return a pointer to a menu element name if the
mel number is known.  NULL is returned if mnum or mel is invalid.  A zero lengt
string is returned if mel has no name.  Don't modify this string.

See Also:

mmgmel, mmgnummels, mmgfirstmel, mmgnextmel, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mnum,mel;
int accrecaction();  /* routine to call when user picks an account */
char *accountname;
 
mnum = mmcreate("acctsrecv",MMPOPUP,0,0,0,0,0,        /* autosize at middle */

                                                                        6 - 37 

                                                                      mmgmelname

                "[ Accounts Receivables ]","",NULL,0,
                0,0,accrecaction,NULL);
 
accountname = getfirstaccountname();   /* some routine you supply */
while (accountname != NULL){
   mel = mmamel(mnum,"",accountname,"","",1,0,0,MMACTIONNULL,NULL);
   if (accountoverdue(accountname))
      mmsmelmark(mnum,mel);
   /* else leave alone, default stat at mmamel time is unmarked */
   accountname = getnextaccountname();
   }
   .
   .
   .
accrecaction(mnum,mel)
/********************/
/*
   This action routine would be called when the user picks a menu element
   in the above menu or presses ESCAPE.
*/
if (mel < 0)   /* user pressed ESCAPE */
   return(0);
else{
   processaccount(mmgmelname(mnum,mel));
   if (!accountoverdue(accountname))
      mmsmelunmark(mnum,mel);
      /* when user is put back in menu, the mark character will be gone. */
   return(-1);    /* this will keep user in accounts receivable menu */
   }


























                                                                        6 - 38 

                                                                    mmgmelronly

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmelronly function will return the read-only status of mel.  A negative
value indicates an invalid mnum or mel.  A zero return means mel is selectable
while a positive value means mel is read-only.
 
A -1 supplied for mel will return a composite value of all the menu elements
in mnum.  A zero return means all elements are selectable.  A positive value
will tell you how many items are read-only.

See Also:

mmgmel, mmgnummels, mmgfirstmel, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
showcalls(mnum)

                                                                        6 - 39 

                                                                    mmgmelronly

/*
   This little routine will build a list which shows the readonly status of
   each item in mnum.
*/
int mnum;
{
int localmnum,mel;
char buf[80];
char *cp;
 
sprintf(buf,"[ Element Read-only Status for menu %s ]",mmgmname(mnum));
localmnum = mmcreate("",MMPOPUP,0,0,80,10,MMABSWH, /* absolute width/height */
                buf,"",NULL,0,0,0,MMACTIONNULL,NULL);
 
mel = mmgfirstmel(mnum);
while (mel > 0){
   if (mmgmelronly(mnum,mel) > 0)
      cp = "Read-Only";
   else
      cp = "Non Read-Only";
   mmamel(localmnum,"",cp,"","",1,0,0,MMACTIONNULL,NULL);
   mel = mmgnextmel(mnum);
   }
 
mmsmelronly(localmnum,-1);       /* make all elements read only for listing */
mmpromenu(localmnum,MMPROCESS,1);/* show the list */
mmdestroy(localmnum);
};



























                                                                        6 - 40 

                                                                      mmgmelstat

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgmelstat function will return the "mark" status of mel.  A negative value
indicates an invalid mnum or mel.  A zero return means mel is not marked while
a positive value indicates mel is marked.
 
A -1 supplied for mel will return a composite value of all the menu elements
in mnum.  A zero return means all elements are unmarked.  A positive value
will tell you how many items are marked.

See Also:

mmgmel, mmgnummels, mmgfirstmel, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelronly

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
See mmgfirstmel().

                                                                        6 - 41 

                                                                      mmgmelstat
























































                                                                        6 - 42 

                                                                      mmgmheader

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmheader function will return a character pointer to the header that was
"tacked on" to menu mnum in the mmcreate call.  A NULL pointer is returned if
no header is found.  You can look at this data and even change the contents of
it, but don't make it bigger.  You'll overwrite something.

See Also:

mmgmname, mmgmnum, mmgmtype, mmgmrow, mmgmcol, mmgmwidth, mmgmheight

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
/*
    Let's create a menu with 3 items on it and along with it, a structure that
    allows us to keep track of how many times each item is selected.
*/
struct file_track_s{
    char *filename;
    int  viewcount;
    int  editcount;

                                                                        6 - 43 

                                                                      mmgmheader

    int  printcount;
    };
 
do_something_to_a_file(filename,ft)
/*********************************/
char *filename;
struct file_track_s *ft;
{
 
int fileaction;          /* what our sub-menu is going to call */
int mnum;
 
mnum = mmcreate("fileops",MMPOPUP,0,0,0,0,0,    /* autosize at middle */
                "[ File Operations ]","",(char *)ft,sizeof(struct keep_track_s),
                0,0,fileaction,NULL);
 
mmamel(mnum,"fovf","View  This File","","",0,0,0,MMACTIONNULL,NULL);
mmamel(mnum,"foef","Edit  This File","","",0,0,0,MMACTIONNULL,NULL);
mmamel(mnum,"fopf","Print This File","","",0,0,0,MMACTIONNULL,NULL);
mmpromenu(mnum,MMPROCESS,2);                            /* start at "edit" */
/*
    now, when user makes a selection, fileaction() will be called.
*/
mmdestroy(mnum);    /* get rid of this temp menu */
};
    .
    .
    .
fileaction(mnum,mel)
/******************/
int mnum,mel;
{
struct file_track_s *ft;
 
if (mel == -1)  /* user wants out of file operations menu */
    return(0);  /* this will cause the mmpromenu() call above to finish */
 
ft = (struct file_track_s *)mmgmheader(mnum);   /* get the header info */
/*
    if you never intend to change the order of your menu elements, you could
    just do a switch() on the mel number.  By defining element names before
    you code and then using those names, you can change the order of your
    items and not have to change the action routines.
*/
if (strcmp(mmgmelname(mnum,mel),"fovf") == 0){
    /* do the stuff to view the file  ft->filename */
    ft->viewcount++;   /* we can change data, just don't make header bigger */
    }
else if (strcmp(mmgmelname(mnum,mel),"foef") == 0){
    /* do the edit stuff for ft->filename */
    ft->editcount++;
    }
else if (strcmp(mmgmelname(mnum,mel),"fopf") == 0){
    /* do the print stuff for ft->filename */

                                                                        6 - 44 

                                                                      mmgmheader

    ft->printcount++;
    }
else{
    /*  you have an internal bug. */
    }
return(-1);     /* this will keep user locked in file operations menu */
};
















































                                                                        6 - 45 

                                                                      mmgmheight

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmwidth and mmgmheight functions return the current size of menu mnum.  A
negative return indicates mnum is invalid.  If you created the menu with abs set
to true, these values will be the same as you supplied.  However, if the menu is
automatically being sized (with each call to mmamel) then these values will
change as you add menu elements.

See Also:

mmgmname, mmgmnum, mmgmtype, mmgmrow, mmgmcol, mmgmwidth, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
my_delete_files_menu_action_routine(mnum,mel)
/*******************************************/
int mnum,mel;
/*
    assume you have built a pop-up menu that has as one of its items:
 
        "Delete all files on hard disk C:"

                                                                        6 - 46 

                                                                      mmgmheight

 
and you of course want to ask the user if this is all right.  Let's put up
a pretty hot-red window exactly over the menu he/she just selected from and
ask if it's ok.
*/
{
int  r,c,w,h;
int  wnum;
char yesno;
 
r = mmgmrow(mnum);
c = mmgmcol(mnum);      /* gets the upper window corners */
w = mmgmwidth(mnum);
h = mmgmheight(mnum);   /* gets the total window size of the menu */
 
wnum = wncreate(r,c,w,c,WNRED,WNWHITE,WNRED,WNWHITE);   /* build window */
wnprintf(wnum,"Are you sure? (Y/<N>) ");
yesno = 'N';
wninput(wnum,WNCHAR | WNDISPLAY, 0,0,&yesno,"yYnN");    /* ask user if ok */
if ((yesno == 'y') || (yesno == 'Y')){
    /*
        do the unspeakable act....
    */
    }
else{
    /*  tell user he/she made a wise choice.. */
    }
wndestroy(wnum);
return(-1);             /* keep user locked in menu */
};

























                                                                        6 - 47 

                                                                        mmgmname

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);       get mnum from name
char    *mmgmname(mnum);      get name from mnum
int     mmgmtype(mnum);       get type of menu mnum
int     mmgmrow(mnum);        get upper left corner row of menu mnum
int     mmgmcol(mnum);        get upper left corner column of menu mnum
int     mmgmwidth(mnum);      get width of menu mnum
int     mmgmheight(mnum);     get height of menu mnum
char    *mmgmheader(mnum);    get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmname function will return a character pointer to the name of menu mnum.
A value of NULL is returned if mnum does not exist.  A zero length string will
be returned if mnum exist but no name was specified.  You are on your own if
you attempt to use this pointer to change the menu name.

See Also:

mmgmnum, mmgmtype, mmgmrow, mmgmcol, mmgmwidth, mmgmheight, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
show_current_menu_names()
/***********************/
{
int i;
int dmnum;
char *mname;
char buf[80];
/*

                                                                        6 - 48 

                                                                        mmgmname

    this little routine will build a menu and add read only items to it.  The
    items will be all names of menus so far defined to the menu manager.
*/
dmnum = mmcreate("$$%%$$",MMPOPUP,0,0,0,0,0,
                 "[ Menus defined ]","",NULL,0,0,0,MMACTIONNULL,NULL);
 
i = 1;
while ((mname = mmgmname(i)) != NULL){
    if (strcmp(mname,"$$%%$$") != 0){    /* don't show this menu */
        if (*mname == 0)
            sprintf(buf,"%-5d  %s,i,"No Name");
        else
            sprintf(buf,"%-5d  %s",i,mname);
        mmamel(dmnum,"",buf,"","",1,1,   /* last 1 set ronly bit */
               0,MMACTIONNULL,NULL);
        }
    i++;
    }
if (i > 1){                     /* menus found, i++ was hit at least once.. */
mmpromenu(dmnum,MMPROCESS,0);   /* show list to user, ESC will get him out */
mmdestroy(dmnum);               /* free up the memory */
};

































                                                                        6 - 49 

                                                                        mmgmnum

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmnum function will return the mnum of the menu with name mname.  A case
insensitive search is performed when looking for mname.  A MMBADMNUM error is
returned if mname can't be found.

See Also:

mmgmname, mmgmtype, mmgmrow, mmgmcol, mmgmwidth, mmgmheight, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
list_a_menu(menuname)
/*******************/
char *menuname;
{
int mnum;
 
if ((mnum = mmgmnum(menuname)) < 0)
    return(-1);                     /* could not find menuname */
 
mmsmelronly(mnum, -1);              /* set all elements read only */
mmpromenu(mnum,MMPROCESS,0);        /* let user look but don't touch */

                                                                        6 - 50 

                                                                        mmgmnum

/*
    because all of the menu elements were made "read only", the only action
    routine that would ever get called would be the one defined for the menu,
    not any of the elements because it's impossible for a read only element
    to be selected.  Also, the only thing that would get passed to the menu
    action routine would be a -1 indicating the user hit ESCAPE which is the
    only way to get out of browsing a menu of read only elements.  Of course
    by using the Keyboard Manager's intercept facility you have total control
    over what gets called when keys get pushed.
*/
mmsmelnonronly(mnum,-1);            /* make em all selectable again */
return(0);
}










































                                                                        6 - 51 

                                                                        mmgmrow

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmrow and mmgmcol functions return the current upper left corner position
of menu mnum.  A negative return means mnum is invalid.  If the menu was create
with abs set to true, these values will be the same as you supplied.  However,
if the menu is automatically being sized (with each call to mmamel) then these
position coordinates will change as you add menu elements.

See Also:

mmgmname, mmgmnum, mmgmtype, mmgmcol, mmgmwidth, mmgmheight, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
my_delete_files_menu_action_routine(mnum,mel)
/*******************************************/
int mnum,mel;
/*
    assume you have built a pop-up menu that has as one of its items:
 
        "Delete all files on hard disk C:"

                                                                        6 - 52 

                                                                        mmgmrow

 
and you of course want to ask the user if this is all right.  Let's put up
a pretty hot-red window exactly over the menu he/she just selected from and
ask if it's ok.
*/
{
int  r,c,w,h;
int  wnum;
char yesno;
 
r = mmgmrow(mnum);
c = mmgmcol(mnum);      /* gets the upper window corners */
w = mmgmwidth(mnum);
h = mmgmheight(mnum);   /* gets the total window size of the menu */
 
wnum = wncreate(r,c,w,c,WNRED,WNWHITE,WNRED,WNWHITE);   /* build window */
wnprintf(wnum,"Are you sure? (Y/<N>) ");
yesno = 'N';
wninput(wnum,WNCHAR | WNDISPLAY, 0,0,&yesno,"yYnN");    /* ask user if ok */
if ((yesno == 'y') || (yesno == 'Y')){
    /*
        do the unspeakable act....
    */
    }
else{
    /*  tell user he/she made a wise choice.. */
    }
wndestroy(wnum);
return(-1);             /* keep user locked in menu */
};

























                                                                        6 - 53 

                                                                      mmgmttitle

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmttitle function will return a pointer to the current top title of menu
mnum.  The titles can be set to something other than the current value by using
the mmsmnum() routine.

See Also:

mmgmname, mmgmnum, mmgmtype, mmgmrow, mmgmcol, mmgmwidth, mmgmheight

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
char *cp;
 
cp = mmgmttitle(mnum);







                                                                        6 - 54 

                                                                        mmgmtype

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmtype function will return a negative value if mnum is invalid, otherwis
one of the constants MMPOPUP, MMPULLDOWN, or MMLIGHTBAR will be returned.

See Also:

mmgmname, mmgmnum, mmgmrow, mmgmcol, mmgmwidth, mmgmheight, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
global_user_help()
/****************/
/*
    This could be a kind of master help giver routine that you could have
    registered as an intercept function with the keyboard manager kmsir()
    function:
                kmsir(KF1,global_user_help);
 
    Everytime the user presses F1, this routine will get called.  This of
    course assumes that you are using the keyboard manager routines for

                                                                        6 - 55 

                                                                        mmgmtype

    fetching keystrokes.
*/
{
int mnum;
 
if ((mnum = mmgcmnum()) > 0)         /* See if user is in an active menu.. */
    switch(mmgmtype(mnum)){
        case    MMPOPUP:
                /* tell how to navigate a pop-up menu */
            break;
        case    MMPULLDOWN:
                /* tell how to navigate a pull-down menu */
            break;
        case    MMLIGHTBAR:
                /* tell how to navigate a lightbar menu */
            break;
        }
else{                                /* user some where else in your app */
    /* give other help */
    }
return(-1);     /* so keyboard manager acts like no key was pressed at all */
};

































                                                                        6 - 56 

                                                                      mmgmwidth

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int     mmgmnum(mname);             get mnum from name
char    *mmgmname(mnum);            get name from mnum
int     mmgmtype(mnum);             get type of menu mnum
int     mmgmrow(mnum);              get upper left corner row of menu mnum
int     mmgmcol(mnum);              get upper left corner column of menu mnum
int     mmgmwidth(mnum);            get width of menu mnum
int     mmgmheight(mnum);           get height of menu mnum
char    *mmgmheader(mnum);          get ptr to header stored when menu created
char    *mmgmttitle(mnum);          get top title of menu mnum
char    *mmgmbtitle(mnum);          get bottom title of menu mnum

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu either by supplying its name (mname) or
number (mnum).

Return Value:

The mmgmwidth and mmgmheight functions return the current size of menu mnum.  A
negative return indicates mnum is invalid.  If you created the menu with abs set
to true, these values will be the same as you supplied.  However, if the menu is
automatically being sized (with each call to mmamel) then these values will
change as you add menu elements.

See Also:

mmgmname, mmgmnum, mmgmtype, mmgmrow, mmgmcol, mmgmheight, mmgmheader

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
my_delete_files_menu_action_routine(mnum,mel)
/*******************************************/
int mnum,mel;
/*
    assume you have built a pop-up menu that has as one of its items:
 
        "Delete all files on hard disk C:"

                                                                        6 - 57 

                                                                      mmgmwidth

 
and you of course want to ask the user if this is all right.  Let's put up
a pretty hot-red window exactly over the menu he/she just selected from and
ask if it's ok.
*/
{
int  r,c,w,h;
int  wnum;
char yesno;
 
r = mmgmrow(mnum);
c = mmgmcol(mnum);      /* gets the upper window corners */
w = mmgmwidth(mnum);
h = mmgmheight(mnum);   /* gets the total window size of the menu */
 
wnum = wncreate(r,c,w,c,WNRED,WNWHITE,WNRED,WNWHITE);   /* build window */
wnprintf(wnum,"Are you sure? (Y/<N>) ");
yesno = 'N';
wninput(wnum,WNCHAR | WNDISPLAY, 0,0,&yesno,"yYnN");    /* ask user if ok */
if ((yesno == 'y') || (yesno == 'Y')){
    /*
        do the unspeakable act....
    */
    }
else{
    /*  tell user he/she made a wise choice.. */
    }
wndestroy(wnum);
return(-1);             /* keep user locked in menu */
};

























                                                                        6 - 58 

                                                                      mmgnextmel

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgfirstmel and mmgnextmel functions are to be used in a loop combination
for traversing the items that have been added to a menu.  Mmgnextmel must be
called after mmgfirstmel and will return a negative error code if no more
elements are found in the menu.

See Also:

mmgmel, mmgnummels, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
see mmgfirstmel() example.




                                                                        6 - 59 

                                                                      mmgnummels

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mmgmel(mnum,name)               get mel if name known
int   mmgnummels(mnum)                get number of menu elements
int   mmgfirstmel(mnum)               get 1st mel of mnum
int   mmgnextmel(mnum)                get next mel
char  *mmgmelname(mnum,mel)           get name if mel known
char  *mmgmelmdata(mnum,mel)          get menu string of mel
char  *mmgmelmdesc(mnum,mel)          get description (if any)
char  *mmgmelmcall(mnum,mel)          get sub-menu to call (if any)
int   mmgmelhotkey(mnum,mel)          get mel hotkey (if any)
int   mmgmelronly(mnum,mel)           get readonly stat (-1 OR's all)
int   mmgmelstat(mnum,mel);           get mark stat (-1 OR's all)
 
int   mnum;                           menu number
int   mel;                            menu element
char  *name;                          menu element name

Description:

The functions listed in the summary above are available for obtaining
information about an existing menu element either by supplying its name (name)
or number (mel).

Return Value:

The mmgnummels function will return the total number of menu elements defined
for mnum.  If elements have not been deleted via mmdmel() you will be able to
use this value in a for(...) loop to traverse the menu items, otherwise you
need to use mmgfirstmel() and mmgnextmel().

See Also:

mmgmel, mmgfirstmel, mmgnextmel, mmgmelname, mmgmelmdata
mmgmelmdesc, mmgmelmcall, mmgmelhotkey, mmgmelronly, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
 
/*
   mfdel.c     Menu File Delete
 

                                                                        6 - 60 

                                                                      mmgnummels

   A little file delete utility which will build a menu of
   files in the current directory and allow you to mark/unmark each file.
   When enter is pressed all marked files will be deleted.
 
   When the list is built, all files with a read-only attribute will show
   up on the list but will be marked read-only so the user can't do anything
   with it.
*/
 
 
 
main(argc,argv)
/*****/
int  argc;
char *argv[];
{
int code,mnum,mel,count;
struct find_t cfile;
int kbhit(),getch();
char *cfs;
 
lminit(malloc,free,0);              /* init list manager */
wninit(0,0,NULL,0,malloc,free);     /* window manager using memory */
kminit(kbhit,getch);                /* keyboard manager */
mminit(kmgetch,NULL);               /* menu manager */
 
mmscparms(BC,FC,BBC,BFC,RBC,RFC,MBC,MFC,HBC,HFC,TBC,TFC,MC,MK);
mnum = mmcreate("files",MMPOPUP,ROW,COL,WIDTH,HEIGHT,ABSATT,
                "[ Files in Current Directory ]",
                "[ Space to Mark, ESC to Abort, Enter to Delete Marked ]",NULL,0
                0,1,MMACTIONNULL,NULL);
 
count = 0;
if (argc > 1)
   cfs = argv[1];
else
   cfs = "*.*";
code = _dos_findfirst(cfs,_A_NORMAL | _A_RDONLY,&cfile);
while (code == 0){
   count++;
   mel = mmamel(mnum,"",cfile.name,"","",1,0,MMNOCASE | cfile.name[0],
                MMACTIONNULL,NULL);
   if (cfile.attrib & (_A_RDONLY | _A_HIDDEN | _A_SYSTEM |
                       _A_VOLID | _A_SUBDIR))
      mmsmelronly(mnum,mel);                    /* make read only */
   code = _dos_findnext(&cfile);
   }
 
if (count){
   code = mmpromenu(mnum,MMPROCESS,1);
   if (code != 0){                              /* user didn't ESCAPE */
      if (mmgmelstat(mnum,-1) > 0){                /* user marked files */
         for (mel = mmgnummels(mnum); mel > 0; mel--){
            if (mmgmelstat(mnum,mel)){

                                                                        6 - 61 

                                                                      mmgnummels

               if (unlink(mmgmelmdata(mnum,mel))){      /* delete file */
                  printf("\nError deleting file [%s].",mmgmelmdata(mnum,mel));
                  }
               }
            }
         }
      }
   }
else{
   printf("\nNo files matching [%s]",cfs);
   }
mmdestroy(mnum);
exit(0);
}









































                                                                        6 - 62 

                                                                          mminit

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int   mminit(mgetch,dynaloadfile);    init menu manager
int   (*mgetch)();                    function to call for keycodes
char  *dynaloadfile;                  supply NULL, not implemented in V1.1

Description:

The mminit function initializes the HIM Menu Manager and must be called before
any other Menu Manager functions and AFTER lminit and wninit.
 
Mgetch is a pointer to the function the Menu Manager will call when it needs
keyboard input.  The type of values expected are of the same format as supplied
by the HIM Keyboard Manager.  If you supply your own mgetch routine, make sure
that double keycode values as returned from the BIOS are converted to a single
integer in the range 300 - 4xx as explained in the Keyboard Manager chapter.
 
Dynaloadfile is for future support of menu loading from a menu definition file
at runtime.  Until written otherwise, supply a value of NULL for dynaloadfile.

Return Value:

A value of 0 is returned if all went well.  A negative value indicates an error.
The symbolic error constants can be found in <mm.h>.
 
A non NULL dynaloadfile value will return an error.
 
Since this module uses the HIM List Manager and Window Manager, they must be
initialized first or mminit will give you an error return value.

See Also:

lminit, wninit, mmcreate, mmamel

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int kbhit(),getch();                  for keyboard manager init
 
lminit(malloc,free,0);                init list manager first thing
wninit(0,0,NULL,0,malloc,free);       init window manager
kminit(kbhit,getch);                  since we'll use kmgetch in mminit call
                                      we need to init keyboard manager here

                                                                        6 - 63 

                                                                          mminit

 
mminit(kmgetch,NULL);                 use keyboard manager to get keycodes





















































                                                                        6 - 64 

                                                                      mmpromenu

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int     mmpromenu(mnum,func,mel);
int     mnum;                       menu number to process
int     func;                       function to perform on menu
int     mel;                        1st menu element to highlight

Description:

The mmpromenu function is used to instruct the Menu Manager that you wish
to perform a function func on menu number mnum.  The current functions
available are:
 
    Func Value      Description
    ==========      ===========
    MMDISPLAY       Display primary portion of menu and return.
    MMDESTROY       Take down any part of menu that is being displayed.
    MMPROCESS       Display menu and interact with user.  Use mel as start.
 
The MMDISPLAY func is mainly for use when you want the pull-down bar of a
pull-down menu to be visible before the user has any interaction with the
menu.  Unlike all of the other menus, the pull-down does not take down the
pull-down bar when it returns from this function.
 
The MMDESTROY func will take down the display put up by a MMDISPLAY call.
 
The MMPROCESS func is what you use to actually allow the Menu Manager to
interact with the user.  If the menu is not currently displayed it will be
put on-screen with menu element mel being the current highlighted item.  A
value of 0 for mel will cause the last item for mnum that was current to be
used.  A brand new menu has item 1 as its current element.  If mel is a menu
element that is read-only then the next element that is not marked read-
only will be used.  If all elements are read-only, the user will not be
allowed to make a menu selection. When the user make a menu selection or
presses ESCAPE, one of three things can happen depending on whether the menu
has a global action routine, the menu element chosen has an action routine,
or the menu element chosen had a sub menu defined.
 
If the keycode entered was ESCAPE:
 
     The global action routine defined for the menu will be called.  If this
     routine returns -1 the user will stay locked in the menu.  Any other
     value will cause the menu to be taken down and the action return value
     is what mmpromenu() will return.  If no action routine is defined, 0
     will be returned from this routine.
 
If a menu selection was made.  Evaluated in order given:
 

                                                                        6 - 65 

                                                                      mmpromenu

    1. Menu item had action routine specified:
 
        The action routine defined for the menu element will be called.  If
    this routine returns a -1 the user will stay locked in the menu.  Any other
    value will cause the menu to be taken down and the action return value
    is what mmpromenu() will return.
 
    2. Menu item had sub-menu defined:
 
        The mmpromenu() function will be called with func equal to MMPROCESS
    and mel set to 0.  This will cause the last item that was current for
    menu mnum to be highlighted.  The return value from this recursive call
    to mmpromenu will be used a little differently than an action routine
    return value.
 
    - A negative value will cause the current menu to be taken down and the
    negative value returned to the caller of mmpromenu.  If you have several
    levels of menus, each linked together by sub-menu definitions, an error
    at any level will cause an immediate return to the top most mmpromenu
    call.
 
    - A value of 0 or greater will cause the user to be locked in this current
    menu.  In order to then get out of this menu, the user will have to press
    ESCAPE.  So, when you link menus together, the only way the user can
    "bubble back" through the menus is by repeatedly hitting ESCAPE.
 
    3. Menu had action routine specified:
 
        The action routine defined for the menu will be called.  If this
    routine returns a -1 the user will stay locked in the menu.  Any other
    value will cause the menu to be taken down and the action return value
    is what mmpromenu() will return.
 
 
    4. No sub-menu or action routines defined:
 
        The menu element number (mel) will be returned after the menu is taken
    down.

Return Value:

A negative integer indicates an error, which can be found in <mm.h>.  See the
discussion above for other possible return values.  A value of MMPORERROR will
be returned if there are no menu items yet defined for the menu mnum.

See Also:

mmcreate, mmael

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";

                                                                        6 - 66 

                                                                      mmpromenu

#include   "wn.h";
#include   "mm.h";
 
/*
    this code stub is part of mmdemo3.c
*/
    .
    .
if (buildmenus() ||
    buildintercepts() ||
    explain()){
   fprintf(stderr,"\nMMDEMO3 -- Error creating menus.  Check memory.");
   }
else{
   mmpromenu(mm,MMDISPLAY,1);   /* display pulldown part of menu */
   while (kmgetch() != KESC)    /* let intercept processor handle menu when */
       ;                        /* hotkey or / is typed */
   }
mmdestroy(-1);
wndestroy(-1);
exit(0);
}
 
menuhandler(keycode)
/******************/
/*
    this routine will get called by the Keyboard Manager everytime one of the
    keys in buildintercepts() is pressed by the user.
*/
int keycode;    /* supplied by Keyboard manager */
{
static int active = 0;
int startel,code,rval;
 
rval = keycode;
if (!active){
    active = 1;
    switch(keycode){
        case    '/':    startel = 0;    break;  /* use last current item */
        case    KAW:    startel = mmgmel(mm,"worksheet");   break;
        case    KAR:    startel = mmgmel(mm,"range");       break;
        case    KAC:    startel = mmgmel(mm,"copy");        break;
        case    KAM:    startel = mmgmel(mm,"move");        break;
        case    KAF:    startel = mmgmel(mm,"file");        break;
        case    KAP:    startel = mmgmel(mm,"print");       break;
        case    KAG:    startel = mmgmel(mm,"graph");       break;
        case    KAD:    startel = mmgmel(mm,"data");        break;
        case    KAS:    startel = mmgmel(mm,"system");      break;
        case    KAQ:    startel = mmgmel(mm,"quit");        break;
        }
    /*
        process the menu.  let all of the action be handled by the action
        routines defined for the menus and menu elements.
    */

                                                                        6 - 67 

                                                                      mmpromenu

    code = mmpromenu(mm,MMPROCESS,startel);
    active = 0;
    rval = -1;         /* pretend like key never hit.. */
    }
return(rval);
};

















































                                                                        6 - 68 

                                                                      mmscparms

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
void mmgcparms(bc,fc,bbc,bfc,rbc,rfc,mbc,mfc,hbc,hfc,tbc,tfc,markchar,markkey);
 
int bc,fc;      menu window background/foreground colors
int bbc,bfc;    menu window border (if any) background/foreground colors
int rbc,rfc;    colors for read-only menu elements
int mbc,mfc;    colors for mark character if menu element is marked
int hbc,hfc;    colors for current menu element
int tbc,tfc;    menu window title colors (if any)
int markchar;   current mark character (default == '*')
int markkey;    current mark/unmark key (default == space)

Description:

The mmscparms function is used to set the default colors assigned to a menu
when it is created via mmcreate().
 
The defaults that are in effect right after mminit is called are:
 
    bc  / fc    ==  WNBLACK / WNWHITE
    bbc / bfc   ==  WNBLACK / WNWHITE
    rbc / rfc   ==  WNBLACK / WNDGRAY
    mbc / mfc   ==  WNBLACK / WNWHITE
    hbc / hfc   ==  WNGRAY  / WNWHITE
    tbc / tfc   ==  WNBLACK / WNWHITE
    markchar    ==  '*'
    markkey     ==  space

Return Value:

This function has no return value.

See Also:

mmgcparms

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int bc,fc,bbc,bfc,rbc,rfc,mbc,mfc,hbc,hfc,tbc,tfc,mc,mk;
 
mmgcparms(&bc,&fc,&bbc,&bfc,&rbc,&rfc,&mbc,&mfc,&hbc,&hfc,&tbc,&tfc,&mc,&mk);

                                                                        6 - 69 

                                                                      mmscparms

 
mmscparms(WNRED,   WNYELLOW,         /* back/fore */
          WNRED,   WNBLACK,          /* border back/fore */
          WNRED,   WNLRED,           /* read only back/fore */
          WNBLACK, WNLCYAN,          /* mark character back/fore */
          WNBLACK, WNRED,            /* hightlight back/fore */
          WNBLACK, WNYELLOW,         /* title colors */
          ' ','\0');                /* mark character, no mark key */
 
mmwg = mmcreate("mmwg",MMPOPUP,4,4,0,0,MMABSRC,"[ Global ]","",NULL,0,0,0,nomore
/*
    now put the creation parms back..
*/
mmscparms(bc,fc,bbc,bfc,rbc,rfc,mbc,mfc,hbc,hfc,tbc,tfc,mc,mk);









































                                                                        6 - 70 

                                                                          mmsmel

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int     mmsmel(mnum,mel,name,mdata,mdesc,mcall,lf,ronly,hotkey,actionr,actionn);
 
int     mnum;           menu to this menu item lives on
int     mel;            menu element to redefine
char    *name;          name of this element
char    *mdata;         string to display as menu item
char    *mdesc;         description line for lightbar menu type
char    *mcall;         name of menu to call when this item selected
int     lf;             static/auto flag for mdata and mdesc
int     ronly;          true if this menu item is read-only
int     hotkey;         pick item immediately key
int     (*actionr)();   action routine to call when item selected
char    actionn;        name of actionr routine.  Not supported in V1.1

Description:

The mmsmel function is used to redefine existing menu element mel on menu mnum.
 
All parameters are the same as in the mmamel function.

Return Value:

A value of zero indicates that mel has been redefined with your new parmeters.
A negative value indicates an error which can be found in <mm.h>.

See Also:

mminit, mmcreate, mmamel

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
/* you can find this code in mmdemo1.c */
 
jumptodos(mnum,mel,hotkey)
/***************/
int mnum,mel,hotkey;
{
static toggle = 0;
int wnum;
int wsave,wscroll,wcmode,ul,ur,ll,lr,vti,vbi,hli,hri,ic,vc,hc;

                                                                        6 - 71 

                                                                          mmsmel

 
wngcparms(&wsave,&wscroll,&wcmode,&ul,&ur,&ll,
          &lr,&vti,&vbi,&hli,&hri,&ic,&vc,&hc);
wnscparms(wsave,wscroll,wcmode,           /* create window wo/border */
          ' ',' ',' ',' ',' ',' ',' ',' ',' ',' ',' ');
wnum = wncreate(0,0,wngscols(),wngsrows(),WNBLACK,WNBLACK,WNBLACK,WNBLACK);
if (wnum > 0){
   spawnl(P_WAIT,getenv("COMSPEC"),NULL);
   wndestroy(wnum);
   }
wnscparms(wsave,wscroll,wcmode,ul,ur,ll,lr,vti,vbi,hli,hri,ic,vc,hc);
/*
    just a little something to demonstrate that you can change a menu
    element on the fly.
*/
if (toggle){
    mmsmel(mnum,mel,"","Yes","Jump to DOS",
                 "",0,0,MMNOCASE | 'y',jumptodos,NULL);
    toggle = 0;
    }
else{
    mmsmel(mnum,mel,"","Yes, jump to DOS","Jump to DOS",
                 "",0,0,MMNOCASE | 'y',jumptodos,NULL);
    toggle = 1;
    }
return(0);
}




























                                                                        6 - 72 

                                                                      mmsmelmark

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int  mmsmelmark(mnum,mel);       mark a menu element
int  mmsmelunmark(mnum,mel);     unmark a menu element
 
int  mnum;                       menu to operate on
int  mel;                        element to mark/unmark

Description:

The mmsmelmark and mmsmelunmark functions are used to turn the "mark" status
of menu element mel on or off.  The menu that mel lives in is given by the
integer menu number mnum.
 
The "mark" status of a menu element can be used by your application as you see
fit.  Additionally, for a pop-up menu, all marked elements will be recognized
by an asterisk (*) symbol which is placed to the left of the element.  You can
override the default (*) by using the mmscparms() function.  If you want to use
element marking but don't want it to show on the menu, use a space for the mark
character when you call mmscparms().
 
A -1 value supplied for mel will mark/unmark ALL menu elements of menu mnum.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid mnum or mel.

See Also:

mmsmelunmark, mmgmelstat, mmsmelronly, mmsmelnonronly

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int mnum,mel;
int accrecaction();  /* routine to call when user picks an account */
char *accountname;
 
mnum = mmcreate("acctsrecv",MMPOPUP,0,0,0,0,0,        /* autosize at middle */
                "[ Accounts Receivables ]","",NULL,0,

                                                                        6 - 73 

                                                                      mmsmelmark

                0,0,accrecaction,NULL);
 
accountname = getfirstaccountname();   /* some routine you supply */
while (accountname != NULL){
   mel = mmamel(mnum,"",accountname,"","",1,0,0,MMACTIONNULL,NULL);
   if (accountoverdue(accountname))
      mmsmelmark(mnum,mel);
   /* else leave alone, default stat at mmamel time is unmarked */
   accountname = getnextaccountname();
   }













































                                                                        6 - 74 

                                                                  mmsmelnonronly

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
mmsmelronly(mnum,mel);        make menu element non-selectable
mmsmelnonronly(mnum,mel);     make it selectable again
 
int mnum;                     menu number
int mel;                      element to operate on

Description:

The mmsmelronly and mmsmelnonronly functions are used to turn the read-only
status of menu element mel on or off.  The menu that mel lives on is given by
the integer menu number mnum.
 
Any menu elements that are marked read-only are NOT selectable by the user and
are displayed in the rbc/rfc colors given in the mmscparms() function call.
When a user is moving around in a menu with a mix of read/nonread items he/she
will only land on the non-readonly items while pressing the arrow keys.  If all
items in a menu are readonly the user will be allowed to view all menu items but
cannot select any.
 
A -1 value supplied for mel will set/reset the readonly status of ALL menu
elements of menu mnum.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid mnum or mel.

See Also:

mmsmelronly, mmsmelmark, mmsmelunmark, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
See mmsmelronly() example.





                                                                        6 - 75 

                                                                    mmsmelronly

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
mmsmelronly(mnum,mel);        make menu element non-selectable
mmsmelnonronly(mnum,mel);     make it selectable again
 
int mnum;                     menu number
int mel;                      element to operate on

Description:

The mmsmelronly and mmsmelnonronly functions are used to turn the read-only
status of menu element mel on or off.  The menu that mel lives on is given by
the integer menu number mnum.
 
Any menu elements that are marked read-only are NOT selectable by the user and
are displayed in the rbc/rfc colors given in the mmscparms() function call.
When a user is moving around in a menu with a mix of read/nonread items he/she
will only land on the non-readonly items while pressing the arrow keys.  If all
items in a menu are readonly the user will be allowed to view all menu items but
cannot select any.
 
A -1 value supplied for mel will set/reset the readonly status of ALL menu
elements of menu mnum.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid mnum or mel.

See Also:

mmsmelnonronly, mmsmelmark, mmsmelunmark, mmgmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
 
/*
   mfdel.c     Menu File Delete
 
   A little file delete utility which will build a menu of

                                                                        6 - 76 

                                                                    mmsmelronly

   files in the current directory and allow you to mark/unmark each file.
   When enter is pressed all marked files will be deleted.
 
   When the list is built, all files with a read-only attribute will show
   up on the list but will be marked read-only so the user can't do anything
   with it.
*/
 
 
 
main(argc,argv)
/*****/
int  argc;
char *argv[];
{
int code,mnum,mel,count;
struct find_t cfile;
int kbhit(),getch();
char *cfs;
 
lminit(malloc,free,0);              /* init list manager */
wninit(0,0,NULL,0,malloc,free);     /* window manager using memory */
kminit(kbhit,getch);                /* keyboard manager */
mminit(kmgetch,NULL);               /* menu manager */
 
mmscparms(BC,FC,BBC,BFC,RBC,RFC,MBC,MFC,HBC,HFC,TBC,TFC,MC,MK);
mnum = mmcreate("files",MMPOPUP,ROW,COL,WIDTH,HEIGHT,ABSATT,
                "[ Files in Current Directory ]",
                "[ Space to Mark, ESC to Abort, Enter to Delete Marked ]",NULL,0
                0,1,MMACTIONNULL,NULL);
 
count = 0;
if (argc > 1)
   cfs = argv[1];
else
   cfs = "*.*";
code = _dos_findfirst(cfs,_A_NORMAL | _A_RDONLY,&cfile);
while (code == 0){
   count++;
   mel = mmamel(mnum,"",cfile.name,"","",1,0,MMNOCASE | cfile.name[0],
                MMACTIONNULL,NULL);
   if (cfile.attrib & (_A_RDONLY | _A_HIDDEN | _A_SYSTEM |
                       _A_VOLID | _A_SUBDIR))
      mmsmelronly(mnum,mel);                    /* make read only */
   code = _dos_findnext(&cfile);
   }
 
if (count){
   code = mmpromenu(mnum,MMPROCESS,1);
   if (code != 0){                              /* user didn't ESCAPE */
      if (mmgmelstat(mnum,-1) > 0){                /* user marked files */
         for (mel = mmgnummels(mnum); mel > 0; mel--){
            if (mmgmelstat(mnum,mel)){
               if (unlink(mmgmelmdata(mnum,mel))){      /* delete file */

                                                                        6 - 77 

                                                                    mmsmelronly

                  printf("\nError deleting file [%s].",mmgmelmdata(mnum,mel));
                  }
               }
            }
         }
      }
   }
else{
   printf("\nNo files matching [%s]",cfs);
   }
mmdestroy(mnum);
exit(0);
}










































                                                                        6 - 78 

                                                                    mmsmelunmark

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int  mmsmelmark(mnum,mel);       mark a menu element
int  mmsmelunmark(mnum,mel);     unmark a menu element
 
int  mnum;                       menu to operate on
int  mel;                        element to mark/unmark

Description:

The mmsmelmark and mmsmelunmark functions are used to turn the "mark" status
of menu element mel on or off.  The menu that mel lives in is given by the
integer menu number mnum.
 
The "mark" status of a menu element can be used by your application as you see
fit.  Additionally, for a pop-up menu, all marked elements will be recognized
by an asterisk (*) symbol which is placed to the left of the element.  You can
override the default (*) by using the mmscparms() function.  If you want to use
element marking but don't want it to show on the menu, use a space for the mark
character when you call mmscparms().
 
A -1 value supplied for mel will mark/unmark ALL menu elements of menu mnum.

Return Value:

A value of 0 is returned if all went well.  A negative return indicates an
invalid mnum or mel.

See Also:

mmsmelmark, mmgmelstat, mmsmelronly, mmsmelnonronly

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int mnum,mel;
int accrecaction();  /* routine to call when user picks an account */
char *accountname;
 
mnum = mmcreate("acctsrecv",MMPOPUP,0,0,0,0,0,        /* autosize at middle */
                "[ Accounts Receivables ]","",NULL,0,

                                                                        6 - 79 

                                                                    mmsmelunmark

                0,0,accrecaction,NULL);
 
accountname = getfirstaccountname();   /* some routine you supply */
while (accountname != NULL){
   mel = mmamel(mnum,"",accountname,"","",1,0,0,MMACTIONNULL,NULL);
   if (accountoverdue(accountname))
      mmsmelmark(mnum,mel);
   /* else leave alone, default stat at mmamel time is unmarked */
   accountname = getnextaccountname();
   }
   .
   .
   .
accrecaction(mnum,mel)
/********************/
/*
   This action routine would be called when the user picks a menu element
   in the above menu or presses ESCAPE.
*/
if (mel < 0)   /* user pressed ESCAPE */
   return(0);
else{
   processaccount(mmgmelname(mnum,mel));
   if (!accountoverdue(accountname))
      mmsmelunmark(mnum,mel);
      /* when user is put back in menu, the mark character will be gone. */
   return(-1);    /* this will keep user in accounts receivable menu */
   }



























                                                                        6 - 80 

                                                                        mmsmnum

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mmsmnum(mnum,name,row,col,width,height,abs,ttitle,btitle,
            retkeyonly,actionr,actionn);
 
int     mnum;                       menu number
char    *name;                      menu name
char    *ttitle,*btitle;            top and bottom titles
int     row,col;                    location of menu
int     width,height;               size of menu
int     abs;                        autosize or absolute
int     retkeyonly;                 must hit CR to select menu item
int     (*actionr)();               menu action routine
char    *actionn;                   for V2.0 dynamic loading of menus

Description:

The mmsmnum function is used to change most existing parameters of existing menu
number mnum.  All of the above parameters are described under routine
mmcreate().
 
The default menu colors as set by mmscparms() will be used when this function
is called.  In other words, if you want to change the color(s) of a menu after
is is created, call mmscparms() with the new colors and then call mmsmnum with
the exact same parameters you used in mmcreate.

Return Value:

A value of 0 will be returned if all went well.  A negative value indicates one
of the errors defined in <mm.h>.  A MMMTBERROR (menu too big error) means either
row, col, width, height, or a combination of these were out of range.

See Also:

mmcreate

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "mm.h";
 
int mnum,mel;
int accrecaction();  /* routine to call when user picks an account */
char *accountname;
 

                                                                        6 - 81 

                                                                        mmsmnum

mnum = mmcreate("acctsrecv",MMPOPUP,0,0,0,0,MMABSDEF, /* autosize at middle */
                "[ Accounts Receivables ]","",NULL,0,
                0,0,accrecaction,NULL);
 
accountname = getfirstaccountname();   /* some routine you supply */
while (accountname != NULL){
   mel = mmamel(mnum,"",accountname,"","",1,0,0,MMACTIONNULL,NULL);
   if (accountoverdue(accountname))
      mmsmelmark(mnum,mel);
   /* else leave alone, default stat at mmamel time is unmarked */
   accountname = getnextaccountname();
   }
    .
    .
/*
    now we changed our minds and want the menu at the upper left corner
*/
mmsmnum(mnum,"acctsrecv",1,1,0,0,MMABSDEF,        /* autosize at upper left */
                "[ Accounts Receivables ]","",
                0,accrecaction,NULL);
    .
    .
    .
mmdestroy(mnum);































                                                                        6 - 82 

                                                                          pmlist

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int  pmlist(lnum,ttitle,btitle,row,col,bc,fc,usewin);
 
int  lnum;                          list of items to display
char *ttitle,*btitle;               top and bottom titles
int  row,col;                       center location of display window
int  bc,fc;                         display colors
int  usewin;                        window number to use

Description:

*** OBSOLETE ***  Use new menu manager functions for new programs.
 
The pmlist function is used to display a list of items lnum, to a user, scroll
thru them via PgUp and PgDn, and leave the list by pressing ESC.  The user does
not have the option of marking or selecting an item.  The sole purpose of pmlist
is to display a list of items.
 
Optional titles can be displayed on the menu both top and bottom by supplying
null terminated title strings ttitle and btitle.  Make the strings zero length
if you do not desire a title.
 
Positioning of the menu is somewhat controlled by you by supplying values for
row and col defining where you want the CENTER of the menu to be placed.  The
ultimate size and location of the menu will be determined by the length of the
longest menu item and number of selections.  A value of 0 supplied for row
and/or col will center the menu on the screen in the respective orientation.
 
The color of the menu including border, titles, and list items are controlled by
the background/foreground values bc and fc.
 
The value of usewin that you supply can cause the pmlist function to operate in
1 of 3 modes:
 
(usewin < 0) - The pmlist function will create a window, display the items,
allow the user to scroll between screens, and wait for ESC.  After the user
presses ESC the window will be destroyed.
 
(usewin = 0) - A window will be created and items will be displayed but, the
function will return immediately without letting the user interact.  The return
value will be the window number that was created.  Note that because this
function returns immediately it is only possible to show 1 page of items.
 
(usewin > 0) - The pmlist function will assume that usewin is an existing
window that was created by previously calling it with a value (usewin = 0).
It acts just like (usewin = 0) except for the fact the window creation will

                                                                        6 - 83 

                                                                          pmlist

not be done.

Return Value:

If the parameter usewin is less than 0 the return value will be 0 if all went we
If usewin was >= 0, the return value will be the same as usewin if all went
well.  A negative return value indicates an error.

See Also:

pmmenu, pmmenumu

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
main()
{
int  kbhit(), getch();                  declare for kminit() function
int  wnum, mnum, lnum;
 
lminit(malloc,free,0);                  init the list manager first
kminit(kbhit,getch);                    now the keyboard manager
wninit(0,0,NULL,0,malloc,free);         do the window manager
hminit("GOODHELP.HLP",0,0,0,
       WNBLACK,WNGREEN);                init help manager
 
wnum = wncreate(0,0,80,25,WNBLUE,WNCYAN,
       WNBLUE,WNCYAN);                  create our main window
wnttitle(wnum,"**[Good Title]**");      add a top title
kmsir(KF1,hmhelp);                      make F1 activate help
hmscontext("help_label1");              set help context
    .
    .
  The above startup code would be used in all or most of your applications.
    .
    .
  The following code is specific to building and using a menu.
    .
    .
lnum = lmcreate(NULL,0,0);              create empty list
 
lmael(lnum,"Gooditem1",0,0);            add items to the list
lmael(lnum,"Gooditem2",0,0);
lmael(lnum,"Gooditem3",0,0);
lmael(lnum,"         ",0,0);            leave 2 empty slots for adding
lmael(lnum,"         ",0,0);            items later
 
mnum = pmlist(lnum,"**[List]**","",0,0,

                                                                        6 - 84 

                                                                          pmlist

              WNBLUE,WNCYAN,0);         create window, show list and return
 
strcpy(lmgel(lnum,lmglastel(lnum)),"Lastitem5");
 
mnum = pmlist(lnum,"**[List]**","",0,0,
              WNBLUE,WNCYAN,mnum);      re-display list with new item added
 
lmdestroy(lnum);                        destroy the list
wndestroy(mnum);                        remove list window
wndestroy(wnum);                        remove the main window
}












































                                                                        6 - 85 

                                                                          pmmenu

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
int  pmmenu(lnum,ttitle,btitle,row,col,bc,fc,hbc,hfc,startpick,actionr);
 
int  lnum;                             list of menu items
char *ttitle,*btitle;                  top and bottom menu titles
int  row,col;                          CENTER menu location
int  bc,fc;                            normal menu text colors
int  hbc,hfc;                          highlighted item color
int  startpick;                        item to be highlighted on entry
int  (*actionr)();                     function to call with selection

Description:

*** OBSOLETE ***  Use new menu manager functions for new programs.
 
The pmmenu function is used to display a list of items, lnum, to the user, allow
him/her to scroll thru the items until a selection or ESC is pressed, and
finally, call the routine pointed to by actionr.  If you do not want an action
routine called, set actionr to the value (int (*))NULL.
 
Optional titles can be displayed on the menu both top and bottom by supplying
null terminated title strings ttitle and btitle.  Make the strings zero length
if you do not desire a title.
 
Positioning of the menu is somewhat controlled by you by supplying values for
row and col defining where you want the CENTER of the menu to be placed.  The
ultimate size and location of the menu will be determined by the length of the
longest menu item and number of selections.  A value of 0 supplied for row
and/or col will center the menu on the screen in the respective orientation.
 
The color of the menu including border, titles, and non-highlighted item are
controlled by the background/foreground values bc and fc.  As the user scrolls
thru the menu he/she is reminded of the current item both by a "->" along side
of the current selection as well as color highlighting.  The highlight color to
use is supplied by hbc and hfc.
 
The item highlighted on entry to pmmenu is specified by startpick.
 
When the user makes a selection or presses ESC, the action routine pointed to by
actionr will be called using the following synopsis:
 
    int  (*actionr)(code,list);
 
    int  (*actionr)();
    int  code;                selection user made
    int  lnum;                lnum passed to pmmenu

                                                                        6 - 86 

                                                                          pmmenu

 
A value of -1 will be passed to the action routine if the user pressed ESC while
in the menu, otherwise the selected item (1 - n) will be passed for code.
 
The parameter lnum passed to your action routine is the list number which
contains the selections the menu function is displaying.  Your action routine
may look at this list but should not alter it by deleting or changing items in
it.

Return Value:

The return value from your supplied action routine will be the value returned by
pmmenu.  If there is no action routine, the value returned will be what would
have been passed to actionr via code.  If actionr returns a value of -1, the
user will stayed locked inside of the menu.

See Also:

pmmenumu, pmlist

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
main()
{
int  kbhit(), getch();                  declare for kminit() function
int  wnum, lnum;
int  mmaction();                        will be called by menu function
 
lminit(malloc,free,0);                  init the list manager first
kminit(kbhit,getch);                    now the keyboard manager
wninit(0,0,NULL,0,malloc,free);         do the window manager
hminit("GOODHELP.HLP",0,0,0,
       WNBLACK,WNGREEN);                init help manager
 
wnum = wncreate(0,0,80,25,WNBLUE,WNCYAN,
       WNBLUE,WNCYAN);                  create our main window
wnttitle(wnum,"**[Good Title]**");      add a top title
kmsir(KF1,hmhelp);                      make F1 activate help
hmscontext("help_label1");              set help context
    .
    .
  The above startup code would be used in all or most of your applications.
    .
    .
  The following code is specific to building and using a menu.
    .
    .

                                                                        6 - 87 

                                                                          pmmenu

lnum = lmcreate(NULL,0,0);              create empty list
 
lmael(lnum,"Print HELLO",0,0);          add items to the list
lmael(lnum,"Print GOODBYE",0,0);
lmael(lnum,"Ring the BELL",0,0);
lmael(lnum,"Exit this program",0,0);
 
pmmenu(lnum,"**[Menu]**","",0,0,        the pmmmenu routine will call mmaction
       WNBLUE,WNCYAN,WNBLACK,WNCYAN,    when the user makes a choice
       1,mmaction);
 
lmdestroy(lnum);                        destroy the list of menu items
wndestroy(wnum);                        remove the window
}
 
mmaction(code)                          will be called by pmmenu above
int code;
{
switch(code){
    case -1:                            user pressed ESCAPE while in menu
    case  4:                            user selected Exit option
        return(0);                      will cause menu to exit
        break;
    case  1:                            user selected "print hello"
        printf("hello");
        break;
    case  2:                            user selected "print goodbye"
        printf("goodbye");
        break;
    case  3:                            user selected "ring the bell"
        printf("\007");
        break;
    }
return(-1);                             will cause user to stay in menu
}




















                                                                        6 - 88 

                                                                        pmmenumu

Summary:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
 
int  pmmenumu(lnum,ttitle,btitle,row,col,bc,fc,hbc,hfc,mbc,mfc,
              mkey,startpick,actionr);
 
int  lnum;                             list of menu items
char *ttitle,*btitle;                  top and bottom menu titles
int  row,col;                          CENTER menu location
int  bc,fc;                            normal menu text colors
int  hbc,hfc;                          highlighted item color
int  mbc,mfc;                          "marked" item color
int  mkey;                             keycode which marks/unmarks item
int  startpick;                        item to be highlighted on entry
int  (*actionr)();                     function to call with selection

Description:

*** OBSOLETE ***  Use new menu manager functions for new programs.
 
The pmmenumu function is used to display a list of items, lnum, to the user,
allow him/her to scroll thru the items until a selection or ESC is pressed, and
finally, call the routine pointed to by actionr.  If you do not want an action
routine called, set actionr to the value (int (*))NULL.
 
While in the menu, the user can "mark" and "unmark" items using the key mkey.
When a user marks an item it will have an "*" placed at the left margin and its
color will be changed to mbc and mfc.  If items in list lnum are already marked
when pmmenumu is called, they will be displayed as being marked.  How this
"mark/unmark" status is used is up to you, it serves no purpose to the menu
function.
 
Optional titles can be displayed on the menu both top and bottom by supplying
null terminated title strings ttitle and btitle.  Make the strings zero length
if you do not desire a title.
 
Positioning of the menu is somewhat controlled by you by supplying values for
row and col defining where you want the CENTER of the menu to be placed.  The
ultimate size and location of the menu will be determined by the length of the
longest menu item and number of selections.  A value of 0 supplied for row
and/or col will center the menu on the screen in the respective orientation.
 
The color of the menu including border, titles, and non-highlighted item are
controlled by the background/foreground values bc and fc.  As the user scrolls
thru the menu he/she is reminded of the current item both by a "->" along side
of the current selection as well as color highlighting.  The highlight color to
use is supplied by hbc and hfc.

                                                                        6 - 89 

                                                                        pmmenumu

 
The item highlighted on entry to pmmenumu is specified by startpick.
 
When the user makes a selection or presses ESC, the action routine pointed to by
actionr will be called using the following synopsis:
 
    int  (*actionr)(code,list);
 
    int  (*actionr)();
    int  code;                selection user made
    int  list;                lnum that was passed to pmmenumu
 
A value of -1 will be passed to the action routine if the user pressed ESC while
in the menu, otherwise the selected item (1 - n) will be passed for code.
 
The parameter lnum passed to your action routine is the list number which
contains the selections the menu function is displaying.  Your action routine
may look at this list but should not alter it by deleting or changing items in
it.

Return Value:

The return value from your supplied action routine will be the value returned by
pmmenumu.  If there is no action routine, the value returned will be what would
have been passed to actionr via code.  If actionr returns a value of -1, the
user will stayed locked inside of the menu.

See Also:

pmmenu, pmlist, wnsnmatt, wnshmatt, lmelstat

Example:

#include   "malloc.h";
#include   "lm.h";
#include   "km.h";
#include   "wn.h";
#include   "hm.h";
#include   "mm.h";
 
main()
{
int  kbhit(), getch();                  declare for kminit() function
int  wnum, lnum;
int  mmaction();                        will be called by menu function
 
lminit(malloc,free,0);                  init the list manager first
kminit(kbhit,getch);                    now the keyboard manager
wninit(0,0,NULL,0,malloc,free);         do the window manager
hminit("GOODHELP.HLP",0,0,0,
       WNBLACK,WNGREEN);                init help manager
 
wnum = wncreate(0,0,80,25,WNBLUE,WNCYAN,
       WNBLUE,WNCYAN);                  create our main window

                                                                        6 - 90 

                                                                        pmmenumu

wnttitle(wnum,"**[Good Title]**");      add a top title
kmsir(KF1,hmhelp);                      make F1 activate help
hmscontext("help_label1");              set help context
    .
    .
  The above startup code would be used in all or most of your applications.
    .
    .
  The following code is specific to building and using a menu.
    .
    .
lnum = lmcreate(NULL,0,0);              create empty list
 
lmael(lnum,"Print HELLO",0,0);          add items to the list
lmael(lnum,"Print GOODBYE",0,0);
lmael(lnum,"Ring the BELL",0,0);
lmael(lnum,"Exit this program",0,0);
 
pmmenumu(lnum,"**[Menu]**","",0,0,      the pmmmenumu routine will call mmaction
         WNBLUE,WNCYAN,WNBLACK,WNCYAN,  when the user makes a choice
         WNBLACK,WNYELLOW,KF10,1,       Function key 10 is the mark/unmark key
         mmaction);
 
lmdestroy(lnum);                        destroy the list of menu items
wndestroy(wnum);                        remove the window
}
 
mmaction(code)                          will be called by pmmenumu above
int code;
{
switch(code){
    case -1:                            user pressed ESCAPE while in menu
    case  4:                            user selected Exit option
        return(0);                      will cause menu to exit
        break;
    case  1:                            user selected "print hello"
        printf("hello");
        break;
    case  2:                            user selected "print goodbye"
        printf("goodbye");
        break;
    case  3:                            user selected "ring the bell"
        printf("\007");
        break;
    }
return(-1);                             will cause user to stay in menu
}








                                                                        6 - 91 

                                                                                
























































                                                                        6 - 92 

                                   Kwik Index

 6-18                  obtaining currently active menu
 5-23                    obtaining current active window number
 5-90                    obtaining current active window number
 6-7                                       adding a menu element
 2-3   list                                adding an element to an existing
 5-54                  test if coordinates are in a window
 2-12   a pointer to a list element's data area                          getting
 2-14         to existing list header data area                obtaining pointer
 2-24       resizing a list element's data area
 5-92              setting highlight color attribute to use if in mono mode
 5-94              setting highlight color attribute to use if in mono mode
 5-25            obtaining highlight color attribute used if in mono mode
 5-26               obtaining normal color attribute used if in mono mode
 3-26                          testing for available keycode
 5-30                        obtain window background color
 5-29                 obtain window border background color
 5-41                 obtain window titles background color
 3-10                    delete registered background routine
 3-17            get pointer to registered background routine
 3-34                         resuming the background routine
 3-54                       suspending the background routine
 3-42  waiting for key input      register background routine to run while
 5-7                                       backspacing in a window
 5-75             obtaining wnprintf count before call
 5-10               clearing a window with blanks
 5-29                        obtain window border background color
 5-97                   setting a window's border colors
 5-95                   setting a window's border drawing character set
 5-31                               obtain border drawing characters for window
 5-32                        obtain window border foreground color
 5-8                setting a title at the bottom of a window
 6-25                       obtaining menu bottom title if menu number known
 5-75      obtaining wnprintf count before call
 6-90       a pop-up menu with mark/unmark capability                 displaying
 5-93                                      changing the size of a window
 5-20              filling a window with a character
 5-58                    setting highlight character colors in a window
 5-78                    setting highlight character colors in a window
 5-60                       setting normal character colors in a window
 5-80                       setting normal character colors in a window
 5-21                          obtaining a character from an existing window
 5-52                          inserting a character in a window
 5-56                   locate and print a character in a window
 5-66                             moving a character in a window
 5-76                           printing a character in a window
 5-95    setting a window's border drawing character set
 5-31                obtain border drawing characters for window
 6-9                         display color choice menu
 5-10                                      clearing a window with blanks
 6-79  element                             clearing mark status of a menu
 3-8                                       close keyboard manager input file
 3-9                                       close keyboard manager output file
 4-13                                      closing an open help file
 3-19            the current filter escape code                        obtaining



                                   Kwik Index

 3-44    setting the current filter escape code
 5-30             obtain window background color
 5-29      obtain window border background color
 5-32      obtain window border foreground color
 5-37             obtain window foreground color
 5-41      obtain window titles background color
 5-42      obtain window titles foreground color
 5-92  mode              setting highlight color attribute to use if in mono
 5-94  mode              setting highlight color attribute to use if in mono
 5-25                  obtaining highlight color attribute used if in mono mode
 5-26                     obtaining normal color attribute used if in mono mode
 6-9                               display color choice menu
 5-97            setting a window's border colors
 5-100             setting a window's text colors
 5-103           setting a window's titles colors
 5-58          setting highlight character colors in a window
 5-78          setting highlight character colors in a window
 5-60             setting normal character colors in a window
 5-80             setting normal character colors in a window
 6-26            obtaining upper left menu column if menu number known
 5-35                        obtain window column location
 5-33                        obtain cursor column position in window
 5-27             obtaining maximum screen columns
 4-5                       displaying help context
 4-4         get a pointer to current help context
 3-30   restoring a saved keyboard manager context
 4-9                  restoring saved help context
 4-10                  saving current help context
 3-32         the current keyboard manager context                        saving
 4-12             setting the current help context
 5-107        window coordinates to screen coordinates                 translate
 5-54                              test if coordinates are in a window
 5-107                    translate window coordinates to screen coordinates
 5-75                   obtaining wnprintf count before call
 6-13                                      creating a menu
 5-11                                      creating a window
 2-5   header information                  creating an empty list with optional
 6-20               obtaining default menu creation parameters
 5-22             obtaining default window creation parameters
 6-69                 setting default menu creation parameters
 5-86                      setting default creation parameters for new windows
 5-34                               obtain curren cursor mode in window
 5-23                            obtaining current active window number
 5-90                            obtaining current active window number
 3-19                        obtaining the current filter escape code
 3-44                          setting the current filter escape code
 4-4                      get a pointer to current help context
 4-10                               saving current help context
 4-12                          setting the current help context
 3-32                           saving the current keyboard manager context
 6-18                            obtaining currently active menu
 5-33                               obtain cursor column position in window
 5-55                               locate cursor in a window
 5-34                        obtain curren cursor mode in window

 

                                   Kwik Index

 5-36                               obtain cursor row position in window
 5-99                   setting a window's cursor style
 2-12        a pointer to a list element's data area                     getting
 2-14      pointer to existing list header data area                   obtaining
 2-24            resizing a list element's data area
 3-14                                      de-register a user input routine
 3-15                                      de-register a user output routine
 3-12                                      de-register an intercept routine
 5-86  windows                     setting default creation parameters for new
 6-20                            obtaining default menu creation parameters
 6-69                              setting default menu creation parameters
 5-22                            obtaining default window creation parameters
 3-10                                      delete registered background routine
 5-16                                      deleting a line in a window
 6-17                                      deleting a menu element
 2-7   list                                deleting an element from an existing
 5-13                                      deleting to end of line in a window
 5-14                                      deleting to end of window
 6-36               obtain pointer to menu description string
 6-15                                      destroying a menu
 5-15                                      destroying a window
 2-8                                       destroying an existing list
 6-9                                       display color choice menu
 6-84                                      displaying a pop-up list
 6-87                                      displaying a pop-up menu
 6-90  mark/unmark capability              displaying a pop-up menu with
 4-5                                       displaying help context
 5-95            setting a window's border drawing character set
 5-31                        obtain border drawing characters for window
 5-18                                      editing within a window
 6-7                         adding a menu element
 6-79       clearing mark status of a menu element
 6-17                      deleting a menu element
 6-22          obtain number of first menu element
 6-59           obtain number of next menu element
 6-71                    redefining a menu element
 6-73        setting mark status of a menu element
 2-7                           deleting an element from an existing list
 6-30                          obtain menu element hot key
 2-21                           marking an element in a list
 2-15             obtaining number of last element in a list
 2-16             obtaining number of next element in a list
 2-18         obtaining number of previous element in a list
 2-10                     searching for an element in a list
 2-26                            unmark an element in a list
 2-13            obtaining number of first element in an existing list
 2-9                       testing if list element is marked or unmarked
 6-41                          obtain menu element mark status
 6-37                          obtain menu element name if number known
 6-28                          obtain menu element number if name known
 6-39                          obtain menu element read-only status
 2-3                             adding an element to an existing list
 6-75                       setting a menu element to be selectable
 6-76                       setting a menu element to read only

 

                                   Kwik Index

 2-12          getting a pointer to a list element's data area
 2-24                      resizing a list element's data area
 2-17                  obtaining number of elements in a list
 2-23                           reordering elements in a list
 6-60                obtain number of menu elements in menu
 2-5   information             creating an empty list with optional header
 5-13                          deleting to end of line in a window
 5-14                          deleting to end of window
 3-19         obtaining the current filter escape code
 3-44           setting the current filter escape code
 2-3               adding an element to an existing list
 2-7           deleting an element from an existing list
 2-8                         destroying an existing list
 2-13        number of first element in an existing list               obtaining
 2-14                 obtaining pointer to existing list header data area
 6-81                        redefining an existing menu
 5-21        obtaining a character from an existing window
 3-8          close keyboard manager input file
 3-9         close keyboard manager output file
 4-13                 closing an open help file
 3-27              opening a keycode input file
 3-29             opening a keycode output file
 3-36         input from a suspended input file                         resuming
 3-39         output to a suspended output file                         resuming
 3-56             input from an open input file                       suspending
 3-59             output to an open output file                       suspending
 5-20                                      filling a window with a character
 3-19                obtaining the current filter escape code
 3-44                  setting the current filter escape code
 2-13                  obtaining number of first element in an existing list
 6-22                     obtain number of first menu element
 5-37                        obtain window foreground color
 5-32                 obtain window border foreground color
 5-42                 obtain window titles foreground color
 5-72                               printf function for windows
 3-23  input routine                       get a pointer to a registered user
 4-4   context                             get a pointer to current help
 3-20                                      get keycode from keyboard manager
 3-21                                      get pointer to intercept routine
 3-17  routine                             get pointer to registered background
 3-24  output routine                      get pointer to registered user
 2-12  element's data area                 getting a pointer to a list
 2-14   obtaining pointer to existing list header data area
 6-43                       obtaining menu header if menu number known
 2-5           an empty list with optional header information           creating
 5-38                        obtain window height
 6-46                       obtaining menu height if menu number known
 4-5                            displaying help context
 4-4              get a pointer to current help context
 4-9                       restoring saved help context
 4-10                       saving current help context
 4-12                  setting the current help context
 4-13                      closing an open help file
 4-7                     initialization of help manager

 

                                   Kwik Index

 5-58  window                      setting highlight character colors in a
 5-78  window                      setting highlight character colors in a
 5-92  in mono mode                setting highlight color attribute to use if
 5-94  in mono mode                setting highlight color attribute to use if
 5-25  mono mode                 obtaining highlight color attribute used if in
 6-30                  obtain menu element hot key
 2-5    an empty list with optional header information                  creating
 2-19                         list manager initialization
 4-7                                       initialization of help manager
 3-25                                      initialization of keyboard manager
 6-63                                      initializing the menu manager
 5-44                                      initializing window manager package
 3-42         to run while waiting for key input     register background routine
 3-8                close keyboard manager input file
 3-27                    opening a keycode input file
 3-36      resuming input from a suspended input file
 3-56        suspending input from an open input file
 3-36                             resuming input from a suspended input file
 3-40  routine                    resuming input from a suspended user input
 5-50                            obtaining input from a user in a window
 3-56                           suspending input from an open input file
 3-14                   de-register a user input routine
 3-23   get a pointer to a registered user input routine
 3-47                      register a user input routine
 3-40          input from a suspended user input routine                resuming
 3-60                    suspending a user input routine
 5-52                                      inserting a character in a window
 5-53                                      inserting a line in a window
 3-12                       de-register an intercept routine
 3-21                       get pointer to intercept routine
 3-45                             register intercept routine
 3-37                 resuming a suspended intercept routine
 3-57                           suspending interception of a keycode
 2-9               testing if list element is marked or unmarked
 6-30              obtain menu element hot key
 3-42     routine to run while waiting for key input         register background
 3-20                     get keycode from keyboard manager
 3-25                    initialization of keyboard manager
 3-30                    restoring a saved keyboard manager context
 3-32                   saving the current keyboard manager context
 3-8                                 close keyboard manager input file
 3-9                                 close keyboard manager output file
 3-57         suspending interception of a keycode
 3-26                testing for available keycode
 3-20                                  get keycode from keyboard manager
 3-27                            opening a keycode input file
 3-29                            opening a keycode output file
 6-37   obtain menu element name if number known
 6-28   obtain menu element number if name known
 6-25     menu bottom title if menu number known                       obtaining
 6-43           menu header if menu number known                       obtaining
 6-46           menu height if menu number known                       obtaining
 6-48        obtaining menu name if number known
 6-50        obtaining menu number if name known

 

                                   Kwik Index

 6-54        menu top title if menu number known                       obtaining
 6-55        obtaining menu type if number known
 6-57            menu width if menu number known                       obtaining
 6-26      left menu column if menu number known                 obtaining upper
 6-52   upper left menu row if menu number known                       obtaining
 2-15                  obtaining number of last element in a list
 6-26  known               obtaining upper left menu column if menu number
 6-52                      obtaining upper left menu row if menu number known
 5-63               setting a title at the left side of a window
 5-16                           deleting a line in a window
 5-13                   deleting to end of line in a window
 5-53                          inserting a line in a window
 2-3      adding an element to an existing list
 2-7           an element from an existing list                         deleting
 2-8                destroying an existing list
 6-84                  displaying a pop-up list
 2-21              marking an element in a list
 2-17    obtaining number of elements in a list
 2-13      of first element in an existing list                 obtaining number
 2-15          number of last element in a list                        obtaining
 2-16          number of next element in a list                        obtaining
 2-18      number of previous element in a list                        obtaining
 2-23             reordering elements in a list
 2-10        searching for an element in a list
 2-26               unmark an element in a list
 2-9                            testing if list element is marked or unmarked
 2-12               getting a pointer to a list element's data area
 2-24                           resizing a list element's data area
 2-14        obtaining pointer to existing list header data area
 2-19                                      list manager initialization
 2-5   information       creating an empty list with optional header
 5-56  window                              locate and print a character in a
 5-62  window                              locate and print a string in a
 5-55                                      locate cursor in a window
 5-35                 obtain window column location
 5-39                    obtain window row location
 3-20            get keycode from keyboard manager
 4-7                initialization of help manager
 3-25           initialization of keyboard manager
 6-63                initializing the menu manager
 3-30           restoring a saved keyboard manager context
 3-32          saving the current keyboard manager context
 2-19                                 list manager initialization
 3-8                        close keyboard manager input file
 3-9                        close keyboard manager output file
 5-44                  initializing window manager package
 6-41                  obtain menu element mark status
 6-79                             clearing mark status of a menu element
 6-73                              setting mark status of a menu element
 6-90        displaying a pop-up menu with mark/unmark capability
 2-9            testing if list element is marked or unmarked
 2-21                                      marking an element in a list
 5-27                            obtaining maximum screen columns
 5-28                            obtaining maximum screen rows

 

                                   Kwik Index

 6-13                           creating a menu
 6-15                         destroying a menu
 6-9                  display color choice menu
 6-87                  displaying a pop-up menu
 6-60    obtain number of menu elements in menu
 6-18           obtaining currently active menu
 6-66                         processing a menu
 6-81               redefining an existing menu
 6-25  known                     obtaining menu bottom title if menu number
 6-26                 obtaining upper left menu column if menu number known
 6-20                    obtaining default menu creation parameters
 6-69                      setting default menu creation parameters
 6-36                    obtain pointer to menu description string
 6-7                              adding a menu element
 6-79            clearing mark status of a menu element
 6-17                           deleting a menu element
 6-22               obtain number of first menu element
 6-59                obtain number of next menu element
 6-71                         redefining a menu element
 6-73             setting mark status of a menu element
 6-30                               obtain menu element hot key
 6-41                               obtain menu element mark status
 6-37                               obtain menu element name if number known
 6-28                               obtain menu element number if name known
 6-39                               obtain menu element read-only status
 6-75                            setting a menu element to be selectable
 6-76                            setting a menu element to read only
 6-60                     obtain number of menu elements in menu
 6-43                            obtaining menu header if menu number known
 6-46                            obtaining menu height if menu number known
 6-63                     initializing the menu manager
 6-48                            obtaining menu name if number known
 6-50                            obtaining menu number if name known
 6-25       obtaining menu bottom title if menu number known
 6-43             obtaining menu header if menu number known
 6-46             obtaining menu height if menu number known
 6-54          obtaining menu top title if menu number known
 6-57              obtaining menu width if menu number known
 6-26            upper left menu column if menu number known           obtaining
 6-52     obtaining upper left menu row if menu number known
 6-52                 obtaining upper left menu row if menu number known
 6-34                    obtain pointer to menu string
 6-54                            obtaining menu top title if menu number known
 6-55                            obtaining menu type if number known
 6-57                            obtaining menu width if menu number known
 6-90                  displaying a pop-up menu with mark/unmark capability
 5-25      color attribute used if in mono mode              obtaining highlight
 5-26      color attribute used if in mono mode                 obtaining normal
 5-92    color attribute to use if in mono mode                setting highlight
 5-94    color attribute to use if in mono mode                setting highlight
 5-34                 obtain curren cursor mode in window
 5-25           color attribute used if in mono mode         obtaining highlight
 5-26    normal color attribute used if in mono mode                   obtaining
 5-92         color attribute to use if in mono mode           setting highlight

 

                                   Kwik Index

 5-94         color attribute to use if in mono mode           setting highlight
 5-66                                      moving a character in a window
 5-67                                      moving a string in a window
 5-65                                      moving a window on the screen
 6-32           obtain pointer to sub-menu name
 6-37                  obtain menu element name if number known
 6-48                       obtaining menu name if number known
 6-28        obtain menu element number if name known
 6-50             obtaining menu number if name known
 5-86      default creation parameters for new windows                   setting
 2-16                  obtaining number of next element in a list
 6-59                     obtain number of next menu element
 5-60                              setting normal character colors in a window
 5-80                              setting normal character colors in a window
 5-26  mono mode                 obtaining normal color attribute used if in
 5-23      obtaining current active window number
 5-90      obtaining current active window number
 6-28                  obtain menu element number if name known
 6-50                       obtaining menu number if name known
 6-37          obtain menu element name if number known
 6-25            menu bottom title if menu number known                obtaining
 6-43        obtaining menu header if menu number known
 6-46        obtaining menu height if menu number known
 6-48               obtaining menu name if number known
 6-54     obtaining menu top title if menu number known
 6-55               obtaining menu type if number known
 6-57         obtaining menu width if menu number known
 6-26       upper left menu column if menu number known                obtaining
 6-52          upper left menu row if menu number known                obtaining
 2-17                            obtaining number of elements in a list
 2-13  existing list             obtaining number of first element in an
 6-22                               obtain number of first menu element
 2-15                            obtaining number of last element in a list
 6-60                               obtain number of menu elements in menu
 2-16                            obtaining number of next element in a list
 6-59                               obtain number of next menu element
 2-18                            obtaining number of previous element in a list
 5-31  window                              obtain border drawing characters for
 5-34                                      obtain curren cursor mode in window
 5-33  window                              obtain cursor column position in
 5-36                                      obtain cursor row position in window
 6-30                                      obtain menu element hot key
 6-41                                      obtain menu element mark status
 6-37  known                               obtain menu element name if number
 6-28  known                               obtain menu element number if name
 6-39                                      obtain menu element read-only status
 6-22                                      obtain number of first menu element
 6-60  menu                                obtain number of menu elements in
 6-59                                      obtain number of next menu element
 6-36  string                              obtain pointer to menu description
 6-34                                      obtain pointer to menu string
 6-32                                      obtain pointer to sub-menu name
 5-40                                      obtain scroll status for window
 5-30                                      obtain window background color

 

                                   Kwik Index

 5-29  color                               obtain window border background
 5-32  color                               obtain window border foreground
 5-35                                      obtain window column location
 5-37                                      obtain window foreground color
 5-38                                      obtain window height
 5-39                                      obtain window row location
 5-41  color                               obtain window titles background
 5-42  color                               obtain window titles foreground
 5-43                                      obtain window width
 5-21  existing window                     obtaining a character from an
 5-23  number                              obtaining current active window
 5-90  number                              obtaining current active window
 6-18                                      obtaining currently active menu
 6-20  parameters                          obtaining default menu creation
 5-22  parameters                          obtaining default window creation
 5-25  used if in mono mode                obtaining highlight color attribute
 5-50  window                              obtaining input from a user in a
 5-27                                      obtaining maximum screen columns
 5-28                                      obtaining maximum screen rows
 6-25  number known                        obtaining menu bottom title if menu
 6-43  known                               obtaining menu header if menu number
 6-46  known                               obtaining menu height if menu number
 6-48                                      obtaining menu name if number known
 6-50                                      obtaining menu number if name known
 6-54  number known                        obtaining menu top title if menu
 6-55                                      obtaining menu type if number known
 6-57  known                               obtaining menu width if menu number
 5-26  used if in mono mode                obtaining normal color attribute
 2-17  list                                obtaining number of elements in a
 2-13  an existing list                    obtaining number of first element in
 2-15  a list                              obtaining number of last element in
 2-16  a list                              obtaining number of next element in
 2-18  in a list                           obtaining number of previous element
 2-14  header data area                    obtaining pointer to existing list
 3-19  code                                obtaining the current filter escape
 6-26  menu number known                   obtaining upper left menu column if
 6-52  menu number known                   obtaining upper left menu row if
 5-75                                      obtaining wnprintf count before call
 6-76       setting a menu element to read only
 4-13                           closing an open help file
 3-56             suspending input from an open input file
 3-59              suspending output to an open output file
 3-27                                      opening a keycode input file
 3-29                                      opening a keycode output file
 2-5           creating an empty list with optional header information
 2-9     testing if list element is marked or unmarked
 3-9                close keyboard manager output file
 3-29                    opening a keycode output file
 3-39       resuming output to a suspended output file
 3-59         suspending output to an open output file
 3-15                   de-register a user output routine
 3-24       get pointer to registered user output routine
 3-52                        register user output routine
 3-41            resuming a suspended user output routine

 

                                   Kwik Index

 3-61                    suspending a user output routine
 3-39                             resuming output to a suspended output file
 3-59                           suspending output to an open output file
 5-44          initializing window manager package
 6-20      obtaining default menu creation parameters
 5-22    obtaining default window creation parameters
 6-69        setting default menu creation parameters
 5-86             setting default creation parameters for new windows
 2-12  area                      getting a pointer to a list element's data
 3-23  routine                       get a pointer to a registered user input
 4-4                                 get a pointer to current help context
 2-14  area                      obtaining pointer to existing list header data
 3-21                                  get pointer to intercept routine
 6-36                               obtain pointer to menu description string
 6-34                               obtain pointer to menu string
 3-17  routine                         get pointer to registered background
 3-24  routine                         get pointer to registered user output
 6-32                               obtain pointer to sub-menu name
 6-84                         displaying a pop-up list
 6-87                         displaying a pop-up menu
 6-90  capability             displaying a pop-up menu with mark/unmark
 5-33                 obtain cursor column position in window
 5-36                    obtain cursor row position in window
 2-18                  obtaining number of previous element in a list
 5-56                           locate and print a character in a window
 5-62                           locate and print a string in a window
 5-72                                      printf function for windows
 5-76                                      printing a character in a window
 5-82                                      printing a string in a window
 6-66                                      processing a menu
 6-76            setting a menu element to read only
 6-39                  obtain menu element read-only status
 6-71                                      redefining a menu element
 6-81                                      redefining an existing menu
 3-47                                      register a user input routine
 3-42  while waiting for key input         register background routine to run
 3-45                                      register intercept routine
 3-52                                      register user output routine
 3-10                               delete registered background routine
 3-17                       get pointer to registered background routine
 3-23                   get a pointer to a registered user input routine
 3-24                       get pointer to registered user output routine
 2-23                                      reordering elements in a list
 2-24                                      resizing a list element's data area
 3-30  context                             restoring a saved keyboard manager
 4-9                                       restoring saved help context
 3-37  routine                             resuming a suspended intercept
 3-41  routine                             resuming a suspended user output
 3-36  input file                          resuming input from a suspended
 3-40  input routine                       resuming input from a suspended user
 3-39  output file                         resuming output to a suspended
 3-34                                      resuming the background routine
 5-83               setting a title at the right side of a window
 3-14             de-register a user input routine

 

                                   Kwik Index

 3-15            de-register a user output routine
 3-12             de-register an intercept routine
 3-10         delete registered background routine
 3-23   pointer to a registered user input routine                         get a
 3-21             get pointer to intercept routine
 3-17     pointer to registered background routine                           get
 3-24    pointer to registered user output routine                           get
 3-47                register a user input routine
 3-45                   register intercept routine
 3-52                 register user output routine
 3-37       resuming a suspended intercept routine
 3-41     resuming a suspended user output routine
 3-40    input from a suspended user input routine                      resuming
 3-34              resuming the background routine
 3-60              suspending a user input routine
 3-61             suspending a user output routine
 3-54            suspending the background routine
 3-42  input           register background routine to run while waiting for key
 6-52            obtaining upper left menu row if menu number known
 5-39                        obtain window row location
 5-36                        obtain cursor row position in window
 5-28             obtaining maximum screen rows
 3-42       register background routine to run while waiting for key input
 4-9                             restoring saved help context
 3-30                          restoring a saved keyboard manager context
 4-10                                      saving current help context
 3-32  context                             saving the current keyboard manager
 5-65               moving a window on the screen
 5-27                    obtaining maximum screen columns
 5-107     translate window coordinates to screen coordinates
 5-28                    obtaining maximum screen rows
 5-102                  setting a window's scroll status
 5-40                               obtain scroll status for window
 5-88                                      scrolling text in a window
 2-10                                      searching for an element in a list
 6-75         setting a menu element to be selectable
 5-95    window's border drawing character set                         setting a
 6-75  selectable                          setting a menu element to be
 6-76                                      setting a menu element to read only
 5-8   window                              setting a title at the bottom of a
 5-63  a window                            setting a title at the left side of
 5-83  a window                            setting a title at the right side of
 5-105 window                              setting a title at the top of a
 5-97                                      setting a window's border colors
 5-95  character set                       setting a window's border drawing
 5-99                                      setting a window's cursor style
 5-102                                     setting a window's scroll status
 5-100                                     setting a window's text colors
 5-103                                     setting a window's titles colors
 5-86  for new windows                     setting default creation parameters
 6-69  parameters                          setting default menu creation
 5-58  in a window                         setting highlight character colors
 5-78  in a window                         setting highlight character colors
 5-92  use if in mono mode                 setting highlight color attribute to

 

                                   Kwik Index

 5-94  use if in mono mode                 setting highlight color attribute to
 6-73  element                             setting mark status of a menu
 5-60  window                              setting normal character colors in a
 5-80  window                              setting normal character colors in a
 3-44  code                                setting the current filter escape
 4-12                                      setting the current help context
 5-63          setting a title at the left side of a window
 5-83         setting a title at the right side of a window
 5-93                         changing the size of a window
 6-41             obtain menu element mark status
 6-39        obtain menu element read-only status
 5-102           setting a window's scroll status
 5-40                        obtain scroll status for window
 6-79                        clearing mark status of a menu element
 6-73                         setting mark status of a menu element
 6-34               obtain pointer to menu string
 6-36   obtain pointer to menu description string
 5-62                   locate and print a string in a window
 5-67                             moving a string in a window
 5-82                           printing a string in a window
 5-99            setting a window's cursor style
 6-32                    obtain pointer to sub-menu name
 3-36                resuming input from a suspended input file
 3-37                           resuming a suspended intercept routine
 3-39                 resuming output to a suspended output file
 3-40                resuming input from a suspended user input routine
 3-41                           resuming a suspended user output routine
 3-60                                      suspending a user input routine
 3-61                                      suspending a user output routine
 3-56  file                                suspending input from an open input
 3-57                                      suspending interception of a keycode
 3-59  file                                suspending output to an open output
 3-54                                      suspending the background routine
 5-54                                      test if coordinates are in a window
 3-26                                      testing for available keycode
 2-9   unmarked                            testing if list element is marked or
 5-100                  setting a window's text colors
 5-88                            scrolling text in a window
 5-8                             setting a title at the bottom of a window
 5-63                            setting a title at the left side of a window
 5-83                            setting a title at the right side of a window
 5-105                           setting a title at the top of a window
 6-25                obtaining menu bottom title if menu number known
 6-54                   obtaining menu top title if menu number known
 5-41                        obtain window titles background color
 5-103                  setting a window's titles colors
 5-42                        obtain window titles foreground color
 5-105              setting a title at the top of a window
 6-54                       obtaining menu top title if menu number known
 5-107 screen coordinates                  translate window coordinates to
 6-55                       obtaining menu type if number known
 2-26                                      unmark an element in a list
 2-9          if list element is marked or unmarked                      testing
 6-26  number known              obtaining upper left menu column if menu

 

                                   Kwik Index

 6-52  known                     obtaining upper left menu row if menu number
 5-92         highlight color attribute to use if in mono mode           setting
 5-94         highlight color attribute to use if in mono mode           setting
 5-25            highlight color attribute used if in mono mode        obtaining
 5-26     obtaining normal color attribute used if in mono mode
 5-50               obtaining input from a user in a window
 3-14                        de-register a user input routine
 3-23        get a pointer to a registered user input routine
 3-47                           register a user input routine
 3-40      resuming input from a suspended user input routine
 3-60                         suspending a user input routine
 3-15                        de-register a user output routine
 3-24            get pointer to registered user output routine
 3-52                             register user output routine
 3-41                 resuming a suspended user output routine
 3-61                         suspending a user output routine
 3-42      background routine to run while waiting for key input        register
 3-42   register background routine to run while waiting for key input
 5-43                        obtain window width
 6-57                       obtaining menu width if menu number known
 5-7                      backspacing in a window
 5-93               changing the size of a window
 5-11                           creating a window
 5-16                 deleting a line in a window
 5-14                   deleting to end of window
 5-13         deleting to end of line in a window
 5-15                         destroying a window
 5-18                     editing within a window
 5-52           inserting a character in a window
 5-53                inserting a line in a window
 5-56    locate and print a character in a window
 5-62       locate and print a string in a window
 5-55                   locate cursor in a window
 5-66              moving a character in a window
 5-67                 moving a string in a window
 5-31        border drawing characters for window                         obtain
 5-34         obtain curren cursor mode in window
 5-33     obtain cursor column position in window
 5-36        obtain cursor row position in window
 5-40             obtain scroll status for window
 5-21         a character from an existing window                      obtaining
 5-50     obtaining input from a user in a window
 5-76            printing a character in a window
 5-82               printing a string in a window
 5-88                  scrolling text in a window
 5-8    setting a title at the bottom of a window
 5-63        a title at the left side of a window                        setting
 5-83       a title at the right side of a window                        setting
 5-105     setting a title at the top of a window
 5-58      highlight character colors in a window                        setting
 5-78      highlight character colors in a window                        setting
 5-60         normal character colors in a window                        setting
 5-80         normal character colors in a window                        setting
 5-54         test if coordinates are in a window

 

                                   Kwik Index

 5-30                               obtain window background color
 5-29                               obtain window border background color
 5-32                               obtain window border foreground color
 5-35                               obtain window column location
 5-107 coordinates               translate window coordinates to screen
 5-22                    obtaining default window creation parameters
 5-37                               obtain window foreground color
 5-38                               obtain window height
 5-44                         initializing window manager package
 5-23             obtaining current active window number
 5-90             obtaining current active window number
 5-65                             moving a window on the screen
 5-39                               obtain window row location
 5-41                               obtain window titles background color
 5-42                               obtain window titles foreground color
 5-43                               obtain window width
 5-20                            filling a window with a character
 5-10                           clearing a window with blanks
 5-97                            setting a window's border colors
 5-95  set                       setting a window's border drawing character
 5-99                            setting a window's cursor style
 5-102                           setting a window's scroll status
 5-100                           setting a window's text colors
 5-103                           setting a window's titles colors
 5-72                  printf function for windows
 5-86          creation parameters for new windows               setting default
 5-18                              editing within a window
 5-75                            obtaining wnprintf count before call