===========================================================
                DDDDD           DDDDD               SSSS
                 D   Dunfield    D   D             S
                 D   D           D   Development    SSSS 
                 D   D           D   D                  Systems
                DDDDD           DDDDD               SSSS
          ===========================================================
          MM   MM  IIIIIII    CCCC   RRRRRR     OOO             CCCC
          M M M M     I      C    C  R     R   O   O           C    C
          M  M  M     I     C        R     R  O     O         C
          M     M     I     C        RRRRRR   O     O  -----  C
          M     M     I     C        R   R    O     O         C
          M     M     I      C    C  R    R    O   O           C    C
          M     M  IIIIIII    CCCC   R     R    OOO             CCCC
          ===========================================================
    
    
    
    
    
                                 A 'C' compiler
    
                                      for
    
                           The IBM Personal Computer
    
    
                                Technical Manual
    
    
    
    
    
                                  Release 3.13
    
                               Revised 13-Feb-95
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1988-1995 Dave Dunfield
                              All rights reserved

    MICRO-C                                                          Page: 1


    1. INTRODUCTION
    
          Dunfield Development Systems (DDS) MICRO-C is a compact,  portable
       compiler suitable for code development targeting small 8  or  16  bit
       systems. At the time of this writing, versions of  the  compiler  are
       available which produce code for the 68HC08,  6809,  68HC11,  68HC16,
       8051/52, 8080/85/Z80, 8086 and 8096 processor families.
    
          This document describes a version of MICRO-C, which runs  on,  and
       produces code for the IBM PC family of desktop computers. Included in
       the  package  is  a  complete  implementation  of  MICRO-C,  with   a
       comprehensive library suitable for the PC. This implementation of the
       compiler requires the Microsoft MASM (or  compatible)  assembler  and
       linker.
    
          Commercial versions of the compiler are  designed  for  "embedded"
       systems. This means  that  the  code  produced  by  the  compiler  is
       ROMable, and does not require that it be  run  under  any  particular
       operating system. These compilers are completely configurable so that
       you can  run  the  compiled  code  in  almost  any  hardware/software
       environment imaginable. The commercial packages  also  include  their
       own assembler, linker and debugger. No other software is required  to
       develop code for the target cpu.
    
          This   MICRO-C   "package"   (software   and   documentation)   is
       copyrighted, and all rights to it are reserved. Permission is granted
       to distribute ORIGINAL UNMODIFIED copies ONLY of this archive via BBS
       and disk copying services. MICRO-C is provided on an "as  is"  basis,
       with no warranty of any kind. In no event shall the author be  liable
       for any damages arising from its use or distribution.
    
                          Dunfield Development Systems
              P.O. Box 31044   Nepean, Ontario (Canada)   K2B 8S8
            Tel: 613-256-5820  Fax: 613-256-5821  BBS: 613-256-6289

    MICRO-C                                                          Page: 2


    
       1.1 Document conventions
    
             The following conventions are used in this document:
    
            PC86            - Indicates the full name of the CPU for which
                              you are developing code.
            <text>          - Text shown in angle braces indicates data or
                              options that the user MUST supply.
            [text]          - Text shown in square braces indicates data or
                              options that are optional.
            ...             - Multiple options may be specified.
            CPU[,CPU ...]:  - Indicates a section or note that applies to
                              only the indicated CPU's.
    
       1.2 Code Portability
    
             With few exceptions, this compiler follows the  syntax  of  the
          "standard" UNIX  compiler.  Programs  written  in  MICRO-C  should
          compile with few changes under other "standard" compilers.
    
          1.2.1 Unsupported Features:
    
                MICRO-C does not currently support the following features of
             standard 'C':
    
                    *Long / Double / Float / Enumerated data types,
                    Typedef and Bit fields.
    
            *   32 bit "long" number functions are supported via library
                function calls. These may easily be modified to support
                larger numbers.
    
          1.2.2 Additional Features
    
                MICRO-C provides a few additional  features  which  are  not
             always included in "standard" 'C' compilers:
    
                    Unsigned character variables, Nested comments, 16 bit
                    character constants, Inline assembly code capability.

    MICRO-C                                                          Page: 3


       1.3 Setting up MICRO-C
    
             Once  you  have  installed  the  files  from  the  distribution
          diskettes (See READ.ME on the diskette(s) for instructions), there
          are  a  few  simple  steps  that  should  be  taken  to   complete
          installation of the compiler.
    
           - Setup the MCDIR and MCTMP environment variables,  as  described
             in the section entitled "THE COMMAND CO-ORDINATOR".
    
           - Add the MICRO-C home directory to your DOS 'PATH' if  you  wish
             to be able to run the MICRO-C compiler and  tools  from  within
             other directories on your system.
    
           - Insure that the MASM and LINK command  are  available  on  your
             system. If you are using a compatible assembler and linker with
             a different command line format, refer to the comments  at  the
             beginning of the included CC.C source file for  instruction  on
             how to modify the CC command.
    
           -  If  you  plan  on  using  the  DDSIDE  integrated  development
             environment, make sure that the assembler  and  linker  command
             lines contained in the PC86.IDE configuration file are  correct
             for your system.
    
             Once everything is installed and configured correctly, you  are
          ready to begin using the compiler. There are three ways to run the
          compiler:
    
           - Use the  Integrated  Development  Environment  (DDSIDE),  which
             allows you to enter, compile and debug  your  programs  from  a
             single menu based environment. Complete documentation on DDSIDE
             is provided in the DDSIDE document.
    
           - Use the  "one  step"  COMMAND  CO-ORDINATOR  (CC)  to  run  the
             compiler from the DOS prompt  with  a  single  command.  CC  is
             described in detail later in this document.
    
           - Run the individual steps of the compiler seperately. This gives
             you the maximum control of the compiling process,  but  is  not
             recommended for the novice user. Complete descriptions  of  the
             compilation  steps  and  commands  are  given  later  in   this
             document.

    MICRO-C                                                          Page: 4


       1.4 The compiling process
    
             There are five  programs  which  work  together  to  completely
          compile a MICRO-C program:
    
             The PREPROCESSOR (MCP) takes  the  original  'C'  source  file,
          performs MACRO expansion and incorporates the contents of  INCLUDE
          files  to  get  a  "pure"  'C'  output  file.  A   less   powerful
          pre-processor is also contained inside the COMPILER, which  allows
          this step to  be  skipped  for  programs  which  use  only  simple
          pre-processor functions.
    
             The COMPILER  (MCC)  reads  a  file  containing  a  'C'  source
          program, and translates it into an  equivalent  assembly  language
          program.
    
             The OPTIMIZER (MCO) reads the assembly language output from the
          compiler identifying and replacing "general" code produced by  the
          compiler with more efficent code which is equivalent  in  specific
          cases. This step is  optional,  allowing  you  to  choose  between
          faster compile time and greater program efficency.
    
             The ASSEMBLER (MASM or compatible) takes  the  assembly  output
          from the COMPILER or OPTIMIZER, and produces an OBJECT FILE  which
          contains the executable code and external reference  map  for  the
          program.
    
             The LINKER combines the executable code from  the  OBJECT  FILE
          with code from  other  programs  which  it  calls  (including  any
          LIBRARY functions), to produce a complete  stand-along  executable
          program.
    
             The IBM/PC ASSEMBLER and LINKER are not included in  this  demo
          package, and must be supplied by the user.

    MICRO-C                                                          Page: 5


    2. THE COMMAND CO-ORDINATOR
    
          'CC' is a utility which co-ordinates  the  execution  of  programs
       required for each step of the compilation process to provide a simple
       "one step" compilation command.
    
       2.1 The CC command
    
             The format of the 'CC' command is:
    
                              CC <name> [options]
    
          2.1.1 Command line options
    
                -A      - produce ASSEMBLER (.ASM) output file
                -C      - Include 'C' source as comments in ASM files
                -F      - Fold identical string constants.
                -K      - KEEP all temporary files (do not delete)
                -L      - Produce LINKABLE (.OBJ) output file.
                -O      - OPTIMIZE the output code (using MCO)
                -P      - use the extended PRE-PROCESSOR (MCP)
                -Q      - QUIET mode (suppress informational messages)
                -S      - Use SMALL/.EXE model (Default is TINY/.COM)
                H=mcdir - specify MICRO-C home directory
                T=mctmp - specify prefix for TEMPORARY files
                name=xx - Predefine macro symbol (use with -P only)
    
                When executing the sub-commands, CC will search the  MICRO-C
             home directory, as well as any  directories  specified  in  the
             'PATH' environment variable. Libraries are  accessed  from  the
             MICRO-C home directory only.
    
                The environment variable 'MCDIR' is  examined  to  determine
             the path to  the  MICRO-C  home  directory.  If  MCDIR  is  not
             defined, CC will assume the string '\MC'. You may override this
             directory by using the 'h=' option on the command line.
    
                Intermediate  results  from  each  command  are  stored   in
             "temporary" files, which are fed as input to the next  command.
             Temporary files will be deleted once they are no longer needed,
             except in the case where a command fails.  When  this  happens,
             any temporary file which  was  being  used  as  input  to  that
             command will not be deleted, allowing you to examine it for the
             cause of the error.

    MICRO-C                                                          Page: 6


                The environment variable 'MCTMP' is examined to determine  a
             prefix to prepend to temporary file  names.  If  MCTMP  is  not
             defined, CC assumes the default prefix of '$'. You may override
             this prefix by using the 't=' option on the command line.
    
                Here are example 'SET' commands suitable  for  inclusion  in
             the AUTOEXEC.BAT file, of an IBM/PC based MICRO-C system  which
             has the home directory in 'C:\MC', and a TEMP  directory  on  a
             RAMDISK as drive 'D':
    
                    SET MCDIR=C:\MC
                    SET MCTMP=D:\TEMP\      (Note trailing '\')
    
                    Note: DO NOT put spaces before or after the '='
    
                The  '-A'  option  causes  CC  to  bypass  the  linker   and
             assembler, and produce an assembly source file (<name>.ASM)  as
             the output file. If the '-C' option is  also  used,  this  file
             will contain the 'C' source code in the form of comments. NOTE:
             The source code inserted by '-C' will restrict the optimizer to
             operate only on sections of code produced by a single 'C' line.
    
                The '-F' option causes the compiler to  "fold"  its  literal
             pool (the area of memory where string  constants  are  stored).
             This means that identical strings  not  contained  in  explicit
             variables, will occur only once in memory. Since most  programs
             never modify such strings, it is usually safe to do this.  Note
             however that this is a violation of the 'C' standard ("The  'C'
             Programming Language"  page  181  -  "All  strings,  even  when
             written identically, are distinct"),  and  it  is  possible  to
             write programs which will not work properly when this option is
             used.
    
                The '-L' option causes CC  to  bypass  the  link  step,  and
             produce a linkable object  module  as  the  output  file  (.OBJ
             extension).
    
                If any of the programs  executed  by  CC  fail  to  complete
             properly, CC will show the message "PGM failed (RC)", where PGM
             is the name of the offending program, and RC is the DOS  return
             code value. Common RC values under MSDOS are:
    
                2   - Command not found (Check MCDIR and PATH setup)
                3   - Path not found    (Check MCDIR and PATH setup)
                254 - Program found errors during processing
                255 - Program was invoked with incorrect arguments

    MICRO-C                                                          Page: 7


       2.2 Using multiple object modules
    
             The 'LC' command takes one or more object modules  produced  by
          'CC' with the '-L' option, and links them with  the  libraries  to
          produce an executable module. This module will be given  the  name
          of the first file specified in the argument list.
    
             When compiling large programs which have more than  one  source
          file, you must first compile all modules using 'CC' with the  '-L'
          option, and the use 'LC' to link the resultant object  files  into
          the final executable program.
    
             The '-S' option may be used as the FIRST argument, to cause  LC
          to link in the SMALL model.
                eg: CC FIRST -L
                    CC SECOND -L
                    LC FIRST SECOND         <-- TINY  Model
                    LC -S FIRST SECOND      <-- SMALL Model
    
             The exact syntax  and  options  available  for  'CC'  and  'LC'
          commands may differ in specific implementations of  the  compiler.
          See the 'READ.ME' file and any additional technical  documentation
          on your distribution disk(s) for details.

    MICRO-C                                                          Page: 8


    3. THE MICRO-C PROGRAMMING LANGUAGE
    
          The following pages contain a brief summary of  the  features  and
       constructs implemented in MICRO-C.
    
       3.1 Constants
    
             The following forms of constants are supported by the compiler:
    
                <num>       - Decimal number        (0 - 65535)
                0<num>      - Octal number          (0 - 0177777)
                0x<num>     - Hexidecimal number    (0x0 - 0xffff)
                '<char>'    - Character             (1 or 2 chars)
                "<string>"  - Address of literal string.
    
             The following "special" characters may be used within character
          constants or strings:
    
                \n          - Newline (line-feed)   (0x0a)
                \r          - Carriage Return       (0x0d)
                \t          - Tab                   (0x09)
                \f          - Formfeed              (0x0c)
                \b          - Backspace             (0x08)
                \<num>      - Octal value <num>     (Max. three digits)
                \x<num>     - Hex value <num>       (Max. two digits)
                \<char>     - Protect character <char> from input scanner.
    
       3.2 Symbols
    
             Symbol names  may  include  the  characters  'a'-'z',  'A'-'Z',
          '0'-'9', and '_'. The characters '0'-'9' may not be  used  as  the
          first character in the  symbol  name.  Symbol  names  may  be  any
          length, however, only the first 15 characters are significant.
    
             The "char" modifier may be used to declare a symbol as an 8 bit
          value, otherwise it is assumed to be 16 bits.
    
                              eg: char input_char;
    
             The "int" modifier may be used to declare a symbol as a 16  bit
          wide value. This is assumed if neither "int" or "char" is given.
    
                                  eg: int abc;
    
             The "unsigned" modifier may be used to declare a symbol  as  an
          unsigned positive only value. Note that unlike some 'C' compilers,
          this modifier may be applied to a character (8 bit) variable.
    
                            eg: unsigned char count;
    
             The "extern" modifier causes the compiler to be  aware  of  the
          existance and  type  of  a  global  symbol,  but  not  generate  a
          definition for that symbol. This allows the module being  compiled
          to reference a symbol which is defined  in  another  module.  This
          modifier may not be used with local symbols.
    
                            eg: extern char getch();

    MICRO-C                                                          Page: 9


             A  symbol  declared  as  external  may  be  re-declared  as   a
          non-external at a later  point  in  the  code,  in  which  case  a
          definition for it will be generated. This allows  "extern"  to  be
          used to inform the compiler of a function or variable type so that
          it can be referenced  properly  before  that  symbol  is  actually
          defined.
    
             The "static" modifier causes global  symbols  to  be  available
          only in the file where they are defined.  Variables  or  functions
          declared  as  "static"  will  not  be   accessable   as   "extern"
          declarations in other object files, nor will they cause  conflicts
          with duplicate names in those files.
    
                         eg: static int variable_name;
    
             When applied to local symbols,  the  "static"  modifier  causes
          those variables to be allocated in  a  reserved  area  of  memory,
          instead of on the processor stack. This has the  effect  that  the
          contents of the variable will be retained  between  calls  to  the
          function. It also means that the variable  may  be  initialzed  at
          compile time.
    
             The "register" modifier indicates to the  code  generator  that
          this is a high priority variable, and should be kept where  it  is
          easy to get at. See "Functions" for a special  use  of  "register"
          when defining a function.
    
                          eg: register unsigned count;
    
             Symbols declared with a preceeding '*' are assumed to be 16 bit
          pointers to the declared type.
    
                             eg: int *pointer_name;
    
             Symbol names declared followed by square brackets  are  assumed
          to be arrays with a number of dimensions equal to  the  number  of
          '[]' pairs that follow. The size of each dimension  is  identified
          by a constant value  contained  within  the  corresponding  square
          brackets.
    
                          eg: char array_name[5][10];
    
             The "void" modifier is a special case which means  this  symbol
          should never be used as a value. It is usually used to indicate  a
          function which returns  nothing,  or  a  pointer  which  is  never
          dereferenced.
    
                               eg: void *pointer;

    MICRO-C                                                          Page: 10


          3.2.1 Global Symbols
    
                Symbols  declared  outside  of  a  function  definition  are
             considered to  be  global  and  will  have  memory  permanently
             reserved for them. Global symbols are defined by  name  in  the
             output file, allowing other modules to access them.
    
                Global variables may be initialized with one or more values,
             which are expressed as a single array of  integers  REGUARDLESS
             of the size and shape of the variable. If more than  one  value
             is expressed, '{' and '}' must be used.
    
                   eg: int i = 10, j[2][2] = { 1, 2, 3, 4 };
    
                When arrays are declared, a null dimension may  be  used  as
             the dimension size, in which case the size of  the  array  will
             default to the number of initialized values.
    
                         eg: int array[] = { 1, 2, 3 };
    
                Initialized global variables are automatically saved  within
             the code image,  insuring  that  the  initial  values  will  be
             available at run time. Any non-initialized alements of an array
             which has been partly initialized will be set to zero.
    
                Non-initialized global variables are not preset in any  way,
             and will be undefined at the beginning of program execution.
    
          3.2.2 Local Symbols
    
                Symbols declared within a function definition are  allocated
             on the stack, and  exist  only  during  the  execution  of  the
             function.
    
                To simplify the allocation and de-allocation of stack space,
             all local symbols must be declared  at  the  beginning  of  the
             function before any code producing statements are encountered.
    
                MICRO-C does not support initialization of non-static  local
             variables in the declaration statement. Since  local  variables
             have to be initialized every time the function is entered,  you
             can get the same effect  using  assignment  statements  at  the
             beginning of the function.
    
                No type is assumed for  arguments  to  functions.  Arguments
             must be explicitly declared, otherwise they will  be  undefined
             within the scope of the function definition.

    MICRO-C                                                          Page: 11


          3.2.3 More Symbol Examples
    
            /* Global variables are defined outside of any function */
            char a;                     /* 8 bit signed */
            unsigned char b;            /* 8 bit unsigned */
            int c;                      /* 16 bit signed */
            unsigned int d;             /* 16 bit unsigned */
            unsigned e;                 /* also 16 bit unsigned */
            extern char f();            /* external function returning char */
            static int g;               /* 16 bit signed, local to file */
            int h[2] = { 1, 2 };        /* initialized array (2 ints) */
    
            main(a, b)                  /* "int" function containing code */
            /* Function arguments are defined between function name and body */
                int a;                  /* 16 bit signed */
                unsigned char *b;       /* pointer to 8 bit unsigned */
            {
            /* Local variables are defined inside the function body */
            /* Note that in MICRO-C, only "static" locals can be initialized */
                unsigned c;             /* 16 bit unsigned */
                static char d[5];       /* 8 bit signed, reserved in memory */
                static int e = 1;       /* 16 bit signed, initial value is 1 */
            /* Function code goes here ... */
                c = 0;                  /* Initialize 'c' to zero */
                strcpy(d, "Name");      /* Initialize 'd' to "name" */
            }
    
       3.3 Arrays & Pointers
    
             When MICRO-C passes an array to a function, it actually  passes
          a POINTER to the array. References to arrays which  are  arguments
          are automatically performed through the pointer.
    
             This allows the use of pointers and arrays to be interchangable
          through the context of a function call. Ie: An array passed  to  a
          function may be declared and used as  a  pointer,  and  a  pointer
          passed to a function may be declared and used as an array.

    MICRO-C                                                          Page: 12


       3.4 Functions
    
             Functions are  essentially  initialized  global  symbols  which
          contain executable code.
    
             MICRO-C accepts  any  valid  value  as  a  function  reference,
          allowing  some  rather  unique  (although  non-standard)  function
          calls.
    
          For example:
    
                function();     /* call function */
                variable();     /* call contents of a variable */
                (*var)();       /* call indirect through variable */
                (*var[x])();    /* call indirect through indexed array */
                0x5000();       /* call address 0x5000 */
    
             MICRO-C accepts both the  "classic"  and  "modern"  formats  of
          argument definition for a function.
    
             In the "classic" format, only the argument names are placed  in
          the brackets following the function name. The closing  bracket  is
          followed by formal declarations for the arguments (in any order):
    
              eg: int function(a, b, c) int a, c; char b; { ... }
    
             If the "modern" format, complete declarations for EACH argument
          are enclosed in the brackets following the function name:
    
                 eg: int function(int a, char b, int c) { ... }
    
             Since this is a single pass compiler, operands to functions are
          evaluated and pushed on the stack in the order in which  they  are
          encountered, leaving the last operand closest to the  top  of  the
          stack. This is the  opposite  order  from  which  many  other  'C'
          compilers push operands.
    
             For functions with a fixed number of arguments,  the  order  of
          which operands  are  passed  is  of  no  importance,  because  the
          compiler looks after generating  the  proper  stack  addresses  to
          reference variables.  HOWEVER,  functions  which  use  a  variable
          number of arguments are affected for two reasons:
    
          1) The location of the LAST arguments are known (as fixed  offsets
             from the stack pointer) instead of the FIRST.
    
          2) The symbols defined as arguments  in  the  function  definition
             represent the LAST arguments instead of the FIRST.
    
             If a function is declared as "register", it  serves  a  special
          purpose and causes the accumulator to be loaded with the number of
          arguments passed whenever the function is called. This allows  the
          function to know how many  arguments  were  passed  and  therefore
          determine the location of the first argument.

    MICRO-C                                                          Page: 13


       3.5 Structures & Unions
    
             Combinations of other variable  types  can  be  organized  into
          STRUCTURES or UNIONS, which allow them  to  be  manipulated  as  a
          single entity.
    
             In a structure, the  individual  items  occur  sequentially  in
          memory, and the total size of the structure  is  the  sum  of  its
          elements. Structures are usually  used  to  create  "records",  in
          which related items are grouped together. An array  of  structures
          is the common method of implementing an "in-memory" database.
    
             A union is similar to a structure, except that  the  individual
          items are overlaid in memory, and the total size of the  union  is
          the size of its largest element. Unions are usually used to  allow
          a single block of memory to be accessed as different 'C'  variable
          types. An example of this would be in handling a message  received
          in memory, in which a "type" byte indicates how the  remainder  of
          the message data should be interpreted.
    
             Here are some example of how structures are  defined  and  used
          (unions are defined and used in an identical manner,  except  that
          the word 'union' is substituted for 'struct'):
    
            /* Create structure named 'data' with 'a,b,c & d' as members */
            struct {
                int a;
                int b;
                char c;
                char d; } data;
    
            /* Create structure template named 'mystruc'... */
            /* No actual structure variable is defined */
            struct mystruc {
                int a;
                int b;
                char c;
                char d; };
    
            /* Create structure named 'data' using above template */
            struct mystruc data;
    
            /* Create structure template 'mystruc', AND define a */
            /* structure variable named 'data' */
            struct mystruc {
                int a;
                int b;
                char c;
                char d; } data;

    MICRO-C                                                          Page: 14


            /* Create an array of structures, a pointer to a structure */
            /* and an array of pointers to a structure *
            struct mystruct array[10], *pointer, *parray[10];
    
            /* To set value in structure variable/members */
            data.a = 10;            /* Direct access */
            array[1].b = 10;        /* Direct array access */
            pointer->c = 'a';       /* Pointer access */
            parray[2]->d = 'b';     /* Pointer array access */
    
            /* To read value in structure variable/members */
            value = data.a;         /* Direct access */
            value = data[1].b;      /* Direct array access */
            value = pointer->c;     /* Pointer access */
            value = parray[2]->d;   /* Pointer array access */
    
          3.5.1 Notes on MICRO-C structure implementation:
    
                Structures and Unions as implemented in MICRO-C are  similar
             to the implementation of the original UNIX  'C'  compiler,  and
             are bound by similar limitations, as  well  as  a  few  MICRO-C
             specific ones.  Here  is  a  list  of  major  differences  when
             compared to a modern ANSI compiler:
    
                All structure and member names MUST  be  unique  within  the
             scope of the definition. A special case  exists,  where  common
             member names may be used in  multiple  structure  templates  if
             they have EXACTLY the same type and offset into the  structure.
             This also saves symbol table memory, since only one copy of the
             member definition is actually kept.
    
                MICRO-C does NOT pass entire structures to functions on  the
             stack. Like  arrays,  MICRO-C  passes  structures  by  ADDRESS.
             Structure variables which are function arguments  are  accessed
             through pointers. For source code compatibility with  compilers
             which do pass the entire structure, if you declare the argument
             as a direct (non-pointer) structure, the direct ('.')  operator
             is used to dereference it, even though it is actually a pointer
             reference.
    
                If you  MUST  have  a  local  copy  of  the  structure,  use
             something like:
    
                func(sptr)
                    struct mystruc *sptr;
                {
                    struct mystruc data;
                    memcpy(data, sptr, sizeof(data));
                    ...
                }

    MICRO-C                                                          Page: 15


                To obtain the size of a structure from  its  template  name,
             use the 'struct'  keyword  in  conjunction  with  the  'sizeof'
             operator.   In   the   above   example,   you   could   replace
             'sizeof(data)' with 'sizeof(struct mystruc)'.
    
                To obtain the size of a structure member, you  must  specify
             it in the context of a structure reference with another symbol:
    
              sizeof(variable.member) or sizeof(variable->member)
    
                NOTE: The current compiler allows almost any symbol  to  the
             left of the '.' or '->' operator in a 'sizeof', however  future
             versions of the compiler may insist on a structure variable  or
             a pointer to structure variable.
    
                Pointers to structures are internally stored as pointers  to
             'char', and therefore will only increment/decrement by  1  when
             ++/-- is used. To advance a pointer by the size of a structure,
             use:
    
                         ptr += sizeof(struct mystruc)
    
                The 'struct' and 'union' keywords  are  not  accepted  in  a
             TYPECAST. This is most commonly used to setup a  pointer  to  a
             structure. Since MICRO-C stores its pointers to  structures  as
             pointers to char, you can use (char*) as the typecast, and  get
             the same functionality.
    
                A structure name by itself (without  '.member')  acts  in  a
             manner similar to a character array name.  With  no  operation,
             the address of the structure is returned. You can also use '[]'
             to access  individual  bytes  in  the  structure  by  indexing,
             although doing so is highly non-portable.
    
                MICRO-C allows static or global structures to be initialized
             in the declaration, however the initial values are read  as  an
             array of bytes, and are assigned directly to  structure  memory
             without regard for the type or size of its members:
    
                struct mystruc data = { 0, 1, 0, 2, 3, 4 };
                /* A=0:1, B=0:2, C=3, D=4 */
    
                You can use INT and CHAR to switch back  and  forth  between
             word/byte initialization within the value list:
    
                struct mystruct data = { int 0, 1, char 2, 3 };
                /* A=0, B=1, C=2, D=3 */
    
                Strings encountered during structure initializations will be
             encoded as a series of bytes if byte initialization  (char)  is
             in effect, or  as  pointers  into  the  literal  pool  if  word
             initialization (int) is in effect.
    
                MICRO-C does not WORD ALIGN structure elements. When using a
             processor which requires word alignment, it is the  programmers
             responsibility to maintain alignment, using filler  bytes  etc.
             when necessary.

    MICRO-C                                                          Page: 16


       3.6 Control Statements
    
             The following control statements are implemented in MICRO-C:
    
                if(expression)
                    statement;
    
                if(expression)
                    statement;
                else
                    statement;
    
                while(expression)
                    statement;
    
                do
                    statement;
                while expression;
    
                for(expression; expression; expression)
                    statement;
    
                return;
    
                return expression;
    
                break;
    
                continue;
    
                switch(expression) {
                    case constant_expression :
                        statement;
                        ...
                        break;
                    case constant_expression :
                        statement;
                        ...
                        break;
                        .
                        .
                        .
                    default:
                        statement; }
    
                label: statement;
    
                goto label;
    
                asm "...";
    
                asm {
                    ...
                    }

    MICRO-C                                                          Page: 17


    3.6.1 Notes on Control Structures
    
        1)  Any "statement" may be a single statement or a compound
            statement enclosed within '{' and '}'.
    
        2)  All three "expression"s in the "for" command are optional.
    
        3)  If a "case" selection does not end with "break;", it will
            "fall through" and execute the following case as well.
    
        4)  Expressions following 'return' and 'do/while' do not have
            to be contained in brackets (although this is permitted).
    
        5)  Label names may preceed any statement, and must be any
            valid symbol name, followed IMMEDIATELY by ':' (No spaces
            are allowed). Labels are considered LOCAL to a function
            definition and will only be accessable within the scope
            of that function.
    
        6)  The 'asm' statement used to implement the inline assembly
            language capability of MICRO-C accepts two forms:
                asm "...";      <- Assemble single line.
                asm {           <- Assemble multiple lines.
                    ...
                    }

    MICRO-C                                                          Page: 18


       3.7 Expression Operators
    
             The following expression operators are implemented in MICRO-C:
    
    3.7.1 Unary Operators
    
        -           - Negate
        ~           - Bitwise Complement
        !           - Logical complement
        ++          - Pre or Post increment
        --          - Pre or post decrement
        *           - Indirection
        &           - Address of
        sizeof      - Size of a object or type
        (type)      - Typecast
    
    3.7.2 Binary Operators
    
        +           - Addition
        -           - Subtraction
        *           - Multiplication
        /           - Division
        %           - Modulus
        &           - Bitwise AND
        |           - Bitwise OR
        ^           - Bitwise EXCLUSIVE OR
        <<          - Shift left
        >>          - Shift right
        ==          - Test for equality
        !=          - Test for inequality
        >           - Test for greater than
        <           - Test for less than
        >=          - Test for greater than or equal to
        <=          - Test for less than or equal to
        &&          - Logical AND
        ||          - Logical OR
        =           - Assignment
        +=          - Add to self assignment
        -=          - Subtract from self assignment
        *=          - Multiply by self assignment
        /=          - Divide by and reassign assignment
        %=          - Modular self assignment
        &=          - AND with self assignment
        |=          - OR with self assignment
        ^=          - EXCLUSIVE OR with self assignment
        <<=         - Shift left self assignment
        >>=         - Shift right self assignment

    MICRO-C                                                          Page: 19


    NOTES:
    
        1)  The expression "a && b" returns 0 if "a" is zero, otherwise the
            value of "b" is returned. The "b" operand is NOT evaluated if
            "a" is zero.
    
        2)  The expression "a || b" returns the value of "a" if it is not 0,
            otherwise the value of "b" is returned. The "b" operand is NOT
            evaluated if "a" is non-zero.
    
    3.7.3 Other Operators
    
        ;           - Ends a statement.
        ,           - Allows several expressions in one statement.
                    + Separates symbol names in multiple declarations.
                    + Separates constants in multi-value initialization.
                    + Separates operands in function calls.
        ?           - Conditional expression (ternary operator).
        :           - Delimits labels, ends CASE and separates conditionals.
        .           - Access a structure member directly.
        ->          - Access a structure member through a pointer.
        { }         - Defines a BLOCK of statements.
        ( )         - Forces priority in expression, indicates function calls.
        [ ]         - Indexes arrays. If fewer index values are given than the
                      number of dimensions which are defined for the array,
                      the value returned will be a pointer to the appropriate
                      address.
    
                    Eg:
                        char a[5][2];
    
                        a[3] returns address of forth row of two characters.
                        (remember index's start from zero)
    
                        a[3][0] returns the character at index [3][0];

    MICRO-C                                                          Page: 20


       3.8 Inline Assembly Language
    
             Although 'C' is a powerful and  flexible  language,  there  are
          sometimes instances where a particular operation must be  peformed
          at the assembly language level. This most  often  involves  either
          some processor feature for which there  is  no  corresponding  'C'
          operation, or a section of very time critical code.
    
             MICRO-C provides access to assembly  language  with  the  'asm'
          statement, which has two basic forms. The first is:
    
                                  asm "..." ;
    
             In this form, the entire  text  contained  between  the  double
          quote characters (") is output as a single line to the  assembler.
          Note that a  semicolon  is  required,  just  like  any  other  'C'
          statement.
    
             Since this is a standard 'C' string, you can  use  any  of  the
          "special" characters, and thus you could output multiple lines  by
          using '\n' within the string. Another important characteristic  of
          it being a string is that it will be protected from  pre-processor
          substitution.
    
             The second form of the 'asm' statement is:
    
                                     asm {
                                      ...
                                       }
    
             In this form, all lines between '{' and '}' are output  to  the
          assembler. Any text following the opening '{' (on the  same  line)
          is ignored. Due to  the  unknown  characteristics  of  the  inline
          assembly code, the closing '}' will only be recognized when it  is
          the first non-whitespace character on a line.
    
             The integral pre-processor will not perform substitution on the
          inline assembly code, however  the  external  pre-processor  (MCP)
          will substitute in this form. This allows you to  create  assembly
          language "macros" using MCP, and have parameters substituted  into
          them when they are expanded:
    
            /*
             * This macro issues a 'SETB' instruction for its parameter
             */
            #define setbit(bit) asm {\
                SETB bit\
            }
    
            /*
             * This macro WILL NOT WORK, since the 'bit' operand to the SETB
             * instruction is contained within a string and is therefore
             * protected from substitution by the pre-processor
             */
            #define setbit(bit) asm " SETB bit";

    MICRO-C                                                          Page: 21


       3.9 Preprocessor Commands
    
             The  MICRO-C  compiler  supports  the  following  pre-processor
          commands. These commands are recognized only if they occur at  the
          beginning of the input line.
    
             NOTE:  This  describes  the  limited  pre-processor  which   is
          integral to the  compiler,  see  also  the  section  on  the  more
          powerful external processor (MCP).
    
          3.9.1 #define <name> <replacement_text>
    
                The "#define" command allows a global name  to  be  defined,
             which will be replaced with the indicated text whenever  it  is
             encountered in the input file. This occurs prior to  processing
             by the compiler.
    
          3.9.2 #file <filename>
    
                Sets the filename of the currently  procssing  file  to  the
             given  string.  This  command   is   used   by   the   external
             pre-processor (MCP) to insure that error messages indicate  the
             original source file.
    
          3.9.3 #include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "#include" in the original file.
    
          3.9.4 #ifdef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is defined.
    
          3.9.5 #ifndef <name>
    
                Processes the following lines (up to #else or  #endif)  only
             if the given name is NOT defined.
    
          3.9.6 #else
    
                Processes the following lines (up to  #endif)  only  if  the
             preceeding #ifdef or #ifndef was false.
    
          3.9.7 #endif
    
                Terminates #ifdef and #ifndef
    
                NOTE: The integral pre-processor does not support nesting of
             the #ifdef and #idndef constructs. If you wish  to  nest  these
             conditionals, you must use the external pre-processor (MCP).

    MICRO-C                                                          Page: 22


       3.10 Error Messages
    
             When MICRO-C detects an  error,  it  outputs  an  informational
          message indicating the type of problem encountered.
    
             The error message is preceeded by the filename and line  number
          where the error occured:
    
                           program.c(5): Syntax error
    
             In the above example, the error occured in the file "program.c"
          at line 5.
    
             The following error messages are produced by the compiler:
    
          3.10.1 Compilation aborted
    
                The preceeding error was so severe than the compiler  cannot
             proceed.
    
          3.10.2 Constant expression required
    
                The compiler requires a constant  expression  which  can  be
             evaluated at compile time (ie: no variables).
    
          3.10.3 Declaration must preceed code.
    
                All local variables must be defined at the beginning of  the
             function, before any code producing statements are processed.
    
          3.10.4 Dimension table exhausted
    
                The compiler has encountered more  active  array  dimensions
             than it can handle.
    
          3.10.5 Duplicate local: 'name'
    
                You have declared the named  local  symbol  more  than  once
             within the same function definition.
    
          3.10.6 Duplicate global: 'name'
    
                You have declared the named global symbol more than once.
    
          3.10.7 Expected '<token>'
    
                The compiler  was  expecting  the  given  token,  but  found
             something else.
    
          3.10.8 Expression stack overflow
    
                The compiler has found a more complicated expression than it
             can handle. Check that it is of  correct  syntax,  and  if  so,
             break it up into two simpler expressions.

    MICRO-C                                                          Page: 23


          3.10.9 Expression stack underflow
    
                The compiler has made an error in  parsing  the  expression.
             Check that it is of correct syntax.
    
          3.10.10 Illegal indirection
    
                You have attempted to perform an indirect operation ('*'  or
             '[]') on an entity which is not a pointer or array. This  error
             will also result if you attempt to index  an  array  with  more
             indices than it has dimensions.
    
          3.10.11 Illegal initialization
    
                Local variables may not be initialized  in  the  declaration
             statement. Use assignments at the  beginning  of  the  function
             code to perform the initialization.
    
          3.10.12 Illegal nested function
    
                You may not declare a  function  within  the  definition  of
             another function.
    
          3.10.13 Illegal pointer operation
    
                You are attempting to perform  an  operation  which  is  not
             allowed in pointer arithmetic.
    
          3.10.14 Illegal use of void type
    
                You have attempted to manipulate  a  value  which  has  been
             declared "void".
    
          3.10.15 Improper type of symbol: 'name'
    
                The named  symbol  is  not  of  the  correct  type  for  the
             operation that you are attempting. Eg: 'goto' where the  symbol
             is not a label.
    
          3.10.16 Improper #else/#endif
    
                A #else or #endif statement is out of place.
    
          3.10.17 Inconsistant member offset: 'name'
    
                The named structure member is multiply defined,  and  has  a
             different offset from its first definition.
    
          3.10.18 Inconsistant member type: 'name'
    
                The named structure member is multiply defined,  and  has  a
             different type from its first definition.
    
          3.10.19 Inconsistant re-declaration: 'name'
    
                You have attempted to redefine  the  named  external  symbol
             with a type which does not match its previously declared type.

    MICRO-C                                                          Page: 24


          3.10.20 Incorrect declaration
    
                A statement occuring outside of a function definition is not
             a valid declaration for a function or global variable.
    
          3.10.21 Invalid '&' operation
    
                You have attempted to reference  the  address  of  something
             that has no address. This error also occurs when you attempt to
             take the address of an array without giving it a  full  set  of
             indicies. Since the address is already returned in  this  case,
             simply drop the '&'. (The error occurs because you  are  trying
             to take the address of an address).
    
          3.10.22 Macro expansion too deep
    
                The compiler has encountered a nested macro reference  which
             is too deep to be resolved.
    
          3.10.23 Macro space exhausted
    
                The compiler has encountered  more  macro  ("#define")  text
             than it has room to store. Use the external  MCP  pre-processor
             which has much greater macro storage capability.
    
          3.10.24 No active loop
    
                A "continue" or "break" statement was  encountered  when  no
             loop is active.
    
          3.10.25 No active switch
    
                A "case" or "default"  statement  was  encountered  when  no
             "switch" statement is active.
    
          3.10.26 Not an argument: 'name'
    
                You have declared the named variable as an argument, but  it
             does not appear in the argument list.
    
          3.10.27 Non-assignable
    
                You have attempted an operation which results in  assignment
             of a value to an entity which cannot be assigned. (eg: 1 = 2);
    
          3.10.28 Numeric constant required
    
                The compiler requires a constant expression which returns  a
             simple numeric value.
    
          3.10.29 String space exhausted
    
                The compiler has encountered more literal  strings  than  it
             has room store.

    MICRO-C                                                          Page: 25


          3.10.30 Symbol table full
    
                The compiler has encountered more symbol definitions than it
             can handle.
    
          3.10.31 Syntax error
    
                The statement shown does not follow syntax rules and  cannot
             be parsed.
    
          3.10.32 Too many active cases
    
                The compiler has run out of space  for  storing  switch/case
             tables. Reduce the number of active "cases".
    
          3.10.33 Too many defines
    
                The compiler has encountered more '#define' statements  than
             it can handle. Reduce the number of #defines.
    
          3.10.34 Too many errors
    
                The compiler is aborting because of excessive errors.
    
          3.10.35 Too many includes
    
                The compiler has encountered more  nested  "#include"  files
             than it can handle.
    
          3.10.36 Too many initializers
    
                You have specified more initialization values than there are
             locations in the global variable.
    
          3.10.37 Too many pointer levels
    
                You have declared an item with more levels  of  re-direction
             ('*'s) than the compiler can handle.
    
          3.10.38 Type clash
    
                You have attempted to use a  value  in  a  manner  which  is
             inconsistant with its typing information.
    
          3.10.39 Unable to open: 'name'
    
                A "#include" command specified the named file,  which  could
             not be opened.
    
          3.10.40 Undefined: 'name'
    
                You have referenced a name which is not defined as  a  local
             or global symbol.

    MICRO-C                                                          Page: 26


          3.10.41 Unknown structure/member: 'name'
    
                You have referenced a  structure  template  or  member  name
             which is not defined.
    
          3.10.42 Unreferenced: 'name'
    
                The named  symbol  was  defined  as  a  local  symbol  in  a
             function, but was never used in that function. This error  will
             occur at the end of  the  function  definition  containing  the
             symbol declaration. It is only a warning, and  will  not  cause
             the compile to abort.
    
          3.10.43 Unresolved: 'name'
    
                The named symbol was forward  referenced  (Such  as  a  GOTO
             label), and was never defined. This error will occur at the end
             of the function definition containing the reference.
    
          3.10.44 Unterminated conditional
    
                The end of file was encountered  when  a  "#if"  or  "#else"
             conditional block was being processed.
    
          3.10.45 Unterminated function
    
                The  end  of  the  file  was  encountered  when  a  function
             definition was still open.

    MICRO-C                                                          Page: 27


       3.11 Quirks
    
             Due  to  its  background  as  a  highly  compact  and  portable
          compiler, and its target application in embedded systems,  MICRO-C
          deviates from standard 'C' in  some  areas.  The  following  is  a
          summary of the major infractions and quirks:
    
             When using the INTERNAL  pre-processor,  the  operands  to  '#'
          commands are parsed based on separating spaces, and any portion of
          the line not required is ignored.  In  particular,  the  '#define'
          command only accepts a definition up to  the  next  space  or  tab
          character.
    
            eg: #define APLUSONE A+1        <-- uses "A+1"
                #define APLUSONE A +1       <-- uses "A"
    
             Comments are stripped by the token scanner, which occurs  AFTER
          the '#' commands are processed.
    
            eg: #define NULL    /* comment */   <-- uses "/*"
    
             Note that since comments can therefore be included in "#define"
          symbols, you can use "/**/" to simulate spaces between tokens.
    
            eg: #define BYTE unsigned/**/char
    
             Include filenames are not delimited by '""'  or  '<>'  and  are
          passed to the operating system exactly as entered.
    
            eg: #include \mc\stdio.h
    
             NOTE:  The  above  quirks  DO  NOT  APPLY  when  the   EXTERNAL
          pre-processor (MCP) is used.
    
             The appearance of a variable name in the argument list  for  an
          old style  function  declaration  serves  only  to  identify  that
          variables location on the  stack.  MICRO-C  will  not  define  the
          variable unless it is explicitly declared  (between  the  argument
          list and the main function body). In other words, all arguments to
          a function must be explicitly declared.
    
             MICRO-C is more  strict  about  its  handling  of  the  ADDRESS
          operator ('&') than most other compilers. It will produce an error
          message if you attempt to take the address of  a  value  which  is
          already a fixed address (such as an array name without a full  set
          of indicies). Since an address is already produced in such  cases,
          simply drop the '&'.
    
             The 'x' in '0x' and '\x' is accepted in lower case only.

    MICRO-C                                                          Page: 28


             When operating on pointers, MICRO-C only scales  the  increment
          (++), decrement (--) and index ([]) operations to account for  the
          size of the pointer:
    
            eg: char *cptr;     /* pointer to character */
                int  *iptr;     /* pointer to integer */
                ++cptr;         /* Advance one character */
                ++iptr;         /* Advance one integer */
                cptr[10];       /* Access the tenth character */
                iptr[10];       /* Access the tenth integer */
                cptr += 10;     /* Advance 10 characters */
                iptr += 10;     /* Advance ONLY FIVE integers */
    
            NOTE: A portable way to advance "iptr" by integers is:
    
                iptr = &iptr[10];   /* Advance 10 integers */
    
             Since  structures  are  internally  represented  as  arrays  of
          "char", incrementing a pointer to a structure  will  advance  only
          one (1) byte in memory. To advance to the "next" instance  of  the
          structure, use:
    
                        ptr += sizeof(struct template);
    
             The INDEXING operator '[]' is not commutative  in  MICRO-C.  In
          other words 'array[index]' cannot be expressed as 'index[array]'.
    
             MICRO-C does  not  support  "complex"  declarations  which  use
          brackets '()' for other than function parameters. These  are  most
          often used in establishing pointers to functions:
                    int (*a)();     /* Pointer to function returning INT */
                    (*a)();         /* Call address in 'a' */
    
             Since MICRO-C allows you to call any value by following it with
          '()', you can get  the  desired  effect  in  the  above  case,  by
          declaring 'a' as a simple pointer to int, and calling it with  the
          same syntax:
                    int *a;         /* Pointer to INT */
                    (*a)();         /* Call address in 'a' */
    
             MICRO-C will not output external  declarations  to  the  output
          file  for  any  variables  or  functions  which  are  declared  as
          "extern", unless that symbol is actually  referenced  in  the  'C'
          source code. This prevents "extern" declarations in system  header
          files (such as "stdio.h") which are used as  prototypes  for  some
          library functions from causing those functions to be  loaded  into
          the  object  file.  Therefore,  any  "extern"  symbols  which  are
          referenced only by inline assembly code must be  declared  in  the
          assembly code, not by the MICRO-C "extern" statement.

    MICRO-C                                                          Page: 29


             Unlike some  'C'  compilers,  MICRO-C  will  process  character
          expressions using only  BYTE  values.  Character  values  are  not
          promoted to INT unless there is  an  INT  value  involved  in  the
          expression. This results in much more efficent code  when  dealing
          with characters, particularily  on  small  processors  which  have
          limited 16 bit instructions. Consider the statement:
    
                                 return c + 1;
    
             On some compilers, this will sign extend the character variable
          'c' into an integer value, and then ADD an integer  1  and  return
          the  result.  MICRO-C  will  ADD  the  character  variable  and  a
          character 1, and then promote the result to INT  before  returning
          it (results of expressions as  operands  to  'return'  are  always
          promoted to int).
    
             Unfortunately, programs have been written  which  rely  on  the
          automatic promotion of characters to INTs to  work  properly.  The
          most common source of problems is code  which  attempts  to  treat
          CHAR variables as UNSIGNED values (many older  compilers  did  not
          support UNSIGNED CHAR). For example:
    
                                return c & 255;
    
             In a compiler which always evaluates character  expressions  as
          INT, the above statement will extract the value of 'c' as positive
          integer ranging from 0 to 255.
    
             In MICRO-C, ANDing a character with 255  results  in  the  same
          character, which gets promoted to an integer  value  ranging  from
          -128 to 127. To force the promotion  within  the  expression,  you
          could CAST the variable to an INT:
    
                              return (int)c & 255;
    
             The same objective can be achieved  in  a  more  efficent  (and
          correct) manner by declaring the variable 'c' as UNSIGNED CHAR, or
          by CASTing the variable to an UNSIGNED value:
    
                              return (unsigned)c;
    
             Note that this is not only more clearly shows the intent of the
          programmer, but also results is more efficent code generated.

    MICRO-C                                                          Page: 30


             A related quirk arises because most processors do not support a
          simple efficent method for adding or subtracting a  SIGNED  8  bit
          quantity and a 16 bit quantity. The code generators supplied  with
          MICRO-C make the assumption that character values being  added  or
          subtracted to/from integers will contain only POSITIVE values, and
          thus use UNSIGNED  addition/subtraction.  This  allows  much  more
          efficent code to be generated, as the carry/borrow  from  the  low
          order byte of the operation is simply propagated to the high order
          byte of the result (an operation  supported  in  hardware  by  the
          CPU).
    
             For those rare instances where you do wish  to  add/subtract  a
          potentially negative character value to/from an int, you can force
          the expression to be performed  in  less  efficent  fully  16  bit
          arithmetic by casting the character to an int.
    
                int i;
                char c;
                ...
                i += c;         /* Very efficent... C should be positive */
                i += (int)c;    /* Less efficent... C can be negative */
    
             Read the notes at the end of the section  entitled  "Structures
          and Unions" for information on  limitations  or  differences  from
          standard 'C' in MICRO-C's implementation of structures and unions.

    MICRO-C                                                          Page: 31


    4. ADVANCED TOPICS
    
          This section provides information on the more advanced aspects  of
       MICRO-C, which  is  generally  not  needed  for  casual  use  of  the
       language.
    
       4.1 Conversion Rules
    
             MICRO-C keep track of the "type" of  each  value  used  in  all
          expressions. This type identifies certain characteristics  of  the
          value,  such  as   size   range   (8/16   bits),   numeric   scope
          (signed/unsigned), reference (value/pointer) etc.
    
             When an  operation  is  performed  on  two  values  which  have
          identical "types", MICRO-C assigns that same "type" to the result.
    
             When the  two  value  "types"  involved  in  an  operation  are
          different, MICRO-C calculates the "type" of the result  using  the
          following rules:
    
          4.1.1 Size range
    
                If both values are  direct  (not  pointer)  references,  the
             result will be 8 bits only if  both  values  were  8  bits.  If
             either value was 16 bits, the result will be 16 bits.
    
                If one value is a pointer, and  the  other  is  direct,  the
             result will be a pointer to the same size value as the original
             pointer.
    
                If both values were pointers, the result will be  a  pointer
             to 16 bits only if both original  pointers  referenced  16  bit
             values. If either pointer referenced an 8 bit value, the result
             will reference an 8 bit value.
    
          4.1.2 Numeric Scope
    
                The result of an expression is considered to be signed  only
             if both original values were signed. If  either  value  was  an
             unsigned value, the result is unsigned.
    
          4.1.3 Reference
    
                If either of the original values was a pointer,  the  result
             will  be  a  pointer.  One  exception  to  this  rule  is   the
             subtraction of two pointers, which yeilds an integer result.
    
             Note that this "calculated" result type  is  used  for  partial
          results within an expression. Whenever a symbol such as a variable
          or function is referenced, the type of that symbol is  taken  from
          its declaration, no matter what "type" of value  was  last  stored
          (variable) or returned (function).
    
             The TYPECAST  operation  may  be  used  to  override  the  type
          calculated for the result of an expression if necessary.

    MICRO-C                                                          Page: 32


       4.2 Assembly Language Interface
    
             Assembly language programs may be called from 'C' functions and
          vice versa. These programs may be in the form of  inline  assembly
          language statements in the 'C' source code, or  separately  linked
          modules.
    
             The MICRO-C runtime  library  includes  a  number  of  assembly
          language subroutines which provide various services  (such  as  16
          bit  multiplication,  division,  etc).  These  routines  are  well
          documented in the library startup code files ({CPU}RL?.ASM), which
          you should examine before  attempting  to  use  assembly  language
          within MICRO-C.
    
             Global variables defined in 'C' exist at absolute addresses and
          may be referenced directly by name from assembly language.  Global
          names which are referenced  by  both  assembly  language  and  'C'
          should not be longer than 15 characters.
    
             When MICRO-C calls any routine ('C'  or  assembler),  it  first
          pushes all arguments to the routine onto the processor  stack,  in
          the order in  which  they  occur  in  the  argument  list  to  the
          function. This means that the LAST argument  to  the  function  is
          CLOSEST to the top of the processor stack.
    
             Arguments are always pushed as 16 bit values. Character  values
          are extended to 16 bits, and arrays are passed as 16 bit  pointers
          to the array. (MICRO-C knows that arrays which are  arguments  are
          actually  pointers,  and  automatically  references  through   the
          pointer).
    
             After pushing the arguments, MICRO-C then generates  a  machine
          language subroutine  call,  thereby  executing  the  code  of  the
          routine.
    
             Once the called routine returns, the arguments are removed from
          the stack by the calling program.
    
             It is the responsibility of the called function to  remove  any
          saved registers and local variable space from the stack before  it
          returns. If a value is to be returned to the calling  program,  it
          is expected to be in the 16 bit ACCUMULATOR.
    
             Examine  the  supplied  library  functions,  as  well  as  code
          produced by the compiler to gain more insight into the  techniques
          of accessing local variables and arguments.

    MICRO-C                                                          Page: 33


          8086,8096:
    
             The 16 bit accumulator is maintained in register AX.
    
             Any assembly language code  should  preserve  the  register  BP
          which is used for stack addressing. Normally, an assembly language
          function would save BP on the stack, and then copy SP  to  BP  for
          its own stack addressing.
    
             Local variables in a function may  be  referenced  as  negative
          offsets from the stack frame pointer. The address of a  particular
          local variable is calculated as:
    
                             "stack frame pointer"
                                       -
                         (Size of all local variables)
                                       +
                    (size of all preceeding local variables)
    
             Arguments to a function may  also  be  referenced  as  positive
          offsets from the stack pointer, in much  the  same  way  as  local
          variables are. The address of a particular argument is  calculated
          as:
    
                             "stack frame pointer"
                                       +
                  (Size of 'BP' stacked at function entry (2))
                                       +
                       (Size of saved return address (2))
                                       +
                      (# arguments from LAST argument) * 2
    
             If a function has been declared  as  "register",  MICRO-C  will
          load the 'AX' accumulator with the number of arguments which  were
          passed, each time the function is called. This allows the function
          to determine the location of the  first  argument,  which  may  be
          calculated as:
    
                             "stack frame pointer"
                                       +
                  (Size of 'BP' stacked at function entry (2))
                                       +
                       (Size of saved return address (2))
                                       +
                           (Accumulator contents) * 2

    MICRO-C                                                          Page: 34


       4.3 Compiling for ROM
    
             The output from the compiler is entirely "clean",  and  may  be
          placed in Read Only Memory (ROM).
    
             The addresses for code and data storage are established by  the
          startup files in the runtime library, called {CPU}RL*.ASM. You may
          examine and modify these files to suit your own particular  memory
          allocation needs.
    
             The compiler places all initialized  global  variables  in  the
          output file as part of the code image. When the program is  stored
          in ROM, those variables are also stored in ROM, and  will  not  be
          modifiable.
    
             When the program is to be placed in ROM, you may not initialize
          any variables which you intend to modify  later.  Those  variables
          must be explicitly initialized by code executed at  the  beginning
          of the program.
    
             Variables which you do not intend to  modify  (such  as  tables
          etc.)  may  be  initialized  in  the  declaration,  and  will   be
          permanently saved in the ROM as part of the static code image.

    MICRO-C                                                          Page: 35


    5. THE MICRO-C PREPROCESSOR
    
          The MICRO-C Preprocessor is a source code filter,  which  provides
       greater capabilities than the preprocessor which is integral  to  the
       MICRO-C compiler. It has been implemented as a  stand  alone  utility
       program which processes the source code before it is compiled.
    
          Due to the higher complexity of  this  preprocessor,  it  operates
       slightly slower than the the integral MICRO-C preprocessor.  This  is
       mainly due to the fact that it reads each line from the file and then
       copies it to a new line while performing the macro substitution. This
       is necessary since each macro may contain parameters  which  must  be
       replaced "on the fly" when it is referenced.
    
          The integral MICRO-C preprocessor is very FAST,  because  it  does
       not copy the input line. When it encounters a '#define'd  symbol,  it
       simply adjusts the input scanner pointer to point to  the  definition
       of that symbol.
    
          Keeping the extended preprocessor as a stand alone utility  allows
       you  to  choose  between  greater   MACRO   capability   and   faster
       compilation. It also allows the system to continue  to  run  on  very
       small hardware platforms.
    
          The additional capabilities of the extended preprocessor are:
    
            - Parameterized MACROs.
    
            - Multiple line MACRO's.
    
            - Nested conditionals.
    
            - Ability to undefine MACRO symbols.
    
            - Library reference in include file names.

    MICRO-C                                                          Page: 36


       5.1 The MCP command
    
             The format of the MICRO-C Preprocessor command line is:
    
                    MCP [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are given, MCP will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  processed
          source code is written. If less than two filenames are  specified,
          MCP will write to standard output.
    
          5.1.1 Command Line Options
    
                MCP accepts the following command line [options]:
    
                -c      - Instructs MCP to keep comments from  the input
                          file (except for those in '#' statements which
                          are always removed). Normally, MCP will remove
                          all comments.
    
                -l      - Causes the output file to contain line numbers.
                          Each line in the output file will be  prefixed
                          with the line number of the  originating  line
                          from the input file.
    
                l=path  - Defines the directory path which will be taken
                          to reference  "library"  files when  '<>'  are
                          used around an  '#include'  file name.  Unless
                          otherwise specified, the path defaults to:
                                        '\mc'
    
                -q      - Instructs MCP to be quiet, and not display the
                          startup message when it is executed.
    
          <name>=<text> - Pre-defines a non-parameterized macro  of  the
                          specified <name> with the string value <text>.

    MICRO-C                                                          Page: 37


       5.2 Preprocesor Commands
    
             The following commands are recognized by the MCP utility,  only
          if they occur at the beginning of the source file line:
    
          5.2.1 #define <name>(parameters) <replacement text>
    
                Defines a global macro name which will be replaced with  the
             indicated <replacement text> wherever it occurs in  the  source
             file.
    
                Macro  names  may  be  any  length,  and  may  contain   the
             characters 'a'-'z', 'A'-'Z', '0'-'9' and '_'.  Names  must  not
             begin with the characters '0'-'9'.
    
                If the macro name is IMMEDIATELY followed by a list of up to
             10 parameter names contained in brackets, those parameter names
             will be substituted with parameters passed to the macro when it
             is referenced. Parameter names follow the same rules  as  macro
             names.
    
                     eg: #define min(a, b) (a < b ? a : b)
    
                If any spaces exist between the macro name and  the  opening
             '(', the macro will not be  parameterized,  and  all  following
             text (including '(' and ')') will be  entered  into  the  macro
             definition.
    
                If the very last character of a  macro  definition  line  is
             '\', MCP will continue the definition with the next  line  (The
             '\' is not included). Pre-processor statements included as part
             of a macro definition will not be processed by MCP, but will be
             passed on and handled by the integral MICRO-C preprocessor.
    
          5.2.2 #undef <symbol>
    
                Undefines the named macro symbol. further references to this
             symbol will not be replaced.
    
                NOTE: With MCP, macro definitions operate on a STACK. IE: If
             you define a macro  symbol,  and  then  re-define  it  (without
             '#undef'ing it first), subsequently '#undef'ing it  will  cause
             it to revert to its  previous  definition.  A  second  '#undef'
             would then cause it to be completely undefined.

    MICRO-C                                                          Page: 38


          5.2.3 #forget <symbol>
    
                Similar  to  '#undef',  except  that  the  symbol  and   ALL
             SUBSEQUENTLY DEFINED SYMBOLS will be undefined.
    
                Useful for releasing any local symbols (used only  within  a
             single include file).
    
                For example:
    
                        #define GLOBAL "xxx"    /* first global symbol */
                            ...                 /* more globals */
                        #define LOCAL   "xxx"   /* first local symbol */
                            ...                 /* more locals */
                        /* body of include file goes here */
                        #forget LOCAL           /* release locals */
    
          5.2.4 #ifdef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is defined as a macro.
    
          5.2.5 #ifndef <symbol>
    
                Causes the following lines (up to '#else' of '#endif') to be
             processed and included in the source file  only  if  the  named
             symbol is NOT defined as a macro.
    
                NOTE: '#ifdef/#ifndef#else/#endif' may be nested.
    
          5.2.6 #else
    
                Toggles the state of the "if_flag", controlling  conditional
             processing. Only has effect in the highest level  of  suspended
             processing. IE: Nested conditionals will work properly.
    
                If the previous  '#ifdef/#ifndef'  failed,  processing  will
             begin again following the '#else'.
    
                If the previous '#ifdef/#ifndef' passed, processing will  be
             suspended until the '#endif' is encountered.
    
                NOTE: Since '#else' acts as a toggle, it may be used outside
             of any '#ifdef/#ifndef' to unconditionally  suspend  processing
             up to '#endif'. You can also use multiple '#else's in a  single
             conditional,  to  swap  back  and  forth   between   true/false
             processing without re-testing the condition.
    
          5.2.7 #endif
    
                Resets  the  "if_flag"  controlling  conditionals,   causing
             processing to resume. Only has effect in the highest  level  of
             suspended  processing.  IE:  Nested  conditionals   will   work
             properly.

    MICRO-C                                                          Page: 39


          5.2.8 #include <filename>
    
                Causes MCP to open the named file and include  its  contents
             as part of the input source.
    
                If the filename is contained within '"' characters, it  will
             be opened exactly as  specified,  and  (unless  it  contains  a
             directory path) will reference a file in the current directory.
    
                If the filename is contained within the characters  '<'  and
             '>', it will be  prefixed  with  the  library  path  (See  'l='
             option), and will therefore reference a file  in  that  library
             directory. The default  library  directory  is  assumed  to  be
             '\mc'.
    
                For example:
    
                        #include "header.h"     /* from current directory */
                        #include <stdio.h>      /* from library directory */

    MICRO-C                                                          Page: 40


       5.3 Error messages
    
             When MCP detects an error during processing of an include file,
          it displays an error message, which is preceeded by  the  filename
          and line number where the error occurs. If more than 10 errors are
          encountered, MCP will terminate.
    
             The following error messages are reported by MCP:
    
          5.3.1 Cannot open include file
    
                A '#include' statement on the  indicated  line  specified  a
             file which could not be opened for reading.
    
          5.3.2 Invalid include file name
    
                A '#include' statement on the  indicated  line  specified  a
             file  name  which  was  not  contained  within  '"'   or   '<>'
             characters.
    
          5.3.3 Invalid macro name
    
                A '#define' statement on the indicated line contains a macro
             name which does not follow the name rules.
    
          5.3.4 Invalid macro parameter
    
                A '#define' statement on the indicated line contains a macro
             parameter name which does not follow the name rules.
    
                A reference to a macro does not have a proper ')'  character
             to terminate the parameter list.
    
          5.3.5 Too many errors
    
                More  than  10  errors  has  been  encountered  and  MCP  is
             terminating.
    
          5.3.6 Too many macro definitions
    
                MCP has encountered more '#define' statements  than  it  can
             handle.
    
          5.3.7 Too many macro parameters
    
                A '#define' statement on the indicated line  specifies  more
             parameters to the macro than MCP can handle.
    
          5.3.8 Too many include files
    
                MCP has encountered more nested '#include'  statements  than
             it can handle.

    MICRO-C                                                          Page: 41


          5.3.9 Undefined macro
    
                A '#undef' or '#forget'  statement  on  the  indicated  line
             references a macro name which has not been defined.
    
          5.3.10 Unterminated comment
    
                The END OF FILE has  been  encountered  while  processing  a
             comment.
    
          5.3.11 Unterminated string
    
                A quoted string  on  the  indicated  line  has  no  end.  To
             continue a string to  the  next  line,  use  '\'  as  the  last
             character on the line. The '\' will  not  be  included  in  the
             string.

    MICRO-C                                                          Page: 42


    6. THE MICRO-C COMPILER
    
          The heart of the MICRO-C programming environment is the  COMPILER.
       This program reads a  file  containing  a  'C'  source  program,  and
       translates it into an equivalent assembly language program.
    
          The compiler includes its  own  limited  pre-processor,  which  is
       suitable for  compiling  programs  requiring  only  non-parameterized
       MACRO substitution, simple INCLUDE file capability, and  single-level
       CONDITIONAL processing.
    
       6.1 The MCC command
    
             The format of the MICRO-C PC86 Compiler command line is:
    
                    MCC [input_file] [output_file] [options]
    
             [input_file] is the name of  the  source  file  containing  'C'
          statements to read. If no filenames are given, MCC will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  generated
          assembly language code is written. If less than two filenames  are
          specified, MCC will write to standard output.
    
          6.1.1 Command Line Options
    
                -c      - Includes the 'C' source code in the output file
                          as assembly language comments.
    
                -f      - Causes the compiler to "Fold" its literal pool.
                          (Identical strings not contained in explicit
                          variables only once in memory).
    
                -l      - Enables MCC to accept line numbers.
                          (At beginning of line, followed by ':').
    
                -q      - Instructs MCC to be quiet, and not display the
                          startup message when it is executed.

    MICRO-C                                                          Page: 43


    7. THE MICRO-C OPTIMIZER
    
          The MICRO-C optimizer is an output code filter which examines  the
       assembly code produced by the compiler, recognizing known patterns of
       inefficent code (using the "peephole" technique), and  replaces  them
       with more optimal code  which  performs  the  same  function.  It  is
       entirely table driven, allowing it to be modified for  virtually  any
       processor.
    
          Due its many table lookup operations, the  optimizer  may  perform
       quite slowly when processing a large  file.  For  this  reason,  most
       people prefer not to optimize during the debugging of a program,  and
       utilize the optimizer only when creating the final copy.
    
       7.1 The MCO command
    
             The format of the MICRO-C Optimizer command line is:
    
                    MCO [input_file] [output_file] [options]
    
             [input_file] is the name of the source file containing assembly
          statements to read. If no filenames are given, MCO will read  from
          standard input.
    
             [output_file] is the name of the file to  which  the  optimized
          assembly  code  is  written.  If  less  than  two  filenames   are
          specified, MCO will write to standard output.
    
          7.1.1 Command Line Options
    
                MCO accepts the following command line [options]:
    
                -d      - Instructs MCO to produce a 'debug' display on
                          standard output showing the  source code  which
                          it is removing and replacing in the input file.
                          NOTE: If you do not specify an  explict  output
                                file, you will get the  debug  statements
                                intermixed with  the  optimized  code  on
                                standard output.
    
                -q      - Instructs  MCO  to be quiet,  and not display
                          the startup message when it is executed.

    MICRO-C                                                          Page: 44


    8. THE MAKE UTILITY
    
          The MAKE utility provides a method of automating the  building  of
       larger programs consisting of more that one module. The main  benefit
       of MAKE is that it keeps track of  the  files  that  each  module  is
       dependant on, and will rebuild a module if any of  those  files  have
       been modified since  the  module  was  last  built.  This  frees  the
       programmer from  the  task  of  remembering  which  files  have  been
       changed, and the commands needed to rebuild the dependant modules.
    
       8.1 MAKEfiles
    
             To use MAKE, you must first create a MAKEFILE, which is a  text
          file containing entries for each module in the program. Each entry
          consists of a DEPENDANCY list, and a series of COMMANDS.
    
          8.1.1 MAKEfile Entries
    
                A dependency list in MAKE is a line which contains the  name
             of the module, followed by a ':', followed by the names of  any
             files on which it depends. The module name MUST begin in column
             1.
    
                When MAKE is invoked, it will process each dependancy  list,
             and  will  execute  any  following  commands  (up  to   another
             dependancy list) if (1) the module does not exist,  or  (2)  if
             any of the files to the right of the ':' have a timestamp which
             is later than that of the module. For example:
    
                main.asm : main.c main.h \\mc\\stdio.h
                    \\mc\\mcc main.c main.tmp
                    \\mc\\mco main.tmp main.asm
                    -del main.tmp
    
                In the above example, the 'main.asm' would  be  rebuilt  (by
             compiling and optimizing 'main.c') if either it did not already
             exist, or any of 'main.c', 'main.h' or '\mc\stdio.h' was  found
             to have a later timestamp.
    
                The '-' preceeding the 'del' command prevents it from  being
             displayed. Unless the '-q' option is enabled, MAKE will display
             any commands not preceeded by '-' as they are executed.
    
                NOTE: To enter a single '\' in the MAKEFILE,  you  must  use
             '\\', this is because like 'C',  MAKE  uses  '\'  to  "protect"
             special  characters  which  otherwise  are  used  for   special
             functions (such as '\', '$' and '#'). The first '\'  "protects"
             the second one, allowing it to pass through as source text.

    MICRO-C                                                          Page: 45


          8.1.2 Macro Substitutions
    
                Sometimes in a MAKEFILE, you have a single file or directory
             path that you use  over  and  over  again.  If  it  is  a  long
             directory path, this may  involve  a  lot  of  typing,  and  it
             becomes inconvenient to change that name (if you want to use  a
             different directory etc.) because it is repeated many times.
    
                MAKE includes a MACRO facility, which allows you  to  define
             variable names which will be replaced with a text  string  when
             used in subsequent MAKEfile lines. Names are defined by placing
             them in the MAKEfile, followed by '=',  and  the  text  string.
             Macro names being defined MUST begin in  column  one,  and  may
             consist of the characters ('a'-'z', 'A'-'Z', '0'-'9', and '_').
    
                Whenever MAKE encounters a '$' in the  file,  it  takes  the
             name immediately following, and performs the macro replacement:
    
                mcdir = \\mc
                main.asm : main.c main.h $mcdir\\stdio.h
                    $mcdir\\mcc main.c main.tmp
                    $mcdir\\mco main.tmp main.asm
                    del main.tmp
    
    
                When a macro name is immediately  followed  by  alphanumeric
             text, use a single '\' to  separate  it  from  the  text.  This
             "protects"  the  first  character  of  the  text   from   being
             interpreted as part of the macro name:
    
                mcdir = \\mc\\
                main.asm : main.c main.h $mcdir\stdio.h
                    $mcdir\mcc main.c main.tmp
                    $mcdir\mco main.tmp main.asm
                    del main.tmp
    
                There  are  several  predefined  macro  symbols  which   are
             available:
    
    
                $*      = The full name of the dependant module (name.type).
                $@      = The name only of the dependant module.
                $.      = The full name of each file in the dependancy list,
                          separated from each other by a single space.
                $,      = The full name of each file in the dependancy list,
                          separated from each other by a single comma.
                $:      = The name only of each file in the dependancy list,
                          separated from each other by a single space.
                $;      = The name only of each file in the dependancy list,
                          separated from each other by a single comma.

    MICRO-C                                                          Page: 46


                File names in the dependancy list which are preceeded by '-'
             will not be included in the '$. $, $: $;' macro expansions:
    
                mcdir = \\mc
                main.asm : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mcc $. $@.TMP
                    $mcdir\\mco $@.TMP $*
                    del $@.TMP
    
          8.1.3 MAKEfile Comments
    
                Whenever MAKE encounters the '#' character in the  MAKEFILE,
             it treats the remainder of the line as a comment, and does  not
             process it:
    
                # Define Directories
                mcdir = \\mc
    
                # Build the MAIN module
                main.asm : main.c -main.h -$mcdir\\stdio.h  # Dependants
                    $mcdir\\mcc $. $@.TMP                   # Compile
                    $mcdir\\mco $@.TMP $*                   # Optimize
                    del $@.TMP                              # Delete tmp
    
          8.1.4 Ordering the MAKEfile
    
                MAKE processes the MAKEfile is sequential fashion, with  the
             entries near the top being processed before  the  entries  near
             the bottom. To insure that each module is built  properly,  any
             files appearing in the dependancy list for a module  which  are
             themselves dependant  on  other  files,  should  have  MAKEfile
             entries which occur BEFORE the entries for  the  modules  which
             are dependant on them:
    
                # Define Directories
                mcdir = \\mc
                # Build the MAIN module
                main.asm : main.c -main.h -$mcdir\\stdio.h
                    $mcdir\\mcc $. $@.TMP
                    $mcdir\\mco $@.TMP $*
                    del $@.TMP
                # Build the SUB module
                sub.asm : sub.c -sub.h
                    $mcdir\\mcc $. $@.TMP
                    $mcdir\\mco $@.TMP $*
                    del $@.TMP
                # Link the final file & generate listing
                # NOTE: If either of the above modules is rebuilt,
                #       this entry will be guarenteed to execute.
                prog.hex : main.asm sub.asm
                    $mcdir\\slink $. $@.asm l=\mc\lib
                    $mcdir\\asm $@ -fs

    MICRO-C                                                          Page: 47


       8.2 Directives
    
             Like 'C', MAKE recognizes several "directives" in the MAKEfile.
          These  directives  are  only  recognized  if  they  occur  at  the
          beginning of the input line:
    
          8.2.1 @include <filename>
    
                This command causes the indicated file to be opened and read
             in as the source  text.  When  the  end  of  the  new  file  is
             encountered, processing will continue with the  line  following
             "@include" in the original MAKEfile.
    
          8.2.2 @ifdef <name> [name...]
    
                Processes the following lines (up to @else of  @endif)  only
             if one of the given MACRO names is defined. NOTE: <name> should
             not be preceeded by '$', otherwise its CONTENTS will be tested.
    
          8.2.3 @ifndef <name> [name...]
    
                Processes the following lines (up to @else of  @endif)  only
             if one of the given MACRO name is NOT defined.
    
          8.2.4 @ifeq <word1> <word2> [word3...]
    
                Processes the following lines (up to @else of  @endif)  only
             if the first word matches one of the remaining  words  exactly.
             This is useful for testing the value of a defined MACRO symbol.
    
          8.2.5 @ifne <word1> <word2>
    
                Processes the following lines (up to @else or  @endif)  only
             if the first word does not match any of the following words.
    
          8.2.6 @else
    
                Processes the following lines (up to  @endif)  only  if  the
             preceeding @ifdef, @ifndef, @ifeq or @ifne was false.
    
          8.2.7 @endif
    
                Terminates @ifdef, @ifndef, @ifeq and @ifne.
    
          8.2.8 @type <text>
    
                Displays the following text.
    
          8.2.9 @abort [text]
    
                Terminates MAKE with an 'Aborted!' message. Any text on  the
             remainder of the line will be appended to the message.

    MICRO-C                                                          Page: 48


       8.3 The MAKE command
    
             The format of the MAKE command line is:
    
                           MAKE [makefile] [options]
    
             [makefile] is the name of the MAKEfile to process. If  no  name
          is given, MAKE assumes the default name 'MAKEFILE'.
    
          8.3.1 Command Line Options
    
                MAKE accepts the following command line [options]:
    
                ?       - Causes MAKE to output a short summary  of  the
                          available command line options.
    
                -d      - Instructs MAKE to operate in "debug" mode, and
                          display the commands which it  would  execute,
                          without actually executing them. This provides
                          a method of quickly testing the MAKEFILE.
    
                -q      - Instructs MAKE to be quiet, and not display the
                          informational messages and commands executed as
                          it progresses.
    
        <name>=<text>   - Pre-defines a macro  of  the  specified  <name>
                          with the string value  <text>.  This  OVERRIDES
                          any definition within the MAKEfile,  which  may
                          be used to establish a "default" value.

    MICRO-C                                                          Page: 49


       8.4 The TOUCH command
    
             TOUCH is a small utility program which sets  the  timestamp  of
          one or more files to the current or  specified  time/date.  It  is
          useful as a  method  of  forcing  MAKE  to  recognize  a  file  as
          "changed", even when it has not.
    
             For example, if  you  had  decided  to  "undo"  several  recent
          changes by restoring a backup of 'main.c', the restored file  will
          probably have a timestamp which is  older  than  the  last  module
          which was built. In this case, MAKE would be unaware that the file
          has changed, and would therefore not rebuild the module.
    
             The TOUCH command could then be used to "update" the  timestamp
          of 'main.c' to the current time, causing MAKE to recognize it as a
          changed file.
    
                                  TOUCH main.c
    
             You could also use TOUCH to force rebuilding of several files:
    
                           TOUCH main.c sub1.c sub2.c
    
             Or even ALL '.C' files:
    
                                   TOUCH *.c
    
             TOUCH can also be used to set the timestamp of  a  file  to  an
          arbritrary value, this may be useful  to  PREVENT  a  change  from
          causing an update:
    
                         TOUCH main.c t=0:00 d=31/10/80
    
             NOTE: Use of the 't=' or 'd=' parameters to  TOUCH  allows  the
          possibility that a changed file  will  go  unnoticed.  CAUTION  is
          advised.
    
             The MSDOS  implementation  of  TOUCH  supports  '-h'  and  '-s'
          options, which cause it to set  the  timestamp  of  HIDDEN  and/or
          SYSTEM files. If these options are not used, TOUCH will not affect
          those types of files.




                                    MICRO-C

                               TABLE OF CONTENTS


                                                                         Page

     1. INTRODUCTION                                                        1

        1.1 Document conventions                                            2
        1.2 Code Portability                                                2
        1.3 Setting up MICRO-C                                              3
        1.4 The compiling process                                           4

     2. THE COMMAND CO-ORDINATOR                                            5

        2.1 The CC command                                                  5
        2.2 Using multiple object modules                                   7

     3. THE MICRO-C PROGRAMMING LANGUAGE                                    8

        3.1 Constants                                                       8
        3.2 Symbols                                                         8
        3.3 Arrays & Pointers                                              11
        3.4 Functions                                                      12
        3.5 Structures & Unions                                            13
        3.6 Control Statements                                             16
        3.7 Expression Operators                                           18
        3.8 Inline Assembly Language                                       20
        3.9 Preprocessor Commands                                          21
        3.10 Error Messages                                                22
        3.11 Quirks                                                        27

     4. ADVANCED TOPICS                                                    31

        4.1 Conversion Rules                                               31
        4.2 Assembly Language Interface                                    32
        4.3 Compiling for ROM                                              34

     5. THE MICRO-C PREPROCESSOR                                           35

        5.1 The MCP command                                                36
        5.2 Preprocesor Commands                                           37
        5.3 Error messages                                                 40

     6. THE MICRO-C COMPILER                                               42

        6.1 The MCC command                                                42

     7. THE MICRO-C OPTIMIZER                                              43

        7.1 The MCO command                                                43

     8. THE MAKE UTILITY                                                   44


    MICRO-C                                                Table of Contents

                                                                         Page
        8.1 MAKEfiles                                                      44
        8.2 Directives                                                     47
        8.3 The MAKE command                                               48
        8.4 The TOUCH command                                              49