SEEKTEST

    
                        A Hard Disk Benchmark In Turbo C




                                  Ryle Design

                   P.O. Box 22, Mt. Pleasant, Michigan  48804

                             CompuServe 73047,1765




 
                                 Introduction

SEEKTEST is a program written in Turbo C to very accurately measure the seek
time of a hard disk installed in an IBM compatible personal computer running
the MSDOS operating system.  By using BIOS interrupt services and a very
high resolution timing methodology, a very meaningful measurement of hard 
disk seek performance can be made that reflects "real world" operating
conditions.  

The test measurements are not destructive to the data on the device under
test.  However, it is essential that this test (or any other disk intensive
benchmark or diagnostic) should only be run on storage devices that are fully
backed up in case of failure.


                                Distribution

The distribution you have received should contain the following:

    SEEKTEST.DOC    This document.
    SEEKTEST.C      Fully commented Turbo C source code.
    SEEKTEST.EXE    Small memory model executable.

NOT included in this distribution is the library containing the high 
resolution timer functions, which is only required if you wish to modify
the source code and recompile the executable.


                        High Resolution Timer Toolbox

SEEKTEST uses TCHRT, the Turbo C High Resolution Timer Toolbox from Ryle 
Design.  A shareware evaluation copy of TCHRT is available in DL 5 of
BPROGB on CompuServe as TCHRTV.ARC.  Various BBS systems may also have
TCHRTV.ARC or TCHRTV2.ARC, which are functionally identical.  These
archives hold version 2 of TCHRT, and contain files with datestamps from
1989.  Version 1 of TCHRT was distributed as TCHRT.ARC in 1988 and will
not link correctly with SEEKTEST.C.

Briefly, TCHRT gives the programmer 100 software timers each with one
microsecond accuracy.  The timer engine calibrates itself to the host PC
speed at run time, and can generate a detailed summary report of all timer
activity.  Precise timing of BIOS interrupts 10h (video services) and 13h
(disk services) is also available, and the timer calls can be used inside
user written interrupt handlers.  TCHRT is an ideal tool for both high 
resolution execution profiling and embedded timer applications.  Registered 
users receive complete source to the timer libraries and example programs 
that illustrate execution profiling, BIOS interrupt timing, and hardware 
interrupt triggered timer activation.  TCHRT registration is $7.50, and a 
form to order TCHRT is provided as the last page of this document.


                                 Seektest Usage

At the DOS prompt type SEEKTEST, and execution will begin.  The system is
checked for physical hard disks present, and the user is prompted to test
any disk found, or exit.  Measurements are made of single track and average
to all tracks seek time, as well as an estimate of software overhead (BIOS
interrupt and controller microcode) for each seek.  The test is completely
non-destructive to the data on the media.


                                      -1-









                            TCHRT Registration Form



    Name __________________________________________________________________

    Address _______________________________________________________________

    City/State/Zip ________________________________________________________

    Daytime Telephone _____________________________________________________

    CompuServ ID (for tech support) _______________________________________

    Where did you get your copy of TCHRT?  ________________________________

    What is your primary use of TCHRT? ____________________________________

    Comments regarding this product _______________________________________

    _______________________________________________________________________

    _______________________________________________________________________

    _______________________________________________________________________


    Check Products desired:


    ____    TCHRT Registered Version (Turbo C V2.0) .................  7.50

    ____    TPHRT Registered Version (Turbo Pascal V5.0) ............  7.50

    ____    MSCHRT Registered Version (Microsoft C V5.1/MSDOS) ......  7.50

    ____    All three of the above (save 2.50) ...................... 20.00


            Subtotal ................................................ _____

            
            Michigan residents add 4% sales tax ..................... _____


            Total enclosed (__check __money order) .................. _____


    Remit to:   Ryle Design
                P.O. Box 22
                Mt. Pleasant, Michigan 48804




                                      -2-