SPA:WN
                   Structured Programming Automated:
                           Warnier Notation

                            Kenneth Conrow
                    University Computing Activities
                             Cardwell Hall
             Kansas State University, Manhattan, KS 66506
                              April 1987

                               CONTENTS

     1. Notes to the Reader

     2. Motivation and Objective

     3. Overview of SPA:WN's Capabilities

     4. Structured Programming

     5. Warnier Diagram Conventions

     6. Simplest Input

     7. Examining Results

     8. Operational Cycle

     9. Automatic Code Generation
        A. SPA:WN Punctuation Substitution  . . . . . . .   9-4
        B. Structure Body Positioning . . . . . . . . . .   9-4
        C. Disambiguation . . . . . . . . . . . . . . . .   9-6

    10. Target Language Adjustments
        A. SPA:WN Comment Dangers . . . . . . . . . . . .  10-1
        B. Statement Formatting . . . . . . . . . . . . .  10-1
        C. Handling Unstructured Languages  . . . . . . .  10-5

    11. Auxiliary Fields

    12. Diagram Layout
        A. Control Parameters . . . . . . . . . . . . . .  12-2
        B. PASCAL Constants . . . . . . . . . . . . . . .  12-3

    13. Helpful Hints
        A. Null Comments as Terminal Children . . . . . .  13-1
        B. Continuation Statements  . . . . . . . . . . .  13-2
        C. Creating Depth-First <fn>.SRC File . . . . . .  13-3
        D. Recursion, State Machines, Parallel Processing  13-3

    14. Program Algorithm

    15. Desperate Topics for Desperate People
        A. Retrofitter Concept  . . . . . . . . . . . . .  15-1
        B. Delimiter Saturation and Escape Characters . .  15-2

    16. Glossary

    17. Bibliography


                      1. NOTES TO THE READER

If the concepts of structured programming and the use of Warnier
diagrams are new to you, you will wish to make frequent reference
to the glossary which closes this document for definitions of
terms which may be unfamiliar.

If you already know structured programming and top-down design
techniques you can probably skip to Chapter 5 or 6, where matters
specific to SPA:WN begin.

A program can be very large and very complex.  Preparing a
Warnier diagram to represent such a program can often seem
overwhelming.  Don't be discouraged.  Everything doesn't have to
be done at once.  You do a very few things at a time.  You
concentrate on one aspect, then another, then still another.
Gradually a sound design and good documentation build up,
little-by-little.

Let the inherent features of your problem dictate what is
important to do first and what you can leave until later.  There
is no need to feel that you have to do everything at one time.
Just the opposite is true: you have to attack a large problem in
small increments, or you can't possibly manage it correctly.
When the design is complete, it will all be in front of you in
the completed Warnier diagram.  As long as your approach gets you
to a good design, it won't matter at all what the detailed
history of its construction was.  Often there are a number of
good approaches to a problem, any one of which will result in a
satisfactory program.

Concentrate as much as possible on top-down design and creation
of a readable Warnier diagram.  Don't worry about trivial errors
you may be committing while making correct fundamental decisions.
Trivial errors are easily discovered and corrected later.  It is
the serious design oversights and misconceptions that you want to
avoid early in your design work.  Vary your work by deliberately
shifting your attention from time to time to different aspects of
the problem.  This reduces the chance that some unexpected aspect
escapes your attention.

As the design evolves, the focus of the work changes.  The
systems you are working with will help discover errors at every
level: early on, SPA:WN diagnostics discover errors you have made
in its input syntax; the Warnier diagram itself is the medium for
reviewing the logic and discovering errors in the logical design;
later, compiler diagnostics find errors in the target language
syntax; still later, test runs reveal semantic difficulties or
details of record, report, or screen layout which need attention.

There is no practical limit to the amount of imagination which
can be applied in the use of SPA:WN.  When you have mastered
SPA:WN, you can embark on journeys of your own devising by
creating conventions and notations never yet imagined; you can
help yourself create readable self-documenting Warnier diagrams
and their corresponding programs or systems at a level of
sophistication far beyond your current reach.  You can apply
SPA:WN to create programs in any computer language you may wish.


                   2. MOTIVATION AND OBJECTIVE

Writing a complex program presents a difficult design problem.  A
program is normally presented as a linear series of program
statements.  It can be very difficult to visualize the logical
structure of a complex program from this presentation even if the
program is well-structured and carefully formatted.  What is
needed is a graphic means of presenting a program structure so
that it can be visualized for review and incrementally improved
as design proceeds.  Also needed is a way to easily modify the
logical structure and obtain a new graphical presentation.
Ultimately, the designed program needs to be produced in the form
of the properly ordered sequence of program statements in the
target language.  The Warnier diagram provides the graphical
presentation and SPA:WN provides support for the whole process.

Writing a program (even quite a simple program) which must be
maintained over a long period of time presents similar
difficulties because the passage of time causes details of its
design and its coding to slip from memory.  Again, there is a
need for a graphic, quickly comprehended, presentation of the
program structure for quick recall on the occasion for
maintenance.  The presence of coded target language statements in
a graphically presented logical context is especially valuable in
maintenance work.

The condition of the logical structure at each stage of
refinement is presented in the Warnier diagram.  This makes it
easy to visualize and critique it.  Editing the input file to
effect any required improvements and expansions is usually quite
simple.  Thus, SPA:WN ameliorates both the difficulty of
visualizing the logical structure (to critique it) and the
difficulty of manipulating the developing entity (to improve it).

The hand generation of Warnier diagrams soon becomes very
tedious.  If a design requires many stages of refinement, you
quickly tire of drawing and designing.  (And no sane person would
ever persevere to hand draw Warnier diagrams so detailed as to
contain target language statements.)  Merely automating the
drawing of the diagrams reduces the tedium of careful, prolonged
design, and invites a much more thorough and protracted design
phase.  Fresh diagrams are obtained with very little effort.  The
psychological lift you gain from a fresh version of the diagram
encourages continued design effort.  Numerous small improvements
in design often clear the way for major breakthroughs.
Remarkably more polished programs result from systematic use of
SPA:WN than can otherwise be achieved.

The capstone is achieved when the design is completed down
through statements of the target language.  Then SPA:WN can be
requested to produce the target language source code in the
sequential order required for compilation or interpretation.

SPA:WN is quite unlike other approaches to automatic programmming
(1), which tend to be knowledge-based, or to consist in a very
high level language.  SPA:WN is essentially a design medium, with
sufficient flexibility to create programs in any target language.


                      MOTIVATION AND OBJECTIVE            2-2

Careful use of SPA:WN as a program design and development tool
can result in rapid production of well-designed, well-documented,
easily-maintained, structured programs.  SPA:WN can be misused or
underused, so its use does not guarantee a breakthrough in
programmer productivity.  The goal for the programmer is to
employ the features and facilities of SPA:WN in such a way that
the resulting program is well-designed, self-documented,
well-structured and therefore easily maintained.  Experience
certainly indicates that this can be done.  While most of the
productivity gain from use of SPA:WN is due to improved design
and resulting improved program structure, part is due to an
increased rate of development due to the support provided by
SPA:WN.  Thus SPA:WN provides the environment for increased
programmer productivity, and programmer self discipline is
required to reap the potential benefits.

We may comment here that the structured discipline supported by
SPA:WN as a programming tool very quickly results in a programmer
world-view which is strikingly language-independent.  The general
structure of a program to do a specified task is nearly the same
independent of the language to be used, even though various
language features change details considerably.  Since every
program is composed of sequential statements plus constructs for
repetition and alternation, the major design-level questions
about a target language are: "What is the syntax of its comment
statements?", "What are its structured constructs?", and "What
are its declarative and executable statements?".  The principal
impact of the choice of language is its effect on the amount of
work it takes to design and code a program.  If the programming
language is very high level, the detail to which design must be
pushed before language statements can be used to implement the
task is much less than is the case for a relatively low level
language where the design must be developed in much more detail
before the programming language's level of competence is reached.


               3. OVERVIEW OF SPA:WN'S CAPABILITIES

SPA:WN is an acronym for Structured Programming Automated:
Warnier Notation.  As the name suggests, it supports the
development and coding of structured programs.  It uses Warnier
diagrams to present the program under design or maintenance.
While it is probably primarily useful in program and computer
system design, it can perfectly well be used in much broader
contexts wherever some graphical means of visualizing the
sequential and hierarchical relationships between the components
of some complex system is required.

SPA:WN automates the programming process in two major ways: 1) it
automatically produces and paginates Warnier diagrams which may
be printed for detailed study; 2) it automatically produces code
in the target language which may be compiled and executed just
like program code generated in any other way.  (The target
language is the computer language in which the Warnier diagram is
couched and in which the completed program is produced.)  SPA:WN
works most easily with relatively high-level, structured
languages as target languages, but it can be used even with
low-level languages devoid of structured constructs.  (Structured
languages are languages which provide structured constructs (like
BEGIN ...  END, IF ...  THEN ...  ELSE, and DOCASE ...  CASEi ...
OTHERWISE ...  ENDCASE).  See Chapter 4 for more details about
structured constructs.)

Continuity is the key virtue of SPA:WN.  The whole design,
coding, and maintenance process is a continuous one, with no
shift of medium or abandonment of outdated materials at any
stage.

Target language comments should always be used in a Warnier
diagram.  Use of comments is most cogent at the beginning of a
design job where English language descriptions of the job at hand
from an overall perspective are used.  These comments become an
integral part of the final program, serving either as parents for
branches of the logic or as explanatory notes accompanying some
sequence of executable statements.  Serving as the very medium of
the initial design process, these comments later serve both at
the Warnier diagram level and at the source code level as
essential documentation.  Use of target language comments in the
early design stages enables continuity in design, coding, and
target language code generation.  If target language comments
weren't used to contain these early descriptive statements, the
target language code wouldn't be acceptable to its compiler, and
the early descriptions would have to be discarded.


                  OVERVIEW OF SPA:WN'S CAPABILITIES       3-2

For continuity then, the design is first developed in comments of
the target language.  The design is considerably elaborated in
English form in them.  Later a few executable statements of the
target language are employed as the design develops to a
sufficiently detailed level.  As design continues, more and more
executable statements of the target language can be put into
place.  Finally, the design is so detailed that every branch
culminates in and every control structure exists as executable
statements of the target language.  Thus the design stage
overlaps with and yields to the coding stage.  Since coding is
completed in the design medium, design changes remain possible
and convenient throughout coding.  There is no feeling of
struggling through a distastefully long, separate design stage.
The result of the combined design and coding process is target
language source code which may be compiled.  The SPA:WN input
stream is kept and becomes the basis for maintenance throughout
the lifetime of the program.

When a control structure of a target language is included in a
Warnier diagram, both its opening portion and its closing portion
are included in the same node.  A special separator (three
hyphens on a line by themselves, which appear as '%---%' in the
input stream; see Chapter 9, below, for details) is used to
indicate to SPA:WN and to the reader of the printed Warnier
diagram where the body of a structured construct fits into the
parental control structure.  Examples of strings representing
structured constructs in three target languages are 'DO I=1 TO
10;%---%END;', '>DO 90 I=1,10 %---% 90>CONTINUE', and 'FOR I:=1
TO 10 DO BEGIN %---%END;'.

Auxiliary fields may additionally be used to annotate a Warnier
diagram so that it completely documents the program.  It is
almost always possible to devise uses of auxiliary fields to
provide any annotation which might be desired.  Design-level
labels, repetition counts, indications of mutually exclusive or
coupled execution of program branches, marks on nodes which are
continuations of statements in the target language, indications
of initiation and rejoin points of parallel execution of program
branches, and short comments are among the possible uses of
auxiliary fields.

You can often take opportunities to insert or delete optional
levels containing comment nodes so as to better distribute the
nodes of a diagram on a page or to facilitate pagination of the
overall diagram by SPA:WN's automatic pagination mechanism.  A
little of this activity soon personalizes the Warnier diagram of
a program on the page to your own tastes, and seems very
worthwhile.

Naturally, use of suggestive variable names and utmost clarity in
the source code statements contribute to readability and
self-documentation.

With all these strategies, the SPA:WN input file becomes the form
in which the program is permanently kept, because both a very
complete, readable documentation and the target language source
code can be generated on demand from this single source.


                  OVERVIEW OF SPA:WN'S CAPABILITIES       3-3

When run, SPA:WN produces a diagnostic file.  If the input is
error free in SPA:WN's view, there is produced a file which
contains the generated Warnier diagram, (optionally) a file of
generated source code, and (optionally) a file which is a
depth-first reordering of the input file.  The format of the
generated Warnier diagram and of the generated target language
code can be varied under parametric control to meet many
particular requirements or preconceptions.

Differentiation between punctuation marks used in the target
language and punctuation marks used to delimit the fields of the
input records for SPA:WN is achieved by providing for
redefinition of the four SPA:WN punctuation marks so that they do
not interfere with those of the target language.  This enables
the use of SPA:WN to design and write programs in any computer
language.  (See Chapter 9 for more details.)


                    4. STRUCTURED PROGRAMMING

The basis of structured programming resides in the fact that any
programmable task can be accomplished by use of only three
elementary control structures: SEQUENCE, ALTERNATION, and
REPETITION.  These fundamental structures can be nested into
arbitrarily deep constructs to achieve a program's ends.  By
restricting the structure of a program to these simple building
blocks, baroquely complex programs are avoided.

A sequence is just a series of statements entered at the top and
executed in order without branches or exception right down to the
bottom.  It is so simple that it is almost hard to recognize as a
structure.

Alternation is a structure in which some one of a set of
alternative statements or code passages is selected for
execution.  None of the other alternatives are executed.
Familiar examples of alternation are the IF ...  THEN ...  ELSE
...  ENDIF and the CASE constructs.

Repetition (or iteration) is a construct in which a statement or
code passage (the body) is executed repeatedly under control of
some counter and/or logical expression whose value is updated
within the body or between successive executions of the body.

Structured languages are languages which provide control
structures for alternation and repetition as part of the syntax
of the language.  (All practical languages provide for sequence;
it is really hard to imagine a language without sequence as a
control feature.)  PASCAL, PL/I, dBASE, TRUE BASIC, FORTRAN 77,
and many others are structured languages.  Different structured
languages vary in the number and varieties of alternation and
repetition structures which they provide, so not all structured
languages are equally easy to use.

Some structured languages do not provide any means affecting the
flow of control other than by their defined structured
constructs.  There is no mechanism for an arbitrary branch to
another segment of code, i.e. there is no GOTO statement.  This
makes it very difficult for a programmer to create wildly
undisciplined programs in these languages.

The antithesis of a structured language is a language which
requires the use of explicit branch commands or GOTO statements
to control the flow of execution in the program.  These languages
permit undisciplined use of GOTO statements.  The result can be
"spaghetti code", which is virtually impossible to understand or
maintain.

Structured programming is sometimes associated with
"GOTOlessness" and unstructured programming with "GOTOfulness",
but this is quite a narrow view.  Even when using a language
which does not provide them in its syntax, you can simulate the
alternation and repetition constructs by adopting a restricted
set of patterns of labels and conditioned GOTO statements.  Using
these, you can write a program which is perfectly structured by


                       STRUCTURED PROGRAMMING             4-2

employing nested instances of these adopted structures.  This
approach confers the logical advantages of being structured
(though it may not be quite so immediately readable) in spite of
containing GOTOs.  It is the restriction of program structure to
nested instances of sequence, alternation, and repetition which
makes a program structured, not the presence or absence of GOTO
statements.

When a program is properly structured, the flow of execution
through it when it is executing is easy to understand from the
structure of the program as it appears on paper.  To say the same
thing more elegantly, there is a close correspondence between the
program's static structure and its dynamic structure.  Structured
code results in this.  It makes the program easier to understand
than an unstructured program would be.  The absence of arbitrary
jumps from one place to another in the code implies the absence
of such arbitrary jumps at run time.  For a structured program
the chronological order of activity at run time matches its
sequence of presentation on the page (i.e. in the Warnier
diagram).

The approach to take in design of a structured program is a
top-down approach.  A top-down approach is a divide-and-conquer
approach.  You start with high level, English statements of the
task to be solved, couched as comments in the target language.
You divide the overall task into an ordered sequence of subtasks,
which together will perform what is required.  These too will
likely be in English and be incorporated as comments.  The more
complex of these will again be subdivided into simpler tasks.
Eventually the tasks are simple enough to be specified as
executable statements of the target language and you have begun
coding the program which is required.  The successful division of
high level tasks described in English into subtasks which can
eventually be programmed isn't always obvious.  It can require a
thorough knowledge of the capabilities of the target language, as
well as a willingness to cut, try, rearrange and restart when a
blind alley is encountered during the design.

The power of the top down process is twofold: (1) it gives
intellectual assistance from the "divide-and-conquer" approach in
that it permits dealing with problems at an abstract level until
it is time for more concrete solutions to be developed, by which
time the context is established and correct concrete solutions
are possible; and (2) it results in structured code, because at
each level of the top down design it is natural to employ only
sequence, iteration, and alternation in the solution to the
design problem at its level of abstraction.  Each lower level of
design produces the body of a structured construct selected at a
higher level, so nested structures arise naturally.  Since these
three basic program elements are sufficient to produce any
computer program, the top-down design methodology is sufficient
to produce any computer program.


                       STRUCTURED PROGRAMMING             4-3

There are quite a number of different design techniques which
have been developed to assist in the process of reducing a
problem to a structured solution.(3,6)  Any of these methods will
help reduce the amount of trial and error involved in the design
process.  SPA:WN is not wedded to any particular design
methodology; its use does not require that any design methodology
be used at all.  SPA:WN can be used to express the emerging
design in a readable and understandable form, no matter what
design approach is being used to tease a design out of the
problem requirements.  But the user faced with a large design
task would be foolish not to learn about one or more of these
design techniques and apply them to his problem.

One long-standing design approach is called HIPO: Hierarchical
Input Process Output.  In the view of this approach, the activity
at every logical level consists of preparing to do something
(input, in some sense), doing it (processing), and cleaning up
afterwards (output, in some sense).  When attempting to solve a
problem in a top-down design, keeping this simple view in mind
will often help to suggest an approach to its further
decomposition.


                  5. WARNIER DIAGRAM CONVENTIONS

A Warnier diagram(2,3) is quickly described as a tree lying on
its side, with its root at the left and its branches and leaves
extending to the right.  The terminology of family trees and
natural trees are often used and intermixed.  The root is the
parent of the whole tree.  The first generation is arrayed
vertically to the right of the root with a bracket indicating the
extent of the set of children.  Any of these children might be a
parent in turn, with a bracket and a new set of children to its
right.  After a few levels there could be a great many branches.
When the farthest extent of a branch is reached, and there are no
more generations of children, we are at the leaves of the tree.
Each individual element of the tree is often called a node (a
term from graph theory, since a tree is just a particular sort of
graph).  Generally, each node in SPA:WN's view is a statement or
comment in the target language, although sometimes a Warnier node
might be just a part of a continued statement in the target
language.

The time sequence of execution of the nodes in a Warnier diagram
is top to bottom at each level.  The higher statements in a
bracket are executed before the lower statements in a bracket.  A
node's subtree is usually executed after the node itself (but see
Chapter 9.B for further discussion).

As an example, there follows a simple Warnier diagram, in which
the logical program is divided into three sections, A, B, and C.
Section B is further divided into two parts.  Sections A, B and C
are the children of the node 'Program' as Parts 1 and 2 of
Section B are children of the node 'Section B'. The order of
execution is A, B1, B2, C, or depth-first, mainly preorder.

Simple Warnier Diagram Example
                                      .-
                 .-                   ^    Body of Section
                 ^    Section A      <     A
                 ^                    ^
                 ^                    '-
                 ^                    .-
                 ^                    ^    Part 1 of
                 ^                    ^    Section B
      Program   <     Section B      <
                 ^                    ^    Part 2 of
                 ^                    ^    Section B
                 ^                    '-
                 ^                    .-
                 ^                    ^    Body of Section
                 ^    Section C      <     C
                 '-                   ^
                                      '_



                     WARNIER DIAGRAM CONVENTIONS          5-2

The layout of the diagram illustrates the logic of the program in
the following way.  Starting at any internal node, the reason for
doing something (the WHY?) can be found by looking to the left --
the comments and control structures among the ancestors indicate
what business this branch of the tree accomplishes.  The way of
doing something (the HOW?) can be found by looking to the right
-- in that direction appear the more detailed descriptions and
statements employed to effect a given task.  The time sequence
(the WHEN?) is judged by looking at the vertical context in which
a given node appears.  This display of the logic in two
dimensions results in a much greater degree of visualization than
the conventional linear presentation of code.

The activities which occur together at a particular level of the
diagram tend to be of roughly equal importance.  If you wish only
a gross overview of program logic, you can focus on only a few
top levels.  If you want to concentrate on a particular set of
details, you can look at some detailed portions of the diagram.
If you need to find your way to a particular passage of code in a
maintenance situation, the hierarchical structure and the
readable comments at all levels let you quickly find your way
down to the program segment at issue.  No matter at what level in
the Warnier diagram an error is committed, it is easy to examine
it in its own proper context because of the carefully developed
and documented hierarchical arrangement.(4)

The opening and closing portions of simple structured constructs
are kept together in a single node in the Warnier diagram.  If
the structured construct is more complex (like CASE constructs or
cascaded IF ...  ELSE IF ...  ELSE IF ... sequences), the
components are best placed in a series of consecutive nodes at a
particular level in the diagram in order to maintain them in a
localized relationship to one another.

Rearranging program segments is very error prone in linearly
depicted programs because of the difficulty of finding matching
components of structured constructs.  These rearrangements are
mechanically easily performed in the SPA:WN input stream, because
the inclusion of all parts of a structured construct in a single
node or localized passage of nodes implies that there is no
searching for separated parts of a construct.  Since each program
branch is guaranteed to be logically self-contained under the
precepts of structured programming, every branch of the tree at
every program level can be moved as an independent unit without
fear of tangling any spaghetti.

One soon becomes accustomed to manipulating branches of trees as
units, thereby making needed structural changes at any level of
depth.  The only thing requiring care is that internal nodes
(i.e. nodes which have children/are not leaves) must not be moved
about too freely.  As we are about to see, the input stream must
introduce the nodes in top-down order, which means that neither
the child-instance nor the parent-instance of an internal node
can be moved so far that its child-instance occurs later in the
input file than its parent-instance.


                     WARNIER DIAGRAM CONVENTIONS          5-3

Since the effect of representing a program structure in a Warnier
diagram is to clearly represent the logical relationships among
its parts, the motivation for breaking a program up into a number
of subroutines is very much decreased.  The principle motivation
for breaking out page-sized subroutines is to confer readability
at various levels of logic.  The Warnier diagram and its
automatic pagination by SPA:WN perform this service in a
different way.  Indeed, arbitrarily breaking out subroutines just
out of habit or a feeling of duty breaks up the correspondence
between the static and the dynamic structure of the program
because the body of the subroutine does not appear where it is
logically executed.  This is certainly unnecessary and perhaps
counterproductive.  Large programs without subroutines are quite
readable in Warnier diagram form if care is taken in the other
dimensions, e. g. careful commenting, careful variable choice,
use of clear constructs, etc.

The other motivation for use of subroutines arises, of course,
when some operation is commonly required from various points in a
program.  A subroutine is certainly the way to provide the
operation.  It avoids duplication of code and raises the logical
level of the rest of the code to provide lower level subroutines
which provide common support operations.

Subroutines are very easily provided for in SPA:WN.  They can be
handled as separate Warnier diagrams by treating each subroutine
as an individual Warnier diagram, each with control parameters
(at least a title specification) and its own 'endwarnierdiagram'
keyword.  A sequence of such individual diagrams will produce a
series of external subroutines.  The input stream for such an
approach would appear as follows.  (Details will be explained
shortly.)  The output would simply be four separate Warnier
diagrams, each showing the logical structure of each subroutine.

        title subroutine a
          rootnode for a,,
            ,<body of subroutine a>,;
        endwarnierdiagram
        title subroutine b
          rootnode for b,,
            ,<body of subroutine b>,;
        endwarnierdiagram
        title subroutine c
          rootnode for c,,
            ,<body of subroutine c>,;
        endwarnierdiagram
        title main routine
          rootnode for d,,
            ,<body of subroutine d>,;
        endwarnierdiagram


                     WARNIER DIAGRAM CONVENTIONS          5-4

Alternatively, the subroutines can be created as internal
subroutines collected together at the beginning or end of the
diagram which represents the main-line program.  A comment or
hierarchy of comments can indicate where the subroutines are from
the highest level of the diagram, so that discovering any
particular subroutine is a simple matter of going down through
the guiding comments from the root node on the first page of the
whole Warnier diagram.  You should adopt a standard way of
including a subroutine section as part of an overall program
structure.  The general appearance of the Warnier diagram in such
an approach might be as follows:

                                    .-                .-
                                    ^   procedure a  <   body of a
                                    ^                 '-
                 .-                 ^
                 ^   (*subroutine   ^                 .-
                 ^   segment*)     <    procedure b  <   body of b
                 ^                  ^                 '-
                 ^                  ^
                 ^                  ^                 .-
program sample   ^                  ^   procedure c  <   body of c
---             <                   ^                 '-
end sample       ^                  '-
                 ^
                 ^                  .-
                 ^   begin          ^   body of main
                 ^   ---           <    procedure
                 ^   end            ^
                 '-                 '-


                        6. SIMPLEST INPUT

The simplest input for SPA:WN arises when designing a system in
pidgin language.  No target language code is wanted.  There are
no complicating features.  The diagram is to have unpunctuated
phrases in its nodes, and no use of auxiliary fields (annotation)
in the diagram is desired.  There are only parent nodes, child
nodes, SPA:WN punctuation characters, and a little control
information in this simple input stream.  Commas and semicolons
are used as the punctuation characters which delimit the input
fields for SPA:WN.  These delimiters actually appear in the
input.  In such a case, the input stream is compactly represented
as follows:

        (title  <some appropriate title for the diagram>
                (<parental node value>,,
                        (,<internal child value>,,) ...
                         ,<final child value>,;) ...
        endwarnierdiagram) ...


The angle brackets, parentheses, and dots in this picture are
metasymbols -- they provide information within the description
but are not used in the actual SPA:WN input stream.  The angle
brackets ('<' and '>') enclose phrases which indicate what
appears in each position in the input stream.  The whole
bracketed phrase is replaced in the input stream by a value of
the indicated type.  The parentheses enclose entities which may
be repeated a varying number of times in their context.  A series
of dots represents the repetitions of the parenthesized entity
just preceding.  Each nested parenthetical expression and set of
dots is replaced in the actual input stream by a series of
instances of information at that level.  The words 'title' and
'endwarnierdiagram' are not metasymbols; they are real control
keywords which tell SPA:WN something.

The foregoing merely shows that the input stream to SPA:WN is
composed of repetitions of three kinds of nested entities:
diagrams, families, and child nodes.  In words: a number of
Warnier diagrams can be specified in a single input file, with
each bearing a 'title' specification to start it off and each
closed with the 'endwarnierdiagram' keyword.  There can be one or
more families (i.e. parents, each with a set of children) in a
sequence which together constitute a particular Warnier diagram.
There can be zero or more internal child nodes between the
parental node and the final child node of any family.

As you see, to define a family you just write the parental node
delimited by two trailing commas, and then the list of its
children.  All but the last child are delimited by a leading
comma and two trailing commas.  The final child is delimited with
a final semicolon in place of the final comma.  Each node appears
on a separate input line.

For example, the input stream which results in the first Warnier
diagram of Chapter 5, above, is as follows.


                           SIMPLEST INPUT                 6-2

 title Simple Warnier Diagram Example
  Program,,
    ,Section A,,
    ,Section B,,
    ,Section C,;
  Section A,,
    ,Body of Section A,;
  Section B,,
    ,Part 1 of Section B,,
    ,Part 2 of Section B,;
  Section C,,
    ,Body of Section C,;
endwarnierdiagram

Another fairly generic example of a SPA:WN input stream and the
resulting Warnier diagram appears early in Chapter 9.

Another possible feature in SPA:WN input streams are comment
lines, as follows.

   *<SPA:WN comments appear anywhere, bear an asterisk in column 1>

SPA:WN comments are not output in the Warnier diagram, and are
output collected together (with leading asterisk stripped) at the
front of the target language source code file.  Because they do
not appear in the Warnier diagram, SPA:WN comments are of little
direct use in application design and maintenance.  They are best
reserved for notes about punctuation and structured construct
conventions of a given application or for providing flags useful
in maintaining the input stream.  A block of narrative comments
at the beginning of the SPA:WN input is transmitted as a block to
the target language output stream.  In this connection they can
be useful as a documentation feature.

It is useful to employ indention in the input stream because it
improves its editability while the program is under development
and maintenance.  However, there are no indention requirements or
limitations with the exception that an asterisk in column 1 marks
a SPA:WN comment, so placing an asterisk there must be avoided if
a diagram node is meant.  This is a problem only if diagram nodes
begin with asterisks, as is the case with comments when SNOBOL or
dBASE are the target languages.

The only thing the above picture doesn't make clear is that input
must be top-down, i.e., a node must appear in its as-child role
before it appears in its as-parent role.

The structure of the whole Warnier diagram is built up by using
copies of nodes which have already appeared as children in a new
role as parents of the next generation.  Some or all of any
generation of children may be repeated in a parental role, with
further descendants, and so on.  The only requirement is that,
excepting the root node, a node must have already appeared
uniquely as a child before it can be used as a parent.  Another
way of saying this is that the Warnier diagram must be input in
top-down order.  Only the root node may appear without having
been specified previously.


                           SIMPLEST INPUT                 6-3

The lexical identity of the two appearances of the node (first as
child and again as parent) is the basis for identifying them with
one another, which enables SPA:WN to build the entire structure
of the Warnier tree.  The uniqueness of parental nodes is
required so that there will be no ambiguity in associating
node-as-parent with node-as-child.

When doing a pidgin language design, it is usually possible to
devise node wordings which are all unique, so that there is no
problem about the ambiguity which would arise if there were two
lexically identical nodes.  If the problem does arise, and can't
be solved by rewording, then you must take recourse to the
disambiguation mechanism which will be detailed below in section
9.C.

The SPA:WN input stream is prepared as a file with the extension
'.WAR' (for Warnier).  Use any filename you may like.  The
preparation of this input stream is done using any text editor or
word processor capable of operating in "non-document mode".  The
preparation of a copy of a previous child node to serve in its
new role as a parent is accomplished by copying the as-child
node, deleting the leading comma, and (if the node was a last
child) converting the trailing semicolon to a trailing comma.
This procedure ensures that there will not be any typos
introduced which would inadvertently prevent the identification
of the two copies of the node with one another.  It also saves
typing.  If you are able to design in a very disciplined top-down
order, whole sets of children can be copied and converted to
parent nodes in batches (and any unneeded ones later deleted).

When the *.WAR file is far enough along that you'd like to see
what you've got so far, you can invoke the SPA:WN system simply
by issuing 'SPAWN <fn>', where <fn> is the filename you assigned
your input file.  The SPAWN.BAT file will run, using your
<fn>.WAR file as its input file, and producing 4 output files,
<fn>.ECH, <fn>.DIA, <fn>.PUN, and <fn>.SRC.  Some of these may be
empty, depending on the success of the diagnostics performed
during the input phase and on the parameters delivered to the
program.


                       7. EXAMINING RESULTS

The first thing to do after a SPA:WN run is to look at the
<fn>.ECH file the run produced.  This file contains an echo of
the input stream and contains diagnostics for any errors which
are detected during processing.  If there are no errors, or if
the errors are judged to be minor, the production of the diagram
is done.  However, most errors are deemed so serious that the
diagram is not produced.  Instead, input is completed and all
diagnostics are produced before shutting down.  Sometimes errors
have so devastating an effect that the program is unable to
complete the input process, and a Turbo Pascal error message and
crash results.  If this happens, look at the <fn>.ECH file,
correct the errors which were detected, and rerun SPA:WN.  Don't
regard crashes which are presaged by error messages in <fn>.ECH
as errors in SPA:WN.  Work to get rid of the error messages, and
the crashes will stop.

One of the first possible occasions for error is the transition
from parameter interpretation to diagram processing.  This
transition is marked by three blank lines in the <fn>.ECH file.
The title and parameter records and one copy of the root node
should all appear before these three blank lines.  The root node
should appear again after the three blank lines where it properly
belongs as the first node of the diagram proper.  If you have
mis-spelled a parameter, parameter interpretation will halt
prematurely, with almost certainly disastrous results.  Watch for
this as a possible source of difficulty.

Most messages which SPA:WN produces upon discovering an error
appear immediately after the input record which provoked them.
Every error is prefaced with 5 asterisks.  To find your errors
quickly, edit the <fn>.ECH file and use the search capability of
your editor or word processor to skip right to each error
instance.

Oversize fields, duplicate nodes used as parents, extra fields,
missing punctuation, illegal infix fields, and attachment
failures (among others) are diagnosed.  Errors often have a
cascading effect: in particular, if the last child of a family
has an error, the program keeps expecting children until a valid
last child is found, and, if a parent has an error, the program
keeps expecting a parent until a valid one is found.  This
behavior can lead to a number of error messages from a single
cause.

The error messages are almost entirely self-explanatory, but
there are situations where some insight is required to see what
happened.  One of these is the case where the leading comma of a
child node is omitted.  SPA:WN is expecting a prefix value, which
is limited to a length of 3 characters by default, so when more
than three characters are present it can't tell whether
punctuation is missing or the prefix field is too long.  You
should decide which is the case and supply the leading comma or
shorten the prefix field.  An identical error situation arises
when a last child doesn't bear a closing semicolon.  SPA:WN is
expecting another child when it encounters what is really the
next parent, and gets upset exactly as just described.


                          EXAMINING RESULTS               7-2

When a semicolon appears incorrectly on an internal child, SPA:WN
expects a parent node next.  In the usual case where there is no
prefix field on the next node, it complains that there is an
incorrect leading comma or a null node value.  In the rarer case
that there is a prefix field on the next node, it accepts it as
the node value and then complains that there are too many fields
(3 when it expects 2).  It keeps on with these behaviors until
the next valid parent appears.  The children who are by-passed
during this search for a parent node are lost, and there will
likely be later messages when the lost children are used as
parents stating that the parent is illegal since it hasn't
already appeared as a child.  You just have to clean up the
punctuation and make a fresh run.

The message 'extra fields present' often results from inadvertent
use of a SPA:WN punctuation mark within a node value.  The SPA:WN
punctuation conventions can be redefined (see Chapter 9.A, below)
and program development continued with the new punctuation
conventions.

In short, when unreasonable diagnostic messages appear, check
carefully for punctuation errors.  Most mysterious errors derive
from punctuation errors.

There are many other diagnosed errors.  Some few, including those
which are detected only during target language code generation,
have diagnostic messages separated from the statement responsible
in the <fn>.ECH file.  A portion of the node text is repeated in
the diagnostic to help you identify it.  Another instance of a
diagnostic separated from the <fn>.ECH file arises when a diagram
cannot be completely paginated and this leaves too many columns
to be printed across a diagram page.  This diagnostic appears at
the top of the affected page of the diagram, and the nodes in the
columns off the edge of the page are simply lost.

A successful SPA:WN run contains time stamps indicating when the
run started and when each of the processing phases completed.
These appear at the start and at the end of each diagram in the
<fn>.ECH file.  This is merely informatory material.  You might
be interested to see how the program divides its time among its
various tasks.  Another line of informatory material gives the
number of nodes in the diagram, the number of pages resulting
from pagination, the average number of nodes per page after
pagination, and the number of pagination passes used in all.  (In
some obscure sense, the program assumes 35 to be par for the
number of nodes per page.)

The Warnier diagram is produced in a file called <fn>.DIA.  If it
is too large to be put on a single output page of the current
size, it is automatically paginated as necessary into a number of
output pages.  The pages of the diagram are output in depth-first
order to keep related pages close together.  Each page bears the
title specified after the 'title' keyword in the control records.


                          EXAMINING RESULTS               7-3

After the title, there is printed a Dewey Decimal notation which
indicates where in the overall diagram structure the root node
for this page of the diagram lies.  Then there is a hyphen
followed by the pagination pass in which the page was selected.
Finally there is a running header and a page number for the page
within the diagram.

The Dewey decimal notation(5) is just a string of numbers
separated by periods which indicates where in the Warnier tree a
particular node is.  For example, 'ROOT.6.3.5' applies to a node
whose grandfather is the sixth child of the root node, whose
father is the third child of his family, and who himself is the
fifth child of his family.  It is usually more convenient for you
to find your way in the diagram by following the forward and
backward references than it is to try to employ the Dewey decimal
locators, which are pretty awkward.  The length of the Dewey
decimal string does give a quick impression of the logical depth
of the diagram page you are looking at.

When pagination occurs, forward and backward references are
produced to enable easy navigation to the attached parts of the
overall diagram.  The forward references (**SEE PAGE nn**) appear
in early, hierarchically superior pages in the tree and reference
later, hierarchically inferior pages.  The forward reference
occurs as a one-line leaf node on the superior page as a child of
the node which is the root of the separated page.  The backward
references (**REPEATED FROM PAGE nn**) occur with the leftmost
node of each subpage (i.e. the root node of each separately
paginated subtree) beneath the value of the node much as an
auxiliary repetition field appears.  The node value of each
page's root node is repeated on the subpage.

The selection of pages is done solely on the basis of their size.
However, it often seems uncanny that a mere mechanical process
can do such a good job of paginating along logical lines.  This
is only an illusion, of course.  When a program is well
structured, it has logical coherence at every level, so it
doesn't matter at what level the pagination breaks off subpages.
In any subdivision, there will be coherence in the activity
selected for presentation on a subpage because there is coherence
at all levels.  If you are startled by the apparent logic of
pagination, it is a good sign that you are developing a coherent
design.  If vice versa shows up, you might take it as a sign that
your design still needs work.


                       8. OPERATIONAL CYCLE

SPA:WN's Warnier diagram output is designed to be obtained on a
printer but all the other activities are done on a VDT. The
preparation of the input file for SPA:WN is done interactively
with any convenient editor, and the SPA:WN program is run to
produce various output files on the basis of its control
parameters and the input file fed to it.  The <fn>.DIA file can
be examined in an editor, but most VDT's do not present a large
enough area for this to be very effective.

Initial entry of a program as a SPA:WN input file can be done at
the computer screen with very little prior preparation if the
design task is fairly routine.  You enter the root node for the
whole diagram followed by whatever set of children can be
visualized at that stage in development.  You make copies of
those children who are destined to be parents of subtrees in
their turn and convert then from child syntax to parent syntax
(by removing the leading comma and changing any final semicolon
to a comma), and then proceed to insert after each derived parent
the set of children which define its family (taking care to close
each set of children with a semicolon and to move on to the next
parent for definition of its children).  The practice of copying
the parent nodes avoids errors in mistyping the node-as-parent to
guarantee that it matches the same node-as-child.  This
successive refinement process ("divide and conquer") can be done
at the screen easily after very little practice.  It is
accommodated by the SPA:WN input stream requirements which are
only that the nodes be input in hierarchical order and that
parent nodes be unique in the preceding input stream.

After some time at node inputting you begin to lose track of the
developing structure of the program.  At such a time, you run the
SPA:WN program.  The diagnostic output file will almost surely
indicate that you made some errors in input structure or
punctuation.  Usually you can find these errors at the VDT screen
without printing the diagnostic file, but it might be necessary
to print the diagnostic file.  You correct the errors which the
diagnostic file indicates in the source file, and run SPA:WN
again.  (Use of an editor with split screen capability is very
desirable for finding errors in one file while correcting their
causes in another.)  After a few passes, you get a clean run of
SPA:WN, and the <fn>.DIA file which contains the Warnier diagram
is printed to show the current structure of the program.

The printed Warnier diagram has plenty of space on it in which to
pencil in new subtrees or insert new nodes among pre-existing
sets of children, indicate with arrows when nodes or subtrees
need to be moved to correct mistakes in the program logic, and
just generally to edit and refine the program.  After the listing
is messy enough, you go back to the VDT screen and edit in all
the changes which have been identified.


                          OPERATIONAL CYCLE               8-2

Major changes in program structure are very easily made because
it is a necessary result of the constantly maintained
hierarchically structured nature of the evolving program that
every subtree is independently relocatable and entire subtrees
can be moved simply by moving a single (parental) line to a new
location in the SPA:WN input file.  The only restraint is that
the node-as-child must appear earlier in the input file than the
node-as-parent.  No attention need be paid to the impact these
rearrangements may have on the shape of the Warnier diagram,
because automatic pagination will find a way to respond to every
structure change you make, and the next Warnier diagram obtained
in the form of a printed listing will represent the structure of
the program at that time just as well, although possibly by a
completely different pagination scheme, as did the one just
altered in an editing step.

When all the changes and additions have been made, the SPA:WN
program is again run, the diagnostic listing again used until all
SPA:WN errors have been corrected, and a fresh Warnier diagram
again printed out.  From the first time a printed diagram was
obtained onwards, all program refinement seems subjectively to be
reduced to a series of editing operations until the design is
complete.  The refinement cycle is repeated until a satisfactory
design is achieved.

Only the initial input of the program at the very highest level
and occasional logically difficult specific tasks feel like
design activity, so subjectively one feels that the design
progresses at the expense of little activity more creative than
merely editing.  This is because incremental refinement can
proceed satisfactorily in small steps and is supported at every
step by a graphical presentation of the program structure.  The
actual production of target language code, being entirely
automatic by addition of 'plipunch y' to the control parameters,
costs no more intellectual effort and seems entirely cost-free.


                   9. AUTOMATIC CODE GENERATION

SPA:WN does not know any target languages.  All target language
specification comes from the input stream and is provided by the
user.  SPA:WN runs solely on a very minimal set of punctuation
conventions.  Hence, it is not much trouble to keep SPA:WN
punctuation out of the way of the target language.  This means
that all features of any target language can be included in the
input stream and that any target language program can be
constructed using SPA:WN.

There are only four punctuation marks employed by SPA:WN: the
comma, semicolon, quote, and percent.  As has been said, the
comma and semicolon serve to delimit the node values (from the
auxiliary field values, see Chapter 11, below) in the SPA:WN
input file.  The quote serves to delimit disambiguation strings
added to otherwise identical parental nodes to make them unique
(see Section C, below).  The percent forces a line break within a
node in the printed Warnier diagram.

The production of target language programs by SPA:WN does not
interfere with its use as a program design tool, because none of
the supporting features are in serious conflict.  All SPA:WN
punctuation, including the special characters '%', '"', and the
'%---%' sequence which separates the preorder- from the
postorder- portion of structured construct nodes (Section B,
below) are removed from the target language output stream.

Generation of target language code is requested by specifying
'PLIPUNCH Y' among the parameters of the control records.  (This
keyword is an anachronism; it dates from the time when we thought
that only PL/I would be available as a target language; if we allow
ourselves to retrofit an acronym, we could say PLIPUNCH requests a
Programming Language Input PUNCHed file, itself an anachronism, since
the output file never goes to a card deck nowadays.)

There follows a simple example to illustrate the general features
of the input stream and the output.  The Warnier diagrams were
made small enough to fit in three columns for this example
instead of the usual six.


                      AUTOMATIC CODE GENERATION           9-2

From the input stream:

   TITLE SIMPLE SAMPLE EXAMPLE
   MINIMUM %FIT SEARCH,,
      ,INITIALIZE,,
      ,DO WHILE(NOT-CONVERGED FLAG),,
      ,OUTPUT RESULT,;
   INITIALIZE,,
      ,SET NOT-CONVERGED FLAG,,
      ,SET OLD_BEST_FIT=LARGE_VALUE,,
      ,STEP_DIR=-1"1,,
      ,READ (X&STEP_SIZE&ENDSIZE),,
      ,CALCULATE INITIAL FITX=FIT(X),;
   DO WHILE(NOT-CONVERGED FLAG),,
      ,SEARCH LOOP BODY,;
   ENDWARNIERDIAGRAM
   TITLE SEARCH LOOP BODY
   SEARCH LOOP BODY,,
      ,IF FITX<OLD_BEST_FIT,-XOR-,
      ,IF STEP_DIR=-1,-XOR-,
      \,STEP_DIR=-1,,
      ,CALCULATE FIT(X),;
   IF FITX<OLD_BEST_FIT,,
      ,BEST_X=X,,
      ,X=X+STEP_DIR*STEP_SIZE,,
      ,OLD_BEST_FIT=FITX,;
   IF STEP_DIR=-1,,
      ,STEP_DIR=1,,
      ,X=BEST_X+STEP_SIZE,;
   \STEP_DIR=-1,,
      ,STEP_DIR=-1"2,,
      ,IF STEP_SIZE<=ENDSIZE THEN %RESET NOT-CONVERGED FLAG,-XOR-,
      ,STEP_SIZE=STEP_SIZE/7,,
      ,X=BEST_X-STEP_SIZE,;
   ENDWARNIERDIAGRAM

the following output arises.


                      AUTOMATIC CODE GENERATION           9-3

    SIMPLE SAMPLE EXAMPLE       WARNIER 1.2  02/02/83 PAGE 1
                                              .-
                                              ^    SET NOT-
                                              ^    CONVERGED FLAG
                                              ^
                                              ^    SET OLD_BEST_
                                              ^    FIT=LARGE_VALUE
                                              ^
                        .-                    ^    STEP_DIR=-1
                        ^    INITIALIZE      <
                        ^                     ^
                        ^                     ^    READ (X&STEP_
                        ^                     ^    SIZE&ENDSIZE)
                        ^                     ^
                        ^                     ^    CALCULATE
       MINIMUM          ^                     ^    INITIAL FITX=
       FIT SEARCH      <                      ^    FIT(X)
                        ^                     '-
                        ^
                        ^    DO WHILE(NOT-    .-
                        ^    CONVERGED FLAG) <     SEARCH LOOP BODY
                        ^                     '-
                        ^    OUTPUT RESULT
                        '-

    SEARCH LOOP BODY            WARNIER 1.2  02/02/83 PAGE 1
                                              .-
                                              ^    BEST_X=X
                                              ^
                        .-                    ^
                        ^    IF FITX<OLD_     ^    X=X+STEP_DIR*
                        ^    BEST_FIT        <     STEP_SIZE
                        ^                     ^
                        ^                     ^    OLD_BEST_FIT=
                        ^    -XOR-            ^    FITX
                        ^                     '-
                        ^
                        ^                     .-
                        ^                     ^    STEP_DIR=1
                        ^    IF STEP_DIR=-1  <
                        ^                     ^    X=BEST_X+STEP_
                        ^                     ^    SIZE
       SEARCH LOOP BODY<                      '-
                        ^
                        ^                     .-
                        ^    -XOR-            ^    STEP_DIR=-1
                        ^                     ^
                        ^                     ^    IF STEP_SIZE<=
                        ^                     ^    ENDSIZE THEN
                        ^                     ^    RESET NOT-
                        ^                     ^    CONVERGED FLAG
                        ^ \  STEP_DIR=-1     <
                        ^                     ^    -XOR-
                        ^                     ^    STEP_SIZE=STEP_
                        ^    CALCULATE FIT(X) ^    SIZE/7
                        '-                    ^
                                              ^    X=BEST_X-STEP_
                                              ^    SIZE
                                              '-


                      AUTOMATIC CODE GENERATION           9-4

A. SPA:WN Punctuation Substitution

The first consideration in defining the SPA:WN input stream when
the intent is automatic generation of target language code is the
matter of conflicting punctuation.  If the target language
statements (including any punctuation marks occurring in literals
in the program being written) employ any of the SPA:WN
punctuation marks, the conflict must be resolved.  A mechanism is
provided for this.  It is the ability to redefine the punctuation
marks which SPA:WN will recognize to separate auxiliary fields,
close a set of children, force a line break in a diagram node, or
delimit a disambiguation string.  These redefinitions are done in
a control record at the start of the input stream.  In it the
names of the punctuation marks are used as keywords and the
substitute values are provided as single characters.  For
example,

    COMMA \ SEMICOLON ! PERCENT $ QUOTE ~

would define the backslash as SPA:WN comma, the exclamation point
as SPA:WN semicolon, the dollar sign as SPA:WN percent, and the
tilde as the SPA:WN quote.

(Now don't worry, you don't have to be prescient.  Just start
with any convenient punctuation until you discover a conflict.
It is time enough then to do a global change of the old symbol to
its SPA:WN substitute and continue with the new punctuation
convention.  The punctuation convention in use is everywhere in
front of you as you work with a program, so it is no trouble to
remember what conventions are in use at any given moment.)

B. Construct Body Positioning

A second major consideration in a diagram intended to produce
target language source code is the necessity to indicate to
SPA:WN where the the body of a construct fits.  Remember that the
entire structured construct, both beginning and end, appear in a
single parental node and that SPA:WN is completely ignorant about
target languages.  The device adopted is to separate the two
parts of the structured construct by use of '%---%'.  (Those are
SPA:WN percents, which means that a substitute may be defined in
the event that percents are required in the target program.)

In the output diagram, the percent signs have their usual effect
(forced line separations) so that three hyphens appear by
themselves on a line of the output node.  The hyphens indicate to
the reader of the diagram where the structure body fits.  (Of
course, even a passing acquaintance with the target language is
enough to make this feature superfluous.)

In the generated target language code, the structure opener is
output in a separate record before the body of the construct and
the structure closer in a separate record after the body.  Thus,
the body of the structured construct is automatically placed
correctly where the special delimiter indicates the proper site
of insertion to be.  SPA:WN does not recognize elements of target
language syntax; it simply responds to the '%---%' delimiter.


                      AUTOMATIC CODE GENERATION           9-5

Note that the program being developed under SPA:WN will not
contain mismatched or improperly nested DO%---%END or
IF%---%ENDIF or IF...ELSE%---%ENDIF constructs.  The
hierarchically nested structure of the Warnier diagram and the
manner in which the target language code is generated from the
SPA:WN input guarantee this.  Every structured construct parent
has its pre-order portion placed before its structure body and
its post-order portion placed after its structure body.  Hence,
the structure opener and the structure closer are correctly
placed to enclose the structure body, independent of the
complexity and length of the structure body.  (Of course, if you
omit or mis-spell some part of a structured construct you can
achieve mismatching and improper nesting.  But that would be
extraordinary.  One desk check you can make on a printed Warnier
diagram is the correctness of every structured construct parental
node.)

Only a single '%---%' separator is permitted in a node.  When a
complex structured construct is used (like a CASE statement), it
is input as a series of Warnier nodes at one logical level.  Each
separate node serves as parent of its own structure body.  The
simpler case of an IF ...  THEN <then clause> ELSE <else clause>
ENDIF construct is handled similarly.  We give two examples.

    . . .                                  . . .
   ,CASE J OF%---%END,,                  ,IF ... THEN,-XOR-,
    . . .                                ,ELSE%---%ENDIF,,
CASE J OF%---%END,,                        . . .
   ,1:BEGIN%---%END,-XOR-,         IF ... THEN,,
   ,2:BEGIN%---%END,-XOR-,               ,<then clause>,;
   ,3:BEGIN%---%END,-XOR-,         ELSE%---%ENDIF,,
   ,OTHERWSIE BEGIN%---%END,;            ,<else clause>,;

which results in

                 ...
                 ^    1:BEGIN
                 ^    ---
                 ^    END
                 ^
                 ^    -XOR-
                 ^    2:BEGIN
                 ^    ---
                 ^    END
   CASE J OF     ^
   ---          <     -XOR-
   END           ^    3:BEGIN
                 ^    ---
                 ^    END
                 ^
                 ^    -XOR-
                 ^    OTHERWISE BEGIN
                 ^    ---
                 ^    END
                 ...

and


                      AUTOMATIC CODE GENERATION           9-6
        ...
        ^   . . .
        ^                   .-
        ^   IF ... THEN    <   <then clause>
        ^                   '-
        ^   -XOR-
        ^
        ^   ELSE            .-
        ^   ---            <   <else clause>
        ^   ENDIF           '-
       <
        ^   . . .
        ...

where the infix auxiliary field (which contains '-XOR-') has yet
to be explained.  (See Chapter 11, below.)

C. Node Disambiguation

The third major consideration in target language code generation
is the matter of disambiguation.  It often happens in a Warnier
diagram which is being written to produce some target language
source program that some node value will occur more than once and
will be employed as a parent one or more of those times.  Since
the rigidity of the target language syntax and the program
requirements don't permit variation in spelling node values, the
problem of dealing with the ambiguity about the choice of node to
serve as parent of a subtree comes up.  In the absence of a
disambiguation mechanism, it would be impossible to distinguish
lexically among the various instances of a node value that one
which is to serve as parent.  (It does make a difference: imagine
a program with two 'DO I=1 TO 20;%---%END;' nodes whose bodies
were interchanged.  The program will work correctly only if each
loop contains the correct body.)

This problem is met by providing a mechanism for disambiguation.
(This stuff is hard to talk about.  Are several nodes with the
same value different instances of the same node?  Or are they
different nodes which accidentally have the same lexical value?
When they are disambiguated, it seems clear that they are
different nodes with the same value, but until then we can speak
ambiguously, which serves to make the point about the ambiguity
problem.)

When multiple nodes are identical in spelling, they can be
differentiated from one another (i.e. disambiguated) by appending
a specific delimiter and unique string to the value of the node.
The disambiguation delimiter is the quote sign (") by default.
Any unique short character string will serve to disambiguate an
ambiguous node.  How can you quickly think up a suitable one?  It
is quick and convenient to use the line number of the as-child
instance of a node when it is created as the value of each one's
disambiguation string.  The parental instance, as usual, is a
copy of the child instance, (including the disambiguation string
but with the usual punctuation changes) so that the correct
identification of the two is made in building the overall
diagram.


                      AUTOMATIC CODE GENERATION           9-7

The use of line numbers is just a quick way of inventing unique
disambiguation strings.  No use is made of the value of the
disambiguation strings other than to identify the as-child
instance with the as-parent instance.  Even though the line
numbers shift during continued development, there is no need to
change the disambiguation strings because it is their pairwise
identity, not their value, which is effective.  It would be very
rare for two identical disambiguations of two identical nodes to
arise by coincidental line number shifts.

SPA:WN diagnoses ambiguous parental nodes, so the user of SPA:WN
need not pay much attention until the problem actually arises in
the form of a diagnostic message.  When such a message appears,
it is well to disambiguate the whole set of identical nodes, not
just those provoking the messages.  At least one node of the set
precedes the first error message concerned with the set.

The values of the disambiguation strings are deleted from the
Warnier diagram and in the target language output code.  The
<fn>.SRC code which may be produced on request is
super-disambiguated -- it contains more than the necessary number
of disambiguation strings.


                  10. TARGET LANGUAGE ADJUSTMENTS

A. SPA:WN Comment Dangers

Remember that an asterisk ('*') in column 1 of the SPA:WN input
stream indicates a a SPA:WN comment.  When the target language is
one where an asterisk is the comment opening character (e.g.
SNOBOL and dBASE) you must take care.  As always, you will have a
number of comment statements intended to be part of the Warnier
diagram and to appear in the target language output stream.
The asterisk of a target language comment used as a parent
must not appear in column 1.  If it does, the comment will be
swallowed up as a SPA:WN comment and the whole mis-punctuated
parent node diagnostic excitement will arise.  Column 2 or any
later column suffices.  (There are examples at the very end of
this chapter.)

When SPA:WN comments are used, they are output collected at the
front of the target language stream, <fn>.PUN.  Since the leading
asterisk of SPA:WN comments is stripped (it has to be for
generality of target language, because not all target languages
will tolerate an asterisk in column 1), the target language
comment syntax must be followed in columns 2 and following of
SPA:WN comments in order that the target language compiler also
accept them as comments.

B. Statement Formatting

Some computer languages are fixed format languages and some are
free format languages.  SPA:WN makes it possible to meet the
target language requirements in either case.  A different
approach is used in SPA:WN for each of these.

B.1. Free Format Target Languages

Actually, when you are working from Warnier diagrams, there is
very little reason to take much care in formatting target
language code, because you work with the Warnier diagram, not the
target language source code.  You can regard the target language
code with as little interest as you regard object code from a
compiler.  For this reason, beyond that required to meet compiler
requirements, formatting target language code is not a
requirement.

Nevertheless, the utility of having a logically indented source
code in a free format computer language is undeniable.  Even
though that code has a short useful lifetime, it is worthwhile to
have it indented because it is so easily and routinely
produced after each design improvement.  There are admittedly
times when you want to make "target language code patches" like
we used to make "object code patches".

A difficulty with writing a program with a useful indention
pattern without use of a generator like SPA:WN is that design
changes cause a degradation of the pattern and it rarely seems
worthwhile to maintain the indention.  SPA:WN will indent the
target language code if you put the control sequence 'INDENT Y'
along with 'PLIPUNCH Y' among the control parameters at the
beginning of a diagram specification.  Thus production of
indented code is another useful feature of SPA:WN.


                      TARGET LANGUAGE ADJUSTMENTS        10-2

The indention produced is one character per logical level in the
Warnier diagram.  The default indention character is a blank.  If
a different indention character is desired, it is specified after
the 'INDENT' keyword, as in 'INDENT &', which causes one
ampersand to be inserted in the target language output line for
each level of depth of a particular statement.  The advantage of
a non-blank as the indention character is that each can be
converted to several blanks (to achieve a steeper indention than
just a single character per level) or to tab characters which can
then be converted to an irregular indention pattern by setting
tabs stops and EXPANDing in a editor which provides this
capability.

Sometimes, due to a large logical depth with a consequent large
number of indention characters, a lengthy node requires more
characters in <fn>.PUN than are available to it under the current
LENLINOUT parameter value.  (The problem is aggravated in
<fn>.SRC, where a number of SPA:WN percents increase the
character count.)  These lines are not indented by SPA:WN; they
remain at the left margin.  The effect of this is to ruin an
otherwise consistent indention pattern.  One solution is to split
such lines into two parts, as is mentioned elsewhere in
connection with continuation lines (Section 13.B).  Another
solution, if the target language compiler can tolerate it, is to
specify LENLINOUT greater than LENLININ by enough characters to
accommodate all the extras which may accrue from line splits,
indentions, and disambiguations (in <fn>.SRC).

B.2. Fixed Format Target Languages

For fixed format languages, it is necessary to provide tab tokens
by which the required indention is passed unobtrusively through
the SPA:WN processor to the target language source file where
they can be converted to the precise requirements of the target
language.  In fixed format languages, you run SPA:WN without
doing indention (default parameter values, or 'INDENT N'). You
provide the requisite indention tokens as part of the node
values.  You can use multiple instances of a single indention
character and then convert them to tab characters and EXPAND to
appropriate tab stops, or you can define a set of tab characters,
each representing a particular tab stop, and expand each in turn
to its proper column.  These tab character expansions are most
easily done in a macro in a powerful editor.  If a consistent
practice is adopted for each target language in use, then a
single edit macro can be used for all programs being developed in
that language to convert SPA:WN output to properly indented
target language code.  The formatting process is easy and quick
in practice.  You just load the <fn>.PUN file into your editor
and issue a single macro command.

For example, if '\' is used as a SPA:WN comma to free natural
commas for target language use, and '>' is used as a tab
character for formatting the target language stream, a FORTRAN
statement used as a child node would appear as

     '\150>DO I=1,100,2\\'.


                      TARGET LANGUAGE ADJUSTMENTS        10-3

If the target language is FORTRAN (as an example of a fixed
format language), one needs to use a token for a tab character
('>' is handy, and not otherwise used in FORTRAN) for later use
in an editor in aligning statements on column 7.  One can use a
token ('<' is used, below) for definition of continuation lines,
and employ XEDIT to properly align the continuation lines in the
same way the tab token is used to align each statement.  NOTE:
This is an example of the mechanism by which successive Warnier
nodes can be used to represent a single target language
statement, if attention is given to providing the target language
statement continuation mechanism.  (More in Chapter 13.B.)

The postprocessing of the output stream when FORTRAN is the
target language to produce correctly formatted FORTRAN source is
not difficult.  First, convert the tab tokens to the correct
number of blanks to align statements in column 7.  This is done
in two steps; first, the '>' is converted to a tab character
(X'05' in EBCDIC or X'09' in ASCII) and then it is expanded to
column 7 the correct location for the body of FORTRAN statements.
(The edit commands are those of XEDIT or KEDIT.)

     stay on#top#alter > 09 *#tabs 1 7#expand *

Then, get the continuation lines aligned in column 6.

     zone 6 *#c/ </</*

Finally store the formatted program as a FORTRAN source file,
assuming the FORTRAN compiler to require fixed length
80-character records.

     ftype fortran#recfm f#lrecl 80#file

Of course, all these steps could be combined in an edit macro.

Here is a simple FORTRAN example of the whole process.  With the
input file SAMPLE.WAR:

     COMMA ? SEMI @ PLIPUNCH Y
     TITLE FORTRAN CONVERSION EXAMPLE
     *C SAMPLE WARNIER TO SOURCE CODE CONVERSION FOR FORTRAN
     C MAIN PROGRAM??
     *C ILLUSTRATE CONTINUATION MECHANISM
        ?>INTEGER*4 I,II,III,J,JJ,JJJ,K,KK,KKK,L,LL,LLL,??
        ?><M,MM,MMM,N,NN,NNN??
     *C ILLUSTRATE NODE SPLITTING FOR LOOP CONTROL NODES
        ?>DO 10 I=1,10,2%---%10>CONTINUE??
        ?>STOP??
        ?>END?@
     >DO 10 I=1,10,2%---%10>CONTINUE??
        ?>J=I*I-2*I-1??
        ?>WRITE(6,100)J??
        ?100>FORMAT(I6)?@
     ENDWARNIERDIAGRAM


                      TARGET LANGUAGE ADJUSTMENTS        10-4

The Warnier diagram is:

 FORTRAN CONVERSION EXAMPLE      WARNIER 1.2  01/13/83 PAGE 1
                     .-
                     ^    >INTEGER*4 I,II,
                     ^    III,J,JJ,JJJ,K,
                     ^    KK,KKK,L,LL,LLL,
                     ^
                     ^
                     ^    ><M,MM,MMM,N,NN,
                     ^    NNN              .-
                     ^                     ^    >J=I*I-2*I-1
                     ^                     ^
    C MAIN PROGRAM  <     >DO 10 I=1,10,2  ^
                     ^    ---             <     >WRITE(6,100)J
                     ^    10>CONTINUE      ^
                     ^                     ^
                     ^                     ^    100>FORMAT(I6)
                     ^    >STOP            '-
                     ^
                     ^
                     ^    >END
                     '-

The SAMPLE.PUN is:

      C SAMPLE WARNIER TO SOURCE CODE CONVERSION FOR FORTRAN
      C ILLUSTRATE CONTINUATION MECHANISM
      C ILLUSTRATE NODE SPLITTING FOR LOOP CONTROL NODES
      C MAIN PROGRAM
      >INTEGER*4 I,II,III,J,JJ,JJJ,K,KK,KKK,L,LL,LLL,
      ><M,MM,MMM,N,NN,NNN
      >DO 10 I=1,10,2
      >J=I*I-2*I-1
      >WRITE(6,100)J
      100>FORMAT(I6)
      10>CONTINUE
      >STOP
      >END

After the postprocessing editing stage, the SAMPLE.FTN file is:

     C SAMPLE WARNIER TO SOURCE CODE CONVERSION FOR FORTRAN
     C ILLUSTRATE CONTINUATION MECHANISM
     C ILLUSTRATE NODE SPLITTING FOR LOOP CONTROL NODES
     C MAIN PROGRAM
           INTEGER*4 I,II,III,J,JJ,JJJ,K,KK,KKK,L,LL,LLL,
          <M,MM,MMM,N,NN,NNN
           DO 10 I=1,10,2
           J=I*I-2*I-1
           WRITE(6,100)J
      100  FORMAT(I6)
      10   CONTINUE
           STOP
           END


                      TARGET LANGUAGE ADJUSTMENTS        10-5

C. Handling Unstructured Languages

When a program is to be designed in a language which does not
feature appropriate structured constructs, the user must
adopt a conventional representation in the target language for
each structured construct he intends to use.  Then on every
occasion of use of that construct, he employs its conventional
representation.  In many languages, these representations will
consist of labels or statement numbers and predicated or computed
GOTO instructions which simulate (i.e. have the effect of) the
desired structured construct.

We would like the adopted conventional representations for
structured constructs to be both readable and effective.  For
readability, we require the labels and branches to labels used in
simulating structured programming constructs to be so positioned
that there is no difficulty at all in finding the target of every
branch instruction in the diagram.  For effectiveness in creating
structured programs, the conditioned branches and the referenced
labels in the simulations need to be positioned so that structure
is enforced in the same sense as when when structured constructs
are used in structured languages.  Fortunately, these needs are
all met if every label is required to appear either in the same
Warnier node as the branch instruction which references it, or in
an ancestral node in the Warnier tree in the line of descent to
the reference.

If such conventions are followed, the labels and the references
to them will be localized enough to make the diagram easy to read
and easy to rearrange as design proceeds.  There is no
restriction imposed by the Warnier program on the contents of the
two parts of a node which serves as structured construct
simulator and contains the '%---%' delimiter -- the two portions
are output in separate output records and can be of quite
different, syntactically unrelated, natures if the case demands
it.  For example, the first part might be a comment, and the
second part a label; the first part might be a predicated branch
to a label and the second part the label; or the first part might
be a label and the second part a predicated branch to the label.

These combinations of node parts allow the construction of
simulations for structured constructs which are effective, i.e.
which have the desired result of simulating structured constructs
in the target language.  The restriction of referenced labels to
use in the same or hierarchically superior nodes in the line of
descent keeps the program structured enough to make it possible
to move subtrees from place to place in the diagram with little
danger of inadvertent tangling of spaghetti.  This represents
another level of effectiveness.

It is sometimes necessary to introduce "extra" levels of logic to
meet the suggestion that labels appear in the line of descent to
their references.  It is often useful to include a comment which
contains the structured language equivalent of its simulation in
the unstructured language.  This comment is particularly useful
to other readers of the program than the original designer,
especially if they are not completely at home in the target
language.


                      TARGET LANGUAGE ADJUSTMENTS        10-6

Here are a few examples of simulations of structured constructs
in unstructured languages.  Certainly the examples are not
exhaustive, but they should serve to convey the general idea.

sample unstructured language construct simulations
                   .-
                   ^  >i = 1
                   ^
  *do i = 1 to     ^
  100 in SPITBOL  <   loop             .-
                   ^  ---              ^  *loop body goes
                   ^  >i = lt(i,100)  <   here
                   ^  i + 1            ^
                   ^  >:s(loop)        '-
                   '-
                                       .-                .-
                   .-                  ^  >eq(x,y)       ^  *then clause
  *if ... then ... ^  *if x=y then ... ^  >:f(elslab)    ^  body goes here
   else ... in    <    else            ^  ---           <
  SPITBOL          ^  ---             <   elslab         ^
                   ^  merge            ^                 ^  >>>:(merge)
                   '-                  ^                 '-
                                       ^  *else clause
                                       ^  body goes here
                                       '-
  C DO WHILE X     .-
  .GT. Y IN        ^  99>IF X.LE.Y     .-
  FORTRAN         <   GOTO 98          ^  C LOOP BODY
  ---              ^  ---             <   GOES HERE
  98>CONTINUE      ^  >GOTO 99         ^
                   '-                  '-

                   .-
  C DO UNTIL X-Y   ^  99>CONTINUE      .-
  .LT. 0.01 IN    <   ---              ^  C LOOP BODY
  FORTRAN          ^  >IF X-Y .GE.    <   GOES HERE
                   ^  0.01 GOTO 99     ^
                   '-                  '-

It might be instructive to study the following input stream, from
which the above samples were produced, because several features
are used.  (The diagram is compressed slightly to better fit on
this page.)  Forced line splits contribute importantly to the
readibility of the diagram fragments, SPA:WN punctuation
definition allows commas to appear in the SPITBOL statements, a
token is used to bring about the required indentions in the
target languages, indention in the input stream clarifies the
family groups, and the mistaking of a SPITBOL comment for a
SPA:WN comment is avoided by having certain lines begin in column
2 of the input stream.


               TARGET LANGUAGE ADJUSTMENTS               10-7

    comma $ title
    sample simulations$$
            $*do i = 1 to 100 in SPITBOL$$
            $*if ... then ... else ... in SPITBOL$$
            $C DO WHILE X %.GT. Y IN FORTRAN%---%98>CONTINUE$$
            $C DO UNTIL X-Y %.LT. 0.01 IN FORTRAN$;
     *do i = 1 to 100 in SPITBOL$$
            $>i = 1$$
            $loop%---%>i = lt(i,100) i + 1%>:s(loop)$;
    loop%---%>i = lt(i,100) i + 1>:s(loop)$$
            $*loop body goes here$;
     *if ... then ... else ... in SPITBOL$$
            $*if x=y then ... else%---%merge$;
     *if x=y then ... else%---%merge$$
            $>eq(x,y)%>:f(elslab)%---%elslab$$
            $*else clause body goes here$;
    >eq(x,y)>:f(elslab)%---%elslab$$
            $*then clause body goes here$$
            $>>>:(merge)$;
    C DO WHILE X .GT. Y IN FORTRAN%---%98>CONTINUE$$
            $99>IF X.LE.Y GOTO 98%---%>GOTO 99$;
    99>IF X.LE.Y GOTO 98%---%>GOTO 99$$
            $C LOOP BODY GOES HERE$;
    C DO UNTIL X-Y .LT. 0.01 IN FORTRAN$$
            $99>CONTINUE%---%>IF X-Y .GE. %0.01 GOTO 99$;
    99>CONTINUE%---%>IF X-Y .GE. %0.01 GOTO 99$$
            $C LOOP BODY GOES HERE$;
    endwarnierdiagram



                         11.  AUXILIARY FIELDS

When it is desired to more completely annotate the Warnier
diagram so that it will better serve as complete documentation of
the program it represents, you can use the auxiliary fields which
are provided.

We divide the operators mentioned in the Warnier literature into
prefix fields and infix fields on the basis of the position of
their appearance in the output.  The prefix field is used for
operators applying to a node or to an entire subtree the node is
the root of.  The infix field is used to indicate
interdependencies or relationships between a pair of adjacent
nodes or their subtrees.  In addition there is a repetition
field, which is associated with a particular parental node to
describe some feature of it or its subtree.

There follows a more elaborate version of the input stream
description with the positions for insertion of the auxiliary
fields identified.  Auxiliary fields are always optional; they
may be used or omitted as desired.

  *<SPA:WN comments appear anywhere, bear an asterisk in column 1>
    (title  <some appropriate title for the page header>
      (<parental node value>,[<repetition value>],
        ([<prefix value>],<internal child value>,[<infix value>],) ...
          ,<final child value>,;) ...
      endwarnierdiagram) ...

The repetition field is specified on the parental node between
the two commas.  It may be up to 12 characters long.  It appears
in the output diagram immediately below the node value.  It is
not output to the target language source code.

The prefix value is specified before the first comma on the child
node.  It is up to 3 characters long by default, but its maximum
length may be changed by specifying a parameter.  It appears in
the output diagram at the left of the node value between the
brace and the node value, repeated as many times as there are
lines of the node value.  It does not appear in the output target
language source code.

The prefix value becomes a part of the node value in the
node-as-parent copy of the node when it is repeated as parent.
This makes nodes which bear prefixes obey the same rules for
creation of the as-parent instance from the as-child instance
that other nodes obey: copy the as-child node, remove the first
SPA:WN comma, and change any SPA:WN semicolon to a SPA:WN comma.

The infix field value is accepted between the SPA:WN commas after
the node value of an internal child node.  It is supplied with
the first of the two child nodes it applies to; no infix value is
allowed on the last of a set of children.  The infix field
appears centered vertically in the diagram between the successive
node values.  It is not output to the target language source
stream.


                              AUXILIARY FIELDS           11-2

The utility of auxiliary fields is highest in Warnier diagrams
which are design efforts solely in pidgin language.  A typical
approach uses prefix fields to indicate negation of logical
expression, repetition fields to indicate expected numbers of
iteration or range of possible selections in alternations, and
infix fields to indicate exclusive or inclusive execution of
successive elements of the logical structure.  Systematic use of
these fields for these purposes ensures that the logical
structure is completely thought out and documented.  The
systematic placement of these items of information increases the
readability of the diagram.  It also frees the node values of any
need to contain these elements of information.

When target language code constitutes the nodes in the Warnier
diagram, much of the utility of the auxiliary fields along the
above lines falls aside.  The semantics of the target language
statements which appear in the node values indicate the precise
sense of logical expressions, specify the precise conditions for
continuing iteration or selection among alternatives, and imply
sequential or mutually exclusive execution of program subtrees.
Since, in a diagram intended to produce target language code all
these features must be entirely specified to the target language,
the use of auxiliary fields to provide these kinds of information
becomes less of a necessity.

Even with target language code in the diagram, it is always
useful to use the infix field to indicate mutually exclusive
subtrees (with 'XO' or '-XOR-' as the field value) and to
indicate when a succeeding node is a continuation statement in
the target language (with '+++' as the infix field value).  If a
continuation of a target language statement is handled as a child
of the first part of the statement, the prefix field value of the
continuation can so indicate (with '+' as its value).  These
simple practices greatly clarify the relationships of the nodes,
especially for readers of the diagram who are not perfectly
familiar with the target language.

Most repetition and alternation control structures are so clear
in any target language syntax that there is little need to use
repetition fields to reinforce their meaning.  It is sometimes
helpful to use the repetition field to hold little comments where
the logical expression controlling alternation or repetition in
the node value is not perfectly self-explanatory because it
contains highly encoded information or convoluted logical
expressions.

All SPA:WN auxiliary fields are removed in the target language
output.  The auxiliary fields appear only in the printed Warnier
diagram.


                       12. DIAGRAM LAYOUT

The default values of the control parameters lead to the
following set of assumptions about the output diagrams.  A double
page (128 lines, including gutter) is the maximum length of a
Warnier diagram page, and six columns is its maximum width.  Six
columns occupy a 129 character line.  There are 16 characters per
line of a Warnier node.  Spaces for braces and prefix fields are
3 characters each.  The root node on each page has no brace.
3+16+5*(3+3+16) gives 129.  The repetition field and the infix
field are limited to 12 characters and are not parametrized.

Automatic separation of each node into 16 character lines is
performed.  The separation is performed at one of a defined set
of break characters when a node value appears which is more than
16 characters long.  If you want to force a break at a particular
point, include a SPA:WN percent at that position in the input
stream in the node-as-child.  (SPA:WN percents in nodes-as-parent
are without effect, but may be included, if desired.)  If a node
has more than 16 characters without a break character, it is
broken arbitrarily after 16 characters.

Control parameters may be included at the head of the stream
specifying a Warnier diagram in the SPA:WN input.  This control
information can be divided across several records, and several
items of control information can be included in a single record.
Fresh control information can be specified for each of a series
of diagrams specified (after each 'endwarnierdiagram' keyword) in
a given input file.  Parameters retain their previous values
unless specifically reset in a control record on a later diagram.
If it shares a control record with other parameters, the 'title'
keyword must be the last parametric keyword on a control record,
because all the rest of the control record is taken as the title
when the 'title' keyword is recognized.  There was an example of
this at the end of Chapter 10.

There follows the basic input stream format with the position of
the parametric information included.  If you are satisfied with
the defaults, you do not need to include any parametric control
records.

   *<SPA:WN comments appear anywhere, bear an asterisk in column 1>
        ([<parametric control keywords and values>]
           title <some appropriate title for the page header>
                (<parental node value>,,
                        (,<internal child value>,,) ...
                         ,<final child value>,;) ...
           endwarnierdiagram) ...


                           DIAGRAM LAYOUT                12-2

Motivation for changing the parameters can come from any of
various sources.  Generally, one wants to set up in such a way
that Warnier diagrams are convenient and readable in the context
of any individual shop or user community.  If a particular
printer configuration or paper size or target language
idiosyncracy makes the default values of the parameters
unsatisfactory in a shop, then the parameters should be changed
(and correct operation of the program verified) to personalize
SPA:WN for the shop.  It is clearly best to select a certain set
of parameters and to stick with it; one subtly arranges a diagram
during its development (by the mechanism of insertion or deletion
of optional levels of comments) to fit on the pages one
customarily uses and a diagram which paginates optimally for one
set of parameters might paginate terribly under another.

One behavior which some users find disconcerting is the
interspersed single and double pages for Warnier diagrams
according to the number of lines each page happens to contain.
If the DIAGPAGEL parameter were changed to 63 (which matches
LINESPHYS=66 and TOPMARGIN=3), the output would be controlled so
that only single pages would be produced, but the cost might be
the appearance of "pagination failed" messages, which arise when
the vertical height of a bracket is greater than the available
vertical space.  To recover from this circumstance, edit the
diagram's source stream to introduce extra levels (perhaps by
insertion of a new level of comments to head some partial ranges
of statements in the too-tall bracket, thereby making them appear
at a deeper level and decreasing the height of the bracket).
This breaks up long vertical sequences so that everything can be
paginated into pages of 63 lines.

The copyright notice is produced after each page of the diagram
on which there is room for it; if there is not room on a given
page, the notice is simply skipped.

The effects of altering parameter values have not been
exhaustively tested; the user is somewhat on his own in
experimenting with them; the program has principally been used
with DIAGCOLS=6 (diagram columns per page), LINESPHYS=66 (lines
per physical page), TOPMARGIN=3 (printer set to skip 3 lines
after page eject), DIAGPAGEL=128 (diagram page length in lines),
NODEWIDTH=16 (width of line in diagram node), LENLININ and
LENLINOUT=80 (length of lines input and length of lines output --
both card image records), and PREFWIDTH=3 (width of prefix field);
most of these values have been changed individually, but there
has been very little testing of simultaneous change in the values
of two or more of these parameters.

A.  Control Parameters

A complete list of the parameters which can be supplied in
control records, their defaults, and meanings follows.  The
control keywords and alphabetic values can be supplied either in
uppercase or lowercase.


                           DIAGRAM LAYOUT                12-3

   Parameter    Default   Brief Description
    Name         Value

   BOTBRACK       '-    Defines bottom bracket corner symbol.
   COMMA          ,     Defines SPA:WN comma.
   DIAGCOLS       6     Columns of Warnier nodes in the diagram.
   DIAGPAGEL      128   Diagram Page Length (in lines; do not exceed
                           n*LINESPHYS-TOPMARGIN for an n-page diagram)
   ECHOPAGEL      60    Echo (diagnostic) file page length (in lines).
   INDENT         N     Requests indention in files from PLIPUNCH and SRCPUNCH.
   LINESPHYS      66    Lines per physical page, your printer.
   LENLINOUT      80    Length of line output to *.PUN and *.SRC files.
   LENLININ       80    Length of line input from *.WAR file.
   NODEWIDTH      16    Maximum line width in a Warnier node in diagram.
   PERCENT        %     Defines SPA:WN percent.
   PLIPUNCH       N     Requests target language code be produced.
   PREFWIDTH      3     Maximum prefix field width.
   QUOTE          "     Defines SPA:WN quote.
   SEMI[COLON]    ;     Defines SPA:WN semicolon.
   SRCPUNCH       N     Requests reordered input file be produced.
   TITLE          -     Provides page title for the diagram produced.
   TOPBRACK       .-    Defines top bracket corner symbol.
   TOPMARGIN      3     Blank lines left on page eject, your printer.
   VERTBAR        ^     Defines vertical bar for bracket formation.

Some of the above values can be changed only up to the maximum
defined by a constant in the Pascal source which determines some
storage allocation.  These are listed in the next section.  You
should get a diagnostic message and then a crash if the
parameters you specify are not within the permitted limits.
There is no enforced limit on the length of output line in the
diagram produced.  Be sure that 3 * (DIAGCOLS - 1) + DIAGCOLS *
(NODEWIDTH + PREFWIDTH) is no greater than your printer can
handle.  Warnier diagrams look absolutely terrible if your
printer wraps their lines!

B.  PASCAL Constants

A few things can only be changed by editing the value of constants in
the source code and doing a new compilation.  The mechanism for altering
the constant values in PWARN (at the .WAR level or at the .PAS level,
depending how you want to create the specialized version) is to edit the
altered values into the constants section of the code.  Then reprocess
the altered source code (through SPA:WN, an editing fixup (see below),
and the Pascal compiler (if done at the .WAR level)), or simply through
the Pascal compiler (if done at the .PAS level) to make a new PWARN.COM
file.  Note that the TIMEDATE.PAS routine is needed on the active disk
do a Turbo Pascal compilation of PWARN.


                           DIAGRAM LAYOUT                12-4

The Pascal source code constants, their values, and uses follow:

 Constant     Current   Brief Description
  Name         Value

 LENSTRPGS      5000  Length of each "page" for holding your diagram.
 MAXCPP         10    Maximum diagram columns per page.
 MAXDEPTH       40    Maximum Nesting Depth of Warnier Tree.
 MAXLLIP1       161   Maximum Length of Line In (Plus 1).
 MAXLLO         160   Maximum Length of Line Out in .SRC & .PUN files
 MAXNW          30    Maximum Node Width.
 MAXPW          10    Maximum Prefix Width.
 NBRSTRPGS      20    Number of "pages" available to hold your diagram.
 NMDEL          13^60 Difference between superscript numerals and ordinary
                           numerals in the character set (faked for ASCII)

If an altered set of break characters which control the automatic
separation of nodes of the diagram into lines is required, it would be
necessary to make the required change in the variables PRES, POSTS, and
INDIFFS which together constitute BREAKERS in the Pascal source code and
to recompile.

Note that if you alter the PWARN.WAR stream, you'll need to
remake the Pascal source from the PWARN.PUN file produced by
'SPA:WN PWARN'.  This involves modifying the code to specify it
for the compiler in use.  The PWARN.PUN file has two alternatives
for the two Pascal dialects, PASCAL 8000 and TURBO PASCAL.  The
(T* ... *T) quasi-comments surround code fragments appropriate
for inclusion in TURBO, but incorrect for PASCAL 8000, and
(8*...*8) quasi-comments surround code fragments appropriate for
PASCAL 8000 but incorrect for TURBO.  Hence to convert the
PWARN.PUN file for TURBO PASCAL you must enable the contents of
(T* ... *T) comments and disable the contents of (8* ... *8)
comments.  The inverse set of changes does the trick for PASCAL
8000.  There are a couple ways to do this, depending on the power
of the editor you use.  With KEDIT or XEDIT (where the change
command is C/<old-string>/<new-string>/ <times> <lines>, and an
asterisk means everywhere or everytime), you use the arbitrary
character feature as follows to specify the code to TURBO PASCAL.

     ARBCHAR ON      (enables the arbchar feature, '$' is the arbchar)
     C/(T*$*T)/$/* * (strips the turbo quasicomment symbols)
     C/(8*$*8)//* *  (deletes the 8000 quasicomments entirely)

With a less powerful editor, convert the pseudocomment's
characters individually, as follows:

     C/(T*//* *    (removes left turbo pseudocomment symbol)
     C/*T)//* *    (removes right turbo pseudocomment symbol)
     C/(8*/(*/* *  (converts left 8000 pseudocomment to real
                    comment symbol)
     C/*8)/*)/* *  (converts right 8000 pseudocomment to real
                    comment symbol)

The latter method leaves messier looking code because the 8000
code is still present in comments, but it is perfectly
serviceable nonetheless.


                        13. HELPFUL HINTS

A. Null Comments as Terminal Children

A common error which arises in the use of SPA:WN is messing up
the punctuation associated with the terminal child.  Either
through addition of new children or through rearrangement of
existing children, a child which was once terminal can become
internal.  When a terminal child is used as a parent, it is easy
(unless an edit macro is used to do the conversion) to forget to
convert the trailing semicolon of the terminal child to the
trailing comma of a parent node.  The error messages (as has been
said above) which are provoked by each/any of these mistakes
sometimes seem oblique and particularly confusing to the novice
user of SPA:WN.

What can be done to avoid this whole set of problems?  Use a
target language null comment as a dummy terminating child for
every family of nodes in the input stream.  All real child nodes
thus become internal child nodes.  As a result no punctuation
change is required when you move any real child node around.
Since all real child nodes have terminating commas, all can be
converted to parental nodes simply by copying them and removing
the leading comma.  This removes that particularly seductive
opportunity for error.  The null comment stands out as an easily
distinguished separator after each family in the input stream,
and its presence in the target language code and the diagram
makes them a little more spacious.  The sets of cousins at a
level in the diagram are more easily distinguished.  In inputting
a diagram initially, a null comment node is simply replicated
whenever a new copy is needed to close a newly constructed
family.

If this modus operandi is adopted, the input stream looks as
follows:

 *<SPA:WN comments appear anywhere, bear an asterisk in column 1>
    ([<parametric control keywords and values>]
       title <some appropriate title for the page header>
         (<parental node value>,[<repetition value>],
            ([<prefix value>],<child value>,[<infix value>],) ...
              ,*,;) ...
       endwarnierdiagram) ...

where the asterisk represents a target language null comment.
For FORTRAN this would be a 'C', for PASCAL a '(**)' or a '{}',
for ICON a '#', for PL/I a '/**/', and for dBASE or SNOBOL a
natural '*'.

Adopting this convention pre-empts the diagnostic for an illegal
infix value on the final child; it will be possible to create a
meaningless infix value between the last real child and the dummy
last child.


                            HELPFUL HINTS                13-2

B. Continuation Statements

One problem which often arises is a target language statement
longer that will fit in a single node of the Warnier diagram.
One way to fix this is to redefine the input line length and the
output line length as is described in the section "Control
Parameters".  This cannot always be done due to limitations on
the input line length of the target language compiler.  Another
way to fix it is to split the statement into a series of pieces
which take advantage of the statement continuation mechanism of
the target language.

As has been indicated above, it is always possible to prepare
SPA:WN input so that the *.PUN output either conforms to the
target language syntax for continued statements, or is such that
it is easily converted to the correct syntax for continued
statements in the target language.  (We illustrated with an
example in FORTRAN.)

If the target language is free format and requires no
continuation symbol (like PL/I, PASCAL, or ICON are), there is no
problem at all: the *.PUN file (probably prepared with INDENT Y
specified) is ready to run.  If the language does require a
continuation symbol in a particular column (like ASM, SNOBOL, and
FORTRAN do), you just define tab tokens and develop a
post-processing scheme to be used to treat the *.PUN output
(probably prepared with INDENT N specified) to convert it to the
required format.  While this does require the preparation of a
program or edit macro to do the job, the post-processing soon
settles into a routine which is quite workable.  The whole method
serves to bring some of these awkward languages under the control
of a structured programming regimen where all the benefits
accrue.  A macro for a powerful editor is a very easy way to
manage these post-processing tasks because you don't have to be
concerned with remembering the details of any messy process and
you only have to get it right once for each language you will
use.

There is the question of how to arrange the series of nodes which
together constitute a continued target language statement.  You
can just put the series of statement continuations in successive
Warnier nodes at the same level as the first, or put the series
of continuations as a set of children of the first line of the
long statement, or even put each continuation as a child of the
previous, so that the whole set strings out across the diagram.
It doesn't make much difference which way you do it.  With a
fixed format target language run with INDENT N, there is no
difference at all in the *.PUN file.  In a free format language
run with INDENT Y, the latter method will have the continuations
indented one more character than the original.  Personally, I
usually decide which method to use based on which will produce
more pleasingly filled pages on the printed Warnier diagram and
which will encourage congenial pagination.  Whichever way you
chose, you can use '+' symbols in infix fields and/or prefix
fields to indicate the continuation relationship in the diagram.


                            HELPFUL HINTS                13-3

C. Creating Depth-First <fn>.SRC File

Sometimes, especially if the program is large and the design
process involved a great many rearrangements of code segments, it
can become difficult to find statements in the input file.  If
there are passages of superficially similar code, this can lead
to a disastrous mistake in which passage to alter.  Code passages
close to one another in the diagram are best close to one another
in the input stream.  If they are scattered, the situation can be
remedied by specifying 'SRCPUNCH Y' as a control parameter.  As a
result of this, SPA:WN will create a file, <fn>.SRC, which is a
rearrangement of the input file in depth-first order.  In this
file, the nodes occur in a specific order, and you will find
nearby families nearby in the source stream.  The file created in
this way is quite filled with SPA:WN percent characters, which
were introduced to control the separation of the nodes into
individual lines when printed in the Warnier diagram.  It is also
over-disambiguated.

D. Recursion, Parallel Processing, State Machines

There are occasions where the big story about structured
programming resulting in programs whose static structure and
dynamic structure are in close correspondence simply breaks down.
The three keywords of the section title reference some typical
situations.  While it can be argued that Warnier diagrams are
inadequate to represent the kinds of complex logic which can
arise dynamically in these programming styles, it is still useful
to use SPA:WN to create the best possible code and documentation
which it is capable of producing.  Auxiliary documentation
detailing the working of the program from an appropriate
viewpoint which encompasses the dynamic activity would be a
required supplement.

In a recursion, one procedure calls itself or several procedures
call one another to perform the required task.  The recursive
invocations may proceed through several levels.  If the situation
is at all complex, with different points in any one invocation
which may make a further call, a great deal of information is
stored implicitly in the local variable values and the addresses
at which processing is to be resumed on return from the deeper
invocations.  This whole complex of information is built
dynamically in a dimension which the static code structure
doesn't even have a hope of representing.

In parallel processing, you create subtasks which go off on their
own to do their work independently of one another.  The
coordination of the subtasks requires understanding of timing
phenomena and synchronization, again matters far beyond the scope
of a static presentation of the code structure.


                            HELPFUL HINTS                13-4

When a large variety of different context sensitive program
responses to a variety of different inputs are required, it is
often valuable to create a state machine to manage the
processing.  Different levels of contexts can be maintained by
nesting state machines.  This general style of programming is
supported by a case statement inside a loop.  Each program action
occurs within one execution of a case statement, and the next
case selection is made in the next execution of the containing
loop.

An initial state is used to start things up arbitrarily.  After
that, an input token always determines the value of the next
state.  The program code implementing the action for each state
is entered as a result of the case statement's selection of a
particular branch, the appropriate action taken, and the next
input token is accepted to determine the next machine state.  In
the next loop iteration that next state is entered, its action
taken, a token accepted, and the next state determined.  Because
each succeeding state is determined both by the value of the next
token and the current state, a very general context sensitive set
of responses can be programmed.  Once again, the view of the
program one can gain from the static program structure hardly
even begins to reveal what may be going on.  In the case
statements, it makes no difference at all what order the
alternative passages of code appear in.  This use of a procedural
language to implement a state machine completely undercuts the
basic assumption of SPA:WN and Warnier diagrams, i.e. that there
is a relatively fixed procedure for solving a problem.

While all these examples represent cases where the actions of the
program must be understood at a higher level or from a different
viewpoint that than of a Warnier diagram, it is still possible
and desirable to develop programs of these kinds using SPA:WN.
It is just that in addition to the documentation and code
developed using SPA:WN there must also be some higher level
documentation explaining the program from an appropriate vantage
point.  Developing the internal logic of the code and desk
checking it in each level of recursion, independent task, or
machine state is perfectly feasible and appropriately done from
SPA:WN.  Auxiliary field values or comments can be employed to
help the reader understand the connection between the components
presented in the Warnier diagram and the overview presented in
the accompanying higher level documentation.


                        14. PROGRAM ALGORITHM

Most readers will have little reason to learn about the algorithm
which SPA:WN employs to do its work.  This chapter is included
for those few with overwhelming curiosity and for those few who
may need to understand things well enough to have a good shot at
making program modifications for some private reason.  If you
want to try to follow the following description in the Warnier
diagram of the SPA:WN program, the first thing to do is to obtain
a printed copy of it.  The SPA:WN source code is provided in the
form of SPA:WN input (in PWARN.WAR) for this purpose.  Simply
issue 'SPAWN PWARN'.  Note, however, that SPA:WN will not run
itself on a computer equipped only with 360K floppy disks -- the
aggregate size of the output files exceeds the capacity of such
floppy disks.

The PWARN program proceeds in a number of distinct stages.  The
first stage accepts the source stream; the second outputs the
target language and depth-first SPA:WN source stream, as
requested; the third constructs a trial Warnier diagram layout on
indefinitely large virtual paper and generates realistic page
candidates; the fourth, if the root segment of the diagram is not
(yet) page-sized, does page selection from the candidates and
loops to the third stage for a new layout on a smaller piece of
virtual paper; once the root page is small enough, the final
stage prints the separated pages in depth-first order and
provides cross references between subpages and parent pages.

The input stage requires little comment.  During input, the
Warnier diagram is built as a general tree using son, brother,
and father pointers.  Simultaneous with the construction of the
Warnier tree during input, a binary search tree is constructed
using the lexical values of the Warnier nodes.  When the location
of each parent in the Warnier tree is needed, the binary search
tree is employed to find it so that its son pointer can be filled
in.  The input records are stored in fairly large "pages", for
which storage is obtained on an as-needed basis.  This allows
SPA:WN to run small diagrams in a small machine and yet expand to
do a large diagram in a large machine.

The production of target language output is achieved in a
recursive routine which traverses the Warnier tree.  The entire
value of a node is output at preorder time (i.e. prior to
visiting any children) if there is no '%---%' separator but, if
that separator is present, only that portion which precedes it is
output at preorder time, and that portion which follows it is
retained for output at postorder time (i.e. after return from
visiting the children).  A fairly similar recursive routine
produces the depth-first source file.


                            PROGRAM ALGORITHM            14-2

Establishing the logical layout of the Warnier diagram is the key
task of the algorithm.  This is done in a recursive routine,
LAYOUT, which provides an excellent example of the difficulty of
understanding the cooperative action of a number of levels of
recursion from the static view of the recursive routine.  Each
tentative layout is done in an indefinitely large space even
though output will ultimately be restricted to DIAGCOLS columns
by DIAGPAGEL lines.  When a tentative layout is oversize,
portions of it are selected for presentation as separate pages,
and the residual diagram reformatted to see if it has been
reduced to page size.

Since subtrees are subject to arbitrary selection as separate
pages, every subtree must be formatted as pleasingly as possible.
To this end, two conventions are established: 1) keep each parent
and its set of children centered on each other and 2) keep
brothers as closely clustered in the layout as the shape of the
tree permits.

When pagination is required, all page candidates which are
subtrees of more favored page candidates in a priority queue are
eliminated.  Proper selection of a subset of the remaining
candidates as pages is pretty sensitive because of the wide range
of tree shapes and page sizes which may be encountered.  We limit
acceptance of pages at each stage to the best ones to avoid
ridiculously small or unnecessary pages, while accepting some
minimum number to guarantee progress.  The accepted pages are
logically separated from the main body of the Warnier tree and
replaced by a new Warnier node whose value is '**SEE PAGE'.  This
logical disconnection of the subpage prevents any penetration
into the subtree, now a page, in subsequent iterations of the
layout routines.  The parent node of the subtree and the forward
reference node will take much less space on the next pagination
pass than the subpage they replace.  They will be repositioned in
later iterations of layout and will ultimately be output on the
hierarchically superior page arising in a different pagination
pass.  Since pages are isolated bottom up in the Warnier tree,
and hierarchically superior pages are formatted to accommodate
forward references, not whole subpages, the diagrams are compact
at every hierarchical level.

Determination of the order of appearance of the pages and
assignment of page numbers is done by ordering the selected pages
on their Dewey decimal locators during page selection and
sequentially numbering them after layout terminates.

The output routine windows on the (column, line number)
coordinate determined for each page in the pagination pass at
which it was isolated and presents the layout determined for it
at that time.  Each page output is produced by parallel level
order traversal, i.e. in each line each column in turn is
considered, producing whatever brace part and node content part
is appropriate in that line.  The details of production of the
output pages are managed by two state machines in each column, a
brace production state machine and a node production state
machine, aided by a system of column descriptors and set
descriptors for the page.  Independent progress of each of these
machines through its paces allows arbitrary relative placement of
all nodes on the output page.


              15. DESPERATE TOPICS FOR DESPERATE PEOPLE

A. Retrofitter Concept

Building Warnier diagrams from the ground up for new programs is
only a little piece of the solution to the problem faced by many
large programming shops.  In shops where there is a program
library built up over many years, maintenance and upgrading of
old, long-forgotten program code is more time consuming than new
program development due to the sheer volume of maintenance work
and the inherent difficulty of relearning old programs' logic.
To attack this problem, what is needed is a way to take existing
programs and bring them into the SPA:WN methodology, i.e. to
retrofit old programs into SPA:WN.

This presents an intricate, but not impossible, challenge.  For
structured languages which boast structure-opening and
structure-closing keywords for every structured construct and
limit their input stream to a single statement per line of source
code (three cheers ... ! ! ! ... for dBASE in this dimension),
writing a retrofitter is pretty straight-forward.  You just have
to maintain a stack of information about the status at each
logical level of the program being retrofitted, parse the input
stream to detect when pushing and popping the stack are
indicated, keep a queue of statements awaiting output at each
level until such time as the whole program is parsed and all
structured constructs are completed, and then output the whole
mess with appropriate punctuation and all-pervasive
disambiguation in level order.  Automatic generation of -XOR-
infix fields between THEN and ELSE clauses and between the
elements of CASE statements is feasbile, too.

If programs to be retrofitted are very large, keeping the queues
may involve outputting all statements at each level to a separate
temporary output file, and then concatenating those files to
produce a top-down, level-order input stream to SPA:WN.  The
so-obtained Warnier diagrams provide a point of departure for
maintenance and for modernization of the structure of the old
programs in the progrm library.  If the level-order SPA:WN input
seems awkward, it can be converted to depth-first by a SPA:WN run
specifying 'SRCPUNCH Y' as a parameter.

When the existing program is in a language which does not have
structure closing keywords for every structured construct, or
when there may be multiple statements on a single line of code,
the parsing to determine when changes of logical level have
occurred is more difficult, but essentially the same overall
program structure will still work.  You have to maintain
countdowns of events at a logical level so that you can recognize
the completion of a structured construct which lacks an explicit
structure closing keyword.


                  DESPERATE TOPICS FOR DESPERATE PEOPLE  15-2

The success of retrofitting will be heavily dependent upon the
extent to which structured programming practices were employed
when the program was originally written.  If the old code is
essentially GOTOless, there is a good chance that retrofitting
will give a workable diagram which will serve as a point of
departure for structural improvement in the SPA:WN mode.  There
is a strong tendency for retrofitted programs to contain very
long sequences of statements, which result in `pagination failed'
messages unless very large DIAGPAGEL parameters are fed.

While it would be a major investment of time and effort to
retrofit whole program libraries in this way, programs which are
in heavy use and which require frequent maintenance would very
likely repay the effort in terms of increased maintainability and
reduced maintenance effort, and might even be improvable in
respect to reducing their execution time.

B. Delimiter Saturation and Escape Characters

If you have a target language program which uses so many
characters of various kinds in literals that there really aren't
any characters left for use as SPA:WN punctuation marks, some
desperate measure must be devised to allow work to go forward.
One way to accomplish this is to pick an arbitrary character
sequence to stand for each of four rarely used characters in the
target language.  These sequences would not contain the actual
punctuation marks themselves.  For example, to free the
characters in the set {!$\~} for use as SPA:WN {"%,;}, you could
use '#e', '#d', '#b', and '#t' to represent them in the target
language statements.  Here the '#' is used as an escape character
to signal that the following letter has a special significance
and the 'e', 'd', 'b', and 't' are the first letters of
'exclamation', 'dollar', 'backslash' and 'tilde'.  It is assumed
that these #<letter> combinations never appear in their own right
in the target language code.  Then the only uses of any of the
characters in the set {!$\~} in the SPA:WN input stream would be
as the SPA:WN delimiters.  The <fn>.PUN file will contain the
#<letter> substitutes.

The conversion of the target language code with these substitutes
in it to contain the real characters is easily accomplished by an
edit macro or by a series of global changes which converts all
instances of each token to the proper character.  This approach
suffers from a loss of readability of the Warnier diagram, but
this is not serious if characters which appear very infrequently
are selected for this treatment.  This approach is closely akin
to that used to provide proper indention for fixed format target
languages, except that a two character token instead of a single
character tab token is employed.  The idea of token use and
replacement in a post-processing step can be further generalized,
but it is hard to imagine what situation might require it.


                          16. GLOSSARY

< > -- Metasymbols indicating that the enclosed text describes
   what manner of information is to be placed in its place in the
   syntax being described.

( ) ... -- Metasymbols indicating that the enclosed structure may
   be indefinitely repeated in its context.

[ ] -- Metasymbols indicating that the included information is
   optional.

Alternation -- Alternation is one of the elementary program
   structures, in which one of a set of alternative code passages
   is selected for execution.

Auxiliary Fields -- Descriptive fields associated with Warnier
   nodes which can be used to annotate the diagram for enhanced
   precision as a documentation device.  SPA:WN provides for
   prefix, infix, and repetition fields.

Body -- The embedded structured passage of code which is
   repetitively or conditionally executed under control of a
   parental repetition or alternation structured construct.

Branch -- A segment of code (equivalently, a subtree of the
   Warnier diagram) which exists as a logical unit in the Warnier
   diagram or program code.

Child Node -- A hierarchically inferior node in a Warnier
   diagram.  It appears with any brothers under a brace which
   points to their parent at their left.

Conditioned Branch (GOTO) Statement -- A branch in the execution
   of a program which is taken or not taken in accord with the
   value of a logical expression which controls it.  Conditioned
   branches are the elementary actions out of which the
   alternation and repetition constructs are built in low level
   unstructured languages.

Control Parameters -- The keywords and associated values
   appearing first in the input stream to SPA:WN which modify the
   behavior of SPA:WN when it produces a Warnier diagram and
   associated outputs.

Default -- The value or action which is in effect in the absence
   of user specification of some parametric value or action.

Depth-First Order -- An order of presentation of the nodes of a
   tree in which every node's child is presented before its next
   brother.  This results in close proximity of the statements of
   a branch of the tree and relatively large separation of
   statements of different branches of the tree.

External Subroutine -- A subroutine complied separately from, and
   later linked to, the other routines of a program.

Infix Field -- An auxiliary field associated with a node in a
   Warnier diagram and appearing in the output diagram between it
   and its next brother.  Specified between the commas after the
   node value in the input stream on a child node.


                              GLOSSARY                   16-2

Interior Nodes -- All the parent or non-leaf nodes of a Warnier
   diagram.

Internal Subroutine -- A subroutine appearing within the confines
   of the main program, compiled with it, and automatically
   accessible from it.

Iteration -- An elementary structured construct.  See Repetition.

Keyword -- A word employed in a processor's context to convey a
   particular meaning to the processor.

Leaf Nodes -- The nodes in a Warnier diagram which appear only as
   child nodes; they have no children or further descendants.

Metasymbols -- Symbols employed to describe a syntactic feature.
   Metasymbols are not included in the actual written language.

Node -- An entry in a Warnier diagram, roughly mapping to a
   statement in the target language.

Null Comment -- A comment in a target language without any
   contents, used to delimit sets of children and space out
   diagrams and target language code in one conventional use of
   SPA:WN.

Pagination -- The process or result of splitting a large Warnier
   diagram into individual pages for presentation on paper.

Pagination Pass -- The count of the iteration instance at which a
   particular page of the output diagram was selected as such.

Parent Node -- A hierarchically superior node in a Warnier
   diagram which heads a list of hierarchically inferior (child)
   nodes.  A parent node appears to the left in Warnier diagrams,
   with its children arrayed vertically to its right, grouped
   under a brace.

Patch -- A temporary fix of code at a lower level than the usual
   level of operation, as in a "source code patch" or an "object
   code patch".

Postorder Time -- The time during the Warnier tree traversal for
   target language code generation (after child visitation) at
   which that part of a node appearing after the '%---%' (SPA:WN
   percents) delimiter is output to the target language output
   stream.

Postorder Traversal -- A tree traversal regime in which a parent
   is visited only after all its children are visited.

Post-processing -- A usually relatively minor separate processing
   stage run after principal processing is completed.  Post-
   processing can effect indention and token substitution in the
   target language code after SPA:WN has produced it to effect
   minor adjustments to meet target language requirements.


                              GLOSSARY                   16-3

Prefix Field -- A auxiliary field associated with a node in a
   Warnier diagram and appearing in the output diagram between
   the brace and the node value.  It appears in the input stream
   before the first SPA:WN comma on child nodes.

Preorder Time -- The time during the Warnier tree traversal for
   target language code generation (before child visitation) at
   which that part of a node appearing before the '%---%' (SPA:WN
   percents) delimiter (or the entire node if the delimiter does
   not appear) is output to the target language output stream.

Preorder Traversal -- A tree traversal regime in which a parent
   is visited before its children are visited.

Repetition -- Repetition is one of the elementary program
   structures, in which a code passage is repeatedly executed
   under control of some counter or logical expression.
   Sometimes named 'iteration'.

Repetition Field -- An auxiliary field associated with parent
   nodes of Warnier diagrams, often used to note the expected
   number of repetitions of a loop body or frequency of selection
   of an alternative.  It appears immediately after the node
   value in the diagram.  In the input stream it appears between
   the SPA:WN commas on parent nodes.

Root Node -- The parent node for the whole Warnier diagram.
   Sometimes used loosely to refer to the root of a subtree
   selected for presentation on a subpage of a Warnier diagram.

Sequence -- Sequence is one of the elementary program structures,
   in which a series of code passages is executed in their order
   of appearance.

SPA:WN -- Acronym for Structured Programming Automated: Warnier
   Notation.

SPA:WN Comma -- The punctuation mark employed to delimit prefix,
   node, infix, and repetition values in the SPA:WN input stream.
   Default is a natural comma (,).  Specified as 'COMMA ?' as a
   control parameter, where '?' is replaced by the desired field
   punctuation symbol.

SPA:WN Percent -- The punctuation mark employed to force a line
   within a node of the printed Warnier diagram in SPA:WN.
   Default is a natural percent (%).  Specified as 'PERCENT ?' as
   a control parameter, where '?' is replaced by the desired
   line-forcing punctuation symbol.

SPA:WN Quote -- The punctuation mark employed to delimit
   disambiguation strings in the SPA:WN input stream, where there
   would otherwise be lexically identical parent nodes.  Default
   is a natural quote (").  Specified as 'QUOTE ?' as a control
   parameter, where '?' is replaced by the desired disambiguation
   punctuation symbol.


                              GLOSSARY                   16-4

SPA:WN Semicolon -- The punctuation mark employed to close the
   set of children of an immediate family in the SPA:WN input
   stream.  Default is a natural semicolon (;).  Specified as
   'SEMI ?' or as 'SEMICOLON ?' as a control parameter, where '?'
   is replaced by the desired family-closing punctuation symbol.

Statement -- The basic unit of a computer language which programs
   the accomplishment of some elementary task, roughly
   corresponding to a node in a Warnier diagram.

Structured Construct -- A syntactic element in a programming
   language which provides for some flavor or variety of control
   of alternation or repetition, e.g.  IF ...  THEN ...  ELSE ...
   ENDIF, or DO WHILE ...  ENDDO.

Structured Programming -- A discipline which can lead to
   comprehensible, maintainable programs in a computer language.
   It is based on the fact that any program can be constructed
   from nested instances of sequence, alternation, and
   repetition.

Structured Programming Language -- A computer language which
   provides an adequate set of control structures for alternation
   and repetition, such that it encourages the use of structured
   programming practices.

Subtree -- A portion of a tree consisting of a node and all its
   descendants.

Syntax -- The punctuation rules and grammar which define legal
   statements in a computer language or process definition
   control stream.

Target Language -- The computer language in which the nodes of
   the Warnier diagram are written and in which SPA:WN produces
   code when 'PLIPUNCH Y' is specified as a control parameter.

Top-Down Order -- An order of presentation of the nodes of a tree
   in which no child is presented before its parent.

Top-Down Design -- A divide-and-conquer approach to program
   design in which a terse description of program mission is
   elaborated and subdivided in successive refinements until a
   workable design is achieved.

Tree -- An acyclic graph with a particular node (the root node)
   singled out as its origin and composed of hierarchically
   arrayed sets of descendants.

Warnier Diagram -- A two-dimensional tree-like display of the
   logical relationships between hierarchically arrayed, ordered
   sets of elements.


                          17. BIBLIOGRAPHY

[1] Michael Hammer and Gregory Ruth, "Automatic Programming"
    in Research Directions in Software Technology, MIT Press,
    Cambridge, Mass (1979)

[2] Jean-Dominique Warnier, Logical Construction of
    Programs, H.F.Stenfert Kroese B.V., Leiden, Holland
    (1974) and, in translation, van Nostrand Reinhold Co.,
    New York (1976)

[3] Ken Orr, Structured Requirements Definition, Ken Orr
    Associates, Topeka, KS (1981)

    Data Structured Systems Development Methodology, Ken Orr
    Associates, Topeka, KS (1982)

    David A. Higgins, Program Design and Construction,
    Prentice Hall, New York (1979)

[4] Warnier, op. cit., p 6.

[5] Donald E. Knuth, The Art of Computer Programming, Vol.I,
    p. 310, Addison-Wesley (1973)

[6] Ken Orr, op. cit.

    M.A. Jackson, Principles of Program Design, Academic
    Press, New York (1975)

    V. Weinberg, Structured Analysis, Yourdon, Inc., New
    York (1978)

    E. Yourdon, How to Manage Structured Programming,
    Yourdon, Inc., New York (1976)