=====================================================================
                               EZMRCI
                            version 1.00

            Easy access to MRCI compression/decompression

                Copyright (c) 1994 Julian M. Bucknall
=====================================================================

Introduction
------------

From a few questions posed on TurboPower's forum on CompuServe
(PCVENB, section 6) about the Microsoft Real-time Compression
Interface (MRCI, pronounced 'mercy'), I decided to write a simple
Borland Pascal wrapper unit that would allow access to Microsoft's
MRCI server as implemented in DoubleSpace. EZMRCI is the result.

MRCI is a set of APIs that allow a client (an application) to request
a server (the compression engine) to compress some data or conversely
to decompress some previously compressed data. The format used for the
compressed data is the Microsoft Real-Time Compression Format (MRCF);
ZIP, LZH, ARJ and the other normal compression format types are not
supported. The compression is said to be lossless, ie no information
is lost. If you compress a buffer and then decompress it you will have
exactly the same data.

The reason for writing a unit to support MRCI is that on many
computers nowadays (with DOS 6.0 and above) DoubleSpace is loaded to
'double' the capacity of the hard disk. DoubleSpace is the single best
known MRCI server (the other being the Microsoft Flash File System).
If you have DoubleSpace loaded, then by using this unit you can easily
take advantage of compression techniques without having to link a
complete compression engine into your program. The disadvantage is
that you do require DoubleSpace to be loaded!

Microsoft publish the MRCI specification on their Developer Network
CDROM, complete with a couple of documentation errors that stung me
when I was testing this unit. They hope that eventually an MRCI server
will be built into some kind of hardware, rather than completely in
software as at present. They also will send separately to ISVs
(Independent Software Vendors) the source code in C for the MRCI
(de)compression algorithm and also the MRCF format. A later version of
this unit might use these extra documents to implement MRCI in
Pascal/Assembler.

There are four services that an MRCI server typically provides:

  o  a query call: to return whether an MRCI server is present, and if
     so information about it.

  o  a compression call: to compress one buffer of data and to place
     the compressed data in another buffer.

  o  a decompression call: to decompress a buffer of compressed data
     and place the decompressed result into another buffer.

  o  an incremental decompression call: to decompress a portion of a
     compressed data buffer. This is an optimisation for DoubleSpace
     and has not been implemented in EzMRCI.

So, to recap, the EZMRCI unit will require an MRCI server to be
present before its (de)compression routines will work. In general this
means DoubleSpace must be have been loaded by DOS. Check your DOS
documentation about DoubleSpace.

EZMRCI can be used with all three targets for Borland Pascal 7.0:
real mode DOS, protected mode DOS and Windows. For the latter two
targets, it requires the use of my EZDPMI unit which can be
downloaded from the BPASCAL forum on CompuServe (look for EZDPMI.ZIP).


Declared types
--------------

type
  PMRCIInfo = ^TMRCIInfo;
  TMRCIInfo = record
    miVendor        : array [1..4] of char; {Vendor ID}
    miServerVersion : word;    {MRCI server version}
    miMRCIVersion   : word;    {MRCI version}
    miEntryPoint    : pointer; {MRCI (de)compress realmode entry point}
    miCapability    : word;    {Server capabilities}
    miHWAssisted    : word;    {Hardware assisted capabilities}
    miMaxBuffer     : word;    {Max buffer size, will be >= 8192}
  end;

A variable of this type is returned by GetMRCIInfo. The fields define
the information known about the MRCI server. miVendor is a four byte
vendor identification, Microsoft use 'MSFT'. miServerVersion is the
version number of the server driver, the major number is in the high
byte and the minor number in the low byte (if miServerVersion was
$0123, then the actual 'displayed' version would be 1.23).
miMRCIVersion is the version of the MRCI spec and works similarly to
miServerVersion. miEntryPoint is the direct-calling interface address
to the MRCI server. miCapability is a bit-mapped word defining what
this server can do (the bit settings are defined by the mrciCapXxxx
constants). miHWAssisted is a bit-mapped word defining what hardware
assisted capabilities the server may have, and uses the same bit
mappings. miMaxBuffer is the size of the largest buffer of data that
the MRCI server can (de)compress at one time.


Declared constants
------------------

const
  mrciErrSuccess        = 0;   {no error}
  mrciErrNotSupported   = 1;   {operation not supported}
  mrciErrBusy           = 2;   {MRCI server is busy, try again later}
  mrciErrBufferOverflow = 3;   {destination buffer is too small}
  mrciErrCannotCompress = 4;   {source buffer is incompressible}
  mrciErrBadFormat      = 5;   {source buffer is not in MRCI format}
  mrciErrBadBufferSize  = 99;  {Buffer is too large to (de)compress}

These are the error codes that will be returned by the routines in
this unit. A note on a couple of them will be in order. mrciErrBusy
means that the MRCI server is busy doing some other work (eg
compressing data for DoubleSpace itself for example) and you should
let it finish its current job first (in DOS, call Int $28; under
Windows, yield) as it is not reentrant. mrciErrCannotCompress means
that if the server were to compress the data, the compressed data
would occupy more space than the uncompressed data (eg you are
compressing an already compressed block, the block you are compressing
is too small). mrciErrBadFormat occurs when decompressing a block, and
generally means that the server overran the end of the block when
decompressing it - and *that* only occurs if you specified a block
that didn't contain compressed data or you got the uncompressed size
wrong.

const
  mrciCapNone       = 0;       {No capabilities}
  mrciCapCompress   = $0001;   {Can compress}
  mrciCapDecompress = $0002;   {Can decompress}
  mrciCapIncDecomp  = $0020;   {Can decompress incrementally}

The different capabilities of a MRCI server. These values will be
or'ed in the TMRCIInfo.miCapability field that's returned by
GetMRCIInfo. DoubleSpace returns $0023 as its capability word, ie it
supports all operations.


Interfaced routines
-------------------

Declaration
  function MRCIPresent : boolean;
Purpose
  Returns true if a MRCI server is loaded. The actual test occurs at
  unit initialisation time, this function returns the value of an
  internal boolean.

Declaration
  function GetMRCIInfo(var Info : TMRCIInfo) : word;
Purpose
  Returns a TMRCIInfo record structure that details data about the
  currently loaded MRCI server. The function either returns
  mrciErrSuccess (and the information record) or mrciErrNotSupported
  if there is no MRCI server or there is one but it cannot be used.
See Also
  TMRCIInfo type

Declaration
  function MRCICompress(var NormalBuffer;
                        var CompressBuffer;
                            NormalSize : word;
                        var CompressSize : word) : word;
Purpose
  Compresses a buffer containing uncompressed data (NormalBuffer) into
  another buffer (CompressBuffer). These buffers *cannot* be the same
  memory block. NormalSize is the number of bytes in NormalBuffer to
  compress. On exit, CompressSize will be the number of bytes of
  resulting compressed data in CompressBuffer if the function was
  successful (ie returns mrciErrSuccess).

  The function result is one of the mrciErrXxxx codes.

  WARNING: the MRCI spec explicitly states that CompressBuffer should
  be at least as large as NormalBuffer. My tests have shown that
  CompressBuffer should be at least 1024 bytes in size, although the
  spec doesn't mention it. Hence, internally, MRCICompress *assumes*
  that the size of CompressBuffer is the larger of 1024 or NormalSize.
  If you are trying to use a smaller CompressBuffer in the belief that
  the data will compress at least 50%, you may encounter a MEMORY
  OVERWRITE.

Declaration
  function MRCIDecompress(var NormalBuffer;
                          var CompressBuffer;
                          var NormalSize : word;
                              CompressSize : word) : word;
Purpose
  Decompresses a buffer containing compressed data in MRCF format
  (CompressBuffer) into another buffer (NormalBuffer). These buffers
  cannot be the same memory block. CompressSize is the number of bytes
  of compressed data. On input NormalSize is the expected size of the
  uncompressed data in bytes, and on return (if the function result is
  mrciErrSuccess) it will be the actual number of bytes. The function
  result is one of the mrciErrXxxx codes.

  WARNING: it is *your* responsibility to ensure that NormalBuffer is
  large enough to hold the uncompressed data, the MRCI server does no
  checking whatsoever. Also the MRCI decompress engine will use the
  expected number of bytes (which is input to the routine in
  NormalSize) to know when to stop decompressing. If you call this
  routine with an invalid value of NormalSize then either the MRCI
  server will not decompress enough bytes, or (perhaps worse) it will
  start decompressing garbage bytes.


WARNINGS (THIS MEANS YOU!!!)
--------

This unit, in the hands of inexperienced programmers or programmers
working too late at night, will cause memory overwrites (!). If you
suddenly find your programs crashing with wierd bugs that come and go,
check your calls to MRCICompress and MRCIDecompress. To recap:

  With MRCICompress, the size of CompressBuffer *must* be the larger
  of 1024 bytes or the size of NormalBuffer.

  With MRCIDecompress, NormalBuffer must be at least NormalSize
  bytes in size. Also make sure that NormalSize is correct, on entry
  it should be the number of decompressed bytes you are expecting,
  *not* the maximum size of NormalBuffer for example.

  Compressed data in MRCF format contains no redundant information,
  there's no byte sequences for identification, etc. This means that
  the MRCI server would quite happily decompress uncompressed data and
  produce complete garbage.

Remember that this unit uses the same compression engine that
DoubleSpace uses. If you manage to trash that engine somehow through
your passing bad, or invalid information to these routines, be aware
that you may also trash DoubleSpace. Use DOS 6.2 with the DoubleGuard
feature. Backup your DoubleSpaced disk frequently. Reboot on a crash.
Test, test and test your programs, again and again, preferably in the
debugger so that you can check parameters.


Tips, Hints and Miscellanea
---------------------------

Always store the compressed size and decompressed size with a
compressed buffer. So, for example, if you are compressing part of a
database record (for a database engine that supports variable length
records), make sure that you store the uncompressed and compressed
size of the record section with the uncompressed bit of the record. It
makes things much easier on decompression.

Be aware that if you write an app that uses MRCI compression for its
data, it will only work on a PC that has DoubleSpace loaded.

In protected mode DOS and Windows the maximum buffer size that can be
supported is 8192 bytes. This is because the memory for the MRCI
server must be in DOS memory, and this memory is preallocated in the
initialisation unit (and disposed of in an exit routine). The
GetMRCIInfo function will force this value in miMaxBuffer in protected
mode.

In protected mode, MRCIPresent could return false even though
DoubleSpace is loaded on the machine. The reason for this is that the
initialisation block failed to allocate some DPMI resource (a selector
or the required amount of DOS memory). In effect this means MRCI
cannot be used and hence MRCIPresent will return false.

The EZMRCI unit has only been tested with Borland Pascal 7.0 - if you
want to use it with other versions of Turbo Pascal, you're on your
own. It should work with TP 6.0 and TPW 1.5 however.

If you want to make some comments or bug reports, I can be reached on
CompuServe on [100116,1572].


Finally
-------

The EZMRCI unit is being released as freeware. That means you are
allowed to use it as is in your programs without paying me any money,
but I retain full copyright in the unit, the code in that unit and
this documentation. You may not sell the EZMRCI unit either as source
code or as a compiled unit file (TPU, TPP or TPW) or object file (OBJ)
or dynamic link library (DLL).

By using this unit in your programs you also agree to the following.
In no event will I be liable to you for any damages whatsoever
(including lost data, lost profits, and lost savings), including any
incidental or consequential damages, arising out of the use of or
inability to use this unit.


              Julian M. Bucknall, Colorado Springs, USA, February 1994

EZMRCI, the unit and this documentation, is
Copyright (c) 1994 Julian M. Bucknall
======================================================================