HIGH PRECISION TIMER
                                  DOCUMENTATION

                                   Version 5.5
                                January 14, 1990


                                  Public Domain
                          by Eagle Performance Software




   TIMERH High Precision Timer                      Documentation, Version 5.5



                       T A B L E   O F   C O N T E N T S

             Features .  . . . . . . . . . . . . . . . . . . . . . 3
             Distribution Files  . . . . . . . . . . . . . . . . . 3
             Demonstration . . . . . . . . . . . . . . . . . . . . 3
             Simple Programming  . . . . . . . . . . . . . . . . . 3
             How It Works  . . . . . . . . . . . . . . . . . . . . 4
             Support . . . . . . . . . . . . . . . . . . . . . . . 5
             Reference . . . . . . . . . . . . . . . . . . . . . . 5
             Revisions . . . . . . . . . . . . . . . . . . . . . . 6














































                                       2

   TIMERH High Precision Timer                      Documentation, Version 5.5


   FEATURES

   This high precision timer written in Pascal allows you to time events or 
   programs with 1 micro-second resolution up to 24 hours.  The program 
   simply uses the extended resolution of the Intel 8253/8254 timer chip 
   which is the same chip that generates an interrupt for the system timer 
   (every 1/18.2... seconds).

   Compatibility - TIMERH works on all IBM PC, XT, AT, PS/2, and 3270 PC 
   compatible computers.  The source code can be compiled with either Turbo 
   Pascal 5.0, 5.5, or QuickPascal.


   DISTRIBUTION FILES

   In this version, TIMERH55.ARC contains:

     TimerH  .pas:  Timer unit source code.
     TimerH  .doc:  This file.
     TimeDemo.arc:  Demonstration file to show elapsed time.


   DEMONSTRATION

   To get a feeling of the timer, let's run the demonstration program that 
   came with the utility.  Do the following steps:

     1. Make and run TIMEDEMO.PAS.
     2. Press RETURN for elapsed time since the beginning of the 
        program.
     3. Press ESC to quit the program.


   SIMPLE PROGRAMMING

   Basically, to time a given event in your program, the source code should 
   look like the following:

     ...
     begin
       ...
       Timer (Sync);   { Optional one time use }
       Timer (Start);
       ...
       { Code to be tested goes here. }
       ...
       Timer (Stop);
       ...
     end.

   Start - Timer(Start) resets the initial starting value of T1 so that all 
   subsequent splits will be referenced to this point in time.  You can use 
   this more that once.

   Stop - Timer(Stop) takes a split in reference to the last Timer(Start) 


   TIMERH High Precision Timer                                         Page 3

   TIMERH High Precision Timer                      Documentation, Version 5.5


   which changes the value of T2.  Subsequent uses of Timer(Stop) are 
   permitted, but there is a little overhead for its execution that is not 
   accounted.

   Sync - Timer(Sync), placed just before the first start, resets the timer at 
   a zero count.  It is recommended that you use the default Sync parameter 
   for consistent results.  The Sync parameter starts the chip timer zero.  
   This puts the next interrupt (which uses about 15-200 microseconds to 
   update the system timer) at 1/18.2 seconds away.  This makes quick events 
   (<1/18.2 seconds) uninterrupted.  Since the system timer is independent of 
   the real time clock, it doesn't affect the time of day on your computer.

   Overhead - The overhead for the elapsed time between the start and stop is 
   kept in the value T0.  The global value ElapsedTime excludes the overhead 
   after Timer(Stop).

   Jitter - Most events will be within plus or minus 3 microseconds depending 
   on your CPU.


   HOW IT WORKS

   To work both on IBM PC which use the 8253 chip and on the IBM AT using the 
   8254 chip, it is necessary to use  the common characteristics of both  
   chips:

     1. The output port to the timer for counter 0 which is a utility counter  
        is $43 and the input port is $40.  The latch code is $00 to read a 
        value from the chip.

     2. The system timer is a four-byte value and updated in memory at 
        0040h:006Ch, but only the first three bytes (21 bits) are used because 
        it only counts up to 1573040 (1800AFh) ticks per day.  At that 
        resolution, it only amounts to:

          1573040/(60*60*24) = 18.206481481 ticks/sec

     3. The chip counts down from $0000 negatively until it wraps to zero 
        again which then sends the usual interrupt every 1/18.2... seconds to 
        update the system timer in the BIOS data area.

     4. Using the chip ports, we can access and lock on to the count down 
        timer and get a value.  Since it has one full word in the count, the 
        total extended resolution of 16 bits is:

          1573040 * 2^16 = 103090749440 ticks/day
                         = 1193179.9704 ticks/sec

     5. This total resolution requires a five-byte value to hold the 37 bit 
        number.  If two days are needed in the calculation which is required 
        when passing midnight, a 38 bit value will be needed, but notice that 
        it never reaches the full 40 bits of five bytes.  This means that 
        6 byte reals are fully capable of handling the value with no loss in 
        resolution.



   TIMERH High Precision Timer                                         Page 4

   TIMERH High Precision Timer                      Documentation, Version 5.5


     6. Interrupt control while taking splits was a problem.  Since the chip 
        and CPU are independent, it is possible that the chip may try to send 
        an interrupt on the bus just as the OUT code is being executed.  The 
        chip will read 0-2 microseconds, but the DOS timer will be one tick 
        short.  An easy solution is to take two readings of the DOS timer low 
        byte and see if they differ - one before the chip is latched and 
        another after.  If they differ, an extra tick is needed for the system 
        timer part of the split only the timer value is small enough (<10000 
        microseconds) to confirm that the interrupt did occur.

     7. It is also important that no conditional statements are used in the 
        code so that the overhead is constant.

     8. The wake up mode of all timer chips is mode 3, but there is no way to 
        use mode 3 on the 8253 with software.  The 8254 chip made mode 3 
        superior with access to its status register, but software accessing 
        this register is incompatible with the IBM PC.  So, TIMERH initializes 
        with the common mode 2.  When the program is terminated, it is 
        restored back to mode 3 in case anything else may expect the default 
        mode.


   SUPPORT

   If you have questions, comments, or suggestions, the Eagle can be contacted 
   by four means - (1) CompuServe, (2) telephone, (3) The Eagle BBS, or 
   (4) mail.

   CompuServe - The most dependable way to contact the Eagle is through 
   CompuServe.  James (Jim) H. LeMay has written the Pascal version of TIMERH, 
   but the person to contact is Jordan Gallagher who can be contacted on the 
   Borland Forum by typing GO BPROGA from the CompuServe main menu.  You will 
   enter the Forum for Turbo Pascal.  You can contact Jordan with his PPN 
   number of 73557,2342.  Messages can also be left through EasyPlex.

   Telephone - Jordan can also be reached by phone at (214) 539-7855 on 
   weekdays and Saturday from 9:00 a.m. to 8:00 p.m CST.

   The Eagle BBS - You can also contact us on our 24-hour BBS at (214) 539-
   9878, 1200/2400 N81.

   Mail - For problems, please write:

       Eagle Performance Software
       P.O. Box 292786
       Lewisville, TX  75029-2786


   REFERENCE

   For more information on the Intel 8253/8254 timer chips, refer to the Intel 
   Microsystem Component Handbook, vol 2.  You can also call Intel literature 
   sales at 1-800-548-4725.




   TIMERH High Precision Timer                                         Page 5

   TIMERH High Precision Timer                      Documentation, Version 5.5


   REVISIONS

   Version 5.5 (01-15-90):
      Original release.





















































   TIMERH High Precision Timer                                         Page 6



         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 2,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                                 MC/Visa/AmEx

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.