STRG UTILITIES
                                 REFERENCE GUIDE

                                  Version 6.1b
                                 June 17, 1991


               Copyright (C) 1989-1991 Eagle Performance Software
                              All Rights Reserved.



                               _______                     
                          ____|__     |               (tm) 
                       --|       |    |------------------- 
                         |   ____|__  |  Association of    
                         |  |       |_|  Shareware         
                         |__|   o   |    Professionals     
                       -----|   |   |--------------------- 
                            |___|___|    MEMBER            



   STRG Utilities                               Reference Guide, Version 6.1b



                       T A B L E   O F   C O N T E N T S

        1. INTRODUCTION  . . . . . . . . . . . . . . . . . . . . . 4
             Purpose . . . . . . . . . . . . . . . . . . . . . . . 4
             Parameters  . . . . . . . . . . . . . . . . . . . . . 4
             Code Size . . . . . . . . . . . . . . . . . . . . . . 5
             Speed . . . . . . . . . . . . . . . . . . . . . . . . 5

        2. PROCEDURES AND FUNCTIONS  . . . . . . . . . . . . . . . 6
             AscStr  . . . . . . . . . . . . . . . . . . . . . . . 6
             ChrDel* . . . . . . . . . . . . . . . . . . . . . . . 6
             ChrFill . . . . . . . . . . . . . . . . . . . . . . . 7
             ChrPad* . . . . . . . . . . . . . . . . . . . . . . . 7
             ChrPos* . . . . . . . . . . . . . . . . . . . . . . . 7
             ChrQty* . . . . . . . . . . . . . . . . . . . . . . . 8
             ChrRepl*  . . . . . . . . . . . . . . . . . . . . . . 8
             Copy  . . . . . . . . . . . . . . . . . . . . . . . . 9
             Delete  . . . . . . . . . . . . . . . . . . . . . . . 9
             Is* . . . . . . . . . . . . . . . . . . . . . . . . . 9
             LnStr . . . . . . . . . . . . . . . . . . . . . . . . 10
             LoCase  . . . . . . . . . . . . . . . . . . . . . . . 11
             Pos . . . . . . . . . . . . . . . . . . . . . . . . . 11
             StrAsc  . . . . . . . . . . . . . . . . . . . . . . . 11
             StrLn . . . . . . . . . . . . . . . . . . . . . . . . 12
             Str*  . . . . . . . . . . . . . . . . . . . . . . . . 12
             StrBin  . . . . . . . . . . . . . . . . . . . . . . . 13
             StrBrk  . . . . . . . . . . . . . . . . . . . . . . . 13
             StrCat* . . . . . . . . . . . . . . . . . . . . . . . 13
             StrCmp* . . . . . . . . . . . . . . . . . . . . . . . 14
             StrCopy . . . . . . . . . . . . . . . . . . . . . . . 14
             StrCut  . . . . . . . . . . . . . . . . . . . . . . . 15
             StrDeTab  . . . . . . . . . . . . . . . . . . . . . . 15
             StrEnum . . . . . . . . . . . . . . . . . . . . . . . 15
             StrFill . . . . . . . . . . . . . . . . . . . . . . . 15
             StrHex  . . . . . . . . . . . . . . . . . . . . . . . 16
             StrIns  . . . . . . . . . . . . . . . . . . . . . . . 16
             StrJ* . . . . . . . . . . . . . . . . . . . . . . . . 17
             StrLwr  . . . . . . . . . . . . . . . . . . . . . . . 17
             StrMemb . . . . . . . . . . . . . . . . . . . . . . . 17
             StrMove . . . . . . . . . . . . . . . . . . . . . . . 18
             StrOvr  . . . . . . . . . . . . . . . . . . . . . . . 18
             StrPeek . . . . . . . . . . . . . . . . . . . . . . . 18
             StrPoke . . . . . . . . . . . . . . . . . . . . . . . 19
             StrPos* . . . . . . . . . . . . . . . . . . . . . . . 19
             StrQty* . . . . . . . . . . . . . . . . . . . . . . . 20
             StrRepl*  . . . . . . . . . . . . . . . . . . . . . . 20
             StrReTab  . . . . . . . . . . . . . . . . . . . . . . 21
             StrRev  . . . . . . . . . . . . . . . . . . . . . . . 21
             StrRoll . . . . . . . . . . . . . . . . . . . . . . . 21
             StrSort . . . . . . . . . . . . . . . . . . . . . . . 22
             StrSpn  . . . . . . . . . . . . . . . . . . . . . . . 22
             StrUpr  . . . . . . . . . . . . . . . . . . . . . . . 23
             UpCase  . . . . . . . . . . . . . . . . . . . . . . . 23


                                       2

   STRG Utilities                               Reference Guide, Version 6.1b


             ValBin  . . . . . . . . . . . . . . . . . . . . . . . 23
             ValHex  . . . . . . . . . . . . . . . . . . . . . . . 23
             Wrd*  . . . . . . . . . . . . . . . . . . . . . . . . 24
             WrdParse  . . . . . . . . . . . . . . . . . . . . . . 25
             WrdPos* . . . . . . . . . . . . . . . . . . . . . . . 25
             WrdQty  . . . . . . . . . . . . . . . . . . . . . . . 26
             WrdToken  . . . . . . . . . . . . . . . . . . . . . . 26

        3. VARIABLES . . . . . . . . . . . . . . . . . . . . . . . 28
             Global  . . . . . . . . . . . . . . . . . . . . . . . 28
             Local . . . . . . . . . . . . . . . . . . . . . . . . 29

        4. ACCESSIBLE MEMORY . . . . . . . . . . . . . . . . . . . 30

        5. QUICK REFERENCE . . . . . . . . . . . . . . . . . . . . 31









































                                       3

   STRG Utilities                               Reference Guide, Version 6.1b


   1.  I N T R O D U C T I O N


   PURPOSE

   This document is a STRG technical reference manual describing each routine 
   and variable in detail in a format similar to the Borland manual.  The 
   routines are described in alphabetical order.  Since this manual is on 
   disk, you can find your interest easily with a search utility.

   Application - All STRG procedures process strings with high-speed optimized 
   assembly code.  To be as fast as possible, almost all routines are 
   procedures rather than functions to increase speed 2 to 3 times.


   PARAMETERS

   Common Parameters - Most procedures use the same parameters.  Rather than 
   repeating them for each routine, detailed descriptions for those parameters 
   are listed below.

     Count    - number of characters or substrings to copy.
     Decimals - number of digits to the right of the decimal.
     Dest     - Pascal destination string (as opposed to source).
     Field    - number of digits in the field.
     Find     - a character or substring to find in a source string.
     Index    - the starting offset in the Pascal source string.
     MaxLen   - the maximum length permitted for the resulting string to 
                prevent overwriting memory.
     Nth      - process until the "Nth" occurrence.
     Repl     - replacement character or substring.
     S        - Pascal source string.
     Source   - Pascal source string (as opposed to destination).

   Order of Parameters - Of course not all of these parameters may be used, 
   but the order of the parameters is consistent throughout the routines.  
   Here is the general order:

     1. Destination - such as Dest
     2. Source      - such as S and Source
     3. Substrings  - such as Find, Repl, Fill, First, and Last
     4. Index       - always of the source
     5. Count       - such as Count, Field, Nth and Qty
     6. Maximum     - maximum length of destination string 

   This arrangement matches that of C.  For procedures, if there is a 
   destination, it is always the first parameter; just like the assignment, 
   (":=") the destination is always on the left.

   Index - All index parameters are 1-based.  If a zero is entered, it is 
   converted to 1.  The Delete procedure is the only exception to this, but it 
   is part of standard Pascal.




   Chapter 1, Introduction                                             Page 4

   STRG Utilities                               Reference Guide, Version 6.1b


   CODE SIZE

   Unit Size - If you use a STRG procedure, only the corresponding object file 
   containing that procedure will be linked and thereby optimizing the code.  
|  Even if all 111 procedures are used, STRG is still quite small at a total 
|  of about 6.3k bytes.  In all, there are 78 object files used to create the 
|  unit which is about 5900 lines of assembly or 250k of code.

   Code Usage - This Shareware unit has been released with the $N+ and $E+ 
   compiler directives set.  This means that an additional 12k of code is 
   included for the IEEE reals library inserted by the compiler.  The IEEE 
   reals are used in the Str* numeric formatting functions and are enabled for 
   your testing.  Should you not want to use these functions and are a 
   registered user, you can turn off these directives at the beginning of the 
   STRG unit.  This will drop the IEEE library from the executable code.


   SPEED

   Speed Bench - How fast is fast?  To have a basis for comparison, a unit of 
   strings-per-second (str/sec) is used for a relative measure of speed.  To 
   get this rating, a routine is repeated with a FOR loop to operate on a 
   given string and any "reset" of the original string is subtracted out as 
   overhead.  The RATE61.PAS program can duplicate this for you so you can 
   bench test your own routines for actual speed.  Overall, if you use STRG 
   for your application, your speeds will easily be 3 times faster or more.

   Relative Speed - The ratings mentioned in the Reference Manual are speeds 
   obtained from actual bench test on an 80386 / 20 MHz machine.  Granted, 
   that this may be faster than most units, but the important aspect of these 
   ratings is relative speed.  By comparing ratings with other routines in 
   this unit, you can judge how to best assemble a program technique that can 
   suit your needs.

   Processing Rating - Not only can machines vary in speed, but the string 
   values in your program are complete variables.  When given a routine like 
   StrPosL, the test performed is on an 80-character string with a 5-letter 
   word at the end of the string.  So the test forces the routine to search 
   the entire string.  This provides a worst case scenario to give you a feel 
   for the length of time for an operation.  Similarly, StrPosR is tested with 
   the 5-letter word at the beginning of the string and so the ratings for 
   both routines are about the same.  But one of these routines may be much 
   better for your program from a strategic standpoint.  So, the rating 
   provided gives one of processing performance and not from the perspective 
   that a better rating means faster speed for your application.











   Chapter 1, Introduction                                             Page 5

   STRG Utilities                               Reference Guide, Version 6.1b


   2.  P R O C E D U R E S   A N D   F U N C T I O N S

   In this section, a detailed description is provided for each procedure and 
   function.


   ---------------------------------------------------------------------------
   AscStr procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Creates ASCIIZ strings from Pascal-type strings.
   Declaration    AscStr (VAR AscDest; S: string)
   Remarks        After AscStr is executed, the global variable AscDestPtr is 
                  updated to point to the next destination address just after 
                  the null.  Source and destination can be the same.  As in 
                  all move-type procedures, it is important to make sure the 
                  destination size is sufficient to fit the source.
   Rating         42,900 str/sec
   See also       LnStr, StrAsc and the variable AscDestPtr.
   Example        Pack three Pascal strings into an array of ASCIIZ strings.

                    uses strg;
                    var
                      S: array[0..4] of string;
                      A: array[0..26] of char;
                      i: byte;
                    begin
                      S[1] := 'Eagle';
                      S[2] := 'Performance';
                      S[3] := 'Software';
                      AscDestPtr := @A;
                      for i:=1 to 3 do
                        AscStr (AscDestPtr^,S[i]);
                    end.

                  The resulting array A would look like:

                    'Eagle'#00'Performance'#00'Software'#00

   ---------------------------------------------------------------------------
   ChrDel* procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Operates on a string to delete a given character.
   Declaration    ChrDel  (VAR S: string; Find: char)
                  ChrDelL (VAR S: string; Find: char)
                  ChrDelR (VAR S: string; Find: char)
   Remarks        ChrDel deletes all finds in the entire string.
                  ChrDelL deletes only left (or leading) finds.
                  ChrDelR deletes only right (or trailing) finds.
   Rating         ChrDel:    9,400 str/sec
                  ChrDelL:  39,000 str/sec
                  ChrDelR: 132,000 str/sec
   See also       StrCut
   Example        Try these examples:



   Chapter 2, Procedures and Functions                                 Page 6

   STRG Utilities                               Reference Guide, Version 6.1b


                    MyString := '   more info ';
                    MyNumStr := '1,234,567';
                    ChrDel  (MyNumStr,',');    { MyNumStr='1234567'      }
                    ChrDelL (MyString,' ');    { MyString='more info '   }
                    ChrDelR (MyString,' ');    { MyString='more info'    }

   ---------------------------------------------------------------------------
   ChrFill procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Fills a string with multiple copies of a character.
   Declaration    ChrFill (VAR S: string; Fill: char; Count: byte)
   Remarks        The fill overwrites S with Count number of repetitions of 
                  Fill and automatically sets the length byte.  Be sure the 
                  destination is large enough.  Up to twice as fast as using 
                  system.fillchar.
   Rating         53,400 str/sec
   See also       StrEnum, StrFill
   Example        Try the following example:

                    ChrFill (S,'a',5);    { S='aaaaa' }

   ---------------------------------------------------------------------------
   ChrPad* procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Pads a string on the left, right, or to center with a given 
                  character to fill a field.
   Declaration    ChrPadC (VAR S: string; Fill: char; Field: byte)
                  ChrPadL (VAR S: string; Fill: char; Field: byte)
                  ChrPadR (VAR S: string; Fill: char; Field: byte)
   Remarks        ChrPadC pads left and right to center the field.
                  ChrPadL pads on the left (or leading) fill.
                  ChrPadR pads on the right (or trailing) fill.
   Rating         ChrPadC: 36,500 str/sec
                  ChrPadL: 42,900 str/sec
                  ChrPadR: 52,000 str/sec
   See also       ChrDel, StrCut, StrJ*
   Example        Try these examples:

                    MyStr := 'abcdefgh';       {        12345678901   }
                    ChrPadC (MyStr,'*',11);    { MyStr='*abcdefgh**'  }
                    ChrPadL (MyStr,'=',11);    { MyStr='===abcdefgh'  }
                    ChrPadR (MyStr,' ',11);    { MyStr='abcdefgh   '  }

   ---------------------------------------------------------------------------
   ChrPos* function                                                       Strg
   ---------------------------------------------------------------------------
   Function       Finds the position of a given character with match/ignore 
                  case.
   Declaration    ChrPosL  (S: string; Find: char; Nth: byte)
                  ChrPosLI (S: string; Find: char; Nth: byte)
                  ChrPosR  (S: string; Find: char; Nth: byte)
                  ChrPosRI (S: string; Find: char; Nth: byte)
                  ChrPosX  (S: string; Find: char; indeX: byte)
                  ChrPosXI (S: string; Find: char; indeX: byte)


   Chapter 2, Procedures and Functions                                 Page 7

   STRG Utilities                               Reference Guide, Version 6.1b


   Result type    byte
   Remarks        Using suffixes, -L routine searches from the left while the 
                  -R searches from the right for the Nth occurrence.  The -X 
                  routine starts at the given index and searches right for the 
                  first occurrence.  These routines match case, while those 
                  with the added -I suffix will Ignore case.
   Rating         ChrPos?:  25,400 str/sec
                  ChrPos?I: 22,500 str/sec  (non-alphabetic Find)
                  ChrPos?I: 10,200 str/sec  (alphabetic Find)
   See also       StrBrk, StrPos*
   Example        Try the following examples:

                    S1 := 'C:\MySubDir\SubDir#2\myfile';
                    S2 := 'Eagle Performance Software';
                    MyByte := ChrPosR  (S1,'\',1);   { MyByte=21 }
                    MyByte := ChrPosLI (S2,'e',3);   { MyByte= 8 }
                    MyByte := ChrPosXI (S2,'s',8);   { MyByte=19 }

   ---------------------------------------------------------------------------
   ChrQty* function                                                       Strg
   ---------------------------------------------------------------------------
   Function       Counts the occurrences of a given character in 
                  a string with match/ignore case.
   Declaration    ChrQty  (S: string; Find: char)
                  ChrQtyI (S: string; Find: char)
   Result type    byte
   Remarks        ChrQty matches case while ChrQtyI ignores case.
   Rating         ChrQty:  23,100 str/sec
                  ChrQtyI: 22,500 str/sec  (non-alphabetic Find)
                  ChrQtyI: 10,200 str/sec  (alphabetic Find)
   See also       StrQty*, WrdQty
   Example        Given a string, S:='Eagle Performance Software', try the 
                  following examples:

                    MyByte := ChrQty  (S,'a');   { MyByte=3 }
                    MyByte := ChrQtyI (S,'e');   { MyByte=5 }

   ---------------------------------------------------------------------------
   ChrRepl* procedure                                                     Strg
   ---------------------------------------------------------------------------
   Function       Finds and replaces a character from a given index for a 
                  specified number of replacements with match/ignore case. 
   Declaration    ChrRepl  (VAR S: string; Find,Repl: char; Index,Qty: byte)
                  ChrReplI (VAR S: string; Find,Repl: char; Index,Qty: byte)
   Remarks        The operation starts from Index and goes to the right.  It 
                  will stop if the index is beyond the end of string or it has 
                  replaced as many as it can.  ChrRepl matches case while 
                  ChrReplI ignores case.
   Rating         ChrRepl:  21,300 str/sec
                  ChrReplI: 20,300 str/sec  (non-alphabetic Find)
                  ChrReplI: 10,000 str/sec  (alphabetic Find)
   See also       ChrDel*, StrRepl*
   Example        Try the following example:



   Chapter 2, Procedures and Functions                                 Page 8

   STRG Utilities                               Reference Guide, Version 6.1b


                    S := '/s -12 -cga /off';
                    ChrRepl (S,'-','/',1,255);   { S='/s /12 /cga /off' }

   ---------------------------------------------------------------------------
   Copy function                                                          Strg
   ---------------------------------------------------------------------------
   Function       Returns a substring of a string.
   Declaration    Copy (S: string; Index,Count: integer)
   Result type    string
   Remarks        It's the exact replacement of the System.Copy function, but 
                  automatically replaces it with one that is up to 34% faster.
   Rating         21,500 str/sec
   See also       StrCopy, StrOvr, Compiler reference manual

   ---------------------------------------------------------------------------
   Delete procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Deletes a substring from a string.
   Declaration    Delete (VAR S: string; Index,Count: integer)
   Remarks        It's the exact replacement of the System.Delete procedure, 
                  but automatically replaces it with one that is up to 5 times 
                  faster.
   Rating         39,300 str/sec
   See also       ChrDel*, StrCut, Compiler reference manual

   ---------------------------------------------------------------------------
   Is* function                                                           Strg
   ---------------------------------------------------------------------------
   Function       Character classification function.
   Declaration    IsAlNum  (C: char)   { Alpha-numeric }
                  IsAlpha  (C: char)   { Upper and lower case letters }
                  IsASCII  (C: char)   { Lower ASCII table }
                  IsCntrl  (C: char)   { Print control characters }
                  IsDigit  (C: char)   { 0 through 9 }
                  IsDos    (C: char)   { Valid DOS directory & wildcards }
                  IsFile   (C: char)   { Valid DOS file name }
                  IsGraph  (C: char)   { Black characters }
                  IsLower  (C: char)   { Lower case letters }
                  IsPath   (C: char)   { Valid DOS path & drive & subdirs }
                  IsPrint  (C: char)   { Printable characters }
                  IsPunct  (C: char)   { Punctuation marks }
                  IsReal   (C: char)   { Real numbers }
                  IsSigned (C: char)   { Signed integers }
                  IsSpace  (C: char)   { Space or line control }
                  IsUpper  (C: char)   { Upper case letters }
                  IsXDigit (C: char)   { Hex digits }
   Result type    boolean
   Remarks        These exactly duplicate the C implementation of character 
                  classification, but a few are unique to STRG.  The best 
                  balance of speed and code is used for each one and they are 
                  more efficient than the use of sets.  All functions only 
                  consider characters in the lower ASCII table (<#128).  The 
                  function will return TRUE if the following characters are 
                  passed (the "-" means through):


   Chapter 2, Procedures and Functions                                 Page 9

   STRG Utilities                               Reference Guide, Version 6.1b



                    IsAlNum:   0-9 A-Z a-z
                    IsAlpha:   A-Z a-z
                    IsASCII:   Less than #128
                    IsCntrl:   #00-#31 #127
                    IsDigit:   0-9
                    IsDos:     ! #-* #45 #46 0-: ?-Z \ ^-{ }-~
                    IsFile:    ! #-) #45 #46 0-9 @-Z   ^-{ }-~
                    IsGraph:   #33-#126
                    IsLower:   a-z
                    IsPath:    ! #-) #45 #46 0-: @-Z \ ^-{ }-~
                    IsPrint:   #32-#126
                    IsPunct:   IsGraph but not IsAlNum
                    IsReal:    0-9 + Minus . e E
                    IsSigned:  0-9 + Minus
                    IsSpace:   Space #09-#13
                    IsUpper:   A-Z
                    IsXDigit:  0-9 A-F a-f

                  IsDos checks for characters that are valid when asking for a 
                  directory at the DOS command prompt such as:

                     C:\MySubDir\Subdir#2\All?.*

                  IsPath is the same as IsDos except it doesn't accept the 
                  wildcards '*' and '?'.  IsFile is the the same as IsPath 
                  except it will not accept the drive and path characters ':' 
                  and '\'.
   See also       StrMemb
   Example        Create a membership string containing only valid Real number 
                  characters:

                    S := '';
                    for MyChar:='+' to 'e' do
                      if IsReal (MyChar) then
                        StrCat (S,MyChar,255);     { S='+-.0123456789Ee' }

   ---------------------------------------------------------------------------
   LnStr procedure                                                        Strg
   ---------------------------------------------------------------------------
   Function       Creates ASCII TEXT strings from Pascal-type strings.
   Declaration    LnStr (VAR LnDest; S: string)
   Remarks        LnStr copies the characters of string S to the line 
                  destination Ln and terminates the line with a CR/LF 
                  (#13/#10).  After StrLn is executed, the global variable 
                  LnDestPtr points to the next destination after the CR/LF.  
                  As in all move-type procedures, it is important to make sure 
                  the destination size is sufficient to fit the source.
   Suggestions    The use of WriteLn for text files is disk intensive.  LnStr 
                  can be used together with BlockWrite for extremely fast text 
                  file operations.
   Rating         42,200 str/sec
   See also       AscStr, StrLn, and variable LnDestPtr
   Example        Similar to the example in StrAsc.


   Chapter 2, Procedures and Functions                                 Page 10

   STRG Utilities                               Reference Guide, Version 6.1b



   ---------------------------------------------------------------------------
   LoCase function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Converts characters to lower case.
   Declaration    LoCase (C: char)
   Result type    char
   Remarks        As the complement of UpCase, this routine converts 
                  characters in the range A..Z to lower case.
   See also       ChrReplI, StrLwr, StrUpr, UpCase

   ---------------------------------------------------------------------------
   Pos function                                                           Strg
   ---------------------------------------------------------------------------
   Function       Finds the position of a substring in a string.
   Declaration    Pos (Find,S: string)
   Result type    integer
   Remarks        It's the exact replacement of the System.Pos procedure, but 
                  automatically replaces it with one that is up to 340% 
                  faster.
   Rating         24,100 str/sec
   See also       ChrPos*, StrBrk, StrPos*, Compiler reference manual.

   ---------------------------------------------------------------------------
   StrAsc procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Creates Pascal strings from ASCIIZ-type strings.
   Declaration    StrAsc (VAR Dest: string; VAR AscSrc; MaxLen: byte)
   Remarks        After StrAsc is executed, the global variable AscSrcPtr 
                  points to the next ASCIIZ string skipping over any null 
                  character.  Should the conversion be truncated with MaxLen, 
                  StrAsc makes sure that AscSrcPtr points to the next string 
                  and not a null.  Source and destination can be the same.  As 
                  in all move-type procedures, it is important to make sure 
                  the destination size is sufficient to fit the source.
   Rating         17,000 str/sec
   See also       StrLn, AscStr
   Example        Disassemble a sequential array of ASCIIZ strings into three 
                  Pascal strings:

                    uses strg;
                    const
                      A: array[0..26] of char = 
                         'Eagle'#00'Performance'#00'Software'#00;
                    var
                      S: array[0..4] of string;
                      i: byte;
                    begin
                      AscSrcPtr := @A;
                      for i:=1 to 3 do
                        StrAsc (S[i],AscSrcPtr^,255);
                    end.

                  The resulting strings would look like:


   Chapter 2, Procedures and Functions                                 Page 11

   STRG Utilities                               Reference Guide, Version 6.1b



                    S[1] := 'Eagle';
                    S[2] := 'Performance';
                    S[3] := 'Software';

   ---------------------------------------------------------------------------
   StrLn procedure                                                        Strg
   ---------------------------------------------------------------------------
   Function       Creates Pascal strings from ASCII TEXT strings.
   Declaration    StrLn (VAR Dest: string; VAR LnSrc; MaxLen: byte)
   Remarks        ASCII text file lines by definition end with a CR (#13) or a 
                  CR/LF (#13/#10).  StrLn searches for the CR and copies the 
                  string prior to that character.  After StrLn is executed, 
                  the global variable LnSrcPtr points to the next line 
                  skipping over any CR or LF even if the string is truncated 
                  with MaxLen.  Source and destination can be the same for 
                  non-sequential conversions.  As in all move-type procedures, 
                  it is important to make sure the destination size is 
                  sufficient to fit the source.
   Suggestions    The use of ReadLn for text files is disk intensive.  StrLn 
                  can be used together with BlockRead for extremely fast text 
                  file operations.
   Rating         16,800 str/sec
   See also       AscStr, LnStr, and variable LnSrcPtr
   Example        Similar to the example in AscStr. 

   ---------------------------------------------------------------------------
   Str* function                                                          Strg
   ---------------------------------------------------------------------------
   Function       Converts numbers to a string representation.
   Declaration    StrC   (C: comp):
                  StrCF  (C: comp; Field: integer)
                  StrCFD (C: comp; Field,Decimals: integer)
                  StrD   (D: double)
                  StrDF  (D: double; Field: integer)
                  StrDFD (D: double; Field,Decimals: integer)
                  StrE   (E: extended)
                  StrEF  (E: extended; Field: integer)
                  StrEFD (E: extended; Field,Decimals: integer)
                  StrL   (L: longint)
                  StrLF  (L: longint; Field: integer)
                  StrR   (R: real)
                  StrRF  (R: real; Field: integer)
                  StrRFD (R: real; Field,Decimals: integer)
                  StrS   (S: single)
                  StrSF  (S: single; Field: integer)
                  StrSFD (S: single; Field,Decimals: integer)
   Result type    string
   Remarks        These functions use the System.Str procedure, but have been 
                  converted to a function form for convenience.  Although they 
                  are a fraction slower, they save code in the long run.  The 
                  IEEE reals are included only if the N/E compiler directives 
                  are appropriately set for your use.
   Rating         Varies: uses System.Str.


   Chapter 2, Procedures and Functions                                 Page 12

   STRG Utilities                               Reference Guide, Version 6.1b


   See also       StrBin, StrHex

   ---------------------------------------------------------------------------
   StrBin function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Converts numbers to binary strings.
   Declaration    StrBin (Num: longint; Field: byte)
   Result type    string
   Remarks        If the field is larger than the resulting string, the field 
                  is balanced with leading zeros.  If no leading zeros are 
                  desired, set Field to 0.  Maximum field is 32.
   Rating         13,300 str/sec
   See also       StrHex, ValBin, ValHex
   Example        In the following examples, the results will be String1=
                  '0000111111' and String2='111111'.

                    MyByte  := 63;
                    String1 := StrBin (MyByte,10);
                    String2 := StrBin (MyByte,3);

   ---------------------------------------------------------------------------
   StrBrk function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Finds first character that is a member of a group of chars.
   Declaration    StrBrk (S,Breaks: string; Index: byte)
   Result type    byte
   Remarks        Breaks (Brk) is a group of characters.  The function returns 
                  the index of the first character found to be a member of 
                  Breaks moving RIGHT from the given index.  Routine has fully 
                  scanned when resulting index is zero.  This routine is 
                  usually used to parse a string.  For greater speed, place 
                  the most commonly used members early in Breaks.
   Rating         1-char Breaks: 23,700 str/sec
                  5-char Breaks:  5,400 str/sec
   See also       ChrPos*, StrMemb, StrPosX, StrSpn
   Example        Find the position of the number in the string S:

                    var 
                      S,Numbers: string;
                      Position: byte;
                    begin
                      S := 'Balance $24567.00';
                      StrEnum (Numbers,'0','9');
                      Position := StrBrk (S,Numbers,1);  { Position=10 }
                    end.

   ---------------------------------------------------------------------------
   StrCat* procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Appends one string or substring to the end of another.
   Declaration    StrCat  (VAR Dest: string; S: string; MaxLen: byte)
                  StrCatX (VAR Dest: string; S: string; 
                           indeX,Count,MaxLen: byte)
   Remarks        This procedure appends the end of string Dest with S for a 


   Chapter 2, Procedures and Functions                                 Page 13

   STRG Utilities                               Reference Guide, Version 6.1b


                  maximum length limit of MaxLen.  StrCat concatenates a full 
                  string while StrCatX does a substring.  This greatly speeds 
                  up concatenation.  Usually the SizeOf function is used for 
                  MaxLen, or 255 can be used if there is no concern.  Like 
                  Concat, but up to 5 times faster.
   Rating         44,100 str/sec
   See also       StrCopy, StrMove, StrOvr
   Example        Given S1='Eagle ' and S2='Performance', try the following:

                    StrCatX (S1,S2,7,3,255);   ( S1='Eagle man'         }
                    StrCut  (S1,6);            { S1='Eagle '            }
                    StrCat  (S1,S2,255);       { S1='Eagle Performance' }

   ---------------------------------------------------------------------------
   StrCmp* function                                                       Strg
   ---------------------------------------------------------------------------
   Function       Compares one substring to another.
   Declaration    StrCmp  (S1,S2: string; Index1,Index2,MaxLen: byte)
                  StrCmpI (S1,S2: string; Index1,Index2,MaxLen: byte)
   Result type    shortint
   Result value   After comparison, here are the possible values:
                    -1:  S1<S2
                     0:  S1=S2
                    +1:  S1>S2
   Remarks        This routine compares (Cmp) two strings and determines Less 
                  Than, Equal, or Greater Than.  The comparison is made 
                  between the resulting substrings starting at each 
                  corresponding index and moving to the right.  The indexes 
                  are not adjusted should they extend beyond the end of string 
                  at which the substring is considered null.  The indexes of 
                  difference are saved in the global variables CmpIndex1 and 
                  CmpIndex2 which are 0 if the two substrings are equal.  
                  StrCmp matches case while StrCmpI ignores case.
   Rating         StrCmp:  27,800 str/sec
                  StrCmpI:  4,600 str/sec
   Example        The following comparison of dates yields -1, CmpIndex1=13 
                  and CmpIndex2=19.

                    S1 := 'MyEvent 90-04-23';
                    S2 := 'Second event: 90-05-17';
                    MyShortInt := StrCmp (S1,S2,9,15,8);

   ---------------------------------------------------------------------------
   StrCopy procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Directly copies a substring to create a new string.
   Declaration    StrCopy (VAR Dest: string; S: string; Index,Count: byte)
   Remarks        This is a move procedure for strings.  Being a procedure 
                  rather than a function, it is up to 3.3 times faster than 
                  System.Copy.  But be sure the Dest is large enough.
   Rating         47,000 str/sec
   See also       Copy, StrCat, StrOvr
   Example        The following example extracts the substring 'target'.



   Chapter 2, Procedures and Functions                                 Page 14

   STRG Utilities                               Reference Guide, Version 6.1b


                    S1 := 'This is the target word';
                    StrCopy (S2,S1,13,6);           { S2='target' }

   ---------------------------------------------------------------------------
   StrCut procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Truncates a string above a maximum size.
   Declaration    StrCut (VAR S: string; MaxLen: byte)
   Rating         430,000 str/sec
   See also       ChrDel*
   Example        Try the following code:

                    S := 'Eagle Performance Software';
                    StrCut (S,17);     { S='Eagle Performance' }

   ---------------------------------------------------------------------------
   StrDeTab procedure                                                     Strg
   ---------------------------------------------------------------------------
   Function       Expands all tabs to spaces at a given tab spacing.
   Declaration    StrDeTab (VAR Dest: string; S: string; TabSpaces: byte)
   Remarks        This routine expands all tabs to spaces given the tab 
                  spacing.  Source and Dest can be the same address.  Position 
                  1 is the first tab setting.  Be sure Dest can handle the 
                  expansion.  Strings are truncated at 255.
   Rating         7,700 str/sec
   See also       StrReTab
   Example        Expand the tabs (#9) in the following string:

                    S := #9'Col 9'#9'Col 17';
                    StrReTab (S,S,8);         { S='        Col 9   Col 17' }
                                              {    1234567890123456789012  }

   ---------------------------------------------------------------------------
   StrEnum procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Enumerates a string of characters from First to Last.
   Declaration    StrEnum (VAR S: string; First,Last: char)
   Remarks        Enumeration can be increasing or decreasing, but do not wrap 
                  through #00.  Be sure the destination is large enough.  
                  Strings are truncated at 255.
   Rating         13,300 str/sec
   See also       StrFill, StrRev, StrSort
   Example        Try the following examples:

                     StrEnum (S,'a','f');   { S='abcdeg' }
                     StrEnum (T,'f','a');   { T='fedcba' }

   ---------------------------------------------------------------------------
   StrFill procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Fills a string with multiple copies of a substring.
   Declaration    StrFill (VAR S: string; Fill: string; Count,MaxLen: byte)
   Remarks        The fill overwrites S with concatenated copies of Fill.  A 
                  special option is built in for single character fills to be 


   Chapter 2, Procedures and Functions                                 Page 15

   STRG Utilities                               Reference Guide, Version 6.1b


                  extremely fast.  Source and destination can be the same. 
                  Strings are truncated by MaxLen.
   Rating         1-char fill: 44,400 str/sec
                  5-char fill: 13,300 str/sec
   See also       ChrFill, StrEnum
   Example        Try the following examples:

                    StrFill (S,'a',5,255);    { S='aaaaa' }
                    StrFill (T,'Fast',3,11);  { T='FastFastFas' }

   ---------------------------------------------------------------------------
   StrHex procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Converts numbers to hex strings.
   Declaration    StrHex (Num: longint; Field: byte)
   Remarks        If the field is larger than the resulting string, the 
                  field is balanced with leading zeros.  If no leading zeros 
                  are desired, set Field to 0.  Maximum field is 8.  No 
                  leading '$' character is inserted.
   Rating         25,100 str/sec
   See also       StrBin, ValBin, ValHex
   Example        Try the following examples:

                    MyWord  := 4095;
                    String1 := StrHex (MyWord,5);   { String1='00FFF'    }
                    String2 := StrHex (MyWord,1);   { String2='FFF'      }
                    String3 := StrHex (MyWord,15);  { String3='00000FFF' }

   ---------------------------------------------------------------------------
   StrIns procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Inserts a substring at a given index.
   Declaration    StrIns (VAR Dest: string; S: string; DestIndex,MaxLen: byte)
   Remarks        The routine is processed as if the insertion was done and 
                  the resulting string truncated after MaxLen.  DestIndex is 
                  adjusted to the minimum of DestIndex and Dest[0].  The 
                  operation is skipped if MaxLen<DestIndex or S[0]=0.  Up to 
                  5 times faster than System.Insert.
   Rating         31,900 str/sec
   See also       StrCat, StrCopy
   Example        Try the following examples:

                    S := 'Hello friends';
                    J := 'Jim';
                    Index := 7;                  {    123456789012345678 }
                    StrIns (S,'my ',Index,255);  { S='Hello my friends'  }

                  Since StrIns lets you control MaxLen, the following line of 
                  code:

                    StrIns (S,J,Index,pred(Index)+length(J));

                  Is the same as the following two lines:



   Chapter 2, Procedures and Functions                                 Page 16

   STRG Utilities                               Reference Guide, Version 6.1b


                    StrCut (S,pred(Index));   {    123456789 }
                    StrCat (S,J,255);         { S='Hello Jim' }

   ---------------------------------------------------------------------------
   StrJ* function                                                         Strg
   ---------------------------------------------------------------------------
   Function       Left, center, or right justifies a string in a field of 
                  spaces.
   Declaration    StrJC  (S: string; Field: byte)   { Justify center }
                  StrJL  (S: string; Field: byte)   { Justify left   }
                  StrJR  (S: string; Field: byte)   { Justify right  }
   Result type    string
   Remarks        If the field is smaller than the source string, the string 
                  is simply returned unaltered.  These routines save from 
                  recopying the string in the stack making it faster.
   Rating         17,500 str/sec
   See also       ChrPad*, StrOvr
   Example        Try the following examples:

                    S := StrJC ('test',7);   { S=' test  ' }
                    S := StrJL ('test',7);   { S='test   ' }
                    S := StrJR ('test',7);   { S='   test' }

   ---------------------------------------------------------------------------
   StrLwr procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Converts strings to lower case.
   Declaration    StrLwr (VAR S: string)
   Remarks        The operation works on the entire string.
   Rating         8,900 str/sec
   See also       ChrReplI, LoCase, StrUpr, UpCase

   ---------------------------------------------------------------------------
   StrMemb procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Reduces a string to its membership in ascending order.
   Declaration    StrMemb (VAR Dest: string; S: string)
   Remarks        Membership is the list of characters that occur in a string.  
                  Only one character is listed in the destination string for 
                  any number of the same character in the source string.  
                  Source and destination may be the same.  This is useful when 
                  repeated scans are used on the same string for speed.
   Rating         4,500 str/sec
   See also       Is*, StrBrk, StrSort, StrSpn
   Example        Try the following example:

                    var
                      S1,S2: string;
                    begin
                      S1 := 'Eagle Performance Software 321';
                      StrMemb (S2,S1);     { S2=' 123EPSacefglmnortw' }
                    end.




   Chapter 2, Procedures and Functions                                 Page 17

   STRG Utilities                               Reference Guide, Version 6.1b


   ---------------------------------------------------------------------------
   StrMove procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Moves a string to another location WITH the length byte.
   Declaration    StrMove (VAR Dest: string; S: string)
   Remarks        It's up to 70% faster than using and assignment (":=").  Use 
                  when speed is essential.  Be sure Dest is large enough.
   Rating         53,400 str/sec
   See also       StrCat, StrCopy, StrOvr, StrPeek
   Example        Assign a string to another:

                    S1 := 'Now is the time';
                    StrMove (S2,S1);       { S2='Now is the time' }  

   ---------------------------------------------------------------------------
   StrOvr procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Overwrites a string at a given index.
   Declaration    StrOvr (VAR Dest: string; S: string; Index: byte)
   Remarks        The length of the original string is increased if the 
                  substring makes it longer.  Any gap between the two 
                  strings is filled with spaces.  This is a move-type 
                  procedure, so be sure the destination is large enough.  
                  However, resulting strings are truncated at 255.
   Suggestions    This is a popular routine.  Use it when strings need to be 
                  aligned for formatting or displayed in columns.
   Rating         44,100 str/sec
   See also       Copy, StrCat, StrCopy, StrJ*, StrMove, StrPoke
   Example        Try the following examples:

                    S := 'Hello world';
                    StrOvr (S,'friends',7);   { S='Hello friends' }
                    T := 'First';             {    123456789012345678  }
                    StrOvr (T,'MI'  , 9);     { T='First   MI'         }
                    StrOvr (T,'Last',15);     { T='First   MI    Last' }

   ---------------------------------------------------------------------------
   StrPeek procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Grabs an array in memory and converts it to a string.
   Declaration    StrPeek (VAR Dest: string; VAR Source; Count: byte)
   Remarks        Takes an array in memory at Source and converts it to a 
                  string at Dest.  Dest[0] cannot overlap Source.  This allows 
                  arrays to be handled as strings.
   Rating         42,100 str/sec
   See also       StrMove, StrPoke
   Example        Try the following example:









   Chapter 2, Procedures and Functions                                 Page 18

   STRG Utilities                               Reference Guide, Version 6.1b


                    const                      { 12345678901234567890123 }
                      A: array[1..23] of char = 'Eagle Performance, Inc.';
                    var
                      S: string;
                    begin
                      StrPeek (S,A[7],11);   { S='Performance' }
                    end.

   ---------------------------------------------------------------------------
   StrPoke procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Pokes the characters of a string into memory.
   Declaration    StrPoke (VAR Dest; S: string)
   Remarks        Pokes the characters of S as an array into memory NOT 
                  including the length byte.  This allows strings to be 
                  handled as arrays.  Dest[0] cannot overlap S.
   Rating         43,600 str/sec
   See also       StrOvr, StrPeek
   Example        Try the following example:

                    const                      { 12345678901234567890123 }
                      A: array[1..23] of char = 'Eagle            , Inc.';
                      S: string = 'Performance';
                    begin                      { 12345678901234567890123 }
                      StrPoke (A[7],S);     { A='Eagle Performance, Inc.' }
                    end.

   ---------------------------------------------------------------------------
   StrPos* function                                                       Strg
   ---------------------------------------------------------------------------
   Function       Finds the position of a given string with match/ignore case.
   Declaration    StrPosL  (S,Find: string; Nth: byte)
                  StrPosLI (S,Find: string; Nth: byte)
                  StrPosR  (S,Find: string; Nth: byte)
                  StrPosRI (S,Find: string; Nth: byte)
                  StrPosX  (S,Find: string; indeX: byte)
                  StrPosXI (S,Find: string; indeX: byte)
   Result type    byte
   Remarks        Using suffixes, -L routine searches from the left while the 
                  -R searches from the right for the Nth occurrence.  The -X 
                  routine starts at the given index and searches right for the 
                  first occurrence.  These routines match case, while those 
                  with the added -I suffix will Ignore case.
   Rating         StrPos?  1-char:  23,900 str/sec
                  StrPos?  5-char:  18,200 str/sec
                  StrPos?I 1-char:   6,800 str/sec
                  StrPos?I 5-char:   5,900 str/sec
   See also       ChrPos*, StrBrk
   Example        Find the position of the following substrings:

                         { 1234567890123456789012345678901234 }
                    S1 := 'Write excellent routines and Excel';
                    MyByte := StrPosL  (S1,'exc',1);     { MyByte=7  }
                    MyByte := StrPosLI (S1,'exc',2);     { MyByte=30 }


   Chapter 2, Procedures and Functions                                 Page 19

   STRG Utilities                               Reference Guide, Version 6.1b


                    MyByte := StrPosR  (S1,'exc',1);     { MyByte=7  }
                    MyByte := StrPosRI (S1,'exc',2);     { MyByte=7  }
                    MyByte := StrPosX  (S1,'exc',4);     { MyByte=7  }
                    MyByte := StrPosXI (S1,'EXC',4);     { MyByte=7  }


   ---------------------------------------------------------------------------
   StrQty* function                                                       Strg
   ---------------------------------------------------------------------------
   Function       Counts the occurrences of a given substring in 
                  a string with match/ignore case. 
   Declaration    StrQty  (S,Find: string)
                  StrQtyI (S,Find: string)
   Result type    byte
   Remarks        StrQty matches case while StrQtyI ignores case.
   Rating         StrQty  1-char:  23,900 str/sec
                  StrQty  5-char:  18,200 str/sec
                  StrQtyI 1-char:   6,800 str/sec
                  StrQtyI 5-char:   5,900 str/sec
   See also       ChrQty*, WrdQty

   ---------------------------------------------------------------------------
   StrRepl* procedure                                                     Strg
   ---------------------------------------------------------------------------
   Function       Finds and replaces a substring from a given index for Qty 
                  number of replacements with match/ignore case. 
   Declaration    StrRepl  (VAR S: string; Find,Repl: string; 
                            Index,Qty,MaxLen: byte)
                  StrReplI (VAR S: string; Find,Repl: string;
                            Index,Qty,MaxLen: byte)
   Remarks        The operation starts from Index and goes to the right.  It 
                  will stop if the index is beyond the end of string or it has 
                  replaced as many as it can.  StrRepl matches case while 
                  StrReplI ignores case.
                    The global variable ReplToDo is the result of Qty less the 
                  number of replacements that were done on the string.
                    MaxLen is used for the special case when the length of 
                  Repl is greater than Find.  The routine will replace as many 
                  as it can.  If one more replacement would cause the string 
                  length to be greater than MaxLen, the routine will stop at 
                  that find and report the index as ReplIndex and will set 
                  ReplOverFlow=true.  Otherwise, ReplIndex=0 and ReplOverFlow 
                  is false.
   Rating         StrRepl:  8,800 str/sec
                  StrReplI: 4,600 str/sec
   See also       ChrDel*, ChrRepl*
   Example        Try the following example:

                    var
                      S: string;
                    begin
                          { 1234567890123456789012345678901234 }
                      S := 'Fast TEST String, FAST test string';
                      StrReplI (S,'st','---',1,255,38);


   Chapter 2, Procedures and Functions                                 Page 20

   STRG Utilities                               Reference Guide, Version 6.1b


                    end.

                  The results will be ReplOverFlow=true, ReplIndex=30, and 
                  ReplToDo=251 with S as follows:

                          { 12345678901234567890123456789012345678 }
                      S := 'Fa--- TE--- ---ring, FA--- test String';

   ---------------------------------------------------------------------------
   StrReTab procedure                                                     Strg
   ---------------------------------------------------------------------------
   Function       Reduces spaces to tabs.
   Declaration    StrReTab (VAR Dest: string; S: string; TabSpaces: byte)
   Remarks        This routine reduces spaces with tabs given the tab spacing.  
                  Embedded tabs are accounted for.  Tab spacing is a minimum 
                  of one and zero values are forced to 1.  Position 1 is 
                  considered column 1.  Source and Dest can be the same 
                  address.
   Rating         6,000 str/sec
   See also       StrDeTab
   Example        Reduce spaces in the following string:

                        { 1234567890123456789012 }
                    S := '        Col 9   Col 17';
                    StrDeTab (S,S,8);         { S=#9'Col 9'#9'Col 17' }

   ---------------------------------------------------------------------------
   StrRev procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Reverses the order of the characters in a string.
   Declaration    StrRev (VAR S: string)
   Rating         16,600 str/sec
   See also       StrEnum, StrSort
   Example        Try the following:

                    S := 'abcdefg';
                    StrRev (S);      { S='gfedcba' }

   ---------------------------------------------------------------------------
   StrRoll procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Rolls the characters in a string forward or backward.
   Declaration    StrRoll (VAR S: string; Count: integer)
   Remarks        A forward roll moves characters from right to left and 
                  appends the rolled out characters on the right end.  A 
                  backward roll (a negative value) does the reverse.  If Count 
                  is greater than S[0], the Count is adjusted by mod.
   Rating         27,800 str/sec
   See also       StrRev, StrSort
   Example        Try the following:

                    S1 := '1234567890';  S2:=S1;
                    StrRoll (S1,2);    { S1='3456789012' }
                    StrRoll (S2,-2);   { S2='9012345678' }


   Chapter 2, Procedures and Functions                                 Page 21

   STRG Utilities                               Reference Guide, Version 6.1b



   ---------------------------------------------------------------------------
   StrSort procedure                                                      Strg
   ---------------------------------------------------------------------------
   Function       Operates on a string by sorting it in ascending order.
   Declaration    StrSort (VAR S: string)
   Remarks        Two algorithms are used for this routine for speed.  For 
                  strings up to 22 chars long, the classic Quick Sort is used.  
                  After 22 chars, the Tally Sort is used which is up to 10 
                  times faster than Quick Sort, because the Tally Sort does it 
                  in only two passes.
   Rating         3,600 str/sec
   See also       StrEnum, StrMemb, StrRev
   Suggestions    This routine is so efficient, you can even use it to sort 
                  any byte arrays by using an absolute variable at the address 
                  you want to sort or you can use StrPeek/StrPoke for arrays 
                  up to 255 bytes.
   Example        Try the following:

                    S := 'fgb1edca';
                    StrSort (S);      { S='1abcdefg' }

   ---------------------------------------------------------------------------
   StrSpn function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Counts the number of consecutive characters that are all 
                  members of a group of chars.
   Declaration    StrSpn (S,Members: string; Index: byte)
   Result type    byte
   Remarks        The function scans the string S starting at Index and scans 
                  RIGHT.  Members is any group of characters.  As long as the 
                  scanned character is in Members, it will continue to scan 
                  for the next one until it finds a non-member of Members.  
                  The result is the span (Spn) of the substring that are all 
                  members.  This routine is usually used to parse a string.  
                  For greater speed, place the most commonly used members 
                  early in Members.
   Rating         1-char Members: 23,600 str/sec
                  5-char Members:  3,600 str/sec
   See also       StrBrk, StrMemb, Wrd*, WrdParse, WrdToken
   Example        Find the length of the number in string S:

                    var 
                      S,Numbers: string;
                      Size: byte;
                    begin
                      S := 'Balance $24,567.00 in credits.';
                      StrEnum (Numbers,'0','9');
                      StrCat (Numbers,'+-.,',255);
                      Size := StrSpn (S,Numbers,10); { Size=9 }
                    end.





   Chapter 2, Procedures and Functions                                 Page 22

   STRG Utilities                               Reference Guide, Version 6.1b


   ---------------------------------------------------------------------------
   StrUpr procedure                                                       Strg
   ---------------------------------------------------------------------------
   Function       Converts strings to upper case.
   Declaration    StrUpr (VAR S: string)
   Remarks        The operation works on the entire string.
   Rating         8,900 str/sec
   See also       ChrReplI, LoCase, StrLwr, UpCase

   ---------------------------------------------------------------------------
   UpCase function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Converts characters to upper case.
   Declaration    UpCase (C: char)
   Result type    char
   Remarks        It's about 3 times faster than System.UpCase producing 
                  identical results.
   See also       ChrReplI, LoCase, StrLwr, StrUpr

   ---------------------------------------------------------------------------
   ValBin function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Converts binary strings to longint.
   Declaration    ValBin (S: string; VAR Code: integer)
   Result type    longint (but smaller types are permissible)
   Remarks        ValBin has these superior features:

                    - Leading spaces are permitted but not trailing ones.
                    - Leading zeros are also permitted.
                    - A non-zero error code points to the invalid character in 
                      the string.
                    - Numbers larger than $FFFFFFFF produce an error.
                    - ValBin salvages a value even if there is an error!
                    - Routine is more flexible as a function rather than being 
                      similar to the Val procedure which is compiler dependent 
                      on the number type.

   Rating         25,500 str/sec
   See also       StrBin, StrHex, ValHex
   Example        In the last example, Code=9.  The others set Code=0.

                    LongInt1 := ValBin ('001100100',Code);  { LontInt1=100 }
                    LongInt2 := ValBin ('111110100',Code);  { LongInt2=500 }
                    LongInt3 := ValBin ('  101101b',Code);  { LongInt3=45  }

   ---------------------------------------------------------------------------
   ValHex function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Converts hex strings to longint.
   Declaration    ValHex (S: string; VAR Code: integer)
   Result type    longint (but smaller types are permissible)
   Remarks        ValHex has these superior features:

                    - Leading spaces are permitted but not trailing ones.


   Chapter 2, Procedures and Functions                                 Page 23

   STRG Utilities                               Reference Guide, Version 6.1b


                    - Leading zeros are also permitted.
                    - The leading '$' is optional!
                    - A non-zero error code points to the invalid character in 
                      the string.
                    - Numbers larger than $FFFFFFFF produce an error.
                    - ValHex salvages a value even if there is an error!
                    - Twice as fast as Val and uses much less code.
                    - Routine is more flexible as a function rather than the 
                      Val procedure which is compiler dependent on the number 
                      type.

   Rating         27,200 str/sec
   See also       StrBin, StrHex, ValBin
   Example        In the last example, Code=5.  The others set Code=0.


                    LongInt1 := ValHex (' 0064',Code);  { LongInt1=100 }
                    LongInt2 := ValHex (' $1f4',Code);  { LongInt1=500 }
                    LongInt3 := ValHex ('  2Dh',Code);  { LongInt1=45  }

   ---------------------------------------------------------------------------
   Wrd* procedure                                                         Strg
   ---------------------------------------------------------------------------
   Function       Parses words separated by spaces.
   Declaration    WrdL  (VAR Dest: string; S: string; Nth: byte)
                  WrdR  (VAR Dest: string; S: string; Nth: byte)
                  WrdLX (VAR Dest: string; S: string; indeX: byte)
                  WrdRX (VAR Dest: string; S: string; indeX: byte)
   Remarks        A word at the beginning or end of a string is considered a 
                  word even though it does not have spaces on both ends.  The 
                  procedures apply as follows:

                    WrdL  - parses Nth word from the Left.
                    WrdR  - parses Nth word from the Right.
                    WrdLX - parses first word from Left starting at indeX.
                    WrdRX - parses first word from Right starting at indeX.

                  WrdLX and WrdRX parses the first word with its first letter 
                  found in the direction of search even if it starts at indeX.
   Rating         Wrd?:  16,400 str/sec
                  Wrd?X: 25,100 str/sec
   See also       StrBrk, StrSpn, WrdPos*, WrdParse, WrdToken
   Example        Try the following parsing:

                    var S,W1,W2,W3,W4: string;
                    begin
                      S := 'Eagle Performance Software Products';     
                      WrdL  (W1,S,2);      { W1='Performance'}
                      WrdR  (W2,S,2);      { W2='Software'   }
                      WrdLX (W3,S,2);      { W3='Performance'}
                      WrdRX (W4,S,255);    { W1='Products'   }
                    end.




   Chapter 2, Procedures and Functions                                 Page 24

   STRG Utilities                               Reference Guide, Version 6.1b


   ---------------------------------------------------------------------------
   WrdParse procedure                                                     Strg
   ---------------------------------------------------------------------------
   Function       Parses substrings separated by individual delimiters.
   Declaration    WrdParse (VAR Dest: string; S,Delims: string; 
                            VAR Index: byte)
   Remarks        Delims is a group of characters considered delimiters.  
                  (Place the most used delimiters early in the string for 
                  faster performance.)  WrdParse extracts the next delimited 
                  word RIGHT from the given Index and does not search 
                  backwards.  WrdParse adjusts Index so it marks where to 
                  start the next parse on the next call.  Routine has fully 
                  scanned when resulting indeX is set to zero.  Different from 
                  WrdToken, nulls are significant; i.e., two delimiters in 
                  sequence is considered a null parse.  So, if a delimiter is 
                  at the end of a string, the final parse returned is null.
   Rating         1-char Delims: 28,500 str/sec
                  5-char Delims:  6,500 str/sec
   See also       StrBrk, StrSpn, Wrd*, WrdPos*, WrdToken
   Example        Parse the following string S into the string array:

                    uses strg;
                    var
                      A: array[0..4] of string;
                      i,j,Index: byte;
                      D,S: string;
                    begin
                      S := 'Faster, yet better';
                      D := ' ,.';       { These are the delimiters. }
                      i := 0;           { First parse will be in Sarray[0] }
                      Index := 1;       { Start at first character }
                      while Index<>0 do
                        begin
                          WrdParse (A[i],S,D,Index);
                          inc (i);
                        end;
                    end.

                  Program will end with i=4 which is the number of parses 
                  found.  The results are A[0]='Faster', A[1]='', A[2]='yet', 
                  and A[3]='better'.  A[1] is null because a null string was 
                  parsed between the comma and space which is useful for 
                  parsing command line entries that are null.

   ---------------------------------------------------------------------------
   WrdPos* function                                                       Strg
   ---------------------------------------------------------------------------
   Function       Returns position of word delimited by spaces.
   Declaration    WrdPosL  (S: string; Nth: byte)
                  WrdPosR  (S: string; Nth: byte)
                  WrdPosLX (S: string; indeX: byte)
                  WrdPosRX (S: string; indeX: byte)
   Result type    byte
   Remarks        A word at the beginning or end of a string is considered a 


   Chapter 2, Procedures and Functions                                 Page 25

   STRG Utilities                               Reference Guide, Version 6.1b


                  word even though it does not have spaces on both ends.  The 
                  procedures apply as follows:

                    WrdPosL  - find Nth word from the Left
                    WrdPosR  - find Nth word from the Right
                    WrdPosLX - find first word from Left starting at indeX.
                    WrdPosRX - find first word from Right starting at indeX.

                  If the index is not located on the first letter of a word, 
                  WrdPosLX and WrdPosRX will continue scanning for the next 
                  word.
   Rating         WrdPos?:  17,700 str/sec
                  WrdPos?X: 26,400 str/sec
   See also       StrBrk, StrSpn, Wrd*, WrdParse, WrdToken
   Example        Try the following examples:

                        { 12345678901234567890123456789012345678 }
                    S := 'Now is the time for all good programs.';
                    MyByte := WrdPosR  (S,1);   { MyByte=30 }
                    MyByte := WrdPosL  (S,3);   { MyByte= 8 }
                    MyByte := WrdPosLX (S,9);   { MyByte=12 }
                    MyByte := WrdPosRX (S,9);   { MyByte= 8 }

   ---------------------------------------------------------------------------
   WrdQty function                                                        Strg
   ---------------------------------------------------------------------------
   Function       Counts the number of words in a string delimited by spaces.
   Declaration    WrdQty (S: string)
   Result type    byte
   Remarks        A word at the beginning or end of a string is considered a 
                  word even though it does not have spaces on both ends.
   Rating         18,400 str/sec
   See also       ChrQty*, StrQty*
   Example        Try the following example:

                    S := 'Now is the time for all good programs.';
                    MyByte := WrdQty (S);    { MyByte=8 }

   ---------------------------------------------------------------------------
   WrdToken procedure                                                     Strg
   ---------------------------------------------------------------------------
   Function       Parses substrings separated by groups of delimiters.
   Declaration    WrdToken (VAR Dest: string; S,Delims: string; 
                            VAR indeX: byte)
   Remarks        Delims is a group of characters considered delimiters.  
                  (Place the most used delimiters early in the string for 
                  faster performance.)  WrdToken extracts the next delimited 
                  word RIGHT from the given indeX and does not search 
                  backwards.  WrdToken adjusts indeX so it marks where to 
                  start the next parse on the next call.  Routine has fully 
                  scanned when resulting indeX is set to zero.  Different from 
                  WrdParse, nulls are NOT significant; i.e., all delimiters 
                  are passed over until the next token is found.  But, if a 
                  delimiter is at the end of a string, the final token 


   Chapter 2, Procedures and Functions                                 Page 26

   STRG Utilities                               Reference Guide, Version 6.1b


                  returned is still null.
   Rating         1-char Delims: 28,500 str/sec
                  5-char Delims:  6,500 str/sec
   See also       StrBrk, StrSpn, Wrd*, WrdPos*, WrdParse
   Example        Parse the following S into the string array:

                    uses strg;
                    var
                      A: array[0..4] of string;
                      i,j,Index: byte;
                      D,S: string;
                    begin
                      S := 'Faster, yet better';
                      D := ' ,.';       { These are the delimiters. }
                      i := 0;           { First parse will be in A[0] }
                      Index := 1;       { Start at first character }
                      while Index<>0 do
                        begin
                          WrdToken (A[i],S,D,Index);
                          inc (i);
                        end;
                    end.

                  Program will end with i=3 which is the number of tokens 
                  found.  The results are A[0]='Faster', A[1]='yet', and 
                  A[2]='better'.






























   Chapter 2, Procedures and Functions                                 Page 27

   STRG Utilities                               Reference Guide, Version 6.1b


   3.  V A R I A B L E S

   There are only a few variables to consider in the STRG unit.  Some can be 
   accessed for global use and just one is local.


   GLOBAL           

   Global Variables - These variables can be used to assist your programs more 
   efficiently:

     Variable      Description
     ------------  -----------------------------------------------------------
     AscDestPtr    (Type: Pointer) After AscStr is executed, this pointer 
                   points to the next ASCIIZ destination after the end-of-
                   string null.  This is very useful for sequential 
                   conversions to save space with ASCIIZ strings.

     AscSrcPtr     (Type: Pointer) After StrAsc is executed, this pointer 
                   points to the next ASCIIZ source after the end-of-string 
                   null or the next valid character if the conversion is 
                   limited by MaxLen.  This is very useful for sequential 
                   conversions from contiguous ASCIIZ strings.

     CmpIndex1     (Type: Integer)  After strings are compared with StrCmp*, 
                   the index of difference for S1 is saved in this variable.  
                   The integer type is used in lieu of byte for the case of 
                   difference at column 256 (Index1+MaxLen>255).  If you do 
                   not use strings out to S1[255], then it is permissible to 
                   use byte assignments to this variable.

     CmpIndex2     (Type: Integer)  Same as CmpIndex1 except it applies to S2.

     LnDestPtr     (Type: Pointer) After LnStr is executed, this pointer 
                   points to the next ASCII text file destination after the 
                   end-of-string CR/LF.  This is very useful for sequential 
                   conversions to an ASCII text file for a block write.

     LnSrcPtr      (Type: Pointer) After StrLn is executed, this pointer 
                   points to the next ASCII text file source after the end-of-
                   string CR/LF, CR, or the next valid character if the 
                   conversion is limited by MaxLen.  This is very useful for 
                   sequential conversions from a block read of an ASCII text 
                   file.

     ReplIndex     (Type: Byte)  After using StrRepl* and there is an 
                   overflow, this variable provides the index where the 
                   operation was halted. 

     ReplOverFlow  (Type: Boolean)  After using StrRepl* when the replacement 
                   string is longer than the find string and the resulting 
                   string would be longer than MaxLen permits, this value is 
                   set to TRUE.  This means the operation went as far as it 
                   could go before overflowing the length.


   Chapter 3, Variables                                                Page 28

   STRG Utilities                               Reference Guide, Version 6.1b



     ReplToDo      (Type: Byte)  After using StrRepl*, this variable indicates 
                   how many replacements are still needed to fulfill the 
                   original request.  If it is zero, then all replacements 
                   were done.


   LOCAL

   Local Constant - There is only one local constant to STRG:

     Constant      Description
     ------------  -----------------------------------------------------------
     ChrClass      (Type: array of char)  Several of the more complicated Is* 
                   functions use this 128 char array to quickly classify 
                   characters by testing individual bits in the array.  
                   Simpler Is* functions do not use this array and it is 
                   optimized out of the program.






































   Chapter 3, Variables                                                Page 29

   STRG Utilities                               Reference Guide, Version 6.1b


   4.  A C C E S S I B L E   M E M O R Y 

   Many of the routines in STRG use 16-bit transfers to increase string 
   processing.  As as you program to normally to RAM, these routines will work 
   fine.  Just remember that certain hardware other than RAM can have 
   limitations.  The only one of which we are aware is trying to use these 
   routines for direct manipulation of the EGA/VGA bit plane memory for video 
   graphics, which would indeed be a bizarre application for these routines.

   For graphics programming, either stick to the BGI drivers, or use routines 
   that only have 8-bit transfers.  For more info on this limitation on video 
   hardware, check out page 114 of Richard Wilton's book "Programmer's Guide 
   to PC & PS/2 Video Systems".











































   Chapter 4, Accessible Memory                                        Page 30

   STRG Utilities                               Reference Guide, Version 6.1b


   5.  Q U I C K   R E F E R E N C E

   For a quick reference for all of the declarations contained in this unit, 
   the following are all the routines listed in alphabetical order.

  procedure AscStr   (VAR AscDest; S: string);
  procedure ChrDel   (VAR S: string; Find: char);
  procedure ChrDelL  (VAR S: string; Find: char);
  procedure ChrDelR  (VAR S: string; Find: char);
  procedure ChrFill  (VAR S: string; Fill: char; Count: byte);
  procedure ChrPadC  (VAR S: string; Find: char; Field: byte);
  procedure ChrPadL  (VAR S: string; Find: char; Field: byte);
  procedure ChrPadR  (VAR S: string; Find: char; Field: byte);
  function  ChrPosL  (    S: string; Find: char; Nth:   byte): byte;
  function  ChrPosLI (    S: string; Find: char; Nth:   byte): byte;
  function  ChrPosR  (    S: string; Find: char; Nth:   byte): byte;
  function  ChrPosRI (    S: string; Find: char; Nth:   byte): byte;
  function  ChrPosX  (    S: string; Find: char; indeX: byte): byte;
  function  ChrPosXI (    S: string; Find: char; indeX: byte): byte;
  function  ChrQty   (    S: string; Find: char): byte;
  function  ChrQtyI  (    S: string; Find: char): byte;
  procedure ChrRepl  (VAR S: string; Find,Repl: char; Index,Qty: byte);
  procedure ChrReplI (VAR S: string; Find,Repl: char; Index,Qty: byte);
  function  Copy     (    S: string; Index,Count: integer): string;
  procedure Delete   (VAR S: string; Index,Count: integer);
  function  IsAlNum  (C: char): boolean;
  function  IsAlpha  (C: char): boolean;
  function  IsASCII  (C: char): boolean;
  function  IsCntrl  (C: char): boolean;
  function  IsDigit  (C: char): boolean;
  function  IsDos    (C: char): boolean;
  function  IsFile   (C: char): boolean;
  function  IsGraph  (C: char): boolean;
  function  IsLower  (C: char): boolean;
  function  IsPath   (C: char): boolean;
  function  IsPrint  (C: char): boolean;
  function  IsPunct  (C: char): boolean;
  function  IsReal   (C: char): boolean;
  function  IsSigned (C: char): boolean;
  function  IsSpace  (C: char): boolean;
  function  IsUpper  (C: char): boolean;
  function  IsXDigit (C: char): boolean;
  procedure LnStr    (VAR LnDest; S: string);
  function  LoCase   (C: char): char;
  function  Pos      (Find,S: string): byte;
  procedure StrAsc   (VAR Dest: string; VAR AscSrc; MaxLen: byte);
  function  StrBin   (Num: longint; Field: byte): string;
  function  StrBrk   (S,Breaks: string; Index: byte): byte;
  function  StrC     (C: comp): string;
  procedure StrCat   (VAR Dest: string; S: string; MaxLen: byte);
  procedure StrCatX  (VAR Dest: string; S: string; indeX,Count,MaxLen: byte);
  function  StrCF    (C: comp; Field: integer):          string;
  function  StrCFD   (C: comp; Field,Decimals: integer): string;
  function  StrCmp   (S1,S2: string; Index1,Index2,MaxLen: byte): shortint;


   Chapter 5, Quick Reference                                          Page 31

   STRG Utilities                               Reference Guide, Version 6.1b


  function  StrCmpI  (S1,S2: string; Index1,Index2,MaxLen: byte): shortint;
  procedure StrCopy  (VAR Dest: string; S: string; Index,Count: byte);
  procedure StrCut   (VAR S: string; MaxLen: byte);
  function  StrD     (D: double): string;
  procedure StrDeTab (VAR Dest: string; S: string; TabSpaces: byte);
  function  StrDF    (D: double; Field: integer):            string;
  function  StrDFD   (D: double; Field,Decimals: integer):   string;
  function  StrE     (E: extended):                          string;
  function  StrEF    (E: extended; Field: integer):          string;
  function  StrEFD   (E: extended; Field,Decimals: integer): string;
  procedure StrEnum  (VAR S: string; First,Last: char);
  procedure StrFill  (VAR S: string; Fill: string; Count,MaxLen: byte);
  function  StrHex   (Num: longint; Field: byte): string;
  procedure StrIns   (VAR Dest: string; S: string; DestIndex,MaxLen: byte);
  function  StrJC    (S: string; Field: byte): string;
  function  StrJL    (S: string; Field: byte): string;
  function  StrJR    (S: string; Field: byte): string;
  function  StrL     (L: longint):                 string;
  function  StrLF    (L: longint; Field: integer): string;
  procedure StrLn    (VAR Dest: string; VAR LnSrc; MaxLen: byte);
  procedure StrLwr   (VAR S: string);
  procedure StrMemb  (VAR Dest: string; S: string);
  procedure StrMove  (VAR Dest: string; S: string);
  procedure StrOvr   (VAR Dest: string; S: string; DestIndex: byte);
  procedure StrPeek  (VAR Dest: string; VAR Source; Count: byte);
  procedure StrPoke  (VAR Dest; S: string);
  function  StrPosL  (S,Find: string; Nth: byte):   byte;
  function  StrPosLI (S,Find: string; Nth: byte):   byte;
  function  StrPosR  (S,Find: string; Nth: byte):   byte;
  function  StrPosRI (S,Find: string; Nth: byte):   byte;
  function  StrPosX  (S,Find: string; indeX: byte): byte;
  function  StrPosXI (S,Find: string; indeX: byte): byte;
  function  StrQty   (S,Find: string):              byte;
  function  StrQtyI  (S,Find: string):              byte;
  function  StrR     (R: real): string;
  procedure StrRepl  (VAR S: string; Find,Repl: string; Index,Qty,MaxLen: byte);
  procedure StrReplI (VAR S: string; Find,Repl: string; Index,Qty,MaxLen: byte);
  procedure StrReTab (VAR Dest: string; S: string; TabSpaces: byte);
  procedure StrRev   (VAR S: string);
  function  StrRF    (R: real; Field: integer):          string;
  function  StrRFD   (R: real; Field,Decimals: integer): string;
  procedure StrRoll  (VAR S: string; Count: integer);
  function  StrS     (S: single):                          string;
  function  StrSF    (S: single; Field: integer):          string;
  function  StrSFD   (S: single; Field,Decimals: integer): string;
  procedure StrSort  (VAR S: string);
  function  StrSpn   (S,Members: string; Index: byte): byte;
  procedure StrUpr   (VAR S: string);
  function  UpCase   (C: char): char;
  function  ValBin   (S: string; VAR Code: integer): longint;
  function  ValHex   (S: string; VAR Code: integer): longint;
  procedure WrdL     (VAR Dest: string; S: string; Nth: byte);
  procedure WrdLX    (VAR Dest: string; S: string; indeX: byte);
  procedure WrdParse (VAR Dest: string; S,Delims: string; VAR Index: byte);


   Chapter 5, Quick Reference                                          Page 32

   STRG Utilities                               Reference Guide, Version 6.1b


  function  WrdPosL  (S: string; Nth: byte):   byte;
  function  WrdPosLX (S: string; indeX: byte): byte;
  function  WrdPosR  (S: string; Nth: byte):   byte;
  function  WrdPosRX (S: string; indeX: byte): byte;
  function  WrdQty   (S: string):              byte;
  procedure WrdR     (VAR Dest: string; S: string; Nth: byte);
  procedure WrdRX    (VAR Dest: string; S: string; indeX: byte);
  procedure WrdToken (VAR Dest: string; S,Delims: string; VAR Index: byte);
















































   Chapter 5, Quick Reference                                          Page 33