This package summarizes my findings on the possibilities of using some of
the high resolution text modes with Turbo Vision.  Included are two demo
programs to try various modes.  The first, LEVEL1, is the simplest but
will not work with all mouse drivers.  LEVEL2 requires more changes but
overcomes at least some of the mouse driver problems.  The executables
for these two programs are included, but to compile your own modified
versions, you'll need BP7.0 and the Run Time Library (RTL) source code
as the library file DRIVERS.PAS needs to be modified.

The stimulus for this investigation was Paradox 4.0.  Paradox now has a
Turbo Vision look and feel and it does support a number of high resolution
text modes which can be selected from a menu.  Once I got into this
investigation, I was surprised to find that Turbo Vision itself apparently
has no problems handling odd text modes like 132x44, 80x60, etc.  There
are problems, but they seem to be external to Turbo Vision:

  1. Not all mouse drivers work properly in the HiRes modes.  In particular,
     LogiTech drivers do, MicroSoft's don't.  Positioning information
     seems to be OK, but the screen is likely to get messed up with mouse
     droppings.  I haven't had a chance to try other drivers.

  2. There's apparently no standard for hires modes.  Basic video boards
     don't support any.  For more deluxe boards, different manufacturers
     support different modes.

  3. Even if the video board support a particular mode the monitor may not
     be able to synchronize satisfactorily.

  4. There seems to be no way for the software to tell in advance if a
     mode is supported.  The effects of attempting to change to an
     unsupported mode vary.  Often nothing happens.  Other times the screen
     may black out or become extremely garbled.

  5. The possibility exists for damage to the monitor for modes that
     don't synchronize correctly.  Don't leave a monitor in a condition
     where it's obviously not working correctly.  It may be necessary to
     reboot.

Below is a summary of various hires modes.  This info comes from the file,
PARADOX.VID, which apparently is the basis for the Paradox video menu
selection list.

    Board                Mode (decimal)       Width x Height

  VGA Wizard             50                   80x34
                         51                   80x45
                         35                   132x25
                         34                   132x44

  ATI VGA                35                   132x25
                         51                   132x44

  Compaq VGS             35                   132x25
                         36                   132x28
                         34                   132x43
                         39                   132x50
                         40                   132x60

  Genoa VGA              35                   132x25
                         36                   132x28
                         34                   132x43

  Orchid VGA             38                   80x60
                         35                   132x25
                         36                   132x28
                         34                   132x44

  Paradise EGA/VGA       85                   132x25
                         84                   132x43

  Sigma VGA              28                   132x25
                         29                   132x44

  STB VGA                35                   132x25
                         34                   132x44

PARADOX.VID also contains info on Video-7 and Everex boards, but I'm not
able at present to interpret exactly what it means.  At this time, I've
had success using the Orchid (but with a Cardinal video card) and ATI
modes listed above.


Program Level1

Level1 is a demo program which may work depending on your mouse driver.
From the Video selection in the menu, you can select the normal TV
80x25 and 80x50 modes along with 'Other'.  'Other' brings up an inputbox
in which you can enter a mode number to see what happens next.

A window contains information on the present state--the mode number,
the contents of StartUpMode, and the current screen height and width.
StartUpMode is the mode from which the program was called and is used
to restore that mode on exit or when shelling to DOS.

To compile Level1.pas, you first have to modify DRIVERS.PAS.  The single
modification consists of commenting out the last line of FixCrtMode, thus:

	(*MOV	AX,smCO80   *)

FixCrtMode is a routine which limits the video mode to monochrome or the
standard VGA color modes.  Removing the last line effectively disables the
routine so that any mode may be programed.

When doing a make on Level1.pas, the object directory list should include
the directory where sysint.obj is located and the unit directory list
should include the TV source directory (normally \bp\rtl\tv).


Program Level2

If the mouse causes problems in the Level1 program, it's time to move on to
Level2.  In Level2, the mouse driver cursor is hidden and the
cursor displayed from DRIVERS.PAS.  The modifications required for
DRIVERS.PAS are much more substantial.  Here they are:

Add the following to the Interface section:

const
  SimulatedMouse : boolean = False;    {indicates if simulated mouse active}

procedure SimMouse;       {switch to simulated mouse}
procedure DriverMouse;    {switch to normal driver mouse cursor}

These are the calls to switch back and forth between the normal usual mouse
cursor and the simulated cursor.

Add the following just before the MouseInt procedure:

var
  OldPos : word;       {marks the current mouse position}
  HideCount : integer; {simulated mouse Hide count}

procedure SimMouse;
begin
HideMouse;
SimulatedMouse := True;
HideCount := 0;
end;

procedure DriverMouse;
begin
SimulatedMouse := False;
ShowMouse;
end;

In MouseInt, change the lines:

@@1:	MOV	EventQTail,DI
	INC	EventCount
@@2:	MOV	MouseIntFlag,1
end;

to:

@@1:	MOV	EventQTail,DI
	INC	EventCount
@@2:      cmp SimulatedMouse,0
            je @@3               {this code for software mouse only}
          cmp HideCount,0
            ja @@3              {mouse is hidden}
          mov al, ScreenWidth
          xor ah,ah
          mul mouseWhere.Y
          add ax, MouseWhere.X
          shl ax,1
          les di, ScreenBuffer
          add di,ax
          cmp di,OldPos
            je @@3     {no position change}
          push di
          mov di, OldPos   {change the old position back}
          mov ax, ES:[di]
          xor ah, $77      {invert the colors to where they were}
          mov ES:[di], ax
          pop di
          mov ax, ES:[di]
          xor ah, $77      {invert the colors}
          mov ES:[di], ax
          mov OldPos,di    {and save the position}
@@3:	MOV	MouseIntFlag,1
end;

Just before the ShowMouse procedure add:

procedure ShowMouse1;
begin
Dec(HideCount);
if HideCount < 0 then HideCount := 0;   {synchronize}
if HideCount = 0 then     {make mouse visible}
  begin
  asm
          mov al, ScreenWidth
          xor ah,ah
          mul mouseWhere.Y
          add ax, MouseWhere.X
          shl ax,1
          les di, ScreenBuffer
          add di,ax
          mov ax, ES:[di]
          xor ah, $77      {invert the colors}
          mov ES:[di], ax
          mov OldPos,di    {and save the position}
  end;
  end;
end;

At the start of the ShowMouse procedure change the following:

asm
	CMP	ButtonCount,0
	JE	@@1
	PUSH	AX

to:

asm
	CMP	ButtonCount,0
	JE	@@1
        cmp SimulatedMouse,0
          je @@2
        push ax
        push bx
        push cx
        push dx
        push si
        push di
        push es
        call ShowMouse1
        pop es
        pop di
        pop si
        pop dx
        pop cx
        pop bx
        pop ax
        jmp @@1

@@2:	PUSH	AX


Just before the HideMouse procedure, add:

procedure HideMouse1;
begin
if HideCount = 0 then
  begin           {remove from screen}
  asm
          les di, ScreenBuffer
          mov di, OldPos
          mov ax, ES:[di]
          xor ah, $77      {invert the colors}
          mov ES:[di], ax
  end;
  end;
Inc(HideCount);
end;

In the HideMouse procedure, change:

asm
	CMP	ButtonCount,0
	JE	@@1
	PUSH	AX

to:

asm
	CMP	ButtonCount,0
	JE	@@1
        cmp SimulatedMouse,0
          je @@2
        push ax     {save everything}
        push bx
        push cx
        push dx
        push si
        push di
        push es
        call HideMouse1
        pop es
        pop di
        pop si
        pop dx
        pop cx
        pop bx
        pop ax
        jmp @@1

@@2:	PUSH	AX


As in Level1, delete or comment out the last line in FixCrtMode, as:

	(*MOV	AX,smCO80   *)


For those of you trying out these demo programs, I'd be happy to hear about
your success (or lack thereof) particulary for the modes and mouse
drivers I haven't been able to try.  Best way is via CompuServe:

Dave Baldwin
CompuServe ID : 76327,53

144 13th St East,
Tierra Verde, FL 33715     {winter}
(813) 867-3030

22 Fox Den Rd.,            {summer}
Hollis, NH 03049
(603) 465-7857


         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 4,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394