zavt	- enhanced MS-DOS ansi/avatar console driver

SYNOPSIS
	Include in \config.sys the line
		device=zavt.sys

DESCRIPTION
	Zavt.sys is a console driver which understands ANSI control sequences
	as well as Avatar level 0. It has several advantages over most other
	drivers.

	1. It supports any display mode the BIOS can set up (see below)
	2. It can be addressed by two different names so the default
		output can be left in raw mode (see below)
	3. The blasted bell is now 1/9 second

	4. Any DOS console entry may make use of a full-screen editor

	  One trivial advantage is the allowing of backspaces across the left
	margin. I don't know what problems this may create, but it is nice
	for the command line.

	COMPATABILITY
	-------------

	  Zavt gets all its information about the console from the BIOS data
	area - nothing is assumed other than that modes 0-3 and 7 are text
	modes. Other drivers assume your screen is 25 lines long, and that
	the video card is always left on page 0. This is a safe assumption
	most of the time, but bad practice. AutoCAD 2.5 for example is more
	efficient in switching between graphics and text when you configure
	it to write text on page one and use page 0 for its graphics, but
	will not give a usable text page with other drivers. Nansi has code
	in it to switch an EGA to 43 line mode, or an AT&T display to 50 line
	mode, but if you switch back by any means other than Nansi's own
	facilities, Nansi continues to assume 43 lines. Zavt responds to
	changes in display size very well. If you switch to a mode with more
	lines on screen (not by means of the driver - system specifics I
	leave to other software), Zavt will use them immediately. If you
	switch to a mode with fewer lines and the cursor is off the new
	screen, the next scroll will bring it along with the screen region
	around it into view. The best way to get a feel for this if you have
	an EGA is to play with the xxLINE.COM programs included. The names
	are for EGA, and will work for VGA, but will give you more lines than
	advertised.


	DEVICE DRIVERS
	--------------

	When you, for example, type
		C:> type foo.txt
	COMMAND.COM opens the file foo.txt, reads it, and writes it to
	the console driver, which puts it up on the screen. DOS has
	two ways of writing to the console driver:

	raw/binary mode: where the device driver is called once for
		a group of characters letting the device driver
		handle them all at once, or

	cooked/ASCII mode: where DOS calls the device driver once for each
		character to be sent, expanding any tabs.

	   Raw mode is much faster as the device driver is called fewer
	times requiring less overhead all together. However, you lose
	the ability to abort in the middle of output. If you TYPE a large
	file, COMMAND.COM sends it to the console driver 32K at a time, so
	if you Ctrl-Break, you'll have to wait until the first 32K have been
	displayed. DOS also no longer expands tabs, but this is easily
	handled by the device driver. Run RAW.COM then type
		C:> dir /w
	and rather than tabs between filenames, the tab character is displayed.
	Run COOKED.COM before continuing.
	   When DOS wants input from the console (such as when reading input
	for a filter such as MORE), raw and cooked mode also apply. In
	cooked mode, DOS will echo each character you enter, and interpret
	the cursor keys and f-keys allowing you to edit what you enter. DOS
	will also end entry when you hit CR, returning what you typed up
	to that point, even if more characters were requested. To demonstrate
	this, type
		C:> more
	and type some gibberish. DOS is requesting 4096 characters, but as soon
	as you type <enter>, entry ends and more prints out what you typed.
	Press f6 and enter to end.

	   When the console is in raw mode however, DOS does not echo
	characters, check for ^C, ^S, or ^P, and asks of the driver however
	many characters the calling program wants. The driver has no choice
	but to oblige, and without feedback, the computer seems frozen. Run
	RAW.COM included in this archive, then try MORE. Unless you type 4096
	characters, with a ^Z included to flag end of file, the computer is
	for all intents and purposes crashed.

	   So while setting the console to raw mode lets you display text
	*MUCH* faster, you have a potential trap if you run into software
	which requests data from the default input. The solution is to write
	to the console in raw mode, and read in cooked mode, but COMMAND.COM
	normally uses the same system handle for doing both. ZKEY.COM from
	this package will create a new default input handle in cooked mode
	while setting both the default output and the error output handle
	(which are still the same system handle) to raw mode. ZKEY does this
	through some underhanded tricks which work for all tested versions
	of COMMAND.COM from MS-DOS and PC-DOS, but will not necessarily work
	other DOS variants - 4DOS users must use both the default input and
	default output in the same mode.


	ANSI (taken from documentation for NANSI 2.4)
	----

	While putting text up on the screen, zavt.sys keeps a lookout for
	the escape character (chr(27), known as ESC); this character signals
	the start of a terminal control sequence.
	Terminal control sequences follow the format
		ESC [ param; param; ...; param cmd
	where
		ESC	is the escape character chr$(27).
		[	is the left bracket character.
		param	is an ASCII decimal number, or a string in quotes.
		cmd	is a case-specific letter identifying the command.
	Usually, zero, one, or two parameters are given.  If parameters
	are omitted, they usually default to 1. Spaces are not allowed
	between parameters.

	For example, both ESC[1;1H and ESC[H send the cursor to the home
	position (1,1), which is the upper left.

	Either single or double quotes may be used to quote a string.
	Each character inside a quoted string is equivalent to one numeric
	parameter.  Quoted strings are normally used only for the Keyboard
	Key Reassignment command.

	ESCAPE.COM from PC-Magazine is included as an easy way to send
	these control sequences, sending the ESC and [ followed immediately
	by whatever is given to it on the command line.

Control Sequences
	The following table lists the sequences understood by nansi.sys.
	Differences between nansi.sys and the standard ansi.sys are marked
	with a vertical bar (|).

Cursor Positioning
Short	Long name		Format		Notes
CUP	cursor position		ESC[y;xH	Sets cursor position.
HVP	cursor position		ESC[y;xf	Same as CUP; not recommended.
CUU	cursor up		ESC[nA		n = # of lines to move
CUD	cursor down		ESC[nB
CUF	cursor forward		ESC[nC		n = # of columns to move
CUB	cursor backward		ESC[nD
DSR	Device Status, Report!	ESC[6n		Find out cursor position.
CPR	Cursor Position report	ESC[y;xR<CR>	Response to DSR, as if typed.
SCP	Save Cursor Position	ESC[s		Not nestable.
RCP	Restore Cursor Position ESC[u

Editing
EID	Erase in Display	ESC[J 	Clears screen to cursor
EID	Erase in Display	ESC[1J	Clears screen from cursor.
EID	Erase in Display	ESC[2J	Clears screen.
EIL	Erase in Line		ESC[K	Clears to end of line.
EIL	Erase in Line		ESC[1K	Clears line up to cursor.
EIL	Erase in Line		ESC[2K	Clears entire line.

IL	Insert Lines		ESC[nL	Inserts n blank lines at cursor line.
DL	Delete Lines		ESC[nM	Deletes n lines, including cursor line.
IC	Insert Characters	ESC[n@	Inserts n blank chars at cursor.
DC	Delete Characters	ESC[nP	Deletes n chars, including cursor char.


Mode-Setting
SGR	Set Graphics Rendition	ESC[n;n;...nm	See character attribute table.
SM	Set Mode		ESC[=nh		See screen mode table.
RM	Reset Mode		ESC[=nl		See screen mode table.

IBMKKR	Keyboard Key Reass.	ESC["string"p
	The first char of the string gives the key to redefine; the rest
	of the string is the key's new value.
	To specify unprintable chars, give the ASCII value of the char
	outside of quotes, as a normal parameter.
	IBM function keys are two byte strings; see the IBM Basic manual.
	For instance, ESC[0;59;"dir a:";13;p redefines function key 1 to
	have the value "dir a:" followed by the ENTER key.
	If no parameters given, all keys are reset to their default values.

Character Attributes
	The Set Graphics Rendition command is used to select foreground
	and background colors or attributes.
	When you use multiple parameters, they are executed in sequence, and
	the effects are cumulative.
	   Attrib code		Value
		0		All attributes off (normal white on black)
		1		Bold
		2		Bold off
		4		Underline
		5		Blink
		7		Reverse Video
		8		Invisible (but why?)
		30-37		foregnd blk/red/grn/yel/blu/magenta/cyan/white
		40-47		background (no effect in graphics modes)

Screen Modes
	The Set Mode and Reset Mode sequences both accept one parameter,
	with the following values:
	    Mode Code	Value (same for Set and for Reset)
		0	text 40x25 Black & White
		1	text 40x25 Color
		2	text 80x25 Black & White
		3	text 80x25 Color
		4	bitmap 320x200 4 bits/pixel
		5	bitmap 320x200 1 bit/pixel
		6	bitmap 640x200 1 bit/pixel
		13	EGA graphics 320x200 4 bits/pixel
		14	EGA graphics 640x200 4 bits/pixel
		15	EGA [ IBM Monochrome display 640x350 2 bits/pixel?]
		16	EGA graphics 640x350 4 bits/pixel [with full 256K]

	    Mode Code	Set			Reset
		7      *Wrap at end of line 	No wrap at EOL
		45     *Graphics Cursor		No simulated graphics cursor

	Note: Modes other than the two set codes are BIOS display modes
	      and modes not listed which may be supported by new cards
	      (VGA for example) can also be selected by these functions.

	    [ * = default ]

Little Dead Blobs
	If you are using a graphics mode, and the cursor leaves little
	dead blobs behind when it moves, you are probably using a program
	which bypasses DOS (naughty, naughty).  It might help to tell
	Nansi to turn off its graphics cursor by sending the string
		ESC [ = 45 l
	(The last character in that string is a lowercase "L".)


	AVATAR
	------

	  While putting text up on the screen, Zavt.sys also looks out for
	^V, ^Y, ^L and ^P. The following is taken from documentation for
	OANSI.


	ALIASING

	In an Avatar sequence, the DLE character is "escaped."

	That's a scheme to let you use characters normally not available
	to an editor.

		DLE    Hex=10 Decimal=16


	Here are some examples of character aliases:

		Hex      Decimal    Real character
		----------------------------------
		10 83    16 131      3   (^c)
		10 9a    16 154     1a   (^z)
		10 90    16 144     10   (^p)
		10 10    16  16     10   (^p)


	When an Avatar terminal runs into a DLE character, it grabs the next 
	available byte and strips off the high-order bit.



	CONTROL CODES


		Command           Description
		-----------------------------------------------

		^v ^a <a>	attribute
				The "<a>" is a single
				byte.  The value of this
				attribute byte corresponds
				to the video attributes
				used by IBM on their CGA
				monitors.  (Intense video
				is supported, black-on-black
				is not.)

		^v ^b		blinking on
				blinking is turned off
				by the next "^v^a" 
				command

		^v ^c		move cursor up a line

		^v ^d		move cursor down a line

		^v ^e		move cursor left a line

		^v ^f		move cursor right a line

		^v ^g		clear to end of line

		^v ^h <r> <c>	set cursor position
				These are 1-based numbers
				with the "Y" (row) coordinate
				first.  The upper left of the
				display is "1,1."  The start 
				of the second line would be
				"2,1."

		^l		set current attribute to cyan
				on black, home cursor and
				clear screen


	   Avatar is a binary based protocol while ANSI is ASCII based.
	As a result, control codes which may have other meanins may
	end up part of an Avatar control sequnce. This is not a problem
	except when something tries to interpret a control code without
	realizing it is to be preserved. The only situation where this
	occurs that is of any concern is with DOS. If the console is in
	cooked mode, any ^i will become some number of spaces as DOS
	considers it to be a tab. This will corrupt any Avatar code with
	a ^i in it. The solution is to set the console to raw mode, which
	is the reccommended setup for speed as well.


	Full-Screen input
	-----------------

	   Code for the full-screen editor was mostly taken from PC-Magazine's
	DOS-EDIT and thus the mechanics are virtually identical. Being part
	of the console handler rather than a TSR however allows the editor
	to be used for any DOS input rather than only the command line.

	   For those not familiar, pressing cursor-up on the command line
	with DOS-EDIT loaded would move the cursor up one line and put
	you into the full-screen editor. From there, the special keys are

	Escape		leave the fullscreen routine
	Cursor keys	move the cursor accordingly
	Home		move the cursor to the left margin
	End		leave the full-screen routine, putting what is
			on the screen under and following the cursor
			into a buffer to be read as keyboard input
	PgUp		move the cursor to its original column
	PgDn		delete all characters on and following the cursor
	Insert		toggle insert/delete mode
	Delete		delete character to left of cursor and move text
			under and to the right of the cursor one space left
	Enter		same as End but adds a CR to the end of the data

	   The alpha-numeric keys print to screen while control codes
	may or may not depending on whether or not they have other purposes.
	Alt-<num> input always prints however, so it is possible to queue
	a sequence of strings by putting typing them on one line and typing
	13 on the numeric keypad while holding Alt in between each string.

	   Since ZAVT treats all console input the same, using cursor-up
	as the full-screen key may preclude software such as 4DOS which
	uses the key for its own purposes. In ZAVT without keyboard remapping
	Ctrl-PgUp is used in its place as it is reasonably obscure but
	still accessible. In ZAVT with keyboard mapping, there is no default.
	When a key maps a double-null, that is taken as the hotkey. Thus
	to define Ctrl-PgUp as the hotkey with ESCAPE.COM, type
		c:>ESCAPE 0;132;0;0p

BUGS
	The Set Mode and Reset Mode code 45 was chosen to match what
	was used in NANSI 2.4 which in turn was chosen without even
	looking to see if there were established codes for those functions.

	Insert and delete character do not work in graphics modes
	because BIOS does not include a scroll left/right function.

	Cursor Position Report has a carriage return in it, which is what
	ansi.sys does, but is nonstandard.

	Avatar RLE doesn't handle control characters - it assumes whatever
	you give it to repeat is printable and prints it, also assuming
	the repeat will not result in wrapping past the right margin.

	Wrap around left margin is nice, but nonstandard.
 
NOTE
	While I polished off this code and added some of my own, the bulk
	of it was written by Daniel Kegel, and Thomas Hanlin III to
	whom credit is due. My distribution policy is the same as for the
	formentioned authors' drivers, which is as follows as taken from
	the documentation for NANSI24.

	This program and all files associated with it are hereby placed
	in the public domain, and thus may be freely copied and distributed.

	If you really like this program, either
	(a) improve it, and place your improvements in the public domain,
	(b) write a neat program which uses Zavt's unique speed, and
	    place your program in the public domain,
	(c) tip the author (Tip; contraction for "To Inspire Programmer";
	    traditionally, a contribution of $5 per copy), or
	(d) resolve to become a better human being in the future.

	Any problems or suggestions can be made to the 'author' at

	FidoNet - 1:250/628.
	RT-Labs (416)867-9663, Toronto.

or by writing
	Luns Tee
	32 Thyra Ave.
	Toronto, Ontario, M4C-5G5
	Canada


FOR PROGRAMMERS

	If the code seems to be a mess, that's because it is. Code from ZANSI
	has been juggled around so as to minimize the number of JMPs that are
	not JMP SHORT. Just a few hints:
		Search for "90" in the .LST files. If any follow a JMP
	instruction, make the JMP a JMP SHORT as these are NOPs to pad
	the size difference between the two variants of this instruction.
		When writing anything which writes to the console, use
	an IOCTL call to get the driver's attributes, save them, and set
	the console to raw mode. Do not write to the console by calling
	Int 21h function 2 once for each character (it's not that uncommon)
	but rather function 40h for each string. Buffering strings larger
	than about 10 characters starts diminishing returns. Just remember
	to return the console to its original state before exiting (and
	do not make any assumptions about the state - check it on entry).

		The file ZAVT.MAK has switches for Turbo Assembler and not
	Microsoft MASM which NANSI was compiled under. The .MAK file itself
	is for Microsoft's MAKE utility however.

FILES

ZAVT*.ASM	- console driver source files
ZAVT.MAK	- make file for ZAVT.SYS
ZAVT.SYS	- full-featured driver
ZAVTNK.SYS	- driver with keyboard remapping disabled
ZKEY.COM	- sets up stdin/stdout/stderr handles to ideal states
RAW.COM		- program to set console to raw
COOKED.COM	-   and cooked mode
ESCAPE.COM	- program to send escape sequences to console
FONTS.ZIP	- assortment of ega/vga fonts with font editor
ZAVT.DOC	- this file