HOST 2.2

                      Miniature BBS host program


                                  by

                               Bob Eyer
                             [73230,2620]

                             April 4, 1992



     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ SEE SHAREWARE NOTICE BELOW ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
         For a fee, the author will modify program for custom
                             applications.


     ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ FEATURES OF HOST ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

     - Uses very little disk space, and less than 50K memory

     - Can be run 'right out of the box' with no configuration at all

     - Two types of local Sysop logon

     - ESC key abort to terminate online caller

     - User specifiable rings to answer on

     - Ringback option - user selectable wait time

     - Chat

     - Messaging

     - File transfer, typing files

     - Sysop shell to DOS - Available only to registered users

     - Caller log inspection for Sysop - Registered users only

     - Expert/novice menu and prompt modes

     - Automatic wipe minor prompts at or above 1200 baud

     - Ctrl-K/X (abort)

     - Selectable timelimit for non-Sysop callers

     - 2-minute prompt inactivity logoff

     - RTS/CTS hardware handshaking for maximum speed

     - In event string pool problems, ejects to DOS with
       error level 2, for batch file reprocessing.

     ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

     Syntax
     ------

     HOST [port baud] [LOCAL BUL]


     port     The number of the communications port to be made  active.
              HOST   is  capable  of  identifying  ports  1-4,  without
              supplementary specification of IRQ lines and addresses.

              If not mentioned, HOST defaults to 1.

     baud     The  baud  rate at which to open the communications port.
              If not mentioned, HOST  defaults  to  9600.   Valid  baud
              rates are 300, 1200, 2400, 9600, and 19200.

              If  19200  is  selected,  HOST will assume the modem is a
              USRobotics Courier HST or Dual Standard,  and  will  send
              &B1  &N8  to  the  modem to fix the modem to the DTE (the
              communications  port),  unless  the  user  overrides   by
              specifying a new value of FIXED in the HOST.CFG file (see
              below).   In  such  case, remote must call at same speed.
              Under such conditions, the modem/DTE link will operate at
              14.4k baud.  Caveat: HOST's default response to  a  19200
              fixed baud setting assumes that the default NRAM1 setting
              contains  either  &M4  or  &M5.   USR fixed baud settings
              require operation at least at level 4.

              At  9600  or  below,  HOST sends &B0, &M4, and &N0 to the
              modem, so that it will follow the caller's connect  rate,
              unless the user overrides the NRAM settings in HOST.CFG.

              HOST   does  not,  in  its  default  configuration,  save
              commands to the modem's NRAM, but resets  modem  settings
              to their previous states on exit.  As a result, it is not
              necessary   to  reconfigure  your  dialling  program  for
              dialling out, after using HOST - unless you add &W to new
              values for NRAM1 or NRAM2.

     LOCAL    A commandline keyword which specifies that HOST is to  be
              run without communicating with the modem at all, for test
              or illustration purposes.

              The  user  may  see how HOST works for the first time and
              without a modem, just by entering the command

              HOST LOCAL

              The  host  may  also be run by the Sysop in local mode by
              pressing the Esc key after HOST is in  WAITING  FOR  RING
              mode.     However,   this   mode   does   involve   modem
              communications, and will abort if a modem is not properly
              connected to your selected communications port.

     BUL      A  commandline  keyword which specifies that the HOST.MSG
              file is to be displayed as  a  bulletin  for  the  caller
              before he or she reaches the Main Menu.  Useful primarily
              where the Sysop anticipates a particular caller and wants
              to display some instructions which might be needed by his
              caller.

     Commandline keywords must appear  AFTER  the  numeric  parameters,
     port and baud, where listed at all.

     Example:  HOST

     will  open  COM1  at 9600 baud, No parity, 8 bits, 1 stop bit, and
     will function so as to enable callers to connect.  The caller will
     not see HOST.MSG before the Main Menu, since BUL is not mentioned.

     'HOST 2400' opens COM1 at 2400 baud.

     'HOST 3' opens COM3 at 9600 baud, if COM3 exists.


     Discussion
     ----------
     I  wrote  this  program chiefly as a very small BBS for occasional
     use, particularly for situations in which  someone  wants  a  file
     from  me, but doesn't want to go the roundabout route of having me
     post on a large BBS for subsequent download.  This  procedure  has
     pitfalls  - such as whether I and my party are members of the same
     BBS, and whether that facility offers private file transfers.

     The largest problem with most host programs in occasional  use  is
     that  they  require  the  user  to  refresh  his  memory on how to
     configure them.  This is often  a  colossal  waste  of  time,  and
     impractical for occasional use.

     Another problem is disk space.  Keeping  a  fully  configured  BBS
     system  on  one's  hard drive can mean wasting 2 or 3 megabytes of
     space or more.   This  is  inappropriate  for  software  which  is
     intended to be used only once in a while.

     RBBS, PCBoard, Wildcat, and other programs have long been  in  the
     "large host" category; and so they just don't fill the need.

     Minihost,  now  known  as  Maxihost,  was  originally designed for
     occasional use, but has long since developed into a  host  of  the
     medium to large variety, intended for 24 hour operation.

     There  are  a  number  of  other small hosts, such as TinyHost and
     JaxHost, which aim at the needs of the occasional user.

     However, even these programs are large compared to HOST, and still
     require the user to check through the configuration  about  files,
     directories, user names, passwords, security levels, and so forth.
     All  this  stuff  is  liable to be inappropriate and forgotten, by
     the time the software is used on the next occasion.

     In  addition,  most  of  the top dialling programs, such as TELIX,
     BOYAN, and QMODEM, provide a script language so that the user  may
     write his own host.  However, the disadvantage of this approach is
     that  it is generally unsuitable for users who don't wish to learn
     script languages.


     In contrast to all these programs, HOST 2.2 can be run IMMEDIATELY
     by any owner of a low speed  Hayes-compatible  modem,  or  a  high
     speed  USRobotics  Courier HST or Dual Standard, with assurance of
     connect on the first ring, unless  the  user  specifies  rings  to
     answer on and/or ringback mode (see below about HOST.CFG).

     There are only a few things to remember:

     - You  must  know  which  port your modem is connected to, and the
       maximum speed.  If different from HOST's defaults, use the  ones
       that  apply.  Do NOT enter a baud rate on the command line which
       exceeds the maximum rating of your installed modem.  See  Syntax
       above.

     - If you don't want to specify your  file  transfer  directory  in
       HOST.CFG,  HOST will assume that it is the root directory of the
       current drive.  Files visible to the caller must  be  either  of
       reset  or  archive attribute status.  Files which are read-only,
       hidden, or system will not be displayed.

     - If  available,  HOST  uses three files which should be kept in a
       separate directory: HOST.CFG, HOST.LOG, and HOST.MSG.   Each  of
       these  files  is  an  ASCII  text file, intelligible to any text
       editor  or  wordprocessor.   The   LOG   and   MSG   files   are
       automatically generated by HOST, and require no maintenance.

       The  HOST.CFG file will probably be most important in specifying
       your secret code name, which gives you alone Sysop access to the
       DOS SHELL and the Inspect callers-log function.  See below about
       how to set up a CFG file.

       Where  a  CFG  file is not specified, HOST will assume all users
       have the same security, and no one will get access to DOS or the
       caller log.

     - HOST does not have any internal protocols for file transfer, but
       takes for granted that the user has a registered copy  of  Chuck
       Forsberg's DSZ.COM, located somewhere in the DOS path.  The four
       protocols  which  HOST  presents as choices all assume access to
       DSZ.  HOST shells out to DSZ and automatically sets up  the  DSZ
       commandline,  conformable  to  the  user's  selected option, and
       DSZ's  syntax.   File  transfer  does  not  involve  setting  up
       special batch files.

       In the event DSZ.COM or DSZ.EXE is not found in the DOS path (or
       in HOST's local directory), HOST simply returns to the Main menu
       without apparent effect to a caller.  However, at the host  end,
       the  message  'Bad command or filename' will be displayed by DOS
       in such an event.

     - HOST  does not check caller names against a user list.  Everyone
       except the Sysop has the same security  level.   Since  HOST  is
       designed  only  to  be  run occasionally, there is no need for a
       userlist.  However, HOST does write out caller names  to  a  log
       file  called  HOST.LOG.   The dates and times, together with the
       name  given  by  the  caller  should  generally  be  more   than
       sufficient for occasional use.

       In addition, HOST's monitoring function will write to HOST.LOG a
       short  descriptions  of  the caller's activities.


     ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
     NOTE:  You  can run HOST IMMEDIATELY at the root directory WITHOUT
     ANY CONFIGURATION AT ALL, and, if the files  needed  for  transfer
     are there, your caller should be able to pick them up.
     ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ



     FINE TUNING - HOST.CFG
     ----------------------
     This  file has a very simple structure.  It is based on the use of
     11 keywords: SYSOP, LOGON,  DELAY,  LIMIT,  RBACK,  RINGS,  FPATH,
     NRAM1,  NRAM2,  MINIT,  and FIXED.  The space character is used to
     associate each keyword with its intended value.   All  values  are
     read  as  strings,  so don't use quotes.  The order in which these
     variables are defined in HOST.CFG is immaterial; HOST will  figure
     out which is which.

     SYSOP         - Your secret name, as the Sysop (no length limit).
                     The default is no Sysop  name,  and  so  no  Sysop
                     privilege.   If SYSOP is defined in HOST.CFG, then
                     the caller logging on with  this  name  will  have
                     access   to  the  shell  and  user  log  functions
                     (available only to registered users).

     LOGON         - This is the message your  caller  will  see  first
                     after establishing connect with HOST.  The default
                     is not to print a logon message at all.

     FPATH         - The  drive-directory  where  file  transfer  takes
                     place.   If  not mentioned, this variable defaults
                     to '\' -  that  is,  the  root  directory  of  the
                     current drive.

     DELAY         - The  delay  time,  in   seconds,   between   modem
                     commands.  In command  mode  (when  no  caller  is
                     online),   instructions  sent  to  the  modem  are
                     followed by responses from the modem.  If commands
                     are sent too  quickly,  they  won't  be  received,
                     since  some  of  them  may  occur during the modem
                     reply.  The default of HOST  is  1  second,  which
                     should  generally be adequate to prevent this kind
                     of effect on USR Couriers.  However, you may  find
                     it  necessary  to  set  the  DELAY at 2 or 3.

     LIMIT         - A  non-Sysop  caller's  session  time limit.  HOST
                     prescribes no time limit for any person  who  logs
                     on  with the Sysop's secret name (see above).  All
                     other callers have a time limit assigned by LIMIT.
                     HOST's default is 20 (minutes).

     RBACK         - The number of seconds the host should wait  before
                     recycling  to  receive  the  caller's  second ring
                     sequence.  If this  number  is a positive integer,
                     ringback mode is automatically assumed by HOST.

                     HOST  does  not  make  any  use  of hardware modem
                     ringback  technology,   but,   instead,   controls
                     ringback processing entirely from within HOST.  As
                     a result, the user may define any kind of ringback
                     mode  he  wishes,  with ringback wait (the minimum
                     interval between the  caller's  first  and  second
                     call)  set  anywhere between 10 and 32767 seconds.
                     Usually, the  appropriate  setting  should  be  at
                     least  10  seconds.   The  standard  length of the
                     telephone ring cycle is about 6 seconds; and a few
                     additional seconds are necessary to distinguish  a
                     new  ring  cycle  from  merely the next one in the
                     same cycle.

                     Where  RBACK  is  omitted or is non-positive, HOST
                     deactivates ring-back mode.

     RINGS         - The number of rings which must occur  before  HOST
                     will make connect with a caller.  Again, HOST does
                     not  make use of modem technology here but handles
                     the ring problem entirely at the software level.

                     Where RINGS is omitted or  set  to  0,  HOST  will
                     attempt a connect on detection of the leading edge
                     of the first ring (i.e.  answer on "zero rings").

     NRAM1,  NRAM2,  MINIT,  and   FIXED   are   modem   initialisation
     variables.   You  may see illustrations of these strings simply by
     running

     HOST LOCAL

     They are summarised below the initial help screen.

     All  these  initialisation strings have default values supplied by
     HOST.  But each may be varied by the user as experiment  warrants,
     by  supplying  the  relevant  variable and associated value in the
     HOST.CFG file.

     FIXED is the only initialisation variable that behaves differently
     from  the  other  three:  The  purpose of FIXED is to override the
     other settings when 19200 is used on the  HOST  commandline.   The
     purpose  here  is  to set up a USR Courier HST or Dual Standard to
     receive fixed baud calls at 19200, so as to achieve throughput  of
     14400  baud.   The  supplied defaults should do this; but, if fine
     tuning is necessary, the  default  value  of  FIXED  can  be  made
     subject to the user's own override values.

     Sample HOST.CFG file:
     --------------------

     SYSOP DD334RTM_2
     LOGON SAM'S PLACE
     DELAY 2
     LIMIT 30

     In  this  example,  the  Sysop's secret name for logon purposes is
     DD334RTM_2, the logon message  will  be  SAM'S  PLACE,  the  modem
     command  delay  is  set  at  2 seconds, and non-Sysop callers will
     receive a maximum of 30 minutes online.


     The advantage of a program like HOST is that  the  user  can  park
     HOST.EXE  and HOST.DOC in his pathed \UTIL directory, and then run
     the program from anywhere.  For example, on some other drive,  the
     user  may  wish  to  keep  a  small subdirectory called \JOHN, for
     communications with, say, John Somebody, who prefers  to  call  at
     19200  baud.   The  directory  would  contain  a  batch file which
     automatically  specifies  the  loading  of  HOST  with  the  19200
     parameter,  so  that  John  can  get  14.4k  speed  downloads.  In
     addition, all the control files will be written in that directory,
     if the batch file is run from there.

     Obviously  other  small  directories could be set up as well.


     The  space  and  human memory saving advantage here is large.  The
     program, docs, and other small directories might  occupy  no  more
     than 60k.  And very few details need be attended to, so as to make
     HOST operational.

     Use of the Shell function
     -------------------------
     There are two main reasons why a person running a BBS should never
     provide general caller access to  DOS  through  a  shell  or  exit
     function.  (1) Any caller could do great damage to the software on
     his  or her computer, and (2) callers who are not knowledgeable on
     the use of shells in communications environments could easily hang
     up the operation of the BBS by doing something that would  prevent
     them  from  exiting  out of DOS level.  A few notes should be made
     about this second danger.

        (a) Normally,  when  BBS operators arrange for the use of a DOS
            shell, they do it by having the BBS program specify a batch
            file to execute the functions intended, and this batch file
            will call some kind of watchdog utility  which  causes  the
            host  computer  to  reboot  in  the  event of a prematurely
            dropped carrier.

            The main reason  for  the  watchdog  utility  is  that,  if
            carrier  is  lost,  the  caller  will be denied any further
            control over processing.  If no program is resident,  which
            can automatically restore the BBS, it will simply hang, and
            no  other  user will be able to log on, until the condition
            of the computer is fixed by the Sysop.

            An arbitrary shell function for Sysops does not provide any
            such utility; so if you call your own host and drop to DOS,
            you could make a simple mistake and cause  your  system  to
            hang  - unless you MANUALLY call a watchdog utility as soon
            as you are  at  DOS  level.   Watchdog  utilities  do  not,
            however,  work  equally well on all types of computers - so
            the risk of hang when drop to DOS  occurs  is  still  quite
            substantial even for the Sysop.

        (b) Certain keys, such as the backspace key, and  perhaps  even
            the cursor keys, may cause infinite loops to develop at DOS
            level,  unless the codes for these keys are redefined.  For
            example,  using  ASCII  8  for  the  backspace  key  in   a
            communications   shell   often   causes   infinite  looping
            behaviour, which cannot be stopped.  These  kinds  of  keys
            should  be  redefined  by using your modem S-registers (the
            backspace key is S5), or avoided altogether.

            DON'T use any keys at DOS level,  except  the  numbers  and
            letters  of  the  alphabet.   Any  deviation from this rule
            could cause your host computer to hang, while  you  are  at
            DOS level within a shell.

            If  you  must  use  DOS  while  online,  use  it through an
            applications program whose  output  is  redirectable  to  a
            communications   port,   and   which  itself  has  internal
            carrier protection.

            Direct  access  to  DOS  in  a  communications  session  is
            strictly for techies only!

            But,  it is made available here, chiefly for the benefit of
            knowledgeable users of communications  programs  who  would
            like  to  take  advantage  of  all  that  free memory space
            (generally, more than 500K) which HOST makes possible.

     Noise
     -----
     Generally, when run on error-correcting modems like the line of US
     Robotics Couriers, noise is rarely a serious problem.  The problem
     arises when a BBS is run  in  non-error  correcting  environments.
     Any  line noise is liable to cause communications to break down or
     be seriously interrupted.  HOST limits this problem  by  filtering
     all  strings transmitted through the echo function of prompts.  In
     particular, the filter passes only those  characters  whose  ASCII
     value  is  less  than 127 at speeds lower than 9600 baud.  At 9600
     baud or above, HOST assumes the modem is of  the  error-correcting
     variety, and so does no filtering.  This filtering process applies
     to  all  echoing  to  remote at opportunities for user input - for
     example, in chat, or in message entry.   It  follows  that,  where
     filtering  is  active,  HOST  does  not  permit remote upload of a
     graphics message to the Enter Note function.

     Errors
     ------
     HOST  2.2  supports  error  detection,  much  of which is used for
     internal reprocessing (such as error handling when the CTS line is
     dropped), and is  of  no  interest  to  the  user.   However,  the
     following errors have diagnostic importance:

     - Modem not connected to port or modem turned off

       This occurs when the modem status register has a value less than
       16, or when the ring and carrier bits are simultaneously set.

       Please let me know if your modem is otherwise  operational,  but
       you  cannot  get past this message.  HOST 2.2 will report to you
       the MSR value on your screen at run time.  I have tested HOST on
       a number of different kinds of modems with successful results on
       this error condition, but admit that  I  don't  have  exhaustive
       information about all modems.

       This  error condition is an attempt to deal with a problem which
       many communications programs simply ignore, with the result that
       they simply hang the computer, if the modem is not connected  or
       electrically  turned  off.


     - Illegal baud rate

       If you select a baud rate not supported by  HOST,  this  message
       will  occur,  returning  you  to DOS.  HOST will inform you what
       baud rates are legal.


     - Wrong port, wrong baud, or hardware problem

       This  message  occurs if HOST encounters any error while opening
       the communications port.  For example, if you select  2  on  the
       commandline   for   the  port,  and  your  machine  only  has  a
       communications  card that supports COM1:, this error will occur.
       It may also occur if you have a hardware problem - for  example,
       if  your  communications  card  needs  to  be  reseated  on  the
       motherboard, or perhaps you should do a cold boot because  of  a
       lost  bit  somewhere  in  RAM.   Try  rebooting  if this message
       occurs.  If that doesn't work, open up your machine  WITH  POWER
       OFF and try reseating your communications card.  Of course, make
       sure  you're  using  the right port and baud on the commandline,
       when the machine is afterwards TURNED ON and rebooted.

       If  all  this  fails  to  make  HOST  get past this message, you
       probably have an electrically defective communications card.


     - STRING SPACE CORRUPT; Please call back in about 20 seconds

       This  error  may  occur  when  HOST's  string  pool  has  become
       corrupt.  HOST  automatically  puts  the  phone  line  off-hook,
       closes  the communications port, and exits to DOS with DOS error
       level 2, when this circumstance occurs.  The appropriate  action
       is merely to start HOST again from DOS, and this can be arranged
       automatically by making direct use of HOST's exit code.

       Since  HOST  allocates far more space (16K) than it needs (about
       4K), the user may never see this error occur.  But, if  HOST  is
       used  as a 24-hour BBS, the activating batch file should take it
       account, in order to avoid losing the host  on  rare  occasions.
       For  example,  the  following statements in the activating batch
       file would do the trick:

       :START
       HOST 2
       IF ERRORLEVEL 2 GOTO START

       In  this  case  HOST's  commandline  indicates  that the port is
       number 2, and that the modem supports speeds  up  to  9600  (the
       default if the baud rate is not specified).


     LOGGING OFF AND RECYCLING
     -------------------------
     HOST  2.2  reports inter-session processing on the local screen as
     it proceeds, so you can see where any error  occurs.

     One important problem that may develop, but for which HOST has  no
     error  detection,  occurs when a caller logs off but HOST does not
     drop his carrier - thus forcing him to drop carrier at  the  other
     end.  This fault is due to the fact that the switches of the modem
     which  HOST  is  using  are  set to force the DTR line high at all
     times.

     HOST drops the caller's carrier by dropping the local DTR line; if
     the host modem does not respond to this command, the remote caller
     will still be online.   The  caller  will  see  evidence  of  this
     malfunction,  by  noting  that  his  line was not dropped after he
     logged off, and that he sees on his screen the message to put  the
     host line offhook (it won't really be offhook if the remote caller
     sees   that  message).   As  a  result,  he'll  have  to  drop his
     own carrier manually.

     Therefore,  do NOT operate HOST on a modem configured to force DTR
     high at all times.  The 'force DTR high' switch should  be  turned
     off.

     In Closing
     ----------
     Please feel free to offer any criticisms or  suggestions  you  may
     have; I can be reached at Compuserve [73230,2620].


     - Regards, Bob




                        ** SHAREWARE NOTICE **

     This program is shareware: if you think it's a worthy addition  to
     your  personal  software,  you  should  make a contribution to the
     author.  In return for your contribution you will receive the most
     recent updates of the items mentioned in the list below.

     Simply purchase a money order from your bank in the amount of  $20
     US made out to Bob Eyer and send with your return address to:

       Bob Eyer
       1100 Bloor Street West
       Suite 16
       Toronto, Canada M6H 1M8

     Please mention in your accompanying note whether you wish 5.25" or
     3.5" diskette format,  and  state  the  name  in  which  you  wish
     registration-only  utilities  to  be  registered.

     Do not send cheques.

     Enquiries may be placed by writing  directly  to  the  author  via
     Easyplex at Compuserve [73230,2620].

     Warranty and Disclaimer:
     -----------------------
     The  author,  Bob  Eyer,  guarantees the physical integrity of the
     diskette covering the points  above,  and  will  replace  free  of
     charge, if it is received defective.  However, in no case will the
     author  be  responsible for any damages due to loss of data or any
     other reason.  In no event does the  author's  liability  for  any
     damages  exceed  the  price  paid  for  the  buyer's order of this
     software, regardless of the form of the claim.  The  person  using
     the  software  bears all risk as to the quality and performance of
     the software.


    DESCRIPTION OF PROGRAMS YOU WILL RECEIVE FREE WITH YOUR REGISTRATION
          ********************************************************

     Many  of the programs in the following list have not been publicly
     posted, and those which have been posted previously  are  unlikely
     to be posted in new updates, except in rare cases.

     Certain  programs  are  registered-only, which means that the user
     must not post copies on bulletin boards.  Some of these have  also
     never  been  posted  at  all, and are available ONLY to registered
     users.

     Versions  new  since last public post are indicated with a + sign.
     Entries marked by double asterisk have never been posted, and  are
     available  only to registered users, copies which will contain the
     user's name on the copy.

     Nearly   all  file-processing  programs  take  full  advantage  of
     wildcard logic, including DOS  shortcuts,  keeping  keystrokes  to
     absolute minimum.

     Total  size  in  compressed form for all of below, including docs:
     about 320K.

  ** MG 3.0
     ------
     Moving average ASCII graphing program.   Especially  designed  for
     obtaining  graphic  updates  on stock-market activity in practical
     trading environments, in which it is essential that the user get a
     quick  graph  immediately,  with  points  of  the  graph  directly
     associated  with  the  numerical  and other text information which
     these points represent (a feat  impractical  in  Lotus  graphics).
     Designed to be used with SETV below.

   + SPC 5.4
     -------
     Multidrive columnar drive report, with fairly complete description
     of  your  machine  including  communications,   important   chips,
     printer,   BIOS,   memory,   processor   and   coprocessor  speed,
     multitasking, networking, and so on, all in one  single  snapshot.
     New   version   doubles   the   amount   of  information  on  each
     communications port and displays the information in columnar  mode
     above  the drive report, adds an environment usage readout as well
     as a new P parameter to pause the PRINT multiplexer,  when  it  is
     used  to  feed  data  to  your  printer.  (DOS PRINT lacks a pause
     command).

     SETV 2.0
     --------
     Sets seven VGA text video modes.  Enables Multisync or VGA user to
     make  use  of seven major video text modes at DOS level, including
     132 column modes.

     HOST 2.2
     --------
     Provides   a   simple   BBS   host   for  occasional  use.   Fully
     configurable, but capable of being run 'right  out  of  the  box',
     HOST provides ringback, file transfer, mail, chat, userlog, shell,
     and much more - in an executable only 27K in size.

     AL 2.3
     ------
     Best  and  most flexible TSR alarm program with clock option.  Has
     time-locking and a full range of options.  7K of memory.

     CA 2.2
     ------
     Four-function fixed point TSR calculator with  formatted  displays
     and  scientific  notation  for  direct  paste  to  text.  Also has
     accumulator.  Four mode groups.  About 13K of memory.

   + CAF 2.2
     -------
     TSR floating point calculator with formatted displays  and  direct
     paste  to  text.   18  functions,  and an accumulation area.  Five
     types of modes.  Number formatting.  CAF is the most sophisticated
     calculator  in  the  business,  for  its  size.   27K  of  memory.

     PAUZ 2.2
     --------
     Replacement for DOS PAUSE, allows specification of seconds to wait
     or target [<=] time,  as  well  as  what  key  to  use  for  pause
     interruption.  User triggering of error levels 1 to 9.

   + MV 2.6
     ------
     Fast  file  mover.   Preserves  date/time/attribute  stamp for all
     moves.  Allows moving Read Only and  Hidden  files,  source  files
     opened  in  SHAREd  mode  for  network  users.   Wildcards.   None
     faster or safer.

  ** SPLT 2.1
     --------
     ASCII file splitter which, for the first time, offers the  ability
     to  prevent  the  split  from resulting in split messages or other
     defined  text  blocks.   Works  with  DIV  and  REV,  below.

  ** OTL 3.0
     -------
     Makes it  possible  to  apply  any  set  of  operations,  say,  as
     specified in a batch file, to every file in an ASCII list, without
     having to specify the path information for each file.  For Sysops.

  ** KALL 2.0
     --------
     For users of DOS 3.0-3.2 who would like batch  file  control  like
     that   offered   in   the  more  advanced  DOS  versions.   Allows
     redirection of batch file output, unlike DOS 4/5 CALL.

  ** SS 1.0
     ------
     Secure shell, protects  your  system  from  keyboard  redefinition
     resulting from ANSI codes read in remote message areas.  Maintains
     default DOS colour scheme, but requires use of NANSI.SYS.

     DIV 3.2
     -------
     Generalisation  of  FGREP-type programs to include blocks of text.
     A single string defines a block in most kinds of  blockable  text.
     DIV  handles  almost  any  kind.  Returns blocks containing one or
     more of up to 64 different strings from large ASCII files.  Useful
     in extracting messages or extended file descriptions containing  a
     range of strings without manual cut and paste.  Can prepare a file
     containing   every   block   EXCEPT   the   ones   selection,  and
     simultaneously.   See REV in short list below.

     COMB 2.2
     --------
     Sorts and combines wildcard text files  in  specified  order  into
     first  file  found  in  that order.  Primarily for eliminating the
     tedium and error involved in accumulating message files  into  one
     file  for  easy  reference.  Essential for systematic followers of
     international correspondence forums.

     ADD 2.4
     -------
     Adds very lengthy columns of numbers found in ASCII text, such  as
     byte  counts  in BBS listings without manual data entry.  (Capable
     of handling the addition of up to 1 billion numbers in one pass).

     CITM 2.4
     --------
     Counts   similar   items  in  formatted  ASCII  lists,  where  the
     similarity is based on a fixed string field found at one  position
     in  each  line of text, and all lines have been previously sorted,
     based on  the  contents  of  that  string  field.   Perfect  as  a
     companion   utility   for  Baker's  QSORT.

   + FVER 2.0
     --------
     Compares  a  file  list,  like  a BBS listing, to the actual files
     found anywhere in the BBS's download path.  Operates  in  FAST  or
     SLOW mode, depending on your safety requirements.  Can be operated
     remotely through a BBS door.

   + MVA 2.0
     -------
     Moves  files,  even if set to read only status, from anywhere in a
     specified download path to a given location.  Operates directly on
     ASCII lists, like directories or BBS listings.   Can  be  operated
     remotely through a BBS door.

     RNF 2.1
     -------
     Minimises keystrokes and keystroke error on  renaming  files  with
     date  or  time  info  or special flags.

     plus:
     ----
   + LF    - Linefeeds printer by user-supplied number of lines.
   + PF    - Pagefeeds printer by user-supplied number of pages.
   + DOSV  - Writes out major element of DOS version as error level.
   + RING  - TSR ring detector for users who don't like phone rings.
   + PORT  - TSR/non-TSR display of modem statistics for specific port.
     ELIM  - Advanced replacement for DEL.
   + EMS   - EMS detector for error level control in batch files.
     LCNT  - Very fast linecounter; formatted output.
     ESRT  - Element sorter.  User specified delimiter.
   + TYME  - Program execution timer.
     CHG   - Attribute file/directory/date/time  file  changer/reader.
   + CBRO  - Compuserve Browse converter.  Old/new  formats.
     REV   - Reverses order of blocks of text (messages, etc).
     DTR   - Toggles modem DTR line.
     RTS   - Toggles RTS line.
  ** CFIX  - Fix cursor to normal, block or off.
  ** EL    - Converts number to error level, for batch files.
     WD    - Gives wildcard support to any program.
     SWP   - Fast single-level sweep program.
     TSTF  - Floppy disk status tester.
     ----------------------
     End of documentation