ЫЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯ
Ы HOW TO USE THIS TROUBLE-SHOOTING GUIDE                                       Ы
ЫДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДЫ
Ы                                                                              Ы
Ы This guide is contained in the file  SAPPHTS.DOC.  You can print it out, but Ы
Ы it works best if you view it via the SYSOP menu, which uses our SEE program. Ы
Ы To do that, enter SYSOP at the DOS prompt, select INFO, then select TROUBLE. Ы
Ы This lets you search the guide for keywords whenever you have a problem.     Ы
Ы                                                                              Ы
Ы Each problem described in this file is  preceded by a list of keywords, each Ы
Ы of which is preceded by  a slash character  (/).   Thus,  if you had a modem Ы
Ы problem, you could press "F" (for Find) then search for  /MODEM.  By repeat- Ы
Ы edly searching  for  /MODEM  (press  F3  after  the initial search)  you can Ы
Ы quickly scan the file for any related problems.                              Ы
Ы                                                                              Ы
Ы When in doubt about  which keyword to choose,  use the shortest one that can Ы
Ы describe your problem.  For example,  if a user has trouble connecting, look Ы
Ы for /CONNECT rather than /CONNECTION PROBLEM,  since /CONNECT would match on Ы
Ы /CONNECT or /CONNECTING or /CONNECTION and so on.  Most important, avoid any Ы
Ы plurals:  search for /MODEM, not /MODEMS.                                    Ы
Ы                                                                              Ы
Ы You can also search major categories.  See the INDEX section, below.         Ы
ЫЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬ


ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                                 == INDEX ==                                  Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ

          
  Major categories in this guide are presented in alphabetical order, as
  follows:

  ю COMMANDS (STANDARD)
  ю COMMANDS (SYSOP)
  ю DISPLAY
  ю DOORS  
  ю EVENTS
  ю FILE TRANSFER
  ю FRONT END
  ю INPUT
  ю MAINTENANCE
  ю MESSAGES
  ю MODEM
  ю NOISE
  ю PROGRAM FAILURE

  Specific headings are preceded by two equals signs and a blank (see INDEX
  heading, above).  Thus, to find the NOISE section, press F for Find, type
  "==", then a blank, then "NOISE".



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                          == COMMANDS (STANDARD) ==                           Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /COMMANDS/SET/NAMES/TEXT
PROBLEM:  How do SET, NAMES or TEXT work?

These commands "tune" other commands to restrict or control what they report.
SET controls them by time, NAMES by the name of the person or file being
referenced, and TEXT by any text (apart from name-oriented text) that might
be presented by the command.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                           == COMMANDS (SYSOP) ==                             Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /COMMANDS/USERS/CLEAN/CLEAN-UP/CLEANUP
PROBLEM:  How do I access clean-up mode?

To clean up the user list, you have to be in UltraMode (turned on and off with
Alt-F10).  Once you're in UltraMode, select the USERS command.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                                == DISPLAY ==                                 Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /SEE/VIEW/43/50/EGA/VGA
PROBLEM:  When viewing text files with SEE, I no longer switch to 43- or
          50-line mode

The version of SEE that accompanies Sapphire is a custom version designed for
Sapphire.  If you find a more recent version of SEE, don't install it in your
Sapphire directory.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                                 == DOORS ==                                  Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /DOORS/OTHER BBS/INTERFACE
PROBLEM:  How do I use doors that weren't specifically designed for Sapphire?

Several interface programs are available which will interface doors for one BBS
to another BBS.  For example, the shareware programs SP2QBBS and DOORMASTER can
be used.  Both of these programs may be obtained from our support system.  If
you use them, please support the author's efforts by registering them.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /DOORS/REMOTE
PROBLEM:  The door comes up but the users don't see anything

Here are a few things to check out:

1.  Are you running a "FOSSIL" driver?  If so, why?  Does the door NEED the
    fossil?  Can you disable the fossil when it's not being used?  If the door
    documentation doesn't explicitly say that it needs a fossil driver, try
    removing the fossil COMPLETELY before trying the door (i.e. reboot and
    don't install it).  Then, if that proves that the fossil was the cause of
    the problem, read the fossil documentation to see if there is some way to
    disable the fossil when it is not needed.

2.  Does the door know which port it is supposed to be using?  You may have to
    use a door interface program (described above) to let it know.

3.  Some programs (such as Pinnacle Software's Pyroto Mountain program) can
    accept the port information on the command line, in which case you should
    make sure that you are not pointing at the console.  Taking Pyroto as an
    example, if the command line specifies a port of 0 (zero), it means the
    console.  If it specifies a port address, it means the serial port.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /DOORS/RETURN
PROBLEM:  How does Sapphire know we are coming back from a door?

When Sapphire creates the batch file EXTERNAL.BAT, it writes the part where it
starts itself back up as follows:

  SAPPHIRE DOOR

This lets Sapphire know that it should not initialize the modem.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                                 == EVENTS ==                                 Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /EVENTS/RETURN
PROBLEM:  How does Sapphire know we are coming back from a event?

When Sapphire creates the batch file EXTERNAL.BAT, it writes the part where it
starts itself back up as follows:

  SAPPHIRE EVENT

This lets Sapphire know that it should not initialize the modem.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                             == FILE TRANSFER ==                              Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /DOWNLOAD/UPLOAD/ABORTS
PROBLEM:  File transfer aborts immediately

Here are a few things to check out:

1.  Are you running a "FOSSIL" driver?  If so, see the discussion of fossils
    in the DOORS section.

2.  If you are running on COM3 or COM4, you must tell DSZ this by specifying
    the DSZPORT parameter.  For example, if you are on COM3, you would have
    to enter the DOS command SET DSZPORT=3.  The DSZ manual explains more.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                               == FRONT END ==                                Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /FRONT END/FIDO/NETWORK
PROBLEM:  Does Sapphire support Fido or other networks?

Not at the moment.  We are looking into the possibility of creating a truly
maintenance-free network.  We have heard from some Fido sysops that they spend
up to 3 hours a week keeping their Fido system up to date.  This is not in keep-
ing with the "install and forget" design of Sapphire.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /FRONT END/INSTALL
PROBLEM:  How do you install a front-end program (to answer the modem)?

Another program can call Sapphire with the command:

  SAPPHIRE FRONT <baudrate>

This will start up Sapphire without touching the modem.  If the baudrate is 0
(zero) or omitted, it means that the user is at the console.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                                 == INPUT ==                                  Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /USER/ENTER/INPUT/FREEZE
PROBLEM:  User has to press Enter twice after each input.

The symptom is that the user will type some input, hit Enter, and the cursor
will "freeze" in column one -- before doing a linefeed -- and will not move
on until he hits another character.

This happens when the user sets his terminal program to send a CTRL-S whenever
he presses Enter.  For some reason, some Macintosh terminal programs seem to
come pre-configured this way.

Over the phone, it is very difficult to explain to a user how to solve this
problem.  In brief, however, he should look through his terminal program's
configuration section for something labelled "handshaking" or "ASCII protocol",
or something like that, and disable handshaking there.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /USER/INPUT/CHARACTERS/MISSING
PROBLEM:  Some of the characters the user types are lost.

Sapphire can have problems with multi-tasking software such as DesqView.  The
Sapphire serial routines are poll-driven rather than interrupt-driven.  What
this means is that, if you're running multi-tasking software, your users may
lose characters when they type.

Poll-driven I/O offers total port compatibility with all hardware platforms
upon which Sapphire is likely to be run, but it does make it inappropriate for
multi-tasking machines.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                              == MAINTENANCE ==                               Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ

ЙНННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННН»
є SEE ALSO:  COMMANDS (SYSOP)                                                  є
ИННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННННј

KEYWORD:  /FILE LIST/FULL/DISK/SPACE
PROBLEM:  File list is full

In most cases, the file list is self-maintaining, but if ALL of the files have
been on the list for less than 14 days, auto-maintenance is disabled.

When this happens, you can manually delete some files, using the FILES command
(when logged in at user level 8), or you can wait for a few days for some files
to time out.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                               == MESSAGES ==                                 Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /MESSAGES/READING/MISSING/NEW
PROBLEM:  The number of "new" messages reported is different from what is
          actually shown.

1.  If the message just before the first one in that message base is yours,
    yours will be diplayed, in order to put the replies in context.  This is
    not, however, a "new" message, so it isn't counted.

2.  Messages with no viewable text (or just the summary line viewable) due to
    use of <<privates>> or ><exclusives>< are not displayed, though they are
    counted in the "new" messages.  (It would take too long for Sapphire to
    look at each message in the message base, in advance, to see which ones 
    are visible.)

3.  If you physically delete message files (instead of using the ERASE 
    command), Sapphire will keep them listed in the message file, but won't
    be able to open the file when it is time to display it.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /MESSAGES/READING/MISSING/NEW/MINE/MOVE
PROBLEM:  When I send a message, I can't see it, even if I use the MOVE command
          to move it to a date ahead of my read date.

In normal reading, Sapphire avoids showing you your own messages unless they
serve to put other messages in context (see the previous item).  You can see
your own message if you do a Temporary SET, however.  But since SET can't be
entered before you logon, this means that you never see your own logon
messages (unless somebody else is also writing logon messages).  If you wish
to check your messages, use the REVIEW or CHANGE command.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                                 == MODEM ==                                  Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


  This categories is divided into the following sub-categories:
   
  ю CONNECTING
  ю DISCONNECTING
  ю MISCELLANEOUS


ЬЫЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЫЬ
Ы                               = CONNECTING =                                 Ы
ЯЫЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЫЯ


KEYWORD:  /MODEM/ANSWER/CONNECTING/CALL
PROBLEM:  Modem doesn't answer incoming calls.

This happens if the modem is not configured correctly, either in hardware or
modem settings.  Check all of the following suggestions; one of them may solve
your problem.

щщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщ
HARDWARE PROBLEMS
ъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъ

1.  If, when you start up Sapphire, it does NOT have an error-free dialog
    with the modem (i.e. if it complains about a carrier, or modem not
    ready, or if the modem never responds "OK"), refer to the trouble-
    shooting section concerned with those problems (do a keyword search for
    (slash)CARRIER, (slash)NOT READY or (slash)OK).

2.  If you have an external modem (a box outside your computer, as opposed
    to a card inside your computer), check the following:

    A.  Is your modem plugged in?  (Are lights glowing on the front panel?)

    B.  Is the modem plugged into the phone line?

    C.  Is the phone line plugged into the CORRECT plug on the modem?
        (Some modems have one plug for the line and one for a handset)

3.  As an aid to understanding the problem, try calling the modem on a voice
    phone.  Does it pick up the line?  If it does pick up the line, do you
    hear a carrier?

щщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщщ
MODEM SETTINGS
ъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъ

1.  If you have an external modem, it may have some lights which indicate how
    it is set, or what signals it is receiving.  Check these lights and
    settings, and compare them with the informatin in your modem manual.

    LIGHT                  USUALLY AFFECTED
    LABEL  MEANING         BY MODEM COMMAND  RELATED ITEMS IN THIS GUIDE
    ДДДДД  ДДДДДДДДДДДДДД  ДДДДДДДДДДДДДДДД  ДДДДДДДДДДДДДДДДДДДДДДДДДДД
    AA     Auto-Answer     ATS0=1            Search for (slash)DIP
    MR     Modem Ready     AT&D1             Search for (slash)DIP
    TR     Terminal Ready  N/A
    OH     Off-hook        ATH0              Should be OFF, not on.

    LIGHT
    LABEL  MEANING         COMMENTS
    ДДДДД  ДДДДДДДДДДДДДД  ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
    SD     Send            Should flash when modem  receives  your commands
    RD     Read            Should flash when modem replies to your commands

2.  If you have an internal modem, you still have to make the settings
    correctly, but you won't see any lights to indicate if your commands
    have been accepted.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /MODEM/ANSWER/CONNECTING/SPEED/9600/V32
PROBLEM:  Modem answers incoming calls okay at some speeds but not at others.

1.  In configuring your modem, you must take care to set the X setting (i.e.
    the ATX command) properly.  For example, some settings may not show the
    baud rate properly.  In general, use the highest X setting supported by
    your modem.

2.  If you are having trouble at baud rates of 9600 or more, you will have to
    consult your modem manual.  A sample problem:  the other person might be
    trying to connect an HST at 9600 to a V32 modem at 9600; the two methods
    are not compatible.

3.  Some modems, when initialized at one speed, will not jump to higher speeds.
    In such case, try initializing the modem at the highest speed it supports.

3A. If you are using a 9600+ baud modem, and you have a machine that runs at 8
    Mhz or faster, try initializing it at 9600 baud.  If that works, AND you
    have a V32bis modem AND you have a machine that is 16 Mhz and faster, you
    can try initializing it at 14400.  Do a search on <slash>HIGH SPEED for some
    additional notes on this topic.

3B. If your machine is slower than 8 Mhz, you will probably have to initialize
    at 2400 baud.  On some modems, this will make it impossible to receive calls
    at 9600 baud because the modem assumes that your initializing baudrate is
    the maximum you can attain.  This is a flaw in the design philosophy of the
    modem, and there is nothing that Sapphire can do about it.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /MODEM/ANSWER/CONNECTING/SPEED/HIGH SPEED/9600/V32/DTE/LOCKING/BAUD
PROBLEM:  People get nothing but noise when they connect to my high-speed
          modem.

The new high-speed modems have a very large number of settings.  In 99% of
Sapphire installation, your best bet is to TURN OFF all the fancy features such
as port speed locking, buffering, renegotiation, handshaking, flow control, and
so on.  These features are important when on-the-fly compression (MNP 5 and
V42bis) is required.  But since:

  (A)  Nobody can read at 9600 baud and...
  (B)  File transfers are generally compressed in archive (e.g. ZIP) files

the on-the-fly compression is usually more trouble than it's worth.

A V32 modem can not go faster than 9600 baud under any circumstances.  Only
compression makes its throughput faster.  A V32bis modem is faster, so you can
configure it at 14400 (if your machine is fast enough).

By the way, some "Fax Modems" claim to support 9600, but the 9600 may refer to
their fax function, not its data rate (caveat emptor).  Moreover, not all 9600
bps modems are compatible.  A "non-dual standard" V-Hayes, Telebit PEP or
CompuComm modem will communicate with a different model at 2400 baud, but can
attain higher speeds when talking to the same kind of modem.  If you're thinking
about getting a high-speed modem, get a V32 or V32bis model, as this has become
the accepted standard.  (Nevertheless, not all V32 modems are created equal and
sometimes different brands refuse to communicate at more than 2400 baud.)

High speed modems support something called "locked baud rates".  This means that
no matter what speed the caller dials in at, the modem will talk to Sapphire at
a specific speed.  When a modem is advertised as supporting more than 14400
baud, it usually means that it is connected to the remote system at a lower
speed, hooked up to the local computer at the higher speed, and uses compression
to try to achieve the higher baudrate (throughput).  But as mentioned earlier,
this rarely produces the expected benefits.

Your modem should be set to have a "floating" or "unlocked" baud rate (different
manufacturers use different words), so that when a 2400 baud call comes in, the
modem says "CONNECT 2400", and when a 1200 baud call comes in, it says "CONNECT
1200".  With a locked baud rate (sometimes called a locked DTE rate), the modem
will always report the same connect speed.  Unless you are very sure of what you
are doing, you best bet is to turn off this feature (and other fancy features).

With all these settings, you might wonder how you can get all the configuration
information into one Sapphire setup command.  Fortunately, most new modems have
"stored profiles" so that a simple command (e.g. ATZ1) can load a particular
configuration.  Most modems use the commands AT&V, AT&W and AT&F to support
stored profiles.  Your modem manual will provide you with the details.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /MODEM/ANSWER/CONNECTING/SPEED/300
PROBLEM:  Modem doesn't work properly on 300 baud calls

Some 9600 baud modems can't support the higher baud-rates and 300 baud at the
same time.  Under some circumstance, the Telebit T1600 exhibits this behaviour.
There is no way to fix this problem except to experiment with the modem's
internal settings.  Be sure to record your modem's present settings before you
start experimenting.



ЬЫЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЫЬ
Ы                              = DISCONNECTING =                               Ы
ЯЫЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЫЯ


KEYWORD:  /MODEM/HANG UP/ECHO
PROBLEM:  When user hangs up, modem endlessly echoes back to Sapphire.

Some modems don't have time to drop the carrier while characters are being
sent.  For this reason, you have to configure the modem not to echo command
characters.  This can cause an echoing loop when somebody hangs up.

ЪъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъї
| The solution given here applies to most modems, but check your modem manual |
АъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъЩ
ЪъДъДъДъДъДъДъДъВъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъї
|   MODEM HAS   |                                                             |
| DIP SWITCHES? | ACTION TO BE TAKEN                                          |
ГъДъДъДъДъДъДъДъЕъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъґ
|     YES       | Set switch 4 to NOT echo characters                         |
ГъДъДъДъДъДъДъДъЕъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъґ
|     NO        | Include E0 - not E1 - in your modem initialization command  |
АъДъДъДъДъДъДъДъБъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъЩ



ЬЫЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЯЫЬ
Ы                              = MISCELLANEOUS =                               Ы
ЯЫЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЬЫЯ


KEYWORD:  /MODEM/CARRIER
PROBLEM:  Sapphire says that the modem is presenting a carrier.

You must set your modem so that it does NOT present a carrier -- unless some-
body has dialed in and is connected.

ЪъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъї
| The solution given here applies to most modems, but check your modem manual |
АъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъЩ
ЪъДъДъДъДъДъДъДъВъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъї
|   MODEM HAS   |                                                             |
| DIP SWITCHES? | ACTION TO BE TAKEN                                          |
ГъДъДъДъДъДъДъДъЕъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъґ
|     YES       | Set switch 6 to use CD line                                 |
ГъДъДъДъДъДъДъДъЕъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъґ
|     NO        | Try including &C1 in your modem initialization command      |
АъДъДъДъДъДъДъДъБъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъЩ

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /MODEM/NOT READY/READY
PROBLEM:  Sapphire says that the modem is not ready.


1.  If you have an external modem, are all wires of the modem cable connected
    properly?

    A.  If you have a "null modem cable" (pins 2 and 3 cross-connected)
        Sapphire won't answer.

    B.  Using some wire, a flashlight battery, and a flashlight bulb as a
        simple continuity tester, check that the important pins are connected
        end-to-end:

        Pin 1 (or Pin 7)   Pin 2   Pin 3   Pin 8   Pin 20

        The pin numbers are usually written in tiny letters on one of the
        connectors, or pin 1 is marked with a little arrow.

ъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъ

2.  Make sure that the modem is configured to use the Terminal Ready line.

ЪъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъї
| The solution given here applies to most modems, but check your modem manual |
АъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъЩ
ЪъДъДъДъДъДъДъДъВъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъї
|   MODEM HAS   |                                                             |
| DIP SWITCHES? | ACTION TO BE TAKEN                                          |
ГъДъДъДъДъДъДъДъЕъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъґ
|     YES       | Set switch 1 to use DTR line                                |
ГъДъДъДъДъДъДъДъЕъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъґ
|     NO        | Try including &D1 or &D2 in modem initialization command    |
АъДъДъДъДъДъДъДъБъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъЩ

ъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъъ

3.  Make sure the modem's DSR behaviour is configured properly.

Some modems allow the selection of the behaviour of the Dataset Ready (DSR)
signal.  The proper setting is "always on", but some modems let DSR indicate
whether or not there is a carrier.

On modems without DIP switches, you can usually set DSR behaviour with the &S
setting.  For example, on most Hayes modems, &S0 sets the corrects behaviour.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /MODEM/OK/AT COMMANDS
PROBLEM:  The modem seldom or never responds "OK" to the commands I send it.

1.  Try configuring the modem at a lower baud-rate -- it may be missing some
    of the responses.  The initialization baud-rate is set via SYSOP:CONFIG.

2.  If the problem happens only after you've used another modem-oriented
    program, turn the modem off and on before starting Sapphire.  The method
    by which some modems figure out their command baudrate may make it
    impossible for Sapphire to reset the modem.

    Technical explanation:  Modems determine their command baudrate by looking
    for an "AT" after a reset.  Some modems reset on a DTR transition; some
    don't.  In such case, the easiest way to do a reset is to turn the modem
    off and on.

ДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

KEYWORD:  /MODEM/DIP SWITCHES
PROBLEM:  Modem has DIP switches.

Older modems have tiny DIP (dual-inline-package) switches (sometimes you have
to open the modem to find the bank of switches).  In most cases, they are set
as follows:

ЪъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъї
| The solution given here applies to most modems, but check your modem manual |
АъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъДъЩ

      Switch 1 UP:   Computer should use the Data Terminal Ready (DTR) line
      Switch 2 UP:   Result codes sent as words
      Switch 3 DOWN: Result codes are sent to the computer
      Switch 4 UP:   Echo incoming characters
      Switch 5 DOWN: Don't answer incoming calls
      Switch 6 UP:   Computer should use the Carrier Detect (CD) line

These modems may also have switches 7 and 8; check your manual to see how
they should be set.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                                 == NOISE ==                                  Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /NOISE/RANDOM/CHARACTERS/GARBAGE/CONNECTING
PROBLEM:  Users see some random characters when they connect.

1.  If only one user has this problem, ask him to try on a different modem,
    or to try from another location.

2.  If everybody has this problem, disconnect ALL phones at your house (even
    those on other lines) except the modem.  If this cures the problem, it
    may indicate the problem.  Some conference phones, for example, cause
    leakage between lines, which causes line noise.

3.  If you have this problem during early testing, make sure that the other
    person has called other BBS's before, at the baud rate being attempted,
    and that the baud rate being attempted is within the capabilities of both
    modems.

4.  See also the CONNECTING items in the MODEM section.



ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ
Ы                                                                              Ы
Ы                            == PROGRAM FAILURE ==                             Ы
Ы                                                                              Ы
ЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫЫ


KEYWORD:  /PROGRAM/FAILURE/ERROR CODE/RUNTIME ERROR/IO ERROR/BUG
PROBLEM:  Program fails with an error code.

Call our BBS at 514-345-8654 and have a look around.  We may have a copy of
SAPPHTS.DOC that covers your problem or a new version of SRUN.EXE that solves
it.  If that doesn't help, call our voice support line at 514-345-9578.

If you think you've spotted a bug in Sapphire, the most helpful thing you can do
is learn to make it happen on demand.  That is to say, before you report a
problem, try to understand it well enough to make it happen on purpose.  Here's
a checklist to help you assess the problem:

  1.   What do you think causes the problem?
  2.   How often does it happen?
  3.   Does it happen to everybody or just certain people?
  4.   Did it start just recently or has it always happened?
  5.   If it just started, what changed just before it started?
  6.   What have you done to try to solve the problem?