Copyright 1990,1991,1992,1993 by A.C.E.  Software & Michael G Phelps




      Please submit all MACRO suggestions to
      (a) a MSG to Michael Phelps on the ACECOMM support BBS
      (b) a MSG to Michael Phelps on Compuserve UID 75120,3306



                              CONTENTS

Chapter 1   ACECOMM  MACRO Programming Language....................2
            Local User Input (LUI) Functions.......................2
            Character I/O Functions................................6
            File Functions.........................................8
            Data Transfer functions................................9
            Modem Functions.......................................12
            FON Record / Dialing..................................13
            Misc Functions........................................15
            Expandable MACRO Parameters...........................16
            Expandable MACRO Functions............................17


      The MACRO PROCESSOR supports MACRO STACKING
      MACRO STACKING means multiple MACROS per line
      Here are three examples of MACRO STACKING

       <SendStr>u z ACE0601.ARJ^M <SendZmo>files\ace0601.arj

       <SendStr>u z ACE0601.ARJ^M <RunProgram>DSZ sz -m files\ace0601.arj

       <SetDTR> ON <SendStr>ATDT846-2940^M <WaitStr>CONNECT <SendStr>^[^[






















MACRO.DOC       Page 1



Chapter 1  ACECOMM  MACRO Programming Language

           Local User Input (LUI) Functions




   <AutoScrGen_LUI>

      - Toggle AutoScrGen(tm) mode

      Toggle AutoScript Generation mode On/Off.  When "On" an extended
      status  line  will  appear at the bottom of the TERMINAL screen.
      At the far left of the extended status line will be  the  phrase
      "AutoSriptGen"


   <BackBuffer_LUI>

      - Menu Area
      - Enter Back Buffer Screen Area

      BackBuffer  contains  the  last n lines of display that scrolled
      off the TERMINAL screen.  BackBuffer has a status line  of  it's
      own.   The status line contains such information as current line
      position into the buffer, total lines buffered, and some of  the
      navigational  keys are displayed.  Hold the ALT key down for the
      POP UP REFERENCE available for the BackBuffer area.


   <CaptureFile_LUI>

      - Toggle Capture File
        Prompts for filename

      Capture  will also prompt for append or overwrite.  Capture does
      absolutely NO filtering of any kind.  All data  is  recorded  to
      file  "as it comes in the port".  The ACECOMM package comes with
      separate utilities which can  strip  video  control  codes  from
      files.


   <FonListDialer_LUI>

      - Menu Area
      - Enter .FON List / Dialer

      Dial/.FON  directory  area.  While ACECOMM allows manual dialing
      from inside the TERMINAL area, it most convenient to dial from a





MACRO.DOC       Page 2



Chapter 1  ACECOMM  MACRO Programming Language

           Local User Input (LUI) Functions (continued)


      record contained in one of the .FON files available for use from
      the DIAL area.


   <FileLister_LUI>

      - Menu Area
      - Enter File Lister

      Files lister inside ACECOMM  provides  a  basic  directory  list
      function   capable   of   changing   directories   and   drives.
      File-marking, deletion, selection for appropriate  file-utility,
      etc.   LISTFILES  may  be created.  ACE.BCH is a file created by
      the Tag feature inside the File Lister Area.  files tagged  will
      be  listed  inside  ACE.BCH  as  CR LF terminated strings.  When
      selecting  any  of  ACECOMM'S  internal  batch  capable  sending
      protocols,  ACECOMM  will  check  for  the  existent of the file
      ACE.BCH and allow sending from the LISTFILE if desired.


   <CommandShell_LUI>

      - Enter Shell to Command Processor/ Operating System

      In most cases "Drop to DOS", if your  DOS  compatible  operating
      system  places  it's  name  in the environment where ACECOMM can
      find it.  "Shell" is not  hard  wired  to  COMMAND.COM  but  the
      COMMAND PROCESSOR as found in the environmental data area.


        Notes:  When  SWAP  is  "ON",  the  serial port is effectively
               disabled during the shell.   When  SWAP  is  "OFF"  the
               serial  port  remains  active  and any incoming data is
               handled  properly,  unless  the  receive  buffer  wraps
               around.


   <PrmDataMenus_LUI>

      - Menu Area
      - Enter PRM-data Menu Area


   <ScrnSnapShot_LUI>





MACRO.DOC       Page 3



Chapter 1  ACECOMM  MACRO Programming Language

           Local User Input (LUI) Functions (continued)



      - Menu Area
      - Take Screen Snapshot

      Create a "SnapShot" of the current screen minus any status lines
      active.   Prompts  for  a  filename.  Filenames always will have
      the .SNA extension.  ACECOMM can  detect  and  will  strip  away
      filename  extensions provided by the user when they do not match
      that of the function.  This command is available from  most  ALT
      POP UP REFERENCE areas.


   <ScrnTag_LUI>

      - Menu Area
      - Enter Screen Tagger Screen Area

      Tagger  will  allow  tagging  to  the  first SPACE_CHAR or press
      RIGHT-ARROW Tagger tags the entire line  of  text.   Tagger  has
      it's  own  status line, and a block cursor will appear inside of
      the Tagger mode.  Tagged items will  be  assigned  to  the  next
      available  SHIFT-Fn key.  Tagger pops up the SHIFT-Fn key window
      and displays each tagged item, as they are  tagged.   Tagger  is
      most  handy  for  grabbing  filenames  for  download  off  a BBS
      screen.  SHIFT-Fn key fires the tagged  item  back  when  ready.
      This command is available from most ALT POP UP REFERENCE areas.


   <SProtocols_LUI>

      - Menu Area
      - Enter Sending Unit Protocols Area


   <RProtocols_LUI>

      - Menu Area
      - Enter Receive Unit Protocols Area


   <RunScriptFile_LUI>

      - List .SCR directory, Allow selection, Run selected .SCR file






MACRO.DOC       Page 4



Chapter 1  ACECOMM  MACRO Programming Language

           Local User Input (LUI) Functions (continued)


      Lists the PRM-data .SCR directory Allows  selection  of  a  .SCR
      file for immediate execution.

      Notes:  ACECOMM  allows  .SCR  file  as an argument when started
      which immediately executes the script.












































MACRO.DOC       Page 5



Chapter 1  ACECOMM  MACRO Programming Language

           Character I/O Functions





   <WaitStr> STRING

      - Waits for a CASE sensitive string (sequence of characters)  to
        come  in the from the modem.  Can TIMEOUT.  Notes: The example
        below contains a SPACE_CHAR as the first character of  STRING.
        Arguments  to  MACROS  are  taken  as  is  up  until the first
        CR_CHAR.  A normal text editor in ASCII TEXT  mode  will  have
        placed  the CR_CHAR as the byte following the ':' character in
        the example STRING below ' name:'.  File Functions internal to
        ACECOMM will filter the  leading  SPACE_CHAR  from  the  MACRO
        ARG.  (unless I missed a function) <WaitStr> name:


   <SendStr> STRING

      -   Sends  a  string  to  the  modem.   Does  CONTROL  CHARACTER
        TRANSLATION.

        <SendStr>^M; Send a single CR_CHAR

        <SendStr> Michael Phelps^M; Note  the  leading  SPACE_CHAR  is
                                  ; part of STRING


   <DoorWayMode>

      -  Toggle  doorway  mode.   Saves  the  key press combo on entry,
        whatever key-combo you assign <DoorWayMode> to,  is  the  only
        way  out.  Doorway sends all key presses to the modem in their
        RAW 'un-cooked' form.  Non extended key presses are  send  LOW
        BYTE ONLY.  Extended key presses are sent LOW BYTE, HIGH BYTE.


   <HostEcho>

      -  Toggle  Host  echo mode.  This macro emulates HostMode's ECHO
        capability.  It does not answer the phone.  However modems set
        up for auto answer function normally.


   <HostMode>





MACRO.DOC       Page 6



Chapter 1  ACECOMM  MACRO Programming Language

           Character I/O Functions (continued)



      -  Toggle HOSTMODE.  PRM-data MDM_HOST_INIT is sent to the modem
        when hostmode flag is toggle "ON".  PRM-data MDM_INIT is  sent
        to  the  modem  when  hostmode flag is toggled "OFF".  ACECOMM
        begins responding to  the  RI  bit  SET,  and  will  send  the
        MDM_ANSWER  string  to the modem when RI BIT becomes asserted.
        <HostEcho> becomes active.

        HostMode  is  also terminated whenever the user dials out from
        the FON LIST MENU AREA.

        See your modems S7 register as an alternative.

   <LocalEcho>'  ,0

      - Toggle local character echo.  Local key-presses will be echoed
        to the screen.  (same effect as sending "ATE1^M" to the modem)
































MACRO.DOC       Page 7



Chapter 1  ACECOMM  MACRO Programming Language

           File Functions






   <SetFonFile> FILENAME

      -  Tacks  FILENAME  onto  the  PATH defined in PRM DATA for .FON
        files.  ACECOMM keeps track of the current(last accessed) .FON
        file.  FILENAME becomes the current .FON  file.   <SetFonFile>
        1_114.fon <DialRecord> 1


   <ChgDir> FILENAME

      - Make FILENAME current directory


   <RunScriptFile> FILENAME

      - Open and run FILENAME
        Notes:  Just FILENAME no PATH.  PATH found in PRM-data as .SCR
        is used.


   <RunProgram> FILENAME

      - Spawn an executable file.   Can  search  the  DOS  PATH.   Can
        determine files's extension (.COM, .EXE).  All system ISRs are
        restored  before  the  spawn  takes place.  The serial port is
        un-hooked.  The state of DCD, and LINE  CONTROL  are  left  in
        tact.

        After the spawn the system ISRs ACECOMM uses are  taken  back,
        the serial port is re-assumed.

        SWAP  FLAG  "ON"  and  XMS,EMS,  or DISK swapping takes place.
        SWAP FLAG "OFF" and ACECOMM is left in memory, with  exception
        to first restoring the serial port and interrupts.











MACRO.DOC       Page 8



Chapter 1  ACECOMM  MACRO Programming Language

           Data Transfer functions




   <SendFile> C:\MSG\COMM\ASCII.TX1

      -  Outputs  from  a file to the modem.  Sends the complete file.
        Does *NO* CONTROL CHARACTER TRANSLATION.   Data  sent  to  the
        modem is paced for buffer FULL, and all handshaking is valid.

        => ESC-key press aborts the function.


   <SendZmo> FILENAME

      Call internal zmodem sending unit with 1k data frame size.

      => ESC-key press aborts the function.


   <RecvZmo>

      Call  internal  zmodem  recv  unit.   ACECOMM's  internal zmodem
      receiver is capable of up to 8k data frame  size.   The  receive
      unit  will continue in batch mode until the sender stops sending
      files, or the user terminates the transfer.   Files  are  placed
      into   the  directory  pointed  to  in  the  PRM-data  area  for
      Downloads.

      => ESC-key press aborts the function.


   <SendYmo> FILENAME

      Call internal ymodem sending unit with 128 byte data frame size.

      => ESC-key press aborts the function.


   <SendYmo1k> FILENAME

      Call internal ymodem sending unit with 1k data frame size.

      => ESC-key press aborts the function.







MACRO.DOC       Page 9



Chapter 1  ACECOMM  MACRO Programming Language

           Data Transfer functions (continued)




   <SendYmoG> FILENAME

      Call internal ymodemG sending unit with 1k data frame size.

      => ESC-key press aborts the function.


   <SendXmo> FILENAME

      Call internal xmodem sending unit with 128 byte data frame size.

      => ESC-key press aborts the function.


   <SendXmo1k> FILENAME

      Call internal xmodem sending unit with 1k data frame size.

      => ESC-key press aborts the function.


   <RecvYmo>

      Call  internal  ymodem.  The receive unit will continue in batch
      mode  until  the  sender  stops  sending  files,  or  the   user
      terminates  the  transfer.   Files are placed into the directory
      pointed to in the PRM-data area for Downloads.

      => ESC-key press aborts the function.

   <RecvYmo1K>

      Call internal ymodem1K.  The receive unit will continue in batch
      mode  until  the  sender  stops  sending  files,  or  the   user
      terminates  the  transfer.   Files are placed into the directory
      pointed to in the PRM-data area for Downloads.

      => ESC-key press aborts the function.









MACRO.DOC       Page 10



Chapter 1  ACECOMM  MACRO Programming Language

           Data Transfer functions (continued)




   <RecvYmoG>

      Call internal ymodemG.  The receive unit will continue in  batch
      mode   until  the  sender  stops  sending  files,  or  the  user
      terminates the transfer.  Files are placed  into  the  directory
      pointed to in the PRM-data area for Downloads.

      => ESC-key press aborts the function.


   <RecvXmo> FILENAME

      Call  internal  xmodem.   Files  are  placed  into the directory
      pointed to in the PRM-data area for Downloads.

      => ESC-key press aborts the function.

   <RecvXmo1K> FILENAME

      Call  internal  xmodem1k.   Files  are placed into the directory
      pointed to in the PRM-data area for Downloads.

      => ESC-key press aborts the function.



   - Xmodem/Ymodem Receive units are capable of adopting to frame size.
     128  /  1024  data frames are determined by the sender and can be
     sent in any combination.

   -  The  Internal  Zmodem  in  ACECOMM  is  capable of up to 8k data
     frames.  For compatibility, ACECOMM only uses larger than 1k data
     frames with it's sending unit in mailer modes.  ACECOMM'S  zmodem
     receive unit can handle up to 8k data frames at any time.













MACRO.DOC       Page 11



Chapter 1  ACECOMM  MACRO Programming Language

           Modem Functions




   <DialRecord> n

      - Retrieves the n record found in current .FON file
        Re dials number until CONNECT or USER ABORT

       <SetFonFile> 1_114.FON <DIALRECORD> 1


   <DialNum> PHONE_NUMBER

      - Builds a  dial  string.   Uses  PRM-data  MDM_DIAL_PREFIX  and
        PHONE_NUMBER Sends the dial string to the modem.  One time.
        No re dials


   <MdmHangUp>

      -  Sends PRM-data MDM_HANGUP string to modem.  Waits 1/2 second,
        then drops DTR for 1 second.


   <SetDTR> ON/OFF

      - SET or RESET UART BIT

        <SetDtr> OFF





















MACRO.DOC       Page 12



Chapter 1  ACECOMM  MACRO Programming Language

           FON Record / Dialing




   <InitFonRec> RECORD NAME
      -  This MACRO must be called first.  The MACRO initializes a FON
      RECORD with ACECOMM defaults.  RECORD NAME is  copied  into  the
      system name for this record.

      <InitFonRec> Compuserve


   <FonRecNum> PHONE_NUMBER

      -  Set  the  phone number field.  Any dial statements in ACE.CFG
      will be applied to this number  when  ACECOMM  builds  the  dial
      string.

      <FonRecNum>468-0285


   <FonRecBaud>BAUD
      -  If  using  a locked port, ACECOMM will ignore this value when
      getting ready to dial.

      <FonRecBaud>19200


   <FonRecLineCtrl> DATA_PARITY_STOPBIT
       - Valid parameters are as follows
         8n1
         7e1
         7n1

      <FonRecLineCtrl>8n1


   <FonRecTerm> VIDEO_TYPE
      - Valid parameters are as follows

        TTY
        Ansi
        Avatar
        Av/An
        VT102






MACRO.DOC       Page 13



Chapter 1  ACECOMM  MACRO Programming Language

           FON Record / Dialing (continued)



   <RedialFonRec>
      - Presents the FON record to the ACECOMM re dial function.














































MACRO.DOC       Page 14



Chapter 1  ACECOMM  MACRO Programming Language

           Misc Functions




   <EndAcecomm>

      - ACECOMM session end.

      Exit   ACECOMM  back  to  the  operating  system.   End  ACECOMM
      session.  A QWIK snap, no  prompt  "Are  you  sure?".   If  your
      online, your still online when you come back unless "drop DTR on
      exit is SET"

      See Drop DTR on EXIT flag inside Terminal Area Options


   <ClearWindow>

      - Clear screen. Clears screen above status line


   <SendDelay> SECONDS

      - Create wait delay before sending the next <SendStr> string


   <Delay> SECONDS

      - Create program function delay.

   <ENDS>

      - Mark the end of a script.


















MACRO.DOC       Page 15



Chapter 1  ACECOMM  MACRO Programming Language

           Expandable MACRO Parameters




   [FON_REC_PWD]

      - Replaced with the current FON RECORD'S PASSWORD string


   [FON_REC_CAP]

      - Replaced with the current FON RECORD'S CAPTURE FILENAME string


   [FON_REC_SCR]

      - Replaced with the current FON RECORD'S SCRIPT FILENAME string


































MACRO.DOC       Page 16



Chapter 1  ACECOMM  MACRO Programming Language

           Expandable MACRO Functions




   %F
      - <FileLister_LUI>
      -  Use  from  File  Lister  Area,  %F is replaced with currently
      "highlighted" filename.

   %P
      - Global
      -  Prompt  for  filename, %P is replaced with what you type into
        the prompt box.

   %WK
      - Global
      - Wait for Key press, stops  MACRO  execution  and  waits  for  a
        key press.