FAX480 480 LINE FACSIMILE PROGRAM

                   Dr. Ralph E. Taggart WB8DQT
                        602 S. Jefferson
                        Mason, MI  48854


                        COPYRIGHT NOTICE

     The  FAX480 program is copyrighted by Dr. Ralph E.  Taggart. 
You are free to make copies of this software for your own use and 
to distribute copies to others, provided that no charge is levied 
for such distribution. ALL OTHER RIGHTS ARE RESERVED. You may not 
incorporate  any  elements of this program  into  other  programs 
offered  for  commercial sale without written permission  of  the 
author. 


                          INTRODUCTION

     Since  the  publication of the original article on  the  480 
line  fax standard in the February 1993 issue of QST, there  have 
been additional enhancements to the release version of the FAX480 
program that are worth noting:

     (1)  The three image conversion utilities (BINFAX,  FAXSSTV, 
and BINSSTV) have now been incorporated into the FAX480  program, 
providing more convenient use from within the FAX480 environment.

     (2)  Two new 480 line display routines  (one  crystal-locked 
and one line-triggered) have been added to permit display of  fax 
transmissions where you might have missed the start tone.

     (3) The synchronous AVT 94 video mode has been added to  the 
SSTV receive options.

     (4)  A synchronous 36 second SSTV receive routine  has  been 
added  for the display of pictures transmitted by  other  FAX480-
equipped  stations.  This  mode, which  depends  on  the  extreme 
accuracy  of the transmission rate from a FAX480-driven  ViewPort 
interface,  provides  the  same noise  immunity  enjoyed  by  the 
crystal-locked  480 line display mode while operating in the  240 
line SSTV module.

                        DISTRIBUTION FILE

     The  FAX480.ZIP  distribution file contains a total  of  six 
archived files:

                           FAX480.DOC

                           FAX480.EXE

                             HOUSE.A

                             HOUSE.B

                             JEN.STV

                            K4OVV.STV


     The  FAX480.DOC  file  is this  documentation  file  on  the 
operation of the FAX480 program.

     The  FAX480.EXE  file is the complete software  package  for 
operation  with  the 480 line fax mode, using  the  modified  A&A 
ViewPort VGA SSTV interface.

     The HOUSE.A and HOUSE.B files represent a sample 480 line fax 
image while JEN.STV and K4OVV.STV are sample SSTV image files.


                      HARDWARE REQUIREMENTS

     The  following hardware requirements must be  satisfied  for 
proper operation of the FAX480 program:

     (1)  An  IBM PC/AT/PS1/PS2 or compatible with a  10  MHz  or 
          faster clock speed and a minimum of 512K of RAM.

     (2)  A VGA display adapter that is bios-compatible  with 
	  the  IBM VGA standard. Virtually all VGA adapters  meet 
	  this requirement.

     (3) A monochrome or color analog VGA monitor. 

     (4)  A minimum of two 360K floppy disk drives, or  a  single 
          1.2  meg 5.25  or 1.4 meg 3.5 inch floppy drive,  or  a 
          hard  drive. The choice of drive options has no  effect 
          on  the  operation of the program but does  impact  the 
          number of fax or SSTV images that can be stored as well 
          as  the speed with which images can be saved or  loaded 
          from  disk. All things being equal, you will enjoy  the 
          program more if you have a hard-drive (a statement true 
          for  most software), but, if you lack one, there  won't 
          be any limitations on what you can do.

     (5) An optional Hewlett-Packard DeskJet or LaserJet  printer 
          for  generating hard-copy printouts of fax images.  The 
          Laser printer must have sufficient memory to handle 300 
          dpi graphics. 

     (6) An A&A Engineering ViewPort VGA SSTV interface, modified 
          by  the addition of a 4 MHz clock circuit as  described 
          in the February, 1993 issue of QST.

     (7) An available parallel printer port.


                          INSTALLATION

Hardware

     Installation  is a simple matter of connecting the  parallel 
port cable between the interface and your computer and making the 
needed  audio  connections.  A shielded  audio  cable  should  be 
connected between the receiver audio output and the SSTV IN  jack 
on  the rear of the interface. A microphone is connected  to  the 
MICROPHONE IN connector on the front panel while a cable connects 
between  the MICROPHONE OUT connector on the rear apron and  your 
transceiver's  microphone  input connector.  The  two  microphone 
connectors on the interface have the the following pin-outs:

               Pin       Function

                1        Microphone audio

                2        PTT "hot"

                3        PTT return/ground

                4        Microphone ground

A  connector  compatible with your transceiver  input  should  be 
installed  at  the  transceiver  end of  the  cable  between  the 
interface  and  the  rig.  Consult  the  documentation  for  your 
transceiver  for  the  equivalent  pins  on  your   transceiver's 
microphone  connector. You can test the connections by  operating 
your rig with the interface either on or off. In either case, the 
rig  should  key  with normal microphone  audio.  The  microphone 
patches  through the interface at all times unless the  interface 
is actually transmitting an image.

     The cable used to connect the parallel port of the  computer 
with the DB-25 connector on the rear apron of the interface is  a 
double-male  and  is  usually sold as a  "parallel  cable".  Such 
cables  will  have all connector  pins  wired.  Similar-appearing 
cable, usually marked "serial cable", will not be fully-wired and 
will NOT function with the interface. 

Software

     If you have a hard drive, the best results will be  obtained 
by  operating  the software from the hard disk.  From  your  root 
directory, create a FAX480 subdirectory by typing:

                       md\fax480  <ENTER>

Switch to the new directory:

                       cd\fax480  <ENTER>

Now  copy  ALL  the distribution files into  this  directory.  In 
operation, you would enter the FAX480 subdirectory to execute the 
program  and  all  image  files  would  be  stored  in  the  same 
subdirectory.  Image file capacity is limited only  by  available 
hard-disk storage.

     The  FAX480  program  can be operated from  a  floppy  drive 
without any penalty other than the number of file images that can 
be stored on a single floppy disk. Copy the programs noted  above 
on to a formatted disk for the drive in question. Operating  from 
a  floppy drive would normally involve booting the software  from 
your  program disk, after which you can remove the  program  disk 
and insert formatted disks for image file storage. Each fax image 
file  requires  128K of available disk storage while  SSTV  image 
files use 64K, so you will have the following image capacity  for 
various floppy drive configurations:

          Drive     Fax Images     SSTV Images

          360K           2             5

          720K           5            11

         1.2 meg         9            18

         1.44 meg       11            22  

These figures assume that no other files are stored on the  disks 
in question.


                            OPERATION

Booting the Program

     The SSTV portion of the FAX480 program inserts a small block 
in the upper left of all transmitted images that contains  either 
<FAX480> or your call (six characters maximum), depending on  how 
you   boot  the  software.  Assuming  you  are  in   the   FAX480 
subdirectory, or you are operating from the floppy drive with the 
program  disk installed, to enable the call-sign  option,  simply 
type:

                     fax480 urcall  <ENTER>

The call letters will appear in upper-case letters,  irrespective 
of  whether you type then in in upper-case or lower-case. If  you 
don't  care  about using your call-letters, boot the  program  by 
typing:

                         fax480 <ENTER>

To make booting the software even move convenient in the  future, 
you might consider using your word processor (in the non-document 
or  ASCI  mode)  to create a batch file (FAX.BAT)  in  your  root 
directory. This file would have the following format:

                          cd\fax480
                          fax480 urcall
                          cd\

with the batch file installed, simply typing:

                           fax <ENTER>

from the root director will move you automatically to the  FAX480 
subdirectoruy and boot the software with your call. When you exit 
the program, you will be back in the root directory.

     As the program boots, a "CHECKING PARALLEL PORTS..." message 
will be posted as the computer checks the three possible parallel 
port  addresses  looking for the interface.  The  interface  unit 
should be connected and turned on PRIOR to booting the  software. 
If the program doesn't find the interface unit, an error  message 
will be posted, outlining the possible problems. You can continue 
at  this point (type <C>) or exit the program (type <Q>). If  you 
continue,  all image file functions will be available to you  but 
the  program will not let you use the receive modes  or  transmit 
modes, since,  lacking a connection to the interface, the program  
would "hang up" and require a keyboard or hard reset to get  back 
on  line. If the problem was a lack of power to the interface  or 
failure  to  connect or switch the parallel  port  cable,  simply 
hit  the <T> key to repeat the port test. If you don't intend  to 
use the interface for a particular operating session, hit <C>  to 
continue.  Almost all program functions will be available to  you 
in  such a case, except that the system will not let you  display 
or transmit images. Typing <Q> will cause you to exit the program 
if your problem requires more in the way of thought or action.

                            MAIN MENU

     This  menu  is  the crossroads of  the  FAX480  program  and 
provides access to all three of the primary program modules:

     <1> This will cause you to jump to the 480 line fax module

     <2> will route you to the SSTV module

     <3> will  take  you  to  the  package  of  file  conversion 
         utilities

     <Q> will  permit you to exit the FAX480 program,  at  which 
         point you will be returned to your operating system.


This  menu  illustrates  a  characteristic  of  all  the  primary 
functions of the FAX480 program. With the exception of file names 
that  must be entered to load, save, or convert images, all  menu 
commands  are  initiated by hitting a single  alpha-numeric  key. 
There  is  no need to use the <ENTER> key -  one  keystroke  will 
accomplish  each designated menu option. Alphabetical  characters 
may  be  entered in either upper or lower case, so  the  keyboard 
shift status is irrelevant. 

     Each of the three functional units will be described in  the 
sections which follow.

                      480 LINE FAX OPTIONS

     Fax  functions  are  organized into two  columns  -  RECEIVE 
FUNCTIONS  and  OTHER  FUNCTIONS.  The  former  deals  will   the 
different  options  for receiving and displaying a 480  line  fax 
image  while  the latter includes a variety of  other  functions. 
Note  that  the display also includes a real-time  clock  display 
that updates every minute. This is included as an aid in  logging 
contacts. The display will be in local or UTC time, depending  on 
how  you have set your computer with the TIME function from  DOS. 
For maximum utility, you should periodically reset the time  from 
an accurate source.

RECEIVE FUNCTIONS

     <1> Live Autostart

     This is the preferred receiving mode since image loading  is 
initiated  by the start tone and controlled by the crystal  clock 
circuit,  providing the maximum in noise immunity. This  mode  is 
used to display transmissions from other stations where the image 
is  transmitted directly from the other computer  ("live").  When 
you  key  <1>  the image display screen will appear  and  the  ** 
ACTIVE ** message will be posted to let you know that the  system 
is attempting to load an image. You must enter this mode prior to 
the start of a transmission from the other station or just as the 
start  tone  is heard, as the system must receive a  valid  start 
tone to begin image display. 

     If  you entered the mode by accident, you missed  the  start 
tone,  or  there  was a problem with  the  transmitting  station, 
simply hit the <Q> key to exit. The ** ACTIVE ** message will  be 
replaced  by  ** COMMAND **, at which point you can  key  <Q>  to 
return to the Main Menu. See <3> and <4> below for how to display 
an image when you have missed the image start tone.

     Assuming image transmission proceeds normally, the  received 
picture will be displayed, line by line, in the 512 x 480 display 
window.  Reception can be aborted at any time by hitting the  <Q> 
key, at which point the ** ACTIVE ** message will be replaced  by 
** COMMAND ** and you can use <Q> to exit back to the Main Menu.

     Assuming  the transmission proceeds to completion, when  the 
display  window  is  filled with image data,  the  **  ACTIVE  ** 
message  will  be replaced by ** COMMAND **. At this  point,  the 
received  image  will be retained and you have four  options,  as 
indicated by the menu on the left side of the screen:

               <S>ave Image

               <T>ransmit

               <P>rint Image

               <Q>uit

See the FAX POST-DISPLAY options for the use of these functions.

     <2> Recorded Autostart

     This  option functions like <1>, except that it is used  for 
transmissions that have been recorded on audio tape. This  option 
does  not  have the noise-immunity of the  clocked  display  mode 
(noise  or  interference can disrupt  line-triggering)  but  does 
provide a useful tape-recording option.

     All display and post-display functions are similar to  those 
described above.

     <3> Live Manual

     This  option  provides crystal-locked display  if  you  have 
missed  the  image  start  tone. In all  other  respects,  it  is 
identical to the preferred Live Autostart option.

     <4> Recorded Manual

     This  option  provides for recorded display when  the  image 
start  tone has been missed. In other respects, this  routine  is 
identical to the Recorded Autostart option.

FAX POST-DISPLAY OPTIONS

     Any  of  the  fax display options  (1-4)  will  provide  the 
following options when image display is complete:

               <S>ave Image

               <T>ransmit

               <P>rint Image

               <Q>uit

     <S>ave Image

     Keying <S> will switch you to a screen prompting you for the 
name  to be used for the image save. This name can be  any  valid 
DOS  filename (8 characters max.) and should not incorporate  any 
extensions. If you are using a floppy drive, be sure a disk is in 
the  drive with enough capacity to hold the 128K image.  Normally 
the file will be created in the default drive/directory. You  can 
save to another drive/directory by including the appropriate path 
data  in the file name you provide. NOTE: Files save  to  another 
drive/directory  will NOT appear on the listing when you  attempt 
to load images from the fax menu. If you want access to the image 
you have saved, the file must be transferred at a later time. See 
the IMAGE FILES section before attempting to do so. When the save 
is complete, you will be returned to the Main Menu. The  received 
image will NOT be lost as it is retained in a RAM buffer and  can 
be recalled at any time using the DISPLAY LAST IMAGE  option from 
the Main Menu or by using the LOAD IMAGE FROM DISK option.

     <T>ransmit

     Hitting the <T> key will post the transmit menu display  and 
send  the image in memory. The system will key the interface  and 
begin image transmission. When you use this option for the  first 
time,  you  will  need to adjust the MIKE  GAIN  control  on  the 
interface  for at RF output reading on your transceiver  that  is 
between  1/2 and 2/3 of the PEAK reading normally  observed  with 
voice  transmission.  Keeping the audio level  down  will  reduce 
distortion  and the possibility of over-driving the  transmitter. 
It is also important since fax transmission (like SSTV)  involves 
a  100%  duty-cycle and you do not want to  overheat  your  final 
amplifier  stage(s).  Using  a  dummy  load  to  make  the   gain 
adjustment  is highly recommended. The setting of the  MIKE  GAIN 
control  has  no  effect on normal  microphone  audio,  which  is 
normally  set by a level or gain control on your transceiver.  If 
you  change this control, readjustment of the MIKE  GAIN  control 
will probably be required.

     Transmission  can be aborted at any time by hitting the  <Q> 
key,  at which point the interface will drop out of the  transmit 
mode and you will be returned to the fax menu. When  transmission 
is  completed  (normally  about  2 minutes  and  8  seconds,  the 
interface will drop out of the transmit mode and you will  return 
to the Main Menu.

     <P>rint Image

     Hitting  the  <P>  key lets you print a  hard  copy  of  the 
displayed image provided you have a compatible printer. Refer  to 
the PRINTING IMAGES section prior to using this function for  the 
first time.

OTHER FUNCTIONS

     <R>ecall Last Image

     If you have previously received an image or loaded one  from 
disk,  that image will be scrolled into the active window of  the 
display screen. When scrolling is complete (** ACTIVE ** switches 
to ** COMMAND **), you have the same options available to you  as 
described under the receive modes.

     If  you  have  not loaded or received  an  image  since  the 
program  was booted, a black screen will be displayed.  IMPORTANT 
NOTE:  Although  unlikely, if you do something  that  causes  the 
program  to abort, you can usually save the image by  immediately 
rebooting  the  program  and calling up the  DISPLAY  LAST  IMAGE 
option.  This is due to the fact that DOS does not  normally  use 
the RAM area allocated for the image buffer. If you  reboot/reset 
the computer, however, the image will be lost since a reset  will 
cause the buffer area to be over-written as part of the  power-on 
system test (POST). While such image recovery is valid for system 
operating  under DOS, I cannot tell you what the results will  be 
using  WINDOWS  or any other GUI operating system. You  can  test 
this option by exiting the program and then rebooting the  FAX480 
program. If the image was corrupted, you may want to operate  the 
program from the DOS environment.


     <L>oad Image From Disk

     When  you key <L> to invoke this function, the names of  all 
FAX480  image  files  on  the  default  directory/drive  will  be 
displayed.  Each  of these will have an ".A" extension  (see  the 
section  on FAX IMAGE FILES). Enter the name of the file to  load 
(less  the .A extension) and the image file will be  loaded,  the 
system  will  switch to the image display screen, and  the  image 
will be transferred to the screen. Any of the secondary functions 
(<S>ave,  <T>ransmit, <P>rint, or <Q>uit can be used if  desired. 
Note  that you can save the image to the default  directory/drive 
under  a  different  file  name  or  you  can  save  to   another 
directory/drive  with  the save or a different  file  name.  This 
provides a convenient way to copy interesting images to a  floppy 
for  backup  purposes or to another disk to  provide  to  another 
fax/SSTV operator.

     <G>rayscale Display

     Keying  <G>  will  fill the entire  screen  with  a  16-step 
grayscale display that is ideal for adjusting the brightness  and 
contrast  of the VGA display or for setting camera exposures  for 
taking  photographs (see PHOTOGRAPHING THE DISPLAY). Hitting  any 
key will return you to the Main Menu.

     <A>dd Label to Image

     This  option  lets  you  add  a  single  line  of  text  (60 
characters  max.)  to  the  bottom of  the  image.  Any  text  or 
numerical  character is acceptable but some punctuation  (period, 
for example) or characters (" quotation marks) are not. You  will 
get  a  RE-DO FROM START message if your text entry  contains  an 
illegal  character.  Also,  although the  480  line  format  will 
resolve lower-case characters, you may want to use upper-case  to 
retain maximum readability under less-than-optimum conditions. If 
you  enter Q instead of a text line, the routine will return  you 
to the Main Menu.

     Assuming you have entered a text line, the routine will jump 
to the image display screen and show you the image with the label 
overlaid  on the bottom. Note that the text, no matter  how  long 
the  line, is centered with respect to the image. This  label  is 
now in the video RAM buffer so will go out with the image if  you 
transmit  it. Also, if you Save the image at this point, it  will 
be saved along with the image. As a general rule, you may want to 
Save  received images before experimenting with labels so an  un-
labeled version can be recovered if desired. If the image is save 
using  the original file name, the labeled version  will  replace 
the unlabeled one. 

     If  you don't like your label, it can be replaced by  keying 
<Q> to exit the display screen, followed by an <A> from the  Main 
Menu  to do another label. Any new label will completely  overlay 
any  previous  one.  Labels on previously  saved  images  can  be 
replaced  or edited using this feature. If you want to  eliminate 
any  label, reload the image in question, provided it  was  saved 
without a label.. 

     The  label  feature can perform several functions.  You  may 
wish   to  label  an  image  just  prior  to  transmission   with 
information specific to that contact:

            WB8DQT TO W1AW  20M  1830Z  20 JULY 1992

You  may also wish to label received images in a similar  manner, 
thus permitting your image files to serve as an image log. Labels 
can  also be used as captions to "explain" images that are  less-
than-obvious in terms of the subject.

     <S>STV Options

Keying  this  option  will  route you to  the  SSTV  menu  to  be 
described in a later section.

     <C>alibration Tone

     This routine causes your interface to transmit one of  three 
possible calibration tones (1200 Hz Sync, 1500 Hz Black, or  2300 
Hz  White) to assist the other station in precision  tuning  your 
signal. You select the tone, depending on the needs of the  other 
station.  For communicating with other FAX480 stations,  use  the 
1500  Hz  (Black)  option.  The calibration  tone  will  be  sent 
continuously until you press the <Q> key. Generally, 5-10 seconds 
will  be  adequate  to allow the other  station  to  make  tuning 
adjustments.

     <T>une Display

     Proper  grayscale  rendition  in both  fax  and  SSTV  modes 
requires  accurate  tuning/carrier insertion  at  your  receiver. 
Usually you can achieve sufficient accuracy by tuning for natural 
voice  quality,  but  this can be ambiguous at  times.  The  tune 
display  provides  a  graphic  aid  for  precision  tuning.   Two 
vertical, parallel lines define the range from 1200 Hz (Sync)  at 
the  top of the display to 2300 Hz (White) at the bottom. If  you 
are uncertain about the accuracy of your tuning, request that the 
transmitting station transmit a 1500 Hz (Black) calibration  tone 
prior  to sending an image. Key <T> for the tone display and  you 
will  note  a  horizontal line between the  two  vertical  lines. 
Carefully adjust the receiver tuning (use the RIT control in  the 
case of a transceiver) until the horizontal line is lined up with 
the two arrows. These arrows are positioned at the 1500 Hz  point 
on the frequency display. When the line is properly aligned  with 
the arrows, your are precisely tuned for image reception.

     To use the tune display for SSTV, you have several  options. 
If  the other station can transmit a short calibration tone  (all 
stations  using  the  FAX480 software can do  so),  ask  them  to 
transmit a black (1500 Hz) tone and tune as noted above for  fax. 
Stations  can also be tuned while transmitting SSTV. If  you  can 
note  the bar at the top of the display that corresponds to  sync 
(1200 Hz), tune to the point where this is positioned JUST at the 
top. Multiple bars should also be noted in the range between  the 
arrows  (black) and the bottom of the display (white). The  black 
threshold can usually be noted because of the clustering of bars. 
If you can see the black threshold, carefully adjust tuning to it 
aligns with the two arrows. The rapidly shifting frequency of  an 
SSTV signal results in the bars, corresponding to the  individual 
frequencies, being fairly faint. They may not be readily  visible 
on  a  laptop computer with an LCD screen because of  the  slower 
response  time  of  such  a  display.  LCD  displays  will   work 
well with the single-tone tuning aid.

     No  matter what your tuning mode, hitting the <Q>  key  will 
return you to the fax menu.

     <Q>uit 480 Line Fax

     This  keystroke  will cause you to exit the fax  module  and 
return to the Main Menu.


                         FAX IMAGE FILES

     Although  I  have referred to image files in  the  singular, 
each  image is actually contained in two 64K binary  files.  This 
strategy  allows for fast loads and save of the image  data.  The 
file name is made up of the name you selected plus the  extension 
A for the upper half of the image and B for the lower half of the 
image:

                           filename.A

                           filename.B

Within the FAX480 program this two file structure is  transparent 
to  the  user but it must be considered if you wish  to  copy  or 
delete  files  from the DOS environment. The wildcard  option  is 
useful in both cases. Use

                    delete filename.* <ENTER>

to remove a specific image file or

                     copy filename.* <ENTER>

to copy an image file.


                       PRINTING FAX IMAGES

     The  <P>rint Image option from the display menu allows  very 
high-quality printing from displayed images. The routine supports 
LaserJet  compatible printers, including the H-P  DeskJet.  Laser 
printers must be equipped with sufficient memory to handle a full 
page  of  300 dpi graphics (typically 1  megabyte).  The  DeskJet 
requires no ancillary memory for printing. 

     The  printer  must  be connected to  the  computer  using  a 
parallel  printer cable. This presents a practical problem  since 
the  ViewPort  VGA interface is also connected  to  the  parallel 
port.  An  A/B  switchbox can be  used  to  facilitate  switching 
between the interface and the printer. The switch MUST be set  to 
the  interface  when the FAX480 program is booted  and  when  you 
desire  to receive or transmit a picture. When you want to  print 
an  image, you must switch to the printer prior to  invoking  the 
print routine.

     Hitting the <P> key will initiate the printing process.  The 
screen  will  clear  to  white and  the  display  image  will  be 
repositioned to the center of the screen. Printing a picture will 
require  several  minutes with a typical printer while  the  time 
required with the DeskJet will be significantly longer. In either 
case,  the result is a printout of very high quality compared  to 
other printing routines. 

     If  you  operational  computer  is not  linked  to  a  laser 
printer,  you can copy the FAX480 program and any  desired  image 
files  to  floppy  disks  and print out  pictures  on  any  other 
computer  that  does have the proper printer. You  will  get  the 
error  message  when you boot the software because you  will  not 
have  the  A&A  interface connected but  that  will  not  inhibit 
loading images from disk and printing them.


                         SSTV OPERATION

     The  basic  fax functions have so much in common  with  SSTV 
that  it made a lot of sense to add an SSTV option to  the  basic 
FAX480  program.  The  program  will  receive  and  display   the 
following formats using a high-quality 64-step grayscale:


                        8/8.5 second B&W

                          36 second B&W

                      12 second Robot color

                      36 second Robot color

                      76 second Robot color

                         Scottie 1 color

                         Scottie 2 color

                          AVT 94 color

In addition, the system will transmit image in either the 8 or 36 
second  B&W  format. Since the ViewPort VGA system comes  with  a 
color SSTV operating program, you might well ask why bother  with 
a  piece  of software that only displays monochrome  images?  For 
someone  who wants to get on every once and a while  and  operate 
SSTV, there are a couple of very good reasons why you may wish to 
use this part of the program:

     IMAGE  QUALITY - if your VGA monitor will only  display  256 
color values, the quality of the color image display is marginal. 
If  the received signal is slightly-mistuned, you will  also  get 
undesirable  color tints on your images. That same monitor (or  a 
monochrome VGA monitor or a VGA laptop) will do an excellent  job 
of displaying grayscale images. Mistuning will only cause  subtle 
shifts in the grayscale display - not a color tint!

     CONVENIENCE  - there is no configuration file to  play  with 
since everything is clocked and all operations are independent of 
your CPU and its clock speed. This program is also much easier to 
use since almost everything works from a single menu.

     IMAGE  STORAGE  - all images stored with  the  ViewPort  VGA 
program require 123K of disk space. Monochrome images are  stored 
in  color format and will be over-laid by color when called  back 
up  from disk. This program stores all images in 64K  disk  files 
and  save  and  load  almost instantly with  no  color  tint.  In 
addition,   information   on  the  original   image   format   is 
automatically stored in the image disk file.

     ESCAPE - With the ViewPort VGA software, you can get trapped 
in  a  receive  routine if the system doesn't get  a  valid  sync 
pulse.  This  program features single key exit from  any  routine 
without the need to re-boot the computer.

The  program  is simple to use and  the  high-quality  monochrome 
image  display  will  typically generate a  nicer  image  with  a 
standard  VGA display system then will the color option. You  may 
well  find  the  program to be your  preferred  operating  system 
unless  you  become a "hard-core" SSTV operator. Of  course,  the 
ViewPort  VGA software can be used at any time for color  display 
and  transmission  and the fax clock modification  will  have  no 
effect  on  the  operation of the  interface  with  the  ViewPort 
software.

                            SSTV MENU

     The  SSTV  Menu is organized like the fax  menu,  supporting 
both receive and other functions.

RECEIVE FUNCTIONS

     The Main Menu provides seven receive display modes. They all 
share a number of operational features in common. When a mode  is 
selected,   the   screen  will  format  for  SSTV   display,   an 
abbreviation  of  the operating mode will appear along  the  left 
edge,  as  will  a small white square in the lower  left  of  the 
display.  This  square  indicates that the  program  is  actively 
processing an image. If display completes in the normal  fashion, 
the  square  will  disappear.  In  a  direct  sense,  the  square 
functions  to perform the same function as the  <**ACTIVE**>  and 
<**COMMAND**>  indicators for fax. If you need to  abort  display 
for  any  reason, simply key <Q> and the  square  indicator  will 
disappear, leaving you in the equivalent of the fax COMMAND mode. 
See the section on Post-Display Options for what you can do  with 
the displayed image. 

     Reliable   SSTV  display  requires  that  the   station   be 
accurately  tuned. Results will depend on noise and  interference 
levels.  Mis-tuning will result in varying degrees of  line  mis-
triggering,  as will noise or QRM (depending on the  strength  of 
the SSTV signal. Absent interference, the noise generated by your 
computer system (on HF) will set the noise floor. My Zenith  lap-
top, for example, requires an S4-S5 signal to overcome the effect 
of  computer  generated  RF (see the section  on  COMPUTER  NOISE 
SUPPRESSION).

     <1> 8/8.5 Second B&W

     This is the standard low-resolution SSTV image format. While 
the  images  are limited in detail, they are  acceptable  if  the 
subject is chosen with care and have the advantage that they  can 
be  transmitted  very  quickly. They  are  also  compatible  with 
virtually  every SSTV system ever built, including  early  analog 
equipment.  This receive mode will also display Robot  12  second 
color images.

     <2> 36 Second B&W <S>

     This  is the high-resolution (240 line)  monochrome  display 
mode. This format provides a combination of the highest available 
SSTV resolution in the shortest possible transmission time.

     Note  the  <S>  following this mode. If  you  are  ready  to 
receive  another FAX480-equipped station, key <S> when the  image 
starts instead of <2>. This will lock the display to the  crystal 
clock  and  completely  avoid  the  possibility  of  false   line 
triggering.  You  can  only use this  option  with  other  FAX480 
stations  since  other SSTV stations  employ  slightly  different 
clocking schemes. With most other SSTV systems, the clock is far 
enough off to result in a "tilt" to the picture that can range 
from mild to severe. Under difficult band conditions, you can use 
the synchronous option is the slant is not too bad. Some individual
SSTV units will be almost on the right frequency and the results will 
be quite satisfactory. With other FAX480 systems, the images will be 
perfectly synchronized if the clock has been adjusted with reasonable
care. 

     <3> 36 Second Robot Color

     This is a popular format because it allows the  transmission 
of  240 line images in a short period of time. Image  quality  is 
distinctly lower, however, that with either the 36 second B&W  or 
72 second Robot Color format.

     <4> 72 Second Robot Color

     This  is  the  highest quality display in  the  Robot  Color 
system and the resulting image will be equivalent to the 36  line 
B&W  format. Having the other station send a 36 second B&W  image 
will  save time, but most operators will wish to  transmit  color 
for the benefit of others on the frequency.

     <5> Scottie 1

     This  is a popular color display mode that requires about  2 
minutes  for  the display of a 240 line  image,  with  resolution 
equivalent to the 36 second B&W and Robot 72 second color modes.

     <6> Scottie 2

     This mode provides results comparable to or slightly  better 
than the 36 second Robot Color mode. The main advantage, compared 
with  Scottie  1. is the shorter transmission time.  In  general, 
Scottie 1 will provide the better quality.

     <7> Amiga AVT 94

     This  is  a synchronous system that is  difficult  for  most 
non-Amiga  systems to handle because the format does  not  employ 
sync  pulses and clocking requirements are quite  stringent.  The 
FAX480  hardware clock is sufficiently accurate, when tuned  with 
care, and the software compensates for the different clock rates, 
yielding essentially perfect synchronization. If you want optimum 
image  noise immunity when working stations equipped with  Amiga, 
Pasokon, or up-graded Robot systems, this is the mode of  choice. 
When  working  other  stations using  the  FAX480  software,  the 
synchronous  36 second B&W option will provide  equivalent  image 
quality in about 1/3 the transmission time.

      Reception of AVT94 images requires that the transmitting 
station be tuned VERY accurately if the software is to lock
properly to the image header. Tuning errors of only 100 Hz will
result in image display being aborted. If the system has locked
on to the header properly, you will see the display start at the
top of the screen. You should key up the mode just as the VIS 
data ends and the 5 second header begins for best results. If the
system fails to lock on to the header data, the square block in 
the lower left of the screen will go out without the image being
displayed. There is no way to display the image if the receiver 
was mis-tuned during the header interval and the <Q> key should 
be used to return you to the SSTV Menu.

OTHER FUNCTIONS

     <R>ecall Last Image

     Whenever you use the <Q> key to exit the display screen (see 
POST DISPLAY OPTIONS), the image is not lost but is saved to disk 
as a 64K file (TEMP.STV). This image can be retrieved at any time 
using  the <R> key. The complete range of functions described  in 
the section on POST DISPLAY OPTIONS are then available.

     <L>oad Image from Disk

     When  you key <L> to invoke this function, the names of  all 
SSTV   image  files  on  the  default  directory/drive  will   be 
displayed.  Each of these will have an ".STV" extension (see  the 
section on IMAGE FILES). Enter the name of the file to load (less 
the extension) and the image file will be loaded, the system will 
switch  to  the  image  display screen, and  the  image  will  be 
transferred to the screen. See the POST DISPLAY OPTIONS for  what 
you can do at this point.

     <G>rayscale Display

     Keying  <G>  will  fill the entire  screen  with  a  16-step 
grayscale display that is ideal for adjusting the brightness  and 
contrast  of the VGA display or for setting camera exposures  for 
taking  photographs (see PHOTOGRAPHING THE DISPLAY). Hitting  any 
key will return you to the Main Menu.

     <P>rint Files

     Printing files takes a fair amount of time, using the  high-
resolution  image printing routine and it makes little  sense  to 
devote  an  entire page to SSTV images. This routine is  a  batch 
printing  routine  that will place up to four SSTV  images  on  a 
sheet  of paper. When you activate this option with the <P>  key, 
you will get a display of the available SSTV image files and  you 
will  be  requested  to supply four file names  in  sequence  (no 
extensions).  Any image can be skipped by hitting <ENTER> at  the 
request.  In  effect,  you can print from  one  to  four  images. 
Printing  four  at a time is  a better investment,  in  terms  of 
printing time, but the choice is yours. If the format of the four 
images is important to you, image 1 is in the upper left, image 2 
is in the upper right, image 3 is in the lower left, and image  4 
is in the lower right of the printed page.

     Once file names have been selected, the four images will  be 
formatted on the screen. This will take several minutes, followed 
by  the  actual  printing routine. You will  find  the  resulting 
prints  quite satisfactory, compared with other SSTV image  print 
routines.

     <C>alibration Tone

     This routine causes your interface to transmit one of  three 
possible calibration tones (1200 Hz Sync, 1500 Hz Black, or  2300 
Hz  White) to assist the other station in precision  tuning  your 
signal. You select the tone, depending on the needs of the  other 
station.  For communicating with other FAX480 stations,  use  the 
1500  Hz  (Black)  option.  The calibration  tone  will  be  sent 
continuously until you press the <Q> key. Generally, 5-10 seconds 
will  be  adequate  to allow the other  station  to  make  tuning 
adjustments.

     <T>une Display

     Proper  grayscale  rendition  in both  fax  and  SSTV  modes 
requires  accurate  tuning/carrier insertion  at  your  receiver. 
Usually you can achieve sufficient accuracy by tuning for natural 
voice  quality,  but  this can be ambiguous at  times.  The  tune 
display  provides  a  graphic  aid  for  precision  tuning.   Two 
vertical, parallel lines define the range from 1200 Hz (Sync)  at 
the  top of the display to 2300 Hz (White) at the bottom. If  you 
are uncertain about the accuracy of your tuning, request that the 
transmitting station transmit a 1500 Hz (Black) calibration  tone 
prior  to sending an image. Key <T> for the tone display and  you 
will  note  a  horizontal line between the  two  vertical  lines. 
Carefully adjust the receiver tuning (use the RIT control in  the 
case of a transceiver) until the horizontal line is lined up with 
the two arrows. These arrows are positioned at the 1500 Hz  point 
on the frequency display. When the line is properly aligned  with 
the arrows, your are precisely tuned for image reception.

     To use the tune display for SSTV, you have several  options. 
If  the other station can transmit a short calibration tone  (all 
stations  using  the  FAX480 software can do  so),  ask  them  to 
transmit a black (1500 Hz) tone and tune as noted above for  fax. 
Stations  can also be tuned while transmitting SSTV. If  you  can 
note  the bar at the top of the display that corresponds to  sync 
(1200 Hz), tune to the point where this is positioned JUST at the 
top. Multiple bars should also be noted in the range between  the 
arrows  (black) and the bottom of the display (white). The  black 
threshold can usually be noted because of the clustering of bars. 
If you can see the black threshold, carefully adjust tuning to it 
aligns with the two arrows. The rapidly shifting frequency of  an 
SSTV signal results in the bars, corresponding to the  individual 
frequencies, being fairly faint. They may not be readily  visible 
on  a  laptop computer with an LCD screen because of  the  slower 
response  time  of  such  a  display.  LCD  displays  will   work 
well with the single-tone tuning aid.

     No  matter what your tuning mode, hitting the <Q>  key  will 
return you to the fax menu.

     <F>ax Menu

     Keying <F> will return you to the fax menu.

     <Q>uit SSTV 

     Hitting  <Q>  will cause you to exit the  SSTV  program  and 
return to the Main Menu. 


                    SSTV POST-DISPLAY OPTIONS

     When  an image has been received, recalled, or  loaded  from 
disk,  you  will note letters arrayed vertically along  the  left 
side of the display:

                               <S>

                               <T>

                               <Q>

                               <C>
     
                               <R>

The  five  letters  correspond to your options  at  the  point  - 
<S>ave, <T>ransmit, <Q>uit, <C>ontrast expansion, and <R>epair.

     <Q>uit

     Keying  <Q> will return you to the SSTV menu.  The  received 
image will NOT be lost and can be recovered at any time using the 
<R>ecall Last Image option from the SSTV menu.

     <S>ave Image

     Keying <S> will switch you to a screen prompting you for the 
name  to be used for the image save. This name can be  any  valid 
DOS  filename  (characters max.) and should not  incorporate  any 
extensions. If you are using a floppy drive, be sure a disk is in 
the  drive with enough capacity to hold the 64K  image.  Normally 
the file will be created in the default drive/directory. You  can 
save to another drive/directory by including the appropriate path 
data  in the file name you provide. NOTE: Files save  to  another 
drive/directory  will NOT appear on the listing when you  attempt 
to  load  images from the Main Menu. If you want  access  to  the 
image  you  have saved, the file must be transferred at  a  later 
time.  See  the IMAGE FILES section before attempting to  do  so. 
When the save is complete, you will be returned to the Main Menu. 

     <T>ransmit Image

     Hitting  the <T> key will cause the screen to clear and  you 
will be presented with the following transmit options:

                      <1> 8/8.5 Second B&W

                      <2> 36 Second B&W

                      <Q>uit Transmit

     Keying <Q> will cause you to exit the transmit menu and  the 
image will be re-posted. Keying either <1> or <2> will cause  the 
image to be re-posted, the interface will key up, and the current 
image will be transmitted in the selected format.

     When  you use this option for the first time, you will  need 
to adjust the MIKE GAIN control on the interface for at RF output 
reading  on your transceiver that is between 1/2 and 2/3  of  the 
PEAK  reading normally observed with voice transmission.  Keeping 
the  audio level down will reduce distortion and the  possibility 
of  over-driving the transmitter. It is also important since  fax 
transmission  (like SSTV) involves a 100% duty-cycle and  you  do 
not want to overheat your final amplifier stage(s). Using a dummy 
load  to  make  the gain adjustment is  highly  recommended.  The 
setting  of  the  MIKE  GAIN control  has  no  effect  on  normal 
microphone  audio,  which  is normally set by  a  level  or  gain 
control  on  your  transceiver.  If  you  change  this   control, 
readjustment of the MIKE GAIN control will probably be required.

     Transmission  can be aborted at any time by hitting the  <Q> 
key,  at which point the interface will drop out of the  transmit 
mode and you will be returned to the Main Menu. When transmission 
is  completed (in either 8.5 or 36 seconds), the  interface  will 
drop  out  of the transmit mode and you will return to  the  Main 
Menu.

     Both  transmit image formats incorporate the standard  Robot 
VIS codes in the vertical sync pulse. This means that Robot 400C, 
450C,  and 1200C scan converters, Amiga AVT systems, the  Pasokon 
system  for the IBM, and any other display systems which use  the 
VIS codes will be able to automatically switch to the proper mode 
with the receipt of your vertical sync pulse. Those with  display 
systems  that require manual display mode selection need to  know 
what  mode  you will be using, so you should clearly  state  your 
option prior to beginning transmission. Even those whose  systems 
normally  trigger on the VIS-coded may need the mode to  manually 
trigger their system if noise or QRM disrupts the VIS interval.

     <C>ontrast Expansion

     Some  SSTV  images you will encounter will  have  relatively 
poor contrast. This may be because of the nature or the  original 
subject, poor lighting or other factors at the transmitting  end, 
or slight mistuning at your end. Regardless of the cause,  keying 
<C>  from the post-display menu will give you the option to  look 
at  the  pixel  distribution of the image  and  correct  contrast 
deficiencies  if you wish. The option takes a little time,  so  I 
suggest you use it for images you have saved to disk, rather than 
attempting to adjust pictures while you are on the air.

     When  you key <C> the system will BEEP, indicating that  the 
command was recognized. NOTHING else will happen for the next few 
minutes  but  be patient. When analysis is complete,  the  screen 
will clear and you will be presented with a histogram showing the 
distribution  of pixel values from black at the left to white  on 
the  right. The further the lines extend down from the  baseline, 
the more pixels have that particular value. If the vertical lines 
are relatively widely spaced and about 16 in number, the original 
image  was probably transmitted with 16 grayscale steps.  If  you 
key  <Q> at this point, you can exit without changing the  image. 
Otherwise, proceed as follows.

     The  first step is to indicate where you want the new  black 
cutoff  to  be. You will notice a short vertical  line  extending 
above  the  baseline at the far left. Pressing the <+>  key  will 
move  this  mark toward the right (white end  of  the  grayscale) 
while pressing <-> will move it back toward black (assuming it is 
not already at the far left. If there are few pixels at the black 
end of the grayscale, move the marker to the right (using the <+> 
key,  until you get to a point where the number of pixels  begins 
to  increase  -  then press the <B> key to  mark  the  new  black 
threshold.  If there is a good clustering of pixels at  the  left 
side of the display, simply key <B> with the marker positioned at 
the far left.

     Once  you have keyed <B>, the marker will re-appear  at  the 
white  (right) end of the display. Move the mark ( using  <+>/<-> 
to the point where you want the white cutoff be be and key <W> to 
mark the white threshold.

     At this point the display will clear and the original  image 
will  re-appear. As you watch, it will be overwritten  using  the 
new pixel distribution. When complete, you can save the image  or 
quite  in  the normal manner. If the contrast-expanded  image  is 
superior,  save  the image using the original file name.  If  you 
aren't sure, save it with another name and compare the two  using 
the Disk Image Load routine.

     For those of you with some image processing background, this 
routine performs a "pixel slide" to the black threshold, followed 
by a pixel expansion keyed to the new white threshold. 

     <R>epair

     One of the common ways in which an image can be degraded  is 
improper  line triggering. This can be caused by improper  tuning 
or by interference or noise. Commonly, the line or lines will  be 
offset  to  the  right.  The  <R>epair  routine  allows  you   to 
reposition such offset lines, greatly improving the appearance of 
the image. The routine takes a bit of time, but is worthwhile  in 
the  cases  where  you want the best possible  appearance  for  a 
significant image.

     When  you key <R> a short white line will appear at the  top 
and  to  the left of the image. This line marks the  line  to  be 
repaired.  Keying  <D> will move the reference  line  DOWN  while 
keying  <U>  will  move  it UP. When  the  marker  is  positioned 
opposite  an offset line (look CAREFULLY), pressing the  <A>  key 
will  cause the line to be offset to the LEFT by one  pixel.  The 
<A> key can be pressed as often as desired to properly align  the 
offset  image line. The <U> or <D> keys can then be used to  move 
the scribe to other lines, where the process can be repeated.

     When the lines have been repositioned to your  satisfaction, 
hitting <Q> will terminate the repair routine. At this point, you 
will  be  prompted  for whether you want the  repaired  image  to 
replace  the  original image file. Keying <Y>  will  replace  the 
original  image  while keying <N> will retain the  original  disk 
file. At that point you will be returned to the normal SSTV post-
display screen. If you elected NOT to replace the original image, 
it can be save to another file-name using the <S> routine.

                        SSTV IMAGE FILES

     All  images  are  saved  as  64K  binary  files,  permitting 
extremely  fast loads and saves. Each image is also labeled  with 
an  .STV file extension. Image files can be deleted,  copied,  or 
re-named,  just  like any other data file. If you rename  a  file 
under DOS, be sure to add the extension to the name. If you  fail 
to  do  so,  the image will not appear  on  the  image  directory 
listing when you load a file.

                      FILE CONVERSION MENU

     Keying  <3>  from the Main Menu will route you to  the  File 
Conversion  Menu.  Prior  to  discussion  of  the  various   file 
conversion options, some discussion is in order regarding sources 
of  images and steps preparatory to conversion. Lets  Start  with 
the latter.

SCREEN IMAGE CAPTURE

     The  key  to all the conversion options is  the  ability  to 
capture  computer  images from various sources into  a  form  the 
conversion  programs can manipulate. This is accomplished with  a 
family of programs called "screen capture" software. As noted  in 
the  original  article on the fax standard, I prefer  the  VGACAP 
program available on the DRIG BBS (see the February 1993 issue of 
QST  for information on this system). This is a TSR program  that 
sits  in  the background until you have an  image  displayed,  at 
which point you invoke the "capture" by keying <Alt-F4). At  this 
point,  VGACAP takes over and converts the screen image  (without 
altering it) to a binary data file. If the image was in the 640 x 
480  x  16 format (suitable for fax), the result will be  a  307K 
binary  file containing all the data for the screen  image.  This 
file will reside in the current directory and will be names:

                          screenxx.raw

where  xx  is  a number from 01 to 99, depending  upon  how  many 
screen  captures  you have executed since booting  VGACAP.  There 
will also be a matching palette file (screenxx.plt), which we  do 
not  need.  Other  capture programs will  operate  in  a  similar 
manner,  but  I  would suggest the use of  VGACAP  for  the  most 
predictable  results. The file conversion routine has one  option 
for converting these 307K files to 480 line FAX480 files.

     If  the  original image was in the 320 x 200 x (16,  64,  or 
256)  format, the result will be a 64K binary file with the  same 
name convention as the larger 307K files, but with the  extension 
".bld"  instead of ".raw". The file conversion module contains  a 
routine  for  converting  these 64K files to  FAX480  SSTV  image 
files.

IMAGE VIEWERS

     Many  image  options (see below)  will  support  full-screen 
display of images they create, but if this is not the case,  they 
will  support conversion of the images to one of several  popular 
formats  (.GIF,  .PCX, .TIF, .IMG, or .TGA). In such  cases,  you 
need  a  viewing  program that will import the  image  files  and 
provide  the  full-screen  display needed for  capture  as  noted 
above. There are many programs that will do this, but one I  have 
had  good success with is VUIMAGE, a shareware package  available 
on  the DRIG BBS. This is an excellent program  supporting  .GIF, 
.PCX, and .TIF display, a wide range of monitor modes, and a very 
wide range of scaling options. Most of my images, from a  variety 
of  sources,  are displayed using VUIMAGE to execute  the  actual 
screen capture. I set the mode to 640x480x16 for high  resolution 
images  I  intend to capture for fax files,  or  320x200x256  for 
generating  64K  files for direct conversion to SSTV  format.  By 
adjusting the scale, I can get just the screen display I wish  to 
capture,  gaining  considerable control over the  dimensions  and 
coverage of the ultimate image file.


SOURCES OF IMAGES

     Hand  scanners  and  flatbed scanners can also  be  used  to 
generate images and most of these devices come with programs that 
support the 640 by 480 x 16 VGA mode. Programs such as VGACAP can 
be used to capture the screen images as described above. 

     TV  frame  grabbers  can  be  used  if  they  support   high 
resolution  image  capture.  Most inexpensive  boards  will  only 
capture 240-256 video lines. In such cases, it makes little  sense 
to transmit these as fax, since 240 line SSTV formats will  match 
the  resolution  of  the  captured images.  Such  images  can  be 
captures  directly  from  the  application  or  using  a   viewer 
(320x200). Higher quality frame grabbers will capture a 512  line 
image (using both interlaced frames that make up a TV picture). A 
high  quality  black  and white  camera  will  typically  produce 
sharper  images  than  a  comparable  color  camera.  These  high 
resolution  frame grabbers usually support 640 x 480 VGA  display 
so  programs  like VGACAP can capture the  images.

     Other sources, such as paint programs, image libraries,  BBS 
sources,  etc. can all provide images suitable for conversion  to 
either  fax  (if the original has a  high-enough  resolution)  or 
SSTV.

COLOR VS. MONOCHROME

     Image conversion is quite predictable with monochrome images 
and most unpredictable with color. B&W hand-scanners and TV image 
capture boards generate such monochrome images automatically  and 
present no problems when used with viewers such as VUIMAGE.

     Color images must be converted to monochrome prior to screen 
capture  is acceptable results are to be obtained.  Many  viewing 
programs  allow  color images to be displayed with  a  monochrome 
palette (VUIMAGE, despite its other useful qualities, does NOT!), 
in  which  case you can screen grab with  good  results.  Lacking 
other options, color images can be converted to monochrome  using 
the  ViewPort  VGA  software  that  comes  with  your  interface, 
provided the .PCX, or .TGA images have the correct resolution  to 
start with (see your program documentation). Assuming the  VGACAP 
program is resident, follow the steps below:

     (1) Boot the ViewPort software

     (2) Use the <ESC> key to get the OTHER OPTIONS menu.

     (3) Load the image (<F7> for .TGA or <Shift-F7> for .PCX)

     (4) Once the image has loaded, use <ESC> to get back to  the 
         OTHER OPTIONS menu.

     (5) Use <F10> to get to the test and diagnostic routines

     (6) Key <Y> to display the Luminance data

     (7) Key <Alt-F4> to capture the screen


Images  captured  in  this  way will  produce  64K  binary  files 
suitable for SSTV conversion.

     All of this sounds very complex to start with, but you can't 
hurt  anything  by  experimenting.  Once  you  have  played  with 
grabbers,  viewers,  and  images for a bit, it  will  all  become 
second nature.

IMAGE CONVERSION OPTIONS

     The  Image  Conversion  menu  supports  three  options   (in 
addition  to  <Q> to exit the conversion menu).  All  share  some 
common characteristics on that they will ask for the name of  the 
file  to convert and the name for the converted file.  The  three 
options are:

     <1> 307K binary files to 480 line fax

     This  program will convert the 307K screen binary  files  to 
FAX480 fax image files. Be sure to specify the entire name of the 
file  to convert (ex. screen05.raw), as well as directory  and/or 
path  data  if  the  source  image file  is  not  in  the  FAX480 
directory.  Conversion will take several minutes but  image  line 
numbers  will  be  posted  to let you know  how  the  process  is 
proceeding.  When complete, you can retreat to the fax  menu  and 
view  the new image. To save disk space, the routine  erases  the 
original 307K binary file when conversion is complete.

     <2> 480 line fax to SSTV

     This  routine will create an SSTV image file from  a  FAX480 
fax  file. The original fax image file is retained and  the  SSTV 
image is posted on the screen as conversion proceeds.

     <3> 64K binary files to SSTV

     This  will convert 64K binary screen grab files directly  to 
SSTV  format. The SSTV image is displayed as conversion  proceeds 
and  the  original  binary  file is  erased  when  conversion  is 
complete. 

Note that routines <1> and <3> do erase the original binary files 
(307K and 64K, respectively, but they don't so anything with  the 
smaller  palette files (.plt extension). You should  periodically 
sweep your directories and erase such files. The 

                         erase screen*.*

command  should  do the job as long as you have  no  un-converted 
screen files in the same directory.


                      PHOTOGRAPHING IMAGES

     Photography provides another way to archive images you  have 
received. A 35 mm camera, equipped with a close-up or macro  lens 
and  black  and white film, will do the job if  positioned  on  a 
tripod. The display image on the VGA monitor should be framed and 
focused  with  the camera so that it fills most of the  field  of 
view.  To avoid a diagonal artifact on your pictures,  caused  by 
the  camera focal plane shutter, set the exposure time to 1/4  to 
1/2  second. The f-stop can be adjusted for the  proper  exposure 
using the grayscale display from the main menu and your  camera's 
built-in light metering. 

     When making photographs, keep the ambient light level low so 
you  don't "wash out" the screen. You also need to be  sure  that 
bright objects such as windows or lamps are no reflecting off the 
monitor  screen  as viewed in the camera viewfinder. Due  to  the 
high resolution of the fax format, the resulting photographs will 
tolerate  a  high degree of enlargement (typically up to 8  x  10 
inches) while retaining acceptable image sharpness. 



                         FUTURE OPTIONS

     When  I first created the FAX480 program, it supported  only 
480 line fax operation. When I realized how effective the  system 
was  going  to be, I added a few basic SSTV options to  make  the 
program  more  attractive.  The present for of  the  SSTV  module 
reflects  added features I wanted when I actually put the  system 
on the air. It is safe to say that the SSTV module has grown  far 
beyond that which I had originally intended. Since the program is 
being  made  available as freeware, you cannot expect  be  to  be 
quite  as  aggressive in adding new features as I would be  if  I 
were selling the program. None-the-less, there are a few  options 
that are likely candidates for future upgrades:

     (1) HF fax receive modes

     The  ViewPort interface provides all the hardware  resources 
needed  for  reception  and display  of  wirephotos  and  weather 
satellite photos and charts transmitted on HF. No transmission in 
these modes will be supported since all are too long, in terms of 
the time required for transmission.

     (2) Amiga AVT fax modes

     The  Amiga  AVT system supports a 640 x 400 fax  mode  which 
could be added without too much difficulty.

     The  extent  to  which I do upgrades  is  dependent  on  two 
factors - the size of the program user base and the enthusiasm of 
users  for  specific  features. If lots of folks  are  using  the 
program and I get comments on-the-air or through my BBS (517-676-
0368), I will be more prone to make upgrades available.

     One  thing I won't do is mess with color display. The  whole 
intent of this project was to make an affordable system available 
for  high-resolution imagery, with the SSTV features added  as  a 
bonus.  John  Montalbano is doing an excellent job  in  providing 
color options using the ViewPort interface and I can see no point 
in  re-inventing  the wheel, particularly since his  software  is 
exceptionally reasonable in terms of price. 

Mason, MI                                January 1993