ntekb:  nterm's Extended Keyboard handler
              ======  =================================

                          Nevil Brownlee
               Computer Centre,  University of Auckland

                          Mon 4 July 88


For a long time now nterm users have asked me 'Why can't you map the PC's 
numeric keyboard like a DEC one?' and 'Can't you do something which will make 
the IBM Enhanced keyboard (with the function keys along the top) easier to use 
with nterm?'

I didn't do this initially since it would have involved writing a keyboard 
interrupt handler.  Instead I simply used the BIOS handler.  That provided 
several advantages, i.e.

   -  It was simpler to write and debug (it's hard to use debug to look at 
      a keyboard interrupt routine, since you don't have a keyboard for
      DEBUG any more).

   -  It works on any machine which implements BIOS properly.

   -  It allows you to use memory-resident routines which 'hook' the
      keyboard interrupts, e.g. mouse drivers and keyboard mappers.

The new handler is an attempt to provide key mappings which use the PC 
keyboard better, without giving away the second two advantages.  Its design 
aims were

   -  To continue using the BIOS key mappings wherever this was possible,
      so as to allow earlier versions of the nterm Terminal Definition (.TDF)
      files to be used unchanged.

   -  To provide new mappings for keys which BIOS doesn't (e.g. Sys Req on 
      the AT, F11, F12, Enter etc. on the Enhanced keyboard).

   -  To provide a set of mappings allowing the numeric keypad to be used
      as a DEC alternate keyboard, including the ability to implement 
      Application Key and Cursor Key modes.

   -  To work properly with the original PC keyboard, the AT keyboard and the 
      'Enhanced' keyboard, without requiring the user to specify which kind of 
      keyboard is being used.

   -  To automatically determine whether the keyboard LEDs can be controlled
      (i.e. whether we have an AT keyboard), and if possible set the keyboard 
      LEDs to correctly indicate the shift status.

The handler is implemented in two parts; a set of routines in ntekb.asm which 
does the actual interrupt handling, and a translate routine in ntntr.c which 
translates the keyboard codes into nterm key codes.

When a keyboard interrupt is received the keyboard scan code is read.  If it 
was a shift key the shift status is updated, the scan code and shift status 
are placed in the nterm keyboard buffer, then the interrupt is passed on to 
BIOS to be handled as usual.  The translate routine looks to see whether there 
is a key code in nterm's keyboard buffer.  If there's also one in the BIOS 
keyboard buffer the buffer is emptied and the BIOS scan code translations are 
used.  This allows nterm to use the nterm keyboard buffer as a signal that a 
key has been pressed, and then pick up all the characters placed in the BIOS 
buffer by a 'hook' routine such as a mouse driver.  Note that the system 
overhead in inspecting the nterm buffer pointers is considerably less than 
that in using a BIOS interrupt to check the BIOS keyboard buffer.

Some key codes are not passed to BIOS; these are the ones which I believe to 
be 'dangerous' to nterm.  For example the Print Screen key can ask BIOS to 
dump the screen to a local printer - but if there isn't a printer I don't know 
any way (except rebooting the system) to stop BIOS waiting indefinitly for the 
printer to become ready!  Control-Num Lock stops BIOS dead, busy waiting for 
another Control-Num Lock.  And so on.

To allow the 'DEC keypad' mapping I decided to use Num Lock to enter 'DEC 
keypad' mode.  In this mode the Num Lock key (in the DEC keypad's PF2 
position) maps to 'PF2', and therefore can't be used to leave this shift 
state.  To return to normal you use Shift-Num Lock.  On the AT keyboard ntekb 
sets the keyboard LEDs to indicate the shift status, and the 'shift key' codes 
are not passed to BIOS.

To cope with the original PC keyboard, which has double-width Num Lock and 
Scroll Lock keys as well as a triple-height Grey + key, ntekb maps Alt-Num 
Lock, Alt-Scroll Lock and Alt-Grey + to key codes which can be used instead of 
the AT Esc (left of Num Lock), Sys Req (right of Scroll Lock) and Grey * 
(above Grey -).  This provides a usable alternate keypad; the only anomoly is 
that the Grey - and + keys on the original PC keypad are thus 'upside down' 
compared to where they are on the AT.

The PC keyboard also has the problem that it doesn't have keyboard LEDs.  
Actually there is no problem if it really doesn't have LEDs, but many of them 
do and those LEDs are just toggled by the Num Lock, Scroll Lock and Caps Lock 
keys.  Since the toggling is done in the keyboard itself there's nothing nterm 
can do to prevent it - instead I've implemented a 'display shift state' 
option, which displays the shift status in the lower right-hand corner of the 
screen.

The Enhanced keyboard has problems of its own; it does have extra keys, and 
some of these send new scan codes which BIOS ignores.  Others send the same 
scan codes as earlier keys, preceded by a code indicating that an 'enhanced' 
key has been pressed.  ntekb sorts out this mess, and presents the translate 
routine with enough information to map the key to its proper nterm key code.

nterm's key codes have been chosen so as to achieve the design aims stated 
above.  To find out which scan code goes with which key you can either use 
kpc's SHOW KEY command - which will tell you the code so you can SET KEY to 
map it to something else - or you can look at the source code for ntvt.c, 
which has a complete list of all the nterm key codes.

Compatibility with earlier versions of .TDF files provided some problems too.  
To provide extra mappable keys for v200.tdf I had used Shifted numeric keypad 
keys, but for ntekb these must simply produce the normal shifted key code.  
One can't use Alt-numeric keypad keys, since BIOS uses these to form an input 
decimal code, e.g. Alt-3,2 produces the ASCII character '2' when the Alt key 
is released.  I therefore had to use Control-numeric keys for ntekb, so the 
codes formerly produced by Shift-numeric keys are now produced by Control- 
numerics, e.g. Control-End produces LF, etc.  One special case of this is that 
Control-Print Screen must be pressed to get a printer screen dump.

Another compatibility issue is that when using an old version of .TDF file 
such as v200.tdf, one will get a set of digits from the Shifted (or Num 
Locked) numeric keypad keys.  This is achieved for the '0'..'9', '.', '+' and 
'-' keys, which appear in their expected places.

One last piece of confusion:  when using vt.tdf, the Grey *, - and + keys 
produce the characters *, - and + when they are unshifted.  But when they are 
shifted they produce the DEC alternate keypad characters ',', '+' and 'Enter'!

Although all this sounds confusing, in practice it seems to work very well.  I 
find it most convenient to leave the numeric keypad unshifted, so that the 
arrow keys (which I use a lot) will move the cursor.  When I want an Alternate 
Keypad key I have to hold down the shift key, but then I don't use these keys 
nearly as much as I use the arrow keys.  The other unshifted keys map the DEC 
editing, Help and Do keys; this also seems to work well.  Should I wish to 
enter a lot of numeric data, Num Lock lets me do it.  Finally the function 
keys; with a good Alternate Keypad mapping these don't get used very often at 
all when working under VMS.  They can therefore either be ignored, or can be 
mapped to user-chosen strings using SET KEY.

I would appreciate hearing any comments you may have about nterm's new 
keyboard mapping.