TN210.DOC
                                    FORWARD
                                  ***********

    With this release one will find extensive revision over that in the earlier
TheNet Plus version 2.06 documentation.   Based on comments received as well as
in-depth observation of network activity, added material on operating practices
and suggested approaches to  laying out modern inexpensive backbone  trunks has
been added.   An effective LAN layout is also described.    The section on node
operation and configuration has been expanded.

    A program appended to this release  is  PATHCALC.EXE,  a shareware  program
written  by Jon Adams, NW6H.   PATHCALC will help  NodeOps in evaluating the RF
path  quality of existing  links and is extremely useful in selecting new radio
links.

    Another  program  appended is R95.EXE.    R95 allows modification of BINARY
files  to  an  ASCII format suitable for transmission over packet BBS networks.
Large files can be ZIPPED, split into smaller files,  then  recombined  on  the
receiving  end.    R95 doesn't  create the  problem of harsh sounds and monitor
lockups  that binary transfers via TCP can cause.    James Jones, WD5IVD is the
author of RADIX 95.


SOFTWARE NOTICE

    TheNet Plus is designated as freeware and is released for amateur radio use
only.     Permission is hereby granted to freely copy and distribute (on a non-
profit basis)  all,  or  portions  of  the  files associated with this release.
If  partial  distributions  of this documentation package are made, please give
the  appropriate  author credit.    Copies of TheNet Plus  source code  are not
available at this time.    Those interested  in  source  code  for the original
TheNet version 1.0 series may direct requests to:

NORD><LINK
3300 Braunschweig
Hinter dem Berge 5
Germany

    WARNING:  Use of  TheNet Plus in  non-conformance  of  local network policy
may  result  in  unsatisfactory  system  performance.     ALWAYS coordinate the
operation  of new nodes on existing networks prior to placing them in service.


ACKNOWLEDGEMENTS

    Special  appreciation goes to NORD><LINK's Hans Georg Giese DF2AU, and Mike
Roehner DC4OX,  authors of TheNet.     We also gratefully acknowledge the ideas
and comments submitted by many individuals.  These include:  Scott Cronk N7FSP,
Mark Frey VE3DTE,  Eric Meth VE3EI, Don Nelsch K8EIW, Dick Sission W5ONL,  Alan
MacPherson VE3KYZ,  John Langtry VE3NEC, John Papay K8YSE,  Dick Schiavo KF4WQ,
Bob  Moorman K5VMX,   Mykle Raymond N7JZT,  Dick Taylor N5NGZ,  Rich Ide N7LDI,
Brett  Mueller KB5CDX,  Juan Pineda EA3CIW, Roy Gould N5RG, Dick Wareing K3AKK,
Dave Weik KB7ZZ,  Dick Jenkins N2AYY, Steve Weidner WB7WHF, Wally Foster N6CDJ,
Fred McKenzie K4DII,  Hartley Gardner W1OQ  and,  Tad Torborg KA2DEW  and  Rich
Place WB2LJR,  of the North East Digital Association.   There has been a lot of
interest in this project and our apologies if we have overlooked anyone.


INTRODUCTION

    The  PURPOSE  of  packet  nodes  in  a  network  is  to act as relay points
extending the range of  users.   Compared to early digipeater  networks  (which
typically  spanned a  maximum  distance of  8 - 10 hops),  nodes allow users to
travel significantly farther.  As of this writing Alan MacPherson, VE3KYZ holds
the distance record of thirty seven sequential hops through the system.  Alan's
route was from Ontario, Canada to Arizona, USA.

    Nodes are  also  useful in allowing  frequency  changes in a radio network.
They  can  be  configured to route circuits between combinations of VHF/UHF/HF.
Nodes can accomplish changing  from  a radio  route to a wire-line route.  This
sometimes is done over satellite or telephone circuits.

    A  prerequisite for proper node software development is to reach a sensible
balance  between  network loading and providing useful features for the  users.
It is tempting  for software developers to design  nodes  with  many "bells and
whistles".    However, our RF networks  are for the  most  part overloaded with
BBS, Packet cluster, and  TCP/IP  traffic.  Until the networks are upgraded for
greater  capacity,  it's important that node design be oriented toward reducing
unnecessary node overhead.

    We  believe TheNet Plus achieves this goal.   Each TheNet Plus  feature was
carefully weighed in terms of usefulness versus the generation of added network
congestion.

    TheNet Plus  conforms  to  the International  Standards  Organization (ISO)
model  for  Open  Systems  Interconnection  (OSI).    OSI is a modular software
construction model for data communications.   It is a  functional guideline for
universal intercomputer communication.   The OSI model was developed during the
1970s' and  formally adopted as an international standard in 1983.   This model
is known as CCITT X.200 or ISO 7498.

    The  TheNet Plus code is written into a 27C256 Electrically Programmed Read
Only Memory (EPROM)  chip.  This EPROM directly replaces U-23 that contains the
TNC program in TAPR TNC-2 or clones.    Thus, a single chip change-out converts
the TNC into an economical and powerful node switch.

    The new node features and networking suggestions in this release came about
through personal observations and user input.  Our goal is to provide practical
nodeware along with information on the art of NodeOping.  To this end, we would
appreciate feedback.  Our points of contact are:

        Software:                                 Documentation:
        *********                                 **************

Packet: NJ7P@NJ7P.AZ.USA.NA                       N7OO@NJ7P.AZ.USA.NA


U.S. Mail:  William A. Beech, NJ7P                Jack Taylor
            PO Box 38                             RR-2 Box 1690
            Sierra Vista, AZ  85636               Sierra Vista, AZ  85635


            Spanish language coordinator and distribution:
            **********************************************

                    Packet: NS7G@NJ7P.AZ.USA.NA

                    U.S. Mail:  Rod Lopez
                                2302 6th st.
                                Douglas, AZ  85607