TN210-7.DOC
                            USER COMMAND LIST
                          *********************

    TNPlus  version  2.10  has the following commands available  to  the  user:
(Commands may be abbreviated as indicated.)

    BYE  (B)  - Use this command when you want the disconnect to  be  initiated
from the far end of the circuit.

    CONNECT  (C) - This is the general command to connect to and from the node.
Examples  are:   "C PDT" to connect to a node, "C KB5CDX" to connect  from  the
node to a local station.   Connecting through a digipeating path is disallowed.

    CQ  - When the node receives a CQ command, it transmits once:  CQ plus  any
user  text up to a maximum length of 77 characters, including spaces.  The node
is also  conditioned  by this action to display the CQing station in its  USERS
response  for a period of time set by Parameter 24 (usually 15 minutes), unless
the  CQing  station  issues  another command before the time runs out.   Should
another  station  perform  a  USERS  command  during  this  time,  he could see
something like this:

DMN:WD5EZC-2> TheNet Plus 2.10st (673)
Circuit(CLOUD:WD5EZC-1 W2RRY)  <..>  CQ(W2RRY-15)

    Anyone  observing  the  CQ  can connect to the node  and  then  connect  to
W2RRY-15  to initiate a QSO.  If the CQing station doesn't get a reply after  a
few minutes,  he can reinitiate the CQ command from time to time  in  hopes  of
attracting  someone on the local frequency.  Remember, each time the CQ command
plus text is given,  it will be broadcast unproto by the node for just that one
time.     If one wants to attract the attention of a monitoring station, the CQ
procedure  can  be  used  to pass a unproto message off a specific node.    For
instance:  "CQ  will  someone  telephone  Pat,  KR5S to turn on his TNC?"   The
request can be repeated every minute or so until the sender is either connected
to, or decides no one is monitoring the local node.

    HEARD  (H)  - The "H" command will display level 2 (normal) users heard  by
the node during the past 15 minute period.  Netnodes and level 3 users will not
normally  be  seen  once the  node has "initialized" itself (a 30 -  60  minute
period  after  startup).  The maximum number of users allocated for  the  Heard
table is  20.   Stations listed in  the heard table  are not ranked in order of
time,  i.e., the first station listed may not be either the  most recent or the
oldest  station heard.    If stations  have  not been heard  during the past 15
minutes, a "No One" response is given.

    The Heard function compares the  new call with the call signs listed in the
node alias table.   If a match isn't made, the new call will show  on the Heard
list.   Thus there may be brief periods when the call sign of either a new node
or a propagated node may appear on the Heard list.  When a match is made of the
alias, the node call sign will no longer be listed.   This is also true of node
aliases,  which  may  temporarily  show.    Additionally,  the list may include
Ka-node and non-node aliases, if heard.

    Callsigns of downlinking stations from local nodes also will be shown.   If
a user  notes  an SSID of -14 or -15  associated with the  callsign,  the  odds
are  these  calls  will be  unconnectable  since  the  originating  station  is
separated by  one or more nodes.   They are picked up in the local node's Heard
list  when  converting to a "Downlink" status in the process of connecting to a
local station.


    INFO  (I)  - Is  SYSOP   programmable  and  has  a  capacity  of  up to 160
characters  including control characters and spaces.    The purpose of the INFO
section  is to  provide  local information  and/or news  of interest  to users.
Distant users find it very convenient to know the location of the node and it's
frequency.   Such  data is  useful for  those exploring  and mapping the packet
network.

    The INFO section is also a good place to identify a local 24-hour maildrop
or BBS.    Or,  one can place routing information, such as the path to a local
DXCluster or gateway.   In some areas, network management policies dictate the
format and content of node INFO messages.

    The procedure for writing to INFO is further explained in the SYSOP COMMAND
LIST.


    NODES (N) - This command calls down a listing of the nodes contained in the
destination table.   It gives a user a listing of possible destination nodes to
connect to.  It's good practice to use this command sparingly.     Owing to the
condition  of our congested  networks,  a NODES dump may cause all users on the
circuit  to  be  disconnected  due to the large barrage of packets this command
normally  yields.   Since VHF networks are relatively stable,  chances are, the
contents  of  a local node table are not apt to change much from hour to  hour.
Thus,  local users should be  encouraged to  NOT command a NODES dump every few
minutes.    For the same  reason,  it's a poor practice to request  NODES, from
distant network connects due to the real possibility of disconnecting all users
along a multiple node connection.


    Variations  on the N command are:  "N *" and "N <alias or callsign>".   The
"N *"  command  ADDITIONALLY yields a NODES dump of the # (hidden) nodes.   The
hidden  nodes are  those normally  associated with backbone trunking.   A  very
useful  command  is  that  of  "N <alias or callsign>."   This allows a user to
find the path quality and identification  of the nearest  node  leading  to the
destination node requested in the command.  An example:

    A  user is  at the  NDGAF  node  and wishes to know the route to NDPMB.  He
issues a "N NDPMB" command and receives this response:

NDGAF:WA0RLE-1> Routes to: NDPMB:WC0M-8
  192 5 0 NDPMB
  146 5 0 NDPET

    This tells him  there is a DIRECT radio path (the 192 and 0) and  that  the
path is fairly recent (as shown by the "5").   He can assume a high probability
of success should he attempt the connect to NDPMB.   He also  notes there  is a
secondary route to NDPMB via NDPET.  The numbers given in the N <alias or call>
command  will  be explained in more detail later.     Here we just want to show
how the N <alias  or  call> command  is a powerful tool,  useful in helping one
navigate throughout the network.