16550 - A UART Control Program
                                   Version 1.0


          DESCRIPTION:

            16550 is a shareware program designed to allow the 'unlocking'
          of the internal fifo buffer present in the UART chip of the same
          name. The program will scan all four COM ports (COM1: - COM4:)
          available on the PC and report the presence (if any...) of the
          16550 UART. The user may optionally set the various parameters
          necessary to utilize this buffered mode of operation.

          DISCUSSION:

            The original PC serial interface specification utilized the
          8250 Programmable Communications Interface, or UART. This device
          converts data from the microprocessor into a format that is
          easily transmittable via a single-wire connection. To accomplish
          this task, the UART takes data from the computer in a parallel
          format (ie: the bits are presented side-by-side) and shifts them
          out via a single pin in a serial (one bit directly after another,
          daisy-chain fashion) data stream. Various extra bits are added
          such as the start, parity and stop bits to provide the UART on
          the other end of the serial data connection with an accurate
          means for the re-assembly of the original data format.

            In the early days of serial communications, particularly that
          involving data transmission via telephone lines, the speed at
          which the data was transmitted wasn't particularly fast. This is
          especially true with telephone lines. The normal voice-grade line
          is extremely limited in it's sound-reproduction qualities. This
          low bandwidth implied that any data must be transmitted very
          slowly to avoid 'overloading' the line. For voice-grade lines,
          the maximum reliable data rate was 300 baud, using the Bell 103
          modem specification. (A modem translates the on/off binary pulses
          into a tone so that the telephone line will treat it as regular
          'voice' information.)

            The UART, of course had to be able to translate data at the
          same rate in order for the system to work. Other serial devices
          such as terminals and printers did not require a modem, but in
          most cases the data rate was still quite slow, usually under
          19,200 baud.

            In the PC, when using the serial port(s) directly, such as
          sending a file to a serial printer, the 8250 UART (or the updated
          16450 version) was more than able to keep up. Even in a
          telecommunications link, the UART was still fast enough, since
          the data over the phone line was relatively slow.

            Another point was that the early PC's weren't terribly fast.
          This was made worse when running a communications program such as
          ProComm or CrossTalk. Since the data rates were slow, there was
          enough time for the computer to run the program instructions



                                                                     Page 1





                           16550 - A UART Control Program


          while fetching the individual bytes as they came in over the
          serial link. Even at 9600 baud, a very-well
          written comm program was able to keep up with the data.

            Time progressed and technology improved serial communications
          (particularly that of modems) to the point where extremely high
          data rates could be achieved. The new V32.bis modems are capable
          of transfer rates of up to 14,400 baud, and with the V42.bis
          compression, data burst rates of over 57,000 baud are feasible.
          Of course, software became more complex as well, but with a
          price. The more complicated the software, the more time it takes
          to handle the program instructions. Couple this with the fact
          that the data is coming in at an extremely high rate, and you
          have a potential problem on your hands!

            What typically happens is a data overrun occurs. This means
          that there was still a byte of data left in the UART when the
          next byte came in. Naturally, a loss of just one single byte is
          enough to crash a program, so this is a very important concern!
          One way around the problem is a handshake scheme, whereby the
          transmitting computer holds off sending data until the receiving
          end is ready. This works very well, but one major drawback is
          that a great deal of time is wasted signalling instead of
          transferring data.

            The 16550 UART gets around this bottlenecking by incorporating
          a buffer directly in the chip itself. This buffer is designed to
          hold up to 16 bytes (or characters) before an overrun occurs. The
          buffer is arranged in a FIFO manner, meaning First In, First Out.
          In programming terminology this is known as a queue. The 16550
          UART also has improved circuitry which allows it the ability to
          transmit data some 4 times faster than the old 8250! This high-
          speed circuitry helps in the PC environment mainly in interrupt
          timing, though the time saved is rather marginal. Of more
          importance is the FIFO. By having a 'reserve' storage area on the
          chip, if the processor is momentarily busy, (say, executing an
          ANSII graphic sequence) the data is not lost, but held in the
          buffer until the processor is free to receive it.

            The problem now lies in the fact that the majority of older
          communications programs do not check for, and utilize the FIFO
          capabilities of the 16550 chip. This is where the 16550 program
          comes to the rescue!

          PROGRAM OPERATION:

            The 16550 UART initially powers up in a non-FIFO state. This
          makes the UART software-compatible with the 16450, and the older
          8250. In most cases, the communications software doesn't know the
          difference. At least until the data comes in faster than the
          program can process it!

            The 16550 program goes in and 'unlocks' the FIFO capabilities
          in the UART, and even in a buffered state, the 16550 still looks



                                                                     Page 2





                           16550 - A UART Control Program


          like the 16450 to older programs! If buffering occurs, then the
          data is held, and subsequently read out at a relaxed pace
          automatically, providing full compatibility with older software,
          yet giving the high-speed protection of a data buffer!

          PROGRAM PARAMETERS:

            The 16550 automatically detects a 16550 UART, and provides
          control for the COM port address, enabling and disabling of the
          FIFO, and the settings for a special interrupt based upon the
          number of characters being held in the FIFO buffer.

            Executing the program without specifying any parameters results
          in a scan of all COM ports, and reports the presence of a 16550
          UART in each. If the user knows that a 16550 device exists,
          additional parameters may be specified to access the FIFO. These
          parameters are as follows:

             COMn - Tells the 16550 program to use COM port n, where n
                    indicates ports 1 through 4. Any value outside of this
                    range results in an error. NOTE: A COM port MUST be
                    specified when setting the UART!

                ? - Echos a brief help text on the screen. No action is
                    taken.

               /f - Enables the 16550 internal buffers.

               /r - Disables the 16550 internal buffers and resets the UART
                    to the 8250/16450 compatibility mode.

              /tn - Allows the adjustment of the FIFO-full interrupt. n
                    specifies the number of characters allowed in the
                    buffer before an interrupt occurs. the values for n are
                    1,4,8 and 14. NOTE: this is a very sensitive setting!
                    For normal operation with old communications software,
                    this parameter should not be used!

            The program defaults to FIFO disabled, and a /t parameter of 1.
          If the command line parameters are valid, the program will verify
          that a 16550 UART is present, and that the parameters have been
          set. Unless another program that recognizes a 16550 UART is
          executed, the UART should remain in the current state.

          SHAREWARE CONCEPT:

            Shareware is a non-conventional approach to software
          distribution. Unlike regular commercial programs, shareware
          allows a 'try-before-you-buy' approach. In most cases, the
          programs are just as bit as good (if not better in some
          instances!) as the programs you buy at a computer store.

            Shareware ISN'T freeware! In most cases, the software author is
          a professional who makes at least part of his or her living on



                                                                     Page 3





                           16550 - A UART Control Program


          the registration of the software program. Typically the user is
          enticed into registration by added features, free updates, etc.

            Shareware depends upon the user to make it work. It's up to
          you!

          Registration:

            This program is 'donate-ware', which is similar in concept to
          shareware. The author makes no claims as being a professional
          software engineer, rather, the author is a disabled hardware
          engineer who enjoys tinkering with programs, and making the
          hardware work better.

            If you find that this program is useful, and saves you some
          time and headaches, the author would appreciate a $5.00 (US)
          suggested donation. This amount would include a 'registered' copy
          of the program (without the shareware notice), and the eternal
          thanks from the author. Considering that the cost of new
          communications software that recognizes the 16550 UART far
          exceeds 5 bucks, you get a pretty good deal! Of course, any
          amount is appreciated. Oh, please specify whether you want a
          360K, 5-1/4" or 720K, 3-1/2" floppy when you register.

          .....and the address is:

                     Brent Turner
                     P.O. Box 3612
                     Fullerton, CA, 92634-3612

            NOTE: Foreign (non-US) users please include a few extra bucks
          for the postage! Thanks.

          THE LEGAL STUFF:

            This software is distributed on an as-is basis. The author has
          made reasonable attempts to ascertain it's performance, but
          cannot guarantee that it will work in every instance. The author
          is not responsible for any damages, or loss of data resulting
          from the use of this program.

            The shareware version of this program may be freely distributed
          as long as all files are included in the package. The registered
          version may not be copied or duplicated.

            Shareware vendors may distribute this program as long as the
          cost per disk does not exceed $5.00. This program may be included
          (bundled) with other programs of like nature, so long as the
          above cost-per-disk stipulation is met.

            The original source code is not available.






                                                                     Page 4