Slickware is Copy(c)right 1989,1992 by Gary M. Raymond, New Orleans, La.
              Slick AT Modem Driver Program V1.2 by Gary M. Raymond

                          Simple <Software> Company
                              HOME of SlickWare

                              Gary M. Raymond
                                P.O.Box 8184
                           New Orleans, La.  70182
                               (504) 288-6550
                            Compuserve 70613,3165

   ====================================================================

   Files Provided:
   AT.COM        Slick DOS Command Modem Driver
   AT.DOC        This document.


   Why AT?  Occasionally the need arrises to send your modem a command
   via a batch file or the DOS command prompt. Having the need myself,
   I tried several similar utilities already on the shareware market and
   discovered several things. Either they were too involved, requiring
   the poking of even more information into my already crowded DOS
   environment (in order to configure the utility), or required the
   selection of one out of many separately pre configured files to
   use on my particular port. Finally, most are written in high level
   languages that produce code that is simple inelegant and requires
   too many CPU cycles to do a job that can be done in less.


   If you type AT (alone) at the DOS prompt, you will see the following
   help screen.

       AT Modem DOS Command Utility Ver 1.1
       The Correct Syntax is AT #+STRING
       # = 1,2,3 or 4  (COM1 thru COM4)

       Examples:
       AT 1DT288-6550 = Tone Dial (COM1)
       AT 2M2 = Turn ON Speaker   (COM2)
       AT 3Z  = Reset Defaults    (COM3)
       AT 4H1 = Phone OFF Hook    (COM4)

   Right off you will notice that this one utility will run any one of
   the four standard IBM port addresses by simply including the port
   number as the leading numeral on the command string. These default
   ports are COM1 = 3F8, COM2 = 2F8, COM3 = 3E8, COM4 = 2E8. This
   utility will even overcome some of the limitations of DOS when it
   comes to operating ports 3 or 4.

   If you attempt to use a port number out of range, AT simply will not
   load and inform you of the reason. If you choose a port that is not
   active, AT will also attempt to inform you of that as well.

   To make AT as useful as possible over a wide range of CPU and modem
   configurations (that all have different UART responce times) it has
   been coded with fixed timing constraints based on CPU clock ticks.

   For an additional five dollar fee I will customize this utility
   for any non standard serial port addresses you might require. Leave
   E-Mail here or on Compuserve.

   Meanwhile, for reference, I have listed below the majority of the
   Hayes string switches. Please note that every modem is somewhat a
   different animal and may not utilize all these switches.


         AT        ATTENTION COMMAND
         A/        REPEAT COMMAND
         A         ANSWER MODE COMMAND
         B/B0      SELECT CCITT V.22 IN 1200 BPS
         B1        SELECT BELL 212A
         Dn        DIAL COMMAND (n = DIAL STRING, 0-9, *, #, !, W, R, AND,
         E         DISABLE ECHO
         E1        ENABLE ECHO 
         H         ON HOOK (HANG UP)
         H1        OFF HOOK
         I/I0      IDENTIFY
         I1        DISPLAY 000
         I2        DISPLAY OK
         I3        DISPLAY MESSAGE PROGRAM ROM
         L/L0      LOW VOLUME
         L1        LOW VOLUME
         L2        MEDIUM VOLUME
         L3        MAXIMUM SPEAKER VOLUME
         M/M0      DISABLE SPEAKER
         M1        SPEAKER ON UNTIL CARRIER
         M2        SPEAKER ALWAYS ON
         M3        DISABLE SPEAKER WHEN DIALING OR CARRIER
         O         GO ON LINE
         O1        RETRAIN (2400 BPS MODE ONLY)
         Q/Q0      ENABLE RESULT CODES
         Q1        DISABLE RESULT CODES
         Sn=X      S REGISTER WRITE (n = VALID S REG, X = ALLOWED VALUE SEE        
                   &F COMMAND)
         Sn?       READ SPECIFIED S REGISTER (n = ANY VALID S REGISTER)
         V0        SELECT DIGIT RESULT CODE
         V1        SELECT WORD RESULT CODE
         X0        BLIND DIAL, DISPLAY "CONNECT"
         X1        BLIND DIAL, DISPLAY "CONNECT 1200/2400"
         X2        DETECT DIAL TONE, DISPLAY "CONNECT 1200/2400"
         X3        DETECT BUSY TONE, DISPLAY "CONNECT 1200/2400"
         X4        DIAL AND BUSY TONE DETECT, DISPLAY "CONNECT 1200/2400"
         Y0        DISABLE LONG SPACE DISCONNECT
         Y1        ENABLE LONG SPACE DISCONNECT 
         Z         SOFTWARE RESET
         +++       ESCAPE CODE (GO TO COMMAND MODE IF ON LINE)
         &C0       DCD ALWAYS ON 
         &C1       DCD FOLLOWS REMOTE CARRIER STATUS
         &D0       IGNORE DTR
         &D1       GO TO COMMAND WHEN DTR ON TO OFF
         &D2       HANGUP AND GO TO COMMAND WHEN DTR ON TO OFF
         &D3       POWER UP RESET WHEN DTR ON TO OFF
         &F        FETCH FACTORY CONFIGURATION for S REGESTERS
         &G0       NO GUARD TONE 
         &G1       550 HZ GUARD TONE
         &G2       1800 HZ GUARD TONE 
         &J0       SELECT RJ-11/RJ-41S/RJ-45S
         &J1       SELECT RJ-12/RJ-13
         &M0       SELECT ASYNCHRONOUS MODE
         &P0       MAKE BREAK RATIO FOR US (40/60)
         &P1       MAKE BREAK RATIO FOR FOREIGN STANDARD (33/66)
         &R0       CTS TRACKS RTS
         &R1       CTS ON WHEN MODEM READY IN DATA MODE
         &S0       DSR ALWAYS ON
         &S1       DSR FOLLOWS RE232 SPECIFICATION
         &T0       STOP TEST 
         &T1       LOCAL ALB TEST
         &T3       LOCAL DLB
         &T        ENABLE DLB REQUEST
         &T5       DISABLE DLB REQUEST
         &T6       REMOTE DLB
         &T7       REMOTE DLB AND SELF TEST
         &T8       LOCAL ALB AND SELF TEST
         &V        VIEW ACTIVE PROFILE


   ====================================================================
   V1.2  Corrects bug in COM4 (geezzzs you guys report fast!)
   ====================================================================
   V1.1  First release.......................................
   ====================================================================

                           ÚÄÄÄÄÄÄÄÄÄ¿
                           ³ MEMBER  ³   Society of
                           ³  ÚÄÄÄÄÄÄÁÄÄ¿ Independent
                           ³  ³         ³   Shareware
                           ÀÄÄ´    þ    ³     Authors
                              ³    º    ³
                              ÀÄÄÄÄÐÄÄÄÄÙ
    This program is produced by a member of the Society of Independent
    Shareware Authors (SISA). The Society wants to ensure that all
    valid shareware principle actually work for you and SISA members.
    The principle behind shareware distribution is simple; try before
    you buy. Society members agree to license all shareware for a minimum
    of 10 days, free of charge, to first time users as an evaluation period.
    After 10 days, buyers are then obligated to license their copy with
    the Society member. Society members are obligated to provide high
    quality, useful shareware, but, are free to choose whatever marketing
    methods suit their specific needs. SISA sanctioned marketing methods
    include: demonstration versions; providing printed documentation
    after purchase; registration keys that unlock additional features
    not necessary to determine basic usefulness; and, providing bug
    fixes free of charge. Any Shareware author may become a member of
    SISA without cost by simply agreeing to the above conditions and
    displaying, at their option, this logo in their documentation.
   ====================================================================

    WARRANTY:
    Software:
    Simple Software warrants that the software contained herein will
    perform in substantial compliance with the documentation
    accompanying the software. If you report, in writing, a significant
    defect to us, and we are unable to correct it within 90 days of the
    date you report the defect, you may return the software and
    accompanying materials, and we will refund the purchase price.

    Diskette's and Documentation:
    Simple Software, warrants all diskette's and documentation to be
    free of defects in materials for a period of 30 days from the date
    of purchase. In the event of notification within the warranty period
    of defects in any materials, Simple Software will replace the
    defective diskette or documentation.

    Remedies:
    The remedy for breach of the warranty shall be limited to
    replacement and shall not encompass any other damages, including but
    not limited to loss of profit, special, incidental, consequential,
    or similar damages, losses, or claims.

    DISCLAIMER:
    Simple Software specifically disclaims all other warranties,
    expressed or implied, including but not limited to, implied
    warranties of merchantability and fitness for a particular purpose
    with respect to defects in the diskette and documentation, and the
    program license granted herein, in particular, and without limiting
    operation of the program license with respect to any particular
    application, use, or purpose.  In no event shall Simple Software be
    liable for any loss of profit or any other commercial damage,
    including but not limited to special, incidental, consequential or
    other damages.

    GOVERNING LAW:
    This statement shall be construed, interpreted, and governed by the
    laws of the State of Louisiana.
    ====================================================================

   Registering your copy will help continue the competitive advantages
   of providing economical shareware. Upon receipt of your payment I
   will provide a registration code number which will allow you to self
   register and personalize your shareware copy. Upon receipt of your
   code  type SLICK REGISTER and enter your first and last name followed
   by the code number. Code numbers may be issued by voice phone if you
   are willing to accept a collect call, otherwise it will be sent to
   you via first class US mail service.

   Yes Gary, I enjoy your program and would like to register and
   obtain the latest version.


   Name_____________________________________________________________

   Mailing Address__________________________________________________

   City & State ___________________________________________________

   ZIP _____________________________ Phone _________________________

   Send $4 + $1 (ship & hand) check or money order to:

                              Gary M. Raymond
                                P.O.Box 8184
                            New Orleans, La. 70182
                                504-288-6550
                            Compuserve 70613,3165
   ====================================================================
                                     EOF