****  TECHTIPS.DOC as of Feb 3rd,1993  ****           
		 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
		 º            C X R  Telcom                º
		 º   521 Charcot Ave, San Jose, CA 95131   º
		 º                                         º
		 º       Fax         (408)955-0502         º
		 º       Sales Dept. (408)435-8520 x 297   º
		 º       BBS         (408)955-0803         º
	     ÉÍÍÍ¼       Repair      (408)435-8520 x 311   ÈÍÍÍ»
	     º  MOST COMMON QUESTIONS, PROBLEMS, AND ANSWERS.  º 
	     º  ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  º
	     º                                                 º
	     º  SECTION1:  Fax96              ("fax-only card")º
	     º  SECTION2:  Fax96 with 1-Liner ("fax-only card")º
	     º  SECTION3:  Fax96 with Modem                    º
	     º  SECTION4:  Fax96 with Modem and 1-Liner        º
	     º  SECTION5:  Windows software                    º
	     º  SECTION6:  Modem Information                   º
	     º  SECTION7:  General Information                 º
	     º  SECTION8:  Winfast 1445 & 1446                 º
ÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍ



SECTION1:  Fax96 ("fax-only card")
__________________________________
1. Q:SOFTWARE RELEASE. What is the latest software release?
   A:      Release 4.15 is the latest fax software for the Fax96. 
	   

2. Q:PRINTING. Why is my printer not printing correctly?
   A:   a. Run FAXCONFG and make sure the correct printer is selected.
	b. If the EPSON-LQ printer giving you problems, run FAXCONFG and select
	   FORTIS-DQ (quality.)
	c. HPII-LaserJet - select HPIIP in FAXCONFG.
	d. HPIIIp-LaserJet - Make sure printer is set to Portrait Mode.
	e. Post-Script printers - Only our Windows s/w will print to it.
	f. Cannon Bubble Jet 300 - select IBM Proprinter X24E in FAXCONFG.
	g. HPII-LaserJet - If TTI header (From: ... Pages 1of2) is not 
	   printing, then select HPIII in FAXCONFG.
	h. HP LaserJet IV - only our Windows Software will print to it.
	   Our DOS Fax software does not have a printer driver for LJ IV.

*****************************************************************************
Note: The Dos based Fax software will not have any additional printer drivers
      added in the future.
*****************************************************************************

3. Q:DEMO MODE. Why do I keep getting "No fax card - Demonstration Mode Only?"
   A:   a. Make sure Jumpers on card match settings in FAXCONFG.
	b. Try a different IRQ and/or I/O settings on card and in FAXCONFG.
	c. Power-off computer and re-seat fax card into computer.
	

4. Q:CAN'T RECEIVE. Why can't I receive a fax?
   A:   a. Is this problem from any fax machine or just one fax? If only one, 
	   then make sure you have the latest software and re-test. If 
	   problem persists, call tech. support and give them the make/model, 
	   and fax phone# of that problem fax machine for us to test.
	b. Put FRECOMRF /ON in your AUTOEXEC.BAT file so that is loads before 
	   and other program. Best place is usually one line below the PATH 
	   statement. This will auto-load the receive program when you turn 
	   on you computer. When sending, displaying, or printing a fax, 
	   use only FCCPRG, not FRECOM.
	

5. Q:NO PHONE LINE. Why does the screen says "No Phone Line Detected" when I 
     try to dial out, and how can I correct it?
   A:    a. Power-off your computer, wait a few seconds,then power back on.
	 b. Check that if the phone cable is plugged from the wall to the Fax96 
	    bottom jack. 
	 c. Exchange the phone cable going from the fax card to the wall.
	 d. Try connecting a phone to the top jack of the fax card and listen 
	    for a dial tone.  If you can hear a dial tone, then the board has
	    a hardware problem, please call our Service department at 
	    408-435-8520, extension 311 for repair or replacement.
	    Business hours from M-F 8-4 pst.
	    

6. Q:QEMM MEMORY MANAGEMENT. How do I load my receive program using QEMM? 
   A:      From a DOS prompt, type  LOADHI /R:2 FRECOMRF /ON 

7. Q:Not Working in Windows.  Why doesn't my Fax96 work with Windows?
   A:      The Fax96 was not built to work under Windows; it is not compatible
	   with windows.

8. Q:Different Software.  Does Fax96 support other manufacturers' faxing 
     software?
   A:      The answer is NO, Fax96 only works with the software packaged with
	   it.

SECTION2:    Fax96 1-Liner ("fax-only")
_______________________________________
1. Q:ANSWERING MACHINE. My ansering machine answers the phone, but 
     the 1-Liner will not detect a fax. Why?
   A:   a: Make sure to connect your answering machine (a/m) to the TOP jack 
	   of the 1-Liner card; cannot have it on another phone jack or 
	   another room. Also set the answering machine to pick up the line 
	   first.
	   Example: Set a/m to 4-rings and the 1-Liner to 6-rings. After 
	   4-rings, the a/m will answer, THEN the 1-Liner can "listen" for a 
	   fax.
	b: Try putting a two second pause before starting and after ending 
	   your greeting message, that should give the fax enough time to 
	   acknowledge the tones.
	c: Do you have a combination Telephone/Answering machine?  If you do
	   then we are aware of the problem, and are currently in the process
	   of conducting tests; the Fax96 does not seem to work with the new
	   digital technology Telephone/Answering machine combination.
	d: Check to see if you have the latest software releases.
	e: Check to see if you have any other memory resident programs(TSR's) 
	   that might conflict with the one-liner not being to detect an incoming
	   fax.

SECTION3:    Fax96 with Modem
_____________________________
NOTE:
    
	   5.20 Software Release on this BBS. 5.20 is the latest 
	   DOS faxing software update. 

1. Q: ERROR:"NO FAX CARD FOUND-DEMO ONLY." I keep getting this when I start  
      the fax software?
   A:   a. Check switches on the card to make sure they match the settings on
	   FAXCONFG.
	b. BIG HELP!!! Disable the existing COM port in your computer.
	   Example: If card is set to COM2, then disable COM2 in your 
	   computer. See your computer operators manual for instructions.
	c. Test the card using COMIT software diagnostics.
	   Follow the keystrokes below:
	   / "brings up the comit menu"
	     Diagnostic
	     Check all comm ports

	   The modem ID is 249. If the test found the modem on the com port.

2. Q: DISPLAY. Can't display some faxes?
   A:      Bug in 5.17. Download 520-1.ZIP from this BBS. 
				 520-2.ZIP
				 520-3.ZIP

3. Q: PRINTER setup. Everytime I enter FAXCONFG, my printer is de-selected?
   A:      Download FAXCONFG.EXE from the BBS.



SECTION4:    Fax96 with Modem and 1-Liner
_________________________________________
1. See SECTION 2 for more 1-Liner tech. tips. See Fax96 with Modem section
   for more fax modem tips.

2. Q: 1-LINER. My 1-Liner detects fax calls but does not detect modem calls?
   A:      FAXDATSR is not working, and is currently in the testing stage

3. Q: 1-LINER. The 1-Liner does not pickup fax calls?
   A: Check to see if you have the latest Software Releases and/or
      latest Firmware Revisions.  Please refer to SECTION 2 for more 
      1-Liner troubleshooting tips.

4. Q: 1-LINER. How can I test the 1-Liner function of the fax card?
   A:      The test below is used to test the Fax/Modem/1-Liner circuit.
	I. Load COMIT software.
       II. Type the following commands to put COMIT into manual control 
	   mode:
		/
		O
		M
       III. Type the following from the COMIT manual control screen:
		AT+FCLASS=0  hit the <Enter> key. Will see "OK"
		AT+FAA=0             <Enter>
		AT*F1                <Enter>        
	IV. Now have someone call you using a regular phone. 
	 V. Pick up the phone attached to your Fax96 1-Liner. You should
	    see +HKLO appear on the screen. 
	VI. Have the caller hit touch-tones on their telephone key pad. You
	    SHOULD see the numbers they are hitting (i.e. +DTMF5 +DTMF4)
	    on your screen. If you do not see anything appearing then the 
	    1-Liner circuit is not working and should be sent back for repair.
       VII. If you DO see numbers appearing, then the fax 1-Liner  card is
	    working.
      VIII. Type the following to get the 1-Liner card out of test mode:
		AT*F0                <Enter> 


6. Q: Why does my release 5.20 software schedule a delayed send when I want 
      the fax to go out immediately?
   A: This is a bug, and the fix is currently being tested.  Will be on this
      BBS soon.

7. Q: One-Liner & Call Waiting.
   A: Please see section 5 for further details.



SECTION5:    Windows software        
_____________________________
1. Q:SOFTWARE RELEASE. What is the latest software release?
   A:      Release 2.05 is the latest software release for Windows. 
   
	   Known fixed bugs:       
			Better Send/Receive.
			Display Log bugs.
			Display Fax bugs.
			Support for Windows 3.1.
			Option to turn off Auto-receive.
			COM 1 thru 4 support AND Alt IRQ's
			Flips in display
			Auto print
			


1. Q: WINDOWS. Can I run my Fax96 card in Microsoft Windows?
   A:      Only Fax96 with Modem cards will run in Windows. 
	   See SECTION 7 for more info.   

2. Q: WINDOWS.  What if my Windows is not installed on its default directory, 
      which is c:\WINDOWS?
   A: The Fax Window will not install unless Windows is in the default 
      directory   C:\WINDOWS

3. Q: WINDOWS.  Why do I get several hundred pages when I attach files to be faxed
      in Windows?
   A: Make sure that the attached files are in the fax, pcx, ascii, or tiff format.  
      If you would like to send MS-Word 2.0 file, simply print to the Fax 
      Window; make sure that the Fax Window is initialized and minimized.


4. Q: WINDOWS.  Why do I get a "Can't open Comport Message" when I try to 
      load the Fax Window?
   A:  a: Make sure that no other communications program is loaded.  
	  For example if you have Terminal loaded, make sure to exit completely 
	  out of it before loading the Fax Window.  The reason is the comport 
	  cannot be shared by the two software applications.
       b: Another thing you can do is change the IRQ settings for COM 3 or 4.
	  Please read your Windows manual on how to setup a different IRQ
	  than the default one that Windows comes with.  Also make sure that
	  the Fax/Modem (hardware) match the Windows (software) settings in 
	  all aspects.  Example to change the IRQ for COM4, you load windows
	  then control panel, then ports, then DOUBLE CLICK ON COM4, that 
	  opens up another window with different baud rates, bits, parity,...etc.
	  Push the advanced option button, and the window for the IRQ and comport
	  addressing pops-up.  Make the necessary changes so that the settings match
	  your fax/modem settings.



5. Q: WINDOWS & 1 LINER.  Will CALL WAITING work with my Fax Board in Windows?
   A: No, if you have call waiting and you are speaking to someone on the line, 
      and you get another call; you click over and if it is a fax 
      IT WILL NOT GO THROUGH, one-liner will not be able to detect it.  
      Our suggestion is to have a telephone line that does not have a 
      CALL WAITING FUNCTION.
      [THE SAME IS TRUE FOR THE 1 LINER FUNCTION IN THE DOS ENVIRONMENT]


6. Q: SCANNERS. Do you have scanner support for the Windows fax software?
   A:      Only scanner support is with our DOS-based software at this time; 
	   Chinon, Canon, and HP scanners.


7. Q:FEATURES. What features are in the DOS-based software but not in the 
     The Fax Window software?
   A:      Some features not YET in The Fax Window Rel. 2.05 include:
	  -Custom Cover Letter
	  -Direct Scanner Support
	  -Able to save/rename LASTSENT fax file.
	  -Able to print the log.
				 


SECTION6:    Modem Information [9624 FAX/MODEM]
______________________________
1. Q: MODEMS. Will it work with my communications programs like 
      Prodigy, Compuserve, Procom, Comit,...etc.
   A:      You can re-set the fax/modem card using AT commands. Best way is 
	   to turn off your computer, turn it back on, get into the Comit 
	   program then follow the key strokes below: 
      /                to bring up the Menu
      O                Go Online...
      M                Manual control of modem 
      You will now be in a blank screen that will allow you to type in modem
      commands. Type the following:
      AT               then hit the <Enter> key. The modem will come back
		       with OK. If you do not see what you are typing, change
		       the ECHO setting  (Alt-E)
      AT&F&C1&D2&W     then hit the <Enter> key. Once again, you will see OK.
		       Note: the W will write these commands into the modem                 
		       so you will not need to do this procedure again.
      Now you can use Prodigy, Compuserve, ...etc.


2. Q: EPROM Revision. How can I find my Eprom Rev. without opening my PC ?
   A1:     Use the AT command below using COMIT, PROCOMM, etc.:  
	   AT+FREV?     then hit the <Enter> key. You will see something like:
	   1.29
   A2:     You can also use CARDTEST /G. (See next Question below.)
   

3. Q: CARDTEST. Another easy way to find information about my fax card?
   A:      Use the cardtest command from a dos prompt:
	   CARDTEST /G    

4. Q: GARBAGE CHARACTERS.
   A:      If you dial into this (or any other BBS) and get garbage 
	   characters on the screen, then check the following:
	a. Turn off MNP compression.
	b. Make sure baud rate matches host computer; i.e. 2400
	
5. Q: DIALTONE. Getting "No dial tone" message using fax and modem.
   A:   a. Check that bottom jack on fax card connects to phone jack in wall.
	b. Using COMIT, get into manual mode and type:
	   ATDT 
	   You should hear a dial tone coming from the fax card speaker. If 
	   you do not hear anything, then the card might be at fault and needs
	   to be serviced or swapped for another Fax96 fax/modem.

SECTION7:    General Information      
________________________________
1. Q: SERIAL NUMBERS. How can I tell which Fax96 card I am using?
   A:      By the first letter in your serial number. The serial number is on 
	   a small, white, bar-coded sticker located on the card as well as in
	   the operators manual.
	   FAXCARD                         SERIAL NUMBER#
	   Fax96                           A00...
	   Fax96 with 1-Liner              L00...
	   Fax96 with Modem                M00...
	   Fax96 with Modem and 1-Liner    B00...   
	   1445 external Fax/modem V32bis  D00...
	   1446 internal Fax/modem V32bis  C00...

2. Q: MONOCHROME MONITORS. How do I put s/w in monochrome mode?
   A:      Start software adding the command "/m" to the end command.
	   (Example: 1)fax /m  2)fccprg /m  3)frecom /m)
	   This switch is needed if running:
		VGA Monochrome monitors
		Laptop LCD computers
		Some CGA monitors

3. Q: PHONE BOOK. Can I import my Dbase phone list into my Fax96 phone book?
   A:      Not yet. Hope to have a utility that will take an ASCII file and 
	   port it to TELBOOK.DAT. Will be on this BBS when ready!


4. Q: WINDOWS. Can I operate my Fax96 card in Microsoft-Windows?
   A:      Fax96 "fax-only" cards run in DOS.
	   Fax96 with Modem cards run in DOS. 
	   To run in Windows you must have:
	a. The Fax Window program ($30 + shipping upgrade from Sales Dept.) 
	b. MS-Windows 3.0 only understands COM1 or COM2. 
	   MS-Windows 3.1 only understands COM1,COM2,COM3,COM4    

5. Q: AUTO-PRINTING. I see "Auto-Print Disabled" in the print menu.  
      How do I enable it?
   A:      Hit the "A" from the Print Menu screen.


6. Q:POST-SCRIPT FILES. How can I covert Post-Script files so they can be 
     faxes by Fax96?
   A:      Call your local software vendor and ask about one of these 
	   programs; QMS Ultrascript, LaserGO, or GoScript.


7. Q:TANDY COMPUTER. I get "Unable to write to Drive D:" when installing the 
     fax software.
   A:      Tandy computers have a ROM-drive on drive D: (read-only). Before 
	   installing our software, get to a DOS prompt and type:
	   SET COMSPEC=C:\COMMAND.COM
	   next, put our install disk#1 in drive A: and from the A:\> prompt, 
	   type: INSTALL A: C: 
	   after the fax program is installed, re-boot you computer.


8. Q:SPEED. Why does my Fax96 send at 9600 baud, but receive at 4800 baud?
   A:       Non-turbo XT, or PC class computers are too slow to accommodate 
	    speeds greater than 4800 in the receive mode.


9. Q:GRAPHIC PROGRAMS. My CAD proram does not support .PCX,.TIF formats. How 
     do I convert them into a "faxable" format?
   A:      Look into getting a file conversion program like "Hijaak," by 
	   Inset Systems (800)828-8088.


10.Q:PCX FILES. How can I convert a received fax into .PCX ?
   A:      You can use the FAX2PRN.EXE utility to convert a fax96 fax file
	   into a PCX file by typing the command below. NOTE: This PCX file
	   will only be read by MS-Windows Paint program. Other programs seem
	   to have problems reading it.
		       FAX2PRN faxname.000 newname.PCX /PCX
	   
	   Example: C:\FAX>FAX2PRN C:\FAX\FAXES\ROSE.000 FLOWER.PCX /PCX


11.Q:WORD PROCESSING. Can't fax Word Perfect files using Faxography.
   A:      Make sure to use the EPSON print driver inside WP51. If you have 
	   WP 5.0 then use their EPSON LQ-500 driver (it works just fine) 
	   You MUST print to a file using this driver and the file name MUST 
	   have the extention of .ECL (example SAMPLE.ECL)
	  *The above note applies to ANY Word Processing program.

12. Q:FAX96 FAX FORMAT?
    A:     We are following the Industry Standard CCITT Group III fax format 
	   as noted in the "Blue Book Volume VIII" To obtain a copy, call:
			Omnicom    (703)281-1135
			    fax    (703)281-1505 

13. Q:MEMORY. How does your program run in memory?
    A:     You can run our background program in EXPANDED, not EXTENDED memory
	   using a memory managment program like QEMM.
	   Memory usage for background programs are:
		FAX96 fax-only: frecomrf /on = about 50k
		FAX96/Modem   : faxsr /on    = about 65k
	   Your computer should have at least 640K of base memory.
	   Our foreground programs ONLY run in base memory. 


14. Q: OPERATING SYSTEMS. Which ones do you support?      
    A:     PC-DOS           YES
	   MS-DOS           YES
	   CONCURRENT DOS   NO
	   UNIX             NO       
	   ZENIX            NO 
	   OS/2             NO 
	   DR DOS 6.0       NO "Intermittent Problems"

15. Q: LOCAL AREA NETWORKS's. Can I run my fax card on a LAN?
    A:     We have ONLY tested it on a Banyan Ethernet network (Only on a 
	   workstation, not the file server.) 
	   If running Novell, Make sure to have IPX 3.0 or higher and make sure
	   you do not have an IRQ conflict with your netwrk card. Printing was
	   tested using a local HPII laserjet printer. 
	   (Novell info. was supplied by a Frecom customer.)


16. Q: PBX PHONE SYSTEM. Can I run my fax card through my phone system?
    A:     Digital PBX phone system  NO
	   Analog phone system       YES


17. Q: VOICE CARDS. Do you work with them?
    A:     Watson Card              NO
	   Complete PC Voice card   NO
	   They seem to compete with our receive TSR when a call comes in.


18. Q: SCANNERS. Which ones do you support?
    A:     We support HP Scan Jet, Canon IX-8, IX-12, Chinon DS-2000, DS-3000.
	   All other vendor's scanners still work but you must scan an image
	   into a .PCX or a .TIF file, set scanner resolution to 200dpi or 
	   below, then enter Fax96 program to send it. 
	  *Will work with HP Scanners NOT HP compatibles.
   
19. Q: MENU SOFTWARE.
    A:     Fax96 has been tested and works with 
			DIRECT ACCESS  Version 4.1
			Delta Tech. International
			P.O. Box 1104 Eau Claire, WI 54702
			(715) 832-0958
	   Thank You Gary!


20. Q: FAXOGRAPHY. 
    A:     If your line drawings are not lining up, make sure to download
	   our latest software from this BBS. Older releases had this bug.


21. Q: SPEAKER. How can I increase the speaker volume on my Fax96/Modem?
    A:     The volume is not as high as we would like, however there is 
	   no means to boost its output at this time.

22. Q: INTEL CAS COMPATIBLE.
    A:     Fax96 is not CAS compatible. Our fax/modem cards are CLASS 2.



SECTION8:       Winfast 1445 & 1446
-----------------------------------
************************************************************************************
IMPORTANT NOTICE TO WINFAST USERS:  1445 & 1446 FAX/MODEMS
************************************************************************************

IF YOU HAVE RECENTLY UPGRADED YOUR FIRMWARE REVISIONS AND ARE UNABLE TO OPERATE THE
FAX/MODEM, THEN YOU NEED TO EXECUTE ANY COMMUNICATIONS SOFTWARE, SUCH AS, COMIT
PROCOMM, TELIX, ETC...
ONCE THE COMMUNICATIONS SOFTWARE IS LOADED YOU NEED TO GO TO A SCREEN WHERE YOU
ARE ABLE TO ENTER AT COMMAND SETS.

AT THE SCREEN WHICH ENABLES YOU TO ENTER "AT" COMMAND SETS; FOLLOW THE INSTRUCTIONS
BELOW:

AT&W255

An 'OK' response should appear, if not check to see that the comport settings
match both the hardware, as well as, the software settings.
************************************************************************************


1.  Q:  Why won't my Winfast fax/modem connect to some fax machines?
    A:  The fax machine you are trying to transmit to, might be out of spec.
	Please check to see if you have the latest Firmware revisions, as well
	as, the latest faxing software release.
	HOW TO CHECK FOR LATEST FIRMWARE:
	LOAD ANY COMMUNICATIONS PROGRAM COMIT, PROCOMM, ETC...
	GO TO WHERE YOU CAN ENTER MANUAL AT COMMANDS.  ONCE AT SCREEN FOLLOW
	THE INSTRUCTIONS BELOW:

	ATI3

	You should get a value depending on which Winfast you have.  If you have
	the
	1446:  Then something like 
	1446 FXD1 69-51446-../..

	For the 1445 external unit you should get
	1445-FXD1 69-51445-.../...


	THE DOTS AT THE END ARE THE REVISION NUMBERS, CHECK WITH TECH SUPPORT
	IF THE ONES YOU HAVE ARE THE LATEST.


2. Q:  Will my Winfast work with any other Fax Software packages in Windows?
   A:  Yes it will work with Eclipse Fax Software, by Eclipse Systems
       ECLIPSE SYSTEMS
       SUITE 1121
       33 W. MONROE STREET
       CHICAGO, ILLINOIS 60603
       312-541-0260
       800-452-0120
       
       The Winfast will not work with any other software in the DOS environment
       except for the one packaged with it.

       1445/1446 have compatability problems with Z-Soft's Ultrafax software,
       Delrina's Winfax Pro, BitFax, and FaxMaster.

   Q:  Will the one-liner work with any other Manufacturers' fax software?
   A:  No, the 1-liner only works with the FAX WINDOW, none of the other fax
       software producers can activate the one-liner option.
    
SECTION9:  FarFetch Fax for Fax96 card only 
-------------------------------------------

1. Q:  FarFetch.  Why do I get beeeep beeeep beeeep instead of beep beep when
       I enter my FarFetch code?
   A:  The Fax96 program needs to be running for the FarFetch Fax feature to work.
       The three long beeeeeps mean that you have new faxes but that the Fax96
       foreground is not running on your PC.  This is because even though the 
       background receive can take your call, the Fax96 foreground needs to be
       running in order to send your faxes.  We considered building a background
       send routine, but believe that the memory required would be more than you
       would be willing to sacrifice.
	

**********************************END****************************************