Slickware is Copy(c)right 1989,1992 by Gary M. Raymond, New Orleans, La.
        Slick Port Modem Register Test Program V1.1 by Gary M. Raymond

                          Simple <Software> Company
                              HOME of SlickWare

                              Gary M. Raymond
                                P.O.Box 8184
                           New Orleans, La.  70182
                               (504) 288-6550
                            Compuserve 70613,3165



   Files Provided:
   ====================================================================

   TESTPORT.COM   Serial Port Test Utility.
   TESTPORT.DOC   This document.

   TestPort will run on just about any version of DOS and with any
   amount of RAM. If nothing else, TestPort will assist you in learning
   more about serial communications and understanding your modem. Having
   written and supported several terminal programs over the past seven
   years, I have long ago realized that most problems involving terminal
   software are actually modem or modem configuration problems. This
   utility should take some of the mystery away from configuring,
   understanding, and diagnosing serial communications hardware. If for
   no other reason than curiosity, you owe it to your modem to use
   TestPort at least once and read through this file. TestPort was
   written in ASIC, and, I will gladly supply the source code with your
   registration, if requested.

   ====================================================================
   TestPort is a basic, easy to use, modem diagnostic tool. Although the
   information TestPort provides will at first be seemingly cryptic to
   the novice user, it can easily be learned and put to good use.  Bit
   mapping the modem registers provides a wealth of information about
   the state of your modem. Your modem is both configured and monitored
   through these registers or electronic switches. Everything from baud
   rate to data parity is determined by the one (on) or zero (off) bit
   settings in these registers. Particular register bits are also used
   to inform the terminal program that a character has arrived or is
   ready to be transmitted along with numerous other useful information.

   According to the IBM scheme of things, you could have as many as
   65,536 port addresses. These ports have an address in the hardware
   set up according to IBM's scheme. Each address points to a one byte
   location called a base address. Since we can both set and retrieve
   bits in these bytes we refer to them as maskable base registers. Each
   of the next subsequent nine bytes (BASE+1, BASE+2 etc) form that
   ports general register set as outlined in the text below. Serial
   communication ports begin with COM Port number one (COM1) with an
   address assigned by IBM as decimal 1016 or 3F8 hex. Hence, the
   address for the COM1 port register is 3F8. This is the place where a
   byte of data is received (3F8 - Received Data Register) or sent (3F8
   - Transmitter Holding Register) depending on requirements at the
   moment. Therefore the base address allows indirect access to both the
   THR and RDR (plus BRDL when bit 7 of LCR is set). The next register
   (the IER) is located at this base address plus one, (3F8 + 1 = 3F9)
   and so on.

   There are two general methods of obtaining bytes of data from a
   serial port after it has been set up. The first involves stoping
   every so often and looking to see if a byte has arrived, and if so,
   taking it. This method of polling the modem registers is ok when
   working at very slow baud rates. Polling is the method used by the
   PC's Basic Input Output Service (BIOS firmware.) Unfortunately, if a
   byte of data arrives before we have had a change to remove the
   previous one, information can be lost. To overcome this drawback of
   polling we can force the PC to react to the arrival of a byte by
   removing and saving it in a special storage area until we have time
   to use it. This is done by designing a special Interrupt Service
   Routine (ISR) that will be activated instantly (no matter what else
   the PC may be doing) to collect and store the byte of data. This is
   referred to as an "interrupt on receive" terminal program, such as
   our product, SLICK terminal.

   There are many things that can go wrong when installing a modem
   on your computer. Usually, problems are evenly divided between
   hardware and software configuration errors. In general, the modem
   itself must be mechanically set, via jumper pins or dip switches,
   to address whatever available serial port is usable on your PC.
   The selected port must also be paired with an interrupt request line
   (IRQ). Note, no two serial devices (examp: modem and mouse) may share
   actively the same serial port IRQ address. Some modems force, or
   allow you to force, certain register bits either high (1) or low (0)
   in lieu of preferred software control. TestPort is useful in
   EXAMINING all of the register settings that occur as a results of
   these various configurations. Improper configuration of software is
   another problem. Here, there are generally three areas of trouble.
   Improper comm port, interrupt and modem command (initialization)
   string settings. So, to review, One: the serial services must first
   be available on the PC. Two: both the modem and terminal software
   must agree in settings with the PC hardware you are attempting to
   access. And finally, the modem initialization command string must
   correctly complete the job of setting any other registers that
   require attention, such as setting FAX mode on or off, hardware error
   correction enabled or disabled, etc. etc. For what its worth, just
   one wrong AT command in the string will cause the entire string to
   FAIL. So, if your particular brand modem does not use &D1 (set dtr)
   as an example, and, it is inserted into your complete string, such as
   ATM1S0=0V1X4&D1S7=45, then the entire string will fail returning an
   error message, leaving your modem still waiting to be configured.

   ====================================================================
   USING TestPort's register mapping ability:

   To run TestPort with mapping action, you must pass the active port
   number via a command parameter. TestPort will work on the four
   standard IBM default ports of 1 (3F8), 2 (2F8), 3 (3E8), and 4 (2E8).
   Let's assume your modem is configured to operate using COM2. Type
   TESTPORT 2 at the DOS prompt. In most cases, you will really want to
   do this while your terminal program is active. You do this by
   dropping to DOS from within your terminal program, then executing
   TestPort. Most all Terminal programs have a drop to DOS feature,
   although it might be called something else. TestPort does a passive
   read only on these registers and therefore will in no way alter or
   change their bit settings. By using the drop to dos feature, which
   allows the modem code to remain loaded in ram, you eliminate the
   possibility that any modem registers will be inadvertently altered,
   by your terminal program, before you get to read the registers. Some
   terminal programs also have features that allow the naming and
   execution of any external dos utility via a combination of trigger
   hot keys. This is a MUCH better way of quickly running TestPort.
   Don't forget in either case to pass the active port number in use.
   (i.e. TESTPORT 2.)  If TestPort is executed as an external utility,
   screen output data will remain until a key is pressed. This will give
   you opportunity to hit Shft PrtSc and save a copy of the screen to
   your printer for evaluation and analysis. If you do not have a
   printer, you should make a long hand record on paper.

   USING TestPort's UART finder:

   Running TestPort without a port parameter will cause TestPort to
   cycle through the four common UART addresses looking for an active
   (U)niversal (A)synchronous (C)ommunications (C)ontroller. (8250 IC)
   If active port addresses are located, TestPort will notify you of
   those that appeared active. Notice, I said appeared active. It is
   possible to have two serial ports but only one terminated to a
   modem. The other may be just a jack on the rear of your PC, there
   for some later expansion. A simple serial card with its open jack
   will still show as an active port.

   Screen Output:
   ------------------------------------------------------------------------
   The Correct Syntax is TESTPORT #, (# to test), i.e. TESTPORT 4,
   however, TestPort will now try to determine what if any serial
   port is responding to TestPort's Inquiries....................

   COM1 appears to have an active UART!
   COM2 appears to be inactive.
   COM3 appears to be inactive.
   COM4 appears to have an active UART!

   Enter Port# to test or Esc to exit ->

   In five seconds type AT <Enter>, active port will echo OK or 0, else Esc!
   ------------------------------------------------------------------------

   Although this kind of information is by far un-conclusive, it does
   give you enough insights to continue experimenting. In the case of
   the information given above, the modem must be attached to either
   COM1 or COM4. To determine which it is, try entering 1 first. If
   there is no echoing of your keystroke or an OK reply to AT (the modem
   attention command) the probability is COM1 is not the port connected
   to your modem. Now try 4. This should test ok! More than likely, COM1
   is an extra, as of yet unused, serial adapter.

   Although this testing facility is only a raw polling terminal, set to
   1200 baud, N81, it can easily be used for simple task, like dialing
   out to test other modems etc. Try typing ATH1 and see if you hear
   your modem take the line off hook....ATH0 to replace it. Fun hun?

   ====================================================================
   SCREEN GENERATED BY TESTPORT when mapping registers:

   When TestPort is run, it produces the following screen, indicating
   the various one byte registers that have been read, their decimal,
   hex, and (binary) bit map values. It's those bit settings you are
   most interested in. The two indirect registers (THR and RDR) read
   via the base register are not useful here. However, those two plus
   the eight indicated account for the 10 registers of a UART chip.

         *******************************************************
             Modem Register Bit Map by Gary M. Raymond SSC
                        Phone (504) 288-6550

         Modem Registers     Dec Value    Hex Value     Bit Map
                                                        76543210
         IER (Int Enable)             0           00    00000000
         IIR (Int ID)                 1           01    00000001
         LCR (Line Control)           3           03    00000011
         MCR (Modem Cont)             8           08    00001000
         LSR (Line Status)           97           61    01100001
         MSR (Modem Status)          48           30    00110000
         BRDL (Low Register)          6           06    00000110
         BRDH (Hi  Register)          0           00    00000000
         *******************************************************


         Hit Any Key to Exit!



   NOTE: Bit positions are read left to right, starting with position
         0 (zero) and ending with 7. This accounts for a full byte of
         eight bits.

   ====================================================================
   SAMPLE USES for TESTPORT:

   Q) My modem wont hang up, what do I look for?
   A) Look at bits 0 and 1 of MCR after starting your terminal program
      but before dialing a number. They should both be set to 1. If not
      check to see if your modem requires external dip switch settings
      to force DTR, RTS or software AT commands like &D2 and &C1.

   Q) How can I tell if my terminal program is interrupt driven or
      a polling BIOS type?
   A) Look at bit 0 of IER, it will be set to 1 if the terminal is
      interrupt driven. Also, bit 3 of MCR is usually set to 1 as
      well. These bits are set to 0 (zero) in a polling terminal.

   Q) My modem wont respond on COM2.
   A) Run TESTPORT 2. If If you see each modem register returning FF hex
      (dec 255 or 11111111 binary) odds are this port is not activated
      correctly via pin or dip settings on the modem card. Check your
      modem manual for correct pin or dip switch settings.

   Q) How can I tell what Baud rate my modem is locked at?
   A) First, run TestPort and obtain the BRDL and BRDH register values.
      Then cross reference them with the Baud Rate Value chart in this
      document file.

   Q) Can I use TestPort to place a call to a BBS?
   A) Yes, but it's VERY limited as a polling terminal and not intended
      for that kind of application. No protocols, no dial directory, no
      no nothing, just a bare foot terminal!

   Q) My modem and software configured for COM3 is brain dead, can
      TestPort help?
   A) You bet! Some serial communications software, especially tsr type,
      use BIOS services for communicating with the serial ports. BIOS
      then depends on DOS to insert the correct port addresses into the
      BIOS area of memory. Some versions of DOS fail to place the
      default addresses for COM3 and COM4 in the required BIOS area of
      memory. TestPort overcomes this limitation by poking ALL of the
      IBM default addresses (3F8 - 2F8 - 3E8 - 2E8) into the correct
      area of bios memory starting at segment 0040. This feature is
      automatic anytime you run TestPort in any mode. To cancel out
      these values, you only need reboot the PC. I will also provide a
      seperate utility (PCA.COM) that can be used via your autoexec.bat
      to insure these addresses are always available after bootup.

   Q) My terminal program has a host mode that allows remote access to
      DOS via a redirection statement in a batch file. Only guess what?
      It locks up my computer. Can TestPort help me?
   A) Well, maybe. There are many computers (clones or otherwise) that
      just do not take kindly to re-direction. (CTTY COM1 or CTTY > AUX1
      type calls) If the reason is due to the problem outlined in the
      answer above, TestPort or PCA will solve it. If not, there is
      a device driver in the public domain called GateWay that usually
      will accept re-direction. It can be found on most BBS'es. One
      nice thing about GateWay is it still allows access to the host
      keyboard and monitor; simple re-direction does not.

   Q) Can I use TestPort to see the default and or active settings
      of all registers in my modem?
   A) Yes, actually, you can do that with any terminal program. To use
      TestPort, type TESTPORT at the dos prompt. Select the active port
      number and wait five seconds for the terminal to respond. Type
      AT&V then hit enter. On some older modems you cannot dump the
      entire register set and you must poll each individually. Say
      you want to see the present value in S7, type ATS7? and so on.

   Q) My old modem had a volume control on the card. My new one does
      not. Can TestPort save my marriage and turn down the volume?
   A) Yes, and again, it can also be done with your present terminal.
      By default most modems allow the speaker on at full volume. You
      can control this by resetting the M and L registers. ATM1 will
      turn off the sound after a connect and ATL0 will reduce the volume
      to the lowest setting. Of cource, these switches belong together
      in your initialization command string. (ATM1L1etc.etc.etc.)

   ====================================================================
   MODEM REGISTER BIT MAP DATA:

       For general purpose information, the port addresses of
       these registers are as follows:

       BASE = COMPORT ADDRESS  (COM1 = 3F8h)
       Therefore, MCR for COM1 equals 3F8h + 4 or 3FCh

       Ten Modem Registers
       ---------------------------------------------
       THR,RDR, *BRDL =  BASE
       IER,     *BRDH =  BASE  + 1  ;  Interrupt Enable Register
       IIR            =  BASE  + 2  ;  Interrupt Identification Register
       LCR            =  BASE  + 3  ;  Line Control Register
       MCR            =  BASE  + 4  ;  Modem Control Register
       LSR            =  BASE  + 5  ;  Line Status Register
       MSR            =  BASE  + 6  ;  Modem Satus Register
       ---------------------------------------------
                *requires bit 7 set to 1 in LCR for access
   ====================================================================

       IER  BIT MAPPING   (Interrupt Enable Register)
       ---------------------------------------------
       BIT     Activates             Action
       0    =  Data Received         Read RDR
       1    =  THR empty             Output to THR
       2    =  Data error/break      Read LSR
       3    =  MSR change            Read MSR
       4    =  zero
       5    =  zero
       6    =  zero
       7    =  zero

       Although the 8250 Uart has 10 one byte registers, only seven have
       direct access, and of the seven, three of these are used
       redundantly to gain access to the three non directly accessible
       registers. This indirect access is achieved by setting bit 7 of
       LSR to 1. Then, the BRDL and BRDH registers are accesses at BASE
       and BASE + 1. These two registers are used to lock the port baud
       rate. The BRD (Baud Rate Divisor) is a 16 bit number (two bytes)
       and therefore requires two (one byte) register access through
       BASE and BASE + 1. Interesting enough, the high byte is only
       necessary for baud rates of 300 or below. At 1200 or higher BRDH
       is set at zero. The formula for calculating the BRD value
       demonstrates why.

                      UART CLOCK SPEED (1.8432mhz)
              BRD =   ----------------------------
                      16 x bit transfer rate (not really baud)

                      1,843,200
              BRD =   ---------   =   256 or    110000000  or 100h
                      16 x 300
                                                B   B
                                                R   R
                                                D   D
                      breaking the result into  H   L
                      two bytes produces =      1 & 1000000

                      where BRDH = 1hex and BRDL = 80h (128 dec)

              FOR 1200 BAUD:

                      1,843,200
              BRD =   ---------   =   96 or    1100000  or 60h
                      16 x 1200
                                                B   B
                                                R   R
                                                D   D
                      breaking the result into  H   L
                      two bytes produces =      0 & 1100000

                      where BRDH = 0hex and BRDL = 60h (96 dec)


       The THR (Transmit Holding Register) and RDR (Received Data Register)
       are accessed via the same physical address as the port base address.
       Since you cannot in theory send and receive at the same instant, this
       little scheme seems ok.



       IIR  BIT MAPPING   (Interrupt Identification Register)
       ---------------------------------------------
       BIT
       0    =  more than 1 intr has occurred

               12                       12
       1-2  =  00  change in MSR        10    data received
               01  THR empty            11    recv error/break

       3    =  zero
       4    =  zero
       5    =  zero
       6    =  zero
       7    =  zero


       LCR  BIT MAPPING   (Line Control Register)
       ---------------------------------------------
       BIT                      01                 01
       01   =  Data Length      00=5bits           10=7bits
                                01=6bits           11=8bits

       2    =  Stop Bits        0=1bit             1=2bits

                                345                345
       345  =  Parity           000=NONE           101=MARK
                                100=ODD            111=SPACE
                                110=EVEN

       6    =  Break Condition  0=disabled         1=enabled
       7    =  Port Toggle      0=Use THR/RDR/IER  1=Use BRDL/BRDH


       SAMPLE: Using N parity, 8 data bits and 1 stop bit requires
       the LCR register of 00000000 to be then set as follows:
                           76543210 = bit pattern
                                 11 = 8 bits
                                0   = 1 stop bit
                             000    = no parity
                            0       = break disabled
                           0        = toggle inactive
                         ----------
                           00000011 = 3h to send to LCR


       Bit 7 of LCR controls the dual function of bits 0 and 1 in the
       IER Register and should be set to zero in the above example.



       MCR  BIT MAPPING   (Modem Control Register)
       ---------------------------------------------
       BIT
       0    =  Set DTR line active
       1    =  Set RTS line active
       2    =  USER BIT #1
       3    =  USER BIT #2
       4    =  UART loopback
       5    =  zero
       6    =  zero
       7    =  zero

       Bit 3 is normally set to 1 for interrupt driven terminal
       programs. Most programs force the modem to hang up by setting
       bits 0 and 1 to 0. Modem software setup for these first two bits
       therefore is usually 1 and 1.


       LSR  BIT MAPPING   (Line Status Register)
       ---------------------------------------------
       BIT
       0    =  byte in RDR (received)
       1    =  overrun in RDR
       2    =  Parity error detected
       3    =  Framing error (out of sync, no stop bit received)
       4    =  Break Detect
       5    =  THR empty
       6    =  TSR empty (removes char from THR)
       7    =  Time Out


       A communications program usually checks bit 5 here before sending
       another character out the base port.


       MSR  BIT MAPPING   (Modem Status Register)
       ---------------------------------------------
       BIT
       0    =  change in [C]lear [T]o [S]end  CTS
       1    =  change in [D]ata [S]et [R]eady DSR
       2    =  change in ring indicator RI
       3    =  change in [D]ata [C]arrier [D]etect  DCD
       4    =  Clear to send ..... [CTS] set high
       5    =  Data set ready .... [DSR] set high
       6    =  Ring Indicator .... [RI]  set high
       7    =  Data Carrier detect [DCD] set high

       Most BBS programs monitor bit 7 of the MSR to determine
       if carrier is lost during a logon.

   ===================================================================
       BAUD RATE DIVISOR (BRD Register) CHART

       Bit Rate            BRDH           BRDL
       ---------------------------------------
       50                   09h            00h
       110                  04h            17h
       300                  01h            80h
       ---------------------------------------
       1200                 00h            60h   From 1200 up, BRDH is
       2400                 00h            30h   always set to zero!
       4800                 00h            18h
       9600                 00h            0Ch
       19200                00h            06h

   ===================================================================

   Registering your copy will help continue the competitive advantages
   of providing economical shareware. As an additional bonus, I will
   ship you several other useful modem and dos utilities free!  If
   you have any comments or suggestions about this utility, feel free
   to write or call.

   Name_____________________________________________________________

   Mailing Address__________________________________________________

   City & State ___________________________________________________

   ZIP _____________________________ Phone _________________________

   Send $4 + $1 (ship & hand) check or money order to:

                              Gary M. Raymond
                                P.O.Box 8184
                            New Orleans, La. 70182
                                504-288-6550
                            Compuserve 70613,3165
   ====================================================================
                                     EOF